COMMUNICATIONS SITE PLAN

ELKO MOUNTAIN

ELKO FIELD OFFICE

Prepared by the United States Bureau of Land Management

Elko Field Office

State of Nevada

Approved: _____/s/ Helen Hankins_____________________________    __June 25, 2004___

Field Manager						Date

ELKO MOUNTAIN COMMUNICATIONS

SITE PLAN

I.	INTRODUCTION	3

A.	Terms and Definitions	3

B.	Purpose	4

C.	Site Description	4

D.	Area Served	5

E.	Access	5

F.	Site History and Development	5

G.	Goals and Objectives of Site Management Plan	6

II.	AUTHORITY AND DIRECTION	6

A.	Authority	6

B.	Relationship to Communications Site Lease	6

III.	GENERAL RESPONSIBILITIES	7

A.	The Bureau of Land Management	7

B.	Facility Owners and Facility Managers	7

C.	FCC and NTIA/IRAC	8

IV.	AUTHORIZED USES AND USERS WITHIN A FACILITY	8

A.	Exclusive Use of a Facility By a Single User	8

B.	Use by Multiple Users	9

V.	FEES	9

VI.	General Operation and Maintenance Direction	9

A.	Unique Resource Considerations at this Communication Site	9

B.	Wiring and Grounding	10

C.	Equipment	10

D.	Cables and Transmission Line (Wave Guides)	13

E.	Radiation	13

F.	Utilities-Availability of and Requirements for:	13

G.	Sanitary Facilities	14

H.	Security And Law Enforcement	14

I.	Site Maintenance	15

J.	Inspections	16

K.	Fire Prevention and Hazard Reduction Requirements	16

L.	Access Maintenance and Restrictions	17

VII.	CONDITIONS FOR CONSTRUCTION, MODIFICATIONS OR EXPANSION	17

A.	Responsibilities	17

B.	Construction Methods and Resource Protection	19

C.	Construction Inspection	20

D.	New or Remodeled/Expanded Buildings	20

E.	New or Remodeled/Expanded Towers	21

VIII.	SITE ASSOCIATION/ADVISORY GROUP	21

IX.	APPENDICES	22

A.	Site Map	22

B.	Authorized Facilities	22

C.	Site Photographs	22

D.	Inspection Checklist	22

E.	User Association By-Laws	22

F.	Road Access and Maintenance Agreement	22

INTRODUCTION

## Terms and Definitions

The terms used in this communication site plan conform to the definitions listed in the October 27, 1995, Federal Register notice “Fee Schedule for Communications Uses on Public Lands” and clarifications provided in Bureau of Land Management Handbook 2860-1.  In the event of a conflict, between the plan and these sources, the Federal Register notice and the Bureau of Land Management Handbook will govern.

The words “lease” and “lessee” as used in this plan refer to the relationship between the Bureau of Land Management and the communications use leaseholder, the lessee.  The words “customer” and “tenant” refer to the relationship between the lessee and the occupants in the lessee’s facilities.

LEASE – An authorization issued to a communication facility owner or facility manager, allowing for the use of Public Lands to construct and or operate a communications facility and unless specifically prohibited, to sublease to occupants in that facility.

LEASEHOLDER OR LESSEE – Facility Owner/Facility Manager

CUSTOMER – Entities that pay a facility owner, facility manager or tenant for communications services and are not re-selling or broadcasting communications services to others

TENANT – A communications user who rents space in a communications facility and operates communication equipment for the purpose of re-selling, or broadcasting communications services to others for profit.

COMMUNICATIONS SITE – An area of Bureau of Land Management administered public land designated through the land and resource management planning process.  A communications site may be limited to a single communications facility, but most often encompasses more than one.  Each site is identified by name; usually a local prominent landmark, such as Elko Mountain Communications Site.

FACILITY MANAGER – The holder of a Bureau of Land Management communications use authorization who leases space for other communication users.  A facility manager does not directly provide communications services to third parties.

FACILITY OWNER – Individual, commercial activities, organizations, or agencies that owns a communication facility on Federal land; own and operate their own communications equipment; and hold a communication use authorization.

NON-BROADCAST – This category includes Commercial Mobile Radio Service (CMRS), Facility Managers, Cellular Telephone, Private Mobile Radio Service (PMRS), Microwave, Local Exchange Network, and Passive Reflector.

BROADCAST – This category includes Television Broadcast, AM and FM Radio Broadcast, Cable Television, Broadcast Translator, Low Power Television, and Low Power FM Radio.

## Purpose

This plan is intended to be used by Bureau of Land Management officials administering communication uses at Elko Mountain, existing lessees, the Users Association, and applicants desiring a lease or a lease amendment.  The plan will be kept updated by amending pages or sections of the plan rather than issuing a revised edition of the plan.  When a revision is necessary, the plan will be amended by letter from the Elko Field Office Manager enclosing a copy of revised pages or sections.  The amendments will be consecutively numbered.

General management direction for all land use is outlined in the Elko Resource Area Resource management Plan, RMP, adopted in 1987, the U.S. Code of Federal Regulations (CFRs) and the BLM Handbook and applicable Instruction Memoranda.  Specific direction for site management planning on designated communications site is contained in BLM Handbook 2860-1.  Primary regulations and policy pertaining to issuance of rights-of-way and leases by the Bureau of Land Management are found in Title 43, Code of Federal Regulations (CFR), Sections 2801- 2803 and BLM Handbook 2860-1.

The 1987 Elko Resources Management Plan, RMP, does not specifically name Elko Mountain.  Elko Mountain was not included in any defined visual resource area in the 1986 RMP.  This RMP will be revised over the next 12-24 months.  Any applicable changes to this communications site plan as a result of the revised RMP will be made to keep this activity plan consistent with the RMP.

Elko Mountain will continue to be managed for low power radio, microwave, cellular, and one LPTV broadcast uses.   The senior use at this site is two way radio traffic control.

A communications site plan was approved for this site in 1992. This plan incorporates applicable information from the 1992 plan and updates direction and technical standards for better management of the Elko Mountain communications site.  This plan governs development and management of Elko Mountain and will be modified in the future as needs and conditions warrant.  Any future such uses must be designed, installed, operated, and maintained to be compatible and not interfere with the senior uses.

This site-specific plan is administrative in nature and is Categorically Excluded from further review under the National Environmental Policy Act (NEPA) (516.DM2, Appendix 1,17).  Any additional development of the site will be addressed in a site-specific NEPA document.

## Site Description

The site is located on lands which are administered by the Elko Field Office, and located north east of Elko, Nevada in portions of Section 26, Township 35 North, Range 56 East in the at approximately 40º 53’ 40” North Latitude and 115º 37’ 45” West Longitude.  Elko Mountain at the north end of the site is approximately 7505 feet above mean sea level (msl).  A site map is provided as Appendix A.

## Area Served

This site does not serve an RMA, Ranally Metro Area.  The largest community served is Elko, Nevada.  The population of Elko, Nevada according to the 2000 Census is between 25,000 – 49,000. Fee determination is based in part on the population zone which may be adjusted annually based upon changes in population and growth or designation of an RMA.

## Access

Access to the site is from Elko on the Highway 227 east toward Lamoille, Nevada.  Approximately 1.5 miles past the turnoff to Jiggs, NV (SR 228), turn left on County Road 711.  Proceed north and then west to the site.  County road access and maintenance ends at the corral turnoff at the private land.  The gravel road crosses private land.  Access and maintenance from the County Road to the site has been secured by the FAA and the FAA maintains this road for their use and others at the site.  See appendix G, Road Maintenance Agreement.

## Site History and Development

Elko Mountain communication site was first developed in 1956 under a grant issued to the FAA for air traffic control.  The FAA built a new facility just south of their original building and the BLM took over ownership of this original building.  From 1969 to 1970, the State of Nevada, Department of Information Technology took over management and improved this facility.  The BLM and FS uses are housed along with other State of Nevada uses.

In 1970 Western Communications was also authorized to construct a facility south of the FAA facility.  In 1989, Nevada Communications placed a facility adjacent to the Western Communications facility. Both of these facilities are now owned by Lambda Communications.  Sierra Electronics, Boehler Construction, Southwest Gas, Ruby Dome, Inc., and NE Nevada Regional Hospital all have their own Right-of-Way grants within facilities owned by Lambda Communications.

Sierra Microwave was authorized to place a microwave tower and facility on the northwest slope of the site in 1973.  This facility has since been sold to Western Telephone, MCI, Western Telephone, and then Pinnacle Towers Inc.  In 1981, Citizens Telephone placed a facility on the southern slopes along the road to provide microwave relay to others sites as well as providing commercial telephone to Elko Mountain.

The final authorization at this site was in 1996, when the National Weather Service was authorized to place a facility just east of the Citizens Telephone Company building.

Current building space and tower space appears to be adequate for the foreseeable demand.  The State of Nevada has plans to eventually replace and upgrade their equipment building and remove the guyed tower.  Lambda Communications also plans to remove the smaller building currently housing the NE Nevada Regional Hospital (Facility Site #3) and erecting a 100’ lattice tower to the north of their current building

If in the future, this existing space becomes utilized to its optimum capacity, ample land area is available for future site development.  Site specific NEPA analysis will be required prior to any future facility modification or new facility construction.

## Goals and Objectives of Site Management Plan

1.	Elko Mountain Site will be managed as a low power two-way radio, microwave, and cellular site.  The low power translator use may remain at a reduced power output, but if it leaves the site, no further broadcast uses will be authorized.  The maximum power output of 400 ERP shall continue to apply to uses at this site.

2.	Future authorizations and additional uses must be designed to prevent degradation of the senior uses at this site.

3.	The overall appearance of the site and the integrity of the natural environment will be improved through stringent maintenance requirements and selection of authorized paint colors.

- The site will be systematically developed to maximize the number of compatible uses while ensuring safety and protection of resources.

- New facilities will be developed only after appropriate site-specific NEPA analysis and coordination with current lease holders and users.

- All lease or grant holders must be members of the Users Association and are required to participate in cooperative management with the BLM and assist in monitoring of site use and maintenance of the access road and other common use facilities.

AUTHORITY AND DIRECTION

## Authority

Bureau of Land Management authority to authorize communications uses on Resource Area (BLM) land is granted by the Federal Land Policy and Management Act of 1976, 90 Stat. 2776 (43 U.S. C. 1761-1771) and is reflected in Title 43, Code of Federal Regulations (CFR), Sections 2801- 2803

and WO IB 98-23.

Bureau of Land Management authority for communications site management planning is contained in Bureau of Land Management Handbook 2801-1, Plan of Development.  Direction on and policy for communication use authorizations is contained in Bureau of Land Management Manual (BLM Manual) section 2860.

Authority for the issuance of authorizations and/or licenses for the transmission and reception of electronic radiation for communication purposes is granted by Congress and administered by the Federal Communications Commission (FCC) and/or the National Telecommunication and Information Administration – Interagency Radio Advisory Committee (NTIA/IRAC).

## Relationship to Communications Site Lease

This site plan will be incorporated into all leases, now and in the future, issued for this communications site and must be used in conjunction with the lease.  PROVISIONS OF THE SITE PLAN ARE ENFORCED THROUGH THE LEASE. Each lessee is expected to include the requirements of the lease and the site plan into any documents, which describe the business relationship between the lessee and the lessee's tenants and customers. The lessee is responsible for enforcing those provisions.

GENERAL RESPONSIBILITIES

## The Bureau of Land Management retains the responsibility for:

Issuing and amending leases and existing rights-of-way to facility owners and facility managers, only for the areas actually occupied by the authorized improvements.  Granting occupancy and use of Public Lands rest exclusively with the Bureau of Land Management Title 43, CFR, Sections 2801-2803

- .  The issuance of a FCC license (authorization), or frequency assignment, does not authorize occupancy of Public Lands.

1.   Approving any new/modified facility(ies) at the site.

- Approving amendments to leases to qualified buyers of facilities on the site.

## Facility Owners and Facility Managers (or their designated representatives) are responsible for:

- Complying with their authorization and all sections of this Site Management Plan.

- Ensuring that all new facilities, expansions, or improvements are consistent with the RMP; any environmental document(s)/decisions for the site; and, this Site Plan.

- Ensuring facilities/equipment not complying with Federal/State/local laws/regulations/ ordinances will be removed or modified within one year of the approval of this plan.  Any modification needs pre-approval by the Bureau of Land Management.

- Keeping all facilities within the established limits of their authorized area.

- Providing the Bureau of Land Management, with the name, address and phone number for a local contact person.  The Facility Owner and Facility Manager and the contact person may be the same individual.  The contact person will be available for emergencies and will have the authority to make decisions about construction issues, facility maintenance and all equipment within the facility.

- Adhering to the terms of the Facility Owner/Manager Lease or Right-of-Way:

  - Facility Owners and Facility Managers are authorized to rent building/tower space to tenants and/or customers without prior written approval from the Bureau of Land Management.

  - Tenants and/or customers may not construct there own equipment shelter (building, shelter or cabinet) or antenna support structure (tower or mast).  The facility owner/manager must own all communication shelters and towers under their lease. [If that is not possible, a separate SF-299 application, cost-recovery deposit, analysis, and authorization are required.  This will also result in the use being a tenant/customer of the original lease holder in additional to being a separate facility for billing purposes.]

  - Tenants and/or customers using a facility covered by a Facility Lease/right-of-way will not have separate Bureau of Land Management permits to authorize the use.

  - Facility Owners and Facility Managers are responsible for complying with the terms and conditions of the Facility Lease or their valid right-of-way.  Facility Owner/Managers are also responsible for ensuring that their tenants and customers are in compliance with the terms and conditions of the Lease or right-of-way, and applicable FCC or NTIA/IRAC license terms and conditions.

  - The Facility Owner and Facility Manager may not place any unreasonable restrictions nor any restriction restraining competition or trade practices on tenants and/or customers, or potential tenants and/or customers.

- Ensuring that all communications equipment is properly installed, operated, and maintained.

- Ensuring that all communication equipment meets ANSI, FCC and Bureau of Land Management regulations, guidelines and standards concerning radiation limitations.

  - Monitoring radiation levels at their facility and;

  - Immediately correcting any radiation levels that are, or could be a hazard to human health or are in violation of FCC or OSHA regulations. (FCC 47CFR sections 1.1307(b), 1.1310 and 2.1093) and FCC OET Bulletin 54, August 1999.

- Providing a certified copy of their use and the category of use along with the current phone numbers and addresses of all tenants and customers as of September 30 each year.  This report is due by October 15th each year.

- Keeping the premises around their buildings free of trash and debris.

- Placing the BLM serial number in six inch lettering on the face of the building visible from the access road.  This numbering system ties to the site map, Appendix A, and will be a physical address in the case of emergencies.

## FCC and NTIA/IRAC are responsible for:

The responsibilities of the FCC and NTIA/IRAC are frequency management.  Correcting interference problems is the responsibility of the affected licensees.  The FCC and NTIA/IRAC are not normally responsible for the resolution of conflicts when the licensees or agencies are operating within the limits of the authorizations.

AUTHORIZED USES AND USERS WITHIN A FACILITY

## Exclusive Use of a Facility By a Single User

All facilities except the FAA facility are currently designed to accommodate multiple users.

## Use by Multiple Users

The capacity of the current facilities is adequate on both the towers and within the existing buildings for future tenants/customers.  Any future proposals must be designed to include multiple users.  This includes multiple use of buildings, towers, back-up generators, grounding systems, fuel containers, access ways and parking areas.

Facility Owners and Facility Managers are not required to lease facility space to others if they can prove to the authorized Bureau of Land Management officer that:

- Space is not available;

- The use is incompatible with the existing facilities;

- Additional space is needed by the facility owner/manager;

- Additional users would violate system security needs; or,

- Potential interference is not resolvable.

FEES

The Bureau of Land Management will charge Facility Owners and Facility Managers annual fees based on the Fee Schedule for Communications Uses on Public Lands as adjusted annually.  These fees will be fair market value for the use of Public Lands.  Since this site is not within an established RMA, Ranally Metro Area, the population zone is between 25,000 – 49,999, Zone 8 will be used for these calculations unless specifically agreed to by the authorizing officer and until populations or RMP designations change.

Fees that Facility Owners and Facility Managers may charge their tenants and “customers” are to be: reasonable (consistent with, and not in excess of, other fees for similar facilities) and commensurate with the uses and occupancy of the facilities and services provided to tenants and “customers”.

General Operation and Maintenance Direction

## Unique Resource Considerations at this Communication Site

- There are no currently identified special resource coordination considerations with on-site or adjacent resource values.  Should special conditions arise through the revision process of the RMP, this plan will be amended accordingly.  The area has been identified as being within suitable sage grouse nesting habitat, but long term use of the site for communications purposes has probably reduced the usefulness of sage grouse nesting in this area.

## Wiring and Grounding

1.	All equipment is to be installed within existing buildings and on equipment racks that are grounded and shielded.  Grounding is to be installed in accordance with accepted standards. (ie. R56, Polyohaser, or equivalent)

2.	All electrical wiring and grounding must meet the ‘National Electrical Code” and applicable estate codes.  All permanent wiring shall be installed in metallic conduit.  Surge protection shall be installed on all power distribution panels.

3.	Lightening protection “down” conductors installed upon communications towers shall be treated as “Transmission lines”.  Therefore, they shall have an insulating jacket.  Periodic bonding of the down conductor to the tower (Galvanized) steel shall be made with proper bonding connectors that are tin plated or made of brass.

4.	Each building is to have its own separate grounding system for all users in that structure.  Wherever practical, interconnection of individual grids and/or the simultaneous placement of a large sized copper ground wire with any new grounding systems that are buried on the site will be required.

5.	Site or facility grounding must be constructed of copper, with #2 AWG or larger wire or 2” or larger solid copper strap, connected to an adequate site/facility ground electrode system.  The site/facility ground electrode system shall be bonded to the power service entrance grounding electrode conductor.  Guy wires should also be grounded using manufacturers approved methods to preclude bi-metallic junction and corrosion.  All equipment on the site (buildings, towers, power units, transmitters, receivers, antennas, combiners, telephone systems, power cabinets, HVAC units, etc) must be connected to the site/facility ground by direct connection.  Electrical system ground wiring is required for electrical ground fault protection and circuit breaker coordination.  The grounding systems shall comply with applicable laws, codes and in accordance with standard engineering practice.  Below ground connections must use either an exothermic welding process (i.e. Cadweld, Thermoweld, etc.), copper wedge pressure devices (i.e. Ampact, Wrench-lock, etc.), or brazed copper connections in conjunction with a mechanical UL listed connector (to be used as a physical strength enhancement component).  Brazing by itself is not an acceptable method of bonding below earth grade (buried).

## Equipment

Equipment Ownership

All equipment shall be labeled with:

- The owner’s name;

- Transmitter frequency(ies);

- A valid FCC, or IRAF, authorization;

- Transmitting power output(s); and

- A current 24-hour phone contact number.

Transmitting Equipment

All transmitters will have protective devices (shields, filters, isolation components), designed into or externally installed, to prevent interference with other users.  All transmitters will meet FCC licensing requirements.

The re-radiation of intercepted signals from any unprotected transmitter and its associated antenna system will be prevented by the use of appropriate filters (wide band and narrow band broadcast transmitters).

The direct radiation of out-of-band emissions (i.e. noise or spurious harmonics) will be reduced to a level such that they may not be identified as a source of interference as defined in the FCC Rules and Regulations (e.g. Part 90.209(e)).  If electromagnetic noise becomes an issue at this site, prior to any additional uses, noise threshold limits must be established, and amended into the Site Plan.

All transmitters not in immediate use and not specifically designated as standby equipment shall be removed.  Loads connected to circulators are to be capable of dissipating the total power output of the transmitter.

Receiving Equipment

A bandpass device (cavity, crystal filter, etc.) is recommended at the input of all receiving devices.  Cavity filters, or other protective device, may be used at receiver inputs to reduce interference.

Where duplexing is used, use of the notch type device should be avoided.  In situations where a notch type device is used, a bandpass filter must be used with the transmitter.

Tower

- Generally only one tower is authorized for each facility owner.  Facility Owners and Facility Managers may obtain permission to construct the second tower only after submitting evidence that demonstrates that their existing tower(s) is/are completely filled and full use has been made of combining systems.  When a single equipment building is required, multiple antenna support structures may need to be designed and authorized to accommodate all uses without interference.

- All towers will be left unpainted, if they are dull, galvanized steel.  Paint is required, only if they have a shiny (i.e. reflective) surface.  Only non-reflective, Bureau of Land Management approved dark gray to green colors will be approved unless FCC requires red/white striping.  All towers will be treated for low to non-reflectance.

- Only lights, beacons or strobes specifically required by the FCC will be allowed on towers (including antennas).

- The maximum tower height for this site is 100 feet.

Antennas

            - Microwave (dish) antennas (other than ground mounted satellite dishes) will be limited to a maximum of ten (12) feet in diameter.  Smallest diameter dishes are preferred if technically feasible.

            - All antenna outputs must meet all OSHA safety standards.  If an antenna output exceeds FCC public or occupation standards (see FCC OET Bulletin 57), it will be remedied within 24 hours after measures are taken or isolated (e.g., fencing, signing, relocation, lowering power levels are all possible remedies).  Ground measurements of Radio Frequency Radiation (RFR), levels will be taken before mitigation measures are implemented.

            - Color(s) for dish antennas, or covers, must be pre-approved by the Bureau of Land Management.  White dish antennas and/or covers will not be approved.  Existing white dishes and covers must be repainted or replaced with grey as repairs or replacement become necessary.

            - Antennas will be treated for low to non-reflectance.

Interference

The responsibility for correcting interference problems is a matter for resolution between the permit/lease holder of the facility(ies), the user causing the interference, and the affected party(ies).  Generally, the first users on a site have seniority with respect to the resolution of interference complaints.  Senior holders have an obligation to maintain their equipment to industry standards, to operate their systems in accordance with the terms of both the FCC license and NTIA/IRAC frequency authorization, and to comply with the Bureau of Land Management authorization.  New users on a site must correct, at their expense, interference problems that they create.  They must cease operation of the suspect equipment until the problem is corrected.  If interference problems cannot be resolved or corrected within a reasonable time, the new use that is causing the interference may be terminated and the equipment removed.

The Bureau of Land Management does not have authority for correcting interference problems, but can act as a mediator to help all affected parties.  Interference problems must be coordinated with the FCC or NTIA/IRAC, whichever is appropriate.

Interference with law enforcement and/or emergency communications must be corrected immediately.  The operation of equipment covered by this Site Plan shall not interfere with United States Government radio or electronic operations already in existence on public land within two (2) miles of the site to which this authorization refers.  The user causing this interference, shall, at its own expense, take all action necessary to prevent or eliminate such interferences.  If it does not eliminate such interference within ten (10) days after receipt of notice from the Bureau of Land Management to do so, this use will be terminated.

If electromagnetic noise becomes an issue, noise thresholds will be established and appended to this Plan.

## Cables and Transmission Line (Wave Guides)

All new cabling will be jacketed and shielded and shall either be flexible or semi-rigid type.  Existing substandard cables will be upgraded as repairs or replacement become necessary.

Cables will be properly installed and will be strapped and fastened down.

All transmission lines (wave guides) are to be supported in accordance with manufacturer’s specifications.

Unjacketed transmission line of any type is prohibited. No transmission lines shall be left unterminated.

Double shielded braided, or solid shielded cable will be used.  No RG-8 type cable is permitted.  No connector-type adapters will be used on transmission lines.  Only correct connectors that will mate to connected devices are to be used.

## Radiation

All communications uses must meet ANSI, FCC and Bureau of Land Management regulations guidelines and standards concerning radiation limitations.

Monitoring radiation levels at the site is the responsibility of all site users and will occur at intervals to comply with FCC regulations and guidelines.  A copy of the monitoring report will be provided to the Bureau of Land Management within 30 days of its completion.

Onsite RFR measurements will be taken using appropriate equipment that can adequately measure both on-tower and on the ground levels before mitigation measures related to RFR are implemented.

Security fences with RFR notice signs are required around areas that exceed public use levels.  All fencing location and design will be pre-approved by the Bureau of Land Management.

Warning signs will comply with ANSI C95.2 color, symbol, and content conventions.  Contact information including name and telephone number will also be included on warning signs.

Lowering power levels for on-tower access during maintenance will be coordinated between affected users.

Any identified RFR radiation problems that are, or could be, a human health hazard must be corrected within 24 hours after measurement tests have been completed or be removed from the site by the site user(s).  If the proposed corrective action involves any new ground disturbance, it must be pre-approved by the BLM.

## Utilities-Availability of and Requirements for:

Commercial Electrical Power

Commercial power is provided to the site under permit to Pacific Power Corp.  The distribution line and the service drops are buried.

Telephone Service

Citizens Telephone provides commercial telephone service to this site from their facility.

Fuel Tanks

All facility owners are responsible for providing fuel storage (propane or diesel) and emergency power for their tenants.  No tenants will be authorized their own separate fuel tank and/or generator.  Fuel storage will preferably be consolidated into a tank large enough in size to accommodate all tenants by each facility owner.  At a minimum, tanks will be grouped together in a consolidated area adjacent to their facilities.  All fuel, storage tanks (e.g. LPG, propane) must meet current fire department, Federal, State and Borough safety and hazardous materials requirements.

- All tanks will be:

a.	Signed in red letters, “SMOKING OR OPEN FLAME PROHIBITED WITHIN 20 FEET”;

b.	In conformance with National Fire Protection Association (NFPA) requirements; and,

c.	Painted an approved color, or screened by an enclosure to blend in with the natural environment.  (If an enclosure is used, it must be pre-approved and painted an approved color).

d.	Propane tanks must be protected from hazards such as falling ice from nearby towers and vehicles backing into them by installing appropriate barriers where needed.

2.	Diesel tanks will also be:

a.	Enclosed in Bureau of Land Management and fire department approved secondary containment vaults that are painted a Bureau of Land Management approved color.

b.	Constructed with underground fuel lines.  Fuel line must be constructed of black, treated pipe and fittings, and must be posted.

## Sanitary Facilities

1.	Plans for any new sanitary facilities must be pre-approved by the Bureau of Land Management.  If it is determined by the Bureau of Land Management that the user needs such facilities, they will be provided by the applicant/holder in a manner and location satisfactory to the Bureau of Land Management and within the requirements of the Borough Health Department.

## Security And Law Enforcement

The Elko County Sheriff’s Department is the key law enforcement agency for the area.  They are responsible for most civil and criminal matters.  The Bureau of Land Management will be responsible for enforcing matters related to uses of BLM lands (e.g. resource protection issues).

Patrol and policing for security purposes is the holder’s responsibility.  If holders desire to have the protection of fencing, Bureau of Land Management approval must be obtained first.  To reduce visual clutter and efficiently utilize existing space, fencing groups of buildings will be encouraged.

Any access gates must be adequate for Bureau of Land Management and County Fire Department access needs.

Fencing

None of the current facilities are currently fenced.  Any future modification must meet the following criteria:

1.	All fences must meet health and safety requirements.

2.	All fence locations and design require Bureau of Land Management pre-approval.  The standard fencing type will be chain-link (i.e. cyclone).

3.	The standard fence height will be eight (8) feet.

4.	Fencing will be designed, maintained, and of a type to minimize interference issues.

5.	Fences will be signed with RFR notices if RFR is above public levels.

## Site Maintenance

The objective of maintenance activities is to present a clean, neat, and orderly appearance at the site and have all of the authorized improvements safe for workers and the public.  All users will keep up the overall appearance of the site.

Miscellaneous debris remaining after any construction and/or equipment installation, removal or modification, is not only a hazard, but can cause interference or intermodulation problems.  In particular, all loose wire or metal objects are to be removed from the site.

The users of the Site will remove all graffiti within 10 working days of finding it.  If graffiti is on natural features (e.g. rocks), the graffiti will be removed in a method approved by the Bureau of Land Management Authorized Officer.

Holders will not be permitted to leave or dispose of trash, garbage or cut brush on public lands.  No outside trash or litter containers will be provided.  Site users (i.e. holders) will remove litter from the site as it is produced.

Policing of litter in common areas (i.e. areas between buildings and developed sites) is the shared responsibility of those holders bordering these areas.

During construction and/or maintenance, paintbrushes will not be cleaned off on the rocks around the site and excess materials (e.g. cement) will be removed from public lands.

Peeling paint on buildings and/or towers will be re-painted within ten (10) days of notification of the holder by the BLM.

The lease/ROW grant holders are collectively and individually responsibly for the abatement and control of noxious weeds according to the Elko Field Office Weed Abatement programs.

## Inspections

Unless waived in writing by the Bureau of Land Management, the holder is to provide, annually, a certified inspection of the facilities and equipment covered by the authorization.  The inspection will include technical review that assures that authorized equipment is operating within the specifics of this Site Plan, the FCC authorization, ANSI Standards, and the manufacturer’s specifications.  In addition, the inspection must assure that the authorized equipment is secure, free of rust, properly grounded, and otherwise properly operated and maintained.  This inspection should also review general good "housekeeping". A copy of the inspection report, certified by a telecommunication specialist, is to be provided to the Bureau of Land Management within 30 days of completion.  Appendix D provides an example of the inspection checklist.  This inspection will be done jointly with a representative of the Users Association and the lease holder.

The Bureau of Land Management may also conduct un-announced periodic reviews to monitor for authorization compliance.

## Fire Prevention and Hazard Reduction Requirements

Facility owners and managers will be required to maintain to mineral soil, a minimum of thirty (30) feet clearance around their buildings and a minimum of ten (10) feet clearance around any propane tanks.  Identified threatened, endangered, or sensitive plant species must remain within the minimum clearance areas.

Smoking is prohibited while walking in flammable vegetation.

The roof structure shall be kept reasonably clear of leaves, twigs, and other debris at all times.

No explosive will be stored at this site.  Flammable materials shall be stored in conformance with the requirements of local fire regulations.  Flammables will be placed in closed containers and stored away from sources of ignition and combustible materials.  If flammables are stored within a building, the building will be locked, properly signed and well ventilated.

Approved spark arresters will be required and maintained on all internal combustion engines.

At least one (1) U.L. rated 4 B:C dye chemical fire extinguisher is required inside each building.  Prior to each June, fire extinguisher(s) shall be inspected and refilled by holders, if necessary.

Any fire will be immediately reported to “911”, the nearest Bureau of Land Management office or the County Sheriff.

Periodic fire prevention inspections are made by Bureau of Land Management Officers.  They will call to your attention any lack of compliance with the above regulations, plus any other existing hazards.  Compliance with these inspections is required within the time limits specified.

All fire protection standards must be accomplished by the beginning of fire season unless otherwise agreed to, and then maintained throughout the fire season.

For new construction, the Bureau of Land Management will provide the Holder with a separate Construction Fire Plan which will be prepared at that time as applicable.

## Access Maintenance and Restrictions

Roads

From Elko take the Lamoille Highway, SR 227 to approximately 1.5 miles east of the Jiggs turnoff then north on County 711 to the corral turnoff at the private land then to public lands and the site.  Access and maintenance over the private land and through the public land is held by the FAA.  See the Road maintenance agreement as Appendix F.

Holders who damage or disturb the access road, or any associated structures, such as ditches, culverts, roadside vegetation, signs and/or underground utilities or facilities, will be required to repair the road or associated structures to conditions equal to or superior to those prior to any damage or disturbance.  These actions may require a new NEPA analysis.

Interior Site Driveways/ Parking Areas

Roads within the communications site will be maintained by the site users.  Interior roads will be planned and approved during establishment of new facilities.  Interior roads will be maintained in a manner to allow only one entrance to the site.  The intent is to discourage off-road vehicle use in and around the site.

Road Closures

Native surface roads are subject to periodic closures to entry during periods of extreme fire danger, inclement weather, or wet conditions.  Authorized site users may use the site during these periods, but should use judgment and may need to seek advance approval from the Bureau of Land Management.

CONDITIONS FOR CONSTRUCTION, MODIFICATIONS OR EXPANSION

## Responsibilities

In addition to the responsibilities listed in Section III, New Facility Owners and Facility Managers are responsible for:

1.	Submitting a complete application to the Elko Field Office prior to any new construction or modifications to existing improvements (ATTN: “Realty Specialist”).  The application must include:

a.	Submitting the appropriate Cost Recovery fees in connection with the application.

b.	A copy of the approved Site Plan Base Map showing all of the proposed (new) facilities including structures, towers, and auxiliary equipment;

c.	Completed drawings/plans prepared by a registered engineer and approved by the Bureau of Land Management;

d.	Identification of any microwave beam paths, a plot of their azimuth(s), and their proposed elevation(s) on the tower;

e.	All proposals must include documentation that shows that proposed facilities will not be obstructing, or interfering with, any existing fixed point to point antennas, omni directional broadcast antennas, or microwave beam paths in the directions of primary population targets.  Proposed beam path needs must be shown on Site Plan Base Map; and,

- Any needed recommendations, changes or modifications to their original proposal, based on any required resource surveys and/or reports.

2.	Demonstrating that their proposals will not cause undue interference with any existing uses before new facilities can be approved by the Bureau of Land Management, the applicant has the responsibility to demonstrate that they will not cause undue interference with any existing uses.  In addition, it is the applicant’s responsibility to show that any new facilities will make the most efficient use of the limited amount of space at the site.

3.	Showing that their proposals will provide for future users without additional construction are encouraged.

4.	Providing engineering and geotechnical investigations for development of specific foundation designs and grading plans.

5.	Providing an Erosion Control Plan prior to construction activities.  At a minimum, the Erosion Control Plan must include: sediment control, stipulations that cut/fill slopes will be graded and contoured to prevent erosion and/or excessive runoff, and recommendations for temporary erosion control measures, (e.g. netting, silt fences, swales, and/or sediment collection areas).

6.	Coordinating with other Federal (e.g., FCC and FAA), State and Borough agencies and obtainment of all required approvals and/or permits.

7.	Providing 30-day notice to all facility owners/managers at the site, as well as the Bureau of Land Management, of all new frequencies proposed for the site.  A completed BLM technical data sheet or equivalent must be sent with the 30-day notice to allow for comment of potential interference.  This would be for new frequencies for themselves and their tenants.

8.	Insuring that all written approvals have been obtained from the Bureau of Land Management prior to construction.  In addition:

New and/or modified facilities will not obstruct existing fixed point-to-point antennas or omni-directional broadcast antennas in directions of primary population targets.

- A bonding stipulation may be required on a case-by-case basis following consultation of the Technical Committee.  The stipulation would include:

  - A bond acceptable to the Authorized Officer shall be furnished by the holder prior to issuance of the grant or lease in an amount to be determined.  Said bond shall be held by the Bureau of land management for a period of six (6) months following completion of construction and continuous operation at the authorized effective radiated power (ERP).  The bond shall be available to cure interference problems to an existing site user’s equipment when, in the judgment of the Authorized Officer, the operation of the facility, as approved herein, is the direct result of that interference.

## Construction Methods and Resource Protection

Plans submitted by an applicant for any new construction or modifications shall specify provisions for soil rehabilitation measures including, but not limited to, soil replacement and stabilization and for proper handling of runoff from buildings, parking area, access roads, and undeveloped common areas.

The following methods and resource protection measures will be required to minimize impacts during construction:

1.	Avoid and protect sensitive resource areas, as identified by the Bureau of Land Management.

2.	Compliance with the Erosion Control Plan.

3.	During construction and/or maintenance, paintbrushes will not be cleaned off on rocks around site and no marks of any kind (including survey marks) will be permitted on rocks.

4.	Minimize ground disturbance and vegetation removal as much as possible during construction activities.  All ground-disturbing activities require Bureau of Land Management pre-approval.

5.	Any extensive cut and fill slopes will be re-vegetated with vegetation species approved by BLM as soon as possible after construction.  All re-vegetation requires Bureau of Land Management pre-approval. If necessary, reseeding will be required until vegetation is successfully established as determined by the Bureau of Land Management.

6.	No grading material will be cast off during construction/reconstruction activities. Excess soil can be used for fill material on road and/or building/tower pads.

7.	Temporary, on-site storage of construction materials will require pre-approval by the Bureau of Land Management.

8.	Construction materials and supplies, except for hazardous materials (see number 10. below) may be left unattended at the construction site at the end of each workday, but at the owner’s risk.

9.	Hazardous materials, including, but not limited to all fuels, oils, and lubricants are not to be left unattended at the site at any time.  During construction, these materials are to be removed from the site at the end of each workday, or temporarily stored inside a locked and signed building until the following workday.

10.	All surplus construction materials and/or waste debris must be removed from the site no later than thirty (30) days after construction has been completed.

11.	Any earth moving or heavy equipment (e.g. dozers, graders, cranes, backhoes, etc.) leaving the designated roadway and/or approved parking area(s) to perform authorized activities at the site, will be washed off prior to being brought onto public land to prevent the introduction and spread of noxious weeds into the area.

## Construction Inspection

1.	All new construction, reconstruction, or major modification shall conform to the established technical standards and accepted engineering practices (i.e., the Uniform Building Code).

2.	Any construction inspections required by other applicable agencies are the responsibility of the holder.  Copies of completed inspections are to be provided to the Field Manager, either as they occur or as part of the final as-built plan.  Inspection information shall become a permanent part of the proponent’s special-use file.

3.	The Holder agrees that corrective work detailed in Bureau of Land Management, or other agency required compliance inspections, would be completed by the scheduled completion date.  If the Holder disagrees or has questions about specific items, the Holder must contact the Bureau of Land Management in order that the disagreement or item may be resolved.

4.	A final set of as-built plans will be submitted to the Field Manager within 90 days of acceptance of structure (if contracted) or of completion date.

## New or Remodeled/Expanded Buildings

- Any new buildings must be designed to accommodate multiple users along with fitting into the physical environment as defined in a site-specific environmental analysis developed at the time of the proposal.

- Buildings are required to be one-story, flat roofed.  The roof must be metal or covered with metal to be fire resistant.  Roofs can be equipped with antenna support structures, such as poles and railings that can extend up to 25-feet above ground level.

- Facility Owners and Facility Managers are encouraged to construct the interior of their buildings in a modular fashion, so that they can:

a.	Sublease sections to others;

b.	Provide tenants and customers with internal separation and security;

c.	Reduce physical interference; and

d.	Increase management effectiveness.

- The following materials are approved for construction of new facilities (i.e. buildings)

#### a.	Floors – Concrete slab with drainage.

b.	Walls – Concrete block, pre-fabricated concrete, or other pre-approved fire resistant materials.

c.	Roof – Metal, or concrete, if painted to eliminate shiny surfaces, or other fireproof material as approved by the Bureau of Land Management.  Proposals for wooden roofs will not be approved.

d.	Partitions – If it is felt partitions are necessary in buildings, ensure they are constructed with fire resistant material (e.g., concrete block, reinforced concrete, or properly grounded expanded metal.

e.	Color – Proposed color for use on all exterior building surfaces must be pre-approved by the Bureau of Land Management. The goal of the color selection for the facilities is to make the building as inconspicuous as possible and make buildings located on the skyline look inconspicuous when viewed from a distance.  The intent is to reduce or eliminate glare from reflective and/or illuminated surfaces such as windowpanes, sheeting and reflective paints.  Non-reflective, Bureau of Land Management approved dark gray to green colors will be used on equipment buildings.

f.	Pre-fabricated equipment shelters which meet the above requirements may be approved.

- Building entry lights must:

a.	Only light the immediate area in the vicinity of the door;

b.	Be motion activated and have a limited time duration (e.g., 3-5 minutes); and

c.	Have a shielded beam that is pointed at the building door.

Requests for all-night (i.e. “dusk-to-dawn”) lighting, or entry lighting that would be visible from outside of the site will not be approved.

## New or Remodeled/Expanded Towers

- All new construction, reconstruction, and modifications to towers will be pre-approved by the Bureau of Land Management prior to implementation.

- It is the applicant/holder’s responsibility to assure that a new, or modified, structure will not unduly interfere electronically or physically with any existing equipment at the site.  Towers must be spaced, so as to prevent ground level radiation and/or interference problems.  This must be clearly demonstrated in writing to the Bureau of Land Management prior to issuance of a lease, permit, or amendment.

- All new towers will comply with current applicable OSHA or ANSI structural and safety specifications and design standards, including safety-climbing devices.  Towers should be as narrow and “open” as safety and structural integrity allow.  New towers will be designed using maximum wind, snow, and/or tower loading anticipated for the site.

SITE ASSOCIATION/ADVISORY GROUP

A Site Association is established and functions at the Elko Mountain Communication Site. The Site Association By-Laws are attached to and are part of this plan as Appendix E

APPENDICES

## Site Map

## Authorized Facilities

## Site Photographs

## Inspection Checklist

## User Association By-Laws

## Road Access and Maintenance Agreement

APPENDIX A

SITE MAP

(See associated AutoCad Map on this website)

APPENDIX B

LEASEE FACILITY TABLE

(See associated User’s Table on this Website)

|  | Auth # | Use | Building | Tower | Access/Parking | Other |
| --- | --- | --- | --- | --- | --- | --- |
| Facility 1 BLM facility managed by State of Nevada Info Technology | NVN 618 | PMRS | 10’x 20’ w 5’x 10’x 10’x 5’ battery room. | 30’ lattice 100’ lattice 48’ guyed | Access and parking | 8’x 10’ metal generator shelter |
| Facility 2 FAA | NVN 043765 | PMRS | 17’x 50’ alum siding | 40’ lattice | Access and parking. ROW across pvt lands and BLM |  |
| Facility 3 Lambda | NVN 4467 | FAM | 27’x 19’ metal 9’x 7’ concrete | 60’ lattice 55’ guyed | Access and parking | 2 - 500 gal propane Outside generator |
| Facility 4 Pinnacle Towers Inc. | NVN 7028 | FAM | 12’x 23’ metal | 40’ lattice | Access and parking | 2 -500 gal & 1000 gal propane 8’x 9’ metal generator bldg |
| Facility 5 Citizens Telephone Co. | NVN 25353 | MIC | 8’x 28’ metal | 40’ lattice | Access and parking | 500 gal diesel, generator in equip bldg |
| Facility 6 Nat’l Weather Service | NVN 60334 | PMRS |  | 20’ monopole |  |  |

APPENDIX C

SITE PHOTOGRAPHS

(See associated Facility Photos on this Website

APPENDIX D

RADIO-COMMUNICATIONS SITE ANNUAL INSPECTION

RIGHT-OF-WAY HOLDER ______________________________  BLDG _____________________________

CURRENT ADDRESS ___________________________________ BLM SERIAL NO. ___________________

MANAGER _____________________  TENANT ________________  CUSTOMER ____________________

SATISFACTORY	UNSATISFACTORY

1.  TOWER STRUCTURAL INTEGRITY	______________	_________________

CORROSION	______________   	_________________

2.  ANTENNAS AND FEEDLINE	______________	_________________

3.  LIGHTNING PROTECTION	______________    	_________________

POWERLINE	______________	_________________

INTERIOR GROUND SYSTEM	______________	_________________

EXTERIOR GROUND SYSTEM	______________	_________________

TRANSMISSION LINES @ ENTRANCE PANEL	______________	_________________

4.  INTERFERENCE PROTECTION

FILTERS/ISOLATORS	______________	_________________

5.  ELECTRICAL

INTERIOR	______________	_________________

EXTERIOR	______________	_________________

6.  GENERAL SAFETY	______________	_________________

7.  TRANSMITTER FREQUENCY AND POWER

AGREE WITH FCC LICENCES/NTIA ALLOCATION

AND BLM PERMIT	______________	_________________

8.  INSIDE HOUSEKEEPING	______________	_________________

9.  OUTSIDE HOUSEKEEPING	______________	_________________

REMARKS _______________________________________________________________________________

_______________________________________________		_________________

TECHNICAL COMMITTEE REPRESENTATIVE		DATE

_______________________________________________		_________________

RIGHT-OF-WAY HOLDER		DATE

_______________________________________________		_________________

BLM REPRESENTATIVE		DATE

APPENDIX E

Elko Mountain Communication Site

Constitution

And

Bylaws

SECTION 1:	  The name of this Association shall be the ELKO MOUNTAIN

COMMUNICATION SITE USER’S ASSOCIATION (EMCSUA).  The EMCSUA will be organized for the cooperative protection from physical and electromagnetic interference to existing radio facilities, ground and air access, protection of property and development of the area for maximum compatible use commensurate with the adequate functioning of existing facilities, in accordance with pertinent regulations of the Bureau of Land Management.  The association is an incorporated, nonprofit association formed solely for the purposes hereinafter set forth and will not directly or indirectly, as an association, engage in any business whatsoever for profit or otherwise.  The signatories to this agreement are in no way deemed to be a partnership, joint venture or association except for the purpose expressly herein set forth.

ARTICLE II

SECTION 1:  The purpose of this association is to form an organization of present and future radio-electronic users under grant of right-of-way on Elko Mountain within the Elko Field Office, Bureau of Land Management (BLM).

The Elko Mountain Communication Site, which is located in T. 35 N., R. 56 E., MDM, Nevada, Section 26, for the purposes of this agreement, shall be defined as the area consisting of the present development on the peak and the land within a radius of two (2) miles around it.  The object is to properly manage future use and development of this communication site to minimize physical and electromagnetic interference for authorized users of it.

The objectives of the association are:

- To advise the BLM Elko Field Office Manager on measures to manage the site to protect the rights and interests of its members, including protection from physical and electromagnetic interference.

- To investigate allegations of physical and/or electromagnetic interference and recommend measure for correction.

- To review applications from prospective users and recommend to the BLM Elko Field Office Manager measures which will adequately protect existing user’s operations.  A prompt report will be made of the recommended course of action with supporting rationale as each situation may require.

- To recommend cooperative arrangements for financing the maintenance and upkeep of existing improvements, such as roads and other developments constructed for the common benefit of the site users.

- To recommend a schedule of fees that will be applicable to all members of the Association for the maintenance of common use improvements benefiting all right-of-way holders.

ARTICLE III

SECTION 1:  The Association will consist of the right-of-way grant holders on the Elko Mountain Communications Site, or a representative for each holder as designated in writing to exercise its voting privilege, and a representative of the Bureau of Land Management.  A right-of-way holder is defined as an individual, association, corporation or governmental entity holding a Bureau of Land Management right-of-way grant or reservation for a communications site.  Notices delivered to the designated representative shall be considered notice to the user itself.

SECTION 2:  The Association shall select a Board consisting of a chairperson, a vice-chairperson, a secretary/treasurer, a site database manager (who will serve on the Technical Committee) and a chairperson of supporting committees as required, from the association members, who will hold office for one year or until their successors are selected.  Selection of officers shall be determined by the drawing of lots.  Members so selected shall then serve their terms on a rotational basis subject to their right of refusal to so serve.  The first name so drawn will serve as chairperson and the other offices will be so filled in descending order as the names are drawn.  As vacancies occur, the next name on the list will occupy that office.  If a vacancy occurs due to turnover in a holder’s internal organization, the authorized replacement may serve out the remainder of the unexpired term.  New users will be added to the roster to serve as officers in the group in the order they receive authorization to locate on the site.  After the chairperson of the Technical Committee is selected, volunteers will be solicited from each type of user to serve on the committee.

For the purposes of this document, the term “user group” and “user” will be used interchangeably to refer to those right-of-way grant holders who have entered into this Association and which have been authorized to occupy the Elko Mountain Communication Site by receipt of a right-of-way grant or right-of-way reservation issued by BLM.

SECTION 3:  All recommendations of the association will be forwarded to the BLM Elko Field Office Manager for action.

SECTION 4:  Each new right-of-way holder on the Elko Mountain Communication Site will be required to become a member of the Association through stipulations included in its right-of-way grant from the BLM.

SECTION 5: Members shall be in good standing when all Association fees and assessments are paid and when they are in compliance with the Association’s constitution and bylaws.

ARTICLE IV

SECTION 1:  Each member shall, during the existence of this Agreement and thereafter, severally release and indemnify each other from and against all liability, cost, expense and valid claims for injuries or deaths of persons and loss or damage to property arising out of use of the access road or electronic site by such party or the employees, agents, guests or assigns of such party, to the extent provided by law.

SECTION 2:  All members shall agree to indemnify and hold harmless the United States, its successors and assigns, its officers, agents and employees, from any and all damages and claims for damages of every description or kind whatsoever, which may result from the exercise of any of the rights reserved herein.

ELKO MOUNTAIN USER’S ASSOCIATION

BYLAWS

ARTICLE 1

SECTION 1:  Chairperson’s Duties

- Arrange for and preside at meetings of the Association.

- Represent the Association in public meetings and meetings with the BLM.

- Supervise the work of the other officers of the Association to assure coordination of efforts and on time completion of necessary tasks.

- Approve and sign all Association expenditures of Association funds.

SECTION 2.  Vice –Chairperson’s Duties

- Assume any and all of the Chairperson’s duties, given appropriate notice, if the Chairperson is unable to fulfill them.

- Monitor site inspections to assure fair and impartial results.

- Coordinate and direct committee work as needed.

- Promote cooperation among site users.

SECTION 3.  Secretary/Treasurer’s Duties.

- Prepare outgoing Association correspondence and present it to the Chairperson for approval and distribution.

- Disseminate incoming correspondence to affected users.

- Record minutes at meetings; keep members apprised of meetings, agendas and planning activities, which affect the Association, including meetings.

- Maintain all Association files, records and accounts to keep them current and accurate.  This will include sending notices to members of assessment payments due and making deposits into the appropriate account so that checks may be written to cover expenses of the Association.  All Association documents shall be open and available for inspection by any member including the BLM.

- Shall establish and maintain a separate and identified account on a locally established and Federally insured financial institution.  Prepare all checks and payments of the Association and present them to the Chairperson for approval and signature. Maintain a record of all transactions, including date, amount received or disbursed, from or to whom, and for what purpose. Disbursement of funds shall be signed by at least two (2) officers of the association.

SECTION 4:  The Financial Committee shall be a standing committee consisting of at least two Association members elected by the membership.  The committee shall set forth a procedure for determining a proper and fair sharing of cost and expense of use, maintenance and reconstruction needs of the access road and common use facilities directly related to use of the site, such as road surface and foundation conditions, bridges, culverts, drains and the like to maintain the site and related facilities in a usable condition.  The committee is also responsible for maintenance and upkeep of gates, locks, helicopter landing area and other common use areas as may be appropriate for use of the site.  The committee shall audit the Treasurer’s financial records just prior to the annual meeting, or on special request, and present a report of its finds to the Association.  The committee shall be responsible for preparation of the Association’s annual budget.  When the Association determines that road or site conditions warrant repair, the committee shall research the work exploring all cost, complexity and contracting options, contract the work to be done and inspect it for acceptance upon completion.

SECTION 5:  The Technical Committee shall be a standing committee, which prepares and maintains the Technical Guidelines with which all users of the site must ultimately conform.  It shall consist of at least three members of the Association from the following areas of expertise, as appropriate, microwave, broadcast, and two-way.  The committee shall select a chairperson, who shall represent the Association in technical matters.  One member shall be designated as the Site Data Base Manager.  The committee shall also help the BLM conduct site inspections and assist in preparation of a report of the findings to be presented to the Association.  It shall perform other duties of a technical nature as deemed necessary to support the Association, such as evaluating the compatibility of additions or modifications to the site and making recommendations to the BLM concerning acceptance or rejection.

Site Data Base Manager’s Duties:

- Develop and maintain a base of the technical datum, which concern the users of the Elko Mountain Communication Site.  This database could be expected to include such things as receiver and transmitter frequencies, ERP output, a list of users, call signs and the detailed site map.  Other information may also be included as the need is identified by the association.

- Preparation of and distribution to the association members of a current listing of relevant site data on an annual basis.  A convenient time for the distribution of this listing would be at the annual or at a scheduled special meeting.

ARTICLE II

SECTION 1:  Interests

Right-of-way holders granted rights for common use facilities, such as access road and helicopter landing area, except backup power facilities, will relinquish those rights after the BLM grants to itself a right-of-way reservation for the common use facilities.  However, the BLM will not unilaterally assume financial responsibility for the common use areas.  Financial responsibility will be maintained jointly by all of the users through the Association.

SECTION 2:  Assessments

An annual assessment shall be made upon all members to provide funds for operational expenses of the Association.  Association expenses are defined to include maintenance of common use facilities such as the access road as well as the incidental expenses of operation such as postal fees and cost of distributing notices of meetings and agendas.  Special assessments may be made and apportioned as approved by the membership to cover unanticipated circumstances, which may arise.  Each individual user shall be responsible to repair excessive damage to the joint use areas caused by abnormal construction work.  Money left over at the end of each year shall carry over to the next year to be applied to the association’s expenses.  The carry-over money will be prorated among all the users who contributed the previous year.  These procedures may need to be amended after a trial period operation.

SECTION 3:  Maximum and Actual Assessment

The beginning annual assessment shall be $100 per year for each user.  The Secretary/Treasurer and the individual user will work out the details for payment.  Future actual annual assessments shall be based on recommendations made by the Secretary/Treasurer and Financial Committee and approved by a simple majority of the members present at the meeting.

SECTION 4:  Pro-ration, Late Payment Penalties, Enforcement and Collection

A) Pro-ration of Assessments

Prorated fees will be paid in advance for a 12-month period.  Those grantees receiving a BLM right-of-way grant after January 1 of each year will pay a prorated fee.  Grants issued prior to the 15th of the month will pay for the full month.  Pro-ration will be based on the following factors:

12 months	1.0000				6 months	0.5000

11 months	0.9167				5 months	0.4167

10 months	0.8333				4 months	0.3333

9 months	0.7500				3 months	0.7500

8 months	0.6667				2 months	0.1667

7 months	0.5833				1 months	0.0833

All amounts will be rounded to the nearest dollar.

B) Enforcement

Failure to pay the annual assessment may result in cancellation of the holder’s right-of-way grant for failure to comply with its terms and conditions.

C) Collection

The Secretary/Treasurer will make collection of assessments, including custody and disbursement of the money.  Billings for assessments will be sent during June of each year or will be due for part of a year when the right-of-way grant is issued.

ARTICLE III

SECTION 1:  Technical Standards

All users on the site will adhere to the following minimum technical standards.  Adherence to these standards will minimize physical and electromagnetic interference, thus providing for improved compatibility of all users.

Required:

- All radio-electronic type equipment, including associated cables, wiring and antenna systems, shall be installed and maintained in a clean, neat and orderly manner, and be permanently secured.  All such installations shall be both electrically and mechanically sound.

- All external transmission line shall be jacketed and have a solid outer conductor (or have shielding > - 90dB).  Unjacketed transmission line of any type is prohibited.

- Transmission lines shall be secured to the tower following manufacturer’s specifications.  Black nylon tie wraps, insulated wire wrap or approved insulated cable clamps must be used.  Use of any uninsulated cabling or wire is prohibited.

- Double shielded, double braded or heliax type coaxial cable is required from radio equipment through isolators, band pass devices, and duplexers, etc., to heliax transmission line.  No RG-8 type cable will be allowed.

- Each transmitter shall be externally identified with a copy of the current FCC license, or IRAC authorization. Name and telephone number of the person responsible for the equipment maintenance, the receiver frequency, transmit/receive tone frequencies, and transmit frequency and power.

- The antenna shall not be indiscriminately moved after initial mounting and tests without prior notification and approval of the Technical Committee and the Authorized Officer.

- When radio interference occurs, notch filters, crystal filters and dual ferrite isolators and/or band pass devices may be required.  The need for additional filtering equipment will be determined on a case-by-case basis.

- All transmitting equipment shall be FCC-type accepted and meet their rules and regulations or conform to Part 5 “Standards” of the NTIA Manual of Regulations and Procedures for Federal Radio Frequency Management.

- All receivers must comply with Parts 2 and 15 of the current FCC rules or conform to Part 5 “Standards” of the NTIA Manual of Regulations and Procedures for Federal Radio Frequency Management.

- All RF transmission line systems shall be engineered, procured and installed with the intention of minimizing any effects upon the ambient RF noise floor environment.

- All antenna cables shall have an identification tag.

- Receivers will not be regulated; however, all receivers experiencing interference may need to be equipped with cavities or crystal filters.

- Power output of any system on the Elko Mountain Site shall not exceed 400 watts ERP (Effective Radiated Power).  Transmitter isolation in the output to the antenna will be determined on a case-by-case basis.  If a transmitter causes interference to another user that cannot be resolved by any know technical means, the new users will cease operation within 24 hours of notice by BLM.  Electromagnetic interference being denied as any radio frequency associated interaction that impedes or hinders another service.  In the event that further negotiations cannot resolve the interference problems, the new station will not be permitted to resume transmitting.

- System design must provide adequate isolation between antennas.

- If harmful spurious emissions and harmonic content are shown to be causing interference, the responsible user shall be required to take additional measure to suppress it.

- Each microwave and point-to-point system change or addition will be addressed individually by the Technical Committee to provide advice to the Authorized Officer to take appropriate actions.

- Any miscellaneous equipment that causes harmful interference shall not be used, or if installed, must be removed.

- Systems must be grounded in a manner that is compatible with existing user’s grounding so interference will not be compounded.

- All antennas and signal transmission media must be terminated with its own characteristic impedance when not in use.

- The noise floor contribution of any new equipment or changes to existing equipment must not cause the total noise floor to exceed the agreed upon maximum level.

- Housekeeping has environmental, visual, aesthetic and electromagnetic compatibility impact.  Debris, which is permitted to remain adrift, raises the noise floor for all users and gives rise to intermodulation potential, which often defies identification.  Therefore, all debris shall be cleaned up immediately and will not be allowed to accumulate on the site.

Recommended:

The following standards are recommended for new and existing installations.  Should it become necessary to eliminate interference, site users will be required to comply with these standards.

- Transmitters operating on this site should have sufficient separation to shield other operating equipment.  It is suggested that the equipment be made by the manufacturer for operation on a multiple user site.

- Transmitters operating on this site should also have a ferrite isolator with a minimum of 50 dB rejection in the reverse direction.  The isolator should be installed between the transmitter and the cavity.

- Notch type duplexers should be preceded by a band pass cavity.

- A low pass filter or a band pass cavity should be between the isolator and the antenna.

- Guy wires, bonding across clevices, brackets, etc., should be insulated.  Loose wire or metal objects must not be left on towers.

- It is recommended that a band pass cavity be placed in the feedline to receivers.

- Type “N” connectors are preferred over other type connectors.  Do not mix coax connectors with adaptors.

- It may be incumbent upon existing users to upgrade existing equipment to resolve interference if the new user is properly set up to prevent interference.  This situation will be addressed by the Technical Committee on a case-by-case basis.

SECTION 2:  Annual Inspection and Enforcement

- The Technical Committee and the BLM shall jointly conduct at least one annual inspection of each facility on the site.  This inspection will verify:

  - compliance with technical standards.

  - structural integrity.

  - electromagnetic compatibility.

  - general safety.

  - as-built plan accuracy.

- Any noncompliance found shall be recorded and include:

  - a description of the defect and the adverse impacts, which result.

  - what corrective action is required.

  - the name and address of the responsible part or organization.

  - the recommended time frame for completion of corrective measures to be taken.

- Copies of non-compliance reports and user responses shall be forwarded to the Technical Committee Chairperson for review and recommendations.

- The Bureau shall provide written notice of the scheduled inspection date to all site users at least 30 days in advance, and each user shall arrange to have a representative available at the site at the time of the inspection.

SECTION 3:  	When Interference Occurs

- All users shall cooperate fully with the Association and the BLM in identification and correction of any interference-related problems.

- Neither this Association nor the Bureau shall recognize interference complaints from users who are not members in good standing.

- When a new user applies for a right-of-way to install a system, or an existing user applies for an amendment on the site, the BLM will advise all of the existing users as to the technical and physical parameters of the proposed system so that they may ascertain if the proposed installation is physically and electronically compatible with their installed systems(s).

- The members will be given a period not to exceed thirty (30) days from receipt of the Notice of Site Availability from the BLM in which to comment to it and the applicant on probable interference.  Comments received will be forwarded to the Technical Committee for evaluation and recommendation for approval of the application to the BLM.

- If the technical evaluations reflect that there may be interference problems with other users, the applicant will have up to thirty (30) days to respond to the BLM on remedies for interference problems.  These remedies may include engineering analysis and other pertinent information.  A field test for compatibility may be requested at the expense of the applicant.  Based on the data submitted by the applicant, the Technical Committee will make a recommendation to the BLM with supporting rationale.

ARTICLE IV

SECTION 1:  Association Meetings

A quorum shall be present at any meeting to conduct any business of the Elko Mountain Communication Site User’s Association.  A quorum shall be defined as a simple majority of the members of the user’s association that are in good standing.

A. Annual

An annual meeting shall be held at the BLM office in Elko, Nevada, during the second week of September of each year.  Additional meeting may be scheduled at any time the Chairperson, with a majority of the association’s officers concurring, requests to carry out the functions of the user group.

B. Special

Special meetings to consider specific new issues shall beheld at a time and place as may be designated by the Chairperson, a quorum (simple majority) of the user group, or the BLM Elko Field Office Manager.  Notices for such meetings shall state the purpose (s) for which the meeting is called, and shall adhere to the advance notice requirement.  No business shall be transacted at special meetings except as stated in the notice unless the members at the meeting give their unanimous consent thereto.

SECTION 2:  Advance Notice

All meeting notices shall be distributed no less than 30 days before the scheduled date.  Exceptions may be made to respond to an emergency.  It shall include the date, time, place and an agenda of items for the meeting.  If any guests are scheduled to attend, that information should also be included.  At the discretion of the Chairperson, the requester of a special meeting may be required to pay the publications cost of advance notice for the associated special meeting.

SECTION 3:  Order of Business

Robert’s Rules of Order shall be followed in all procedural matters. Meetings shall have the following general form:

- Call to order

- Sign-in

- Reading of minutes of last meeting

- Report of Financial Committee

- Report of Technical Committee

- Determination of standing of members

- Old Business

- New Business

- Election of Officers (annual meeting)

- Appointment of Committees (annual meeting)

- Comments from Members

- Adjournment

ARTICLE V

SECTION 1:  The Association may amend or repeal bylaws if two-thirds of the voting members favor such action.  Proposed changes to the bylaws will be presented in writing to the Secretary/Treasurer at least 60 days prior to the annual meeting.  The proposed changes shall be reviewed by the officers of the Association, the chairperson of the Technical Committee and the BLM representative for presentation to the Association members at the annual meeting.  Votes may be cast in person by the holder, an authorized representative, by a written proxy carried by an attending member or by a prewritten decision.

SECTION 2:  The Association may enact such necessary supplements and committees that are deemed to be appropriate to carryout its functions.

SECTION 3:  The undersigned members of the Elko Mountain Communication Site User’s Association hereby adopt the Constitution and Bylaws of the Association and agree to support them.  Execution of this Constitution and Bylaws will bind the signatories to abide by the terms of the Elko Mountain Communication Site Management Plan.

Implementation of this agreement shall become effective upon its execution by the BLM Elko Field Office Manager after the signature of each of the existing right-of-way grant holders on the site.

APPENDIX F

ELKO MOUNTAIN COMUNICATION SITE

ROAD USERS AGREEMENT

This agreement pertains to the normal use and maintenance of the access road to the Elko Mountain Communication Site that is located on public land within T. 35 N., R. 56 E., MDM, Nevada, Section 26.  The access road will be authorized by a right-of-way reservation held in the name of the Bureau of Land Management.  The road is needed by all of the users of the communication site for surface access to the top of Elko Mountain.  The BLM shall not unilaterally assume financial responsibility for maintenance of the access road.

For the purposes of this agreement, normal maintenance shall be considered to be that which is necessary to keep the road in a serviceable condition for safe passage of vehicles and to prevent deterioration from that condition.

Since the FAA currently requires daily travel to the site, it must maintain passage for its own needs.  Until that situation changes, the Users Association will cooperate with FAA as the situation warrants contributing material, etc., to maintain the road in a safe condition.  No specific annual assessment is anticipated at this time.  Should conditions change so that FAA no longer requires daily travel to the site, this agreement must be modified to meet the new situation.  Should an assessment become necessary for normal maintenance of the road, the Secretary/Treasurer of the Association will collect each users pro rata share and maintain the money in a separate account to be used for the expenses of the Association to maintain the road in useable condition.  A process to determine a pro rata share will also be developed when it is needed.

Normal maintenance costs may vary from year to year as a result of unusual climatic conditions, unusually heavy traffic on the road or other unforeseen circumstances that may arise.  The pro rata share of the costs may also vary as existing users leave the site and/or new users occupy the site.  New applicants to occupy the Elko Mountain Communication Site shall be required to execute this Road Users Agreement by a stipulation to be placed in their right-of-way grant.

Damage to the road caused by unusual construction activity of a user(s) shall be repaired by the affected user(s) at its (their) sole expense.