# GLR-IN-069 Safety Briefing for October, 2003

Subj:   (a)  Refresher on Winter Operations

(b)  Emergency Checklist Memory Items Exercise of the Month

(a)  Refresher on Winter Operations

1.  Two kinds of in-flight icing:  airframe ice and carburetor ice.

2.  Airframe ice

-  Requires below-freezing temperatures and visible moisture (as in clouds, or rain falling into

below-freezing air).  Sleet (now called ice pellets) and dry snow are not significant

airframe icing concerns.

-  You must get out of it immediately.  Make a change.  E.g., reverse course to where you came

from, change altitude, or land (probably the surest thing to do).  Know what the freezing

level is.

-  Frost on wings (most often found in the morning) is a no-no for takeoff.

3.  Carb ice

-  Actually, this is a year-round potential.

-  Apparent by an unexplained drop in rpm (as the throttle venturi closes down with ice).  You

may first notice a loss in airspeed and/or altitude.

-  Apply full carb heat.  You may see engine roughness as the ice melts and is ingested into the

engine.  Keep it on until it smooths out.

4.  Other considerations

-  Watch for things like slush or blowing snow getting into control hinges or wheel pants, and

freezing in colder air aloft.

-  Watch out taxiing - sliding on ice, prop or wingtip strike in a snowdrift.

-  Don't slip on icy surface during preflight, getting plane out of or into hangar, etc.

5.  Cold weather starting

-  See the POH for the approved procedure for cold weather starting.

-  Don't over-prime.

-  Don't open throttle before cranking as much as you do in warm weather.  You need less of the

denser air to get the correct mixture for starting.

6.  Group add any thoughts or experiences.

(b)  Emergency Checklist Memory Items Exercise of the Month

This exercise asks each pilot to immediately write down the Memory/Immediate Action items (ONLY) from a random emergency.  Pilots have a designated number of seconds (8   seconds for this emergency) to do this, then must hold their paper in the air.

1.  The emergency for this month is .............ENGINE FAILURE DURING TAKEOFF ROLL

2.  Answer (spelled backwards):    -----         		ELTTORHT    -    ELDI

SEKARB         -	  YLPPA

CODE WORD:  BRAKES

A. Cecere, Safety Officer JCSS (GLR-IN-069)