Table 4.2b Description of 17-category (SiB) vegetation categories and physical parameters for N.H. summer (15 April - 15 October) and winter (15 October - 15 April).

| Vegetation Integer Identification | Vegetation Description | Albedo(%) | Moisture Avail. (%) | Emissivity (% at 9 m m) | Roughness Length (cm) | Thermal Inertia (cal cm-2 k-1 s-1/2) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Sum | Win | Sum | Win | Sum | Win | Sum | Win | Sum | Win |
| 1 | Evergrn. Broadlf. | 12 | 12 | 50 | 50 | 95 | 95 | 50 | 50 | 0.05 | 0.05 |
| 2 | Broadlf, Decids. | 16 | 17 | 30 | 60 | 93 | 93 | 50 | 50 | 0.04 | 0.05 |
| 3 | Decids. Evergrn. | 14 | 14 | 35 | 70 | 95 | 95 | 40 | 40 | 0.05 | 0.06 |
| 4 | Evergrn. Needlf. | 12 | 12 | 30 | 60 | 95 | 95 | 50 | 50 | 0.04 | 0.05 |
| 5 | Decids. Needlf. | 16 | 17 | 30 | 60 | 93 | 93 | 50 | 50 | 0.04 | 0.05 |
| 6 | Grnd. Tree Shrb. | 20 | 20 | 15 | 15 | 92 | 92 | 15 | 15 | 0.03 | 0.03 |
| 7 | Ground only | 19 | 23 | 15 | 30 | 92 | 92 | .12 | .10 | 0.03 | 0.04 |
| 8 | Broadlf. Shrb.P.G. | 19 | 23 | 15 | 30 | 92 | 92 | 12 | 10 | 0.03 | 0.04 |
| 9 | Broadlf. Shrb.B.S. | 19 | 23 | 15 | 30 | 92 | 92 | 12 | 10 | 0.03 | 0.04 |
| 10 | Grndcvr. DT. Shrb | 15 | 70 | 50 | 90 | 92 | 92 | 10 | 10 | 0.05 | 0.05 |
| 11 | Bare Soil | 25 | 25 | 2 | 5 | 85 | 85 | 10 | 10 | 0.02 | 0.02 |
| 12 | Agricltr. or C3 Grs | 17 | 23 | 30 | 60 | 92 | 92 | 15 | 5 | 0.04 | 0.04 |
| 13 | Perst. Wetland | 14 | 14 | 50 | 75 | 95 | 95 | 20 | 20 | 0.06 | 0.06 |
| 14 | Dry Coast Cmplx | 19 | 23 | 15 | 30 | 92 | 92 | 12 | 10 | 0.03 | 0.04 |
| 15 | Water | 8 | 8 | 100 | 100 | 98 | 98 | .01 | .01 | 0.06 | 0.06 |
| 16 | Ice cap & Glacier | 55 | 70 | 95 | 95 | 95 | 95 | 5 | 5 | 0.05 | 0.05 |
| 17 | No data |  |  |  |  |  |  |  |  |  |  |