| Job Number: SHSD- JRA- 16 Job Title: Ozone Generation during IAQ Remediations | Point Value → Parameter ↓ | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- |
| Job Description: Operation of an ozone generator to treat viable microbes in indoor air and on surfaces. | Frequency (B) | <once/year | <once/month | <once/week | <once/shift | >once/shift |
| Name(s) of Specific Application Risk Team Members: R. Wilson, R. Selvey, M. Rankine, J. Allen, J. Peters, F. Horn | Severity (C) | First Aid Only | Medical Treatment | Lost Time | Partial Disability | Death or Permanent Disability |
| Training Procedures List (Optional): Applicable Standard Operating Procedures: IH97300 | Likelihood (D) | Very Unlikely | Unlikely | Possible | Probable | Multiple |
| Approved by: R. Selvey Date: 05/17/07 Rev. #: 1 |  |  |  |  |  |  |
| Stressors (if applicable, please list all) Hypersensitive Individuals to mold and other IAQ allergens | Reason for Revision (if applicable): Reviewed JRA for continued applicability. Updated to remove note from “additional Control” column. | Comments: |

|  |  | Without Controls | Before Additional Controls | After Additional Controls |  |
| --- | --- | --- | --- | --- | --- |
| Activity | Hazard | # of People A | Frequency B | Severity C | Likelihood D | Risk* AxBxCxD | Control(s) | Stressor | # of People A | Frequency B | Severity C | Likelihood D | Risk* AxBxCxD | Control(s) Added to Reduce Risk | Stressors | # of People A | Frequency B | Severity C | Likelihood D | Risk* AxBxCxD | % Risk Reduction |
| Loading equipment into and out of the transportation vehicle (ozone generator, signs, power cord) | ergonomics- lifting injury, slips, trips, falls | 1 | 2 | 3 | 2 | 12 | Equipment is not heavy and has handles for lifting | N | 1 | 2 | 3 | 2 | 12 |  |  |  |  |  |  |  |  |
| Driving to and from the test site | Automobile accident- impact injury | - | - | - | - | - | See driving JRA for site. SHSD has no additional risk in our operation. | - | - | - | - | - | - |  |  |  |  |  |  |  |  |
| Exposure to IAQ in areas of concern | Inhalation of irritants, allergens, toxic mold spores | 1 | 2 | 3 | 3 | 18 | Limited time in area, access by normal occupants as an indicator of exposure potential, respiratory protective equipment if necessary. | N | 1 | 2 | 3 | 2 | 12 |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | Hypersensitive individuals- another non-sensitive IKH evaluator conducts the ozonation. | Y | 1 | 1 | 3 | 2 | 6 |  |  |  |  |  |  |  |  |
| Operation of the ozone generator | toxic gas – ozone and by-products of oxidization of room materials | 2 | 2 | 5 | 5 | 100 | SOP limits occupancy during gas generation, procedures limits exposure to the operator to a few seconds at the start of generation, posting, barrier tape, access control, required delay time before occupancy, test strips for ozone for re-occupancy, leave exhausting HVAC on, Isolating multiple room HVAC systems, Timer on the unit, remove plants and food stuff from area prior to ozonation. | N | 1 | 2 | 3 | 2 | 12 |  |  |  |  |  |  |  |  |
|  | Electrical Shock | 1 | 2 | 3 | 3 | 18 | Sealed Unit, grounded cord, fuse. [NOT UL listed.] | N | 1 | 2 | 3 | 2 | 12 |  |  |  |  |  |  |  |  |
|  | Moving Parts | 1 | 2 | 3 | 1 | 6 | Fan has metal grill preventing access by body parts | N | 1 | 2 | 2 | 1 | 4 |  |  |  |  |  |  |  |  |
|  | UV light from ozone generation lamp | 1 | 2 | 3 | 2 | 12 | Unit designs shield most light, no direct path to eye | N | 1 | 2 | 2 | 2 | 8 |  |  |  |  |  |  |  |  |
|  | Noise | 1 | 2 | 3 | 2 | 12 | Unit makes less than 65dBA by design. | N | 1 | 2 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |

Further Description of Controls Added to Reduce Risk: Need to have AHJ analysis on meter for electrical safety. Call mfgr regarding UL listing. If not, AHJ evaluation will be needed. {Status: All equipment was evaluated and manufacturers called when applicable.]

Lesson Learned from this Risk Assessment: Ozone generator is not UL listed.

| *Risk: | 0 to 20 | 21 to 40 | 41-60 | 61 to 80 | 81 or greater |
| --- | --- | --- | --- | --- | --- |
|  | Negligible | Acceptable | Moderate | Substantial | Intolerable |