Appendix B. Special Codes

Exchange File Format

Version 3.3 (9/10/2004)

Special Codes

Some fields have ranges defined by special codes.  The following tables define these codes.

Existence Flags

Each data field has a corresponding existence flag.  The following are the positions for each existence flag:

Column 94:	Existence flag for field 1

Column 96:	Existence flag for field 2

Column 98:	Existence flag for field 3

Column 100:	Existence flag for field 4

Column 102:	Existence flag for field 5

Column 104:	Existence flag for field 6

Column 106:	Existence flag for field 7

Column 108:	Existence flag for field 8

Column 110:	Existence flag for field 9

Column 112:	Existence flag for field 10

The following are valid values for Existence Flags:

0 		Known

1  		Unknown

Obstruction Accuracy Codes

Accuracy codes are 2 character codes which designate the accuracy of a feature. The accuracy code is not the accuracy at which a feature is collected but rather the minimum accuracy required for a feature depending on where it falls within the OIS.

The first character of the accuracy code is the horizontal accuracy.

Value		Accuracy

1		20 feet

2		50 feet

3		100 feet

The second character of the accuracy code is the vertical accuracy.

Value		Accuracy

A		3 feet

B		10 feet

C		20 feet

D		50 feet

M		ESTIMATED MAXIMUM ELEVATION*

?		NO TOP ELEVATION – NO VERTICAL ACCURACY

The special accuracy code 99 indicates features that are not obstructions (such as Geodetic Control, Photo Control, Polygons, etc.). Refer to the “FAA No. 405” for minimum allowable accuracies for these features.

A vertical accuracy designation of M, estimated maximum elevation, is provided when the elevation of an object cannot be determined precisely, as with mobile cranes.

Horizontal Datum Tie Codes

- 	 			UNDEFINED

B  	5 CM			GPS ANA

C 	50 CM			GPS ADAM

D 	1:100,000		CLASSICAL 1ST ORDER

E 	1:50,000			CLASSICAL 2ND ORDER CLASS I

F 	1:20,000			CLASSICAL 2ND ORDER CLASS II

G 	1:10,000			CLASSICAL 3RD ORDER CLASS I

H 	1:5,000			CLASSICAL 3RD ORDER CLASS II

I 	15 FT			PHOTOGRAMMETRIC

J 	> 15 FT			OTHER

Ellipsoidal Datum Tie Codes

-  				UNDEFINED

B  	15 CM			GPS ANA

C 	50 CM			GPS ADAM

D 	1 M		 	GEOID 96 MODEL (ORTHO+GEOID)

E 	> 1 M			OTHER

Orthometric Datum Tie Code

-  				UNDEFINED

A  	1.0 MM * SQRT(K)	CLASSICAL 1ST ORDER CLASS I

B 	1.4 MM * SQRT(K)	CLASSICAL 1ST ORDER CLASS II

C 	2.0 MM * SQRT(K)	CLASSICAL 2ND ORDER CLASS I

D 	2.6 MM * SQRT(K)	CLASSICAL 2ND ORDER CLASS II

E 	4.0 MM * SQRT(K)	CLASSICAL 3RD ORDER

F	24.0 MM * SQRT(K) 	CLASSICAL AOC VERTICAL TIE

G 	25 CM			GPS ANA

H 	10 FT			PHOTOGRAMMETRIC

I 	> 10 FT			OTHER

Point Survey Status Attribute Code

- 	Undefined

D   	Not Verified

C   	Checked by Survey Methods

W  	New Point

I    	Checked by Visual Inspection

G   	Checked by General Inspection

R   	Retied

B   	New Base Elevation

T   	New Top Elevation

V   	New Vertical Position

?   	Questionable Position Change

P 	Photogrammetrically Determined Position

Control Type Attribute Code

-	Undefined

P	PACS

A	SACS

C	TACS

T	Triangulation Station

L	Local Control

S	Sub Point (Photo Control)

NAVAID Type Attribute Code

Code	Abbreviation	Full Name

-			Undefined

+	APBN		Airport Beacon

=	ALS		Approach Lights

W	ARSR		Air Route Surveillance Radar

A	ASR		Airport Surveillance Radar

,	ATCBI		ATCBI

J	BCM		Back Course Marker

D	DME		Distance Measuring Equipment

Y	FM		Fan Marker

F	GS		Glide Slope

G	IM		Inner Marker

K	LDA		Localizer Type Directional Aid

Z	LFR		Low Frequency Radio Range

R	LMM		Locator Middle Marker

E	LOC		Localizer

S	LOM		Locator Outer Marker

>	LRR		Long Range Radar

L	MLSAZ		MLS Azimuth Guidance

N	MLSEL		MLS Elevation Guidance

V	MLSDME	DME associated with MLS

H	MM		Middle Marker

X	NDB		Nondirectional Beacon

#	NDB/DME

B	OTHER		Other NAVAID

I	OM		Outer Marker

&	PAPI		Precision Approach Path Indicator

%	PAR		Precision Approach Radar

!	PLASI		PLASI

*	PVASI		Pulsating Visual Approach Slope Indicator

$	REIL		Runway End Identifier Lights

O	SDF		Simplified Directional Facility

:	STARS		STARS component

M	TACAN		Tactical Air Navigation

C	TDR		GCA Touchdown Reflectors

(	TRCV		Tri-color Visual Approach Slope Indicator

)	TVASI		(T(-Visual Approach Slope Indicator

~	VASI		Visual Approach Slope Indicator

P	VOR		VHF Omni Directional Range

T	VOR/DME

Q	VORTAC	VOR + TACAN

Special Attribute Code

-	Undefined

T	Outside specified Obstruction Identification Surface (OIS)

Note: T refers to a feature which falls outside the surfaces defined in the FAA NO. 405 but which is of interest.

Runway Approach Type Codes

Runway_Approach_Types:  ANA surveys

NUL  	NUL

PC1  	ANA PC, Cat 1

PC2  	ANA PC, Cat 2/3

AP1  	ANA PC, Cat 1 Revision Date: January 28, 2004

AP2  	ANA PC, Cat 2/3 Revision Date: January 28, 2004

Runway Approach Types: CGR surveys

NUL  	NUL

CGP  	PRECISION INSTRUMENT APPROACH, INCLUDES APPROACH AND PRIMARY SURFACES ONLY

CGD	NONPRECISION APPROACH – VISIBILITY MINIMUMS AS LOW AS ¾ MILE INCLUDES APPROACH AND PRIMARY SURFACE ONLY

Runway Approach Types: F77 surveys

NUL  	NUL

PIR  	PRECISION INSTRUMENT APPROACH

ANP  	NONPRECISION APPROACH - UTILITY RUNWAY

C       NONPRECISION APPROACH - VISIBILITY MINIMUMS GREATER THAN 3/4 MILE

D       NONPRECISION APPROACH - VISIBILITY MINIMUMS AS LOW AS 3/4 MILE

AV   	VISUAL APPROACH - UTILITY RUNWAY

BV   	VISUAL APPROACH

BVC  	BV w/Supplemental C

Runway Approach Types: OEP surveys

NUL  	NUL

OEP  	Operation Evolution Plan

Runway Approach Types: RBI surveys

NUL  	NUL

RBI  	Ron Brown Airport Initiative

Poly Feature Survey Status Attribute Code

- 	Undefined

D   	Not Verified

C   	Checked by Survey Methods

W  	New Feature

I    	Checked by Visual Inspection

G   	Checked by General Inspection

R   	Retied

B   	New Base Elevation

T   	New Top Elevation

V   	New Vertical Position

?   	Questionable Position Change

P   	Photogrammetrically Determined Position

Source Codes

F – Field (ground survey: GPS or Classical)

E – Manual Entry (direct numerical edits performed in the field)

R – Remote Sensing (measurements made from interpreted imagery)

O – Office (direct numerical edits performed in the office)