November 21, 1997

Contract # TW-0928

SPECIAL SPECIFICATION

SECTION 08711-S

FINISH HARDWARE

Page

PART 1 - GENERAL

1.01 	Description of Work

1.02 	References

1.03 	Submittals

1.04 	Quality Assurance

1.05 	Delivery, Storage, and Handling

PART 2 - PRODUCTS

2.01 	Manufacturers

2.02 	General Hardware Schedule

PART 3 - EXECUTION

3.01 	Examination	10

3.02	Installation	10

3.03 	Adjustments	10

SPECIAL SPECIFICATION

SECTION 08710-S

FINISH HARDWARE

# PART 1 - GENERAL

## 1.01	DESCRIPTION OF WORK

Section includes furnishing and installing finish hardware as scheduled and/or as called for on Contract documents.  It does not include hardware for aluminum entrance doors.

## 1.02	REFERENCES

A.	American National Standards Institute/Builder's Hardware Manufacturer's Association (ANSI/BHMA)

A156.1	Specification for Butts and Hinges

A156.2	Specification for Locks and Latches

A156.3	Specification for Exit Devices

A156.4	Specification for Closers

A156.5	Specification for Auxiliary Locks

A156.6	Specification for Architectural Door Trims

A156.10	Specification for Automatic Doors

A156.15	Specification for Closer/Holder Release Devices

A156.16	Specification for Auxiliary Hardware

A156.18	Specification for Materials and Finishes

A156.19	Specification for Assisted Doors and Low Energy Power Operated Doors

B.	Factory Mutual (FM)

Fire Tests of Materials

C.	Federal Specifications (FS)

FF-L-2740	Locks, Combination

D.	National Fire Protection Association (NFPA)

101	Life Safety Code

E.	Underwriter's Laboratory, Inc. (UL)

UL 768	Standard for Safety Combination Locks

UL 305	Standard for Safety

F.	Uniform Building Code (UBC)

G.	Uniform Federal Accessibility Standards (UFAS)

## 1.03	SUBMITTALS

General:  Submit the following items in accordance with provisions of  Division 1, Section 01300-S "Descriptive Submittals."

A.	Product Data:  Submit manufacturer's catalog data for each item of finish hardware, including evidence of UL listing for fire rated hardware.

B.	Quality Certification:  Submit manufacturer's written certification that hardware to be used on Project is Grade One quality.

## 1.04	QUALITY ASSURANCE

A.	Qualifications:  Finish hardware manufacturer shall have minimum of ten (10) years experience in manufacturing of hardware.

B.	Product Quality:  Provide products which have been tested and are in compliance with references listed in Section 1.02 of this specification for required assemblies.

C.	Warranties:  Provide ten (10) year warranty on closers and one (1) year warranty on all other hardware.

## 1.05	DELIVERY, STORAGE, AND HANDLING

A.	Packing and Shipping:  Finish hardware shall be packed and shipped to job site in unopened boxes, clearly labeled with manufacturer's name and item description.

B.	Storage and Protection:  Store finish hardware in manner to prevent damage until needed for installation.

# PART 2 - PRODUCTS

## 2.01	MANUFACTURERS

A.	General:  Provide Finish Hardware as Follows:

1.	Stanley:  Butt hinges, electric hinges.

2.	Sargent:  Exit devices, locksets, padlocks, door closers, mullions and latchsets.  --No substitutions allowed except in the case of door closers--

3.	Simplex:  Mechanical push button combination locks.

4.	Hirsch:  Electrical push button combination locks.

5.	Trimco:  Silencers, door bumpers, mop plates, kick plates, stops/holders, flush bolts, push/pull latches.

6.	Honeywell:  Electro-magnetic door holders.

7.	National Guard Products (NGP):  Thresholds, door sweeps and door bottoms, weatherstripping, smoke seals, astragals.

8.	Horton Automatics, Power Access Corporation or Gyro Tech:  Low energy, power-operated interior door openers.

B.	Substitutions:  Only under the provisions of Division 1, Section 01600-S.

## 2.02	GENERAL HARDWARE SCHEDULE

A.	General: Hardware shall be identified by ANSI as Grade One hardware where applicable.  Where applicable, function shall be as noted on Contract documents, or as chosen at time of submittals.

B.	Opening Force:  Maximum force for pushing or pulling open door shall be 8.5 pounds (3.9 kg) for exterior and 5 pounds (2.3 kg) for interior doors.

C.	Manufactured Units:  Unless otherwise indicated in finish hardware schedule or elsewhere in Contract documents, provide the following hardware:

1.	Butt Hinges: 4-1/2 inches (114 mm) x 4-1/2 inches (114 mm), steel, full mortise, five knuckle, ball bearing, flat tip hinges with polished and plated finish.

a.	Provide heavy weight hinges on exterior doors, airlock entry doors, doors with closers, and toilet room entry doors.  Use Stanley FBB 168.

b.	Provide standard weight hinges on all other doors.  Use Stanley FBB 179.

c.	Provide manufacturer's heavy duty non-removable pins at exterior doors, designated vault type room doors, and other doors as designated on Contract documents.

2.	Electric Hinges:  Provide one each electric hinge on doors where electric devices or electric locks are specified elsewhere in Contract documents.  Use Stanley CE FBB 168.

3.	Locks and Latches:  Locks and latches shall be lever type, positive latching, and shall be bored locks and latches with 2-3/4 inch (70 mm) backset, 1/2 inch (13 mm) latch bolt throw, 4-1/2 inch (114 mm) lever with 3-1/2 inch (89 mm) outside and inside rose where applicable to conceal through bolts.

a.	Locksets shall be Sargent 10 Line Series with number 808 strike and appropriate function.

(1)	28-10G04-LL for equipment and mechanical chase doors only.

(2)	28-10G05-LL provide only when indicated elsewhere in Contract documents.

b.	Latchsets shall be Sargent 10 Line Series with number 808 strike and appropriate function.

Provide 28-10U15-LL for all doors, including utility rooms, where locksets, exit devices, combination locks  and auxiliary latchsets are not specified.

c.	At all toilet room doors, provide auxiliary latchsets.

Provide Sargent 24-114P x 808 strike.

4.	Exit Devices:  Provide exit device only where specified on Contract documents.  Exit device latch bolts shall be released by depressing actuating push pad.

a.	For single doors and double doors with removable or fixed center mullion, exit device shall be Sargent Series 8888.  The device shall have reversible rim, appropriate strike, and lever handle trim.

(1)	At non-fire rated doors, provide Model 8888 x 713-8 ETL with Model 641 strike, and at double doors add Sargent model 980 aluminum removable mullion or fixed steel mullion.

(2)	For fire rated doors, provide Model 12-888 x 713-8ETL with Model 649 strike, and at double doors add Model 12-980 fire rated steel removable mullion or fixed steel mullion.

b.	For pair of active doors without center mullion, exit devices on each leaf shall be Sargent Series 8700 vertical rod type exit device.  The devices shall have appropriate model 629 top and model 624 bottom strikes and shall have lever handle trim.

(1)	For non-fire rated door, provide model 8713 x 713 ETL.

(2)	For fire rated doors, provide model 12-8713 x 713 ETL.

c.	For single doors and double doors with removable or fixed center mullion, and which are indicated to be unlocked via electric actuation device (e.g., badge reader, key switch), provide Sargent Series 8800 exit device with electro-mechanical lever control.

(1)	At non-fire rated doors, provide Model 8876-776ETL with appropriate strike, electric butt hinge, power supply, and at double doors add Sargent Model 980 mullion if fixed steel mullion is not indicated to be installed.

(2)	At fire rated doors, provide Model 12-8876-776ETL with appropriate strike, electric butt hinge, power supply, and at double doors add Model 12-980 fire rated steel removable mullion if fixed steel mullion is not indicated to be installed.

5.	Closers:  Closers shall be surface mount type with parallel arms, back check, key control valves, and 50% power adjustments and shall facilitate automatic closure of door.

Provide Sargent Model EB350 series closers on exterior doors, interior fire rated doors, doors with electro-magnetic door holders, interior doors with exit devices, push-pull devices, auxiliary latchsets and additional doors indicated on Contract documents.

6.	Mechanical Push-Button Combination Locks:  Provide mechanical push-button combination locks only when noted in Contract documents.  Provide Simplex Unican L1000-2B with key bypass.  Provide uncombinated Falcon core 12607A.

7.	Electrical Push-Button Combination Locks:  Provide electrical push-button combination locks only when noted elsewhere in Contract documents.  Unless otherwise indicated, provide Hirsch key pads, controllers, etc. per Contract documents.

8.	Architectural Door Trim:  Kick plates shall be of heavy duty 16 gauge (2 mm) smooth surface metal.

Provide Trimco 1024- 12" x 2" (305 mm x 51 mm) LDW on push side of doors scheduled for exit devices, on both sides of doors with push/pull devices or auxiliary latchsets.

9.	Electro-Magnetic Door Holder:  Provide electro-magnetic door holder device only when specified in Contract documents.  The device shall be UL listed and FM approved and shall be fail safe, conforming to National Fire Code Nos. 80 and 101.  The release device shall be so designed that it may be automatically released by power interruption and manually released by some simple and readily obvious operation.

Provide Honeywell series S4003 for 120 VAC.  Provide appropriate floor mount pedestal where needed for floor mount installation.

(1)	In new construction, where indicated to be installed on walls, door holder shall be flush mounted.

10.	Door Coordinators:  Provide coordinator at all pairs of active doors without center mullion.  Use Sargent Model 3487 with Model 3497 carry open bar .

11.	Auxiliary Hardware:  Auxiliary hardware shall be provided only where specified herein and/or elsewhere on Contract documents.

a.	Combination stop and holder device shall be Trimco model 1224-5  manually operated device.

b.	Concave wall mount door bumpers shall be provided at doors opening onto adjacent walls.	Provide Trimco model W1276-CCS Series  with appropriate fasteners.

c.	Floor mount door bumpers shall be provided on doors where wall type door bumpers are not provided.  Provide Trimco model W1210ES Series.

d.	Provide Trimco model 1229A  neoprene door silencers on non-fire rated  doors.  Provide three per each door.

e.	Provide flexible silicone rubber smoke seal on fire rated doors.  Use NGP 2525 x D.S.

f.	Manual flush bolts shall be Trimco 3917 top and bottom.

g.	Provide weatherstripping, door sweep(s), and threshold at exterior doors.

(1)	Provide NGP 160 weatherstripping at all non-fire rated exterior doors.

(2)	Provide NGP 200 NA door sweep at exterior doors.

(3)	Provide NGP 424 threshold at exterior doors.

h.	Provide security astragal on exterior pairs of doors without center mullions and exit devices.  Provide NGP 139 SP.

i.	Provide NGP 125 NGA astragal for all other fire rated and non-fire rated double doors without center mullion where security astragal is not specified.

j.	Automatic door bottoms for both fire rated and non-fire rated doors shall be NGP 420A.

12.	Low Energy Power Operated Door Openers:  On specified doors only, provide power operated door opener(s).  The power opener shall be low energy, self-contained electric operating mechanism.  It shall be powered open with DC motor working through reduction gears.

a.	The motor shall be off when door is in closing mode.

b.	The door shall be capable of being manually opened or closed with power on or off without damage to mechanism.

c.	The opener shall include the following variable adjustments in compliance with ANSI A156.19.

(1)	Opening Speed - three to five seconds

(2)	Closing Speed - three to five seconds

(3)	Time Delay Before Closing - five to twenty-five seconds

d.	Opening and closing force, measured 2" (51 mm) out from lock stile of door, shall not exceed 15 pounds (6.8 kg) of force to stop door when operating in either direction.

e.	The opener shall include means of turning off opening force when door is stopped for one second.  After stopping door, it should then close and opener shall reset itself to accept another signal.

f.	The opener shall be mounted in extruded aluminum cover.

g.	Provide two (2) 6" (152 mm) round stainless steel push plate control switches marked "Handicapped" on each side of opening, unless otherwise indicated in Contract documents.

h.	Furnish 120 VAC, 60 cycle, single phase, 15 amp service to the operator.

14.	Electric Strikes:  When noted elsewhere in Contract documents, provide heavy duty electric strikes fully compatible with door, frame, and hardware specified for intended application.  Strike shall have latchbolt monitoring capability.

D.	Fire Rated Door Hardware:  Fire rated door hardware shall be listed and labeled by Underwriter's Laboratories (UL) and Factory Mutual (FM) as "Fire Exit Hardware."  Exit devices on fire rated doors shall not have dog down capability.

E.	Finishes:  Finish for all hardware shall be US32D, plated satin stainless, steel.

F.	Cylinders and Keys:  Unless otherwise specified, locks shall be furnished with cylinders and two keys and shall be capable of accepting Sargent six-pin tumbler cylinders without modification.  Keyway style will be selected at time of submittals.  Unless otherwise directed, provide zero pinned cylinders.

G.	Fabrication:  Manufacturer's hardware shall conform to published templates prepared for screw installation.

H.	Fasteners:  Furnish screws for installations with each hardware item.  Provide concealed fasteners for hardware units which are exposed when door is closed.

# PART 3 - EXECUTION

## 3.01	EXAMINATION

Examine materials on which hardware is to be installed to check for surface defects including warpage which might impede performance of hardware.

## 3.02	INSTALLATION

Install hardware per manufacturer's installation instructions, being careful not to damage finish on hardware.

A.	Butt Hinges:  Install minimum of 1-1/2 pair per door on doors no taller than 7 feet 2 inches (2.18 m), otherwise install two (2) pair butt hinges per door.

B.	Lock and Latches:  Install locks and latches at 36 inches (914 mm) above bottom of door.

C.	Dial and Push Button Combination Locks:  Install per manufacturer's installation instructions at 48 inches (1.2 m) above finish floor.

D.	Push Plate Control Switches:  Install 6" (152 mm) round push plate control switches at 9" (229 mm) and 39" (991 mm) above finish floor to center line of round plates.  Two (2) plates are required on each side of opening.

## 3.03	ADJUSTMENTS

Hardware shall be adjusted and demonstrated to function properly.  Damaged or defective hardware shall be replaced at no cost to Sandia National Laboratories (SNL).

Manufactures Listed:

Hinges									Stanley

Exit devices, locksets, push/pull latch, door closers			Sargent

Automatic door operator, wall switch					Norton

Flushbolts, kickplates, stops						Trimco

Thresholds, weatherstripping, door bottoms, smokeseal		NGP

Electrified strike							HES

Special Exiting Hardware						Adams Rite

HW Set 1

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF 90 min.

3 EA		Hinges	FBB168 4.5” x 4.5”  x US32D		STA

1 EA		Exit Device 12-8813-ETL x US32D			SAR

1 EA		Door Closer EB350-UO				SAR

1 EA		Kickplate 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 17’					NGP

HW Set 2

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF

3 EA		Hinges	FBB168 4.5” x 4.5”  x  NRP  US32D		STA

1 EA		Exit Device 12-8813-ETL x US32D			SAR

1 EA		Door Closer EB350-UO				SAR

1 EA		Kickplate 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 424 x 36”					NGP

1 SET		Weatherstripping 160-36” x 84”			NGP

1 EA		Door bottom zoona x 36”				NGP

HW Set 3

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF

3 EA		Hinges	FBB168 4.5” x 4.5” x US32D		STA

1 EA		Lockset 28-10G04-LL x US32D    			SAR

(knurled surface)

1 EA		Door Closer EB350-UO				SAR

1 EA		Wall Stop W1276CCS x US32D			TRI

HW Set 4

Pair

3/0 x 7/0 x 1 ¾”

6 EA		Hinges	FBB168 4.5” x 4.5” x US32D		STA

2 EA		Flushbolts 3917-12” x US32D			TRI

1 EA		Lockset 28-10G04-LL x US32D			SAR

(knurled handle)

1 EA		Lockset 28-10U94-LL x US32D			SAR

(knurled handle)

1 EA		Door Closer EB350-UO @ active leaf		SAR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

2 EA		Wall Stops W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 20’					NGP

HW Set 5

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF

3 EA		Hinges	FBB168 4.5” x 4.5” x  US32D		STA

1 EA		Lockset 28-10GO5-LL x US32D			SAR

(knurled handle)

1 EA		Door Closer EB350-UO				SAR

1 EA		Wall Stop W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 17”				NGP

HW Set 5A

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF 20 min.

3 EA		Hinges	FBB168 4.5” x 4.5”  x  US32D		STA

1 EA		Lockset 28-10U15-LL x US32D			SAR

(knurled handle)

1 EA		Door Closer EB350-UO				SAR

1 EA		Wall Stop W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 17’					NGP

HW Set 6

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF  90 min.

3 EA		Hinges	FBB168 4.5” x 4.5” x  NRP  US32D		STA

1 EA		Exit Device 12-8813-ETL x US32D			SAR

1 EA		Door Closer EB350-UO				SAR

1 EA		Kickplate 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 424 x 36”					NGP

1 SET		Weatherstripping 160-36” x 84”			NGP

1 EA		Door bottom zoona x 36”				NGP

HW Set 6A

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF  20 min.

3 EA		Hinges	FBB168 4.5” x 4.5” x  NRP  US32D		STA

1 EA		Exit Device 8813-ETL x US32D			SAR

1 EA		Door Closer EB350-UO				SAR

1 EA		Kickplate 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 424 x 36”					NGP

1 SET		Weatherstripping 160-36” x 84”			NGP

1 EA		Door bottom zoona x 36”				NGP

HW Set 7

Single Door

3/0 x 80 x 1 ¾”  Alum. X Alum.

4 EA		Hinges	FBB168 4.5” x 4.5” x   US32D		STA

1 EA		Exit Device 12-8813-ETL x US32D			SAR

1 EA		Automatic Door Operator 6660-POR x DB		NOR

2 EA		Wall Switches 661 x DB				NOR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 513 x 36”					NGP

1 SET		Weatherstripping 160-36” x 96”			NGP

1 EA		Electrified Strike 7083 x  US32D			HES

1 EA		Door bottom Zoona x 36”				NGP

HW Set 8

Pair Doors

6 EA		Hinges	FBB168 4.5” x 4.5” x   US32D		STA

2 EA		Exit Devices 12-8715-ETL x US32D			SAR

2 EA		Door Closers EB350-UO				SAR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

2 EA		Wall Stops W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 20’					NGP

HW Set 9

Single Door

3/0 x 7/0 x 1 ¾” WD x HMF

3 EA		Hinges	FBB179 4.5” x 4.5” x  NRP  US32D		STA

1 EA		Lockset 28-10G05-LL x US32D			SAR

(knurled handle)

1 EA		Wall Stops W1276CCS x US32D			TRI

HW Set 10

Pair Doors

3/0 x 7/0 x 1 ¾” WD x HMF

6 EA		Hinges	FBB168  4.5” x 4.5” x   US32D		STA

2 EA		Flushbolts 3917-12” x US32D			SAR

1 EA		Lockset 10U94-LL x US32D				SAR

(knurled handle)

1 EA		Lockset 28-10G05-LL x US32D			SAR

(knurled handle)

1 EA		Door Closer EB350-UO @ Active Leaf		SAR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

2 EA		Wall Stops W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 20’					NGP

HW Set 11

Single Door

3/0 x 7/0 x 1 ¾” WD x HMF

3 EA		Hinges	FBB168  4.5” x 4.5” x   US32D		STA

1 EA		Push/Pull Latch 24-114P x 808 Strike		SAR

1 EA		Door Closer EB350-UO 				SAR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 17’					NGP

HW Set 12

Single  Door

3/0 x 7/0 x 1 ¾” HMD x HMF

3 EA		Hinges	FBB168  4.5” x 4.5” x   NRP x US32D	STA

1 EA		Lockset 28 10G04-LL x US32D			SAR

(knurled handle)

1 EA		Door Closer EB350-UO 				SAR

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 424 x 36”					NGP

1 SET		Weatherstripping 160-36” x 84”			NGP

1 EA		Door Bottom Zoona x 36”				NGP

HW Set 13

Pair  Doors

3/0 x 7/0 x 1 ¾” HMD x HMF

6 EA		Hinges	FBB168  4.5” x 4.5” x  US32D		STA

1 EA		Lockset 28 10G05-LL x US32D			SAR

(knurled handle)

2 EA		Flushbolts 3917-12” x US32D			TRI

1 EA		Lockset 10U94-LL x US32D				SAR

1 EA		Door Closer EB350-UO @ Active Leaf		SAR

1 EA		Threshold 424 x 72”					NGP

1 EA		Electrified Strike   7083 x US32D			HES

1 SET		Weatherstripping 160-72” x 84”			NGP

HW Set 14

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF  90 min.

3 EA		Hinges	FBB168 4.5” x 4.5” x  NRP  US32D		STA

1 EA		Special Exiting Hardware:  Heavy Duty

Deadlatch Series  #4710 with #4560

latch handle.						Adams Rite

1 EA		Door Closer EB350-UO				SAR

1 EA		Kickplate 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 424 x 36”					NGP

1 SET		Weatherstripping 160-36” x 84”			NGP

1 EA		Door bottom zoona x 36”				NGP

HW SET 15

3 EA  		Hinges # FBB 179 4 ½” x 4 ½” US32D		STA

1 EA		Lockset 28-10G04 LL CL Keyway			SAR

1 EA		Electric Strike	 712 x 24VPC x LCM			FOLAD

1 EA		Closer	 EB350-UO					SAR

1 EA		Door bumper	 W1276-CCS				TRI

1 EA		Smoke Seal # 2525 x 17’				NGP

1 EA		Kick aluminum plate 1025 - 12 x 34” US32D	TRI

1 EA		Door Sweep   #98v					NGP

HW Set 16

Single Door

3/0 x 80 x 1 ¾”  Alum. x Alum.

4 EA		Hinges	FBB168 4.5” x 4.5” x   US32D		STA

1 EA		Exit Device 12-8813-ETL x US32D			SAR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

1 EA		Wall Stop W1276CCS x US32D			TRI

1 EA		Threshold 513 x 36”					NGP

1 SET		Weatherstripping 160-36” x 96”			NGP

1 EA		Door bottom Zoona x 36”				NGP

HW Set 17

Single Door

3/0 x 7/0 x 1 ¾” HMD x HMF 20 min.

1 EA		Mechanical Push-Button Combination Lock

Unican L1000-2B					Simplex

3 EA		Hinges	FBB168 4.5” x 4.5” x  US32D		STA

1 EA		Lockset 28-10GO5-LL x US32D			SAR

(knurled handle)

1 EA		Wall Stop W1276CCS x US32D			TRI

1 Roll		Smokeseal 2525 x 17”				NGP

HW set 18

Pair Doors

6 EA		Hinges FBB168  4.5” x 4.5” x NRP US32D		STA

2 EA		Exit Devices 12-8715-ETL x US32D			SAR

2 EA		Door Closers EB350 -	 UO				SAR

2 EA		Kickplates 1025-12” x 34” x US32D			TRI

1 EA		Wall Stops  W1276 CCS x US32D			TRI

1 Roll		Smokeseal  2825 x 20’				NGP

2 EA		Electric Holdopens Surface Mounted

Model  S 4003A  1011				Honeywell

END OF SECTION