August 7, 2008

Amendment 6:  Modifications to Summary of the work Section 01100

1.2	Work Under These Specifications

A.  	Contractor shall furnish all materials, labor and equipment for the work described below. Measurement and payment shall be as defined below.  Supply all labor materials and equipment necessary to layout; perform earthwork; aggregate base, broom finished concrete under shelter, sidewalks; wood benches; prefabricated shelter with masonry restroom and storage room including all plumbing and electrical work; seeding; construction of trash enclosure; installation of government supplied bridge and  modification/renovation of that bridge including concrete bridge abutments; boardwalk with curbs and guardrails at locations shown along with concrete boardwalk abutments; and all other miscellaneous work as shown on drawings.

Item 1 – Prefrabricated Shelter and Masonry Restroom with storage and kiosk shall include all work, labor materials and equipment necessary, but not limited to excavation, foundations, footings, supplying and erection trash enclosure and shelter with metal roof, concrete, carpentry, masonry work for restroom/storage, including, siding, doors, windows, insulation; toilet accessories; plumbing, electrical, ventilation, and electric heat; staining and painting and all other miscellaneous work as shown on drawings.

This work shall also include the construction of trash enclosure (concrete work for trash enclosure only is in place).

Shelter/Restroom and trash enclosure will not be measured for payment and will be paid for on a lump sum basis.

Item 2 - Bridge: Installation and modification of Government supplied used metal pedestrian bridge frame. The work shall include all work, labor materials and equipment necessary, but not limited to concrete abutments; placement of bridge; complete renovation of bridge, including reducing length of bridge, new plastic lumber decking, handrail/raining modifications, sandblasting, priming and painting bridge.

Bridge installation will not be measured for payment and will be paid for on a lump sum basis.

Item 3 – Boardwalk “East section” Boardwalk work shall include all work, labor materials and equipment necessary, but not limited to excavation, grading, concrete pier foundations, helical piers (see Item 3 b.) , framing, and approach abutments, plastic lumber decking, and curbs, and all other miscellaneous work as shown on drawings.

Payment for Boardwalk “East section” will be made by lineal foot  of boardwalk  acceptably installed/placed. Length shall be measured along the center of the boardwalk All associated work and the cost of the concrete piers shall be reflected in the per foot cost. The estimated length is approximately 500 Linear feet.

a. Guardrail for Boardwalk “East section” Guardrail work shall include all work, labor materials and equipment necessary, but not limited to supplying and installing plastic lumber guardrail and all other miscellaneous handrail work as shown on drawings.

Payment for Guardrail for Boardwalk “East section” will be made by lineal foot  of guardrail acceptably installed/placed. Length shall be measured along the guardrail. The estimated length is approximately 220 Linear feet.

b. Helical Anchor “East section”: shall include all work, labor materials and equipment necessary to supply and install helical Anchors “east section” and H-frame assembly acceptably furnished and installed. All associated work items shall be considered incidental.

Payment for Helical Anchor “East section” will be made by lineal foot of anchors acceptably installed/placed. The estimated length is approximately 375 Linear feet.

Option No. 1

Item 4 - Boardwalk “West section” Boardwalk work shall include all work, labor materials and equipment  necessary, but not limited to excavation, footings, helical piers, framing, and approach abutments, plastic lumber decking, and curbs, and all other miscellaneous work as shown on drawings.

Payment for Boardwalk “West section” will be made by lineal foot of boardwalk acceptably installed/placed. Length shall be measured along the center of the boardwalk. The estimated length is approximately 690 Linear feet.

a. Guardrail for Boardwalk “West section” Guardrail work shall include all work, labor materials and equipment necessary, but not limited to supplying and installing plastic lumber guardrail and all other miscellaneous handrail work as shown on drawings.

Payment for Guardrail for Boardwalk “West section” will be made by lineal foot of guardrail acceptably installed/placed. Length shall be measured along the guardrail. The estimated length is approximately 990 Linear feet.

b. Helical Anchor “West section”: shall include all work, labor materials and equipment necessary to supply and install helical Anchors “west section” and H-frame assembly acceptably furnished and installed. All associated work items shall be considered incidental.

Payment for Helical Anchor “West section” will be made by lineal foot of anchors acceptably installed/placed. The estimated length is approximately 1350 Linear feet.

Option No. 2

Item 5 – Gravel Trail shall include all work, labor materials and equipment, necessary, but not limited supplying and installing gravel trail, filter fabric and timber edge.

Trail will not be measured for payment and will be paid for on a lump sum basis.

Option No. 3

Item 5 - Benches shall include all work, labor materials

and equipment, necessary, but not limited

supplying and installing five (5) benches

Benches will not be measured for payment and will be paid for on a lump sum basis.