HQ 957723

June 2, 1995

CLA-2 R:C:M 957723 KCC

CATEGORY: Classification

TARIFF NO.: 8531.20.00

Area Director

U.S. Customs Service

Building #77, JFK Airport

Room 228

Jamaica, New York 11430

RE:  IA 2/95; liquid crystal devices; LCDs; 9013.80.60; liquid crystal devices not constituting

articles provided for more specifically in other headings; HRLs 955447, 954788, 953115,

952502, 951288, 952360, 954638 and 955062; EN 90.13; signaling apparatus; EN 85.31

Dear District Director:

This is in regards to Internal Advice 2/95, initiated by counsel for Sanyo Semiconductor

Corporation, in a letter to your office dated October 20, 1994, which concerns the tariff

classification of liquid crystal displays under the Harmonized Tariff Schedule of the United States

(HTSUS).  We note that the National Import Specialists knowledgeable about liquid crystal

displays visited a Sanyo facility to view samples and meet with counsel.

FACTS:

The liquid crystal displays (LCDs) at issue are referred to as fixed LCDs or icon-type

LCDs, which are represented by model numbers LCD 9108H, LCD 9077JPH, and LCD

4192RF1.  They are low character fixed displays showing limited information, i.e., numbers or

symbols.  These are relatively simple displays using icons, segments, bar graphs, and fixed text.

The LCDs are fitted with electrical connectors.  They do not contain a printed circuit board or any

integrated circuits, but are inserted as one of many components on a circuit board inside the

machine into which it is designed to be incorporated.  The IA applicant describes this merchandise

in their sales literature and on their commercial invoices as LCD panels.  However, they state that

there is not an industry-applied term for this particular type of LCD.

ISSUE:

Are the LCDs classified under subheading 8531.20.00, HTSUS, as "[e]lectric sound or

visual signaling apparatus...[i]ndicator panels incorporating liquid crystal devices (LCD's)...", or

under subheading 9013.80.60, HTSUS, as "[l]iquid crystal devices not constituting articles

provided for more specifically in other headings..."?

LAW AND ANALYSIS:

The classification of merchandise under the HTSUS is governed by the General Rules of

Interpretation (GRI's).  GRI 1, HTSUS, states, in part, that "for legal purposes, classification shall

be determined according to the terms of the headings and any relative section or chapter notes...."

The subheadings at issue are:

8531.20.00     Electric sound or visual signaling apparatus (for example, bells, sirens, indicator

panels, burglar or fire alarms), other than those of heading 8512 or 8530; parts

thereof...Indicator panels incorporating liquid crystal devices (LCD's) or light

emitting diodes (LED's)....

9013.80.60     Liquid crystal devices not constituting articles provided for more specifically in

other headings; lasers, other than laser diodes; other optical appliances and

instruments, not specified or included elsewhere in this chapter; parts and

accessories thereof...Other devices, appliances and instruments...Other.

There is no dispute that the LCDs are limited by design and function to that of signaling

and are, therefore, classifiable under heading 8531, HTSUS.  Additionally, you contend that the

LCDs are classifiable under subheading 9013, HTSUS, as liquid crystal devices not constituting

articles provided for more specifically in other headings.  You state that the industry frequently

refers to the LCDs at issue as glass sandwiches.  This classification opinion is based on

Headquarters Ruling Letters (HRL) 955477 dated February 9, 1994, which classified glass

sandwiches under subheading 9013.80.60, HTSUS, and Explanatory Note (EN) 90.13 (pg. 1478),

which states:

(1)  Liquid crystal devices consisting of a liquid crystal layer sandwiched between

two sheets or plates of glass or plastics, whether or not fitted with electrical

connections, presented in the piece or cut to special shapes and not constituting

articles described more specifically in other headings of the Nomenclature

(emphasis in original).

In understanding the language of the HTSUS, the Harmonized Commodity Description and

Coding System (HCDCS) ENs may be consulted.  The ENs, although not dispositive, provide a

commentary on the scope of each heading of the HTSUS and are generally indicative of the

proper interpretation of the HTSUS.  See, T.D. 89-90, 54 Fed. Reg. 35127, 35128 (August 23,

1989).

We are of the opinion that the glass sandwiches classified under subheading 9013.80.90,

HTSUS, in HRL 955477 are not similar to the LCDs at issue.  Glass sandwiches are incomplete

units which generally are not dedicated to a particular function at the time of importation.  In

HRL 955447, as imported, the glass sandwiches required row and column drivers to be installed

in order for the unit to operate as designed.  The LCDs at issue do not require row and column

drivers because they are not organized to display information in rows or columns.  We note that

the LCDs at issue, appear, by visual inspection, to be glass sandwiches.  However, as imported,

they are workable, complete LCDs without a power source which, by design, do not require row

and column drivers to function.  Moreover, the LCDs do not require integrated circuits containing

software to define what the displayed graphics or numbers will look like because all the graphics

and numbers that will be displayed on the LCDs are ingrained into the LCDs themselves.

Everything that is needed to enable the LCDs to function, other than a power source, is included

in the LCDs at the time of importation.  Therefore, it is our opinion that the LCDs are not

classifiable as glass sandwiches under subheading 9013.80.90, HTSUS.

We agree with the IA applicant that the LCDs at issue are specifically described under

subheading 8531.20.00, HTSUS, as "[e]lectric sound or visual signaling apparatus...[i]ndicator

panels incorporating liquid crystal devices (LCD's)...."  Only those LCD's which are principally

used and/or limited by design to "signaling" are classifiable under subheading 8531.20.00,

HTSUS.  See, HRL 954788 dated December 1, 1993, HRL 953115 dated May 10, 1993, HRL

952502 dated March 18, 1993, HRL 952360 dated October 15, 1992, HRL 951868 and HRL

951288.  The articles under consideration are complete, workable LCDs which present limited

indication information to a user, i.e., a feature is in use, battery usage, administration of

medication, etc.  This type of indication information is similar to the types of limited indication

functions enumerated in EN 85.31 (1381).  Therefore, the LCDs are principally used for visual

signaling, and are classifiable under subheading 8531.20.00, HTSUS.  See also, HRL 955062

dated March 21, 1994 (global positioning, traffic signal controller, portable data collector, lottery

system, pipeline monitoring, gasoline pump indicator, and medical, measurement and industrial

instruments), HRL 954638 dated December 2, 1993 (electronic price tags, medical

instrumentation, diving equipment, camera controls, and industrial controls) and HRL 953115

dated May 10, 1993 (avionics LCDs for collision avoidance systems), which classified LCDs with

limited operational capabilities for signaling functions under subheading 8531.20.00, HTSUS, as

signaling apparatus.

HOLDING:

The LCDs, represented by model numbers LCD 9108H, LCD 9077JPH, and LCD

4192RF1, are classified under subheading 8531.20.00, HTSUS, as "[e]lectric sound or visual

signaling apparatus...[i]ndicator panels incorporating liquid crystal devices (LCD's)...."  The

corresponding duty rate for articles of this subheading is 2.4 percent ad valorem.

This decision should be mailed by your office to the internal advice requester no later than

60 days from the date of this letter.  On that date the Office of Regulations and Rulings will take

steps to make the decision available to Customs personnel via the Customs Rulings Module in

ACS and the public via the Diskette Subscription Service, Freedom of Information Act and other

public access channels.

Sincerely,

John Durant, Director

Commercial Rulings Division