| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 6 to Document 39-E |
|  | 28 August 2007 |
|  | Original: Arabic |
| Arab States Common Proposals |
| proposals for the work of the conference |
| Agenda item 1.7 |

1.7	to consider the results of ITU-R studies regarding sharing between the mobile-satellite service and the SRS (passive) in the band 1 668-1 668.4 MHz, and between the mobile-satellite service and the mobile service in the band 1 668.4-1 675 MHz in accordance with Resolution 744 (WRC-03)

Introduction

Agenda item 1.7 addresses two issues related to the mobile-satellite service (MSS) use of the band 1 668-1 675 MHz. Issue A relates to sharing between mobile earth stations (MESs) and systems in the space research service (SRS) (passive) in the band 1 668-1 668.4 MHz. Issue B relates to sharing between the mobile service (MS) and the MSS in the band 1 668.4-1 675 MHz.

# Issue A

The Arab States propose the use of the existing coordination threshold based on the e.i.r.p. of a mobile earth station (MES) of 2.2 dB(W/4 kHz). This approach will consequently cap the protection to be provided to new SRS (passive) systems.

APPENDIX  5  (Rev.WRC-03)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9

TABLE  5-1     (Rev.WRC-03)

Technical conditions for coordination
(see Article 9)

MOD	ARB/39A6/1

TABLE  5-1     (Rev.WRC-07)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.13 GSO/non-GSO | A station in a GSO satellite network in the frequency bands for which a footnote refers to No. 9.11A or No. 9.13, in respect of any other non-GSO satellite network, with the exception of coordination between earth stations operating in the opposite direction of transmission | Frequency bands for which a footnote refers to No. 9.11A or No. 9.13 | Bandwidths overlap For the band 1 668-1 668.4 MHz with respect to MSS network coordination with SRS (passive) networks, in addition to bandwidth overlap, the e.i.r.p. of an MES in an MSS network exceeds 2.2 dBW in a reference bandwidth of 4 kHz | Check by using the assigned frequencies and bandwidths |  |
| ... |  |  |  |  |  |

Reasons:	To ensure the protection to be provided to the space research service (SRS) (passive).

# Issue B

The Arab States propose to modify Resolution 744 (WRC-03). The use of the MS allocation is to be limited to transportable radio-relay systems (with the exception of the territory of the administration mentioned in the resolves section of this Resolution), and a hard limit is to be placed on the e.i.r.p. spectral density of transportable radio-relay stations in Resolution 744 (WRC-03) for example, as shown below:

MOD	ARB/39A6/2

RESOLUTION  744  (WRC-07)

Sharing between the mobile-satellite service (Earth-to-space) and the space 
research (passive) service in the band 1 668-1 668.4 MHz and between 
the mobile-satellite service (Earth-to-space) and the fixed and 
mobile services in the band 1 668.4-1 675 MHz

The World Radiocommunication Conference (Geneva, 2007),

considering

a)	that WRC-03 made a global allocation to the mobile-satellite service (MSS) (Earth-to-space) in the band 1 668-1 675 MHz and a global allocation to the MSS (space-to-Earth) in the band 1 518-1 525 MHz;

b)	that due to sharing conditions between MSS (space-to-Earth) and the aeronautical mobile service for telemetry in the band 1 518-1 525 MHz (see No. 5.348B), MSS operation in the United States of America is unlikely to be feasible;

c)	that the above constraints on the MSS in the band 1 518-1 525 MHz therefore limit the possible use of the band 1 668-1 675 MHz by the MSS in the United States of America;

d)	that the band 1 660.5-1 668.4 MHz is allocated to the space research (passive) service;

e)	that in the band 1 668-1 668.4 MHz, mobile earth stations and space research (passive) stations are subject to coordination under No. 9.11A;

f)	that the band 1 670-1 675 MHz is currently planned for use in the United States of America for the fixed and mobile services,

resolves

1	that the use of the band 1 668.4-1 675 MHz by systems in the mobile service is limited to transportable radio-relay systems;

2	that administrations operating such systems shall limit the e.i.r.p. spectral density radiated in the direction of the geostationary arc to –27 dB(W/4 kHz) in this band;

3	that, in the band 1 670-1 675 MHz, stations in the MSS shall not claim protection from fixed and mobile stations operating in the United States of America;

4	that resolves 1 and 2 do not apply to fixed and mobile stations operating in the United States of America.

Reasons:	To provide adequate protection to the mobile-satellite service from the mobile service.

____________