| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 11 to Document 39-E |
|  | 28 August 2007 |
|  | Original: Arabic |
| Arab States Common Proposals |
| proposals for the work of the conference |
| Agenda item 1.12 |

1.12	to consider possible changes in response to Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference: “Advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks” in accordance with Resolution 86 (WRC-03)

Introduction

Under its Agenda item 1.12, WRC-07 is invited by Resolution 86 (Rev. Marrakesh, 2002) to consider possible changes in the advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks, including the associated technical characteristics, and the related Appendices of the RR.

## 1	Provisions of No. 5.538

The Arab States propose to add the band 27.500-27.501 GHz to Table 21-4 of RR Article 21 in order to apply the pfd limits in the adjacent frequency band to the 25.25-27.5 GHz band.

ARTICLE  21

Terrestrial and space services sharing frequency bands above 1 GHz

MOD	ARB/39A11/1

TABLE  21-4  (continued)     (WRC-03)

| Frequency band | Service* | Limit in dB(W/m2) for angles of arrival () above the horizontal plane | Reference bandwidth |
| --- | --- | --- | --- |
|  |  | 0-5 | 5-25 | 25-90 |  |
| ... |  |  |  |  |  |
| 19.3-19.7 GHz 22.55-23.55 GHz 24.45-24.75 GHz 25.25-27.5 GHz 27.500-27.501 GHz | Fixed-satellite (space-to-Earth) Earth exploration-satellite (space-to-Earth) Inter-satellite Space research (space-to-Earth) | –115 | –115 + 0.5( – 5) | –105 | 1 MHz |
| ... |  |  |  |  |  |

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	ARB/39A11/2

5.538	Additional allocation:  the bands 27.500-27.501 GHz and 29.999-30.000 GHz are also allocated to the fixed-satellite service (space-to-Earth) on a primary basis for the beacon transmissions intended for up-link power control. Such space-to-Earth transmissions shall not exceed an equivalent isotropically radiated power (e.i.r.p.) of 10 dBW in the direction of adjacent satellites on the geostationary-satellite orbit.

## 2	Coordination arc value for triggering coordination between broadcasting-satellite service (BSS) serving Region 2 and fixed-satellite service (FSS) (space-to-Earth) networks serving Region 1 in the band 17.3-17.8 GHz, and among BSS networks serving Region 2 in bands above 17.3 GHz

MOD	ARB/39A11/3

The Arab States propose to endorse the proposed modifications to Appendix 5 in order to adopt the proposed coordination arcs for the identification of the affected administrations in both cases.

## 3	Provisions of RR No. 11.43A

The Arab States prefer Option B to Option A, as Option B limits the modification to the reference position (6°, with the modification of the provisions of RR No. 11.43A as follows:

ARTICLE  11

Notification and recording of frequency
            assignments1, 2, 3, 4, 5, 6     (WRC-03)

Section II  –  Examination of notices and recording of frequency assignments
in the Master Register

MOD	ARB/39A11/4

11.43A		A notice of a change in the characteristics of an assignment already recorded, as specified in Appendix 4, shall be examined by the Bureau under Nos. 11.31 to 11.34, as appropriate. Any change to the characteristics of an assignment that has been notified and confirmed as having been brought into use shall be brought into use within five years from the date of the notification of the modification. Any change to the characteristics of an assignment that has been notified but not yet brought into use shall be brought into use within the period provided for in No. 11.44. Cumulative changes to the orbital position shall be in accordance with No. 9.2. If the modification concerns the notification of assignment(s) in frequency band(s) not covered by other assignment(s) already recorded in the Master Register, this provision does not apply and the notice will be processed under No. 11.2 or 11.9, as appropriate.

## 4	Provisions of RR No. 11.47

The Arab States propose to modify the provisions of RR No. 11.47, as follows:

MOD	ARB/39A11/5

11.47		All frequency assignments notified in advance of their being brought into use shall be entered provisionally in the Master Register. Any frequency assignment to a space station provisionally recorded under this provision shall be brought into use no later than the end of the period provided under No. 11.44. Any other frequency assignment provisionally recorded under this provision shall be brought into use by the date specified in the notice, or by the date of expiry of the extension granted under No. 11.45, as the case may be. Unless the Bureau has been informed by the notifying administration of the bringing into use of the assignment, it shall, no later than fifteen days before the notified date of bringing into use, in the case of an earth station, or the end of the regulatory period established under No. 11.44 or No. 11.45, as appropriate, send a reminder requesting confirmation that the assignment has been brought into use within the regulatory period. If the Bureau does not receive that confirmation within thirty days following the notified date of bringing into use, in the case of an earth station, or the period provided under No. 11.44 or No. 11.45, as the case may be, it shall cancel the entry in the Master Register. The Bureau shall inform the administration concerned before taking such action.

## 5	Provisions of RR No. 22.2

The Arab States propose to modify RR No. 22.2 in order to clarify the relation between non-GSO systems and GSO networks in the fixed-satellite and broadcasting services. The original text stipulated that non-GSO systems shall not cause unacceptable interference to GSO networks, but did not precise that such systems shall not claim protection from GSO networks. The proposed modification is as follows:

ARTICLE  22

Space services1

Section II  –  Control of interference to geostationary-satellite systems

MOD	ARB/39A11/6

22.2	§ 2	1)	Non-geostationary-satellite systems shall not cause unacceptable interference to or claim protection from geostationary-satellite networks in the fixed-satellite service and the broadcasting-satellite service operating in accordance with these Regulations. No. 5.43A does not apply in this case.     (WRC-07)

## 6	Coordination distances for cases involving ground-based earth stations and aircraft stations

The Arab States propose a coordination distance of 500 km for a mobile earth station (aircraft) (while noting that this value represents the scenario which is the nearest to the worst case for conducting coordination). The following modification is proposed to Appendix 7 which addresses the methods for the determination of the coordination area around an earth station in frequency bands between 100 MHz and 105 GHz.

APPENDIX  7  (Rev.WRC-03)

Methods for the determination of the coordination area around an earth
station in frequency bands between 100 MHz and 105 GHz

ANNEX  7

System parameters and predetermined coordination distances for determination of the coordination area around an earth station

MOD	ARB/39A11/7

TABLE  10     (Rev.WRC-07)

Predetermined coordination distances

| Frequency sharing situation | Coordination distance (in sharing situations involving services allocated with equal rights) (km) |
| --- | --- |
| Type of earth station | Type of terrestrial station |  |
| ... |  |  |
| Ground-based in bands in which the frequency sharing situation is not covered in rows above | Mobile (aircraft) | 500 |

## 7	RR Appendix 4 data element (C.8.d.2); contiguous satellite bandwidth

The Arab States propose to modify Appendix 4 containing the consolidated list and tables of characteristics for use in the application of the procedures of Chapter III. It is thus proposed to modify Annex 2 to RR Appendix 4, in order to request the submission of item C.8.d.2 only if it is different from the item C.3.a concerning the assigned bandwidth.

APPENDIX  4  (Rev.WRC-03)

Consolidated list and tables of characteristics for use in the
application of the procedures of Chapter III

ANNEX  2

Characteristics of satellite networks, earth stations 
or radio astronomy stations2     (WRC-03)

MOD	ARB/39A11/8

| Items in Appendix | C _ CHARACTERISTICS TO BE PROVIDED FOR EACH GROUP OF FREQUENCY ASSIGNMENTS FOR A SATELLITE ANTENNA BEAM OR AN EARTH STATION OR RADIO ASTRONOMY ANTENNA | Advance publication of a geostationary-satellite network | Advance publication of a non-geostationary-satellite network subject to coordination under Section II of Article 9 | Advance publication of a non-geostationary-satellite network not subject to coordination under Section II of Article 9 | Notification or coordination of a geostationary-satellite network (including space operation functions under Article 2A of Appendices 30 or 30A) | Notification or coordination of a non-geostationary-satellite network | Notification or coordination of an earth station (including notification under Appendices 30A or 30B) | Notice for a satellite network in the broadcasting-satellite service under Appendix 30 (Articles 4 and 5) | Notice for a satellite network (feeder-link) under Appendix 30A (Articles 4 and 5) | Notice for a satellite network in the fixed-satellite service under Appendix 30B (Articles 6 and 8) | Items in Appendix | Radio astronomy |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C.8.d.2 | each contiguous satellite bandwidth |  |  |  | + | + |  |  |  |  | C.8.d.2 |  |
|  | For the maximum saturated peak envelope power of the satellite transponder, this corresponds to the bandwidth of each transponder |  |  |  |  |  |  |  |  |  |  |  |
|  | Required only for a space-to-Earth or space-to-space link, and only if different from item C.3.a |  |  |  |  |  |  |  |  |  |  |  |

## 8	Resolution 88 (WRC-03)

The Arab States propose to suppress this Resolution on the rationalization of Articles 9 and 11 of the Radio Regulations, as no progress has been achieved in this regard since the time of its adoption.

SUP	ARB/39A11/9

RESOLUTION  88  (WRC-03)

Rationalization of Articles 9 and 11 of the Radio Regulations

## 9	RR Appendix 4 – Advance Publication Information for non-GSO satellite systems not subject to coordination

MOD	ARB/39A11/10

The Arab States propose to modify the table of characteristics to be supplied for space and radio astronomy services in Annex 2 to RR Appendix 4, so as to add the request for information for non-GSO satellite systems not subject to coordination, at the publication stage also and not only at the notification stage, subject to not causing additional costs and to serving the needs of the majority of the membership and not of only a few operators (content of the reservation from the Arab States during CPM).

## 10	RR Appendix 4 – Active and passive sensors on satellites

MOD	ARB/39A11/11

The Arab States propose to modify Annex 2 to RR Appendix 4 by adding comments for specific data elements requested for active and passive sensors in Tables B and C (no change is required for Tables A and D), subject to not causing additional costs and to serving the needs of the majority of the membership and not of only a few operators (content of the reservation from the Arab States during CPM).

## 11	Radionavigation-satellite service in the bands 1 215-1 300 MHz and 1 559-1 610 MHz

The Arab States propose to modify footnotes 5.329A and 5.328B. The modification to footnote 5.329A is to clarify that “other systems” in this footnote refer to the radionavigation-satellite service (space-to-Earth) and that the word “services” refers to services other than the radionavigation-satellite service. Modifications to RR No. 5.328B are also needed to make it clear that the application of the coordination procedure in RR Nos. 9.7, 9.12, 9.12A and 9.13 to RNSS (space-to-space) systems and networks is only with respect to other radionavigation-satellite service (space-to-space) systems and networks in the bands 1 215-1 300 MHz and 1 559-1 610 MHz and in these bands to limit the application of Resolution 610 (WRC-03) in such coordinations to transmitting space stations.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	ARB/39A11/12

5.329A	Use of systems in the radionavigation-satellite service (space-to-space) operating in the bands 1 215-1 300 MHz and 1 559-1 610 MHz is not intended to provide safety service applications, and shall not impose any additional constraints on radionavigation-satellite service (space-to-Earth) systems or on other services operating in accordance with the Table.     (WRC-07)

MOD	ARB/39A11/13

5.328B	The use of the bands 1 164-1 300 MHz, 1 559-1 610 MHz and 5 010-5 030 MHz by systems and networks in the radionavigation-satellite service for which complete coordination or notification information, as appropriate, is received by the Radiocommunication Bureau after 1 January 2005 is subject to the application of the provisions of Nos. 9.12, 9.12A and 9.13. Resolution 610 (WRC-03) shall also apply; however, in the case of radionavigation-satellite service (space-to-space) networks and systems, Resolution 610 (WRC-03) shall only apply to transmitting space stations. In accordance with No. 5.329A, for systems and networks in the radionavigation-satellite service (space-to-space) in the bands 1 215-1 300 MHz and 1 559-1 610 MHz the provisions of Nos. 9.7, 9.12, 9.12A and 9.13 shall only apply with respect to other systems and networks in the radionavigation-satellite service (space-to-space).     (Rev.WRC-07)

## 12	Provisions of RR No. 11.49

NOC	ARB/39A11/14

The Arab States propose to maintain without any change the provisions of RR No. 11.49 concerning the period of two years for replacing a satellite in case of malfunction. They are ready to review their position as may be required during the Conference.

## 13	Provisions of RR No. 9.1

NOC	ARB/39A11/15

The Arab States propose not to change the provisions of RR No. 9.1 while addressing the question of misuse, if confirmed, during the Conference.

## 14	Resolution 86 (WRC-03)

SUP	ARB/39A11/16

The Arab States propose to suppress this Resolution and to modify Agenda item 7.1 of WRCs (which is a standing agenda item for each and every WRC) as indicated below:

MOD	ARB/39A11/17

7.1	to consider and approve the Report of the Director of the Radiocommunication Bureau:

–	on the activities of the Radiocommunication Sector since WRC-03;

–	on any difficulties or inconsistencies encountered in the application of the Radio Regulations, including any suggested improvements to the procedures pertaining to advance publication, coordination, notification and recording of frequency assignments for satellite networks or systems; and

–	on action in response to Resolution 80 (Rev.WRC-2000);

## 15	Application of the provisions of RR No. 9.14

MOD	ARB/39A11/18

The Arab States propose to transfer the Rule of Procedure to RR No. 9.14, thus modifying this number to indicate that the space station is “transmitting” and that the terrestrial station is “receiving” when the interference threshold value is exceeded in respect of terrestrial stations.

## 16	Provisions of RR Nos. 9.15 to 9.18

NOC	ARB/39A11/19

The Arab States propose not to merge RR No. 9.15 with RR No. 9.17 and not to merge RR No. 9.16 with RR No. 9.18.

## 17	Application of the provisions of RR No. 9.11A with respect to the category of services

MOD	ARB/39A11/20

The Arab States endorse View A in the CPM Report in order to transfer the related Rule of Procedure to the RR to reflect that coordination under RR No. 9.11A applies only between services allocated with equal rights. They do not accept View B except in the case of coordination between the satellite-broadcasting stations operating according to the provisions of Regions 1 and 3 Plan of RR Appendices 30 and 30A and the fixed, fixed-satellite and mobile primary services, pursuant to footnotes 5.487 and 5.487A, as stations operating according to the Plan are considered to have priority over other primary services pursuant to these footnotes.

## 18	Inconsistencies in Article 2A of each of RR Appendices 30 and 30A

MOD	ARB/39A11/21

The Arab States propose that the time-limit for the space operation functions in the guardband supporting a BSS network be the same for the same satellite.

## 19	Consideration of a request for extension of the time-limit for bringing
into use in RR Article 11

MOD	ARB/39A11/22

The Arab States propose to directly bring the matter to the attention of the Conference.

## 20	Other issues regarding the application of RR No. 22.2 in the frequency band 1 467-1 492 MHz

MOD	ARB/39A11/23

The Arab States confirm that they reject this proposal as it is not related to Agenda item 1.12 and contradicts the objective of Resolution 86 (Rev. Marrakesh, 2002). This justifies the position taken by the Arab States to suppress it as proposed in the last Plenipotentiary Conference (Antalya, 2006).

_______________