### 6.2.3 Vacuum System

#### 6.2.3.1 Synchrotron Radiation

With a proton energy of 87.5 TeV and a bending radius of 29.9 km, the critical energy of the synchrotron radiation emitted by the protons is 8 keV, which corresponds to a  wave-length of ~1.6 Å. At a peak current of 57.4 mA each beam releases 4.7 W/m and 1.2(1016 photons/sec/m in the bending magnets. The total synchrotron radiation power emitted by the two beams is 9.4 W/m. This, combined with additional heat load contributions such as resistive wall power loss and emittance growth related loss due to multipactoring electrons and ion-induced desorption – estimated to <1 W/m/beam all together, would be an excessive heat load for the cold mass. Thus, a beam screen, maintained at a higher temperature by a flow of gaseous helium, is inserted inside the magnet cold bore to intercept this power.

The synchrotron radiation photons impinging on the beam screen desorb gas molecules from the near surface layer and convert them into a steadily increasing surface density of loosely bound (physisorbed) states. These physisorbed surface molecules are easily redesorbed by the photons, deteriorating the quality of the vacuum in the beam chamber. Therefore, the beam screen will be perforated over a few percent of its surface, to allow cryopumping to the 5 K cold bore surface, where the vapor pressure of all gases (except H2 and He) is negligible and the condensed gas is shielded from synchrotron radiation and ion bombardment.

#### 6.2.3.2 Beam Screen Cooling

##### 6.2.3.2.1 Optimum Beam Screen Temperature

The cooling of the beam screen is a key issue in the VLHC – the beam screen refrigeration power requirement is the leading contributor to the total cryo-budget. The beam screen refrigeration power requirement is a strongly varying function of the beam screen operational temperature. The optimum beam screen temperature balances between the heat load absorbed by the beam screen refrigeration system and the heat load absorbed by the cold mass. At low beam screen temperature the heat load is absorbed mainly by the beam screen, at low thermodynamic efficiency and thus at high cost. For a high beam screen temperature the cost of beam screen refrigeration is reduced, but a significant part of the heat load is transferred from the beam screen by conduction and radiation to the cold mass, where it is extracted with low thermodynamic efficiency. The thermodynamic optimum beam screen temperature in the VLHC-2 was calculated to be 86 K [1] for the case of 5 W/m/beam. The base-line VLHC-2 cryo-concept [Section 6.2.2] foresees that the beam screens are cooled in series with the cold-mass thermal shield by the same high pressure helium gas. Although both systems have different optimum operational temperatures when separated, the optimum (average) operating temperature of the cold mass thermal shield in the combined system is 84 K, and the ensuing average beam screen temperature is 100 K. At this temperature the beam screen refrigeration system requires a total plug power of 14.1 MW (both beams). In these conditions the heat load transferred from two beam screens to the cold mass is 0.26 W/m (conduction) and 0.07 W/m (radiation). At a cold mass temperature of 5 K the evacuation of the heat load transferred from both beam screens to the cold mass represents a plug power requirement of 12 MW for the complete ring.

##### 6.2.3.2.2 Concept for a Beam Screen Cooling System

Following a calculation procedure outlined in [1], the beam screen cooling system requires 12% of the area enclosed by the cold bore (ID=34 mm), or 110 mm2 in cross-sectional area, to be taken up by the coolant at an average temperature of 100 K, The coolant is high pressure gaseous helium, entering the beam screen cooling system at 89.3 K, 19.2 bar and exiting at 108.4 K, 18.1 bar. The beam screen cooling system length is assumed to be the length of a half-cell (135 m). The total flow rate per beam screen is 6.6 g/s. In the calculations the stainless steel cooling duct wall thickness was assumed to be 0.5 mm.

#### 6.2.3.3 Vacuum

##### 6.2.3.3.1 Synchrotron Radiation

The high photon flux is the dominant source of gas – on the other hand it is very effective in cleaning the exposed surfaces via photo induced desorption. The use of superconducting magnet technology results in the amenity of a low cold bore temperature of ~5 K, at which most gases have a very low saturation vapor pressure. Therefore most gases get trapped at the cold bore walls and remain there until the magnets are warmed up again to room temperature. The pumping capacity of such a cryo-pump is very large and compatible with the accelerator lifetime. In addition, the high beam screen temperature decreases the rate of re-adsorption of gas on the beam screen and thus facilitates the cleaning process. The higher saturation vapor pressure of H2 at 5 K on the other hand results in the limitation that H2 cannot be cryo-pumped beyond one monolayer. Therefore the cold bore will have to be warmed up to room temperature at regular intervals (some years) to allow regeneration of the cryo-pumping surfaces.

##### 6.2.3.3.2 Residual Gas Pressure

The residual beam-tube pressure must be low enough to limit beam-gas scattering to a level at which the luminosity lifetime of the beam is not significantly affected, and at which the radiation into the magnet cold mass remains below a stipulated limit. Estimations of the bounds on the beam tube gas pressure for the most common UHV gases are listed in Table 6.13. The beam lifetime limiting pressure is calculated, stipulating that the beam-gas scattering lifetime be five times larger than the luminosity lifetime (13 hours). The beam lifetime reduction stemming from beam-gas scattering related emittance growth is neglected because of strong radiation damping. The limiting pressure to restrict the power radiated into the magnet cold mass due to beam-gas scattering is calculated, stipulating that the beam-gas scattering power be less than 0.1 W/m/beam.

Table 6.13. Numerical bounds on the beam tube gas pressure for the most common UHV gases in the VLHC2 – calculated for each gas “alone” for ambient room temperature equivalent pressure.

| Gas | Max pressure for a beam gas scattering lifetime of 5(13 hours (nTorr) | Max pressure for a Beam gas scattering power of 0.1 W/m/beam (nTorr) |
| --- | --- | --- |
| H2 | 35 | 50.3 |
| CH4 | 6.6 | 9.3 |
| H2O | 6,2 | 8.7 |
| CO | 4.2 | 6 |
| CO2 | 2.7 | 3.8 |

According to the table, the limiting pressure in the VLHC has to be in the nTorr range for the most common UHV gases.

##### 6.2.3.3.3 Photo Desorption and Pumping Speed

Photo-induced desorption due to synchrotron radiation with a critical energy of 8 keV is the most important source of vacuum contamination in the VLHC. Calculations, based on procedures formerly developed in [3], have recently [2] been performed to estimate the quantity of gas desorbed by synchrotron radiation from a copper coated beam screen. Copper can be prepared (baked) to have a small initial photo-desorption coefficient (0 (e.g. ~0.0035 H2 molecules per photon) and offers the advantage of a low secondary electron emission coefficient (reducing the electron cloud effect). It is believed that the initial photo-desorption coefficient does not increase further with the critical energy of the photons, above some keV, a range for which reliable measurements exist [4]. The photo-desorbed gas load has to be matched by a pumping speed to remain within the specified pressure. The CO equivalent pumping speed required to keep the heat dissipation in the magnet below 0.1 W/m after one third of an operational year (I(t=48 A-hours) is 5.6 lit/sec-m. For H2 this pumping speed is 21 lit/sec-m. During the commissioning phase of the machine the photo-desorption rate is larger, requiring a larger pumping speed and/or a smaller beam current. A possible commissioning beam- current profile (for a CO equivalent pumping speed of 61 l/sec-m) was proposed [2]. The current in the profile is calculated for the condition that the beam-gas scattering power always remains below 0.1 W/m. It consists of 3 15 hour cycles with initial currents of 30 mA, 38 mA and 54 mA. The total conditioning time is thus 45 hours.

##### 6.2.3.3.4 Cryo-pumping

Due to its low saturation vapor pressure, H2 cannot be cryo-sorbed on a 5 K surface beyond one monolayer (~3(1015 H2/cm2). Pumping speeds of 61 lit/sec-m, as required for conditioning, can be achieved through cryo-pumping the gas onto the cold (5 K) magnet bore. The beam screen surface fraction occupied by pumping slots to obtain 60 lit/sec-m is ~1.5 %. The integrated gas-load set free by the synchrotron photons during a 20 year accelerator operation is ~1.1(1019 H2 molecules/m. This represents 3.3 mono-layers of H2. This gas-load can be managed by periodic warm-up of the machine to allow regeneration of the cryo-pumping surfaces.

#### 6.2.3.4 Conceptual Beam Screen Design

We propose a vacuum system design (Figure 6.16), similar to the LHC design [6], using a perforated liner, operating at ~100 K. The beam screen is a 1 mm thick non-magnetic stainless steel (µr<1.005) tube with a round cross-section, flattened top and bottom. The space between it and the surrounding cold bore contains the cooling pipes carrying the forced flow supercritical helium. The pipes, e.g. made of stainless steel, are laser welded to the beam screen. The beam screen is centered within the cold bore by steel/bronze rings, every 0.5 m. The assumed magnet bore ID is 40 mm. A 1.5-mm gap is needed to allow the insertion of the cold bore into the

# Figure 6.16. A schematic view of the beam screen showing supports, cooling pipes and pumping slots.

magnet. Then, to withstand the quench-pressure, the cold bore tube needs a wall thickness of 1.5 mm, hence the cold bore inner diameter becomes 34 mm. The supports require an additional 0.75-mm gap between the cold bore and the beam screen. The remaining aperture for the beam screen becomes 32.5 mm. The inner dimensions of the beam screen are 30.5 mm in width and 20 mm in height. To minimize resistive wall heating and longitudinal beam impedance the interior surface of the screen is covered by a thin co-laminated layer of high purity copper. The pumping slots are rounded (1.5 mm wide, 8 mm long)) and randomly distributed to reduce beam-coupling impedance and resonance effects.

To obtain a pumping speed of 60 lit/sec-m 120 holes are required per meter of beam screen (e.g. 4 rows of 30 holes, one hole every 5 cm). As in the case of LHC [6] the beam-screen is fabricated from sheet metal with stamped cooling slots and cold rolled with the copper foil and cold pressed into the shape of a half tube, which are then welded together. To eliminate the effects of heat load variations between the apertures the cooling tubes should cross-over to the other aperture at every half cell (as proposed in Section 6.2.2).

#### 6.2.3.5 Photon Stops

##### 6.2.3.5.1 Justification

The strong synchrotron radiation in the VLHC 2 results in a refrigeration power requirement of ~25 MW. Intercepted at room temperature, the synchrotron radiation heat load would represent a reduced power at the plug of ~1.9 MW. Motivated by the considerable cost saving potential the use of room temperature operated photon stops, which are commonly used in synchrotron light sources [7], is under evaluation. Photon stops are devices that protrude into the beam tube at the end of each bending magnet and scrape off the synchrotron light beam emitted in the second magnet up-stream from their location. A preliminary feasibility study was recently performed [8], showing that, given the arc bending radius in the VLHC of 29.9 km, it is possible to place photon stops between the magnets with a length and aperture compatible with the current VLHC design. We believe that synchrotron radiation in the VLHC is a sufficiently serious issue to justify even the use of both a traditional beam screen system and photon stops together. In the case that the photon stops are retractable, the synchrotron heat load could be shared in a controlled way between both systems which would allow operation of the accelerator at energies and luminosities above nominal.

##### 6.2.3.5.2 Geometrical Issues

A geometrical model, based on the assumptions 1) that the bending magnets are straight and positioned such that the average distance between the ideal particle orbit and the magnet center is minimal and 2) that all particles are moving very close to the ideal orbit, allows to estimate the maximum permissible magnet length and the minimum distance between the photon stop and the beam. Given that the photon stops are placed at the beginning of the 3 m long straight section between the magnets and a 30 mm diameter beam screen aperture, the maximum permissible bending magnet length is 14 m, which is compatible with the maximum magnet length imposed by quench protection and transportation constraints. In this condition the synchrotron radiation emitted from the beginning of the second up-stream magnet will heat the photon stop at its base (where it enters the beam tube) and the radiation emitted from the end of the same magnet will hit  its tip. The emission angle of the SR is 1/~10 µrad. The total radial extension of the photon stop is 1 cm, such that its (minimum) distance from the particle orbit becomes 5 mm.

##### 6.2.3.5.3 Engineering Design

Assuming that a single photon stop intercepts the synchrotron radiation heat load emanating from one magnet, the thermal load is given with ~5 W/m times the magnet-length, which is 70 W. The required [9] heat exchange surface is ~1 cm2 at a coolant flux of 0.2 liter/sec, given a cooling tube wall thickness of 1 mm and a cooling tube diameter of 10 mm. The coolant assumed in this calculation is water at room temperature, the coolant temperature rise is 5 K. The peak heat flux of 0.6 MW/m2 remains safely below the critical heat flux of ~2 MW/m2. The largest SR power fraction is transported by photons with a wave-length of 0.5 Å. The radiation length of steel, which was used as reference material in the thermal calculation, is ~0.04 g/cm2 or 0.05 mm. The synchrotron radiation hits the absorber in a ~0.5 mm (rms) thin strip. The absorber surface material needs sufficient thermal conductivity to distribute the heat load over a larger area to dilute the surface heat flux density to the coolant. Heaters, wrapped around the cooling tubes, are required to prevent the cooling liquid from freezing when no synchrotron radiation heat load is present. An engineering design that satisfies the above mentioned thermal stipulations was presented [9].

# Figure 6.17. Photon-stop sketch according to the engineering design proposal.

According to this design, the photon stop is a T-shaped piece, consisting of a ~6 cm short copper tube shaped like the beam screen (but without holes) with flanges at the ends, to which a ~0.5 m long warm finger, the photon-stop, is attached perpendicularly. The photon-stop enters the beam screen from the side, where it is hit by the synchrotron radiation (Figure 6.17). The warm finger consists of an outer hull with flanges on top and bottom to fix it to the cryostat hull and the short beam screen piece with vacuum tight seals. Into this hull the core of the photon-stop is inserted. The core piece consists of the cooling tubes with the radiation absorber at the end. The short beam screen piece is inserted into a specially prepared gap in the beam-screen / cold-bore assembly and welded at each end.

The cold-bore tube is discontinued over the ~10 cm of the photon-stop to reduce the heat influx from the 100 K beam screen / photon stop system. The bellows, required to allow the beam tubes contract during magnet cool-down, are placed in sections further away from the photon stop. The beam-screen cooling tubes have to be guided out of the beam screen to bypass the bellows, usually in the form of flexible tubes. In the case of the photon-stop we propose that the cooling tubes bypass as well the photon stop system. Furthermore it is assumed that the photon stop will be placed close to the magnet anchoring point. This offers the advantage of not having to cope with longitudinal thermal contraction effects. At the heart of the photon-stop is the radiation absorber, a hollow cylinder, machined at one end to a special shape. The inside of the end piece is hollow to allow the cooling liquid to extract the heat deposited by the synchrotron radiation on its outer surface. The wall thickness of the absorber is ~ 2 mm. It is made from copper to obtain a low initial photo-desorption coefficient and a high thermal conductivity. To reduce the thermal emissivity and the photo-desorption coefficient the outer surface of the end piece requires a high grade polishing. The shape of the absorber was optimized to yield low impedance. It has the shape of a prism (Figure 6.17) with axial / radial / azimuthal (with respect to the beam tube) extensions 35 x 10 x 10 mm and rounded edges. The impedance calculations are discussed next.

##### 6.2.3.5.4 Photon Stop Impedance

The longitudinal impedance of the photon-stop has to be small to 1) reduce the impedance related power loss per turn and 2) to avoid beam instabilities, such as for example the microwave instability. The transverse impedance has to remain below beam instability thresholds, such as for example for the transverse mode coupling instability (TMCI). A major issue is whether the photon stops can be treated as independent – in the coupled case the sum of the impedances of all coupled devices would be the relevant parameter, and thus the impedance limitations would be more stringent. A first estimation of the coupling strength can be obtained from the damping length of the first order mode. The damping length was calculated [10] to be 4.2 cm, which is sufficiently smaller than the projected distance between the photon stops of ~14 m, such that coupling is suppressed.

The beam tube impedance of a copper coated, round beam tube (ID=30 mm) is of the order of some . The cut-off frequency of a similar pipe is 2((7.6 GHz, which is larger than the largest characteristic beam frequency in the VLHC, the intra-bunch frequency at collision of 2·5.8 GHz. A simple, analytical model to calculate the impedance of a “half ellipsoidal” protrusion in the beam pipe [11] predicts , for a total number of 14500 photon stops and a longitudinal extension of the protrusion of 3.5 cm and a radial/azimuthal extension of 1 cm, the longitudinal impedance ZII/n becomes 25 m. The transverse impedance for all photon-stops together becomes Z(=8 Mm.

An estimate [10] of the micro-wave instability threshold bunch population is 3(1012, two orders of magnitude larger than the VLHC-2 bunch population. Numerical wake calculations [10] indicate a Transverse Mode Coupling Instability threshold bunch-population of 4.5(1011, still larger than the design peak number of protons per bunch. We believe that the photon stops will not cause TMCI. Trapped modes are of concern in cavity like structures, e.g. holes in the beam pipe, sharp edges, ..etc. We believe that photon stops, with the appropriate design, will not be a major cause of trapped modes.

The impedance calculations were performed assuming that the photon stops are made of e.g. copper. The preliminary calculations have indicated the viability of this concept. Another possible approach to the design of this device would be the use of dielectric materials with low electrical permittivity and high thermal conductivity, such as sapphire or diamond. Although this approach would be advantageous from an impedance standpoint, complications are expected to arise in conjunction with the removal of surface charge and the lack of knowledge on the photo-desorption coefficients. In addition these solutions could be more expensive.

##### 6.2.3.5.5  Photon Stop –Vacuum Issues

The strong synchrotron radiation flux impinging on the photon stop results in a fast clean-up of the photon stop surface. However, it is necessary to pump the desorbed gas load. According to the engineering design proposed the beam screen in the photon stop system has no pumping holes. The desorbed gas load has to diffuse ~5 cm to each side into the beam tube to reach sections where active pumping to the cold-bore removes the gas from the beam area. The high temperature of the photon stop (~300 K) and the beam screen (~100 K) certainly prevents re-adsorption of the desorbed gases and thus the pumping task is simplified. The high surface temperatures result as well in a high molecular speed, accelerating the gas diffusion into the adjacent beam screen regions, where the pumping occurs. On the other hand the high temperature of the photon stop raises the thermal desorption rate. Vacuum simulations are required to determine if the longitudinal diffusion is sufficient to ensure a proper vacuum at the photon stop locations. Another issue, still to be investigated in further detail, pertains to the thermal desorption at 300 K, the surface temperature of the photon stop. It will certainly be necessary to perform a high temperature heat treatment (bake-out) of the photon stop insert before installation.

# References: {ed. note—for Sec. 6.2.3}

[1] C. Darve et al., “VLHC Beam Screen Cooling”, Fermilab Technical Division Note TD-01-005, 02/01.

[2] P. Bauer et al., “Vacuum Calculations for the VLHC - stage 2”, Fermilab, Technical Division Note, TD-01-011, 04/01.

[3] W.C. Turner, “Beam Tube Vacuum in Low Field and High Field Very Large Hadron Colliders”, LBNL- 39482, UC 414, presented at the Snowmass Conference, Oct. 1996.

[4] A. Mathewson, O. Groebner, P. Strubin, R, Marin, R. Souchet, AIP Conf. Proc., 236, 313, 1990.

[5] C. Benvenuti, R.S. Calder, G. Passardi, J. Vac. Sci. Techn., 13,6,1976, p. 1172.

[6] O. Groebner, “The LHC Vacuum System”, Proceedings of the Particle Accelerator Conference1997.

[7] D. Cheng et al., “Status of the PEP II Low Energy Ring Vacuum System”  Proceedings of the Particle Accelerator Conference1997.

[8] I. Terechkine, “Synchrotron Radiation in the VLHC”, Fermilab, Technical Division Note, unpublished note, 01/01.

[9] P. Bauer et al., “A Photon Stop for VLHC-2 – Engineering Design – Part 1”, Fermilab, Technical Division Note, TD-01-023, 04/01.

[10] P. Bauer, N. Solyak, “A Photon Stop for the VLHC-2 – Impedance Calculations”, Fermilab Technical Division Note TD-01-014, 04/01.

[11] S. Kurennoy in M. Tigner, A. Chao, “Handbook of Accelerator Physics and Engineering”, p. 207, World Scientific, 1998.