TABLE OF CONTENTS

| SECTION A -- Solicitation/Contract Form |  |
| --- | --- |
| A.1 | Summary of Changes | 2 |
| A.2 | Scope of Work | 2 |

SECTION A -- Solicitation/Contract Form

| A.1 | Summary of Changes |
| --- | --- |

The free form item ‘Scope of Work’has been edited.

| A.2 | Scope of Work |
| --- | --- |

Mechanical Removal of Cabbage Palm

CONTRACT SPECIFICATIONS

Florida Panther NWR

Naples Florida, Collier County

Project Purpose:   The purpose of this project is to restore vegetation communities in hydric pine flatwoods and wet prairies by removing cabbage palms that have invaded these communities due to hydrological changes that have occurred over the past 50 years.

Scope of Work:

"	Obligations of the U.S. Fish and Wildlife Service (FWS)

The FWS shall provide the Contractor with maps and other information to locate work sites and direct the Contractor to these sites.

The FWS shall locate sites for the storage of the Contractor's equipment as close as possible to the various work sites.

The FWS will designate refuge entry points and roads for the Contractor to access work sites.

The FWS reserves the right to move cutting operations to other units within the specified contract area when it is determined that it is for the convenience of the Government, due to weather and soil conditions, or the current site is unsuitable or unavailable for performance of the specified work.

The FWS reserves the right to restrict Contractor vehicles and equipment from using refuge roads if excessive wet conditions exist.

"	Obligations of the Contractor

The Contractor shall furnish all labor, materials, maintenance and repairs, equipment, fuel, insurance, tools, transportation and mobilization, lodging, supervision and supplies and perform all work necessary for the cutting, but not removal, of cabbage palms within designated compartments on the Florida Panther National Wildlife Refuge (FPNWR).  No equipment or supplies will be furnished by the Government.

The Contractor will provide equipment operator(s) that are qualified to operate, transport and maintain the equipment.

Work shall begin no later than 30 days after the contract is awarded depending on current ground conditions.  The actual start date will be determined during the post-award conference.

Following the contract award and issuance of a Notice To Proceed from the Government, the project will be completed within two-years from the date of the award.

The contractor shall cut all cabbage palms within the designated project sites.  The cut palms will be left in place, or piled, as directed by the FWS.  The refuge staff will designate any cabbage palm trees to be left uncut with either blue flagging or blue paint.  The Contractor shall take every precaution necessary to prevent damage to non-target trees, particularly pine trees with a DBH greater than 8 inches and all oak trees.  All cabbage palms shall be cut to within 6 inches of the ground.  However, the Contractor shall not be responsible for cabbage palms that are unsuitable for cutting due to their growing stem being in close proximity (less than 6 inches) to the ground, thus minimizing the risk of damage to equipment cutting parts.  The contractor is responsible for the restoration or replacement of all damaged non-target native trees to the satisfaction of the U.S. Fish and Wildlife Service, and at no cost to the FWS.

The contractor shall be responsible for and repair, replace or restore to original condition all property damaged as a result of any activity by the Contractor, to the satisfaction of the FWS.  This includes, but is not limited to, soil grade disturbance resulting from heavy equipment and damage to man-made structures and equipment.

Work may be postponed due to inclement weather or wet soil conditions for the purpose of preventing adverse impacts to soils and access roads, or for the convenience of the Government.

The required machinery for cabbage palm cutting (not removal) shall be a Track-type Feller Buncher with saw head that can reach and cut a 20-foot radius from the engine and track assembly. This equipment configuration will minimize the overall track travel over sensitive ground surfaces and it promotes a more efficient use of equipment and better contract value to the government.  To further minimize disturbance to habitat ground surfaces and low growth vegetation, the required machinery will also have low-ground pressure tracks that shall not exceed 4.5 psi when the cutting machine is fully fueled at its' maximum gross weight.

The Contractor may use specialized off-road equipment such as swamp buggies or ATV's to access equipment and project site.

All equipment used shall be in good repair and operating condition at all times, and be in compliance with all federal, state, and local vehicle regulations.  The equipment shall be of the proper type and sufficient size to enable the Contractor to perform the work in accordance with these specifications.   The Contractor shall furnish all fuel, oil, grease, repairs, replacement parts and other expenses incidental to the operations of their equipment.  All equipment will meet all safety standards as established for that piece of equipment.  All equipment will be operated and maintained in accordance with the manufacturer's recommendations.  All equipment shall be equipped with all appropriate safe guards, as specified by the manufacturer.  FWS reserves the right to request replacement of equipment or personnel if deemed to be unsafe or operating in an unsafe manner.

Upon completion of the work and prior to accepting the work as being completed, all trash and rubbish generated by the Contractor's operation shall be removed from Refuge land and disposed of in a designated landfill or other appropriate location.

All machinery will be equipped with approved containment systems in the event of a contaminant spill.

Onsite fueling and maintenance is permissible with the use of approved storage facilities and contaminant containment systems.

Description and Location:

The project site(s) consist of nine compartments with variable densities of trees and brush.  Dominant species of trees are Florida slash pine, species of oak trees, and cabbage palm.  The total acreage of the project site is approximately 2571 acres (see attached map).  Only designated areas within each compartment will be treated.   These areas have cabbage palm densities, of cutable size, ranging from 20 to 200 stems per acre.

Inspection and Acceptance:

The FWS reserves the right to inspect, at any time, the Contractor's procedures and to approve operating personnel.  Inspection, however, shall not relieve the Contractor of any obligations or responsibilities nor shall it transfer any liability to the FWS.  Inspection of the work performed under this contract will be made by the FWS or the designated inspector of the FWS as the work progresses and at such intervals as are necessary to insure compliance with the contract specifications and provisions.

The FWS reserves the right to require the Contractor to replace any operating personnel or equipment used in the performance of this contract if the personnel or equipment are violating, or have violated, any state or federal laws; or are unsafe; or for any valid reason.  In this event, the Contractor shall immediately, upon written or verbal (to be later reduced to writing) communication from the FWS, provide replacements satisfactory to the FWS at no additional cost.

The Contractor shall ensure that the technical specifications are being met and are in agreement with the FWS or designated Service inspector.  Upon completion of the work in a compartment, the Contractor will notify the FWS that the work within the compartment is completed and the FWS will make an overall inspection of the work completed.  If the work is accepted, the Contractor shall proceed with work on the next compartment.  If the work is not accepted by the FWS, the Contractor shall complete any remedial work as required for acceptance prior to commencing work on the next compartment.

The Government may allow an extension of the contract term if it is determined that the contractor cannot complete the contract within the normal contract period due to excessive inclement weather, high water or Government-caused delays that exceed a total of 21 days

Show Me Trip:

Prospective contractors wishing to bid on this contract will be offered the opportunity to make an onsite visit to the contract area in question.  This onsite visit is strongly suggested, in order to provide prospective contractors the necessary information to submit an accurate bid.

Table of target management units, listed in the order of cutting, with approximate acreages within each habitat type.

Fire Management Unit	Pineland (acres)	Prairie (acres)	Hammock (acres)	Total Cutting within Unit

2	320	17	3	340

6	254	10	5	269

3	196	73	0	269

8	413	0	18	431

5	231	23	17	271

4	186	11	0	197

1	356	10	41	407

7	272	15	7	294

9	68	0	25	93

Total acres	2296	159	116	2571

Grand Total:  2571 acres