TO:	EPA Docket No. EPA-HQ-OAR-2003-0146

FROM:	Bob Lucas, EPA/SPPD

DATE:	August 16, 2007

SUBJECT:	Wastewater Impact Analysis

I.	Purpose

The purpose of this memorandum is to document the potential impacts of wastewater treatment system emissions from enhanced biological treatment systems.

II.	Background

Section 112 (f) of the Clean Air Act Amendments (CAA) directs the U.S. Environmental Protection Agency (EPA) to assess source categories regulated under Section 112(d) of the CAA and determine whether any human health or environmental risks remain from the continued emissions of hazardous air pollutants (HAP) following implementation of maximum achievable control technology (MACT) standards.  The CAA further states that if the MACT standards do not reduce lifetime excess cancer risk to the most exposed individual to less than one in one million,  EPA must set additional standards to protect human health and the environment, in accordance with the interpretation set forth in the Benzene NESHAP.  Additionally, the EPA is required to review these technology-based standards and to revise them “as necessary (taking into account developments in practices, processes and control technologies)” no less frequently than every 8 years, under CAA section 112(d)(6).  The Refinery MACT 1 (40 CFR Part 63 Subpart CC) was promulgated over 8 years ago and is now being reviewed.

The standards for wastewater in the Refinery MACT 1 rule reference the Benzene Waste Operations NESHAP (BWON) of 40 CFR Part 61 Subpart FF.  One of the primary control options allowed under BWON is suppression controls until treatment in an enhanced biological treatment unit (EBU).  Subpart FF as defines EBU as any unit that “… is a suspended-growth process that generates biomass, uses recycled biomass, and periodically removes biomass from the process.”  Although some parameters ranges for EBU are provided in the general description of an EBU, operation within these parameter values are not specifically required by the rule.  As such, the level of performance for different EBU may be vastly different.

Since the development of BWON and the Refinery MACT 1, EPA developed testing procedures to better characterize the performance of EBU; these testing procedures are provided in  40 CFR Part 63 Appendix C:  Determination of the Fraction Biodegraded (Fbio) in a Biological Treatment Unit.  For most highly volatile organic compounds, 1 – Fbio represents the fraction of the mass feed to the EBU that is emitted into the air.   Therefore, requiring EBU to meet a minimum Fbio will directly impact the emissions performance of the unit.

# III.	Emission Assessment

The actual emissions from the EBU are difficult to directly measure.  In reviewing data from the 22 Facility Study, many refiners assume the emissions from their EBU are negligible.  However, if the EBU is not well-mixed or has low biomass concentrations, the emissions from the EBU can be significant.  The wastewater benzene load for each petroleum refinery was estimated using the wastewater production factors and benzene concentrations presented in EPA, 1998.  These wastewater production factors are provided in Table 1.  The production factor and concentrations in Table 1 were combined with facility-specific, process-specific production capacities reported by EIA (2006) to calculate a total benzene load and a total organic HAP load to the wastewater treatment system.   The facility-specific benzene and organic HAP loads are presented in Attachment 1.  It should be noted that the total benzene load was calculated including all wastewaters; a small fraction of this loading would not be included in a refinery’s total annual benzene (TAB) calculation.  Wastewater streams with concentrations less than 10 ppmw are exempt from the BWON rules requirements and these streams are not included in a facility’s TAB.  TABs were also projected for each refinery by not including wastewater streams with average benzene concentrations of less than 10 ppmw.  The projected TABs are also provided in Attachment 1.

Table 1.  Model Process Unit Characteristics for Petroleum Refinery Wastewater

| Process Unit | Average Flow Factora (gal/bbl)b | Average Benzene Concentrationc (ppmw)d | Average Organic HAP Concentration (ppmw) |
| --- | --- | --- | --- |
| Crude distillation | 2.9 | 21 | 140 |
| Alkylation unit | 6 | 3 | 6.9 |
| Catalytic reforming | 1.5 | 106 | 238 |
| Hydrocracking unit | 2.6 | 14 | 72 |
| Hydrotreating/hydrorefining | 2.6 | 6.3 | 32 |
| Catalytic cracking | 2.4 | 13 | 165 |
| Thermal cracking/coking | 5.9 | 40 | 75 |
| Thermal cracking/visbreaking | 7.1 | 40 | 75 |
| Hydrogen plant | 80e | 62 | 278 |
| Asphalt plant | 8.6 | 40 | 75 |
| Product blending | 2.9 | 24 | 1,810 |
| Sulfur plant | 9.7f | 0.8 | 3.4 |
| Vacuum distillation | 3 | 12 | 53 |
| Full range distillation | 4.5 | 12 | 65 |
| Isomerization | 1.5 | 33 | 117 |
| Polymerization | 3.5 | 0.01 | 0.04 |
| MEK dewaxing units | 0.011 | 0.1 | 27 |
| Lube oil/specialty processing unit | 2.5 | 40 | 75 |
| Tank drawdown | 0.02 | 188 | 840 |
| Source: U.S. EPA (1998) |
| a All flow factors were derived from Section 114 questionnaire responses |
| b gal/bbl = gallons of wastewater per barrel of capacity at a given process unit |
| c Average concentration in the wastewater |
| d ppmw = parts per million by weight |
| e This flow factor is given in gal/MM ft3 of gas production |
| f This flow factor is given in gal/ton of sulfur |

Based on the benzene loads calculated for this analysis, wastewater loads of benzene can range from 1 to 224 tons per year (tpy); the average benzene load was 46 tpy and the median benzene load was 28 tpy.  For many refineries, this benzene load is treated using the EBU provisions in the BWON rule.

Nationwide, the total organic HAP load to wastewater treatment systems is estimated to be 89,252 tpy, and the total benzene load is estimated to be 6,922 tpy (or 7.8 percent of the total HAP load).  A significant portion of the HAP and benzene wastewater load is expected to be recovered and recycled in the oil-water separator.  We assumed that 50 percent of the benzene load is recovered in the oil-water separator.  Of the remaining 50 percent benzene load, we assumed that 20 percent would be treated using stream strippers at 99 percent removal efficiencies.  Therefore, we anticipate that 2,769 tpy (i.e., 40 percent of 6,922 tpy) of benzene will be treated using EBU.  In a preliminary analysis of EBU, we estimated that the average EBU treatment efficiency would be 92 percent (Allen, 2001).  However, in this analysis, the operating parameters were limited to the “typical ranges” indicated in BWON.   As stated previously, operation within these parameter values are not specifically required by the rule.  Therefore, some operations may fall outside these ranges.  Additionally, only one model treatment plant that utilized submerged aeration was modeled.  Many refineries use surface aeration and may have significantly higher emissions than the model plant used for this preliminary analysis.

We assumed that 50 percent of the EBU had a performance of greater than 90 percent; we assumed the average performance of these EBU to be 92 percent (i.e., 8 percent emissions).  We assumed the average performance of the remaining EBU to average 80 percent (i.e., 20 percent emissions).  Based on these assumptions, the baseline emissions are projected to be 388 tpy [i.e., 2,769×(0.5×0.08 + 0.5×0.20)].  By altering the operating characteristics of the unit (e.g., changing mixing characteristics, adding submerged aeration, increasing biomass recycle to increase the biomass concentration in the unit, ), all of the units not originally achieving a 90 percent treatment efficiency are assumed to meet exactly the 90 percent Fbio requirement.  Therefore, the emissions are reduced to 249 tpy [i.e., 2,769×(0.5×0.08 + 0.5×0.10)] after achieving an Fbio of 90 percent for all of these units.  Therefore, a total benzene emission reduction of 139 tpy is estimated from the baseline.  Using the 7.8 percent benzene to HAP ratio determined previously, we estimate that the performance improvements of EBUs will also achieve a total organic HAP emission reduction of 1,782 tpy (i.e., 139/0.078).

# V.	Cost Assessment

The cost of performing an Fbio test is expected to be $25,000 per refinery.  These one-time costs were averaged over 5 years, so that the annual cost of the performance evaluation was $5,000/yr.  Once the performance evaluation is completed, refineries are expected to develop operating limits for the minimum mixed liquor suspended solids (MLVSS) concentration and the maximum food to microorganism ratio, which must be determined on a weekly basis.  Although owners and operators of EBU are expected to routinely conduct these analyses, we estimated that an additional cost of $5,000/yr would be incurred for these analyses and the associated recordkeeping and reporting requirements.  Therefore, refineries using EBU for treatment of affected wastewater streams would incur, on average, a cost of $10,000/yr over the first 5 years from the initial compliance data.

Only refineries with total annual benzene (TAB) quantities exceeding 10 Mg/yr are subject to the BWON requirements.  Using the benzene wastewater loading rates predicted using the methods reported in EPA 1998, we estimate that 113 refineries are potentially subject to an EBU performance evaluation.  Therefore, that total nationwide annual cost of the EBU performance evaluation and ongoing compliance monitoring is estimated to by $1.13-million per year.

# VI.	References

Allen, C.  2001.  Memorandum to Elaine Manning, W&CPG.  “Evaluation of air emissions from enhanced biodegradation units.  March 8, 2001.

EIA (Energy Information Agency).  2006.  Refinery Capacity Report 2006.  Prepared by the Energy Information Administration, Washington, DC. June 15.

U.S. EPA (Environmental Protection Agency).  1998.  Locating and Estimating Air Emissions from Sources of Benzene.  EPA-454/R-98-011.  Office of Air Quality Planning and Standards, Research Triangle Park, NC.

U.S. EPA (Environmental Protection Agency).  2002.  Industrial Waste Air Model Technical Background Document.  EPA-530-R-02-010.  Office of Solid Waste, Washington, DC.  http://www.epa.gov/epaoswer/non-hw/industd/iwair.htm

ATTACHMENT 1

Petroleum Refinery Wastewater Load Estimates

| Table A-1. Facility-specific Estimates of Benzene and Organic HAP Load to Wastewater |
| --- |
| Facility No. | FacName | City | State | Refinery Through-put Capacity (bbl/cd) | Total Benzene load to WWTS, tons/yr | Organic HAP load to WWTS, tons/yr | Esti-mated TAB, Mg/yr |
| 37 | Valero Energy | Delaware City | DE | 181,500 | 74.7 | 956.9 | 63.4 |
| 37.5 | Citgo Petroleum | Savannah | GA | 28,000 | 16.1 | 72.0 | 14.6 |
| 87 | Hess Corporation | Port Reading | NJ | 58,500 | 6.8 | 230.8 | 5.6 |
| 87.3 | Chevron USA | Perth Amboy | NJ | 80,000 | 31.7 | 283.4 | 28.8 |
| 87.6 | Citgo Asphalt Refining Co. | Paulsboro | NJ | 32,000 | 31.3 | 80.2 | 28.4 |
| 88 | Sunoco | Westville | NJ | 145,000 | 42.7 | 734.5 | 35.2 |
| 89 | ConocoPhillips | Linden | NJ | 238,000 | 74.1 | 1,280.0 | 62.2 |
| 90 | Valero Energy Corp. | Paulsboro | NJ | 160,000 | 61.6 | 740.0 | 52.3 |
| 105 | Sunoco, Inc. | Marcus Hook | PA | 175,000 | 46.1 | 893.2 | 38.2 |
| 106 | Sunoco, Inc. | Philadelphia | PA | 335,000 | 99.6 | 1,746.9 | 83.3 |
| 107 | ConocoPhillips | Trainer / Marcus Hook | PA | 185,000 | 52.9 | 960.3 | 44.6 |
| 140 | Giant Refining | Yorktown | VA | 58,600 | 23.3 | 303.8 | 20.3 |
| 104 | American Refining Group | Bradford | PA | 10,000 | 2.4 | 36.4 | 2.1 |
| 108 | United Refining Co. | Warren | PA | 65,000 | 27.8 | 276.6 | 23.6 |
| 147 | Ergon-West Virginia Inc. | Newell (Congo) | WV | 20,000 | 5.6 | 77.7 | 4.9 |
| 41 | PDV Midwest Refining | Lemont | IL | 167,000 | 65.1 | 853.5 | 55.1 |
| 42 | ExxonMobil Corp. | Joliet | IL | 238,500 | 95.9 | 1,262.2 | 80.4 |
| 43 | Marathon Petroleum Co. | Robinson | IL | 192,000 | 73.8 | 1,067.1 | 61.7 |
| 46 | ConocoPhillips | Wood River | IL | 306,000 | 127.5 | 1,500.7 | 110.4 |
| 47 | BP | Whiting | IN | 410,000 | 170.8 | 2,002.9 | 143.8 |
| 48 | Countrymark Cooperative | Mt. Vernon | IN | 23,000 | 8.2 | 119.1 | 6.7 |
| 53 | Marathon Petroleum Co. | Catlettsburg | KY | 222,000 | 89.2 | 1,140.4 | 73.6 |
| 54 | Somerset Refinery Inc. | Somerset | KY | 5,500 | 1.2 | 28.3 | 1.1 |
| 75 | Marathon Petroleum Co. | Detroit | MI | 100,000 | 38.6 | 476.6 | 32.8 |
| 95 | BP PLC | Toledo | OH | 131,000 | 62.9 | 718.8 | 54.4 |
| 96 | Marathon Petroleum Co. | Canton | OH | 73,000 | 28.0 | 367.0 | 23.8 |
| 97 | Valero Energy | Lima | OH | 146,900 | 61.8 | 807.3 | 52.2 |
| 98 | Sunoco, Inc. | Toledo | OH | 160,000 | 51.0 | 863.7 | 43.4 |
| 109 | Valero Energy | Memphis | TN | 180,000 | 45.3 | 967.7 | 37.2 |
| 76 | Flint Hills Resourses | Rosemount | MN | 279,300 | 136.1 | 1,355.6 | 114.0 |
| 77 | Marathon Petroleum Co. | St. Paul Park | MN | 70,000 | 28.8 | 352.0 | 23.6 |
| 94 | Tesoro | Mandan | ND | 58,000 | 14.6 | 307.1 | 12.4 |
| 148 | Murphy Oil USA Inc. | Superior | WI | 34,300 | 13.4 | 160.9 | 11.4 |
| 50 | Coffeyville Refining | Coffeyville | KS | 112,000 | 35.2 | 548.6 | 29.6 |
| 51 | National Cooperative Refinery Association | McPherson | KS | 81,200 | 32.8 | 417.0 | 26.6 |
| 52 | Frontier Oil Corp. | El Dorado | KS | 106,000 | 40.4 | 546.1 | 32.6 |
| 99 | ConocoPhillips | Ponca City | OK | 194,000 | 69.5 | 1,017.8 | 57.1 |
| 100 | Wynnewood Refining Co. | Wynnewood | OK | 54,000 | 20.7 | 266.3 | 18.1 |
| 101 | Sinclair Oil Corp. | Tulsa | OK | 70,300 | 27.7 | 326.0 | 23.1 |
| 102 | Sunoco, Inc. | Tulsa | OK | 85,000 | 27.3 | 387.4 | 23.5 |
| 103 | Valero Energy | Ardmore | OK | 83,640 | 31.9 | 403.6 | 26.7 |
| 110 | AGE Refining & Manufacturing | San Antonio | TX | 12,200 | 2.1 | 59.5 | 1.9 |
| 111 | Alon USA Energy Inc. | Big Spring | TX | 67,000 | 29.3 | 348.6 | 25.1 |
| 114 | Western Refining | El Paso | TX | 116,000 | 33.9 | 594.0 | 28.9 |
| 121 | Delek Refining Ltd | Tyler | TX | 58,000 | 18.4 | 308.3 | 15.8 |
| 125 | ConocoPhillips | Borger | TX | 146,000 | 40.5 | 795.8 | 31.5 |
| 130 | Valero Energy | Three Rivers | TX | 90,000 | 39.8 | 472.0 | 34.1 |
| 131 | Valero Energy | Sunray | TX | 158,327 | 61.8 | 842.1 | 53.8 |
| 112 | Total SA | Port Arthur | TX | 232,000 | 75.4 | 1,102.3 | 64.2 |
| 113 | BP | Texas City | TX | 437,000 | 191.9 | 2,166.2 | 159.0 |
| 115 | Citgo | Corpus Christi | TX | 156,000 | 75.0 | 735.1 | 63.4 |
| 117 | Pasadena Refining Systems | Pasadena | TX | 100,000 | 32.0 | 506.3 | 27.7 |
| 118 | ExxonMobil Oil Corp | Baytown | TX | 562,500 | 224.3 | 2,824.1 | 185.5 |
| 119 | ExxonMobil Oil Corp | Beaumont | TX | 348,500 | 139.7 | 1,737.8 | 116.7 |
| 120 | Flint Hills Resources | Corpus Christi | TX | 288,126 | 101.7 | 1,344.5 | 85.7 |
| 122 | Lyondell-Citgo Refining Co. | Houston | TX | 270,200 | 116.0 | 1,299.6 | 97.3 |
| 123 | Marathon Petroleum Co. | Texas City | TX | 72,000 | 18.3 | 353.9 | 16.3 |
| 124 | Motiva Enterprises | Port Arthur | TX | 285,000 | 97.4 | 1,307.5 | 82.7 |
| 126 | ConocoPhillips | Sweeny | TX | 247,000 | 100.3 | 1,203.6 | 84.0 |
| 127 | Valero Energy Corp. | Port Arthur | TX | 260,000 | 113.0 | 1,269.8 | 94.6 |
| 128 | Shell Oil - Deer Park | Deer Park | TX | 333,700 | 127.6 | 1,620.7 | 106.4 |
| 129 | Trigeant Ltd. | Corpus Christi | TX | 26,100 | 10.8 | 67.2 | 9.8 |
| 129.5 | South Hampton Resources | Silsbee | TX | 3,600 | 1.4 | 18.7 | 1.0 |
| 132 | Valero Energy | Corpus Christi | TX | 142,000 | 96.0 | 652.4 | 78.9 |
| 133 | Valero Energy | Houston | TX | 83,000 | 34.0 | 432.0 | 29.5 |
| 134 | Valero Energy | Texas City | TX | 213,750 | 96.4 | 1,097.6 | 80.3 |
| 1 | Gulf Atlantic Operations | Mobile Bay | AL | 16,700 | 10.3 | 55.7 | 9.3 |
| 3 | Shell Chemical LP | Saraland | AL | 80,000 | 20.6 | 379.0 | 17.4 |
| 55 | Pelican Refining Co. | Lake Charles | LA | 13,500 | 1.6 | 54.5 | 1.5 |
| 56 | Calcasieu Refining Co. | Lake Charles | LA | 30,000 | 5.0 | 133.7 | 4.3 |
| 61 | Citgo Petroleum Corp. | Lake Charles | LA | 429,500 | 169.4 | 2,052.2 | 144.9 |
| 62 | ConocoPhillips | Westlake | LA | 239,400 | 94.2 | 1,075.8 | 79.8 |
| 63 | ExxonMobil Corp. | Baton Rouge | LA | 501,000 | 178.6 | 2,440.1 | 150.5 |
| 64 | ExxonMobil Corp. | Chalmette | LA | 188,160 | 75.2 | 921.6 | 62.4 |
| 65 | Marathon Petroleum Co. | Garyville | LA | 245,000 | 123.3 | 1,232.1 | 100.6 |
| 66 | Motiva Enterprises | Convent | LA | 235,000 | 69.0 | 1,200.0 | 56.0 |
| 67 | Motiva Enterprises | Norco | LA | 226,500 | 76.4 | 1,159.0 | 65.1 |
| 68 | Murphy Oil USA Inc. | Meraux | LA | 120,000 | 53.4 | 574.0 | 46.0 |
| 69 | Valero Energy | Norco | LA | 185,003 | 76.1 | 905.6 | 64.0 |
| 71 | Placid Refining Inc. | Port Allen | LA | 56,000 | 18.2 | 281.6 | 15.8 |
| 72 | Shell Chemical Co. | St. Rose | LA | 55,000 | 10.0 | 248.6 | 9.1 |
| 73 | ConocoPhillips | Belle Chasse | LA | 247,000 | 78.5 | 1,187.0 | 67.5 |
| 74 | Valero Energy | Krotz Springs | LA | 80,000 | 20.3 | 393.2 | 17.5 |
| 78 | Chevron USA Inc. | Pascagoula | MS | 330,000 | 165.0 | 1,551.3 | 142.6 |
| 1.5 | Goodway Refining | Atmore | AL | 4,100 | 0.7 | 15.2 | 0.6 |
| 2 | Hunt Refining Co. | Tuscaloosa | AL | 34,500 | 20.9 | 115.1 | 18.2 |
| 11 | Cross Oil & Refining Co. | Smackover | AR | 7,200 | 2.7 | 11.8 | 2.3 |
| 12 | Lion Oil Co. | El Dorado | AR | 70,000 | 28.5 | 275.0 | 23.5 |
| 57 | Calumet Lubricants Co. | Cotton Valley | LA | 13,020 | 2.1 | 47.8 | 1.8 |
| 58 | Calumet Lubricants Co. | Princeton | LA | 8,300 | 3.6 | 12.5 | 3.1 |
| 70 | Calumet Lubricants | Shreveport | LA | 42,000 | 18.4 | 139.8 | 15.6 |
| 79 | Ergon Refining Inc. | Vicksburg | MS | 23,000 | 10.8 | 42.8 | 9.5 |
| 80 | Hunt Southland Refining | Lumberton | MS | - | (facility is currently idled) |
| 81 | Hunt Southland Refining | Sandersville | MS | 11,000 | 5.0 | 32.1 | 4.6 |
| 91 | Giant Refining Co. | Bloomfield | NM | 16,800 | 4.3 | 94.6 | 3.8 |
| 92 | Giant Refining Co. | Gallup | NM | 20,800 | 6.2 | 120.5 | 5.1 |
| 93 | Navajo Refining Co. | Artesia + Lovington | NM | 75,000 | 24.2 | 407.9 | 19.9 |
| 35 | Suncor Energy | Commerce City | CO | 62,000 | 21.8 | 285.1 | 18.9 |
| 36 | Suncor Energy | Denver | CO | 32,000 | 9.0 | 164.6 | 7.9 |
| 82 | Cenex Harvest States | Laurel | MT | 55,000 | 26.4 | 238.2 | 22.7 |
| 83 | ConocoPhillips | Billings | MT | 58,000 | 24.7 | 303.8 | 20.5 |
| 84 | ExxonMobil Corp. | Billings | MT | 60,000 | 27.8 | 271.9 | 23.7 |
| 85 | Montana Refining Co. | Great Falls | MT | 8,200 | 4.0 | 31.6 | 3.4 |
| 135 | Tesoro | Salt Lake City | UT | 58,000 | 14.2 | 293.1 | 12.2 |
| 136 | Chevron USA | Salt Lake City | UT | 45,000 | 15.4 | 232.0 | 13.1 |
| 137 | Silver Eagle Refining Inc. | Woods Cross | UT | 10,250 | 3.3 | 46.7 | 2.9 |
| 138 | Big West Oil Co. | Salt Lake City | UT | 29,400 | 8.0 | 150.7 | 6.5 |
| 139 | Holly Corp. | Woods Cross | UT | 24,700 | 10.7 | 127.9 | 9.1 |
| 149 | Frontier Oil & Refining Co. | Cheyenne | WY | 47,000 | 22.6 | 203.0 | 19.5 |
| 150 | Little America Refining Co. | Evansville (Casper) | WY | 24,500 | 7.5 | 120.5 | 6.5 |
| 150.5 | Silver Eagle Refining Inc. | Evanston | WY | 3,000 | 1.2 | 15.8 | 0.9 |
| 151 | Sinclair Oil Corp. | Sinclair | WY | 66,000 | 22.4 | 323.0 | 19.2 |
| 152 | Wyoming Refining Co. | Newcastle | WY | 12,500 | 3.3 | 64.4 | 2.8 |
| 4 | BP | Prudhoe Bay | AK | 12,500 | 2.1 | 58.9 | 1.9 |
| 5 | ConocoPhillips Alaska | Kuparuk | AK | 14,000 | 2.4 | 66.0 | 2.1 |
| 6 | Petro Star Inc. | North Pole | AK | 17,000 | 2.7 | 79.2 | 2.5 |
| 7 | Petro Star Inc. | Valdez | AK | 48,000 | 7.7 | 223.3 | 7.0 |
| 8 | Tesoro Petroleum Corp. | Kenai | AK | 72,000 | 18.7 | 351.8 | 16.3 |
| 9 | Flint Hills Resources | North Pole | AK | 210,000 | 36.7 | 970.1 | 33.3 |
| 14 | BP | Carson | CA | 260,000 | 97.0 | 1,367.8 | 82.9 |
| 15 | Chevron USA Inc. | El Segundo | CA | 260,000 | 100.2 | 1,343.3 | 82.6 |
| 16 | Chevron USA Inc. | Richmond | CA | 242,901 | 125.9 | 1,325.4 | 104.3 |
| 17 | Big West of CA | Bakersfield | CA | 66,000 | 26.5 | 328.5 | 23.3 |
| 18 | Shell Oil Products US | Martinez | CA | 155,600 | 74.2 | 809.0 | 62.3 |
| 19 | Shell Oil Products US | Wilmington | CA | 98,500 | 50.9 | 541.7 | 40.7 |
| 19.5 | Edgington Oil Co. | Long Beach | CA | 26,000 | 14.4 | 109.0 | 13.1 |
| 20 | ExxonMobil Corp. | Torrance | CA | 149,500 | 64.6 | 792.6 | 54.4 |
| 22 | Greka Energy | Santa Maria | CA | 9,500 | 4.9 | 29.9 | 4.4 |
| 24 | Valero Energy | Wilmington | CA | 6,200 | 2.9 | 20.2 | 2.6 |
| 25 | Kern Oil & Refining Co. | Bakersfield | CA | 26,000 | 5.3 | 124.4 | 4.5 |
| 26 | Paramount Petroleum | Paramount | CA | 50,000 | 20.2 | 202.8 | 17.7 |
| 27 | San Joaquin Refining Co. | Bakersfield | CA | 15,000 | 11.6 | 58.2 | 10.4 |
| 28 | Ten By Inc. | Oxnard | CA | 2,800 | 1.3 | 10.8 | 1.2 |
| 29 | ConocoPhillips | LA - Carson/ Wilmington | CA | 139,000 | 63.8 | 726.2 | 52.9 |
| 30.1 | ConocoPhillips | SF - Rodeo | CA | 76,000 | 37.4 | 404.6 | 31.5 |
| 30.2 | ConocoPhillips | Arroyo Grande (Santa Maria) | CA | 44,200 | 17.1 | 208.1 | 15.5 |
| 31 | Tesoro | Golden Eagle | CA | 166,000 | 72.5 | 909.0 | 61.2 |
| 32 | Valero Energy | Wilmington | CA | 80,887 | 35.7 | 424.7 | 28.6 |
| 33 | Valero Energy | Benicia | CA | 144,000 | 63.1 | 766.3 | 52.9 |
| 34 | Lunday-Thagard Co. | South Gate | CA | 8,500 | 4.6 | 27.9 | 4.2 |
| 39 | Chevron USA Inc. | Honolulu (Barber's Point) | HI | 54,000 | 19.0 | 232.3 | 16.8 |
| 40 | Tesoro Hawaii Petrol. | Kapolei | HI | 93,500 | 27.7 | 465.6 | 24.9 |
| 86 | Foreland Refining Co. | Tonopah/Eagle Springs | NV | 2,000 | 3.4 | 9.3 | 3.1 |
| 103.5 | Chevron USA | Portland | OR | 9,000 | 4.4 | 20.3 | 4.0 |
| 141 | BP | Ferndale | WA | 225,000 | 86.6 | 1,154.4 | 75.9 |
| 142 | Shell Oil Products US | Anacortes | WA | 145,000 | 49.5 | 742.9 | 41.6 |
| 144 | Tesoro | Anacortes | WA | 120,000 | 50.6 | 634.0 | 43.8 |
| 145 | ConocoPhillips | Ferndale | WA | 96,000 | 26.7 | 502.0 | 21.8 |
| 146 | US Oil & Refining Co. | Tacoma | WA | 37,850 | 13.0 | 163.7 | 11.2 |
| 153 | Hovensa LLC | Kingshill (St. Croix) | V.Isl | 495,000 | 188.4 | 2,528.4 | 158.2 |
| 155 | Shell Chemical Yabucoa Inc. | Yabucoa | P.Rico | 77,900 | 21.0 | 391.4 | 18.6 |
|  |  |  |  | Totals | 6,922 | 89,252 | 5,843 |