# NCSX

# Product Specification

# Prototype Modular Coil Winding Form

# NCSX-CSPEC-141-02-00

April 6, 2004

Prepared By: ___________________________________________________________

P. Heitzenroeder, Technical Representative for Modular Coil (WBS 14) Procurements

Concurred By: __________________________________________________________

D. Williamson, WBS Manager for Modular Coils (WBS 14)

Concurred By: __________________________________________________________

B. Nelson, Project Engineer for Stellarator Core Systems (WBS 1)

Concurred By: __________________________________________________________

F. Malinowski, PPPL Procurement QA Representative

Approved by:  __________________________________________________________

W. Reiersen, NCSX Engineering Manager

REVISIONS

| Revision No. | Affected Pgs. | Date |
| --- | --- | --- |
| Rev. 0 (Initial Release) | All | 04/05/04 |

TABLE OF CONTENTS

1	INTRODUCTION AND SCOPE	1

1.1	Introduction	1

1.2	Scope	1

2	APPLICABLE DOCUMENTS	1

2.1	Codes and Standards	1

3	REQUIREMENTS	2

3.1	Winding Form Definition	2

3.2	Characteristics	3

3.2.1	Performance	3

3.2.1.1	Mechanical and Physical Properties of Casting Alloy	3

3.2.1.2	DELETED	4

3.2.1.3	DELETED	4

3.2.1.4	Electrical Properties of the Poloidal Electrical Break	4

3.2.1.5	Surface Finish	5

3.2.1.6	Relative Magnetic Permeability	5

3.3	Design and Construction	5

3.3.1	Production Drawings	5

3.3.2	Standards of Manufacture	6

3.3.2.1	Heat Treatment	6

3.3.2.2	Repairs	6

4	Quality Assurance Provisions	6

4.1	General	6

4.1.1	Responsibility for Inspection	7

4.2	Quality Conformance Inspections	7

4.2.1	Verification of Mechanical and Physical Properties of Casting Alloy	7

4.2.2	DELETED	8

4.2.3	DELETED	8

4.2.4	Verification of the Electrical Properties of the Poloidal Break	8

4.2.5	Verification of Surface Finish	8

4.2.6	Verification of Relative Magnetic Permeability	8

4.2.7	Dimensional Inspection	8

4.2.8	Visual Inspection	8

4.2.9	Liquid Penetrant Inspection	9

4.2.10	Inspection for Internal Defects	9

5	Preparation for delivery	9

5.1	Marking	9

5.2	Cleaning	9

5.3	Crating	10

5.4	Shipping	10

# INTRODUCTION AND SCOPE

## Introduction:

Stellarators and the National Compact Stellarator Experiment

Stellarators are a class of magnetic fusion confinement devices characterized by three dimensional magnetic fields and plasma shapes and are the best-developed class of magnetic fusion devices after the tokamak.  The stellarator concept has greatly advanced since its invention by Dr. Lyman Spitzer, the founding director of the Princeton Plasma Physics Laboratory (PPPL), during the 1950’s. A traditional stellarator uses only external magnetic fields to shape and confine the plasma. The National Compact Stellarator Experiment (NCSX) is the first of a new class of stellarators known as “compact stellarators.”  The differentiating feature of a compact stellarator is the use of plasma current in combination with external fields to accomplish shaping and confinement.  This combination permits a more compact device. The NCSX project is managed by PPPL in partnership with the Oak Ridge National Laboratory. This Subcontract will be administered by PPPL.  Operation of NCSX is scheduled to begin in July 2007

## Scope

This specification establishes the manufacturing and acceptance requirements for the National Compact Stellarator Experiment (NCSX) Modular Coil Winding Forms.  There are total of (18) winding forms:  3 each of Types A, B, and C.

# APPLICABLE DOCUMENTS

## Codes and Standards

# ASTM (American Society for Testing and Materials )

# A703/A703M-01 “Specification for Steel Castings”.

A800/A800M-01 “Standard Practice for Steel Casting, Austenitic Alloy, Estimating Ferrite Content Thereof”.

# A802/A802M–95 “Standard Practice for Steel Castings, Surface Acceptance Standards, Visual Examination”.

# A 903/A903/M–99 “Standard Specification for Steel Castings, Surface Acceptance Standards, Magnetic Particle, and Liquid Penetrant Inspection”.

# Manufacturers Standardization Society of the Valve and Fittings Industry, Inc.

# MSS SP-54-2001:  “Quality Standard for Steel Castings for Valves, Flanges, Fittings, and Other Piping Components;  Radiographic Inspection Method”.

# REQUIREMENTS

## Winding Form Definition

The winding forms are austenitic (non-magnetic) stainless steel structures which are one of the most important components of the modular coils and the NCSX device.   The winding forms perform two very important functions:  (1) the conductors are wound on the winding forms, and are located in precise position by these forms; (2) the winding forms serve as their structural support during assembly and operation.  There are three distinct shapes of winding forms; six of each are required for a total of 18.  The winding forms shall be manufactured by casting followed by machining.  A machined winding form is illustrated in Fig. 3.1-1.

Figure 3.1-1 A Machined Modular Coil Winding Form.   Illustrated is one of three winding form types.

NOTE:  Figure 3.1-1 is illustrative only and not to be used for manufacture.

## Characteristics

### Performance

#### Mechanical and Physical Properties of Casting Alloy

Background

The winding form is to be cast with the alloy developed and qualified by the subcontractor during their Manufacturing Development and Prototype Manufacture. (Note: This section will be replaced with the exact chemical composition for the successful offeror prior to the award of the subcontract).

Requirement

The prototype winding form shall be fabricated from stainless steel alloy that meets the following requirements.  (Note: This section will be replaced with the properties of the successful offeror’s casting alloy prior to award of the Subcontract).

0.2% Yield strength:  >180 MPa  (>26 ksi) at room temperature (RT); >360 MPa ( >52  ksi) at 77K.

Ultimate tensile strength: >360  MPa (52 ) at RT;  >690  MPa (99.7 ksi) at 77 K.

Elongation:  30% (min.) at RT and 77 0K.

Thermal conductivity: >9.5 W/m-K at RT; >7W/m-K at 77K

Electrical Resistivity:  >83 x 10-8 m at RT; >64 x 10-8 m at 77K

Fracture Toughness: TBD

#### Electrical Properties of the Poloidal Electrical Break

The electrical resistance between any bolt to the winding form and the insulation break mid-plate to winding form shall be >500 kwhen tested at 100 VDC.

#### Surface Finish

All machined surfaces must have a RMS (root mean square) surface finish <125 -inches.  Uniform “scallops” which exceed 125 -inches, which may result from some machining processes, may be acceptable, subject to PPPL approval.

#### Relative Magnetic Permeability

The local relative magnetic permeability shall not exceed 1.02.

## Design and Construction

### Production Drawings

The Pro/Engineer CAD files listed in Table 3.3-1 shall be used to manufacture the production winding forms.  They reside in a zip file (se-141-116p.zip) located at the production winding form ftp site ( ftp://ftp.pppl.gov/pub/ncsx/manuf/producton_winding_form/ ).

Table 3.3-1 List of Pro/ENGINEER Models and Drawings

| Document Type | File Name | Rev | Description |
| --- | --- | --- | --- |

### Standards of Manufacture

#### Heat Treatment

The castings are to be heat treated per the supplier’s  approved heat treatment procedure as defined in their MIT / QA Plan for dimensional stability and materials property control prior to final measurements of mechanical properties and relative magnetic permeability.  Heat treatment records shall be prepared and maintained as defined in S21 of ASTM Spec. A703/A703M , and supplied to PPPL.  Test specimens shall be heat treated together with the castings they represent per Supplementary Requirement S22 of ASTM Spec. A703/A703M.

#### Repairs

Unacceptable defects must be repaired.  Major repairs shall be welded and documented as defined in Sections S12 and S20 of ASTM Spec. A703/A703M. Repairs shall be considered major when the depth of the cavity prepared for welding exceeds 10% of the actual wall thickness or 1”, whichever is smaller, or when the extent of the cavity exceeds approximately 10 in2.    Non-conformance reports for major repairs (which include in the disposition the proposed corrective action) shall be prepared for each major weld repair and  will be subject to the prior approval of PPPL.   Weld preparation shall be per Section S10 of ASTM Spec. A703/A703M.  Weld repairs are to be inspected per Sections 4.2.8, 4.2.9, and 4.2.10 of this specification.

# Quality Assurance Provisions

## General

Tests shall be conducted at the supplier’s facility or otherwise suitable location.

### Responsibility for Inspection

The responsibility for performing all tests and verifications rests with the supplier.  PPPL reserves the right to witness or separately perform all tests specified or otherwise inspect any or all tests and inspections.

## Quality Conformance Inspections

### Verification of Mechanical and Physical Properties of Casting Alloy

Yield Strength: The yield strength at 0.2% elongation for the cast stainless steel in the as heat-treated condition at room temperature and 77K shall be provided. Tensile test specimen coupons shall be cast with each winding form in accordance with ASTM A703/A703M-01, Supplementary Requirement 7.

Ultimate Tensile Strength and Elongation: The ultimate tensile strength and elongation for the cast stainless steel in the as heat-treated condition at room temperature and 77K shall be provided. Tensile test specimen coupons shall be cast with each winding form in accordance with ASTM A703/A703M-01, Supplementary Requirement 7.

Elastic Modulus: The elastic (Young’s) modulus at room temperature and 77K shall be provided for each casting.

Chemical Composition: The material chemical composition shall be measured and provided for each casting.

Thermal Conductivity:  The thermal conductivity of the casting alloy at room temperature and 77K shall be provided for each casting.

Electrical Resistivity: The electrical resistivity of the  casting alloy at room temperature and 77K shall be provided for each casting.

Fracture Toughness: The KIC and the Paris Constants (C, n) of the casting alloy at room temperature and 77K shall be provided for each casting.

### Verification of the Electrical Properties of the Poloidal Break

The insulation resistance of the poloidal break insulator and the insulation for each bolt shall be measured by performing an insulation resistance (Megger) test.

### Verification of Surface Finish

All machined surfaces shall be inspected for compliance with surface finish requirements specified in Section 3.2.1.3.

### Verification of Relative Magnetic Permeability

All cast surfaces and features shall be checked with a calibrated Severn Permeability Indicator for compliance with Section 3.2.1.4.  Flange faces and edges shall be checked at locations no greater than 2 inches apart and at all weld repairs.   Relative magnetic permeability measurements on all other surfaces  shall be made at locations approximately 6” apart (to approximate a 6” x 6” grid).   Relative magnetic permeability of any final machined casting that exceeds 1.02 must be documented on a nonconformance report and will require approval on a case-by-case basis. Permeabilty measurements shall be per Supplementary Requirements S24 of ASTM Spec. A703/A703M and S1 of ASTM A800/A800M, except that the results shall be expressed as relative permeability, , rather than ferrite content (FN).

### Dimensional Inspection

All cast surfaces and features shall be dimensionally checked using a Computerized Measureing Machine (CMM).   The dimensional inspections shall be performed with measurements taken to approximate a 4” x 4” grid on the shell sections and a 2” x 2” grid on the “T” sections and shall be performed in accordance with the details defined in the approved Manufacturing/Inspection/QA Plan.

### Visual Inspection

Visual surface inspection and treatment of unacceptable surface defects shall be performed per ASTM Spec. A703/A703M, paragraph 10.1.   Evaluation criteria shall be per ASTM A802/A802M, Level II using graded reference comparators available from Castings Technology International.

### Liquid Penetrant Inspection

Each casting shall be examined for surface discontinuities using liquid penetrant inspection per Supplementary Requirement S6 of ASTM Spec. A703/A703M.   Evaluation criteria shall be per ASTM A903/A903M Level I for those regions of the winding forms shown shaded in the drawings in Attachment 1 and Level II for all other areas.  Certified test reports are required per ASTM A903, Supplementary Requirement S1.

### Inspection for Internal Defects

Each casting shall be examined for internal defects as defined in ASTM Spec.A703/A703M using radiographic inspection per Supplementary Requirement S5.  Acceptance criteria shall be per MSS SP 54 for radiography.

# Preparation for delivery

## Marking

The prototype winding form shall have a serial number and its weight engraved or stamped at its outer horizontal centerline with characters 1/4” high.

## Cleaning

The prototype winding form shall be degreased/cleaned using a solvent which  must be able to dissolve grease, oils and other soils, and leave the casting residue free.  	.

## Crating

The crate shall protect the prototype winding form from shock and weather conditions, including precipitation.  The crate shall be built for moving on rollers, handling with slings from overhead cranes, and transport by forklifts.

## Shipping

Subcontractor is responsible arranging shipment, and for the safe arrival of the prototype winding form at PPPL in Princeton, New Jersey, USA. Subcontractor’s name, shipper, purchase order number, contents and gross weight shall be marked on the shipping container.

# Footnotes

Publications are available from http://www.astm.org/cgi-bin/SoftCart.exe/index.shtml?E+mystore.

Publications are available from Manufacturers Standardization Society of the Valve and Fittings Industry, Inc., 127 Park Street, NE , Vienna, Virginia 22180 .  Tel. (703)-281-6613.

The copper cladding has been removed from the prototype winding form to be fabricated by the Subcontractor in Rev. 1 of this specification.

The copper cladding has been removed from the prototype winding form to be fabricated by the Subcontractor in Rev. 1 of this specification.

http://www.castingsdev.com/

# Text boxes

Controlled Document

This is a controlled document.  Check the NCSX Procurement Web prior to use to assure that this document is current.