Solar Orbiter

Visible Imager / magnetograph (VIM)

Optical Layout

Oskar von der Lühe1 and Achim Gandorfer2

1)  Kiepenheuer-Institut für Sonnenphysik, Freiburg, Germany

2)  Institut für Astronomie, Eidgenössische Technische Hochschule, Zürich, Switzerland

June 2000

Introduction

We studied the optical layout for the Visible Imager and Magnetograph (VIM) for the Solar Orbiter Mission based on a filtegraph concept which includes a tandem Fabry-Pérot interferometer. The optics consists of three subsystems:

- 25 cm High Resolution Telescope (HRT)

- 6 cm Full Disk Telescope (FDT)

- Filtergraph Optics (FO)

The two telescopes, HRT and FDT, deliver an image of the sun at a common telescope focal plane. The FO produces a magnified image of the telescope focus on the instrument's only detector. While the HRT provides an image with a high resolution at its diffraction limit, the FDT adjusts its focal length such as to fill the detector with the full solar disk. The filtergraph optics include a tandem Fabry-Pérot interferometer equipped with a narrow-band interference filter as a prefilter, tuned to the Na D 589 nm line. The Magneto-Optical filter which was  originally included in the design is unable to adjust to the lineshifts due to sun-spacecraft relative velocities up to 40 km s-1. We describe all components in the following sections.

High Resolution Telescope

The HRT is a 25-cm-diameter Gregorian reflector. It provides the high-resolution image, with a spatial resolution as high as 37 km on the solar surface during the near-Sun orbital phase. The telescope has an F/17 focus with a radius of 5.2 mm and an effective focal length of 4250 mm. The full field of view is 0.138 degrees or 8.3 arc minutes.

A broad-band interference filter covers the entire telescope and reflects most of the incident sunlight, with the exception of the spectral range of interest. This makes a field stop at the primary focus unnecessary. The F/2 primary mirror produces a solar image at its (primary) focus whose diameter varies between 5 mm and 25 mm throughout the orbital phases of the spacecraft. A combination of decentering and tilt of the secondary mirror provides telescope pointing on the solar disk without disturbing the image quality. Baffling at the focus and at intermediate pupils rejects remaining sunlight. Secondary magnification is 8.5.

A polarisation modulator is foreseen in the optical path behind the main mirror in the F/17 beam and before the first oblique reflection.

Figure 1 shows an annotated perspective view of the HRT and FO. Table 1 shows the surface design data which are used in this document.

Figure 1: perspective view of the optical layout of high resolution telescope and filtergraph.

Full Disk Telescope

It is impractical to combine the functions of full-disk and high resolution viewing of the sun into a single telescope. Therefore, a separate telescope will provide a full disk image at the same position as the secondary image of the HRT. The filtergraph is therefore shared by both telescopes. A folding mirror which delivers the FDT image is movable and can be inserted into the optical path of the HRT. The mechanism will be such that the mirror will be removed from the optical beam in the case of a mechanism failure. The high resolution function will therefore have precedence.

The FDT consists of a 6-cm diameter refractor with a variable focal length which provides a full-disk image with the same diameter during all orbital phases. A zoom range of 3.5:1 is needed to fully fill the detector throughout the later orbital phases between 0.2 and 0.7 AU. A separate mechanism will provide the zoom function.

Figure 2 shows the annotated optical layout of the FDT from a similar point of view as the HRT in Figure 1. Note that the layout is "horizontal" (in the XZ plane) compared to the vertical (YZ plane) layout of the HRT proper. A separate modulator is necessary for the FDT in order to perform polarisation modulation within the centered optical path before the first oblique reflection. The preliminary surface design data of the FDT are given in Table 1. The zoom lens consists of a PNP triple lens made from singlets, because chromatic aberrations are of no concern with a single wavelength narrow-band filtergraph. The zoom lens may be replaced by an exchange mechanism for discrete objectives during a refinement of the design.

Figure 2: perspective view of the optical layout of the full disk telescope.

Filtergraph Optics

The FO consists of two singlet lenses which combine the functions of collimator and camera witha 1:2 magnification. A system of two off-axis paraboloid mirrors provide a 1:1 pupil relay function and produce an F/132 telecentric intermediate image plane.

Two 50 mm diameter  Fabry-Pérot etalons at the telecentric image plane provide the required spectral resolution of typically 3 pm. If necessary, a separate narrow band interference filter will block the secondary transmission maxima of the combined etalons. The gap width of the two etalons are electronically controlled to also provide spectral scanning over a (50 pm range which is sufficiently large to cover both line width and sun-spacecraft velocity shifts.

The principle proposed here is the same as used in the TESOS filtergraph which operates at the Vacuum Tower Telescope of the Kiepenheuer-Institut on Tenerife.

Figure 3 shows a plane view of the filtergraph optics. The etalons are not included but their position indicated.

Overall Configuration

The combination of all optical subsystems is shown in Figure 4. The HRT is the large cylinder on top of the Y and Z views. The FDT is to the lower left of the Z view and near the bottom of the X view. The FO are to the lower left of the Z view and near the top of the X view.

Figure 3: optical arrangement of filtergraph optics.

Figure 4: plan views (top left: Y, top right: Z, bottom: X) of the combined VIM. The HRT is arranged above the FDT and the FO, both of which are mounted on a common optical bench. The optics fit a 300 mm x 400 mm x 1600 mm envelope.

Solar Orbiter Magnetograph - High Resolution Telescope

SRF      RADIUS      THICKNESS   APERTURE RADIUS   GLASS  NOTE

OBJ       --        1.4900e+14    1.7944e+11         AIR  Solar Surface at 1 AU

AST       --        700.000000    125.000000         AIR  Entrance aperture

2   -1.0000e+03   -500.000000    125.842994        REFL  Main Mirror

3        --       -150.000000      0.602139         AIR  Primary Focus

4    268.422000    150.000000     38.029882        REFL  Secondary Mirror

5        --        500.000000     33.222977         AIR  Primary Focus on return beam

6        --        100.000000     20.732507         AIR  Primary Mirror on Return beam

7        --         50.000000     25.000000         BK7  Modulator

8        --         50.000000     25.000000         AIR

9        --            --         16.161891         AIR

10        --            --         16.161891        REFL  Folding Mirror 1

11        --       -200.000000     16.161891         AIR

12        --            --         11.165703         AIR

13        --            --         11.165703        REFL  Folding Mirror 2

14        --        242.078619     11.165703         AIR

15        --        100.000000      5.118352         AIR  Intermediate focus

Solar Orbiter Magnetograph - Full Disk Telescope

SRF      RADIUS      THICKNESS   APERTURE RADIUS   GLASS  NOTE

OBJ       --        1.4900e+14    3.1211e+12         AIR  Solar Surface at 1 AU

1        --        400.000000     28.378806         AIR  Entrance aperture

AST       --            --         20.000000         AIR

3    352.681541      8.000000     25.000000         BK7  First lens of zoom system

4        --        109.200000     25.000000         AIR

5   -149.042262      5.000000     25.000000         BK7  Second lens of zoom system

6   -275.699183 V   77.800000     25.000000         AIR

7    112.330000      8.000000     25.000000         BK7  Third lens of zoom system

8    300.726795 V   49.700000     25.000000         AIR

9        --         20.000000     20.000000         BK7  Modulator

10        --         50.000000     20.000000         AIR

11        --            --         16.080690         AIR

12        --            --         16.080690        REFL  Folding mirror 1

13        --       -100.000000     16.080690         AIR

14        --            --         12.146739         AIR

15        --            --         12.146739        REFL  Folding mirror 2

16        --        100.000000     12.146739         AIR

17        --          1.023967      8.212789         AIR  Intermediate focus

Solar Orbiter Magnetograph - Filtergraph Optics

SRF      RADIUS      THICKNESS   APERTURE RADIUS   GLASS  NOTE

15        --        100.000000      5.118352         AIR  Intermediate focus

16    113.628966     10.000000     15.000000         BK7  | Collimator Lens

17    -98.316225    109.850909     15.000000         AIR  |

18        --        400.000000      3.048863         AIR  Pupil 1

19   -800.000000   -400.000000     22.806033        REFL  Off-axis paraboloid 1

20        --       -400.000000     19.757170         AIR  Telecentric image plane

21    800.000000        --         22.790932        REFL  Off-axis paraboloid 2

22        --        400.000000     22.790932         AIR

23        --        190.149091      3.048863         AIR

24    225.582023     10.000000     15.000000         BK7  | Camera Lens

25   -200.980693    202.520691     15.000000         AIR  |

26        --          1.931746     10.259100         AIR

IMS       --            --         10.236975              Detector surface

Table 1: optical design data of HRT, FDT, and FO.

# Text boxes

Primary Mirror

Entrance Aperture

Modulator

Telescope Focus

FPI focus

Detector

Primary focus with field stop

Telescope focus

Movable folding mirror

Zoom lens arrangement

Modulator

Telescope focus

Detector focus

Off-axis paraboloid

Off-axis paraboloid

FPI etalon position