I.  Worker Protection needed during construction- Ensure the specifications and plans address the following:

|  | Acceptable | Not Acceptable | Not Applicable |
| --- | --- | --- | --- |
| Identify the applicable occupational exposure limits/industrial hygiene standards, including ACGIH, OSHA, and DOE Exposure Standards e.g., 8-hour time-weighted average (TWA) concentration, short-term exposure level (STEL), peak or ceiling concentration, or average sound pressure level dBA, and Action Levels. |  |  |  |
| Commit to monitor for occupational exposure limits and to provide BNL with copies of assessment results and reports. |  |  |  |
| Commit to provide BNL with all sampling data and reports utilized in the exposure determination, including the chain of custody, field sampling forms, and laboratory results. |  |  |  |
| Commit to communicate to BNL on any exposures that impact BNL workers or building occupants impacted by the construction operation. |  |  |  |
| Commit to use low hazard material of construction where feasible, including avoidance of isocyanate and epichlorhydrin polymers. |  |  |  |
| State the required PPE (e.g., respiratory protection or other PPE). |  |  |  |
| Describe any required additional control measures, (including engineering, administrative, work practice controls, and/or personal protective equipment), to reduce worker exposure. |  |  |  |
| Determine if the construction will trigger a need for Medical Surveillance. |  |  |  |
| Determine if the construction will trigger a need for new or additional Training for the exposed workers. |  |  |  |
| Require all chemicals brought onsite to be stored, and handled safely. MSDSs are to be readily available to all workers on site. |  |  |  |
| Require all work changes to be thoroughly evaluated for safety concerns prior to implementation. |  |  |  |
| Require all workers to be fully informed of the hazards and controls. |  |  |  |
| Identify measures to be taken if unforeseen hazards are encountered. |  |  |  |
| Provides a clear chain of command for safety and health activities (safety and health personnel). |  |  |  |
| Provides an Emergency Response Contingency Plan and Emergency Action Plan |  |  |  |
| Identifies the need for, and documents, specific plans required by regulations such as: confined space program, respiratory protection program, etc. |  |  |  |

## INDUSTRIAL HYGIENE GROUP

## Review of Construction & Renovation Designs, Specifications, and Health & Safety Plans

IH60700 Attachment 9.1  page 2 of ___

II.  Design ramifications on future or current occupancy- Ensure the specifications and plans address the following:

|  | Acceptable | Not Acceptable | Not Applicable |
| --- | --- | --- | --- |
| HVAC system is designed to provide adequate makeup air for the occupancy of the building. |  |  |  |
| HVAC system in laboratory and chemical use areas is one-pass, and is designed to prevent chemical laden air from entering areas where chemicals are not used or to be re-entrained into a recirculation HVAC supply. |  |  |  |
| Toxic exhaust systems are located as necessary for source of hazards. |  |  |  |
| Laser facilities have appropriate interlock systems designed. |  |  |  |
| Compressed gas lines are constructed of the proper materials depending on the gas involved. |  |  |  |
| Monitors are set up and appropriate for the gases involved. |  |  |  |
| Toxic Exhaust ventilation systems are designed with single pass and adequate make up air to maintain negative pressure in chemical use areas and to prevent chemical laden air from re-entraining into a recirculation HVAC supply. |  |  |  |
| Toxic Exhaust ventilation systems with a laboratory hood containment design are acceptance certified by the contractor to deliver 100 fpm face velocity with the opening fully open. |  |  |  |
| Toxic Exhaust ventilation systems with an exhaust cleaning technology (HEPA filter, Sorbent filter, or scrubber) are acceptance certified by the contractor to meet manufacturer’s specification for collection efficiency. |  |  |  |
| Toxic Exhaust ventilation systems with an exhaust cleaning technology (HEPA filter, Sorbent filter, or scrubber) are designed with sampling ports for future surveillance testing. |  |  |  |
| Chemical use areas are designed with eyewash and safety shower that meet ANSI Z358.1 specification, including tepid water delivery, travel distance and obstruction-free pathway from the chemical use point)s) to the emergency equipment. |  |  |  |
| Occupied areas are provided with adequate restroom and lunchroom facilities for the planned occupancy of the building. |  |  |  |
| Specialty areas are designed for the specific hazards. |  |  |  |

Revisions or Corrective Actions Recommended

| Review Item # | Document Reference (Page or Section#) | Comment/Recommendation |
| --- | --- | --- |