# Literature Survey for

## Creation of a Set of Benchmark Experiments

to Validate the LAHET Code System and MCNPX

Farzad Rahnema and Nolan Hertel

# Co-Principal Investigators

Nuclear Engineering and Health Physics Programs

G. W. Woodruff School of Mechanical Engineering

Georgia Institute of Technology

February, 1999

The objective of this report is to present the results of the benchmark experiment

literature survey for the Accelerator Production of Tritium program.  A comprehensive search has been conducted to identify and collect literature that is appropriate for benchmarking and validating the LAHET Code System and MCNPX.  Summaries for the literature reviewed are presented in the following listings and tables.

A list of the technical journals and proceedings from conferences and symposiums that have been reviewed is presented in Table 1.  The journals listed were systematically researched from the most recent issue back to the earliest.  Relevant conferences and symposiums are thoroughly researched for useful experiments and references.

Following Table 1 is a list of all of the relevant literature that has been located. The listing consists of 88 papers, which have been reviewed for content and pertinent information.  Detailed descriptions of these papers are listed in Table 2, which includes information on target geometry and composition, beam type and energy, measured and calculated parameters, and codes used for any calculations.

Table1- Reviewed Literature

| No. | Journal | Years | Call number |
| --- | --- | --- | --- |
| 1 | Annals of Nuclear Energy | 1980-1997 | TK 9001 .A55 |
| 2 | Nuclear Science and Engineering | 1958-1997 | QC 770 .N8 |
| 3 | Nuclear Instruments and Methods in Physics and Research | 1961-1983 | QC 786 .N75 |
| 4 | Nuclear Instruments and Methods in Physics and Research (Section A) | 1984-1997 | QC 786 .N752x |
| 5 | Nuclear Instruments and Methods in Physics and Research (Section B) | 1984-1997 | QC 786 .N753x |
| 6 | Radiation Measurements (nuclear track and radiation measurements) | 1982-1997 | QC 787 .N83 N8x |
| 7 | Radiation Research | 1980-1997 | QC 770 .R3 |
| 8 | Radiation Protection Dosimetry | 1981-1997 | QC 795.32 .R3 .R32x |
| 9 | Health Physics | 1980-1995 | QH505 .A1 .H4 |
| 10 | CERN | 1980-1997 | Q770 .E82 |
| 11 | Nuclear Physics A | 1980-1997 | QC173.N8838 |
| 12 | Nuclear Physics B | 1996, 1997 | QC173.N8839 |
| 13 | Annals of Physics | 1997 | QC1.A72 |
| 14 | Physical Report | 1997 | QC 1.P6563x |
| 15 | Physics Today | 1997 | QC 1.P658 |
| 16 | Physics of Particles & Nuclei | 1997 | QD793.F5913 |
| 17 | Physics of Atomic Nuclei( | 1993-1997 | QC173.I252x |
| 18 | Soviet Journal of Nuclear Physics | 1980-1993 | QC173.I252x |
| 19 | Physics Letters | 1997 | QC 1.P6561x |
| 20 | Physical Review A | 1981, 1997 | QC 1.P42x |
| 21 | Physical Review B | 1981, 1997 | QC 176.A1 P4x |
| 22 | Physical Review C | 1980-1997 | QC 770.P45 |
| 23 | Physical Review D | 1980-1997 | QC 771.P4x |
| 24 | Physical Review Letters | 1997 | QC 1.P43 |
| 25 | American Nuclear Society- Transactions | 1980-1997 | QC 770.A46x |
| 26 | Particle Accelerators | 1979-1990 | QC 787.P3 P35 |
| 27 | Proceedings from the Symposium on Neutron Cross-Sections From 10 to 40 MeV | 1977 |  |
| 28 | Proceedings from the Symposium on Neutron Cross-Sections From 10 to 50 MeV | 1980 |  |
| 29 | Nuclear Cross Section for Technology Proceedings | 1980 |  |
| 30 | Health Physics of Radiation Generating Machines. Proceedings of the 20th mid year topical symposium of the Health Physics Society | 1987 |  |
| 31 | Proceedings from the First Annual Specialists’ Meeting on Shielding Aspects of Accelerators, Targets, and Irradiation Facilities. (SATIF-1) | 1994 |  |
| 32 | Proceedings from the Second Annual Specialists’ Meeting on Shielding Aspects of Accelerators, Targets, and Irradiation Facilities. (SATIF-2) | 1995 |  |
| 33 | Proceedings from the First Annual Specialists’ Meeting on Simulating Accelerator Radiation Environments (SARE-1) | 1993 |  |
| 34 | Proceedings from the International Collaboration on Advanced Neutron Sources (ICANS 3, 5, 6, 8, 9, 10, 12, 13) | 1979-1995 |  |

List of relevant literature.

1.  Gautan D. Badhwar, et al.  “Measurements of the Secondary Particle Energy Spectra in the Space Shuttle,”

Radiation  Measurements,  24, No.2, 129-138 (1995).

2a.  J.V. Siebers, et al.  “Shielding Measurements for 230-MeV Protons,” Nucl. Sci. and Eng. 115, 13-23 (1993).

2b.  J.V. Siebers, et al.  “Shielding Calculation for 230-MeV Protons Using the LAHET Code System,”  Nucl. Sci. Eng.,

122, 258-266 (1996).

3.  V.I. Belyakov-Bodin, et al.  “Heat Deposition in Targets Bombarded by Medium-Energy Protons,”  Nucl. Instr. and Meth.,

A 335, 30-36 (1993).

4.  T. A. Broome, et al.  “Particle Distribution Around a Copper Beam Stop for 72 MeV Protons,” Health Phys., 44, No.5,

487-499 (1983).

5.  Claudio Birattari and Annalisa Salomone, “Neutron Spectrum Measurements at a 40 MeV Proton Cyclotron,”

Health Phys., 49, No. 5, 919-936, (1985).

6.  Toshio Ishikawa and Takashi Nakamura, “Thermalization of Accelerator-Produced Neutrons in a Concrete Room,”

Health Phys., 60, No.2, 209-221 (1991).

7.  Lutz E. Moritz, “Measurement of Neutron Leakage Spectra at a 500-MeV Proton Accelerator,” Health Phys.,

56, No.3, 287-296 (1989).

8a.  JAERI-Data/Code 96-029, “Neutron Fluxes in and Around Iron Beam Stop Irradiated by 500  MeV  Protons.”

8b.  Yoshio Arakita, et al.  “Study of an Iron Beam Stop for 500 MeV Protons.”  Nucl. Instr. and Meth. 164, 255-265 (1979).

8c.  Syuichi Ban, et al.  “Measurements of Secondary Neutron Fluxes Around Beam Stop for 500 MeV Protons.”  Nucl.

Instr. and Meth.  184, 409-412 (1981).

9.  V.I. Belyakov-Bodin, et al.  “Calorimetric Measurements of the Spatial Component of Heat Deposition in Targets

from Beryllium, Carbon, and Aluminum Bombarded by Medium-Energy Protons,”  Nucl. Instr. and Meth., A 379,

50-56 (1996).

10.  V.I. Belyakov-Bodin, et al.  “Calorimetric Measurements of the Spatial Component of Heat Deposition in Targets

from Lead and Bismuth Bombarded by Medium-Energy Protons,”  Nucl. Instr. and Meth. A 373, 316-319 (1996).

11.  D. R. Nethaway, et al.  “Neutron Spectra from 30-MeV Deuterons on a Thick Beryllium Target,” Proceedings from the

Symposium on Neutron Cross-Sections From 10 to 40 MeV (1977).

12.  R. G. Graves, et al.  “Thick Target Neutron Yields From the d-Be Reacction at  Ed=15.6, 29.9 and 49.0 MeV,” Proceedings

from the Symposium on Neutron Cross-Sections From 10 to 40 MeV (1977).

13.  C.E. Nelson, et al., “Neutron Spectra from Deuteron and Proton Bombardment of Thick Lithium Targets, “

Proceedings from the Symposium on Neutron Cross-Sections From 10 to 40 MeV (1977).

14.  S. Cierjacks, et al.  “Neutron Yields and spectra From 590 MeV (p,n) Reactions on Lead Targets,” Proceedings

from the Symposium on Neutron Cross-Sections From 10 to 50 MeV (1980).

15.  M.A. Lone and B.C. Robertson, “Low Energy Neutron Emission from Be(d,n) and Be(p,n) Reactions,”

Proceedings from the Symposium on Neutron Cross-Sections From 10 to 50 MeV (1980).

16.  S. D. Howe, et al.  “Neutron Spectrum At 900 From 800 MeV (p,n) Reactions on a Ta Target,”  Nuclear Cross Section for

Technology Proceedings (1980).

17.  D.L. Johnson , et al.  “Thick Target Neutron Yields and Spectra from the Li (d,xn) Reaction at 35 MeV,”

Proceedings from the Symposium on Neutron Cross-Sections From 10 to 50 MeV (1980).

18.  J. S. Fraser, P.M. Garvey and J. C.D. Milton, “Neutron production in Thick Targets of Lead, Thorium and Uranium

Bombarded by 480 MeV protons,” Proceedings from the Symposium on Neutron Cross-Sections from 10 to 50 MeV (1980).

19.  S.L. Eaton, C.A. Beard, and M.L. Adams, “Comparison of LAHET Code System Calculations with Experimental

Results for Protons of Energies Less than 50 MeV Incident on Copper and Iron,”  Nucl. Sci. Eng., 125, 249 (1997).

20.  Toshio Ishikawa et al., “Neutron Penetration Through Iron and Concrete Shields with the Use of 22.0- and 32.5-MeV

Quasi-Monoenergetic Sources,”  Nucl. Sci. Eng., 116, 278 (1994).

21.  Yoshitomo Uwamino, “Measurement of Neutron Activation Cross Sections of Energy up to 40 MeV Using

Semimonoenergetic p-Be Neutrons,”  Nucl. Sci. Eng., 111, 391 (1992).

22a.  Yoshitomo Uwamino et al., “Penetration Through Shielding Materials of Secondary Neutrons and Photons Generated

by 52-MeV Protons,”  Nucl. Sci. Eng., 80, 360 (1982).

22b.  Kazuo Shin et al., “Penetration of Secondary Neutrons and Photons from a Graphite Assembly Exposed to 52-MeV

Protons,”  Nucl. Sci. Eng., 71, 294 (1979).

22c.  Takashi Nakamura, et al.  “Spectral Measurements of Neutrons and Photons from Thick Targets of C, Fe, Cu, and Pb

by 52 MeV Protons.”  Nucl. Instr. and Meth., 151, 493-503 (1978).

22d.  Kazuo Shin, et al.  “Spectral Measurements of Neutrons Produced by 52 MeV Protons with Activation Detectors.”

Nucl. Instr. and Meth., 187, 587-594 (1981).

22e.  Takashi Nakamura et al., “Neutron Production from Thick Targets of Carbon, Iron, Copper, and Lead by 30- and 52-

MeV Protons,”  Nucl. Sci. Eng., 83, 444 (1983).

23.  William W. Wadman III, “Shielding of Neutrons from 80-MeV Alpha-Particle Bombardment of Tantalum,”  Nucl.

Sci. Eng., 35, 220 (1969).

24.  A.M. Kalend et al., “Energy and Angular Distributions of Neutrons from 90 MeV Protons and 140 MeV Alpha-

particle Bombardment of Nuclei,”  Phys. Rev. C 28, 237 (1983).

25.  K. Shin, et al.  “Transmission of Medium Energy Neutrons Through Concrete Shields.”  Rad. Prot. Dos. 37, 175

(1991).

26a.  Shun-ichi Tanaka and Takashi Nakamura, et al., “Shielding Experiments and Analysis at 90 Mv AVF Cyclotron

Facility, TIARA.”  (Quasi-monoenergetic neutron source) SATIF 1, p.195 (1994).

26b.  Shun-ichi Tanaka and Takashi Nakamura, et al., “Shielding Experiments and Analysis at 90 Mv AVF Cyclotron

Facility, TIARA.”  (Transmission through concrete and iron shields) SATIF 1, p.195 (1994).

26c.  Shun-ichi Tanaka and Takashi Nakamura, et al., “Shielding Experiments and Analysis at 90 Mv AVF Cyclotron

Facility, TIARA.”  (Cavity and Labyrinth Experiments) SATIF 1, p.195 (1994).

27.  Y. Uwamino, et al., “Study on Bulk Shielding of an 800-MeV Proton Accelerator.”  SATIF 1, p. 185 (1994).

28.  R. Michel, et al.  “Nuclide Production by Proton-Induced Reactions on Elements (6 ( Z ( 29) in the Energy Range

from 800 to 2600 MeV.”  Nucl. Instr. and Meth., B 103, 183-222 (1995).

29.  Th. Schiekel, et al.  “Nuclide Production by Proton-Induced Reactions on Elements (6 ( Z ( 29) in the Energy Range

from 200 to 400 MeV.”  Nucl. Instr. and Meth., B 114, 91-119 (1996).

30.  Kazuo Shin, et al.  “Transmission of Intermediate Energy Neutrons and Associated Gamma Rays Through Iron, Lead,

Graphite, and Concrete Shields.”  Nucl. Sci. Eng. 109, 380-390 (1991).

31.  R. Michel, et al.  “On the Depth Dependence of Spallation Reactions in a Spherical Thick Diorite Target

Homogeneously Irradiated by 600 MeV Protons.”  Nucl. Instr. and Meth. B16, 61-82 (1986).

32.  R.G. Vasil'kov, et al.  “Neutron Yields and Thermal Neutron Fluxes in a Lead-Water System Bombarded by High

Energy Protons.”  Sov. At. Energy, 25, 1307 (1968).

33.  D. West and E. Wood.  “Neutron Yield from Protons and Deuterons of Momenta between 0.85 and 1.7 GeV/c Totally

Absorbed in Lead.”  Canadian Jour. Phys., 49, 2061 (1971).

34a.  M.A. Lone, et al.  “Total Neutron Yields from 100 MeV Protons on Pb and 7Li Targets.”  Nucl. Instr. and Meth. 214,

333-339 (1983).

34b.  R.T. Jones, et al.  “Measured and Calculated Neutron Yields for 100 MeV Protons on Thick Targets of Pb and Li.”

ICANS-VI, 583-603 (1982).

35.  D.K. Bewley, et al.  “New Neutron Sources for Radiotherapy.”  Phys. Med. Biol., 29, No. 4, 341-349 (1984).

36.  H.M. Butler, et al.  “Half-value Thicknesses of Ordinary Concrete for Neutrons from Cyclotron Targets.”  Health

Phys., 24, 438-439 (1973).

37.  N.M.J. Crout, et al.  “Neutron Physics Studies Relating to Cancer Therapy on the Clatterbridge Cyclotron.  Rad. Prot.

Dosi., 23, 381-384 (1988).

38.  W.E. Fisher, et al.  “On the Neutronics of SINQ, A Continuous Spallation Neutron Source.”  Nucl. Instr. and Meth.,

A249, 116-122 (1986).

39.  C. B. Fulmer, et al.  “Radiation Leakage Through Thin Cyclotron Shield Walls.”  Particle Accelerators, 4, 63-68

(1972).

40.  K. Hayashi and T. Nakamura.  “Evaluation of Neutron Skyshine from a Cyclotron.”  Nucl. Sci. Eng., 87, 123-135

(1984).

41.  H. Conde, et al.  “Time of Flight Measurements of the Energy Spectrum of Neutrons Emitted from a Spallation

Source and Moderated in Water.”  Nucl. Instr. and Meth. A261, 587-590 (1987).

42.  M.A. Lone, et al.  “Total Neutron Yield from 100 MeV Protons on Cu, Fe, and Th.”  Nucl. Instr. and Meth. A256, 135-

142 (1987).

43.  H.A. O'Brien.  “Utilization of an Intense Beam of 800 MeV Protons to Prepare Radionuclides.”  Nucl. Instr. and

Meth., B40/41, 1126-1131 (1989).

44.  Y. Uwamino, et al.  “Semi-Monoenergetic Neutron Field for Activation Experiments up to 40 MeV.”  Nucl. Instr. and

Meth. A271, 546-552 (1988).

45.  Tatsushi Nakamoto, et al.  “Spallation Neutron Measurement by the Time-of-Flight Method with a Short Flight Path.”

Jour. of Nucl. Sci. and Tech., 32 (9), 827-833 (Sept. 1995).

46.  Y. Sakamoto, et al.  “Source Neutron Spectrum in Streaming Experiment at TIARA.”  JAERI Review, 96-012 (6.5),

123-125.

47.  H. Takada, et al.  “Measurement and Analysis of Reaction Rate Distribution on Thick Tungsten Target Surface for

0.895 and 1.21 GeV Proton Bombardment.”  JAERI Review, 97-011 (10.4), 220-222.

48.  A. Mazal, et al.  “Shielding Measurements for a Proton Therapy Beam of 200 MeV:  Preliminary Results.”  Rad.

Prot. Dos.,  70 (1-4), 429-436 (1997).

49.  L.R. Veeser, et al.  “Neutrons Produced by 740-MeV Protons on Uranium.”  Nucl. Instr. and Meth., 117, 509-512

(1974).

50.  B.M. Preedom, et al.  “The Response of Plastic Scintillator to Stopping Protons in the Energy Range 70 to 100 MeV.”

Nucl. Instr. and Meth., 133, 311-314 (1976).

51.  A. Fasso and M. Höfert.  “Distributions of Secondary Particles Around Various Targets Exposed to 50 MeV Protons.”

Nucl. Instr. and Meth., 133, 213-218 (1976).

52.  M.A. Lone, et al.  “Thick Target Neutron Yields and Spectral Distributions from the 7Li (dp, n) and 9Be(dp,n) Reactions.”

Nucl. Instr. and Meth., 143, 331-344 (1977).

53.  C.A. Goulding and J.G. Rogers.  “Measurements and Calculations of Reaction Losses of Medium-Energy Protons in

NaI Detectors.”  Nucl. Instr. and Meth., 153, 511-515 (1978).

54.  M.A. Lone, et al.  “Characteristics of Neutrons from Be Targets Bombarded with Protons, Deuterons, and Alpha

Particles.”  Nucl. Instr. and Meth., 189, 515-523 (1981).

55.  H.H. Chen, et al.  “A Measurement of Stopped (+ Decays in a Copper Beam Dump With Incident Protons of 720

MeV.”  Nucl. Instr. and Meth., 160, 393-405 (1979).

56.  B.N. Belyaev, et al.  “Isotope Effects in Fragment Yields in Uranium Nuclear Fission Induced by Intermediate-Energy

Protons.”  Phys. Atom. Nuc., 57, 1163-1166 (1994).

57.  B.N Belyaev, et al.  “Measurement of the Yields of the Nuclear Reaction Products with a Mass Spectrometer On-Line

with a Proton Accelerator at Ep = 1 GeV.” Sov. Jour. Nuc. Phys., 24, 617-619 (1977).

58.  M.M. Meier, et al.  “Neutron Yields from Stopping- and Near-Stopping-Length Targets for 256-MeV Protons.”  Nucl. Sci.

and Eng., 104, 339-363 (1990).

59.  D.M. Drake, et al.  “Experimental Simulation of Martian Neutron Leakage Spectra.”  Nucl. Instr. and Meth., A309, 575-

580 (1991).

60.  Shin-ichiro Meigo, et al.  “Measurements of Spallation Neutrons from a Thick Lead Target Bombarded with 0.5 and 1.5

GeV Protons.”  ICANS-XIII, T-2 (1995).

61a.  T.O. Brun, et al.  “LAHET Code System/ CINDER'90 Validation Calculations and Comparison with Experimental

Data.”  ICANS-XII, T-26 (1993).

61b.  J.S. Gilmore, et al.  “Fertile-to-Fissile and Fission Measurements for Depleted Uranium and Thorium Bombarded by

800-MeV Protons.”  Nucl. Sci. and Eng., 99, 41-52 (1988).

61c.  G.J. Russell, et al.  “Fertile-to-Fissile and Fission Measurements for Depleted Uranium and Thorium Bombarded by

800-MeV Protons.”  ICANS-V, 621-639 (1981).

61d.  V.I. Belyakov-Bodin, et al.  “Calorimetric Measurements of Medium-Energy Protons Bombarding Beryllium, Carbon,

and Aluminum Targets.”  Nucl. Instr. and Meth., A314, 508-513 (1992).

61e.  V.I. Belyakov-Bodin, et al.  “Calorimetric Measurements and Monte Carlo Analyses of Medium-Energy Protons

Bombarding Lead and Bismuth Targets.”  Nucl. Instr. and Meth., A295, 140-146 (1990).

62.  W. Amian, et al.  “Measurements of the Spallation and Fission Product Production for Depleted Uranium and Natural

Lead Targets Bombarded by 1100 MeV Protons.”  ICANS-VI, 551-570 (1982).

63.  G.S. Bauer, et al.  “How Much Thermal Neutron Flux is Gained Using Deuterons Instead of Protons?”  ICANS-VI, 619-

627 (1982).

64.  S. Cierjacks, et al.  “High Energy Particle Spectra from Spallation Targets.”  ICANS-V, 215-240 (1981).

65.  F. Raupp, et al.  “Neutron Production Yields and Spectra from 590 MeV Proton Bombardment of Thick Uranium

Targets.” ICANS-V, 333-342 (1981).

66.  N.F. Peek, et al.  “Gamma-Ray Measurements of Isotopes Produced by 1.1 GeV Protons on Lead and Uranium Targets.”

ICANS-V, 355-375 (1981).

67.  G.S. Bauer, et al.  “Measurement of Time Structure and Thermal Neutron Spectra for Various Target-Moderator-

Reflector Configurations of an Intensity-Modulated Spallation Neutron Source.”  ICANS-V, 475-488 (1981).

68.  Y. Hino, et al.  “Measurement of the High Energy Component of the Neutron Spectrum from a Moderated Source.”

ICANS-V, 489-495 (1981).

69.  V. Drüke, et al.  “Measurements of Neutron Fluxes at Spallation Source Models and Bare Targets.”  ICANS-V, 503-517

(1981).

70.  S.F. Mughabghab, M.S. Zucker.  “The Role of the Nuclear Level Density in Spallation Neutron Studies.”  Int. Conf. on the

Phys. of Nucl. Sci. and Tech., 1315-1319 (1998).

71.  S. Leray, et al.  “Spallation Neutron Studies at SATURNE.” Int. Conf. on the Phys. of Nucl. Sci. and Tech., 1320-1326

(1998).

72.  J.P. Deffain, et al.  “Spallation Neutron Source for Multi-Purpose Irradiations.” Int. Conf. on the Phys. of Nucl. Sci. and

Tech., 1341-1348 (1998).

73.  H.J. Brede, et al.  “Neutron Yields from Thick Be Targets Bombarded with Deuterons or Protons.”  Nucl. Instr. and Meth.,

A274, 332-344 (1989).

74.  M.M. Meier, et al.  “Differential Neutron Production Cross Sections and Neutron Yields from Stopping-Length Targets

for 113-MeV Protons.”  Nucl. Sci. and Eng., 102, 310-321 (1989).

Table 2. Summary of relevant literatures.

| No | Paper | Target | Incident Particle | Measured Parameter | Calculated Parameter/Code |
| --- | --- | --- | --- | --- | --- |
| 1 | Gautan D. Badhwar et al. “Measurements of the Secondary Particle Energy Spectra in the Space Shuttle,” Radiation Measurement, 24, No.2, 129-138 (1995) | Space shuttle shielding | Galactic Cosmic Radiation | Energy spectra of secondary particles (protons, deuterons, tritons, He3, He4) produced by GCR | Energy spectra of secondary particles (protons, deuterons, tritons, He3, He4) produced by GCR HZETRN |
| 2a | J.V. Siebers et al. “Shielding Measurements for 230-MeV Protons,” Nucl. Sci. and Eng. 115, 13-23 (1993) | Al, iron, and lead (thick targets) | Protons 230 MeV | Energy deposition spectra of neutron induced interactions at different depths (absorbed dose and dose-equivalent values) | Attenuation length HETC-DO |
| 2b | J.V. Siebers et al. “Shielding Calculations for 230-MeV Protons Using the LAHET Code System,” Nucl. Sci. Eng., 122, 258 (1996) | Thick Iron target (75.1 mm long, 116 mm diameter) | Protons 230 MeV | Absorbed dose, dose equivalent, attenuation parameters | Absorbed dose, dose equivalent, attenuation parameters LAHET |
| 2c | J.V. Siebers et al. “Measurement of Neutron Dose Equivalent and Penetration in Concrete for 230 MeV Proton Bombardment of Al, Fe, and Pb Targets,” Rad. Prot. Dos., 44, 247-251 (1992) | Al, iron, and lead (thick targets) | Protons 230 MeV | Energy deposition and spectra of secondary neutrons in concrete shield | None |
| 3 | V.I. Belyakov-Bodin et al. “Heat Deposition in Targets Bombarded by Medium-Energy Protons,” Nucl. Instr. and Meth., A 335, 30-36 (1993) | Iron and copper (solid cylindrical target) | Protons 0.8, 1.0, and 1.2 GeV | Heat deposition in iron and copper | Heat deposition in iron and copper (first part of the paper) MARS10 |
| 4 | T. A. Broome et al. “Particle Distribution Around a Copper Beam Stop for 72 MeV Protons,” Health Phys., 44, No. 5, 487-499 (1983) | Copper (thick target) | Protons 72 MeV | Neutron yields at different production angles using activation methods. Neutron spectrum | Neutron spectrum using Monte Carlo HETC |
| 5 | Claudio Birattari and Annalisa Salomone, “Neutron Spectrum Measurements at a 40 MeV Proton Cyclotron,” Health Phys., 49, No. 5, 919-936, (1985) | 20mm-diameter -hemicylindrical thick targets of Al (7mm), Fe (3mm), Cu (3mm), Ta (2mm), and Stainless Steel (3mm). | Protons 40 MeV | Neutron spectra | None |
| 6 | Toshio Ishikawa and Takashi Nakamura, “Thermalization of Accelerator-Produced Neutrons in a Concrete Room,” Health Phys., 60, No. 2, 209-221 (1991) | 32-mm thick copper beam stopper | Protons 30 MeV | Neutron spectra and its thermal component | Neutron spectra MORSE-CG, ANISN |
| 7 | Lutz E. Moritz, “Measurement of Neutron Leakage Spectra at a 500-MeV Proton Accelerator,” Health Phys., 56, No. 3, 287-296 (1989) | Liquid 2H (0.2 m), Be (0.1 m) | Protons 500 MeV | Neutron spectra | None |
| 8a | JAERI-Data/Code 96-029, “Neutron Fluxes in and Around Iron Beam Stop Irradiated by 500 MeV Protons.” | Iron | Protons 500 MeV | Saturated activity | None |
| 8b | Yoshio Arakita, et al. “Study of an Iron Beam Stop for 500 MeV Protons.” Nucl. Instr. and Meth. 164, 255-265 (1979) | 35 cm thick x ~30 cm wide x 30 cm tall iron beam stop | Protons 500 MeV | Distributions of induced radionuclides and dose rate due to residual activities (derived target cross sections) | Thick target cross sections (see T.W. Armstrong, J. Geophys. Res. 74, 1361 (1969)) |
| 8c | Syuichi Ban, et al. “Measurements of Secondary Neutron Fluxes Around Beam Stop for 500 MeV Protons.” Nucl. Instr. and Meth. 184, 409-412 (1981) | 40 cm thick x (probably) ~30 cm wide x 30 cm tall iron beam stop | Protons 500 MeV | Saturated activities, attenuation lengths, and particle flux densities at 0o, 65o, 80o, 90o, 100o | Saturated activities, attenuation lengths, and particle flux densities NMTC |
| 9 | V.I. Belyakov-Bodin et al., “Calorimetric Measurements of the Spatial Component of Heat Deposition in Targets from Beryllium, Carbon, and Aluminum Bombarded by Medium-Energy Protons,” Nucl. Instr. and Meth., A 379, 50-56 (1996) | several (20 cm diameter, 2.5 cm thick) discs of Be, C, and Al | Protons 0.8, 1.0, and 1.2 GeV | Heat deposition | None |
| 10 | V.I. Belyakov-Bodin et al., “Calorimetric Measurements of the Spatial Component of Heat Deposition in Targets from Lead and Bismuth Bombarded by Medium-Energy Protons,” Nucl. Instr. and Meth. A 373, 316-319 (1996) | several (20 cm diameter, 2.5 cm thick ) discs of Pb and Bi | Protons 0.8, 1.0, and 1.2 GeV | Heat deposition | None |
| 11 | D. R. Nethaway, R. A. Van Konynenburg, and M. W. Guinan, “Neutron Spectra from 30-MeV Deuterons on a Thick Beryllium Target,” Symposium on Neutron Cross-Sections From 10 to 40 MeV(1977) | Thick Be target | Deuterons 30 MeV | Neutron Spectra | None |
| 12 | R. G. Graves, J. B. Smathers, N. Hertel. V.A. Otte, P.R. Almond and W. Grant, “Thick Target Neutron Yields from the d-Be Reacction at Ed=15.6, 29.9 and 49.0 MeV,” Symposium on Neutron Cross-Sections From 10 to 40 MeV(1977) | Thick Be target | Deuterons 15.6, 29.9, and 49.0 MeV | Neutron Yield measurements | None |
| 13 | C.E. Nelson et al., “Neutron Spectra from Deuteron and Proton Bombardment of Thick Lithium Targets,” Symposium on Neutron Cross-Sections From 10 to 40 MeV. (1977) | Thick Li target | Deuterons 8,12, and 15 MeV | Neutron spectra and yield | None |
| 14 | S. Cierjacks, et al. “Neutron Yields and Spectra from 590 MeV(p,n) Reactions on Lead Targets,” Symposium on Neutron Cross-Sections From 10 to 50 MeV. (1980) | Thick Pb target (10 cm diameter x 60 cm long) | Protons 590 MeV | Absolute measurement of angular dependent particle (proton and neutrons) emission spectra. | Neutron spectrum HETC |
| 15 | M.A. Lone and B.C. Robertson, “Low Energy Neutron Emission from Be(d,n) and Be(p,n) Reactions,” Symposium on Neutron Cross-Sections From 10 to 50 MeV.(1980) | Thick Be target | Deuterons and protons, ~ 14, 18, and 22 MeV, and 12 MeV deuterons | Neutron yield, neutron spectra | Neutron yield |
| 16 | S. D. Howe, et al., “Neutron Spectrum at 900 From 800 MeV(p,n) Reactions on a Ta Target,” Nuclear Cross Section for Technology (1980) | Thick (1.27 cm radius x 15 cm long) cylindrical Ta target | Protons 800 MeV | Neutron yield and spectra | Neutron yield NMTC |
| 17 | D.L. Johnson , et al. “Thick Target Neutron Yields and Spectra from the Li(d,xn) Reaction at 35 MeV,” Symposium on Neutron Cross-Sections From 10 to 50 MeV. (1980) | Thick Li target (92.5% 7Li) | Deuterons 35 MeV | Neutron yields and spectra | None |
| 18 | J. S. Fraser, et al. “ Neutron Production in Thick Targets of Lead, Thorium and Uranium Bombarded by 480 MeV Protons,” Symposium on Neutron Cross-Sections From 10 to 50 MeV. (1980) | Cylindrical target of Pb, Th, depleted U, UO2 (5 cm radius, 60 cm long; also some Pb of 10 cm radius) | Protons 480 MeV beam impinging on the central element of hexagonal arrays of targets | Neutron capture rates | Neutron capture rates NMTC ANISN MORSE |
| 19 | S.L. Eaton, et al. “Comparison of LAHET Code System Calculations with Experimental Results for Protons of Energies Less than 50 MeV Incident on Copper and Iron,” Nucl. Sci. Eng., 125, 249 (1997) | Copper Iron | Protons Ep 50 MeV | Neutron yield, energy and angular distribution of neutrons, spallation products | Neutron yield, energy and angular distribution of neutrons, spallation products LAHET |
| 20 | Toshio Ishikawa et al., “Neutron Penetration Through Iron and Concrete Shields with the Use of 22.0- and 32.5-MeV Quasi-Monoenergetic Sources,” Nucl. Sci. Eng., 116, 278 (1994) | Natural lithium, 2 mm thick | Protons 25 and 35 MeV | Spectra of neutrons that penetrate shield | Spectra of neutrons that penetrate shield MORSE-CG |
| 21 | Yoshitomo Uwamino, “Measurement of Neutron Activation Cross Sections of Energy up to 40 MeV Using Semi-monoenergetic p-Be Neutrons,” Nucl. Sci. Eng., 111, 391 (1992) | Be, 1 mm and 2 mm thick | Protons 20-40 MeV | Neutrons activation cross sections | Neutrons activation cross sections SAND-II NEUPAC |
| 22a | Yoshitomo Uwamino et al., “Penetration Through Shielding Materials of Secondary Neutrons and Photons Generated by 52-MeV Protons,” Nucl. Sci. Eng., 80, 360 (1982) | Graphite (2.14 cm thick) | Protons 52 MeV | Spectra of neutrons and gammas through graphite, iron, concrete, and water shielding | Spectra measurement MMCR-U ANISN FERDO |
| 22b | Kazuo Shin et al., “Penetration of Secondary Neutrons and Photons from a Graphite Assembly Exposed to 52-MeV Protons,” Nucl. Sci. Eng., 71, 294 (1979) | Graphite (2.145 cm thick) | Protons 52 MeV | Spectra & attenuation of neutrons & gamma-rays | Spectra & attenuation of neutrons & gamma-rays FERDO |
| 22c | Takashi Nakamura, et al. “Spectral Measurements of Neutrons and Photons from Thick Targets of C, Fe, Cu, and Pb by 52 MeV Protons.” Nucl. Instr. and Meth., 151, 493-503 (1978) | Thick targets of C (1, 3.05, 5.1, 8.2, 13.3, and 21.45 mm thick, 1.7g/cm3 density), Fe (6.0 mm and 7.86 g/cm3), Cu (8.2 mm and 8.93 g/cm3), and Pb (10.0 mm and 11.34 cm3) | Protons 52 MeV | Energy and angular distributions of secondary neutrons and photons at 0o, 15o, 30o, 45o, and 75o | Neutron and photon energy spectra FERDO |
| 22d | Kazuo Shin, et al. “Spectral Measurements of Neutrons Produced by 52 MeV Protons with Activation Detectors.” Nucl. Instr. and Meth., 187, 587-594 (1981) | Thick targets of C (21.5 mm thick and 1.7 g/cm3 density), Al (18.0 mm and 2.69 g/cm3), and Pb (10.0 mm and 11.34 cm3) | Protons 52 MeV | Neutron spectra | Activation rates SAND2 |
| 22e | Takashi Nakamura et al., “Neutron Production from Thick Targets of Carbon, Iron, Copper, and Lead by 30- and 52-MeV Protons,” Nucl. Sci. Eng., 83, 444 (1983) | Carbon, Iron, Copper, Lead (20 cm diameter, twice the length of incident proton) | Protons 30 and 52 MeV | Energy spectra | Energy spectra MECC-7 |
| 23 | William W. Wadman III, “Shielding of Neutrons from 80-MeV Alpha-Particle Bombardment of Tantalum,” Nucl. Sci. Eng., 35, 220 (1969) | Thick tantalum target | Alpha particles 80 MeV | Angular distribution yield, spectra & attenuation of fast neutrons | FLUXPOS |
| 24 | A.M. Kalend et al., “Energy and Angular Distributions of Neutrons from 90 MeV Protons and 140 MeV Alpha-Particle Bombardment of Nuclei,” Phys. Rev. C 28, 237 (1983) | Thin targets of Al, Ni, Zr, Bi, and Au | Protons 90 MeV Alpha particles 140 MeV | Energy & angular distribution of neutrons | Energy & angle distribution of neutrons Intranuclear-cascade model |
| 25 | K. Shin et al., “Transmission of Medium Energy Neutrons through Concrete Shields,” Radiat. Prot. Dosim. 37, 175(1991) | Cu, 1 cm thick (stopping range) | Protons 75 MeV | Neutron penetration through concrete shields, source spectra | Neutron penetration through concrete shields MORSE |
| 26a | Shun-ichi Tanaka and Takashi Nakamura, et al., “Shielding Experiments and Analysis at 90 Mv AVF Cyclotron Facility, TIARA.” (Quasi-monoenergetic neutron source) SATIF 1, p.195 (1994) | 7Li | Protons 43 and 67 MeV | Neutron energy spectra, reaction rates of 238U and 232Th | Reaction rates of 238U and 232Th, |
| 26b | Shun-ichi Tanaka and Takashi Nakamura, et al., “Shielding Experiments and Analysis at 90 Mv AVF Cyclotron Facility, TIARA.” (Transmission through concrete and iron shields) SATIF 1, p.195 (1994) | 7Li | Protons 43 and 67 MeV | Neutron energy spectra and reaction rates | Neutron energy spectra and reaction rates of 232Th DOT 3.5, MORSE, and HETC |
| 26c | Shun-ichi Tanaka and Takashi Nakamura, et al., “Shielding Experiments and Analysis at 90 Mv AVF Cyclotron Facility, TIARA.” (Cavity and Labyrinth Experiments) SATIF 1, p.195 (1994) | Cu (stopping length) | Protons 67 MeV | Distributions of fission rates, thermal neutrons, and gamma exposure, angular distributions of source neutrons | Neutron dose distribution (Tesch’s Formula) |
| 27 | Y. Uwamino, et al., “Study on Bulk Shielding of an 800-MeV Proton Accelerator.” SATIF 1, p. 185 (1994) | Many Ta disks of 9 cm diameter (thicknesses: 8 at 8.2 mm, 8 at 10.2mm, 4 at 17.3 mm, and 3 at 26.7 mm) | Protons 800 MeV | Flux density distributions of thermal neutrons | Flux density distributions of thermal neutrons HETC-KFA2, ANISN |
| 28 | R. Michel, et al. “Nuclide Production by Proton-Induced Reactions on Elements (6 ( Z ( 29) in the Energy Range from 800 to 2600 MeV.” Nucl. Instr. and Meth. B, 103, 183-222 (1995) | Stacks of foils (diameter 15.7 mm, thicknesses between 0.0025 and 0.25) of C, Mg, Al, Si, Ti, V, Fe, Co, Ni, Cu, Nb, Rh, Zr, Y, Au, N, Rb, Ca, Ba, Mn, O and Sr or disks (diameter 15.7 mm, thicknesses between 1 and 3 mm) of suitable compositions | Protons 800, 1200, 1600, and 2600 MeV | Production cross sections of radionuclides | Cross sections HETC |
| 29 | Th. Schiekel, et al. “Nuclide Production by Proton-Induced Reactions on Elements (6 ( Z ( 29) in the Energy Range from 200 to 400 MeV.” Nucl. Instr. and Meth. B, 114, 91-119 (1996) | Stacks of foils of C, Mg, Al, Si, Ti, V, Fe, Co, Ni, Cu, Nb, Rh, Zr, Y, Au, N, Rb, Ca, Ba, Mn, O and Sr or disks of suitable compositions (diameter 15.7 mm, thicknesses between 0.036 to 3.25 mm) | Protons 200-400 MeV | Proton flux density, nuclide production cross sections | Nuclide production cross sections HETC, AREL |
| 30 | Kazuo Shin, et al. “Transmission of Intermediate Energy Neutrons and Associated Gamma Rays Through Iron, Lead, Graphite, and Concrete Shields.” Nucl. Sci. Eng. 109, 380-390 (1991) | 1 cm thick Cu (stopping range) | Protons 65 MeV | Neutron energy spectra ((65 MeV) | Neutron energy spectra MORSE (DLC-87) |
| 31 | R. Michel, et al. “On the Depth Dependence of Spallation Reactions in a Spherical Thick Diorite Target Homogeneously Irradiated by 600 MeV Protons.” Nucl. Instr. and Meth. B16, 61-82 (1986) | An arrangement of four sequential targets: two thin targets (one 8 mm diameter and 1.8 cm thick stack of foils of various metals; one 0.3 mm thick quadratic stack of 20 mm x 20 mm foils), followed by one Diorite sphere (radius 5 cm - irradiated isotropically) with an Al “catcher foil” before and after, and a 30 cm diameter cylindrical Fe beam stop. | Protons 600 MeV | Depth dependent production of radionuclides | Production rates HETC/KFA-1 |
| 32 | R.G. Vasil'kov, et al. “Neutron Yields and Thermal Neutron Fluxes in a Lead-Water System Bombarded by High Energy Protons.” Sov. At. Energy, 25, 1307 (1968) | Cylinder of Pb, 55 cm thick with diameter ranging from 10-25 cm | Protons 660 MeV | Neutron yield and thermal neutron fluxes | none |
| 33 | D. West and E. Wood. “Neutron Yield from Protons and Deuterons of Momenta between 0.85 and 1.7 GeV/c Totally Absorbed in Lead.” Canadian Jour. Phys., 49, 2061 (1971) | Pb, 10 cm diameter, 60 cm thick | Protons and Deuterons 0.85 - 1.7 GeV/c | Distribution of thermal neutrons inside a polythene moderator | none |
| 34a | M.A. Lone, et al. “Total Neutron Yields from 100 MeV Protons on Pb and 7Li Targets.” Nucl. Instr. and Meth. 214, 333-339 (1983) | Pb (1.6 cm long x 6.2 cm diameter) and 7Li (99.995 wt %, 17.4 cm long x 5.7 cm diameter) - both stopping range | Protons 100 MeV | Neutron yields, thermal neutron flux distribution in water moderator | Neutron yields, thermal neutron flux distribution NMTC |
| 34b | R.T. Jones, et al. “Measured and Calculated Neutron Yields for 100 MeV Protons on Thick Targets of Pb and Li.” ICANS-VI, 583-603 (1982) | Pb (1.6 cm long x 6.2 cm diameter) and 7Li (99.995 wt %, 17.4 cm long x 5.7 cm diameter) - both stopping range | Protons 100 MeV | Neutron yields | Neutron yields NMTC |
| 35 | D.K. Bewley, et al. “New Neutron Sources for Radiotherapy.” Phys. Med. Biol., 29, No. 4, 341-349 (1984) | Thick, round targets of Be, C, Cu, Ta | Protons 30-60 MeV | Attenuation of total kerma depth-dose | none |
| 36 | H.M. Butler, et al. “Half-value Thicknesses of Ordinary Concrete for Neutrons from Cyclotron Targets.” Health Phys., 24, 438-439 (1973) | Thick targets of C, Al, Cu, Ta | Protons (20-66 MeV), Deuterons (25, 40 MeV), Alpha particles (50, 80 MeV), Carbon ions (100 MeV) | Half-value thicknesses of ordinary concrete for attenuation of fast neutrons | none |
| 37 | N.M.J. Crout, et al. “Neutron Physics Studies Relating to Cancer Therapy on the Clatterbridge Cyclotron. Rad. Prot. Dosi., 23, 381-384 (1988) | Be, 17.8 mm thick, backed by Cu | Protons 62 MeV | Neutron spectra and microdosimetric measurements | Neutron spectra and microdosimetric measurements MORSE-H |
| 38 | W.E. Fisher, et al. “On the Neutronics of SINQ, A Continuous Spallation Neutron Source.” Nucl. Instr. and Meth., A249, 116-122 (1986) | Pb/Bi sphere of 10 cm radius, Pb/Bi or depleted Uranium cylinder of 15 cm diameter and 60 cm length | Protons 592 MeV | Saturated activities, neutron flux | Saturated activities, neutron flux HETC |
| 39 | C. B. Fulmer, et al. “Radiation Leakage Through Thin Cyclotron Shield Walls.” Particle Accelerators, 4, 63-68 (1972) | Thick targets of C, Al, Cu, Ta | Protons (20, 31, 40, 66 MeV), Deuterons (25, 40 MeV), Alpha particles (50, 80 MeV), Carbon ions (100 MeV) | Sum of dose rates of fast and thermal neutrons and gamma rays | none |
| 40 | K. Hayashi and T. Nakamura. “Evaluation of Neutron Skyshine from a Cyclotron.” Nucl. Sci. Eng., 87, 123-135 (1984) | Carbon beam stop | Protons 52 MeV | Source neutron spectrum and dose distribution | Source neutron spectrum and dose distribution MMCR-2, SHYSHINE-II, ANISN |
| 41 | H. Conde, et al. “Time of Flight Measurements of the Energy Spectrum of Neutrons Emitted from a Spallation Source and Moderated in Water.” Nucl. Instr. and Meth. A261, 587-590 (1987) | Stopping length Cu | Protons 72 MeV | Neutron energy spectrum at 90o | Neutron energy spectrum at 90o MORSE |
| 42 | M.A. Lone, et al. “Total Neutron Yield from 100 MeV Protons on Cu, Fe, and Th.” Nucl. Instr. and Meth. A256, 135-142 (1987) | Fe, Cu, and Th targets of 6 cm diameter x ~1.6 cm thick (stopping range) | Protons 100 MeV | Total neutron yields from 100 MeV protons on Fe, Cu, and Th | Total neutron yields from 100-400 MeV protons on Fe, Cu, Sn, Ta, Pb, and U (thick targets) MORSE, NMTC |
| 43 | H.A. O'Brien. “Utilization of an Intense Beam of 800 MeV Protons to Prepare Radionuclides.” Nucl. Instr. and Meth., B40/41, 1126-1131 (1989) | Thin targets (for 590 MeV) of C, Mg, Al, Si, Ti, V, Cr, Fe, Co, Ni, Cu, Zn, Ge, As, Se, Nb, Mo, In, Sn, Ba, La, Ce, Tb, Lu, Hf, Ta, W, Au, Pb, Bi, and U; and thick targets (for 300 and 590 MeV) of Fe, Nb, Bi (~2.5 cm thick); and thin targets (for 800 MeV) of Ni, As, Pb, and Bi | Protons 300, 590, and 800 MeV | Spallation yields | none |
| 44 | Y. Uwamino, et al. “Semi-Monoenergetic Neutron Field for Activation Experiments up to 40 MeV.” Nucl. Instr. and Meth. A271, 546-552 (1988) | Be (1 mm for 20~35 MeV, 2 mm for 40 MeV) | Protons 20, 25, 30, 35, and 40 MeV | Neutron energy spectrum at 0o, neutron flux angular distributions at every 4o | none |
| 45 | Tatsushi Nakamoto, et al. “Spallation Neutron Measurement by the Time-of-Flight Method with a Short Flight Path.” Jour. of Nucl. Sci. and Tech., 32 (9), 827-833 (Sept. 1995) | C (20 g/cm2) and Pb (15 g/cm2) | Protons 0.8 and 1.5 GeV | Neutron production double-differential cross sections at 15o, 30o, 60o, 90o, 120o, 150o | Neutron production double-differential cross sections at 15o, 30o, 60o, 90o, 120o, 150o HETC |
| 46 | Y. Sakamoto, et al. “Source Neutron Spectrum in Streaming Experiment at TIARA.” JAERI Review, 96-012 (6.5), 123-125 | Cu | Protons 67 MeV | Source neutron strength and angular distribution of neutron reaction rates | Neutron spectra for 90o and 120o NMTC and SAND2 |
| 47 | H. Takada, et al. “Measurement and Analysis of Reaction Rate Distribution on Thick Tungsten Target Surface for 0.895 and 1.21 GeV Proton Bombardment.” JAERI Review, 97-011 (10.4), 220-222 | Thick cylindrical tungsten target (20 cm diameter, 60 cm length, 19.25 g/cm3 density, and 99.95% purity) | Protons 0.895 and 1.21 GeV | Reaction rate distributions | Reaction rates NMTC/JAERI-MCNP4A, LAHET, and HERMES |
| 48 | A. Mazal, et al. “Shielding Measurements for a Proton Therapy Beam of 200 MeV: Preliminary Results.” Rad. Prot. Dos., 70 (1-4), 429-436 (1997) | Stopping range Al (90mm diameter and 150 mm length) and water (200 x 200 mm2 and 320 mm length) | Protons 201 MeV | Neutron yields and attenuation at 0o, 22.5o, 45o, 67.5o, and 90o | none |
| 49 | L.R. Veeser, et al. “Neutrons Produced by 740-MeV Protons on Uranium.” Nucl. Instr. and Meth., 117, 509-512 (1974) | A 30 cm long cylinder of thick, depleted uranium composed of twelve 2.5 cm thick x 15 cm diameter disks | Protons 740 MeV | Neutron spectra | Neutron spectra at 50o and 130o NMTC and MCN |
| 50 | B.M. Preedom, et al. “The Response of Plastic Scintillator to Stopping Protons in the Energy Range 70 to 100 MeV.” Nucl. Instr. and Meth., 133, 311-314 (1976) | NE102A plastic scintillators: a cone (1” front diameter, 3” back diameter, 6” length) and a truncated wedge (3.5” x 5” front face, 5” x 5” back face, 4” length) | Protons 70, 80, 90, 100.9 MeV | Differential spectra | none |
| 51 | A. Fasso and M. Höfert. “Distributions of Secondary Particles Around Various Targets Exposed to 50 MeV Protons.” Nucl. Instr. and Meth., 133, 213-218 (1976) | Thick targets of carbon, aluminum, and copper (6 cm long and 2 cm diameter) | Protons 50 MeV | Angular distribution of secondary particles | Cascade and evaporation emission spectra of nucleons (referenced) |
| 52 | M.A. Lone, et al. “Thick Target Neutron Yields and Spectral Distributions from the 7Li (dp, n) and 9Be(dp,n) Reactions.” Nucl. Instr. and Meth., 143, 331-344 (1977) | Thick 7Li and 9Be targets (0.82 g/cm2) | Protons and deuterons 14.8, 18, and 23 MeV | Neutron yields and spectral distributions of neutrons at 0o, 10o, 20o, 30o, and 40o | none |
| 53 | C.A. Goulding and J.G. Rogers. “Measurements and Calculations of Reaction Losses of Medium-Energy Protons in NaI Detectors.” Nucl. Instr. and Meth., 153, 511-515 (1978) | Stopping range NaI detectors | Protons 86, 133, and 146 MeV | Reaction losses of protons | Expected tail-to-peak ratios from 40-240 MeV (method referenced) |
| 54 | M.A. Lone, et al. “Characteristics of Neutrons from Be Targets Bombarded with Protons, Deuterons, and Alpha Particles.” Nucl. Instr. and Meth., 189, 515-523 (1981) | Thin and thick Be targets | Protons (9, 12, 14.8, 18, and 23 MeV), deuterons (3, 5, 6, 7, 9, 12, 14.8, 18, and 23 MeV), and alpha particles (12, 20, 24, and 30 MeV) | Neutron yields and average energies at 0o | None |
| 55 | H.H. Chen, et al. “A Measurement of Stopped (+ Decays in a Copper Beam Dump With Incident Protons of 720 MeV.” Nucl. Instr. and Meth., 160, 393-405 (1979) | Cu beam dump | Protons 720 MeV | Distribution and number of stopped (+ decays | None |
| 56 | B.N. Belyaev, et al. “Isotope Effects in Fragment Yields in Uranium Nuclear Fission Induced by Intermeditate-Energy Protons.” Phys. Atom. Nuc., 57, 1163-1166 (1994) | 0.6 g of uranium carbide in pressed plates of 0.4 mm thickness | Protons 70 and 90 MeV | Relative yields of 86-97Rb and 130-144Cs | None |
| 57 | B.N Belyaev, et al. “Measurement of the Yields of the Nuclear Reaction Products with a Mass Spectrometer On-Line with a Proton Accelerator at Ep = 1 GeV.” Sov. Jour. Nuc. Phys., 24, 617-619 (1977) | 20-30 graphite plates, each 0.1 mm thick and 9 x 18 mm in area, separated by 0.1 mm space with deposits of zirconium oxide 6-7 mg/cm2, all placed in a tantalum box with 0.03 mm thick walls | Protons 1 GeV | Relative yields of Li and Rb isotopes | None |
| 58 | M.M. Meier, et al. “Neutron Yields from Stopping- and Near-Stopping-Length Targets for 256-MeV Protons.” Nucl. Sci. and Eng., 104, 339-363 (1990) | Stopping range targets of natural carbon (8 cm radius x 30 cm length), aluminum (8 x 20), and iron (8 x 8), and 238U (4 x 5) | Protons 256 MeV | Absolute neutron yields at 30, 60, 120, and 150 degrees | Intranuclear cascade evaporation HETC and ISABEL |
| 59 | D.M. Drake, et al. “Experimental Simulation of Martian Neutron Leakage Spectra.” Nucl. Instr. and Meth., A309, 575-580 (1991) | Sand mixed to resemble Martian soil in container 0.7 m diameter x 1.2 m long (3 % H2O) | Protons 800 MeV | Neutron spatial and energy distribution | Neutron production and leakage spectra LAHET, MCNP, ONEDANT |
| 60 | Shin-ichiro Meigo, et al. “Measurements of Spallation Neutrons from a Thick Lead Target Bombarded with 0.5 and 1.5 GeV Protons.” ICANS-XIII, T-2 (1995) | Thick lead target, rectangular parallelepiped 15 x 15 x 20 cm3 (stopping range for 0.5 GeV protons) | Protons 0.5 and 1.5 GeV | Double differential neutron spectra | Double differential neutron spectra NMTC/JAERI, MCNP-4A |
| 61a | T.O. Brun, et al. “LAHET Code System/ CINDER'90 Validation Calculations and Comparison with Experimental Data.” ICANS-XII, T-26 (1993) | see following four references for target specifications | Protons see following four references for energies | see following four references for measured parameters | see following four references for calculated parameters LAHET code system |
| 61b | J.S. Gilmore, et al. “Fertile-to-Fissile and Fission Measurements for Depleted Uranium and Thorium Bombarded by 800-MeV Protons.” Nucl. Sci. and Eng., 99, 41-52 (1988) | Depleted uranium rod clusters (0.251 wt% 235U, 37 rods, 19.04 g/cm3, 19.7 cm total diameter, 3.2393 cm diameter per rod, 30.46 cm length), and thorium rod clusters (19 rods, 11.38 g/cm3, 18.28 cm total diameter, 4.194 cm diameter per rod, 36.31 cm length) | Protons 800 MeV | Axial distributions of fissile and fertile-to-fissile conversions | Axial distributions of fissile and fertile-to-fissile conversions HETC and MCNP |
| 61c | G.J. Russell, et al. “Fertile-to-Fissile and Fission Measurements for Depleted Uranium and Thorium Bombarded by 800-MeV Protons.” ICANS-V, 621-639 (1981) | Depleted uranium rod clusters (0.251 wt% 235U, 37 rods, 19.04 g/cm3, 19.7 cm total diameter, 3.2393 cm diameter per rod, 30.46 cm length) | Protons 800 MeV | Axial distributions of fissile and fertile-to-fissile conversions | Axial distributions of fissile and fertile-to-fissile conversions HETC and MCNP |
| 61d | V.I. Belyakov-Bodin, et al. “Calorimetric Measurements of Medium-Energy Protons Bombarding Beryllium, Carbon, and Aluminum Targets.” Nucl. Instr. and Meth., A314, 508-513 (1992) | Be, C, and Al targets, 0.2 m diameter x 0.6 m thick | Protons 0.8, 1.0, and 1.2 GeV | Energy deposition | Energy deposition MARS-10 |
| 61e | V.I. Belyakov-Bodin, et al. “Calorimetric Measurements and Monte Carlo Analyses of Medium-Energy Protons Bombarding Lead and Bismuth Targets.” Nucl. Instr. and Meth., A295, 140-146 (1990) | Pb and Bi targets, 0.2 m diameter x 0.6 m thick | Protons 0.8, 1.0, and 1.2 GeV | Energy deposition | Energy deposition MARS-10 |
| 62 | W. Amian, et al. “Measurements of the Spallation and Fission Product Production for Depleted Uranium and Natural Lead Targets Bombarded by 1100 MeV Protons.” ICANS-VI, 551-570 (1982) | Thick natural lead and depleted uranium targets of 3 cm diameter x 1 mm thick disks | Protons 1100 MeV | Mass yield distributions for spallation and fission reactions | none |
| 63 | G.S. Bauer, et al. “How Much Thermal Neutron Flux is Gained Using Deuterons Instead of Protons?” ICANS-VI, 619-627 (1982) | Thick targets of lead (10x50x75 cm3) and uranium (10x45x50 cm3) (height x width x depth) followed by a water moderator | Protons 400, 600, 750, and 1100 MeV Deuterons 400, 600, and 750 MeV | Neutron flux | Neutron flux |
| 64 | S. Cierjacks, et al. “High Energy Particle Spectra from Spallation Targets.” ICANS-V, 215-240 (1981) | Cylindrical lead target composed of 12 cylindrical blocks each 5 cm long and 10 cm diameter (60 cm thickness); 50 cm thick lead and uranium blocks with polyethylene and aluminum plates, moderated by 2 m of light water on the sides | Protons 590 and 1100 MeV | High energy particle yields and spectra | None for thick targets |
| 65 | F. Raupp, et al. “Neutron Production Yields and Spectra from 590 MeV Proton Bombardment of Thick Uranium Targets.” ICANS-V, 333-342 (1981) | Thick depleted uranium target 10 cm x 10 cm x 40 cm long | Protons 590 MeV | Neutron production yields and spectra | None |
| 66 | N.F. Peek, et al. “Gamma-Ray Measurements of Isotopes Produced by 1.1 GeV Protons on Lead and Uranium Targets.” ICANS-V, 355-375 (1981) | Targets of 3 cm x 1 mm thick disks of natural Pb and depleted U with Al monitoring foils, placed between 5 cm thick blocks of Pb or U, for total target thickness of 45 cm (stopping range for U but not for Pb) | Protons 1.1 GeV | Isotope production | None |
| 67 | G.S. Bauer, et al. “Measurement of Time Structure and Thermal Neutron Spectra for Various Target-Moderator-Reflector Configurations of an Intensity-Modulated Spallation Neutron Source.” ICANS-V, 475-488 (1981) | Lead and uranium targets with lead and beryllium reflectors | Protons 1.1 GeV | Time structure of chrystal reflections, neutron spectra | None |
| 68 | Y. Hino, et al. “Measurement of the High Energy Component of the Neutron Spectrum from a Moderated Source.” ICANS-V, 489-495 (1981) | Alternating plates of lead (20 mm), polyethylene (2 mm), and aluminum (1 mm) | Protons 1.1 GeV | High energy neutron spectra | None |
| 69 | V. Drüke, et al. “Measurements of Neutron Fluxes at Spallation Source Models and Bare Targets.” ICANS-V, 503-517 (1981) | Cylindrical and slab targets of Pb, Pb-Bi, depleted U, and W-Pb with light water or heavy water and polyethylene neutron moderators | Protons 590 MeV | Neutron flux | None |
| 70 | S.F. Mughabghab, M.S. Zucker. “The Role of the Nuclear Level Density in Spallation Neutron Studies.” Int. Conf. on the Phys. of Nucl. Sci. and Tech., 1315-1319 (1998) | Thick tungsten target, 10.2 cm diameter x 40 cm length | Protons 0.8, 1.0, 1.2, 1.4 GeV | Neutron yields per incident proton | Neutron yields per incident proton LAHET, MCNP |
| 71 | S. Leray, et al. “Spallation Neutron Studies at SATURNE.” Int. Conf. on the Phys. of Nucl. Sci. and Tech., 1320-1326 (1998) | Thin Pb targets and thick targets of Pb and Fe | Protons 0.8, 1.2, and 1.6 GeV for thin targets, 1.2 GeV for thick targets | Double-differential cross-sections and energy spectra | Double-differential cross-sections and energy spectra TIERCE, LAHET, NMTC, and MCNP |
| 72 | J.P. Deffain, et al. “Spallation Neutron Source for Multi-Purpose Irradiations.” Int. Conf. on the Phys. of Nucl. Sci. and Tech., 1341-1348 (1998) | Molten lead-bismuth cylinder, 2500 mm height x 2500 mm diameter, with a 1000 mm high x 1.5 mm thick x 320 mm diameter steel window at the center | Protons 1.2 GeV | Neutron flux | Neutronics SPARTE, HETC coupled with Tripoli4 for transport under 20 MeV, and Darwin as depletion code |
| 73 | H.J. Brede, et al. “Neutron Yields from Thick Be Targets Bombarded with Deuterons or Protons.” Nucl. Instr. and Meth., A274, 332-344 (1989) | Beryllium (98.15% Be) disk of 35 mm diameter and 2 mm thick for deuterons, 5 mm thick for protons | Protons 17.2 - 22 MeV Deuterons 9.4 - 13.6 MeV | Spectral neutron yield per unit beam charge, and angular dependence of spectral neutron yield from 0o to 150o | Neutron response functions for NE213 scintillator NRESP5 and NEFF5 |
| 74 | M.M. Meier, et al. “Differential Neutron Production Cross Sections and Neutron Yields from Stopping-Length Targets for 113-MeV Protons.” Nucl. Sci. and Eng., 102, 310-321 (1989) | Thick targets of Be (5.7 cm thick), C (5.83), Al (4.03), and Fe (1.57), all in natural isotopic abundances and with 3.65 cm radius, and 238U with 4 cm radius and 3 cm thickness; thin targets of Be, C, Al, Fe, 238U, BeO, W, and Pb | Protons 113 MeV | Differential cross sections and neutron yields at 7.5, 30, 60, and 150 degrees | Intranuclear-cascade evaporation HETC |
| 75 | J.W. Wachter, et al. “Neutron and Proton Spectra from Targets Bombarded by 160-MeV Protons.” Phys. Rev., 161, 971-981 (1967) | Thick targets of Al, Bi, C, Co, Cu, and H2O, and thin targets of Al, Be, Bi, C, Co, Cu, D2O, and H2O | Protons 160 MeV | Secondary neutron and proton spectra at 0, 10, 45, 60, and 135 degrees | Secondary neutron and proton spectra at 0, 10, 45, 60, and 135 degrees |

HZETRN  : Deterministic code, numerical solution of the Boltzman equation, straight-ahead approximation.

HETC-DO: High Energy Transport Code [Monte Carlo] - Discrete Ordinate

FLUKA, MARS-10    : Monte Carlo type codes

Tesch’s Formula:  See Particle Accelerators, 12, 169 (1982).

# Footnotes

( Formerly Soviet Journal of Nuclear Physics