IEEE P1451.3 Proposal

| Proposal Title: | Enhancements to Transducer Bus Management Messages |
| --- | --- |
| Proposal Number: | 03-012 |
| Revision Number: | A |
| Date: | 3/14/2003 |
| Name: | Larry Malchodi |
| Company: | Boeing |
| Phone Number: | 206-655-5695 |
| Fax Number: | 206-655-7724 |
| Email Address: | larry.a.malchodi@boeing.com |
| Proposal Status: | Initial Draft Revised Draft X Ready for Vote |
| Impacts: |  |
| Action: | X Approved Approved with changes Rejected Returned for revision |

Summary of Issue:

Alice Law pointed out that there was no description of the Disarm Streaming message under clause 10.3.5 in draft D2.03. This description was contained in proposal P02-025F and mistakenly removed in proposal P02-25G. Therefore, it was not in proposal P02-25H that was approved by the working group. In addition, the current description in that section should be enhanced to point the reader to those services that add constraints or specify behavior of the messages.

Discussion:

Proposed solution:

Draft changes:

### 10.3.5	Transducer bus management messages

The transducer bus management message shall be as listed in Table 1. All of these messages are sent using the short format as described in 10.3.3.

Table 1—Transducer bus management messages

| Message code | Command | Addressed to |
| --- | --- | --- |
|  |  | Broadcast | Specific TBIM | TBC |
| 0 | Reserved | — | — | — |
| 1 | Initiate discovery | Yes | No | No |
| 2 | Discovery reply | No | No | Yes |
| 3 | Assign alias | Yes | No | No |
| 4 | Assign alias response | No | No | Yes |
| 5 | Assign time slot | No | Yes | No |
| 6 | Assign time slot reply | No | No | Yes |
| 7 | Define epoch | Yes | No | No |
| 8 | Disarm streaming | Yes | No | No |
| 9 | Beginning-of-epoch message | Yes | No | No |
| 10 | Start asynchronous interval | Yes | No | No |
| 11 | Reflect | No | Yes | No |
| 12 | Reflect reply | No | No | Yes |
| 13 | Enable transmitter | Yes | Yes | No |
| 14 | Disable transmitter | Yes | Yes | No |
| 15 – 127 | Reserved | — | — | — |
| 128 - 255 | Open for manufacturers | — | — | — |

#### 10.3.5.1	Initiate discovery message

A request for the InitiateDiscovery service (see 9.4) causes the Data Link layer to issue an Initiate discovery message to all TBIMs on the bus. The data field for this message shall be as shown in Table 2. Only the TBC shall generate this message.

Table 2—Initiate discovery message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |

#### 10.3.5.2	Discovery reply

The receipt of the request alias service request causes the service in the TBIM Data Link layer (see 9.5) to wait for an initiate discovery message from the TBC. Upon receipt of this message it shall return a Discovery reply message containing the fields shown in Table 3 to the TBC using the asynchronous communications mode. This reply shall only be generated if the TBIM does not currently possess a TBIM Alias assignment.

This message is required in all TBIMs.

Table 3—Discovery reply message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | UUID | This field shall contain the eighty-bit UUID for the TBIM. |

#### 10.3.5.3	Assign alias message

A request for the AssignAlias service (see 9.4.2) causes an assign alias message to be broadcast to all devices on the transducer bus. The data field for this message is shown in Table 4. This message shall be transmitted using the asynchronous transmission mode. The TBC is the only device on the bus that shall generate this message. All TBIMs shall be able to accept and respond to it. All TBIMS shall monitor for reassignment of their alias (see 9.5.2).

Table 4—Assign alias message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | UUID | This field shall contain the eighty-bit UUID for the TBIM. |
| 3 | U8C | The eight-bit alias for the TBIM. |

#### 10.3.5.4	Assign alias response

Upon receipt of an assign alias message from the TBC, the TBIM shall transmit an assign alias response message containing the information listed in Table 5 only when they receive an assign alias message that contains their UUID.

Table 5—Assign alias response message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | U8E | Assigned alias |
| 3 | U8E | Asynchronous-only flag (same as in PHY TEDS) |
| 4 | U8C | Highest supported payload encoding (same as in PHY TEDS) |
| 5 | F32 | Start delay (same as in PHY TEDS) |
| 6 | F32 | Reflect delay (same as in PHY TEDS) |
| 7 | F32 | Reflect delay uncertainty (same as in PHY TEDS) |

#### 10.3.5.5	Assign time slot message

Upon receipt of a SetupStreamingCommunicationChannel service request the TBC shall compute the number of packets required and the beginning time slot for each packet from the information supplied in the request and internally maintained information about the layout of the isochronous interval. It shall then broadcast an assign time slot message containing the information in Table 6 to the TBIM. Only the TBC shall generate this message.

Table 6—Assign time slot message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | U16E | The sixteen-bit TransducerChannel Address |
| 3 | U16C | The beginning time slot for a packet. |
| 4 | U8C | Number of consecutive slots required |

#### 10.3.5.6	Assign time slot reply message

Upon receipt of an assign time slot message the TBIM shall return an assign time slot reply message containing the information in Table 7 to the TBIM. TBCs shall not generate this message.

Table 7—Assign time slot reply message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | U8E | The status as listed in Table 8. |

Table 8—Assign time slot status bits

| Bit | Function |
| --- | --- |
| 0 | This bit shall be set to 1 to indicate that the message was received and processed successfully. |
| 1 | This bit shall be set to 1 if the TBIM does not support streaming data. |
| 2 | Reserved |
| 3 | Reserved |
| 4 | Open to manufacturers |
| 5 | Open to manufacturers |
| 6 | Open to manufacturers |
| 7 | Open to manufacturers |

#### 10.3.5.7	Define epoch message

Upon the receipt of the Initiate Streaming Communications service request the TBC shall issue the define epoch message as defined in Table 9 to all TBIMs on the bus. This message has two arguments. These two arguments define the length of the isochronous and the asynchronous intervals. The maximum length of the isochronous interval is 1200 slot times. The minimum length of the asynchronous interval is 50 slot times. The epoch length is the sum of the isochronous interval and the asynchronous interval and shall not exceed 1250 slot times. If the isochronous interval length is zero then the bus is being operated in the asynchronous mode only and the value in the asynchronous interval argument is not used. The default condition after reset or power up is with the length of the isochronous interval equal to zero.

TBIMs shall not generate this message.

Table 9—Arguments for the define epoch message

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | U16C | Isochronous interval - This field contains the number of slot times that are required in the isochronous interval (See Error! Reference source not found.). The isochronous interval length requires a maximum of eleven bits and they shall be in the eleven least significant bits of the U16C. The five most significant bits shall be zero. |
| 3 | U16C | Asynchronous interval - This field contains the number of slot times that are required in the asynchronous interval (See Error! Reference source not found.). The asynchronous interval length requires a maximum of eleven bits and they shall be in the eleven least significant bits of the U16C. The five most significant bits shall be zero. |

#### 10.3.5.8	Disarm streaming

A request for this service (see 9.2.4) causes the Data Link layer in the TBC to issue a disarm streaming message to all TBIMs on the bus. The data field for this message shall contain the information shown in Table 34. Only the TBC shall generate this message.

Table 34—Terminate streaming message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown inTable 1. |

#### 10.3.5.9	Beginning-of-epoch message

This message is always broadcast. It marks the beginning of an isochronous transmission interval. Isochronous transmission intervals are 0.25 seconds or less in length so if this message is not received within a one second period TBIMs may assume that the bus is being operated asynchronously without a defined epoch. The data field for this message shall be as described in Table 10. This message always occupies slot zero in the isochronous interval.

Only the TBC shall issue this message.

Table 10—Beginning-of-epoch message data field

| Data Field | Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | U16C | The epoch number to be used during the next epoch. The epoch is incremented for each new epoch. It rolls over to zero for the next epoch after it reaches 65,535. This epoch number shall be written into the sequence number register defined in Error! Reference source not found. at the beginning of the next epoch. |
| 3 | U8C | Number of solicited retransmissions in this message = N |
|  |  | Fields 4 and 5 will be repeated N times. |
| 4 | U16C | The slot number in which the invalid packet began being transmitted. |
| 5 | U8E | Reply priority |

The data link layer may need to communicate the receipt of this message to the TBIM application. This may be done in either of two ways. By a hardware signal or by a trigger message addressed to the TBIM using the trigger protocol. If a message is sent using the trigger protocol, it shall have the form described in Table 11.

Table 11—Trigger message resulting from a beginning-of-epoch message

| 1-Octet | 1-Octet |
| --- | --- |
| 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| Protocol Identifier | 0 | 0 | Version | — | Priority |
| TBIM Alias | zero |
| TBIM Alias | zero |

Solicited retransmissions may be sent in this message for packets received with errors in the previous epoch. Fields 4 through 6 are used for this function.

To avoid collisions each packet to be retransmitted shall be assigned a different priority starting at priority seven and working down.

Note: This technique allows for the possibility of up to seven different packets receiving a solicited retransmission message during any one epoch. If less priority levels are used for solicited retransmissions then fewer packets can receive a solicited retransmission request in one epoch. The length of the asynchronous interval will also limit the number of packets that can be retransmitted.

Note: The solicited retransmissions are from data that was sent in the previous epoch. If these packets are not retransmitted within the asynchronous interval of this epoch they are lost. This means that these packets should have the highest priority with lower priorities used by non-time critical traffic.

The TBIMs do not reply to the data link layer in the TBC to any of this communication. A packet may be retransmitted as a result of a solicited retransmission but that communication is directed up through the protocol stack.

#### 10.3.5.10	Start async message

This message is always broadcast to all TBIMs on a bus. It marks the end of an isochronous transmission interval and the beginning of the asynchronous interval. The data field for this message is shown in Table 12. This message always occupies the last slot in the isochronous interval. Only the TBC shall generate this message.

Table 12—Start async message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | S32 | This field gives time error between when the Beginning-of-epoch message should have been transmitted and when it was actually transmitted. It is a signed 32-bit two’s complement integer giving the time error in nanoseconds. If the TBC does not provide this information the contents of this field shall be zero. |

#### 10.3.5.11	Reflect message

The TBC issues a message as shown in Table 13 when it receives a request for the delay measurement service (see 9.9). This message shall be transmitted using the asynchronous transmission mode. Only the TBC shall generate this message.

Table 13—Reflect message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |
| 2 | U8C | The eight-bit alias for the TBIM. |

#### 10.3.5.12	Reflect reply

The TBIM changes the message code in the first field of the reflect request message as shown in Table 13, the source address and the destination address and returns the message to the TBC with a consistent delay between receipt and retransmission. This message shall be transmitted using the asynchronous transmission mode. Only TBIMs shall generate this message.

#### 10.3.5.13	Enable transmitter

A request for the enable transmitter service (see 9.6.2) causes an enable transmitter message to be broadcast to all devices on the transducer bus or to a specific TBIM. The data field for this message is shown in Table 14. This message shall be transmitted using the asynchronous transmission mode. Only the TBC shall generate this message.

Table 14—Enable Transmitter message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |

#### 10.3.5.14	Disable Transmitter message

A request for this service (see 9.6.1) causes a disable transmitter message to be broadcast to all devices on the transducer bus or to a specific TBIM. The data field for this message is shown in Table 15. This message shall be transmitted using the asynchronous transmission mode. Only the TBC shall generate this message.

Table 15—Disable Transmitter message data field

| Data Field | Data Type | Function |
| --- | --- | --- |
| 1 | U8E | This field shall contain the message code shown in Table 1. |

# Comments

In order to properly fill out this form, you MUST do the following:

- Click on the CUSTOM tab, under FILE,PROPERTIES.

- Click on the PropTitle property, enter your proposal name, click on MODIFY.

- Click on the PropDate property, enter the date, click on MODIFY.

- Click on the PropRev property, enter your revision symbol (space is OK, empty is not), click on MODIFY.

- In NORMAL view, click on SELECT ALL under the EDIT menu.

- Press the F9 key to update fields.