Hydraulic Design Series No. 6

river engineering for

highway encroachments

Highways in the River Environment

Publication No. FHWA-NHI-01-004

December 2001

Document Availability:

To download an electronic copy:  http://www.fhwa.dot.gov/engineering/hydraulics/library_listing.cfm

Related NHI Training Course:

FHWA-NHI-135010, River Engineering for Highway Encroachments

http://www.nhi.fhwa.dot.gov/category.asp?category_id=7

Related Software:

Surface-water Modeling System (SMS)

http://www.ems-i.com/

FHWA Technical Contact:

Dr. Larry Arneson 					Phone:  (720) 963-3200

Sr. Hydraulics Engineer, FHWA Resource Center	Email:  larry.arneson@fhwa.dot.gov

# Text boxes

Abstract:

In the United States, the average annual damage related to hydraulic problems at highway facilities on the Federal-aid system is $40 million.  Damages by streams can be reduced significantly by considering channel stability including:  (1) lateral bank erosion; (2) degradation and aggradation of the streambed that continues over a period of years, and (3) natural short-term fluctuations of streambed elevation that are usually associated with the passage of floods.

The Federal Highway Administration document “Highways in the River Environment – Hydraulic and Environmental Design Considerations” was first published in 1975, and is now issued as River Engineering for Highway Encroachments:  Highways in the River Environment, Hydraulic Design Series No. 6 (HDS-6).  In HDS-6, hydraulic problems at stream crossings are described in detail, and the hydraulic principles of rigid and moveable boundary channels are discussed.  This document has proven to be a singularly authoritative document for the design of highway associated hydraulic structures in moveable boundary waterways.  Topics discussed in this document are:  sediment transport, natural and human induced causes of waterway response, stream stabilization, hydraulic modeling and computer applications, countermeasures, and case histories of typical human and natural impacts on waterways.