MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A17820 | In-Flight Anomaly Number -- | Contractor Report Number E-170 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 LIQUID LEVEL SENSOR FAILED DIELECTRIC WITHSTANDING VOLTAGE ATP |
| EICN# -- | ELEMENT ET | Contractor LMM | FSCM# -- | FCRIT 1R |
| HCRIT 1R | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LH2 LIQUID LEVEL SEN | PART# 74L4-2 | SER/LOT# 0003354 | MANUFACTURER GOODRICH |
| Test/Operation AI - ATI | Prevailing Condtion FT - FUNCTL TEST | F / U F | Fail Mode EL - SHORT | Cause DH - DES-HDW |
| System ELECTRICAL | Defect EM - ELADJ | Material E - EL C/W | Work Contact M. PENO | Fail Date 11/19/2002 |
| Received at MSFC 11/21/2002 | Date Isolated 11/21/2002 | FMEA Reference 3.6.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GOODRICH | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 01/31/2003 | Contractor Req Defer Until Date 01/31/2003 | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 01/30/2003 | CN RSLV SBMT -- | Defer Date -- | Add Date 11/21/2002 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design M. BUTLER | Chief Engineer T. GREENWOOD | S & MA K. LAYNE | Project -- | Project MGR J. SMELSER |
| Approval |
| Design M. BUTLER | Chief Engineer T. GREENWOOD | S & MA K. LAYNE | Project -- | Project MGR J. SMELSER |
| PAC Assignee T. WHITE | PAC Review Complete TLW | MSFC Closure Date 01/30/2003 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type NC - PROB RPT | Related Document ID NCD N052304 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description LIQUID LEVEL SENSOR S/N 0003354 FAILED DIELECTRIC WITHSTANDING VOLTAGE TEST AT THE SUPPLIER, GOODRICH. SUPPLIER ACCEPTANCE TEST (ATP) 945, REVISION AB, PARAGRAPH 6.2 REQUIRES 500 VOLTS ALTERNATING CURRENT BE APPLIED TO THE PART FOR ONE MINUTE. THERE SHALL BE NO EVIDENCE OF ARC- OVER OR LEAKAGE CURRENT GREATER THAN 1.8 MILLIAMPS. THE SENSOR FAILED WITH A LEAKAGE CURRENT OF 2.9 MILLIAMPS. |
| Contractor Investigation/Resolution 11/21/2002 - CONTRACTOR SUBMITTED OPENER REQUEST AS FOLLOWS: PROBLEM DESCRIPTION: ------------------- LIQUID LEVEL SENSOR S/N 0003354 FAILED DIELECTRIC WITHSTANDING VOLTAGE TEST AT THE SUPPLIER, GOODRICH. SUPPLIER ACCEPTANCE TEST (ATP) 945, REVISION AB, PARAGRAPH 6.2 REQUIRES 500 VOLTS ALTERNATING CURRENT BE APPLIED TO THE PART FOR ONE MINUTE. THERE SHALL BE NO EVIDENCE OF ARC- OVER OR LEAKAGE CURRENT GREATER THAN 1.8 MILLIAMPS. THE SENSOR FAILED WITH A LEAKAGE CURRENT OF 2.9 MILLIAMPS. GENERAL: -------- TWELVE 74L4-2 SENSORS ARE USED IN THE LH2 TANK TO MONITOR DISCRETE LEVELS OF LH2. WHEN THE SENSOR IS IMMERSED IN THE LIQUID PROPELLANT (WET) THE SIGNAL VOLTAGE FROM THE ELECTRONICS SHALL BE ZERO. WHEN THE SENSOR IS FREE OF THE LIQUID (DRY) THE SIGNAL VOLTAGE FROM THE ELECTRONICS SHALL BE 28 VOLTS DC. THE LEVEL SENSOR UTILIZES THE DECREASE IN THE ELECTRICAL RESISTANCE OF A METAL WHEN COOLED TO DETECT THE PRESENCE OF A CRYOGENIC FLUID. THE SENSOR USES A GOLD FLASHED PLATINUM WIRE, .0005 INCH IN DIAMETER, AS THE SENSING ELEMENT. THE LEVEL SENSOR SIGNAL CONDITIONER, WHICH IS MOUNTED IN THE ORBITER, PROVIDES A CONSTANT CURRENT TO THE SENSING ELEMENT, WHICH CAUSES IT TO RISE IN TEMPERATURE. THE TEMPERATURE AND RESISTANCE OF THE ELEMENT DECREASE RADICALLY WHEN IMMERSED IN A CRYOGENIC LIQUID. THE SIGNAL CONDITIONER DETECTS THE DECREASE IN RESISTANCE AND CONVERTS IT TO A "WET" OUTPUT SIGNAL. THE SIGNAL CONDITIONER IS ALSO DESIGNED TO GIVE A "WET" SIGNAL IN THE EVENT OF AN OPEN CIRCUIT IN THE LEVEL SENSOR. BASED ON THE VOLTAGE ACROSS THE SENSING ELEMENTS, THE ELECTRONIC CIRCUITS GENERATE DISCRETE ELECTRICAL SIGNALS REQUIRED FOR CONTROL AND MONITORING OF PROPELLANT LOADING AND DRAINING, FOR TELEMETRY, AND FOR SHUTDOWN OF THE MAIN ENGINES UPON DEPLETION OF LH2. THE SENSOR HAS AN ALUMINUM CASE, WHICH IS PRODUCED BY INVESTMENT CASTING. VERY FEW OF THE INTERNAL SURFACES, AND NONE OF THE EXTERNAL SURFACES, ARE FINISH MACHINED FOR DIMENSIONAL CONTROL. THE INTERNAL SURFACES OF THE CASE AND THE COVER ARE PAINTED WITH A SPRAYED- ON, BAKED, TEFLON(R) PAINT. THE PAINT PREVENTS WETTING OF THE CASE, I.E. RETENTION OF CRYOGENIC FLUIDS, AND ALSO PROVIDES SOME ELECTRICAL INSULATION BETWEEN THE CASE AND THE SENSOR ELEMENT. THE ELEMENT IS SUPPORTED BY A CERAMIC SUBSTRATE. THE SUBSTRATE HAS FIRED-ON GOLD CIRCUIT PATHS WHICH PROVIDE A MEANS TO TERMINATE THE ELEMENT WIRE BY WELDING. THE SENSOR OUTPUT WIRES ARE ATTACHED TO THE SUBSTRATE BY STEEL TERMINALS HELD IN PLACE WITH RIVETS AND SPRING WASHERS. BACKGROUND ---------- THE 74L4-2 LH2 LEVEL SENSOR WAS UNDERGOING ACCEPTANCE TESTING AT THE SUPPLIER, GOODRICH CORPORATION, SIMMONDS PRECISION DIVISION, IN VERGENNES, VERMONT. THE TESTING IS CONTROLLED BY ACCEPTANCE TEST PLAN 946 REVISION AB, PARAGRAPH 6.2. THE DIELECTRIC WITHSTAND VOLTAGE TEST REQUIRES THE APPLICATION OF 60HZ, 500 VOLTS RMS FOR 60 SECONDS. THERE SHALL BE NO ARC-OVER OR LEAKAGE GREATER THAN 1.8 MILLIAMPS. MULTIPLE SENSORS ARE SUBSEQUENTLY TESTED IN PARALLEL. INITIAL TESTING ESTABLISHED A MEASURED LEAKAGE CURRENT OF 2.9 MILLIAMPS ON THE FAILED SENSOR. THE SENSOR WAS ELECTRICALLY ISOLATED FROM THE OTHER SENSORS (BUT NOT PHYSICALLY MOVED) AND RETESTED. THE LEAKAGE CURRENT OF THE SENSOR UPON RETEST WAS WAVERING BETWEEN .024-.026 MILLIAMPS. THE SENSOR LEAD WIRE INSULATION WAS INSPECTED AND NO DAMAGE OR ANOMALIES WERE NOTED. LEAKAGE CURRENT WAS AGAIN MEASURED UNDER THE APPLIED LOAD AND THE WAVERING VALUE OF .024-.026 MILLIAMPS WAS REPEATED. THIS NONCONFORMANCE HAS BEEN DOCUMENTED ON NCD NUMBER N052304. TASK I FAILURE/PROBLEM INVESTIGATION ----------------------------- A. THE FAILED SENSOR, S/N 0003354, WAS DOCUMENTED ON NCD N052304. THE NCD DISPOSITION DIRECTS A FAILURE ANALYSIS TO BE PERFORMED AT THE SUPPLIER. RESPONSIBILITY: J. HILL, DEPT. 3977/S. PARIKH, DEPT. 3760 M. PENO, DEPT. 3741 / D. WESTPHAL, DEPT. 3740 ECD: 12/20/02 B. DOCUMENT ANY FAILURES OF THIS TYPE THAT HAVE OCCURRED PRE- ATP. IF FAILURES OCCURRED PRE-ATP, HOW WERE THEY DISPOSITIONED AND WHAT WERE THE S/N(S) OF THE SENSORS. RESPONSIBILITY: J. HILL, DEPT. 3977 / S. PARIKH, DEPT. 3760 ECD: 11/25/02 COMPLETE: 11/20/02 CLOSURE STATEMENT: ------------------ LO2 SENSOR 74L4-1, S/N 0002832 FAILED PRE-ATP 946 DIELECTRIC WITHSTAND VOLTAGE TEST ON 10-24-02. PRIOR TO REMOVAL OF THE COVER, THE CLEAR TFE TEFLON(R)INSULATING SLEEVING APPEARED TO BE PINCHED BETWEEN THE HOUSING AND THE COVER. AFTER REMOVAL OF THE COVER IT WAS CONFIRMED THAT THE SLEEVING WAS PINCHED, LEAVING THE WIRE IN CLOSE PROXIMITY WITH THE EDGE OF THE HOUSING. THE COVER WAS REMOVED FROM THE HOUSING TO PERFORM THE FAILURE INVESTIGATION. THE LEAD WIRE/TERMINAL WAS STRAIGHTENED TO ALLOW THE WIRE TO EXIT THROUGH THE CHANNEL STRAIGHT AND NOT AT AN ANGLE. THE PINCHED INSULATING SLEEVING WAS THEN REPLACED ON THE EFFECTED LEAD WIRE. THE COVER WAS REINSTALLED, AND ATTACHMENT SCREWS WERE TORQUED TO 35-38 INCH-OUNCES. CAUTION WAS EXERCISED TO ENSURE THAT THE INSULATING SLEEVING WAS NOT PINCHED UNDER THE COVER OR KINKED. THE PART WAS TESTED PER ATP- 946 DIELECTRIC STRENGTH PER PARAGRAPH 6.2 AND PASSED WITH A LEAKAGE CURRENT OF .028 MILLIAMPS. CORRECTIVE ACTIONS WERE IMPLEMENTED TO ADD THE FOLLOWING OPERATION SPECIFIC INSTRUCTIONS: 1. WHEN INSTALLING SENSOR ELEMENT INTO HOUSING CHECK THAT THE SENSOR WIRES ARE POSITIONED TOWARDS THE CENTER OF THE HOUSING CHANNEL. 2. PRIOR TO ASSEMBLING COVER ON HOUSING VERIFY THAT WIRES ARE POSITIONED TOWARDS THE CENTER OF THE HOUSING CHANNEL. (REF. E-MAIL FROM J. HILL DATED 11/20/02) CAUSE: PENDING INVESTIGATION RESULTS TASK II CORRECTIVE ACTION ----------------- PENDING COMPLETION OF INVESTIGATION. TASK III CLEARANCE OF EFFECTIVITIES -------------------------- FLEET CLEARANCE FOR ALL EFFECTIVITIES IS GRANTED BASED ON THE REQUIREMENT THAT ALL 74L4-2 CRYOGENIC LIQUID LEVEL SENSORS PASS THE 500 VOLTS ATP DIELECTRIC WITHSTAND VOLTAGE TEST. IN ADDITION TO THE ATP REQUIREMENT, ALL 74L4-2 CRYOGENIC LIQUID LEVEL SENSORS ARE TESTED FOR INSULATION RESISTANCE WITH 50 VOLTS AT MAF. FURTHERMORE, THOSE SENSORS USED IN LH2 DEPLETION SENSOR (CRITICALITY 1R) APPLICATIONS ARE TESTED WITH 50 VOLTS FOR INSULATION RESISTANCE AT KSC. (REFERENCE E-MAIL FROM A. GRECONIA DATED 11/20/02) TASK CLOSED ----------- TASK IV CAPS CLOSURE SUMMARY -------------------- PENDING COMPLETION OF INVESTIGATION. 1/13/2003 - CONTRACTOR SUBMITTED FULL CLOSURE REQUEST AS FOLLOWS: GENERAL: -------- TWELVE 74L4-2 SENSORS ARE USED IN THE LH2 TANK TO MONITOR DISCRETE LEVELS OF LH2. WHEN THE SENSOR IS IMMERSED IN THE LIQUID PROPELLANT (WET) THE SIGNAL VOLTAGE FROM THE ELECTRONICS SHALL BE ZERO. WHEN THE SENSOR IS FREE OF THE LIQUID (DRY) THE SIGNAL VOLTAGE FROM THE ELECTRONICS SHALL BE 28 VOLTS DC. THE LEVEL SENSOR UTILIZES THE DECREASE IN THE ELECTRICAL RESISTANCE OF A METAL WHEN COOLED TO DETECT THE PRESENCE OF A CRYOGENIC FLUID. THE SENSOR USES A GOLD FLASHED PLATINUM WIRE, .0005 INCH IN DIAMETER, AS THE SENSING ELEMENT. THE LEVEL SENSOR SIGNAL CONDITIONER, WHICH IS MOUNTED IN THE ORBITER, PROVIDES A CONSTANT CURRENT TO THE SENSING ELEMENT, WHICH CAUSES IT TO RISE IN TEMPERATURE. THE TEMPERATURE AND RESISTANCE OF THE ELEMENT DECREASE RADICALLY WHEN IMMERSED IN A CRYOGENIC LIQUID. THE SIGNAL CONDITIONER DETECTS THE DECREASE IN RESISTANCE AND CONVERTS IT TO A "WET" OUTPUT SIGNAL. THE SIGNAL CONDITIONER IS ALSO DESIGNED TO GIVE A "WET" SIGNAL IN THE EVENT OF AN OPEN CIRCUIT IN THE LEVEL SENSOR. BASED ON THE VOLTAGE ACROSS THE SENSING ELEMENTS, THE ELECTRONIC CIRCUITS GENERATE DISCRETE ELECTRICAL SIGNALS REQUIRED FOR CONTROL AND MONITORING OF PROPELLANT LOADING AND DRAINING, FOR TELEMETRY, AND FOR SHUTDOWN OF THE MAIN ENGINES UPON DEPLETION OF LH2. THE SENSOR HAS AN ALUMINUM CASE, WHICH IS PRODUCED BY INVESTMENT CASTING. VERY FEW OF THE INTERNAL SURFACES, AND NONE OF THE EXTERNAL SURFACES, ARE FINISH MACHINED FOR DIMENSIONAL CONTROL. THE INTERNAL SURFACES OF THE CASE AND THE COVER ARE PAINTED WITH A SPRAYED-ON, BAKED, TEFLON* PAINT. THE PAINT PREVENTS WETTING OF THE CASE, I.E. RETENTION OF CRYOGENIC FLUIDS, AND ALSO PROVIDES SOME ELECTRICAL INSULATION BETWEEN THE CASE AND THE SENSOR ELEMENT. THE ELEMENT IS SUPPORTED BY A CERAMIC SUBSTRATE. THE SUBSTRATE HAS FIRED-ON GOLD CIRCUIT PATHS WHICH PROVIDE A MEANS TO TERMINATE THE ELEMENT WIRE BY WELDING. THE SENSOR OUTPUT WIRES ARE ATTACHED TO THE SUBSTRATE BY STEEL TERMINALS HELD IN PLACE WITH RIVETS AND SPRING WASHERS. * BACKGROUND ---------- THE 74L4-2 LH2 LEVEL SENSOR WAS UNDERGOING ACCEPTANCE TESTING AT THE SUPPLIER, GOODRICH CORPORATION, SIMMONDS PRECISION DIVISION, IN VERGENNES, VERMONT. THE TESTING IS CONTROLLED BY ACCEPTANCE TEST PLAN 946 REVISION AB, PARAGRAPH 6.2. THE DIELECTRIC WITHSTAND VOLTAGE TEST REQUIRES THE APPLICATION OF 60HZ, 500 VOLTS RMS FOR 60 SECONDS. THERE SHALL BE NO ARC-OVER OR LEAKAGE GREATER THAN 1.8 MILLIAMPS. INITIAL TESTING ESTABLISHED A MEASURED REJECTABLE LEAKAGE CURRENT OF 2.9 MILLIAMPS ON THE FAILED SENSOR. THE SENSOR WAS RETESTED AND THE LEAKAGE CURRENT UPON RETEST WAS WAVERING BETWEEN .024-.026 MILLIAMPS. THE SENSOR LEAD WIRE INSULATION WAS INSPECTED AND NO DAMAGE OR OTHER ANOMALIES WERE NOTED. LEAKAGE CURRENT WAS ONCE AGAIN MEASURED UNDER THE APPLIED LOAD AND THE WAVERING VALUE OF .024-.026 MILLIAMPS WAS REPEATED. THIS NONCONFORMANCE WAS DOCUMENTED ON NCD NUMBER N052304. TASK I FAILURE/PROBLEM INVESTIGATION ----------------------------- A. THE FAILED SENSOR, S/N 0003354, WAS DOCUMENTED ON NCD N052304. THE NCD DISPOSITION DIRECTED A FAILURE ANALYSIS TO BE PERFORMED AT THE SUPPLIER. RESPONSIBILITY: J. HILL, DEPT. 3977 / S. PARIKH, DEPT. 3760 M. PENO, DEPT. 3741/D. WESTPHAL, DEPT. 3740 ECD: 12/20/02 * CLOSED: 11/25/02 * CLOSURE STATEMENT: ------------------ A FAILURE ANALYSIS WAS PERFORMED AT GOODRICH CORPORATION TO DISCERN THE CAUSE OF THE FAILURE. PRIOR TO DISASSEMBLY, THE SENSOR LEADWIRE ALIGNMENT WAS INSPECTED AND FOUND TO BE ACCEPTABLE AT THE LOCATION WHERE THE WIRES EXIT THE HOUSING CHANNEL. THE COVER WAS REMOVED AND INSPECTED FOR PARTICULATE CONTAMINATION UNDER MAGNIFICATION. THE ELEMENT ASSEMBLY WAS ALSO INSPECTED FOR CONTAMINATION PRIOR TO REMOVAL FROM THE HOUSING. NO CONTAMINATION WAS FOUND THAT COULD HAVE CAUSED THE FAILURE. IT WAS ALSO NOTED THAT THE SENSOR LEADWIRES WERE PROPERLY CENTERED IN THE HOUSING CHANNEL. THE POSITION OF THE SENSOR SUBSTRATE ASSEMBLY RELATIVE TO THE HOUSING WAS NORMAL, AND THE GOLD PINS WERE NOT ABNORMALLY CLOSE TO THE INTERIOR OF THE HOUSING. THE ELEMENT ASSEMBLY WAS THEN REMOVED FROM THE HOUSING AND INSPECTED UNDER MAGNIFICATION FOR PROPER INSTALLATION OF THE ELEMENT COMPONENTS AND FOR ANY DAMAGE OR CONTAMINATION. ARC BURNS WERE DISCOVERED ON THE SURFACES OF THE GOLD- FIRED PAD OF THE SENSING ELEMENT AND ON THE INTERNAL SURFACE OF THE TEFLONR COATED CASE. THERE WAS NO EVIDENCE OF ANY CONTAMINATION IN THE AREA OF THE BURN MARKS. THE ARC BURNS ARE EVIDENCE OF, AND REVEAL THE ORIGIN OF THE CURRENT LEAKAGE FAILURE. B. DOCUMENT ANY FAILURES OF THIS TYPE THAT HAVE OCCURRED PRE- ATP. IF FAILURES OCCURRED PRE-ATP, HOW WERE THEY DISPOSITIONED AND WHAT WERE THE S/N(S) OF THE SENSORS. RESPONSIBILITY: J. HILL, DEPT. 3977 / S. PARIKH, DEPT. 3760 ECD: 11/25/02 COMPLETE: 11/20/02 * CLOSURE STATEMENT: ------------------ IN A SIX YEAR TIME PERIOD, ONLY ONE 74L4 SENSOR HAS FAILED PRE-ATP DIELECTRIC WITHSTAND VOLTAGE TESTING. LO2 SENSOR 74L4-1, S/N 0002832 FAILED PRE-ATP TESTING ON 10-24-02. INVESTIGATION REVEALED THAT THE CLEAR TFE TEFLONB INSULATING SLEEVING APPEARED TO BE PINCHED BETWEEN THE HOUSING AND THE COVER. AFTER REMOVAL OF THE COVER IT WAS CONFIRMED THAT THE SLEEVING WAS PINCHED, LEAVING THE WIRE IN CLOSE PROXIMITY TO THE EDGE OF THE HOUSING. THE COVER WAS REMOVED FROM THE HOUSING TO PERFORM THE FAILURE INVESTIGATION. THE LEAD WIRE/TERMINAL WAS STRAIGHTENED TO ALLOW THE WIRE TO EXIT THROUGH THE CHANNEL STRAIGHT AND NOT AT AN ANGLE. THE PINCHED INSULATING SLEEVING WAS THEN REPLACED ON THE EFFECTED LEAD WIRE. THE COVER WAS REINSTALLED, AND THE ATTACHMENT SCREWS WERE TORQUED TO 35- 38 INCH- OUNCES. CAUTION WAS EXERCISED TO ENSURE THAT THE INSULATING SLEEVING WAS NOT PINCHED OR KINKED UNDER THE COVER. THE PART WAS RETESTED PER ATP-946 DIELECTRIC STRENGTH PER PARAGRAPH 6.2 AND PASSED WITH A LEAKAGE CURRENT OF .028 MILLIAMPS. CORRECTIVE ACTIONS WERE IMPLEMENTED TO ADD THE FOLLOWING OPERATION SPECIFIC INSTRUCTIONS: 1. WHEN INSTALLING SENSOR ELEMENT INTO HOUSING CHECK THAT THE SENSOR WIRES ARE POSITIONED TOWARDS THE CENTER OF THE HOUSING CHANNEL. 2. PRIOR TO ASSEMBLING COVER ON HOUSING VERIFY THAT WIRES ARE POSITIONED TOWARDS THE CENTER OF THE HOUSING CHANNEL. (REF. E-MAIL FROM J. HILL DATED 11/20/02) TASK CLOSED ----------- CAUSE: ------ THE ROOT CAUSE COULD NOT BE DETERMINED. NO MECHANICAL DEFECT WAS FOUND IN THE SENSOR COMPONENTS. EVIDENCE OF ARCING BETWEEN THE SENSING ELEMENT AND THE HOUSING WAS NOTED DURING FAILURE ANALYSIS. TASK II CORRECTIVE ACTION ------------------ * NO CORRECTIVE ACTION IS REQUIRED. A LIMITED NUMBER OF ISOLATION RESISTANCE TEST FAILURES CAN BE EXPECTED TO OCCUR DURING SUPPLIER TESTING AS A NATURAL RESULT OF THE SENSOR DESIGN. THE DESIGN OF THE SENSOR DOES NOT PROVIDE POSITIVE MECHANICAL SEPARATION BETWEEN THE GOLD CIRCUIT PATH ON THE INTERNAL SENSING ELEMENT AND THE TEFLON(R) COATED METAL CASE. THESE FACTS WERE DOCUMENTED IN CAPS E-100 AND CAPS E-138. THE SUPPLIER ATP PROVIDES AN ADEQUATE SCREEN FOR FAILURES OF THIS TYPE. TASK CLOSED ----------- TASK III CLEARANCE OF EFFECTIVITIES -------- * FLEET CLEARANCE FOR ALL EFFECTIVITIES IS BASED ON THE REQUIREMENT THAT ALL 74L4 CRYOGENIC LIQUID LEVEL SENSORS PASS THE 500 VOLTS ATP DIELECTRIC WITHSTAND VOLTAGE TEST. IN ADDITION TO THE ATP REQUIREMENT, ALL 74L4 CRYOGENIC LIQUID LEVEL SENSORS ARE TESTED FOR INSULATION RESISTANCE WITH 50 VOLTS AT MAF. FURTHERMORE, THOSE SENSORS USED IN LH2 DEPLETION SENSOR (CRITICALITY 1R) APPLICATIONS ARE TESTED WITH 50 VOLTS FOR INSULATION RESISTANCE AT KSC. (REFERENCE E- MAIL FROM A. GRECONIA DATED 11/20/02) TASK CLOSED ----------- TASK IV CAPS CLOSURE SUMMARY -------------------- * LIQUID LEVEL SENSOR 74L4-2, S/N 0003354 FAILED DIELECTRIC WITHSTANDING VOLTAGE TEST DURING SUPPLIER ATP. FAILURE ANALYSIS VERIFIED THE SOURCE OF THE LEAKAGE CURRENT TO BE AT THE GOLD PAD OF SENSOR ELEMENT. ARC BURNS WERE FOUND ON THE SENSING ELEMENT AND ALSO ON THE INTERIOR SURFACE OF THE SENSOR HOUSING. A LIMITED NUMBER OF SUCH FAILURES ARE INHERENT IN THE SENSOR DESIGN. SUPPLIER ACCEPTANCE TESTING IS ADEQUATE TO SCREEN FOR FAILURES OF THIS TYPE. NO CORRECTIVE ACTION IS REQUIRED. THIS SENSOR IS NOT ACCEPTABLE FOR FLIGHT AND IS TO BE SCRAPPED. TASK CLOSED ----------- |
| MSFC Response/Concurrence 11/21/2002 - MSFC APPROVED INTERIM CLOSURE THRU 1/31/2003 BASED ON NSTS 08126, REV. H RATIONALE 4.3B: THE PROBLEM CONDITION IS CLEARLY SCREENED DURING PRE-FLIGHT CHECKOUT OR SPECIAL TEST. SIGNATURES ON FILE IN THE PAC. 01/30/2003 - BOARD ACCEPTED PROBLEM CLOSURE RATIONALE. SIGNATURES ARE ON FILE IN THE PAC. THIS PROBLEM IS OFFICIALLY CLOSED. |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A17820 | IFA# -- | Contractor RPT# E-170 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 74L4-2 | Asmnt Part Name LH2 LIQUID SENSOR LV | Asmnt Serial/Lot# 0003354 |
| HCRIT CD 1R | FCRIT CD 1R | CAUSE CD DH - DES-HDW | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.6.1.1 | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |