217/782-2113

# TITLE V - CLEAN AIR ACT PERMIT PROGRAM (CAAPP) PERMIT

# and

# TITLE I PERMIT1

PERMITTEE

The Solar Corporation

Attn:  Greg Miller

100 Solar Drive

Libertyville, Illinois  60048

Application No.:  95110108			I.D. No.:  097090ABS

Applicant’s Designation:  			Date Received:  November 29, 1995

Operation of:  Plastic and Fiber Component for Auto and Home Entertainment

Date Issued:  					Expiration Date2:

Source Location:  100 Solar Drive, Libertyville, Lake County

Responsible Official:  Ken Formanski, Director of Human Resources

This permit is hereby granted to the above-designated Permittee to operate a plastic and fiber components for autos and home entertainment appliances plant, pursuant to the above referenced permit application.  This permit is subject to the conditions contained herein.

If you have any questions concerning this permit, please contact David Hulskotter at 217/782-2113.

Donald E. Sutton, P.E.

Manager, Permit Section

Division of Air Pollution Control

DES:DWH:psj

cc:	Illinois EPA, FOS, Region 1

USEPA

# 1	This permit may contain terms and conditions which address the applicability, and compliance if determined applicable, of Title I of the CAA and regulations promulgated thereunder, including 40 CFR 52.21 – federal PSD and 35 IAC Part 203 – Major Stationary Sources Construction and Modification.  Any such terms and conditions are identified within this permit.

# 2	Except as provided in Condition 8.7 of this permit.

Table of Contents

|  |  |  | PAGE |
| --- | --- | --- | --- |
| 1.0 | Source Identification | 4 |
|  | 1.1 | Source |  |
|  | 1.2 | Owner/Parent Company |  |
|  | 1.3 | Operator |  |
|  | 1.4 | General Source Description |  |
| 2.0 | List of Abbreviations/Acronyms Used in This Permit | 5 |
| 3.0 | Insignificant Activities | 7 |
|  | 3.1 | Identification of Insignificant Activities |  |
|  | 3.2 | Addition of Insignificant Activities |  |
| 4.0 | Significant Emission Units at This Source | 9 |
| 5.0 | Overall Source Conditions | 10 |
|  | 5.1 | Source Description |  |
|  | 5.2 | Applicable Regulations |  |
|  | 5.3 | Non-Applicability of Regulations of Concern |  |
|  | 5.4 | Source-Wide Operational and Production Limits and Work Practices |  |
|  | 5.5 | Source-Wide Emission Limitations |  |
|  | 5.6 | General Recordkeeping Requirements |  |
|  | 5.7 | General Reporting Requirements |  |
|  | 5.8 | General Operational Flexibility/Anticipated Operating Scenarios |  |
|  | 5.9 | General Compliance Procedures |  |
| 6.0 | Emission REDUCTION MARKET SYSTEM (ERMS) | 15 |
|  | 6.1 | Description of ERMS |  |
|  | 6.2 | Applicability |  |
|  | 6.3 | Obligation to Hold Allotment Trading Units (ATUs) |  |
|  | 6.4 | Market Transaction |  |
|  | 6.5 | Emission Excursion Compensation |  |
|  | 6.6 | Quantification of Seasonal VOM Emissions |  |
|  | 6.7 | Annual Account Reporting |  |
|  | 6.8 | Allotment of ATUs to the Source |  |
|  | 6.9 | Recordkeeping for ERMS |  |
|  | 6.10 | Federal Enforceability |  |
|  | 6.11 | Exclusions from Further Reductions |  |
|  |  |  | PAGE |
| 7.0 | Unit Specific Conditions | 23 |
|  | 7.1 | Paint Spraying Operation |  |
|  | 7.2 | Adhesive Spray Application |  |
|  | 7.3 | Natural Gas Fired Boilers |  |
| 8.0 | General Permit Conditions | 38 |
|  | 8.1 | Permit Shield |  |
|  | 8.2 | Applicability of Title IV Requirements |  |
|  | 8.3 | Emissions Trading Programs |  |
|  | 8.4 | Operational Flexibility/Anticipated Operating Scenarios |  |
|  | 8.5 | Testing Procedures |  |
|  | 8.6 | Reporting Requirements |  |
|  | 8.7 | Obligation to Comply with Title I Requirements |  |
| 9.0 | STANDARD PERMIT CONDITIONS | 44 |
|  | 9.1 | Effect of Permit |  |
|  | 9.2 | General Obligations of Permittee |  |
|  | 9.3 | Obligation to Allow Illinois EPA Surveillance |  |
|  | 9.4 | Obligation to Comply with Other Requirements |  |
|  | 9.5 | Liability |  |
|  | 9.6 | Recordkeeping |  |
|  | 9.7 | Annual Emissions Report |  |
|  | 9.8 | Requirements for Compliance Certification |  |
|  | 9.9 | Certification |  |
|  | 9.10 | Defense to Enforcement Actions |  |
|  | 9.11 | Permanent Shutdown |  |
|  | 9.12 | Reopening And Reissuing Permit For Cause |  |
|  | 9.13 | Severability Clause |  |
|  | 9.14 | Permit Expiration and Renewal |  |
| 10.0 | Attachments |  |
|  | 10.1 | Attachment 1 - Example Certification by a Responsible Official | 1-1 |

1.0	Source Identification

1.1	Source

The Solar Corporation

100 Solar Drive

Libertyville, Illinois  60048

(847) 367-2500

I.D. No.:  097090ABS

Standard Industrial Classification:	2221, Broad Woven Fabric Mills, Man-Made Fiber and Silk

1.2	Owner/Parent Company

The Solar Corporation

100 Solar Drive

Libertyville, Illinois  60048

1.3	Operator

The Solar Corporation

100 Solar Drive

Libertyville, Illinois  60048

Ken Formanski, Director of Human Resources

(847) 367-2500

1.4	General Source Description

The Solar Corporation is located at 100 Solar Drive, Libertyville, Lake County.  The source produces custom made plastic and fabric components for autos and home entertainment appliances.

2.0	List of Abbreviations/Acronyms Used in This Permit

| Act | Environmental Protection Act [415 ILCS 5/1 et seq.] |
| --- | --- |
| AP-42 | Compilation of Air Pollutant Emission Factors, Volume 1, Stationary Point and Other Sources (and Supplements A through F), USEPA, Office of Air Quality Planning and Standards, Research Triangle Park, NC 27711 |
| Btu | British thermal unit |
| CAA | Clean Air Act [42 U.S.C. Section 7401 et seq.] |
| CAAPP | Clean Air Act Permit Program |
| CFR | Code of Federal Regulations |
| ft3 | cubic foot |
| gal | gallon |
| HAP | Hazardous Air Pollutant |
| hr | hour |
| IAC | Illinois Administrative Code |
| I.D. No. | Identification Number of Source, assigned by Illinois EPA |
| Illinois EPA | Illinois Environmental Protection Agency |
| kg | kilogram |
| kW | kilowatts |
| lb | pound |
| Mg | Megagram |
| MW | Megawatt |
| mmBtu | Million British thermal units |
| NOx | Nitrogen Oxides |
| NSPS | New Source Performance Standards |
| PCB | Pollution Control Board |
| PM | Particulate Matter |
| PM10 | Particulate matter with an aerodynamic diameter less than or equal to a nominal 10 microns as measured by applicable test or monitoring methods |
| ppm | parts per million |
| PSD | Prevention of Significant Deterioration |
| psia | pounds per square inch absolute |
| SO2 | Sulfur Dioxide |
| T | tons |
| T1 | Title I – identifies Title I conditions that have been carried over from an existing construction permit |
| T1N | Title I New – identifies Title I conditions that are being established in this permit |
| T1R | Title I Revised – identifies Title I conditions that have been carried over from an existing construction permit and subsequently revised in this permit |
| USEPA | United States Environmental Protection Agency |
| wt% | weight percent |
| VOM | Volatile Organic Material |
| yr | year |

3.0	Insignificant Activities

3.1	Identification of Insignificant Activities

The following activities at the source constitute insignificant activities as specified in 35 IAC 201.210:

3.1.1	Activities determined by the Illinois EPA to be insignificant activities, pursuant to 35 IAC 201.210(a)(1) and 201.211, as follows:

Ink printing; and

Molding machines.

3.1.2	Activities that are insignificant activities based upon maximum emissions, pursuant to 35 IAC 201.210(a)(2) or (a)(3), as follows:

Infrared dryers for drying painted components;

Space heaters;

Resin Grinder;

Roller coat laminators; and

Wet solvent Degreasers.

3.1.3	Activities that are insignificant activities based upon their type or character, pursuant to 35 IAC 201.210(a)(4) through (18), as follows:

Direct combustion units designed and used for comfort heating purposes and fuel combustion emission units as follows:  (A) Units with a rated heat input capacity of less than 2.5 mmBtu/hr that fire only natural gas, propane, or liquefied petroleum gas; (B) Units with a rated heat input capacity of less than 1.0 mmBtu/hr that fire only oil or oil in combination with only natural gas, propane, or liquefied petroleum gas; and (C) Units with a rated heat input capacity of less than 200,000 Btu/hr which never burn refuse, or treated or chemically contaminated wood  [35 IAC 201.210(a)(4)].

Storage tanks of organic liquids with a capacity of less than 10,000 gallons and an annual throughput of less than 100,000 gallons per year, provided the storage tank is not used for the storage of gasoline or any material listed as a HAP pursuant to Section 112(b) of the CAA  [35 IAC 201.210(a)(10)].

Die casting machines where a metal or plastic is formed under pressure in a die  [35 IAC 201.210(a)(12)].

3.1.4	Activities that are considered insignificant activities pursuant to 35 IAC 201.210(b).

3.2	Addition of Insignificant Activities

3.2.1	The Permittee is not required to notify the Illinois EPA of additional insignificant activities present at the source of a type that is identified in Condition 3.1, until the renewal application for this permit is submitted, pursuant to 35 IAC 201.212(a).

3.2.2	The Permittee must notify the Illinois EPA of any proposed addition of a new insignificant activity of a type addressed by 35 IAC 201.210(a)and 201.211 other than those identified in Condition 3.1, pursuant to Section 39.5(12)(b) of the Act.

3.2.3	The Permittee is not required to notify the Illinois EPA of additional insignificant activities present at the source of a type identified in 35 IAC 201.210(b).

4.0	Significant Emission Units at This Source

| Emission Unit | Manufacturer | Control Equipment | Date Constructed/ Replaced |
| --- | --- | --- | --- |
| 1 | 3 Paint Booths (#1, #2 &#3) Hand Held Air Atomized Spray Gun With Infrared Heaters | None | November, 1987 |
| 2 | Adhesive Spray Booth, Hand Held Air Atomized Spray Gun (SP14, SP2, SP18, SP4, SP17, SP6, SP12, SPM, SP9, SP10, and SP11) | None | May 1987 |
| 3 | Adhesive Autospray Machine, Air Atomized with Heaters (Auto #1, 2, 3, 4, 5, 6, 7, 8, 9, 10, and 11) | None | June 1992 |
| Boilers | Natural Gas Fired Boilers. Maximum Heat Input Capacity: Boiler 1 (B1): 9.8 mmBtu/Hr Boiler 2 (B2): 14.3 mmBtu/Hr | None | May 1987 May 1987 |

5.0	Overall Source Conditions

5.1	Source Description

5.1.1	This permit is issued based on the source requiring a CAAPP permit as a major source of VOM and HAP emissions.

5.2	Applicable Regulations

5.2.1	Specific emission units at this source are subject to particular regulations as set forth in Section 7 (Unit-Specific Conditions) of this permit.

5.2.2	In addition, emission units at this source are subject to the following regulations of general applicability:

a.	No person shall cause or allow the emission of fugitive particulate matter from any process, including any material handling or storage activity, that is visible by an observer looking generally overhead at a point beyond the property line of the source unless the wind speed is greater than 40.2 kilometers per hour (25 miles per hour), pursuant to 35 IAC 212.301 and 212.314.

Compliance with this requirement is considered to be assured by the inherent nature of operations at this source, as demonstrated by historical operation.

b.	No person shall cause or allow the emission of smoke or other particulate matter, with an opacity greater than 30 percent, into the atmosphere from any emission unit other than those emission units subject to the requirements of 35 IAC 212.122, pursuant to 35 IAC 212.123(a), except as allowed by 35 IAC 212.123(b) and 212.124.

c.	No person shall cause or allow the emission of sulfur dioxide into the atmosphere from any process emission unit to exceed 2,000 ppm  [35 IAC 214.301].

5.2.3	The Permittee shall comply with the standards for recycling and emissions reduction of ozone depleting substances pursuant to 40 CFR Part 82, Subpart F, except as provided for motor vehicle air conditioners in Subpart B of 40 CFR Part 82:

a.	Persons opening appliances for maintenance, service, repair, or disposal must comply with the required practices pursuant to 40 CFR 82.156.

b.	Equipment used during the maintenance, service, repair, or disposal of appliances must comply with the standards for recycling and recovery equipment pursuant to 40 CFR 82.158.

c.	Persons performing maintenance, service, repair, or disposal of appliances must be certified by an approved technician certification program pursuant to 40 CFR 82.161.

5.2.4	Should this stationary source, as defined in 40 CFR Section 68.3, become subject to the Accidental Release Prevention regulations in Part 68, then the owner or operator shall submit a Risk Management Plan (RMP) by the date specified in Section 68.10 and shall certify compliance with the requirements of Part 68 as part of the annual compliance certification as required by 40 CFR Part 70 or 71.

5.2.5	Should this stationary source, as defined in 40 CFR Part 63, become subject to 40 CFR Part 63, then the owner or operator shall comply with the applicable requirements of 40 CFR Part 63 by the date(s) specified in the NESHAP and shall certify compliance with the applicable requirements of 40 CFR Part 63 as part of the annual compliance certification as required by 40 CFR Part 70 or 71.

5.3	Non-Applicability of Regulations of Concern

None

5.4	Source-Wide Operational and Production Limits and Work Practices

In addition to the source-wide requirements in the Standard Permit Conditions in Section 9, the Permittee shall fulfill the following source-wide operational and production limitations and/or work practice requirements:

None

5.5	Source-Wide Emission Limitations

5.5.1	Permitted Emissions for Fees

The annual emissions from the source, not considering insignificant activities as addressed by Section 3.0 of this permit, shall not exceed the following limitations.  The overall source emissions shall be determined by adding emissions from all emission units.  Compliance with these limits shall be determined on a calendar year basis.  These limitations (Condition 5.5.1) are set for the purpose of establishing fees and are not federally enforceable.

Permitted Emissions of Regulated Pollutants

| Pollutant | Tons/Year |
| --- | --- |
| Volatile Organic Material (VOM) | 99.69 |
| Sulfur Dioxide (SO2) | -- |
| Particulate Matter (PM) | -- |
| Nitrogen Oxides (NOx) | 11.30 |
| HAP, not included in VOM or PM | -- |
| TOTAL | 110.99 |

5.5.2	Emissions of Hazardous Air Pollutants

Source-wide emission limitations for HAPs as listed in Section 112(b) of the CAA are not set.  This source is considered to be a major source of HAPs.

5.5.3	Other Source-Wide Emission Limitations

a.	Emissions of volatile organic material (VOM) from all plant operations (adhesives, paints, coatings, thinners, clean-up, etc.) shall not exceed 99 tons per year.

b.	Compliance with this annual limit shall be determined from a running total of 365 days of data on a daily basis.

c.	Compliance with this annual limit of 99 tons volatile organic material per year shall be determined from a running total of 365 days of data.  For example, compliance with the first month shall be determined by utilizing the last 11 months of historical data and the current data required to be maintained pursuant to this permit.

d.	The limitations in Condition 5.5.3 originate from Construction Permit #94030082.  [T1]

5.6	General Recordkeeping Requirements

5.6.1	Emission Records

The Permittee shall maintain records of the following items for the source to demonstrate compliance with Condition 5.5.1, pursuant to Section 39.5(7)(b) of the Act:

a.	Total annual emissions on a calendar year basis for the emission units covered by Section 7 (Unit Specific Conditions) of this permit.

b.	Total annual HAP emissions on a calendar year basis for emission units covered by Section 7 (Unit Specific Conditions) of this permit.

5.6.5	Records for Operating Scenarios

N/A

5.6.6	Retention and Availability of Records

a.	All records and logs required by this permit shall be retained for at least five years from the date of entry (unless a longer retention period is specified by the particular recordkeeping provision herein), shall be kept at a location at the source that is readily accessible to the Illinois EPA or USEPA, and shall be made available for inspection and copying by the Illinois EPA or USEPA upon request.

b.	The Permittee shall retrieve and print, on paper during normal source office hours, any records retained in an electronic format (e.g., computer) in response to an Illinois EPA or USEPA request for records during the course of a source inspection.

5.7	General Reporting Requirements

5.7.1	General Source-Wide Reporting Requirements

The Permittee shall promptly notify the Illinois EPA, Compliance Section of noncompliance with the permit requirements as follows, pursuant to Section 39.5(7)(f)(ii) of the Act.  Reports shall describe the probable cause of such deviations, and any corrective actions or preventive measures taken.

5.7.2	Annual Emissions Report

The annual emissions report required pursuant to Condition 9.7 shall contain emissions information for the previous calendar year.  The total annual HAP emissions shall also be included with this report.

5.8	General Operational Flexibility/Anticipated Operating Scenarios

N/A

5.9	General Compliance Procedures

5.9.1	General Procedures for Calculating VARIABLE Emissions

Compliance with the source-wide emission limits specified in Condition 5.5 shall be based on the recordkeeping and reporting requirements of Conditions 5.6 and 5.7, and Compliance Procedures in Section 7 (Unit Specific Conditions) of this permit.

6.0	EMISSION REDUCTION MARKET SYSTEM (ERMS)

6.1	Description of ERMS

The ERMS is a “cap and trade” market system for major stationary sources located in the Chicago ozone nonattainment area.  It is designed to reduce VOM emissions from stationary sources to contribute to further reasonable progress toward attainment, as required by Section 182(c) of the Clean Air Act.

The ERMS addresses VOM emissions during a seasonal allotment period from May 1 through September 30.  Once the ERMS begins, participating sources must hold “allotment trading units” (ATUs) for their actual seasonal VOM emissions.  Each year participating sources are issued ATUs based on allotments set during initial issuance of the sources’ CAAPP permits.  These allotments are established from historical VOM emissions or “baseline emissions” lowered to provide the emission reduction from stationary sources required for further progress.

By December 31 of each year, the end of the reconciliation period following the seasonal allotment period, each source shall have sufficient ATUs in its account to cover its actual VOM emissions during the preceding season.  An account’s balance as of December 31 will include any valid ATU transfer agreements entered into as of December 31 of the given year, provided such agreements are promptly submitted to the Illinois EPA for entry into the account database.  The Illinois EPA will then retire ATUs in sources’ accounts in amounts equivalent to their seasonal emissions.  When a source does not appear to have sufficient ATUs in its account, the Illinois EPA will issue a notice to the source to begin the process for Emissions Excursion Compensation.

In addition to receiving ATUs pursuant to their allotments, participating sources may also obtain ATUs from the market, including ATUs bought from other participating sources and general participants in the ERMS that hold ATUs (35 IAC 205.630) and ATUs issued by the Illinois EPA as a consequence of VOM emission reductions from an Emission Reduction Generator or an Intersector Transaction (35 IAC 205.500 and 205.510).  During the reconciliation period, sources may also buy ATUs from a secondary reserve of ATUs managed by the Illinois EPA, the Alternative Compliance Market Account (35 IAC 205.710).  Sources may also transfer or sell the ATUs that they hold to other sources or participants (35 IAC 205.630).

6.2	Applicability

This source is considered a “participating source” for purposes of the ERMS, 35 IAC Part 205.

6.3	Obligation to Hold Allotment Trading Units (ATUs)

a.	Pursuant to 35 IAC 205.150(c)(1) and 205.720, and as further addressed by condition 6.8, as of December 31 of each year, this source shall hold ATUs in its account in an amount not less than the ATU equivalent of its VOM emissions during the preceding seasonal allotment period (May 1 - September 30) not including VOM emissions from the following, or the source shall be subject to “emissions excursion compensation,” as described in Condition 6.4.

i.	VOM emissions from insignificant units and activities as identified in Section 3 of this permit, in accordance with 35 IAC 205.220;

ii.	Excess VOM emissions associated with startup, malfunction or breakdown of an emission unit as authorized elsewhere in this permit, in accordance with 35 IAC 205.225;

iii.	Excess VOM emissions to the extent allowed by a Variance, Consent Order, or Compliance Schedule, in accordance with 35 IAC 205.320(e)(3);

iv.	Excess VOM emissions that are a consequence of an emergency as approved by the Illinois EPA, pursuant to 35 IAC 205.750; and

v.	VOM emissions from certain new and modified emission units as addressed by Section 6.7(b), if applicable, in accordance with 35 IAC 205.320(f).

b.	Notwithstanding the above condition, in accordance with 35 IAC 205.150(c)(2), if a source commences operation of a major modification, pursuant to 35 IAC Part 203, the source shall hold ATUs in an amount not less than 1.3 times its VOM emissions attributable to such major modification during the seasonal allotment period, determined in accordance with the construction permit for such major modification or applicable provisions in Section 7.0 of this permit.

6.4	Market Transaction

a.	The source shall apply to the Illinois EPA for and obtain authorization for a Transaction Account prior to conducting any market transactions, as specified at 35 IAC 205.610(a).

b.	The Permittee shall promptly submit to the Illinois EPA any revisions to the information submitted for its Transaction Account, pursuant to 35 IAC 205.610(b).

c.	The source shall have at least one account officer designated for its Transaction Account, pursuant to 35 IAC 205.620(a).

d.	Any transfer of ATUs to or from the source from another source or general participant must be authorized by a qualified Account Officer designated by the source and approved by the Illinois EPA in accordance with 35 IAC 205.620 and the transfer must be submitted to the Illinois EPA for entry into the Transaction Account database.

6.5	Emission Excursion Compensation

Pursuant to 35 IAC 205.720, if the source fails to hold ATUs in accordance with Condition 6.3, it shall provide emissions excursion compensation in accordance with the following:

a.	Upon receipt of an Excursion Compensation Notice issued by the Illinois EPA, the source shall purchase ATUs from the ACMA in the amount specified by notice, as follows:

i.	The purchase of ATUs shall be in an amount equivalent to 1.2 times the emissions excursion; or

ii.	If the source had an emissions excursion for the seasonal allotment period immediately before the period for the present emission excursion, the source shall purchase ATUs in an amount equivalent to 1.5 times the emissions excursion.

b.	If requested in accordance with paragraph (c) below or in the event that the ACMA balance is not adequate to cover the total emissions excursion amount, the Illinois EPA will deduct ATUs equivalent to the specified amount or any remaining portion thereof from the ATUs to be issued to the source for the next seasonal allotment period.

c.	Pursuant to 35 IAC 205.720(c), within 15 days of receipt of an Excursion Compensation Notice, the owner or operator may request that ATUs equivalent to the amount specified be deducted from the source’s next seasonal allotment by the Illinois EPA, rather than purchased from the ACMA.

6.6	Quantification of Seasonal VOM Emissions

a.	The methods and procedures specified in Section 5 and 7 of this permit for determining VOM emissions and compliance with VOM emission limitations shall be used for determining seasonal VOM emissions for purposes of the ERMS, with the following exceptions  [35 IAC 205.315(b)]:

No exceptions

b.	The Permittee shall report emergency conditions at the source to the Illinois EPA in accordance with 35 IAC 205.750, if the Permittee intends to deduct VOM emissions in excess of the technology-based emission rates normally achieved that are attributable to the emergency from the source’s seasonal VOM emissions for purposes of the ERMS.  These reports shall include the information specified by 35 IAC 205.750(a), and shall be submitted in accordance with the following:

i.	An initial emergency condition report within two days of the time when such excess emissions occurred due to the emergency; and

ii.	A final emergency condition report, if needed to supplement the initial report, within 10 days after the conclusion of the emergency.

6.7	Annual Account Reporting

a.	For each year in which the source is operational, the Permittee shall submit, as a component of its Annual Emission Report, seasonal VOM emission information to the Illinois EPA for the seasonal allotment period. This report shall include the following information  [35 IAC 205.300]:

i.	Actual seasonal emissions of VOM from the source;

ii.	A description of the methods and practices used to determine VOM emissions, as required by this permit, including any supporting documentation and calculations;

iii.	A detailed description of any monitoring methods that differ from the methods specified in this permit, as provided in Section 205.337 of this Subpart;

iv.	If a source has experienced an emergency, as provided in 35 IAC 205.750, the report shall reference the associated emergency conditions report that has been approved by the Illinois EPA;

v.	If a source’s baseline emissions have been adjusted due to a variance, consent order or CAAPP permit compliance schedule, as provided for in 35 IAC 205.320(e)(3), the report shall provide documentation quantifying the excess VOM emissions during the season that were allowed by the Variance, Consent Order, or Compliance Schedule, in accordance with 35 IAC 205.320(e)(3); and

vi.	If a source is operating a new or modified emission unit for which three years of operational data are not yet available, as specified in 35 IAC 205.320(f), the report shall specify seasonal VOM emissions attributable to the new emission unit or the modification of the emission unit.

b.	This report shall be submitted by November 30 of each year, for the preceding seasonal allotment period.

6.8	Allotment of ATUs to the Source

a.	i.	The allotment of ATUs to this source is 272 ATUs per seasonal allotment period.

ii.	This allotment of ATUs reflects the Illinois EPA's determination that the source's baseline emissions were 30.88 tons.

iii.	The source's allotment reflects 88% of the baseline emissions (12% reduction) except for the VOM emissions from specific emission unit excluded from such reduction, pursuant to 35 IAC 205.405 including units complying with MACT or using BAT, as identified in Condition 6.11 of this permit.

iv.	ATUs will be issued to the source's Transaction Account by the Illinois EPA annually.  These ATUs will be valid for the seasonal allotment period following issuance and, if not retired in this season, the next seasonal allotment period.

v.	Condition 6.3(a) becomes effective beginning in the seasonal allotment period following the initial issuance of ATUs by the Illinois EPA into the Transaction Account for the source.

b.	Contingent Allotments for New or Modified Emission Units

Not applicable.

In accordance with 35 IAC Part 205, for the above referenced emission units, the source is required to hold the appropriate amount of ATU's for these emission units.

c.	Notwithstanding the above, part or all of the above ATUs will not be issued to the source in circumstances as set forth in 35 IAC Part 205, including:

i.	Transfer of ATUs by the source to another participant or the ACMA, in accordance with 35 IAC 205.630;

ii.	Deduction of ATUs as a consequence of emission excursion compensation, in accordance with 35 IAC 205.720; and

iii.	Transfer of ATUs to the ACMA, as a consequence of shutdown of the source, in accordance with 35 IAC 205.410.

6.9	Recordkeeping for ERMS

The Permittee shall maintain copies of the following documents as its Compliance Master File for purposes of ERMS [35 IAC 205.700(a)]:

a.	Seasonal component of the Annual Emission Report;

b.	Information on actual VOM emissions, as specified in detail in Sections 5 and 7 of this permit and Condition 6.6(a); and

c.	Any transfer agreements for the purchase or sale of ATUs and other documentation associated with the transfer of ATUs.

6.10	Federal Enforceability

Section 6 becomes federally enforceable upon approval of the ERMS by USEPA as part of Illinois' State Implementation Plan.

  - Exclusions from Further Reductions

a.	VOM emissions from the following emission units, if satisfying subsection (a)(1), (a)(2), or (a)(3) prior to May 1, 1999, shall be excluded from the VOM emissions reductions requirements specified in IAC 205.400(c) and (e) as long as such emission units continue to satisfy subsection (a)(1), (a)(2), or (a)(3) [35 IAC 205.405(a)]:

i.	Emission units that comply with any NESHAP or MACT standard promulgated pursuant to the CAA;

ii.	Direct combustion emission units designed and used for comfort heating purposes, fuel combustion emission units and internal combustion engines; and

iii.	An emission unit for which a LAER demonstration has been approved by the Agency on or after November 15, 1990.

The source has demonstrated in their ERMS application and the Illinois EPA has determined that the following emission units qualifies for exclusion from further reductions because they meet the criteria as indicated above [35 IAC 205.400(a) and (c)]:

None

b.	VOM emissions from the emission units using BAT for controlling VOM emissions, prior to May 1, 1999, shall not be subject to the VOM emissions reductions requirements specified in IAC 205.400(c) or (e) as long as such emission unit continues to use such BAT [35 IAC 205.405(b)].

The source has demonstrated in their ERMS application and the Illinois EPA has determined that the following emission units qualifies from further reductions because these emission units use BAT for controlling VOM emissions as indicated above [35 IAC 205.400(b) and (c)]:

None

Please note that the baseline and associated ATU’s may be revised prior to issuance of this permit.

7.0	UNIT SPECIFIC CONDITIONS

7.1	Paint Spraying

7.1.1	Description

The Permittee is a manufacturer of painted, custom-made, plastic components for automobiles and home entertainment appliances.

7.1.2	List of Emission Equipment and Pollution Control Equipment

| Emission Unit | Manufacturer | Control Equipment | Date Constructed/ Replaced |
| --- | --- | --- | --- |
| 1 | 3 Paint Booths (#1, #2 & #3) Hand Held Air Atomized Spray Gun With Infrared Heaters | None | November, 1987 |

7.1.3	Applicability Provisions and Applicable Regulations

a.	Affected paint booths” for the purpose of these unit specific conditions is a coating operation that includes paint booths and drying infrared heaters which are used to apply a coating to plastic that falls under the category of Plastic Parts Coating: Automotive/Transportation.  As of the “date issued” as shown on page 1 of this permit, the affected paint booths are identified in Condition 7.1.2.

b.	The affected paint booths at the source are subject to 35 IAC 218.204(n)(1)(B)(i) for Plastic Parts Coating: Automotive/Transportation, Interiors Air Dried color coat, which provides that:

i.	No owner or operator of the affected paint booths shall apply at any time any coating in which the VOM content exceeds the following emission limitations for the coating as applied to Plastic Parts Coating Automotive/Transportation. The following emission limitation is expressed in units of VOM per volume of coating (minus water and any compounds which are specifically exempted from the definition of VOM) as applied at each coating applicator:

kg/liter     lb/gallon

0.49          3.2

ii.	Compounds which are specifically exempted from the definition of VOM should be treated as water for the purpose of calculating the “less water” part of the coating composites.

7.1.4	Non-Applicable Regulations of Concern

a.	The affected paint booths are not subject to the New Source Performance Standard for Automobile and Light Duty Truck Surface Coating Operation, 40 CFR 60, Subpart MM, because affected paint booths are coating plastic component for automobiles and home entertainment industries.

b.	The affected paint booths are not subject to the New Source Performance Standard for Industrial Surface Coating: Surface Coating of Plastic Parts for Business Machines, 40 CFR 60, Subpart TTT, because affected paint booths are coating plastic component for automobiles and home entertainment industries.

c.	The affected paint booths are not subject to 35 IAC 218.301, Use of Organic Material, pursuant to 35 IAC 218.209, Exemption From General Rule on Use of Organic Material which excludes affected paint booths from this requirement.

d.	The affected paint booths are not subject to 35 IAC 216.121, Emissions of Carbon Monoxide from Fuel Combustion Emission Units, because the affected paint booths are not by definition a fuel combustion emission unit.

e.	The affected paint booths are not subject to 35 IAC 217.121, Emissions of Nitrogen Oxides from New Fuel Combustion Emission Sources, because the affected paint booth is not by definition a fuel combustion emission unit.

7.1.5	Operational and Production Limits and Work Practices

a.	Plastic parts from the affected paint booths shall only be air dried.  However, infrared heaters are used to make the parts more pliable.

b.	Affected paint booth is allowed to use solvent-based or water-based adhesives.

7.1.6	Emission Limitations

In addition to Condition 5.2.2, the source-wide limitations in Condition 5.5, and the VOM content limitations of Condition 7.1.3(d), the affected paint booth is subject to the following:

N/A

7.1.7	Testing Requirements

Testing for VOM content of coatings and other materials shall be performed as follows [35 IAC 218.105(a), 218.211(a), and Section 39.5(7)(b) of the Act]

Upon reasonable request by the Illinois EPA, the VOM content of specific coatings and cleaning solvents used on the affected paint booths shall be determined according to USEPA Reference Methods 24 and 24A of 40 CFR 60 Appendix A and the procedures of 35 IAC 218.105(a) and 218.211(a).

a.	The VOM content of representative coatings “as applied” on the affected paint booths shall be determined according to USEPA Reference Methods 24 and 24A of 40 CFR 60 Appendix A and the procedures of 35 IAC 218.105(a).

b.	This testing may be performed by the supplier of a material provided that the supplier provides appropriate documentation for such testing to the Permittee and the Permittee’s records pursuant to Condition 7.1.9(b) directly reflect the application of such material and separately account for any additions of solvent. [35 IAC 218.105(a)  and 218.211(a)]

7.1.8	Inspection Requirements

N/A

7.1.9	Recordkeeping Requirements

The Permittee shall maintain records of the following items for the affected paint booths to demonstrate compliance with this section, pursuant to Section 39.5(7)(b) of the Act:

a.	i.	The name and identification number of each coating, thinner, and cleaning solution as applied on each affected paint booth;

ii.	The daily usage of each coating, thinner, and cleaning solution;

iii.	The weight of VOM per volume of each coating (minus water and any compounds which are specifically exempted from the definition of VOM) as applied each month on the affected paint booths;

iv.	The aggregate annual VOM emissions from the affected coating lines based on the coating, thinner, and cleaning solution usage and VOM content, and with supporting calculations; and

v.	If credit is desired for VOM emissions from waste materials, aggregate records of materials disposed of or recycled shall be maintained for all coatings, cleaning solvents, and any other VOM containing material use on the affected paint booth on a monthly basis.

b.	When coatings and cleaning solvents are tested for VOM content and HAP content due to a request by the Illinois EPA, the Permittee shall maintain test records that include the following [Section 39.5(7)(e) of the Act]:

i.	Identification of material tested;

ii.	Results of analysis;

iii.	Documentation of analysis methodology; and

iv.	Person performing analysis.

c.	The operating schedule of the affected paint booth.

7.1.10	Reporting Requirements

The Permittee shall promptly notify the Illinois EPA, Compliance Section of noncompliance with the control and operating requirements as follows pursuant to Section 39.5(7)(f)(ii) of the Act:

Pursuant to 35 IAC 218.211(c)(3)(A), the Permittee shall notify the Illinois EPA of any record showing violation of Condition 7.1.3(c) (see also 35 IAC 218.204(n)(1)(B)(i)) within 30 days of such an occurrence.

7.1.11	Operational Flexibility/Anticipated Operating Scenarios

The Permittee is authorized to make the following physical or operational change with respect to the affected spray booths without prior notification to the Illinois EPA or revision of this permit. This condition does not affect the Permittee’s obligation to properly obtain a construction permit in a timely manner for any activity constituting construction or modification of the source, as defined in 35 IAC 201.102:

Usage of coatings, thinners, or cleaning solvents at this source with various VOM contents provided that the materials are tested in accordance with Condition 7.1.7, the source wide emission limitations in Condition 5.5.1 are not exceeded and the affected paint booth remains in compliance with Condition 7.1.3(c).

7.1.12	Compliance Procedures

Calculation of VOM emissions shall be calculated using the following equation:

VOM Emissions =	VOM Containing Material Usage x VOM Content

7.2	Adhesive Spray Application

7.2.1	Description

The Permittee is a manufacturer of painted, custom-made, plastic components for automobiles and home entertainment appliances.  The adhesive spray application is for the joining fabric with plastic parts.

7.2.2	List of Emission Equipment and Pollution Control Equipment

| Emission Unit | Manufacturer | Control Equipment | Date Constructed/ Replaced |
| --- | --- | --- | --- |
| 2 | Adhesive Spray Booth, Hand Held Air Atomized Spray Gun With No Oven (SP14, SP2, SP18, SP4, SP17, SP6, SP12, SPM, SP9, SP10, And SP11) | None | May 1987 |
| 3 | Adhesive Autospray Machine, Air Atomized with No Oven (Auto #1, 2, 3, 4, 5, 6, 7, 8, 9, 10 and 11) | None | June 1992 |

7.2.3	Applicability Provisions and Applicable Regulations

a.	An “affected adhesive spray booth” for the purpose of these unit specific conditions is a coating operation that includes a adhesive spray booth with no oven which is used to apply a coating to injection molded plastic.  As of the “date issued” as shown on page 1 of this permit, the affected adhesive spray booths are identified in Condition 7.2.2.

b.	Each affected adhesive spray booth at the source is subject to 35 IAC 212.321(a), which provides that:

i.	No person shall cause or allow the emission of particulate matter into the atmosphere in any one hour period from any new process emission unit, either alone or in combination with the emission of particulate matter from all other similar process emission units for which construction or modification commenced on or after April 14, 1972, at a source or premises, exceeds the allowable emission rates specified in subsection (c) of 35 IAC 212.321 [35 IAC 212.321(a)].

ii.	The emissions of particulate matter into the atmosphere in any one hour period from each of the affected adhesive spray booths shall not exceed the allowable emission rates specified in the following equation:

E = A(P)B

where:

P = process weight rate;

E = allowable emission rate; and,

A.	For process weight rates up to 408 Mg/hr (450 T/hr):

Metric	English

P	Mg/hr		T/hr

E	kg/hr		lbs/hr

A	1.214		2.54

B	0.534		0.534

B.	For process weight rates in excess of 408 Mg/hr (450 T/hr):

Metric	English

P	Mg/hr		T/hr

E	kg/hr		lbs/hr

A	11.42		24.8

B	0.16		 0.16

c.	Each affected adhesive spray booth at the source is subject to Board Order PCB AS-94-2, which provides that:

i.	The emission limitation of VOM for the adhesive applied for joining fabric to plastic parts at affected adhesive spray booth subject to this adjusted standard is:

kg/liter     lb/gallon

Adhesive        0.69          5.75

ii.	This limitation is based on the adhesive as applied by each adhesive applicator (minus water and any compounds specifically exempted from the definition of VOM).  Compounds which are specifically exempted from the definition of VOM should be treated as water for the purpose of calculating the “less water” part of the coating composites.

iii.	Compliance with this adjusted standard must be demonstrated through the applicable coating analysis test methods and procedures specified at 35 IAC 218.105(a) and the recordkeeping and reporting requirements specified at 35 IAC 218.211(c).

iv.	Solar shall continue its research and development efforts regarding alternatives to solvent-based adhesives and will utilize such alternatives as they become available, if and when they are technically feasible and economically reasonable.

7.2.4	Non-Applicable Regulations of Concern

a.	Each affected adhesive spray booth is not subject to 35 IAC 218.301, Use of Organic Material, pursuant to 35 IAC 218.209, Exemption From General Rule on Use of Organic Material which excludes affected adhesive spray booths from this requirement.

b.	The affected adhesive spray booth is not subject to 35 IAC Subpart PP, control requirement of Miscellaneous Fabricated product manufacturing processes, because the affected adhesive spray booth is exempted by the Board Order PCB AS-94-2.

7.2.5	Operational and Production Limits and Work Practices

a.	Plastic parts from each affected adhesive spray booth shall only be air dried.

b.	Affected adhesive spray booth is allowed to use solvent-based or water-based adhesives.

7.2.6	Emission Limitations

In addition to Condition 5.2.2, the source-wide limitations in Condition 5.5, and the VOM content limitations of Condition 7.2.3(c), the affected adhesive spray booth is subject to the following:

Emissions and operation of equipment shall not exceed the following limits:

Volatile Organic

Coating Usage    Material Emissions

Item of Equipment       (Lb/Hour)      (Lb/Hour)  (Ton/Yr)

3 Auto Spray Machines

(Model IAI)		    0.35           0.27        3.5

These limits are based on the information provided in the permit application.  Compliance with annual limits shall be determined from a running total of 12 months of data.

These limitations originate from Construction Permit #94030082.  [T1]

7.2.7	Testing Requirements

Testing for VOM content of adhesives and other materials shall be performed as follows [35 IAC 218.105(a), 218.211(a), and Section 39.5(7)(b) of the Act]

Upon reasonable request by the Illinois EPA, the VOM content of specific adhesive and cleaning solvents used on each affected adhesive spray booth shall be determined according to USEPA Reference Methods 24 and 24A of 40 CFR 60 Appendix A and the procedures of 35 IAC 218.105(a) and 218.211(a).

a.	The VOM content of representative adhesive “as applied” on the affected adhesive spray booth shall be determined according to USEPA Reference Methods 24 and 24A of 40 CFR 60 Appendix A and the procedures of 35 IAC 218.105(a).

b.	This testing may be performed by the supplier of a material provided that the supplier provides appropriate documentation for such testing to the Permittee and the Permittee’s records pursuant to Condition 7.2.9(b) directly reflect the application of such material and separately account for any additions of solvent. [35 IAC 218.105(a)  and 218.211(a)]

7.2.8	Inspection Requirements

N/A

7.2.9	Recordkeeping Requirements

The Permittee shall maintain records of the following items for the affected adhesive spray booth to demonstrate compliance with this section, pursuant to Section 39.5(7)(b) of the Act:

a.	i.	The name and identification number of each adhesive, thinner, cleaning solution as applied on each affected adhesive spray booth;

ii.	The daily usage of each adhesive, thinner, and cleaning solution;

iii.	The weight of VOM per volume of each adhesive (minus water and any compounds which are specifically exempted from the definition of VOM) as applied each month on the affected adhesive spray booth;

iv.	The aggregate annual VOM emissions from the affected coating booths based on the coating and solvent usage, VOM content, and with supporting calculations; and

v.	If credit is desired for VOM emissions from waste materials, aggregate records of materials disposed of or recycled shall be maintained for all coatings, cleaning solvents, and any other VOM containing material use on the affected adhesive spray booth on a monthly basis.

b.	Records of the testing of VOM and HAP content (in wt%) of each adhesive and cleaning solvent as tested pursuant to the conditions of this section, which include the following [Section 39.5(7)(e) of the Act]:

i.	Identification of material tested;

ii.	Results of analysis;

iii.	Documentation of analysis methodology; and

iv.	Person performing analysis.

c.	The operating schedule of the affected adhesive spray booth.

7.2.10	Reporting Requirements

a.	The Permittee shall promptly notify the Illinois EPA, Compliance Section of noncompliance with the control and operating requirements as follows pursuant to Section 39.5(7)(f)(ii) of the Act:

Pursuant to 35 IAC 218.211(c)(3)(A), the Permittee shall notify the Illinois EPA of any record showing violation of Condition 7.2.3(c) within 30 days of such an occurrence.

7.2.11	Operational Flexibility/Anticipated Operating Scenarios

The Permittee is authorized to make the following physical or operational change with respect to the affected spray booths without prior notification to the Illinois EPA or revision of this permit. This condition does not affect the Permittee’s obligation to properly obtain a construction permit in a timely manner for any activity constituting construction or modification of the source, as defined in 35 IAC 201.102:

Usage of adhesive, thinners, or cleaning solvents at this source with various VOM contents provided that the materials are tested in accordance with Condition 7.2.7, the source wide emission limitations in Condition 5.5.1 are not exceeded and the affected adhesive spray booth remains in compliance with Condition 7.2.3(c).

7.2.12	Compliance Procedures

a.	Compliance with the particulate matter limitations in this section is assured and achieved by the proper operation and maintenance and the work-practices inherent in operation of an affected adhesive spray booth.

b.	Calculation of VOM emissions shall be calculated using the following equation.

VOM Emissions =	VOM Containing Material Usage x VOM Content

7.3	Natural Gas Fired Boilers

7.3.1	Description

Boilers are used to produce steam for heating at the source.

7.3.2	List of Emission Equipment and Pollution Control Equipment

| Equipment | Description | Date Constructed |
| --- | --- | --- |
| Boilers | Natural Gas Fired Boilers. Maximum Heat Input Capacity: Boiler 1 (B1): 9.8 mmBtu/Hr Boiler 2 (B2): 14.3 mmBtu/Hr | May 1987 May 1987 |

7.3.3	Applicability Provisions and Applicable Regulations

a.	An “affected boiler” for the purpose of these unit specific conditions, is each boiler listed in Condition 7.4.2.

b.	No person shall cause or allow the emission of carbon monoxide into the atmosphere from boiler B2 to exceed 200 ppm, corrected to 50 percent excess air on a per boiler basis [35 IAC 216.121].

7.3.4	Non-Applicability of Regulations of Concern

a.	The New Source Performance Standard for Small-Industrial-Commercial-Institutional Steam Generating Units, 40 CFR 60, Subpart Dc, applies to units constructed, reconstructed, or modified after June 9, 1989, with firing rates of 100 mmBtu/hr or less, but greater than 10 mmBtu/hr. The firing rates of boiler B1 is below the firing rates for which the NSPS would be applicable and affected boilers are constructed prior to June 9, 1989. Therefore, these rules do not apply.

b.	Boiler B1 is not subject to 35 IAC 216.121, emissions of carbon monoxide from fuel combustion emission sources, since the actual heat input from boiler B1 is less than 2.9 MW (10 mmBtu/hr).

c.	The affected boilers are not subject to 35 IAC 217.141, Existing Emission Sources in Major Metropolitan Areas, since the actual heat input of the affected boilers is less than 73.2 MW (250 mmBtu/hr).

d.	The affected boilers are not subject to 35 IAC 218.301, Use of Organic Material, pursuant to 35 IAC 218.303, Fuel Combustion Emission Sources, which excludes the affected boilers from this requirement.

7.3.5	Operational and Production Limits and Work Practices

Natural gas shall be the only fuel fired in the affected boilers.

7.3.6	Emission Limitations

In addition to Condition 5.2.2 and the source wide emission limitations in Condition 5.5.1, the boilers are subject to the following:

N/A

7.3.7	Testing Requirements

None

7.3.8	Monitoring Requirements

None

7.3.9	Recordkeeping Requirements

In addition to the records required by Condition 5.6, the Permittee shall maintain records of the following items for the affected boilers to demonstrate compliance with Condition 5.5.1 pursuant to Section 39.5(7)(b) of the Act:

a.	Natural gas Fuel usage (ft3/yr); and

b.	Natural gas Fuel combustion emissions calculated in accordance with the procedures given in Condition 7.4.12 (ton/yr).

7.3.10	Reporting Requirements

If there is an exceedance of the requirements of this permit as determined by the records required by this permit, the Permittee shall submit a report to the Illinois EPA Compliance Section in Springfield, Illinois within 30 days after the exceedance.  The report shall include the emissions released in accordance with the recordkeeping requirements, a copy of the relevant records, and a description of the exceedance or violation and efforts to reduce emissions and future occurrences [Section 39.5(7)(f)(ii) of the Act].

7.3.11	Operational Flexibility/Anticipated Operating Scenarios

None

7.3.12	Compliance Procedures

a.	Compliance with Condition 7.4.3(b) is assumed to be achieved by the work practices inherent in operation of a natural gas-fired boiler, thus no compliance procedures are set in this permit addressing this regulation.

b.	To determine compliance with Condition 5.5.1 emissions from the affected boilers shall be based on the emission factors listed below:

|  | Natural Gas Emission Factors for Boilers |
| --- | --- |
| Pollutant | (lb/106 ft3) |
| NOx | 100 |
| PM | 7.6 |
| SO2 | 0.6 |
| VOM | 5.5 |

These are the emission factors for uncontrolled natural gas combustion in boilers, Tables 1.4-1, and 1.4-2, AP-42, Volume I, Supplement F, October, 1996.

Boiler Emissions (lb) = (Natural Gas Consumed, ft3) x (The Appropriate Emission Factor)

8.0	General Permit Conditions

8.1	Permit Shield

Pursuant to Section 39.5(7)(j) of the Act, the Permittee has requested and has been granted a permit shield.  This permit shield provides that compliance with the conditions of this permit shall be deemed compliance with applicable requirements which were applicable as of the date the proposed permit for this source was issued, provided that either the applicable requirements are specifically identified within this permit, or the Illinois EPA, in acting on this permit application, has determined that other requirements specifically identified are not applicable to this source and this determination (or a concise summary thereof) is included in this permit.

This permit shield does not extend to applicable requirements which are promulgated after ________{insert public notice start date} (the date of issuance of the draft permit) unless this permit has been modified to reflect such new requirements.

8.2	Applicability of Title IV Requirements (Acid Deposition Control)

This source is not an affected source under Title IV of the CAA and is not subject to requirements pursuant to Title IV of the CAA.

8.3	Emissions Trading Programs

No permit revision shall be required for increases in emissions allowed under any USEPA approved economic incentives, marketable permits, emissions trading, and other similar programs or processes for changes that are provided for elsewhere in this permit and that are authorized by the applicable requirement  [Section 39.5(7)(o)(vii) of the Act].

8.4	Operational Flexibility/Anticipated Operating Scenarios

8.4.1	Changes Specifically Addressed by Permit

Physical or operational changes specifically addressed by the Conditions of this permit that have been identified as not requiring Illinois EPA notification may be implemented without prior notice to the Illinois EPA.

8.4.2	Changes Requiring Prior Notification

The Permittee is authorized to make physical or operational changes without applying for or obtaining an amendment to this permit, provided that the changes do not constitute a modification under Title I of the CAA, emissions will not exceed the emissions allowed under this permit following implementation of the physical or operational change and the Permittee provides written notice to the Illinois EPA, Division of Air Pollution Control, Permit Section, at least 7 days before commencement of the change  [Section 39.5(12)(a) of the Act].  This notice shall:

a.	Describe the physical or operational change;

b.	Identify the schedule for implementing the physical or operational change;

c.	Provide a statement of whether or not any New Source Performance Standard (NSPS) is applicable to the physical or operational change and the reason why the NSPS does or does not apply;

d.	Provide emission calculations which demonstrate that the physical or operational change will not result in a modification; and

e.	Provide a certification that the physical or operational change will not result in emissions greater than authorized under the Conditions of this permit.

8.5	Testing Procedures

Tests conducted to measure composition of materials, efficiency of pollution control devices, emissions from process or control equipment, or other parameters shall be conducted using standard test methods.  Documentation of the test date, conditions, methodologies, calculations, and test results shall be retained pursuant to the recordkeeping procedures of this permit.  Reports of any tests conducted as required by this permit or as the result of a request by the Illinois EPA shall be submitted as specified in Condition 8.6.

8.6	Reporting Requirements

8.6.1	Monitoring Reports

a.	A report summarizing required monitoring as specified in the conditions of this permit shall be submitted to the Air Compliance Section of the Illinois EPA every six months as follows  [Section 39.5(7)(f) of the Act]:

| Monitoring Period | Report Due Date |
| --- | --- |
| January - June | September 1 |
| July - December | March 1 |

All instances of deviations from permit requirements must be clearly identified in such reports.  All such reports shall be certified in accordance with Condition 9.9.

b.	If monitoring is not required this report is not required to be submitted.

8.6.2	Test Notifications

When testing is requested by Illinois EPA, a written test plan shall be submitted to the Illinois EPA for review at least 60 days prior to the testing pursuant to Section 39.5(7)(a) of the Act.  The notification shall include at a minimum:

a.	The name and identification of the affected unit(s);

b.	The person(s) who will be performing sampling and analysis and their experience with similar tests;

c.	The specific conditions under which testing will be performed, including a discussion of why these conditions will be representative of maximum emissions and the means by which the operating parameters for the source and any control equipment will be determined;

d.	The specific determination of emissions and operation which are intended to be made, including sampling and monitoring locations;

e.	The test method(s) which will be used, with the specific analysis method, if the method can be used with different analysis methods;

f.	Any minor changes in standard methodology proposed to accommodate the specific circumstances of testing, with justification; and

g.	Any proposed use of an alternative test method, with detailed justification.

8.6.3	Test Reports

Unless otherwise specified elsewhere in this permit, the results of any test required by this permit shall be submitted to the Illinois EPA within 60 days of completion of the testing.  The test report shall include at a minimum  [Section 39.5(7)(e)(i) of the Act]:

a.	The name and identification of the affected unit(s);

b.	The date and time of the sampling or measurements;

c.	The date any analyses were performed;

d.	The name of the company that performed the tests and/or analyses;

e.	The test and analytical methodologies used;

f.	The results of the tests including raw data, and/or analyses including sample calculations;

g.	The operating conditions at the time of the sampling or measurements; and

h.	The name of any relevant observers present including the testing company’s representatives, any Illinois EPA or USEPA representatives, and the representatives of the source.

8.6.4	Reporting Addresses

a.	The following addresses should be utilized for the submittal of reports, notifications, and renewals:

i.	Illinois EPA - Air Compliance Section

Illinois Environmental Protection Agency

Bureau of Air

Compliance Section (MC 40)

P.O. Box 19276

Springfield, Illinois  62794-9276

ii.	Illinois EPA - Air Regional Field Office

Illinois Environmental Protection Agency

Division of Air Pollution Control

Eisenhower Tower

1701 South First Avenue

Maywood, Illinois  60153

iii.	Illinois EPA - Air Permit Section (MC 11)

Illinois Environmental Protection Agency

Division of Air Pollution Control

Permit Section

P.O. Box 19506

Springfield, Illinois  62794-9506

iv.	USEPA Region 5 - Air Branch

USEPA (AR - 17J)

Air & Radiation Division

77 West Jackson Boulevard

Chicago, Illinois  60604

b.	Unless otherwise specified in the particular provision of this permit, reports shall be sent to the Illinois EPA - Air Compliance Section with a copy sent to the Illinois EPA - Air Regional Field Office.

8.7	Obligation to Comply with Title I Requirements

Any term, condition, or requirement identified in this permit by T1, T1R, or T1N is established or revised pursuant to 35 IAC Part 203 or 40 CFR 52.21 (“Title I provisions”) and incorporated into this permit pursuant to both Section 39.5 and Title I provisions.  Notwithstanding the expiration date on the first page of this permit, the Title I conditions remain in effect pursuant to Title I provisions until the Illinois EPA deletes or revises them in accordance with Title I procedures.

9.0	Standard Permit Conditions

9.1	Effect of Permit

9.1.1	The issuance of this permit does not release the Permittee from compliance with State and Federal regulations which are part of the Illinois State Implementation Plan, as well as with other applicable statutes and regulations of the United States or the State of Illinois or applicable ordinances, except as specifically stated in this permit and as allowed by law and rule  [Section 39.5(7)(j)(iv) of the Act].

9.1.2	In particular, this permit does not alter or affect the following:

a.	The provisions of Section 303 (emergency powers) of the CAA, including USEPA's authority under that Section;

b.	The liability of an owner or operator of a source for any violation of applicable requirements prior to or at the time of permit issuance;

c.	The applicable requirements of the acid rain program consistent with Section 408(a) of the CAA; and

d.	The ability of USEPA to obtain information from a source pursuant to Section 114 (inspections, monitoring, and entry) of the CAA.

9.1.3	Notwithstanding the conditions of this permit specifying compliance practices for applicable requirements, any person (including the Permittee) may also use other credible evidence to establish compliance or noncompliance with applicable requirements.

9.2	General Obligations of Permittee

9.2.1	Duty to Comply

The Permittee must comply with all terms and conditions of this permit.  Any permit noncompliance constitutes a violation of the CAA and the Act, and is grounds for any or all of the following:  enforcement action, permit termination, revocation and reissuance, modification, or denial of a permit renewal application  [Section 39.5(7)(o)(i) of the Act].

The Permittee shall meet applicable requirements that become effective during the permit term in a timely manner unless an alternate schedule for compliance with the applicable requirement is established.

9.2.2	Duty to Maintain Equipment

The Permittee shall maintain all equipment covered under this permit in such a manner that the performance or operation of such equipment shall not cause a violation of applicable requirements.

9.2.3	Duty to Cease Operation

No person shall cause, threaten or allow the continued operation of any emission unit during malfunction or breakdown of the emission unit or related air pollution control equipment if such operation would cause a violation of an applicable emission standard, regulatory requirement, ambient air quality standard or permit limitation unless such malfunction or breakdown is allowed by a permit condition  [Section 39.5(6)(c) of the Act].

9.2.4	Disposal Operations

The source shall be operated in such a manner that the disposal of air contaminants collected by the equipment operations, or activities shall not cause a violation of the Act or regulations promulgated thereunder.

9.2.5	Duty to Pay Fees

The Permittee must pay fees to the Illinois EPA consistent with the fee schedule approved pursuant to Section 39.5(18) of the Act, and submit any information relevant thereto  [Section 39.5(7)(o)(vi) of the Act].  The check should be payable to "Treasurer, State of Illinois" and sent to:  Fiscal Services Section, Illinois Environmental Protection Agency, P.O. Box 19276, Springfield, Illinois  62794-9276.

9.3	Obligation to Allow Illinois EPA Surveillance

Upon presentation of proper credentials and other documents, the Permittee shall allow the Illinois EPA, or an authorized representative to perform the following  [Section 39.5(7)(p)(ii) of the Act]:

a.	Enter upon the Permittee's premises where an actual or potential emission unit is located; where any regulated equipment, operation, or activity is located or where records must be kept under the conditions of this permit;

b.	Have access to and copy, at reasonable times, any records that must be kept under the conditions of this permit;

c.	Inspect during hours of operation any sources, equipment (including monitoring and air pollution control equipment), practices, or operations regulated or required under this permit;

d.	Sample or monitor any substances or parameters at any location:

i.	At reasonable times, for the purposes of assuring permit compliance; or

ii.	As otherwise authorized by the CAA, or the Act.

e.	Obtain and remove samples of any discharge or emission of pollutants; and

f.	Enter and utilize any photographic, recording, testing, monitoring, or other equipment for the purposes of preserving, testing, monitoring, or recording any activity, discharge or emission at the source.

9.4	Obligation to Comply With Other Requirements

The issuance of this permit does not release the Permittee from applicable State and Federal laws and regulations, and applicable local ordinances addressing subjects other than air pollution control.

9.5	Liability

9.5.1	Title

This permit shall not be considered as in any manner affecting the title of the premises upon which the permitted source is located.

9.5.2	Liability of Permittee

This permit does not release the Permittee from any liability for damage to person or property caused by or resulting from the construction, maintenance, or operation of the sources.

9.5.3	Structural Stability

This permit does not take into consideration or attest to the structural stability of any unit or part of the source.

9.5.4	Illinois EPA Liability

This permit in no manner implies or suggests that the Illinois EPA (or its officers, agents or employees) assumes any liability, directly or indirectly, for any loss due to damage, installation, maintenance, or operation of the source.

9.5.5	Property Rights

This permit does not convey any property rights of any sort, or any exclusive privilege  [Section 39.5(7)(o)(iv) of the Act].

9.6	Recordkeeping

9.6.1	Control Equipment Maintenance Records

A maintenance record shall be kept on the premises for each item of air pollution control equipment.  As a minimum, this record shall show the dates of performance and nature of preventative maintenance activities.

9.6.2	Records of Changes in Operation

A record shall be kept describing changes made at the source that result in emissions of a regulated air pollutant subject to an applicable requirement, but not otherwise regulated under this permit, and the emissions resulting from those changes  [Section 39.5(12)(b)(iv) of the Act].

9.6.3	Retention of Records

a.	Records of all monitoring data and support information shall be retained for a period of at least 5 years from the date of the monitoring sample, measurement, report, or application.  Support information includes all calibration and maintenance records, original strip-chart recordings for continuous monitoring instrumentation, and copies of all reports required by this permit  [Section 39.5(7)(e)(ii) of the Act].

b.	Other records required by this permit shall be retained for a period of at least 5 years from the date of entry unless a longer period is specified by a particular permit provision.

9.7	Annual Emissions Report

The Permittee shall submit an annual emissions report to the Illinois EPA, Compliance Section no later than May 1 of the following year, as required by 35 IAC Part 254.

9.8	Requirements for Compliance Certification

Pursuant to Section 39.5(7)(p)(v) of the Act, the Permittee shall submit compliance certifications annually or more frequently as specified in the applicable requirement or by permit condition.

a.	The certifications shall include descriptions of means to monitor the compliance of the source including emissions limitations, standards, and work practices in accordance with applicable requirements and permit conditions.  The certification shall include the identification of each term or condition of this permit that is the basis of the certification; the compliance status; whether compliance was continuous or intermittent; the method(s) used for determining the compliance status of the source, both currently and over the reporting period consistent with the conditions of this permit.

b.	All compliance certifications shall be submitted to USEPA Region 5 in Chicago as well as to the Illinois EPA.

c.	All compliance reports required to be submitted shall include a certification in accordance with Condition 9.9.

9.9	Certification

Any document (including reports) required to be submitted by this permit shall contain a certification by a responsible official of the Permittee that meets the requirements of Section 39.5(5) of the Act  [Section 39.5(7)(p)(i) of the Act].  An example Certification by a Responsible Official is included as an attachment to this permit.

9.10	Defense to Enforcement Actions

9.10.1	Need to Halt or Reduce Activity Not a Defense

It shall not be a defense for the Permittee in an enforcement action that it would have been necessary to halt or reduce the permitted activity in order to maintain compliance with the conditions of this permit  [Section 39.5(7)(o)(ii) of the Act].

9.10.2	Emergency Provision

a.	An emergency shall be an affirmative defense to an action brought for noncompliance with the technology-based emission limitations under this permit if the following conditions are met through properly signed, contemporaneous operating logs, or other relevant evidence:

i.	An emergency occurred as provided in Section 39.5(7)(k) of the Act and the Permittee can identify the cause(s) of the emergency.  Normally, an act of God such as lightning or flood is considered an emergency;

ii.	The permitted source was at the time being properly operated;

iii.	The Permittee submitted notice of the emergency to the Illinois EPA within two working days of the time when emission limitations were exceeded due to the emergency.  This notice must contain a detailed description of the emergency, any steps taken to mitigate emissions, and corrective actions taken; and

iv.	During the period of the emergency the Permittee took all reasonable steps to minimize levels of emissions that exceeded the emission limitations, standards, or regulations in this permit.

b.	This provision is in addition to any emergency or upset provision contained in any applicable requirement.  This provision does not relieve a Permittee of any reporting obligations under existing federal or state laws or regulations.

9.11	Permanent Shutdown

This permit only covers emission units and control equipment while physically present at the indicated source location(s).  Unless this permit specifically provides for equipment relocation, this permit is void for the operation or activity of any item of equipment on the date it is removed from the permitted location(s) or permanently shut down.  This permit expires if all equipment is removed from the permitted location(s), notwithstanding the expiration date specified on this permit.

9.12	Reopening and Reissuing Permit for Cause

9.12.1	Permit Actions

This permit may be modified, reopened, and reissued, for cause pursuant to Section 39.5(15) of the Act.  The filing of a request by the Permittee for a permit modification, revocation, and reissuance, or of a notification of planned changes or anticipated noncompliance does not stay any permit condition  [Section 39.5(7)(o)(iii) of the Act].

9.12.2	Reopening and Revision

This permit must be reopened and revised if any of the following occur  [Section 39.5(15)(a) of the Act]:

a.	Additional requirements become applicable to the equipment covered by this permit and three or more years remain before expiration of this permit;

b.	Additional requirements become applicable to an affected source for acid deposition under the acid rain program;

c.	The Illinois EPA or USEPA determines that this permit contains a material mistake or inaccurate statement when establishing the emission standards or limitations, or other terms or conditions of this permit; and

d.	The Illinois EPA or USEPA determines that this permit must be revised to ensure compliance with the applicable requirements of the Act.

9.12.3	Inaccurate Application

The Illinois EPA has issued this permit based upon the information submitted by the Permittee in the permit application.  Any misinformation, false statement or misrepresentation in the application shall be grounds for revocation under Section 39.5(15)(b) of the Act.

9.12.4	Duty to Provide Information

The Permittee shall furnish to the Illinois EPA, within a reasonable time specified by the Illinois EPA any information that the Illinois EPA may request in writing to determine whether cause exists for modifying, revoking and reissuing, or terminating this permit, or to determine compliance with this permit.  Upon request, the Permittee shall also furnish to the Illinois EPA copies of records required to be kept by this permit, or for information claimed to be confidential, the Permittee may furnish such records directly to USEPA along with a claim of confidentiality  [Section 39.5(7)(o)(v) of the Act].

9.13	Severability Clause

The provisions of this permit are severable, and should any one or more be determined to be illegal or unenforceable, the validity of the other provisions shall not be affected.  The rights and obligations of the Permittee shall be construed and enforced as if this permit did not contain the particular provisions held to be invalid and the applicable requirements underlying these provisions shall remain in force  [Section 39.5(7)(i) of the Act].

9.14	Permit Expiration and Renewal

The right to operate terminates on the expiration date unless the Permittee has submitted a timely and complete renewal application.  For a renewal to be timely it must be submitted no later than 9 and no sooner than 12 months prior to expiration.  The equipment may continue to operate during the renewal period until final action is taken by the Illinois EPA, in accordance with the original permit conditions  [Section 39.5(5)(l), (n), and (o) of the Act].

10.0	ATTACHMENTS

10.1	Attachment 1	Example Certification by a Responsible Official

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted.  Based on my inquiry of the person or persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete.  I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.

Signature:		______________________________________________

Name:			______________________________________________

Official Title:	______________________________________________

Telephone No.:	______________________________________________

Date Signed:		______________________________________________

DWH:psj