Modeled Snow Cover Product (Snow Water Equivalent) 

Posted snow water equivalent (SWE) graphs are the product of a spatially distributed snowmelt model forced with a remotely sensed and assimilated meteorological data as weather data input. The model is based upon the Utah Energy Balance (UEB) snowmelt model developed by Tarboton (Tarboton, 1994; Tarboton et al., 1995). The UEB model is very parsimonious with only three state variables. The model uses a lumped representation of the snowpack with two primary state variables, namely, water equivalence (or total amount of water, expressed in depth, in the snowpack), and energy content relative to a reference state of water in the ice phase at 0 oC. This version of the model runs in a spatially distributed mode using a grid resolution of 10 km. 

The energy content is used to determine average snowpack temperature, and/or fraction of the snowpack that is in liquid form. Age of the snow surface is retained as a third state variable, used for the calculation of albedo (or reflectance properties of the surface). The model is driven by inputs of air temperature, precipitation, wind speed, humidity, and radiation at a 6-hourly time step, a time step that is sufficient to resolve the diurnal cycle. The model uses physically-based calculations of the radiative, sensible, latent and advective heat exchanges (i.e., exchanges, or fluxes, of energy due to incoming and outgoing short- and long-wave radiation, thermal or heat conduction, evaporation and condensation, and horizontal heat transport). An equilibrium parameterization of snow surface temperature accounts for differences between snow surface temperature and average snowpack temperature, without having to introduce additional state variables. Melt outflow is a function of the liquid fraction, and is parameterized according to Darcy's law; this parameterization allows the model to account for continued outflow even when the energy balance is negative. 

The daily rainfall input grids are the satellite rainfall estimates (RFE) provided by NOAA/CPC (Climate Prediction Center) (Xie et al., 1997). The RFE is calculated on a 0.1-degree latitude/longitude grid. The remaining input variables required by the model (solar radiation, air temperature, wind, humidity, and atmospheric pressure) are estimated from downscaled output fields from NOAA's Global Data Assimilation System (GDAS) and the Air Force Weather Agency's MM5 (Mesoscale Model, version 5) weather forecast model. 

The (daily) snow water equivalent maps show the spatial distribution of the modeled water content of the snowpack. As such, the maps also portray the spatial distribution of snow cover extent, and provide an indication of relative snow depth and water available for irrigation when the snow melts. 

Three years means were calculated for each day of the year based on data from the years 2005 to 2008. Anomaly maps are produced to display the absolute difference from the mean and the percent difference from the mean for each day. 

Tarboton, D. G., T. G. Chowdhury and T. H. Jackson, (1995), "A Spatially Distributed Energy Balance Snowmelt Model", in Biogeochemistry of Seasonally Snow-Covered Catchments, ed. K. A. Tonnessen et al., Proceedings of a Boulder Symposium, July 3-14, IAHS Publ. no. 228, p.141-155. 

Tarboton, D. G., (1994), "Measurement and Modeling of Snow Energy Balance and Sublimation From Snow", in Proceedings, International Snow Science Workshop, Snowbird, Utah, October 31 to November 2, Utah Water Research Laboratory working paper no. WP-94-HWR-DGT/002. 

Xie, P. and P.A. Arkin, (1997), "A 17-year monthly analysis based on gauge observations, satellite estimates, and numerical model outputs", Bulletin of the American Meteorological Society 78(11): 2539-58.