LNA/Limiter 1st First Article Test Procedures

The purpose of the 1st article of 3 units is to ensure that the design of the LNA/Limiter assembly is within the specifications denoted in the solicitation package.  This particular test will consist of a static bench test of the 1st article units.

A network analyzer, Agilent model 8753ES and power supply will be used to power up and measure the following parameters:  input and output VSWR, gain, phase flatness, 1db compression point, voltage margin test for the supplied power (20V +/- some margin), etc.

A noise figure meter, HP model 8970B and noise source, HP model 346A will be used to measure the noise figure.

A LeCroy model Wavepro 7300A will be used to measure ON/OFF times.

The units will also be subjected to a temperature fluctuation to determine any gain loss or phase shift.

All tests will be performed with government test equipment and procedures.  Government test equipment, procedures, and measured data will take precedence over contractor’s test equipment, procedures and measured data.