Guidelines for locking 433/434 truck lock door

- When a temperature sensitive experiment is in operation in 12IDD, the BP will notify the FC that the roll up door will require an administrative LOTO.

- FC retrieves the LOTO covers, ANL FD locks, and signs from the 434 FC office (two covers, two locks & two signs above the printer).

- Attach the LOTO covers to their other halves, which are mounted behind the inner roll up door controls inside and outside.

- Apply the ANL FD locks to the LOTO devices on the inside and outside of the inner roll up door. Attach the sign that directs people to call the FC for access. Fill in the appropriate start/stop dates on the sign.

- Notify Bob Whitman and the ANL Fire Department that the truck lock door has an administrative LOTO and the duration of the LOTO.

The electrical disconnect for the roll up door is mounted on the column above the inside control (on the EHF), about 15’ above the floor. LOTO is not required on this disconnect.

The FD emergency override switch is located adjacent to the outer controls (inside the truck lock) and is labeled as such. This always has a gang lock and FD lock on it; unless in use by the ANL FD. Do not remove this lock.