ULS Public Access Release Notice

Effective Date:	May 6, 2001

Description:

The format of the ULS public access files is being modified to incorporate changes to support the Maritime Coast and Aviation Ground Radio Services [Parts 80 and 87]; the Commercial Radio, Restricted Radiotelephone, and Restricted Radiotelephone-Limited Use Radio Services [Part 13]; and the Tribal Lands Information in ULS.

The changes are:

- Addition of record type CG.
CG is a new record type that is used for Maritime Coast & Aviation Ground data.  It corresponds to the Form 601 Schedule G Maritime & Aviation Services information.  This record type is used for both applications and licenses.

- Addition of record type FA.
FA is a new record type that is used for the Commercial Radio, Restricted Radiotelephone, and Restricted Radiotelephone-Limited Use Radio Services data.  It corresponds to the Form 605 Schedule E information.  This record type is used for both applications and licenses.

- Addition of record type IA.
IA is a new record type that is used for international addresses for the Restricted Radiotelephone radio services.  This record type is used for both applications and licenses.

- Addition of record type TL.
TL is a new record type that is used for Tribal Lands Information data.  It corresponds to the Form 601 Schedule B for Geographically Licensed Services.  This record type is used for both applications and licenses.

- Addition of record type RZ.
RZ is a new record type that is used to provide the Receive Zone data for the Maritime Coast & Aviation Ground Radio Services.  The RZ record type was created so multiple receive zones can be provided.  This record type is used for both applications and licenses.

- Addition of record type FT.
FT is a new record type that is used to provide the Frequency Type data for the Aviation Ground Radio Service.  The FT record type was created so multiple frequency types can be provided.  This record type is used for both applications and licenses.

- Addition of five fields to the end of the MK record type.

Positions 14, 15, 16, 17 and 18 for the Tribal Credit Indicator, the Tribal Credit Calculation, the Additional Tribal Credit Requested, the Tribal Credit Awarded and the Additional Tribal Credit Awarded has been added to accommodate Form 601 Schedule B Tribal Lands Information section [boxes 6 through 12].

- Addition of one field to the end of the AN record type.

Position 34 for Line Loss has been added to accommodate Form 601 Schedule G box 16 [Transmission Line Loss].

- Addition of one field to the end of the EM record type.

Position 13 for Frequency Number has been added to clarify for which frequency the requested emission action is for.

- Modify position 13 of the MK record type.  
The Definition of Position 13 [Population] of the MK record type has been changed from numeric(18,0) to numeric(9,0) to agree with the database.

- Modify position 37 of the LO record type.  
The Definition of Position 37 [Quiet Zone Notification Date] of the LO record type has been changed from mm/yyyy to mm/dd/yyyy to agree with the database.

- Modify position 15 of the AN record type.  
The Definition of Position 15 [Tilt] of the AN record type has been changed from numeric(2,0) to numeric(3,1) to agree with the database.

- Modify position 16 of the FR record type.  
The Definition of Position 16 [Power Output] of the FR record type has been changed from numeric(7,3) to numeric(15,3) to agree with the database.

- Modify position 17 of the FR record type.  
The Definition of Position 17 [Power ERP] of the FR record type has been changed from numeric(7,3) to numeric(15,3) to agree with the database.

- Modify position 11 of the EM record type.  
The Definition of Position 11 [Digital Mod Rate] of the EM record type has been changed from numeric(8,4) to numeric(8,1) to agree with the database.