Pavement Smoothness Initiative

Update July 2001

In the area of Pavement Smoothness FHWA’s Office of  Pavement Technology (HIPT) and Office of Asset Management (HIAM) undertook a joint initiative to enhance pavement smoothness on the NHS.  This initiative was developed in response to the results of the 1996 NQI Highway Users Survey and the FHWA Performance Plan.  The performance goal is to increase the NHS mileage rated at 170 inches/mile for International Roughness Index (IRI) as reported for HPMS from 91.7% in 1998 to greater than 93% in 2008.

HPMS data collected in 1999 and released in late 2000 indicates we have achieved this goal.  Subsequently, a revised 2008 goal, effective 2002 is for 95% of travel will occur on NHS facilities with IRI of 170”/mile or less.  Additionally a parallel goal to improve the “good” pavements to 60% of travel on NHS facilities with IRI of 95”/mile or less.

To achieve the Strategic Goal of  >95% of travel on NHS less than 170"/mile by 2008, States need a program that contains four things:

- Programming process that identifies construction projects that will address smoothness on a network basis in terms of location and strategy selection.

- Method for specifying smoothness.

- Method for measuring smoothness on new construction that is objective and reliable

- Tools for contractors to achieve the smoothness targets specified.

To accomplish these tasks the Smoothness Initiative has activities that address these four critical areas.

- Showcasing a management approach to pavement smoothness

- Development of a guide specification for pavement smoothness measurement based upon lightweight profilers.

- Demonstration of lightweight profilers for smoothness measurement after construction.  Includes specifying smoothness goals in terms of IRI

- Development of “Best Practice” videos for both HMA and PCC pavement construction

Through 7/2001, activities under the auspices of the Pavement Smoothness Initiative included:

- Completion of 8 demonstration projects for lightweight, non-contact profilers which involved 9 states.  All field evaluations are complete.  A paper summarizing the reports received has been prepared.

- Development of a “Best Practice” video for PCC pavement with Kansas DOT.  John Madden is the celebrity endorser.   Kit is complete and duplicated. Initial distribution is complete.

- Distribution of “Best Practice” video for HMA pavement developed by Arizona DOT and the WRC.  Two thousand five hundred copies have been distributed in FY 1999 and 2000.

- Development of a laminated card highlighting Georgia DOT’s approach to management of their pavement system that achieves one of the smoothest inventories in the country.

- Development of a draft guide specification for pavement smoothness.  Preliminary smoothness targets recommended by HIPT.

- Development of a display booth highlighting the FHWA Smoothness Initiative

- Contract to develop a Pavement Profile Viewer has been awarded to Transtec Group, Austin, TX.  The Pavement Profile Viewer will allows users to view, edit and analyze pavement profile data from a number of different vendors.  Product is anticipated to be available in March 2002.

- Ryan Rizzo, MI Division, has completed a survey of current state practices for smoothness specs.  The survey was released in November 2000.

- NHI Training Course is under development by BRE-Fugro, of Austin, TX.  Course NHI 131065 Pavement Smoothness:  Factors Affecting Inertial Profiler Measurements Used for Construction QC”.

- Pavement Smoothness Strategies: a solicitation is currently pending for MIHE to work with a state to help make improvements in network smoothness.

- Development of pavement smoothness best practices documents.  These documents will complement the videos on HMA and PCC construction.  Deliverables expected by August 31, 2001.

Activities conducted by others relating to the Pavement Smoothness Initiative include:

- The Innovative Pavement Research Foundation (IPRF) is developing a RFP for a project to look at Smoothness Criteria for PCC Pavements (Task 16).   An RFP has been developed.

- NCHRP 20-51(1) LTPP Product Development: National Workshop on Pavement Smoothness, scheduled for August 26-28, 2001 in Irvine, CA.

- NCHRP 20-50(08/13) LTPP Data Analysis: Factors Affecting Pavement Smoothness.  The objectives are to determine the factors that cause changes in pavement smoothness and to quantify the factors.

- RD&T  (Peter Kopac) has a project out for solicitation to evaluate the impact of smoothness specs on PCC construction.  Anticipate award by August, 2001.

- Maryland SHA is currently developing a procedure to calibrate/validate/verify inertial profilers using a shaking table rather than a test pavement.  A pooled fund project may be developed.

- Budget Update:  The following balances are available.  $60,000 of STR and $15,000 of TAD for development of technical materials.  $30,000 in TAD for deployment of smoothness initiative.

Smoothness Specifications Update:  States currently revising their smoothness specifications are SC, NJ, MD, SD, ND, VA, PA, TX, IN, AR, WV, and Alaska.  The Port Authority of NY and NJ (creating) and the province of Newfoundland and Labrador, Canada are also revising their specifications.

To Do List:

Lightweight Profiler Demo:

Obtain evaluation reports from participating states ( MN, AR, AZ) (Law)

Incorporate results into presentations  (Law)

Presentations on Lightweight profiler Demo (Law)

Development of NHI training courses:

Pavement Smoothness: Developing Smoothness Specification using Inertial Profilers for Construction Quality Control (Swanlund, Newman)

AASHTO Guide Spec:

Refinement of  Draft Guide Spec (Law/ETG)

Presentations on Guide Spec (Law)

Development of QC/QA procedure (Law)

Certification and  Calibration process/method (Law)

PCC Best Practices:

Distribution of PCC Smoothness Kit  (distribution conducted: Swanlund)

Presentations on PCC Best practices (Swanlund)

HMA Best Practices:

Distribution of HMA Video, 500 copies available (Swanlund)

Presentations on HMA Best Practices (Swanlund)

Georgia Management Practices:

Distribution of Georgia Management Card and Technical Report (Rodriguez)

Presentations on GA Management Practices (Rodriguez)

Overall:

Develop Smoothness Strategic Plan (Swanlund)

Develop Comprehensive Marketing Plan (Bergeron)

Provide Direction/Priorities for program (ETG)

Presentation of Overview (Swanlund)

Possible new activities:

Incorporation of module on strategy selection for smoothness

FHWA Pavement Smoothness Team

Mark Swanlund, Office of Pavement Technology (Co-manager)

David Law, SC Division (Co-manager)

Mike Voth, CFLHD

Kathleen Bergeron, WRC

Luis Rodriguez, SRC

Keith Herbold, MRC

Joe Huerta, ERC

Jim Walls, ERC

Mark Zitzka, MT Division

Ryan Rizzo, MI Divsion

Byron Lord, Office of Pavement Technology