POLAR Spacecraft Status As of: Tues 14 Aug 07, 12:00 EST

(Changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:59=AN STIP data only No IPD processing | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO |
| ADACS | Nominal Mode Autonomous swap to YGC 30 Aug 06, commanded back to nominal 31 Aug RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB Pitch wheel bias 2400 *Z gas unload = 145 Gyro2 safe macro | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB GAS Enabled Dec 05 *Z Gas unload =45 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Z-momentum transition complete Pitch Torquer again active |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 2 (since 4/3/03) 3 channels inop | 2 since 4/18/05 (analog drifting?) | 2 Swapped 9/20/06 | 1 Analog telem drifting |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B 4b low pressure | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 4A Pressure leak | SSRs 1,2,3,4,5 Safestate=5B Current spikes |
| VTX (APT data) | #1 ON 137.50 MHZ | #1 ON As of 19 June 07 | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 2-Omni HRPT 2 Omni=rcp Power TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 off INOP-10 Aug 2007 3 low power INOP -10 Aug 2007 | 3 – HRPT TOAR424 low power 2 & 1 Playback STX-1 Power drop STX-4 no modulation | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, eclipse states and sun angle) | ArrayOff +90 since 8/8/07 Full Sun Sun Angle 16 uptrend to 20 in early Jan 07 Shunts severely degraded SA CANT=37 degs PSSS trigger =18.5 BVR & PSE to Back-up 8/7/07 | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Uptrend to 18 early Jan 07 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 34 Steady trend SA CANT=22 degs Transitioning to full sun S/C in Sept 07 BVR Phase Control auton swap 7/19/07 | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 66 Steady trend SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 63 uptrend to 65 on 1 Jan 07 SA CANT=22 BVR Phase Control auton swap 3/29/06 & 1/4/07 |
| AVHRR | Nominal HRPT and APT data only | Nominal Channel 3B only Occasional minor scan motor instabilities | Nominal Recent SM current increases TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Previous scan motor current mini surges | Nominal Channel 3B only Scan motor current drop 29 Aug 06 |
| AMSU-A1 |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| `AMSU-A2 |  | Nominal | Nominal | Nominal | Nominal |
| AMSU-B |  | Operational Bias in All Chans. Degraded Chan-3 | Operational Space Position-3 Chan-8 degradation | Nominal | Replaced by MHS |
| HIRS | ON/Inop Turned On 4/30/05 for power balance Filter Wheel OFF Outgas & Filter Wheel Htrs On 8/6/07, Pwr Bal | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | NOMINAL New all time high filter motor current reached 9/17/06. Imagery occasionally exhibits high levels of radiometric noise | NOMINAL 1 Pixel cross-track misalignment. | Operational Filter Heat OFF. LW channel 1-12 noise TOAR 448 Loose LWIR lens. LW imagery erratic. |
| MHS/MIU |  |  |  |  | Nominal Fly Wheel Motor Current Spiking but not alarming since 27 Dec 06 Entered Motor Spin State on 27 March 07 |
| MSU | ON/Inop Turn on 7/9/07 for power balance |  |  |  |  |
| SSU |  |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR |  | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | ON/Nominal Autonomous reset 8 Jun 06, back to nominal 10 June Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 0615:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 06 16:00z | Nominal Elec-CH-HVPS=1 27 June 06 17:00z Prot-CH-HVPS=0 |
| SBUV |  |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops TOAR 463 sun glint IBSL test performed 12 Sept 06 Grating motor investigation | Nominal Anode mode since 6 July 05 13:30z Electronics turnoff taken out of STESM safestate table TOAR 462 sun glint |
| SADPOS |  |  | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | TCE26 & 15H Telem valid TOAR 432 closed TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active HIRS filter heater turned OFF 9/28/06 |

COMMENTS/CHANGES:

MISC:	 Planning for a partial solar eclipse on 11 Sep 2007 is being planned.

NOAA-12:	After spending many days attempting to power balance NOAA-12, it was decided to decommission the spacecraft.  It was decommissioned on 10 August 2007 at 17:18:38z

There were relatively no changes to the rest of the NOAA-12 health situation during the past week.  MSU power balance appears to continue to hold stable at the motor's turn on temperature of 70 C.

NOAA-12’s power	balance situation continued to degrade significantly.  There were been numerous SAD Bias responses to the Filtered Bus Voltage exceeding 28.5V.  Once the SA was moved to +90 º, for part of the orbit the bus was stealing the charge current from the batteries.  The discharge rate was 0 but the charge rate was not at its nominal levels of 1.7 or .75 amps.  This led us to believe that we could not achieve a power neutral situation during a full sun orbit. (See Figure 1)

During the depletion of the fuel it was noted that the N2 low pressure (the regulator pressure) was decreasing where it should have bounced back to 500psi after the thruster firings to close the regulator until the high pressure was equal to 500psi (see Figure 2).   Also noted as more fuel was the attitude response was weakening.  After discussions with NASA/GSFC personnel and EMOSS investigating the OV report for NOAA-12, it was discovered that at handover to NOAA the N2 high pressure in the tank was ~900psi. This high pressure was now reading ~2800psi.  The high pressure transducer did have a problem quickly after launch where its reading went to 0 for ~20 min and then returned to a nominal value.  When EMOSS investigated the pressure reading, it was noticed that it was rising slowly for the past 10 years or so.  Therefore there was not as much N2 fuel left then believed, thus the regulator pressure dropping was indicative of the amount of pressure left in the tank.  We actually were below the blow-down threshold.  After this discovery we proceeded with the deactivation.

A change to this deactivation from NOAA-14’s was the addition of firing only the N2 thruster for 25.5 seconds and opening all thruster valves (including hydrazine) to deplete all possible fuel.  Very little attitude disturbance was noted, thus proving as much of the fuel as possible was depleted.

For Battery Information see Figure 2, note that since the Solar Array offset of +95º, NOAA-12 has been going power negative every orbit.

Below is the list of actions taken:

8 August 2007

- 16:20z

  - Slewed the Solar Array to a +95º offset from +90º.

- 19:40z

  - Thrusters were fired (4 yaw/roll thrusters) for 1 second to test the depletion of the fuel

10 August 2007

- 15:30z

  - Thrusters were fired (4 yaw/roll thrusters) for 5 second to test the depletion of the fuel; this was done numerous times during the pass.

- 17:40z

  - NOAA-12 was decommissioned

NOAA-15:	There were relatively no changes to the NOAA-15 payload health situation during the past week.  N-15 has come out of summer eclipse season.  EPS in nominal

The Z RWA has completed its migration to negative RPM. No impact on operations. The #2 gyro is still unstable since about July 24th. This has affected yaw control (yaw updates as high as 0.7 degrees). The trend is not evident in gyro motor current or thermal data.

NOAA-16: 	There was relatively no change in the performance of the NOAA-16 payload subsystems during the past week and the rest of the spacecraft subsystems were also nominal during this time.

On 10 August 2007 at 08:01z, the AET was not able to achieve bit sync or frame sync lock on STX-4.  The CDA noticed that there was an RF carrier with no modulation; very similar to the NOAA-17 STX-4 anomaly.  STX-4 is currently unusable.  The schedules were updated to use STX-3 which is known to have a lower output power of ~1 watt but thought to be usable.  After 2 uses of STX-3, it became too noisy to retrieve the data.  It is also considered unusable at this time.  The schedules were again updated to reflect the 2 unusable STXs.

A request from NASA has been made to move the SA from -40 to -35 so the shunts are always on to possibly avoid the spikes on the recorders.  An evaluation and a date for move is TBD.  NOAA-16 will be in full sunlight beginning in mid-September.  This is the first time ever it will not be eclipsing.

NOAA-17: 	There was relatively no change in the performance of the NOAA-17 payload subsystems during the past week. The HIRS filter wheel period noise calmed down this week.

No updates or conclusion were reached about the Attitude disturbance on 17 July 2007.  The investigation continues.

NOAA-18:	There were relatively no changes to the NOAA-18 health situation during the past week.

On 13 August 2007 at 05:11z the following mnemonics flagged and have remained out of limits:  MSPH4VAL (YL), MSPH3VAL (YL),  MSPDCOFV (YL),  MSPDCOFE (YH),  MHKDCOFE (YH),  QSPPRFLT (YH).  These are indications that the DC offsets for channels H3 and H4 have moved out of the optimum range.  The instrument data is degraded, but there is no health and safety risk.

The VTX will be switched from side 2 to 1 on 16 Aug 2007 at 14:43.

MetOp A:	No significant changes reported on the NOAA instruments on MetOp.  The HRPT transmitter failure investigation continues.

Trend Observations (NOAA Instruments)

·         AMSU-A1 Dig A temperatures dropped steadily by approximately 0.5 deg C over the course of the week.  This trend has also been observed over the past month, where the average drop in temperature has been approximately 1 deg C.  AMSU-A2 temperatures have remained stable during the same period.

·         With one exception (refer to AR8360, described below under “Anomalies”), all other housekeeping telemetry and science data were stable during this reporting period.

·         EUMETSAT confirmed an error in their NEdN calculation method for the CVF HIRS Daily Report.  This was corrected on August 8 and now the NEdN values are very stable.

·         HIRS Filter Wheel resyncs have remained at the same approximate rate as reported last week (approximately once every 93 seconds).

Anomalies

·         AR8360, “HIRS Scan Mirror Temperature Out-of-Limits”:  Anomalous temperature telemetry was observed between August 6-8, but has returned to nominal since then.  There was also a correlation observed between jumps in the Scan Mirror Temperature telemetry and slight drops in the Patch Power.  This is currently under investigation by ITT.

·         Investigations continued on trying to isolate the cause of the HRPT SSPA failure.

Operations Performed

·         The SEM IFCs were run on Tuesday, August 7, with the TED IFC starting at 08:53:03 UTC and the MEPED IFC starting at 08:54:23 UTC.

Operations Planned

·         The SEM IFCs will be run again on their weekly schedule (Tuesday, Aug 14).

NOTES: Figures 3 – 5 have been omitted for web listing.

Figure 1 NOAA-12 EPS (2007/218-221)

Figure 2 NOAA-12 RCE (2007/217-223) 30-226)

Figure 6 NOAA-16 STX-3 Output Power (2007/222-223)

Figure 7 NOAA-16 STX-3 Temperature (2007/222-223)

Figure 8 NOAA-16 STX-4 Output Power (2007/218-222)

Figure 9 NOAA-16 STX-4 Temperature (2007/218-222)