Customer No/Issue

SH-SAG-NT-TP007

Document No

P-SHM-NOT-0007-SE

| Date | Issue | Page |
| --- | --- | --- |
| 11 Jun 1999 | 1 | 1/17 |

PROJECT

SOHO

TITLE

COBS Gyroless Functions – Software User's Manual

|  | Name | Function | Date | Signature |
| --- | --- | --- | --- | --- |

| Prepared : | B Enoksson | SW Design |  |  |
| --- | --- | --- | --- | --- |

| Checked : | S Lernvall | SW Design |  |  |
| --- | --- | --- | --- | --- |

| Authorised : | L Börjesson | Project Manager |  |  |
| --- | --- | --- | --- | --- |

Distribution

| Complete : | DP-BE DP-SL DV-PL MMS |
| --- | --- |
| Summary : | DLL |

| Class : | CUSTOMER | Host System : | Microsoft Word 97 for Windows, SE Macro Rev 3.0 |
| --- | --- | --- | --- |
| Contract No : |  | Host File : | P-SHM-NOT-0007_01.doc |

SUMMARY

This manual describes how to install and operate the COBS Gyroless Functions patch. It is intended to serve as a supplement to the COBS Software User’s Manual, describing changes and addenda to it as a consequence of installing the patch.

# DOCUMENT CHANGE RECORD

Changes between issues are marked with a left-bar.

| Issue | Date | Paragraphs affected | Change information |
| --- | --- | --- | --- |

| 1 | 11 Jun 1999 | All | New document containing a preliminary TC/TM interface. |
| --- | --- | --- | --- |

TABLE OF CONTENTS	PAGE

1.	INTRODUCTION	4

1.1	Notation	4

2.	DOCUMENTS	4

2.1	Applicable	4

2.2	Referenced	4

3.	COBS GYROLESS FUNCTIONS OVERVIEW	5

3.1	Description	5

3.2	User Interface	5

4.	INSTALLATION PROCEDURE	6

4.1	Relation to Other Patches	6

4.2	Procedure	6

5.	TELECOMMANDS	7

5.1	Changes/Addenda to Existent TCM’s	7

5.1.1	Software Mode Change (KNK01000)	7

5.1.2	Select PROM/RAM Mode (KNK02000)	7

5.1.3	Authorize/Inhibit Function (KNK0A000)	8

5.1.4	Define Functions Authorize/Inhibit Status at Warm Start-Up (KNK0B000)	9

5.1.5	Define Execution Profile of Process (KNK0C000)	10

5.1.6	Reset Corrective Action Status (KNK24000)	10

5.1.7	Trigger Corrective Action for Gyro Monitoring (KNK51000)	10

5.2	Load Memory Interface	11

5.2.1	General	11

5.2.2	Initialize Gyroless Functions	12

5.2.3	Enable/Disable Corrective Action for Gyroless Functions	12

5.2.4	Define Parameters for Gyroless Functions	13

6.	TELEMETRY	14

6.1	Changes/Addenda to Permanent Part	14

6.1.1	Function Authorization Status (§0, offset 17..18)	14

6.1.2	Corrective Action Enable/Disable Status (§0, offset 101..103)	15

6.1.3	Corrective Action Triggered Status (§0, offset 104..106)	15

6.2	Changes/Addenda to Programmable Part, Group 1	15

6.2.1	Functions Warm Start-Up Table (§1, offset 1..2)	15

6.2.2	Process Execution Profiles (§1, offset 3..18)	15

6.3	Dump Memory Interface	16

7.	ANOMALIES	17

# INTRODUCTION

This manual describes how to install and operate the COBS Gyroless Functions patch. It is intended to serve as a supplement to the COBS Software User’s Manual [COBSUM], describing changes and addenda to it as a consequence of installing the patch.

The purpose and definition of the patch can be found in [GLSPEC].

Note:		The present issue contains a preliminary TC/TM interface.

## Notation

See [COBSUM].

# DOCUMENTS

The valid document issue numbers are defined in [GLTNOT].

## Applicable

[GLSPEC]	SOHO Gyroless – COBS Functions Definition
SH-MAT-NT-37922

[COBSRD]	Software Requirements Document for SOHO COBS
SH-SAG-SD-2A-00 (SHM/SPC/0014/SE)

## Referenced

[COBSUM]	Software User’s Manual for the SOHO CDMU COBS v14
SH-SAG-NT-T0181 (SHM/TNT/0181/SE)

[COBS14]	Software Configuration Item Data List for COBS v14
SH-SAG-CS-2A-00 (SHM/MLS/0004/SE)

[GLTNOT]	COBS Gyroless Functions – Technical Note
SH-SAG-NT-TP006  (P-SHM-NOT-0006-SE)

# COBS GYROLESS FUNCTIONS OVERVIEW

## Description

The COBS Gyroless Functions patch performs the following changes to COBS:

- The existent function Thruster Monitoring runs in all AOCS modes.

- The existent function ESR Monitoring inhibits the five new Gyroless functions when triggered.

- The existent functions ESR Gyro Setting, Trouble-Shooting Function (“free process”), Gyro Monitoring, ISA and SAD Function and RAAD Monitoring are disconnected from the COBS scheduler. The possibility to trigger CA for Gyro Monitoring by TCM is also removed.

- A new function ACU Reset Monitoring initiates ESR when ACU reset is detected.

- A new function Hx Flag Monitoring initiates ESR when AOCS indicates that the wheels X-axis momentum exceeds expected limits.

- A new function CRP Flag Monitoring aborts any on-going thruster actuation and commands transition to CRP mode when AOCS indicates CRP flag (in NM or RMW mode).

- A new function RW Speed Monitoring aborts any on-going thruster actuation and commands transition to CRP mode when a RW speed exceeds expected limits.

- A new function Experiments Off-Pointing Warning Message sends off-pointing warning messages to the UVCS, LASCO, MDI and SUMER experiments when AOCS indicates unexpected off-pointing.

Refer to [GLSPEC] for a more detailed description.

## User Interface

The Gyroless functions are assigned five new function id’s (Table 2) but reuse the five processes released by the disconnected old functions (Table 4). In addition, four new corrective actions (Table 9) and five new anomalies (section 7) are introduced.

The general TC/TM interface towards application functions [COBSUM 4.9.1 & 2] applies to the Gyroless functions as well. Changes or notes that arise from the introduction of the Gyroless functions are identified in sections 5.1, 6.1, 6.2 and 7.

Commands or parameters specific to the Gyroless functions are accessed through memory load and dump commands as described in sections 5.2 and 6.3.

# INSTALLATION PROCEDURE

## Relation to Other Patches

The COBS Gyroless Functions patch is valid for COBS version 14 only [COBS14]. The coexistence with previously delivered COBS patches is restricted according to the following table:

| Other patch | Can coexist with Gyroless | Interference |
| --- | --- | --- |
| ACU Monitoring Function | No | Gyroless patch does not allow TSM to execute |
| Virgo LOI Cover Open Function | No | Gyroless patch does not allow TSM to execute |
| DMA Patch | Yes | - |
| TM Subformat 6, 2&3, 3B | Yes | - |
| Thruster Monitoring Patch | Partly, but not meaningful | Last loaded patch determines whether the Thruster Monitoring function shall be active during ISA mode. |

Table 1 – Coexistence with other COBS patches

Note that trouble-shooting modules (TSM) cannot be executed while the Gyroless patch is installed. This is because the Gyroless patch takes the “free process” for one of its own functions, disconnecting the Trouble-Shooting Function from the COBS scheduler.

## Procedure

TBD

# TELECOMMANDS

## Changes/Addenda to Existent TCM’s

### Software Mode Change (KNK01000)

Note:

- Entering BOOTSTRAP mode will load the original COBS from PROM, discarding the Gyroless functions patch.

- Entering INITIALIZATION mode will not affect the Gyroless functions patch, but the Gyroless functions are not re-initialized. To ensure proper initialization when this TCM is used, it is recommended to also perform steps 1 and 3 below:

- Inhibit Gyroless functions at warm start-up, see 5.1.4.

- Enter INITIALIZATION mode, taking any else associated measures.

- Initialize the Gyroless functions, see 5.2.2.

- During transition to TM/TC or NOMINAL mode, the Gyroless Functions Installed indication flag (reported in Function Authorization Status, §0, see 6.1.1) may temporarily read zero.

### Select PROM/RAM Mode (KNK02000)

Note:

- It is not recommended to switch to PROM mode as the Gyroless patch is effective only in RAM mode. PROM mode will execute the original COBS.

### Authorize/Inhibit Function (KNK0A000)

The Function Id parameter is interpreted according to the following table. Changes compared to original COBS are shown in boldface.

| Id | Mnemonic | Function |
| --- | --- | --- |
| 0 | HGA_Stat | HGA-APME Station Keeping Function |
| 1 | ESRW | ESR Warning Flag |
| 2 | No function | - |
| 3 | ESR_Mon | ESR Detection Function |
| 4 | ExpMon | Experiment Monitoring |
| 5 | No function | - |
| 6 | No function | - |
| 7 | HGA_Mon | HGA-APME Monitoring Function |
| 8 | HGA_Nom | HGA-APME Nominal Control Function |
| 9 | IIDE | Inter-Instrument Data Exchange |
| 10 | No function | - |
| 11 | MinMaxMon | Min/max Recording Function |
| 12 | No function | - |
| 13 | StartUpDld | Start-Up Function |
| 14 | StdMon | Standard Monitoring |
| 15 | SubHeatMon | Substitution Heater Monitoring |
| 16 | TC_WD | Telecommand Watchdog Function |
| 17 | TR_ThmCtrl | Mode 3 Thermal Control |
| 18 | TR_ThmMon | Mode 3 Thermal Monitoring |
| 19 | ThmCtrl | Thermal Control |
| 20 | ThmMon | Thermal Monitoring |
| 21 | ThrusterMon | Thruster Monitoring |
| 22 | ACU_ResetMon | ACU Reset Monitoring |
| 23 | CRP_FlagMon | CRP Flag Monitoring |
| 24 | RW_SpeedMon | RW Speed Monitoring |
| 25 | HxFlagMon | Hx Flag Monitoring |
| 26 | ExpOffPointing | Experiment Off-pointing Warning Message |
| 100 | DP | Daily Pulse Distribution |
| 101 | MemScr | Memory Scrubbing |
| 102 | USO_Mon | USO Monitoring |

Table 2 - Function Id

Note:

- The unused function id’s 2, 5, 6, 10 and 12 are still allowed, but concern no function. They should be inhibited to avoid confusion.

### Define Functions Authorize/Inhibit Status at Warm Start-Up (KNK0B000)

The bit-map of the Function Status parameter is shown in the following table. Changes compared to original COBS are shown in boldface.

| Bit | Mnemonic | Function |
| --- | --- | --- |
| 0 | HGA_Stat | HGA-APME Station Keeping Function |
| 1 | ESRW | ESR Warning Flag |
| 2 | ESR_GyroSet | ESR Gyro Setting {1} |
| 3 | ESR_Mon | ESR Detection Function |
| 4 | ExpMon | Experiment Monitoring |
| 5 | FreeProcess | Trouble-Shooting Function {1} |
| 6 | GyroMon | Gyro Monitoring {1} |
| 7 | HGA_Mon | HGA-APME Monitoring Function |
| 8 | HGA_Nom | HGA-APME Nominal Control Function |
| 9 | IIDE | Inter-Instrument Data Exchange |
| 10 | ISA_SAD | ISA and SAD Function {1} |
| 11 | MinMaxMon | Min/max Recording Function |
| 12 | RAAD_Mon | RAAD Monitoring {1} |
| 13 | StartUpDld | Start-Up Function |
| 14 | StdMon | Standard Monitoring |
| 15 | SubHeatMon | Substitution Heater Monitoring |
| 16 | TC_WD | Telecommand Watchdog Function |
| 17 | TR_ThmCtrl | Mode 3 Thermal Control |
| 18 | TR_ThmMon | Mode 3 Thermal Monitoring |
| 19 | ThmCtrl | Thermal Control |
| 20 | ThmMon | Thermal Monitoring |
| 21 | ThrusterMon | Thruster Monitoring |
| 22 | ACU_ResetMon | ACU Reset Monitoring {2} |
| 23 | CRP_FlagMon | CRP Flag Monitoring {2} |
| 24 | RW_SpeedMon | RW Speed Monitoring {2} |
| 25 | HxFlagMon | Hx Flag Monitoring {2} |
| 26 | ExpOffPointing | Experiment Off-pointing Warning Message {2} |
| 27..30 | Don’t care | - |
| 31 | Reserved | Gyroless Functions Installed indication; must be 0 |

Table 3 – Functions Warm Start-Up Table

Note:

- The authorize/inhibit status for a function has a meaning only if the function exists after the start-up. There are two cases:

- Normally, e.g. after reconfiguration or reset, BOOTSTRAP loads the original COBS from PROM, discarding the Gyroless functions. Bits marked {2} have no meaning in this case.

- The only exception is when INITIALIZATION mode is entered directly through the TCM Software Mode Change, thereby bypassing BOOTSTRAP. In this case, the Gyroless patch is still effective and bits marked {1} have no meaning.

- Bit 31 is reserved for the Gyroless Functions Installed indication. In order for this indication to be correct after a reconfiguration or reset, this bit must be zero.

### Define Execution Profile of Process (KNK0C000)

The Process Id parameter is interpreted according to the following table. Changes compared to original COBS are shown in boldface.

| Name | Process Id | No. of processes |
| --- | --- | --- |
| ESRW | 1 | 1 |
| ACU_ResetMon | 2 | 1 |
| ESR_Mon | 3 | 1 |
| ExpMon | 4 | 1 |
| ExpOffPointing | 5 | 1 |
| CRP_FlagMon | 6 | 1 |
| HGA_Mon | 7 | 1 |
| HGA_Nom | 8 | 1 |
| HGA_Stat | 9 | 1 |
| IIDE | 10 | 1 |
| RW_SpeedMon | 11 | 1 |
| HxFlagMon | 12 | 1 |
| StartUpDld | 13 | 1 |
| SubHeatMon | 14 | 1 |
| TC_WD | 15 | 1 |
| ThrusterMon | 16 | 1 |
| MinMaxMon | 17..41 | 25 |
| StdMon | 42..76 | 35 |
| TR_ThmCtrl | 77..78 | 2 |
| TR_ThmMon | 79..80 | 2 |
| ThmCtrl | 81..180 | 100 |
| ThmMon | 181..280 | 100 |

Table 4 - Process Id

### Reset Corrective Action Status (KNK24000)

Note:

- The corrective action triggered status for the Gyroless functions are reset as well.

### Trigger Corrective Action for Gyro Monitoring (KNK51000)

This TCM has no effect except being acknowledged.

## Load Memory Interface

### General

Commands and parameters that are specific to the Gyroless functions are accessed by means of the TCM Load Memory (KNK2C000). This section identifies the commands and parameters concerned.

Each command or parameter occupies one single memory address. It can be controlled independently or as part of a parameter block on consecutive addresses. This may be done while functions are authorized, but note that each function may execute between each pair of TCM’s, using the newly modified value(s). Memory protection need not be disabled.

Examples:

- Format of TCM to modify a single parameter or perform a single command:

| “KNK2C000” | 0 |
| --- | --- |
| Address (FCxxH) | 1 |
| Value | 2 |

- Format of TCM to modify n parameters on consecutive addresses on a single occasion in relation to the Gyroless functions:

| “KNK2C000” | 0 |
| --- | --- |
| Address of 1st parameter | 1 |
| Value of 1st parameter | 2 |
| Value of 2nd parameter | 3 |
| ... | .. |
| Value of nth parameter | n+1 |

Caution:

- Using incorrect memory addresses may hazard the integrity of COBS. The addresses to be used for accessing Gyroless commands and parameters ranges from FC00H through FC12H.

### Initialize Gyroless Functions

The Gyroless functions can be (re-)initialized by writing to the address specified below. All Gyroless parameters and internal data/states will take their default values. Furthermore, the Gyroless functions will be disabled, their execution profiles set to 1 Hz execution, and their corrective actions disabled.

| Address (hex) | Label | Format | Command |
| --- | --- | --- | --- |
| FC00 | InitGyroless | all-ones | Initialize Gyroless Functions |

Table 5 - Address of Gyroless initialization command

Formats:

all-ones:	FFFFH	=> Perform initialization

other	=> No action

### Enable/Disable Corrective Action for Gyroless Functions

The corrective actions for the Gyroless functions can be enabled or disabled by writing to the following addresses:

| Address (hex) | Label | Format | Command |
| --- | --- | --- | --- |
| FC01 | CAS_ACU_Reset | toggle | Enable/Disable CA for ACU Reset Monitoring |
| FC02 | CAS_CRP_Flag | toggle | Enable/Disable CA for CRP Flag Monitoring |
| FC03 | CAS_RW_Speed | toggle | Enable/Disable CA for RW Speed Monitoring |
| FC04 | CAS_HxFlag | toggle | Enable/Disable CA for Hx Flag Monitoring |

Table 6 - Addresses of Gyroless CA enable/disable commands

Formats:

toggle:		0000H	=> Disable

FFFFH	=> Enable

other	=> No action

Note:

- The current corrective action enable/disable status is transmitted in §0.

- The Experiment Off-Pointing Warning Message function has no corrective action associated, but a list of experiments to warn, see OffPointingExpSet parameter in Table 7.

### Define Parameters for Gyroless Functions

The specific Gyroless parameters can be modified by writing to the following addresses:

| Address (hex) | Label | Format | Parameter | Initial value |
| --- | --- | --- | --- | --- |
| FC05 | ACU_ResetFilter | integer | Filter value for ACU Reset Monitoring | 1 |
| FC06 | CRP_FlagFilter | integer | Filter value for CRP Flag Monitoring | 1 |
| FC07 | RW_SpeedFilter | integer | Filter value for RW Speed Monitoring | 1 |
| FC08 | RW_SpeedMin (1) | rwspeed | RW1 minimim speed threshold | -4095 |
| FC09 | RW_SpeedMin (2) | rwspeed | RW2 minimim speed threshold | -4095 |
| FC0A | RW_SpeedMin (3) | rwspeed | RW3 minimim speed threshold | -4095 |
| FC0B | RW_SpeedMin (4) | rwspeed | RW4 minimim speed threshold | -4095 |
| FC0C | RW_SpeedMax (1) | rwspeed | RW1 maximum speed threshold | +4095 |
| FC0D | RW_SpeedMax (2) | rwspeed | RW2 maximum speed threshold | +4095 |
| FC0E | RW_SpeedMax (3) | rwspeed | RW3 maximum speed threshold | +4095 |
| FC0F | RW_SpeedMax (4) | rwspeed | RW4 maximum speed threshold | +4095 |
| FC10 | HxFlagFilter | integer | Filter value for Hx Flag Monitoring | 1 |
| FC11 | OffPointingFilter | integer | Filter value for Experiment Off-pointing | 1 |
| FC12 | OffPointingExpSet | expset | Set of experiments to receive off-pointing warning message | None |

Table 7 - Addresses of specific Gyroless parameters

Formats:

integer:	16-bit signed integer (2’s complement)

rwspeed:	RW speed on the format provided by the AOCS Hk1 packet:

bit 0:	1 => positive (CW); 0 => negative (CCW)

bits 4-15:	12-bit unsigned integer

others:	don’t care

expset:		One bit per experiment:

bit 6:	LASCO

bit 7:	MDI

bit 8:	SUMER

bit 10:	UVCS

others:	don’t care

1 => Send off-pointing warning message to experiment

0 => Do not send warning message to experiment

Note:

- Filter values < 1 will behave as 1.

- The off-pointing warning message is different for each experiment, see [GLSPEC].

# TELEMETRY

## Changes/Addenda to Permanent Part

### Function Authorization Status (§0, offset 17..18)

The bit-map of the Function Authorization Status table (FAS) is shown in the following table. Changes compared to original COBS are shown in boldface.

| Bit | Mnemonic | Function |
| --- | --- | --- |
| 0 | HGA_Stat | HGA-APME Station Keeping Function |
| 1 | ESRW | ESR Warning Flag |
| 2 | Don’t care | - |
| 3 | ESR_Mon | ESR Detection Function |
| 4 | ExpMon | Experiment Monitoring |
| 5 | Don’t care | - |
| 6 | Don’t care | - |
| 7 | HGA_Mon | HGA-APME Monitoring Function |
| 8 | HGA_Nom | HGA-APME Nominal Control Function |
| 9 | IIDE | Inter-Instrument Data Exchange |
| 10 | Don’t care | - |
| 11 | MinMaxMon | Min/max Recording Function |
| 12 | Don’t care | - |
| 13 | StartUpDld | Start-Up Function |
| 14 | StdMon | Standard Monitoring |
| 15 | SubHeatMon | Substitution Heater Monitoring |
| 16 | TC_WD | Telecommand Watchdog Function |
| 17 | TR_ThmCtrl | Mode 3 Thermal Control |
| 18 | TR_ThmMon | Mode 3 Thermal Monitoring |
| 19 | ThmCtrl | Thermal Control |
| 20 | ThmMon | Thermal Monitoring |
| 21 | ThrusterMon | Thruster Monitoring |
| 22 | ACU_ResetMon | ACU Reset Monitoring |
| 23 | CRP_FlagMon | CRP Flag Monitoring |
| 24 | RW_SpeedMon | RW Speed Monitoring |
| 25 | HxFlagMon | Hx Flag Monitoring |
| 26 | ExpOffPointing | Experiment Off-pointing Warning Message |
| 27..30 | Don’t care | - |
| 31 | GyrolessInstalled | Gyroless Functions Installed indication; reads 1 |

Table 8 – Function Authorization Status Table

Note:

- Bit 31 does not represent an ordinary function, but is used to indicate that the Gyroless functions patch is effective.

### Corrective Action Enable/Disable Status (§0, offset 101..103)

The bit-map of the Corrective Action Enable/Disable Status table (CAS) is shown in the following table. Changes compared to original COBS are shown in boldface.

| Bit | Corrective Action |
| --- | --- |
| 0 | Experiment Monitoring |
| 1 | Undefined |
| 2 | HGA Monitoring |
| 3..37 | Standard Monitoring, entries 1..35 |
| 38 | Substitution Heater Monitoring |
| 39 | TR Thermal Monitoring |
| 40 | Thermal Monitoring |
| 41 | Thruster Monitoring |
| 42 | ACU Reset Monitoring |
| 43 | CRP Flag Monitoring |
| 44 | RW Speed Monitoring |
| 45 | Hx Flag Monitoring |
| 46..47 | Undefined |

Table 9 – Corrective Action Status Table

### Corrective Action Triggered Status (§0, offset 104..106)

The bit-map of the Corrective Action Triggered Status table (CAT) is shown in Table 9 above.

## Changes/Addenda to Programmable Part, Group 1

### Functions Warm Start-Up Table (§1, offset 1..2)

The bit-map of the Functions Warm Start-Up Table (WAR) is shown in Table 3, page 9.

### Process Execution Profiles (§1, offset 3..18)

The Process numbering (i in 1..16) is the same as the process id shown in Table 4, page 10.

## Dump Memory Interface

The parameters for the Gyroless functions are telemetered by means of the TCM Dump Memory (KNK2F000). Start address and parameter formats are given by Table 7, page 13.

The TCM’s to initiate telemetry of Gyroless parameters in §4 thus become:

- Dump Memory:

| “KNK2F000” | 0 |
| --- | --- |
| FC05H | 1 |

- Select Item for Software Packet Programmable Part:

| “KNK20000” | 0 |
| --- | --- |
| 0004H | 1 |
| 0000H | 2 |

Note:

- The data transmitted in §4 always reflects the current memory contents.

# ANOMALIES

The Gyroless functions add one anomaly each with id’s 93H through 97H:

«ACU_ResetMon»	ACU reset detected

Data 0:	Anomaly id (93H)

Data 1..5:	0

Ensuing action:	Corrective action triggered if enabled.

Probable cause:	ACU indicates memory parity error or watchdog elapsed.

«CRP_FlagMon»	CRP flag detected

Data 0:	Anomaly id (94H)

Data 1:	AOCS active mode (4 => RMW, 7 => NM)

Data 2..5:	0

Ensuing action:	Corrective action triggered if enabled.

Probable cause:	AOCS indicates CRP flag when in NM or RMW mode.

«RW_SpeedMon»	RW speed outside limits

Data 0:	Anomaly id (95H)

Data 1:	RW number (in the range 1..4)

Data 2..5:	0

Ensuing action:	Corrective action triggered if enabled.

Probable cause:	RW speed exceeds the expected limits.

«Hx_FlagMon»	Hx flag detected

Data 0:	Anomaly id (96H)

Data 1..5:	0

Ensuing action:	Corrective action triggered if enabled.

Probable cause:	AOCS indicates that the wheels X-axis momentum exceeds expected limits.

«ExpOffPointing»	Experiment off-pointing warning

Data 0:	Anomaly id (97H)

Data 1..5:	0

Ensuing action:	Off-pointing warning messages are sent to preselected set of experiments.

Probable cause:	AOCS indicates unexpected off-pointing.

# Footnotes

The start-up mode will be that indicated by the latest BOOTSTRAP execution (reported in §0, Start-up mode) rather than be re-evaluated.