# Summary

An Anomaly Review Team (ART) was formed to investigate the recurring upset of the GGS Telemetry Module (GTM) onboard the POLAR spacecraft.  Since launch the primary GTM side (GTM-1) upset four times between May 1998 and September 2000.  A separate anomaly required the switchover to the redundant GTM side (GTM-2) in March 2001.  Since the switchover GTM-2 has upset eight times (see summary in Tables 1 & 2 below).  The upset anomaly is characterized by a corruption of all real-time data, with the exception of parameters for the minor frame sync pattern and the minor frame number.  All housekeeping and science data is corrupted for the duration of the anomaly.  This corrupt data is also recorded to the onboard tape recorders and is likewise corrupt when the recorded data is downlinked and analyzed.

The primary focus of this ART was on the possible reasons for the upsets.  A secondary focus was to determine the science impact and if proper recovery procedures are in place.  This report documents the history and status of the GTM, the investigation undertaken by the ART, and the findings of that investigation.  In summary, it is not possible to definitely determine a cause of the upsets at this time, but it is believed to be caused by environmental conditions in the mission orbit.  At this time the flight operations team (FOT) is able to recover from the upset quickly and return all the instruments to science mode while minimizing the impact to science data collection.  Currently the upset is an inconvenience to the missions operations but is recoverable.

# Background

The GTM collects and formats spacecraft telemetry and instrument science data into a continuous bit stream.  A block diagram is shown in Figure 1.  As shown in the figure the GTM is internally redundant.

The telemetry stream is formatted in one of four fixed schemes, as follows:

- Science Mode – nominal mode for the mission, with most of the available bandwidth utilized by the instruments

- Maneuver Mode – used during orbit or attitude adjust maneuvers and during deployments.  It provides higher repetition rates for certain Attitude Control and Determination Subsystem (ACADS) channels at the expense of some science data.

- Contingency Mode – designed for use in the event of a total failure of the despun platform.  Science data is collected only from the main body instruments, with no provision for science data from despun instruments.  Currently used to provide increased bandwidth to the main body instruments during periods when the platform instrument data are not particularly useful.

- Engineering Mode – only utilized during recovery from certain spacecraft anomalies.  The bite rate is much slower, at only 2% of the other modes.  The entire bandwidth is occupied by spacecraft subsystem data without any instrument science data.

The GTM responds to the mode select commands received serially from the Command Distribution Unit (CDU) and changes mode at the end of the major frame currently in progress.

### Figure 1: GTM Block Diagram

During each of the GTM events all of real-time housekeeping and science data is corrupted, with the exception of parameters for the minor frame sync pattern and the minor frame number.  This corrupt data is also recorded to the onboard tape recorders and is likewise corrupt when the recorded data is downlinked and analyzed.

| Upset # | Date | Time |
| --- | --- | --- |
| 1 | 05/06/1998 | 08:15 UT |
| 2 | 09/30/1998 | 14:00 UT |
| 3 | 10/22/1998 | 21:48 UT |
| 4 | 09/22/2000 | 01:26 UT |
| Switch to GTM-2 | 03/27/2001 | 22:10 UT |

### Table 1: GTM-1 Upset Summary

| Upset # | Date | Time |
| --- | --- | --- |
| 1 | 11/10/2003 | 18:26 UT |
| 2 | 11/17/2003 | 15:13 UT |
| 3 | 11/24/2003 | 16:38 UT |
| 4 | 12/06/2003 | 21:44 UT |
| 5 | 12/18/2003 | 09:36 UT |
| 6 | 02/12/2004 | 03:04 UT |
| 7 | 03/03/2004 | 20:14 UT |
| 8 | 04/03/2004 | 09:04 UT |

### Table 2: GTM-2 Upset Summary

For the first eight GTM upsets, the FOT followed the Real-Time Telemetry Downlink Anomaly contingency procedure (PCPG-05) to recover the GTM to its previous configuration. To accomplish this, the contingency flow calls a previously developed TPOCC Spacecraft Test and Operating Language (TSTOL) procedure that was designed to switch GTM sides in the blind.  The TSTOL procedure performs the following steps:

- Place the digital tape recorders (DTR) in standby (in case a data rate change is required),

- Disable clock to both GTMs,

- Select the GTM to be used,

- Select the telemetry mode for the Command and Attitude Processor (CAP), GTM, and Remote Interface Unit (RIU)

- Re-enable the clock to the correct side of the GTM.

- Place the DTR back into record mode to resume science data collection.

The spacecraft subsystems were never endangered by the anomaly and remained healthy.

A consequence of the GTM upset is that several of the instruments must also be recovered.  The following instrument anomalies follow almost every GTM upset:

- TIMAS telemetry latchup.

- TIDE telemetry latchup.

- MFE ADC upset.

- HYDRA eeprom write protect flag switches to the "enabled" state

Immediately following recovery of the GTM, the following instrument recovery is initiated:

- Reset MFE ADC and restart MagAz/El processing.

- Reset HYDRA EEPROM write protect flag to the "disabled" state.

- Return TIMAS to full operation.

- Return TIDE to full operation.

The exact reason for the subsequent instrument anomalies was originally suspected to be due to the loss of clock sync in the recovery procedure when disabling the GTM.

After several GTM upsets, analog telemetry parameters were found to have invalid or altered readings.  Telemetry parameters affected by GTM Side-1 upsets remained impaired after the switch to GTM Side-2.  The affected parameters are not considered crucial to the monitoring of spacecraft health and safety.  A history of the affected telemetry parameters is given in Appendix A.

Review of the design information noted that several actions are required when changing the telemetry format.  Each format-sensitive component has to be commanded to change format.  This means one or more commands to each instrument, to the RIU, to Flight Software (FSW) in the currently selected CAP, and to the GTM itself.  Data will be garbled if these components are in any way mismatched, therefore, all of these commands should be executed within a single major frame, to take effect together at the next major frame sync pulse.  For operational simplicity the individual commands are stored in macros for rapid execution by the CAP to insure that all commands are executed within the same major frame.  If this condition is adhered, there should be no interruption in the data for changes between science, maneuver, and contingency formats.  However, changes into and out of the engineering format have complications associated with changes in bit rate.

At the ART meeting following the fourth GTM-2 upset, it was suggested that for future recovery operations, only the telemetry mode commands of the recovery procedure be sent to determine which command or commands were directly responsible for recovering from the GTM upset.  It was hypothesized that the GTM clock disable/enable commands were not necessary for recovery and may be contributing to the upset of the science instruments as noted above.

After the fifth GTM-2 upset on December 18, 2003, the telemetry select commands were sent individually to observe each potential response.  The CAP science mode telemetry select was sent first without affect.  The GTM select command was then sent, and the telemetry was restored.  This demonstrated that the upset is occurring in the GTM itself and that the clock disable/enable commands were not necessary for recovery.  The revised recovery process using only the telemetry select commands has been used for all subsequent upsets.  Unfortunately, the associated instrument anomalies still occurred.   The cause of the associated instrument anomalies is still unknown, but they are now believed to occur when the GTM is upset and not during the associated recovery.

# Current Status

After the eighth GTM-2 upset on April 3, 2004, the GTM and instruments were fully recovered.  Currently the GTM is working properly, and the spacecraft and instruments are healthy.

# ART Charter

- Analyze all relevant telemetry and other data to assess; if possible, the cause of the GTM upsets.

- Determine, if possible, any detrimental affects from the upsets on the GTM.

- Review the recovery procedures and the impact on the science data collection.

- Issue a recommendation regarding the recovery of the GTM.

- Produce a report detailing the findings of the ART.

# ART Membership

Scott Glubke / GSFC 444 / SSMO Spacecraft Engineering Lead (ART Chairman)

Steve Odendahl / GSFC 444 / POLAR Mission Director
Patrick Crouse / GSFC 444 / SSMO Deputy Project Manager

Terry Smith / GSFC 561 / C&DH Engineer
Steve Hearn / LMECO / GGS-POLAR Spacecraft Lead Engineer

Barbara Giles / GSFC 692 / POLAR Project Scientist

Mike Machado / HTSI / POLAR FOT Lead

# ART Investigation

## Telemetry review

Following each anomaly the FOT would review the telemetry data to determine when the upset occurred.  Because the upset causes all the telemetry to be corrupted, data review post-upset is not possible.  This is also the reason that the cause for the associated instrument anomalies is unknown.

## Failure Analysis

Various schematic diagrams of the GTM subassemblies were obtained from the FOT.  These diagrams were reviewed with the GSFC C&DH engineer, Terry Smith.  A complete set of schematics was not available so only a limited failure analysis was done.  Despite the limited information, several potential components were identified that could be the specific component affected.  Without further design details or access to the design engineers, further identification of the affected components is not possible.  A task allowing discussion with the design engineers has been initiated but is not in place at this time.

As previously noted the FOT found that sending the GTM telemetry select command always cleared the errors.  Knowing this, the limited schematic diagrams were reviewed to identify what components might be affected.  Terry Smith was able to narrow down the problem to three potential sources:

- Component U28 (CD4035B) – a CMOS 4-Stage Parallel In/Parallel Out Shift Register on the GTM Miscellaneous Logic Board.  This part receives the serial mode command from the Command Distribution Unit (CDU) and selects the GTM telemetry format.  It is the only register that gets upset as a result of the GTM telemetry select command.  Corruption of the contents of this shift register is the only possible explanation for the errors that we are seeing and the clearing of the error condition.

- Component U28 could be getting corrupted by noise on the GTM +10 V Line.  Very little of the electronics requires +10V.  U28 is one of the few ICs that are powered from this line.  The noise could be coming from the GTM power supply.

- Component U28 could be getting corrupted by noise on the Mode Command Lines from the Command Distribution Unit.  However, this is rather unlikely because it would require that noise be present simultaneously on both the Mode Command Start line and the Mode Command Clock Line.

## Additional Testing/Investigation

No additional testing has been done after the identification of the GTM as the component being upset.  No other testing is planned at this time.

# ART Discussion & Findings

The GTM has been identified as the source of the telemetry corruption.  Some suspected environmental effect is upsetting the telemetry format definition within the GTM and subsequently causing the instrument anomalies.  Even though components have been identified as having the potential to be upset, further refinement is not possible without additional design details.  Once potential upset scenarios have been reviewed and resolved, individual component susceptibility to environmental conditions (e.g. proton flux, radiation, etc.) can be reviewed.

With the exception of the loss of several non-crucial analog telemetry points there doesn’t appear to be any detrimental affect on spacecraft subsystems or instruments from the GTM upsets and no indication of potential failure.  The only impact is the loss of science and engineering data for a period of time.  Streamlining the FOT recovery procedures and close cooperation with the instrument teams has minimized the overall data impact.

# Final Disposition & Recommendation

The final recommendation of the ART is to continue the mission operations with GTM-2.  The spacecraft and instruments are currently healthy and operating properly.  The upset of the GTM causes a loss of science data but does not appear to have any potential impacts or failure of the GTM.  Procedures exist to successfully recover from upsets with minimal science data impact. Further review of design information, discussions with design engineers, and analysis to determine the root cause will occur in the future as information becomes available.  No other actions are necessary.

#### GTM Upset #1

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| H_TH1 | Corrupted | Corrupt value not identifiable | Not required for operations |
| H_TH2 | Corrupted | Corrupt value not identifiable | Not required for operations |
| H_TPPA1 | Corrupted | Corrupt value not identifiable | Not required for operations |
| H_TPPA2 | Corrupted | Corrupt value not identifiable | Not required for operations |
| M_ELTEMP | Corrupted | Corrupt value not identifiable | Not required for operations |
| M_IBTEMP | Corrupted | Corrupt value not identifiable | Not required for operations |
| M_OBTEMP | Corrupted | Corrupt value not identifiable | Not required for operations |
| ISIESTEMP | Biased | Reading Biased By ~+18( C | Not required for operations |

#### GTM Upset #2:  No Apparent Damage

#### GTM Upset #3

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| DGTM25V | Corrupted | Corrupt value not identifiable | Represents powered-off side of GTM. Not required for operations while unit is powered off. |
| DGTM210V | Corrupted | Corrupt value not identifiable | Represents powered-off side of GTM. Not required for operations while unit is powered off. |
| DGTM2128 | Biased | Biased approximately one decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM2256 | Biased | Biased approximately two decimal counts | Represents powered-off side of GTM. Not required for operations. |
| DGTM2384 | Biased | Biased approximately three decimal counts | Represents powered-off side of GTM. Not required for operations. |
| DGTM2512 | Biased | Biased approximately four decimal counts | Represents powered-off side of GTM. Not required for operations. |

GTM Upset #4

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| NX2INTTP | Altered | Reading bounces between zero and one decimal count | Not required for operations while unit is powered off. Represents un-powered reading of temperature. |
| NX1PWLVL | Biased | Powered-off reading biased one decimal count | Only powered-off reading is affected. Does not affect monitoring of operational unit. |
| NX2PWLVL | Biased | Reading biased one decimal count | Not required for operations while unit is powered off |
| NS2PWLVL | Altered | Reading bounces between zero and one decimal count | Not required for operations while unit is powered off. Represents un-powered reading. |
| DGTM2128 | Biased | Biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM2256 | Biased | Biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM2384 | Biased | Biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM2512 | Biased | Biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| GMTRBI | Biased | Biased approximately one decimal count | Represents powered-off side of DPM. Not required for operations. |

#### Post GTM Upset #4: 00/267/15:00 UTC

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| NX1PWLVL | Altered | Powered-off reading bounces between zero and one decimal count | Only powered-off reading is affected. Does not affect monitoring of operational unit. |
| NS2PWLVL | Restored | Apparently restored. Reading unexpectedly returned to zero counts. | Not required for operations while unit is powered off. Represents un-powered reading. |
| DGTM2128 | Restored* | Reading unexpectedly returned to biased value seen prior to Upset #4 | Represents powered-off side of GTM. Not required for operations. |
| DGTM2256 | Restored* | Reading unexpectedly returned to biased value seen prior to Upset #4 | Represents powered-off side of GTM. Not required for operations. |
| DGTM2384 | Restored* | Reading unexpectedly returned to biased value seen prior to Upset #4 | Represents powered-off side of GTM. Not required for operations. |
| DGTM2512 | Restored* | Reading unexpectedly returned to biased value seen prior to Upset #4 | Represents powered-off side of GTM. Not required for operations. |

GTM Side Switch

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| NX2INTTP | Restored | Reading returned to zero counts | Not required for operations while unit is powered off. Represents un-powered reading of temperature. |
| NX1PWLVL | Restored | Off reading returned to zero counts | Powered-off value restored after switch |
| NX2PWLVL | Restored | Reading returned to zero counts | Not required for operations while unit is powered off |
| DGTM25V | Restored | Restored after switch to GTM Side 2 | Restored by GTM Side switch |
| DGTM210V | Restored | Restored after switch to GTM Side 2 | Restored by GTM Side switch |
| DGTM15V | Corrupted | Corrupted after switch to GTM Side 2 | Represents powered-off side of GTM. Not required for operations. |
| DGTM110V | Corrupted | Corrupted after switch to GTM Side 2. Value mimics mnemonic DSRVOER2 in Science Telemetry Format. | Represents powered-off side of GTM. Not required for operations. |
| DGTM2128 | Restored | Restored after switch to GTM Side 2 | Restored by GTM Side switch |
| DGTM2256 | Restored | Restored after switch to GTM Side 2 | Restored by GTM Side switch |
| DGTM2384 | Restored | Restored after switch to GTM Side 2 | Restored by GTM Side switch |
| DGTM2512 | Restored | Restored after switch to GTM Side 2 | Restored by GTM Side switch |
| DGTM1128 | Biased | Values resemble GTM Side 1 values prior to GTM side switch | Represents powered-off side of GTM. Not required for operations. |
| DGTM1256 | Biased | Values resemble GTM Side 1 values prior to GTM side switch | Represents powered-off side of GTM. Not required for operations. |
| DGTM1384 | Biased | Values resemble GTM Side 1 values prior to GTM side switch | Represents powered-off side of GTM. Not required for operations. |
| DGTM1512 | Biased | Values resemble GTM Side 1 values prior to GTM side switch | Represents powered-off side of GTM. Not required for operations. |
| GMTRBI | Biased | Biased reduced approximately one-half decimal count | Represents powered-off side of DPM. Not required for operations. |
| H_TH1 | Altered | New pattern to corrupt values | Not required for operations |
| H_TH2 | Altered | New pattern to corrupt values | Not required for operations |
| H_TPPA1 | Altered | New pattern to corrupt values | Not required for operations |
| H_TPPA2 | Altered | New pattern to corrupt values | Not required for operations |
| M_ELTEMP | Altered | New pattern to corrupt values | Not required for operations |
| M_IBTEMP | Altered | New pattern to corrupt values | Not required for operations |
| M_OBTEMP | Altered | New pattern to corrupt values | Not required for operations |
| ISIESTEMP | Corrupted | No longer simply biased reading | Not required for operations |

#### GTM Upset #5

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| NX2INTTP | Altered | Reading bounces between zero and one decimal count | Not required for operations while unit is powered off. Represents un-powered reading of temperature. |
| NS2PWLVL | Altered | Reading bounces between zero and one decimal count | Not required for operations while unit is powered off. Represents un-powered reading. |
| RRCBnTP (n=1 to 12) | Biased | Reading Biased By Average of +3( C | Thruster Catalyst Bed Temperatures continue to operate normally with positive bias noted |

#### GTM Upset #6

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| DGTM110V | Altered | New pattern of corrupt values. No longer mimics DSRVOER2. | Represents powered-off side of GTM. Not required for operations |
| DGTM1256 | Altered | New value biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM1384 | Altered | New value biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM1512 | Altered | New value biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| H_TH1 | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| H_TH2 | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| H_TPPA1 | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| H_TPPA2 | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| M_ELTEMP | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| M_IBTEMP | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| M_OBTEMP | Altered | Returned to post-Upset #1 pattern | Not required for operations |
| RRCBnTP (n=1 to 12) | Biased | Reading Additionally Biased By Average of +8( C | Thruster Catalyst Bed Temperatures continue to operate normally with net positive bias noted |

#### GTM Upset #7

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| NX2INTTP | Restored | Apparently restored after upset. Reading returned to zero counts. | Not required for operations while unit is powered off. Represents un-powered reading of temperature. |
| DGTM110V | Altered | Returned to post-GTM Switch pattern. Value mimics mnemonic DSRVOER2 in Science Telemetry Format. | Represents powered-off side of GTM. Not required for operations. |
| DGTM1128 | Altered | New value biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM1256 | Altered | New value biased approximately one additional decimal count | Represents powered-off side of GTM. Not required for operations. |
| DGTM1384 | Altered | New value biased approximately two additional decimal counts | Represents powered-off side of GTM. Not required for operations. |
| DGTM1512 | Altered | New value biased approximately two additional decimal counts | Represents powered-off side of GTM. Not required for operations. |
| H_TH1 | Altered | Returned to post-GTM Switch pattern | Not required for operations |
| H_TH2 | Altered | Returned to post-GTM Switch pattern | Not required for operations |
| H_TPPA1 | Altered | Returned to post-GTM Switch pattern | Not required for operations |
| H_TPPA2 | Altered | Returned to post-GTM Switch pattern | Not required for operations |
| M_IBTEMP | Altered | Altered to new pattern | Not required for operations |
| M_OBTEMP | Altered | Altered to new pattern | Not required for operations |
| RRCBnTP (n=1 to 12) | Biased | Reading Additionally Biased By Average of +14( C | Thruster Catalyst Bed Temperatures continue to operate normally with net positive bias noted |

#### GTM Upset #8

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| M_IBTEMP | Altered | Altered to new pattern | Not required for operations |
| M_OBTEMP | Altered | Returned to post-GTM Switch pattern | Not required for operations |

GTM Upset #9

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| DGTM1256 | Altered | Bias reduced by approximately one count | Represents powered-off side of GTM. Not required for operations. |
| M_IBTEMP | Altered | Altered to new pattern | Not required for operations |
| M_OBTEMP | Altered | Altered to new pattern | Not required for operations |
| RRCBnTP (n=1 to 12) | Biased | Reading Additionally Biased By Average of +5( C | Thruster Catalyst Bed Temperatures continue to operate normally with net positive bias noted |

#### GTM Upset #10

| Mnemonic | Event Effect | Comment | Status |
| --- | --- | --- | --- |
| M_IBTEMP | Altered | Altered to new pattern | Not required for operations |

#### GTM Upset #11:  No Apparent Damage

#### GTM Upset #12:  No Apparent Damage

Glossary

| Mnemonic | Telemetry Type | Description |
| --- | --- | --- |
| H_TH1 | Passive Analog | HYDRA Instrument DDEIS 1 Sensor Temperature |
| H_TH2 | Passive Analog | HYDRA Instrument DDEIS 2 Sensor Temperature |
| H_TPPA1 | Passive Analog | HYDRA Instrument PPA 1 Sensor Temperature |
| H_TPPA2 | Passive Analog | HYDRA Instrument PPA 2 Sensor Temperature |
| M_ELTEMP | Passive Analog | MFE Instrument Electronics Box Temperature |
| M_IBTEMP | Passive Analog | MFE Instrument Inboard Sensor Temperature |
| M_OBTEMP | Passive Analog | MFE Instrument Outboard Sensor Temperature |
| ISIESTEMP | Passive Analog | CEPPAD Instrument IES Sensor Temperature |
| NX2INTTP | Active Analog | Transponder 2 Internal Temperature |
| NX1PWLVL | Active Analog | Transponder 1 Power Converter Voltage, Telemetry Range 0 to 29.6 Volts |
| NX2PWLVL | Active Analog | Transponder 2 Power Converter Voltage, Telemetry Range 0 to 29.6 Volts |
| NS2PWLVL | Active Analog | SSPA 2 Power Level, Telemetry Range 0 to 30.6 Watts |
| DGTM15V | Active Analog | GTM Side-1 +5 Volt Supply, Telemetry Range 0 to 7.37 V |
| DGTM110V | Active Analog | GTM Side-1 +10 Volt Supply, Telemetry Range 0 to 11.2 V |
| DGTM1128 | Active Analog | GTM Side-1 1.28 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM1256 | Active Analog | GTM Side-1 2.56 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM1384 | Active Analog | GTM Side-1 3.84 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM1512 | Active Analog | GTM Side-1 5.12 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM25V | Active Analog | GTM Side-2 +5 Volt Supply, Telemetry Range 0 to 7.37 V |
| DGTM210V | Active Analog | GTM Side-2 +10 Volt Supply, Telemetry Range 0 to 11.2 V |
| DGTM2128 | Active Analog | GTM Side-2 1.28 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM2256 | Active Analog | GTM Side-2 2.56 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM2384 | Active Analog | GTM Side-2 3.84 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| DGTM2512 | Active Analog | GTM Side-2 5.12 Calibrated Voltage, Telemetry Range 0.01 to 5.11 V |
| GMTRBI | Active Analog | DPM Side-2 Motor Current, Telemetry Range 0 to 1020 mA |
| RRCBnTP | Low-Level Active Analog | REA Thruster Catalyst Bed Temperature, n = 1 through 12 |

All affected mnemonics are 8-bit analog parameters

The eight science instrument temperatures are known to share common multiplexer (mux) chips on analog telemetry board A4 in the GTM.  These parameters use chips U35/U36 for GTM Side 1, and U48/U49 for GTM Side 2. U36 (or U49, depending on the GTM side powered) is used to route a 0.5 mA current source to the thermistor of interest, and U35 (or U48) passes the generated voltage to the A/D converter in the GTM.  The mux chips in the GTM are Harris HI-508A CMOS Analog Multiplexers.

Mux chips and analog telemetry boards used by the other telemetry parameters are not known.

Definitions:

Passive Analog:  Passive analog telemetry, primarily thermistors, in the range of 0 ( to 10.2 k(.  Converted to analog voltages, ready to digitize, by routing a 0.5 mA current source through the transducer.

Active Analog:  Active analog voltage readings, in the range of 0 V to 5.12 V, digitized in the GTM

Low-Level Active Analog:  Low-level analog voltage readings from thermocouples in the range of 0 mV to 32 mV