NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 12/20/2006, 12/20/2006

LOCATION: Woodville

STREAM: Paint Rock River

BASIN: Paint Rock                       HSA: HUN

REFERENCES:

USGS WRD

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level	TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: WDVA1

NWS INDEX NUMBER: 03574500

USGS NUMBER: 03574500

MAP OF GAGE LOCATION

LATITUDE: 34 37 27  		SOURCE: USGS

LONGITUDE: 86 18 23

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:  570.950         VERTICAL DATUM: NGVD OF 1929

LEVELING AGENCY AND DATE: Level                  CHECKBAR:    0.000

RATING AGENCY:

BENCHMARK     DESCRIPTION                                                                   GAGE ZERO      DATUM

----------------------------------------------------------------------------------------    ---------     -------

RM1           RM1 AND RM2 ABANDONED                                                            23.370     594.320

RM10          (10/20/83) TABLET SET IN CONCRETE BASE FOR GAGE HEIGHT ON LEFT BANK AT           29.980     600.930

LEFT DOWNSTREAM ABUTMENT.

RM11          BOLT SET VERTICALLY IN LEFT DOWNSTREAM WINGWALL AT THE LEFT DOWNSTREAM           30.424     601.374

ABUTMENT OF THE DOWNSTREAM BRIDGE.

RM3           (10/12/38) (ABANDONED) (BASE FOR LEVELS) IS A TVA BRONZED TABLET SURVEY          29.050     600.000

MARKER SET IN THE TOP OF THE DOWNSTREAM END OF THE RIGHT ABUTMENT OF THE

UPSTREAM BRIDGE.

RM4           (3/3/40) (USED BMPR21) A CHISELED CROSS IN CIRCLE ON DOWNSTREAM,                 23.150     594.100

STREAMWARD CORNER OF PLATFORM OKF RIGHT ABUTMENT OF RAILROAD BRIDGE 1000

FT BOVE THE GAGE.

RM5           (7/24/40) (ABANDONED) THE HEAD OF A BOLT IN THE SHOREWARD SIDE OF                12.780     583.730

DOWNSTREAM PILE OF FIRST TIMBER BENT SHOREWARD FROM THE LEFT CONCRETE

PIER ON THE LEFT BANK.

RM6           (10/9/63) (ABANDONED) BOLT IN STREAMWARD SIDE OF UPSTREAM PILING OF 3 RD         12.650     583.600

BENT FROM LEFT ABUTMENT.

RM7           (9/6/66) (ABANDONED) BOLT IN STREAMWARD SIDE OF UPSTREAM PILING OF THIRD         12.646     583.596

BENT FROM LEFT ABUTMENT.

RM8           (9/2/75) (DESTROYED) BOLT IN CURB AT STILLING WELL LOCATION.                     30.090     601.040

RM9           (10/20/83) (DESTROYED) BOLT SET VERTICALLY IN LEFT DOWNSTREAM WING WALL OF       30.380     601.330

DOWNSTREAM BRIDGE.

RP1           (9/6/66) (DESTROYED) POINT IN FLOOR OF GAGE HOUSE.                               29.950     600.900

RP2           (9/6/66) POINT ON WIRE-WEIGHT GAGE BRACE MARKED BY PENCILED ARROW.               31.460     602.410

RP3           (9/6/66) (DESTROYED) STEEL ANGLE BOLTED ON DOWNSTREAM SIDE OF HAND RAIL          31.290     602.240

NEAR GAGE WELL.

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID: 16742432                TYPE OF TELEMETRY:

OWNER: USGS                                OWNER:

REPORT TIME: 01:28                        PHONE NUMBER:

INTERVAL: 240                              INTERVAL:

PAYOR/COST OF LINE:  / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- -------------------------------------------------------

staff       NWS         NWS         12/23/1935 01/17/1938 STAFF GAGE ATTACHED TO DS SIDE OF BRIDGE.

float       USGS        USGS        01/17/1938 12/26/1973 GRAPHIC RECORDER.  THIS GAGE WAS MOVED DOWNSTREAM 20 ON	                                                      7/24/40. CONCRETE GAGE STRUCTURE USED TO HOUSE GRAPHIC

RECORDER. STRUCTURE 5 X 5 FT WALK-IN CONCRETE STANDARD

HOUSE AND WELL.

pres trans  USGS        USGS        07/31/1963 05/21/1965 3/12/63 HOUSE DESTROYED BY FLOOD. BETWEEN 3/12/63 AND

7/31/63 OBSERVER WAS HIRED TO TAKE READINGS. JULY 31	                                                     1963 MANOMETER AND GRAPHIC RECORDER INSTALLED IN METAL 	                                                     SHELTER ON LEFT BANK.

pres trans  USGS        USGS        05/21/1965 12/26/1973 5/21/65 REMOVED MANOMETER AND STRUCTURE, INSTALLED	  	                                                     GRAPHIC RECORDER IN METAL SHELTER ATOP 21-INCH PIPE								        STILLING WELL ATTACHED TO DS SIDE OF BRIDGE. FLOOD OF							        12/26/73 DESTROYED THE STILLING WELL. OBSERVER HIRED							        UNTIL THE WELL WAS REPLACED.

float       USGS        USGS        07/19/1974 09/14/1980 DIGITAL RECORDER IN ALUMINUM HOUSE ATOP 18 INCH PIPE 							        WELL ATTACHED TO DOWNSTREAM SIDE OF BRIDGE. FLOOD OF 	                                                     3/21/80 DESTROYED THE STILLING WELL. BETWEEN 3/21/80				                               AND 9/14/80 OBSERVER WAS HIRED TO TAKE READINGS.

pres trans  USGS        USGS        09/14/1980            INSTALLED SERVO MANOMETER (ACCUBAR) IN 4 X 4 FIBERGLASS

HOUSE WITH DIGITAL AND GRAPHIC RECORDERS. HANDAR 570							        DCP INSTALLED (DATE UNRECORDED). REFERENCED TO WIRE-						                WEIGHT GAGE ATTACHED TO THE DS SIDE OF THE DS BRIDGE						                AND LOCATED OVER THE ORIFICE.

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

USGS                                  12/23/1935

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

staff                     NWS         12/23/1935       01/17/1938

float                     USGS        01/17/1938       12/26/1973

pres trans                USGS        07/31/1963       05/21/1965

pres trans                USGS        05/21/1965       12/26/1973

float                     USGS        07/19/1974       09/14/1980

pres trans                USGS        09/14/1980

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

570.950                              12/23/1935

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 16.00    ACTION STAGE: 14.00     BANKFULL STAGE: 12.00

FLOOD FLOW: 0           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ---------------------------------------------

02/04/1936 UNDEF   19.20            X

01/03/1937 UNDEF   18.90

04/09/1938 UNDEF   18.00

02/04/1939 UNDEF   20.40

12/28/1942 UNDEF   20.50  31300

03/29/1944 UNDEF   18.60

02/18/1945 UNDEF   18.30

01/09/1946 UNDEF   18.80

02/13/1948 UNDEF   19.90

01/05/1949 UNDEF   20.84

01/07/1950 UNDEF   19.40

03/29/1951 UNDEF   20.30

03/11/1952 UNDEF   18.90

01/16/1954 UNDEF   19.80

02/04/1956 UNDEF   19.90

02/01/1957 UNDEF   20.20

01/22/1959 UNDEF   18.70

02/23/1961 13:00   19.68  21700

03/09/1961 01:00   17.82   9190

12/13/1961 10:00   17.72   8780

12/18/1961 13:30   20.00   2400

01/28/1962 06:30   18.59  13300

02/24/1962 05:30   19.40  19000

04/13/1962 02:30   17.26   7180

03/06/1963 17:00   19.14  17400

03/12/1963 18:30   22.60  46700

04/30/1963 14:00   18.52  12900

01/26/1964 07:00   16.40   8140

03/15/1964 17:30   19.40  23200

03/26/1964 20:30   17.10   9650

04/07/1964 16:30   17.88  12100

04/14/1964 21:30   15.68   6890

04/28/1964 16:00   16.67   8680

05/04/1964 08:00   15.73   6970

02/12/1965 13:00   17.42  10600

03/27/1965 01:00   18.74  18400

03/30/1965 19:00   17.18   9850

02/14/1966 10:20   17.58  11000

02/21/1967 20:00   16.12   7850

03/08/1967 02:00   15.35   6870

04/27/1967 18:00   16.00   7840

07/13/1967 18:00   16.63   8600

12/04/1967 04:00   16.10   7810

12/19/1967 UNDEF   20.10  32300

12/23/1967 12:00   15.47   6560

01/07/1968 20:00   15.08   6100

01/11/1968 14:00   16.72   8960

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 5: CRESTS

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ---------------------------------------------

05/17/1968 22:00   15.52   7050

01/20/1969 20:00   17.66  11300

02/02/1969 24:00   19.32  22700

04/11/1969 09:20   16.52   7650

05/19/1969 16:00   17.36  10100

12/31/1969 UNDEF   20.60  34300

04/02/1970 05:00   17.84   9590

01/24/1971 18:00   17.15   7780

02/06/1971 10:00   16.92   7410

02/22/1971 24:00   18.39  15200

02/27/1971 20:00   17.19   8050

12/07/1971 22:00   19.01  20000

01/05/1972 18:30   17.01   7410

01/11/1972 16:30   17.34   8380

12/12/1972 03:00   16.84   6260

02/15/1973 20:00   16.67   6000

03/16/1973 20:00   24.40  74200                                FLOOD OF RECORD

11/29/1973 09:00   17.09   6680

12/27/1973 02:00   21.06  28100

01/12/1974 15:00   18.65  11700

01/27/1974 10:30   17.55   7960

02/18/1974 09:00   16.85   6580

03/22/1974 10:00   17.70   8440

04/05/1974 12:00   17.50   7800

03/14/1975 UNDEF   20.40  22700

03/25/1975 18:00   17.11   6720

03/30/1975 24:00   19.10  13800

09/26/1975 01:00   17.52   7860

10/09/1975 17:00   19.57  16500

10/18/1975 15:00   19.55  16400

05/16/1976 03:00   17.61   8090

03/05/1977 17:00   17.09   6720

04/05/1977 14:00   18.60  11400

10/03/1977 18:00   19.01  13200

10/11/1977 04:00   16.71   6380

11/06/1977 08:00   19.62  16800

11/30/1977 23:00   17.88   9440

01/02/1979 UNDEF   17.40   7530

01/22/1979 12:00   17.22   7060

03/04/1979 21:00   19.50  16000

04/14/1979 01:00   18.32  10400

09/29/1979 09:00   19.25  14600

03/09/1980 04:00   17.90   8830

03/21/1980 06:00   21.00  31200

03/29/1980 16:00   16.70   6070

05/18/1980 20:00   17.67   8290

03/31/1981 UNDEF   16.93   6930

01/04/1982 16:00   19.57  17200

01/22/1982 15:00   17.51   8240

02/18/1982 05:00   16.62   6300

03/16/1982 23:00   16.47   6010

04/06/1983 17:00   19.96  19700

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                   NWS FORM E-19 PAGE 5-2: CRESTS

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ---------------------------------------------

05/20/1983 08:00   19.67  17800

11/29/1983 06:00   18.51   9920

12/04/1983 17:00   18.55  10100

12/29/1983 18:00   17.33   6740

05/04/1984 06:00   18.94  11700

11/29/1984 17:00   16.73   6520

02/02/1985 21:00   17.01   7100

02/19/1986 14:00   17.49   7500

03/14/1986 15:00   17.75   8480

11/26/1986 03:00   17.50   7540

12/11/1986 12:00   17.32   6910

01/20/1987 07:00   18.35  10900

02/28/1987 16:00   17.93   9210

01/20/1988 23:00   19.36  15500

01/13/1989 24:00   17.77   7460

03/07/1989 05:00   17.79   7550

04/05/1989 23:00   17.85   7780

02/04/1990 23:00   19.30  15800

02/16/1990 23:00   19.89  19700

03/17/1990 15:00   17.88   9000

12/23/1990 09:00   23.42  56900

02/20/1991 11:00   20.04  20800

03/30/1991 04:00   19.53  17400

04/10/1991 04:00   16.94   7170

05/06/1991 22:00   17.30   8040

12/02/1991 UNDEF   21.36  31400

12/22/1992 UNDEF   17.10

03/24/1993 UNDEF   20.64  25200

02/11/1994 UNDEF   21.08  28800

10/07/1995 02:00   17.39   7150

11/09/1995 05:00   16.07   4850

12/20/1995 UNDEF   16.00

12/21/1995 08:00   15.38   4360

01/03/1996 17:00   14.02   3230

01/08/1996 07:00   17.06   6080

01/13/1996 07:00   14.43   3570

01/28/1996 05:00   15.91   4730

02/10/1996 04:00   12.44   2280

03/08/1996 01:00   18.53  11800

03/20/1996 16:00   16.68   5380

03/29/1996 12:00   13.85   3110

04/23/1996 UNDEF   18.20

01/17/1997 UNDEF   16.50                                       STAGE ESTIMATED.

03/04/1997 21:00   17.02

05/04/1997 UNDEF   16.50                                       ESTIMATED STAGE.

10/27/1997 16:00   17.56

01/08/1998 UNDEF   20.87  25700

03/10/1998 UNDEF   16.50                                       ESTIMATED STAGE.

01/24/1999 UNDEF   18.35  11100

05/08/1999 05:30   18.50                                       Estimated Stage

03/21/2000 UNDEF   18.34

04/04/2000 UNDEF   19.73  17500

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                   NWS FORM E-19 PAGE 5-3: CRESTS

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ---------------------------------------------

12/18/2000 UNDEF   16.64

01/20/2001 08:45   18.84

02/18/2001 14:30   16.80

03/21/2001 18:00   17.57

06/09/2001 20:00   16.60

12/15/2001 07:15   18.87

02/17/2003 05:00   20.20                                       FLOOD

02/23/2003 20:40   17.66

05/06/2003 23:40   18.46                                       estimated crest...gauge was inoperative		                                                               from 05/07 05:00Z until 05/08 01:40Z.

02/07/2004 05:00   20.10

03/07/2004 12:00   18.30   9821                                Inserted from the FloodTS table via Hydrobase

03/07/2004 13:30   18.34  10016                                Inserted from the FloodTS table via Hydrobase

09/19/2004 09:00   17.01   5230                                Inserted from the FloodTS table via Hydrobase

09/19/2004 UNDEF   17.01

11/05/2004 23:00   16.24   4504                                Inserted from the FloodTS table via Hydrobase

11/26/2004 00:00   17.50   6777                                Inserted from the FloodTS table via Hydrobase

12/08/2004 01:30   20.46  23995                                Inserted from the FloodTS table via Hydrobase

12/10/2004 17:30   19.32  15560                                Inserted from the FloodTS table via Hydrobase

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                   NWS FORM E-19 PAGE 5-4: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

10/21/1954     0.28

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH: 26.6       DRAINAGE AREA: 320.0      POOL STAGE: 0.0

STREAM BED: GRAVEL AND SAND

REACH: 20 US TO 4 DS

REGULATION: NONE. THE LOW-WATER CONTROL IS UNSTABLE SAND AND GRAVEL. THE

CHANNEL CONTROL RANGE SHOULD BE FAIRLY STABLE. THE BANKS

ARE UNSTABLE, BUT WELL-DEFINED.

DIVERSION: NONE.

WINTER: LITTLE TO NO ICE EFFECT EXPERIENCED.

TOPOGRAPHY: CHANNEL IS STRAIGHT FOR ABOUT 1000 FT ABOVE AND BELOW THE

GAGE. BANKS ARE CLEARED, CULTIVATED LAND, FRINGED WITH

BRUSH.

REMARKS: BOTH BANKS OVERFLOW ABOVE ABOUT 12 FEET BUT ALL FLOW PASSES

UNDER BRIDGE EXCEPT AT EXTREME HIGH STAGES...AT WHICH TIME

SOME FLOW MAY BE OVER THE HIGHWAY ON THE RIGHT BANK.

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  ----------------------------------------------------------------------------------------------------

12.00  SOME MINOR OVERFLOW OF FARMLAND BEGINS AT HIGHER STAGES.

14.00  THE BUTLER BOTTOM LOWLANDS NEAR THE RIVER ARE FLOODED. HIGH WATERS ARE APPROACHING COUNTY ROAD 20

NORTH OF THE TOWN OF PAINT ROCK.

16.00  FLOOD STAGE. FLOOD WATERS AFFECT MOSTLY BOTTOMLAND ALONG THE RIVER...INCLUDING LOW-LYING FARM AND

PASTURELANDS.

19.00  MODERATE FLOODING. WATER IS COVERING ALABAMA STATE ROUTE 65 ABOUT TWO MILES NORTH OF U.S. HIGHWAY

72. SEVERAL COUNTY ROADS IN PAINT ROCK VALLEY ARE FLOODED...INCLUDING JACKSON COUNTY ROAD 20.

21.00  SEVERAL PORTIONS OF ALABAMA STATE HIGHWAY 65 ARE CLOSED DUE TO HIGH WATER.

22.00  MAJOR FLOODING.

23.00  FLOOD WATERS COVER U.S. HIGHWAY 72 NEAR WOODVILLE AND PAINT ROCK. SOME EVACUATIONS MAY BECOME

NECESSARY AS WATER APPROACHES RESIDENCES.

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  28-|

|-----|

|-----|

|-----|

|-----|

|  26-|

|-----|

|-----|

|-----|

|-----|

|  24-|   24.40  03/16/1973

|-----|

|-----|   23.42  12/23/1990

23.00 - FLOOD WATERS COVER U.S. HIGHWAY 72 NEAR WOODVILLE AND PAINT ROCK. SOME EVACUATIONS      |-----|

MAY BECOME NECESSARY AS WATER APPROACHES RESIDENCES.                                    |-----|   22.60  03/12/1963

|  22-|

22.00 - MAJOR FLOODING.                                                                         |-----|

|-----|   21.36  12/02/1991

21.00 - SEVERAL PORTIONS OF ALABAMA STATE HIGHWAY 65 ARE CLOSED DUE TO HIGH WATER.              |-----|   21.08  02/11/1994

|-----|   20.64  03/24/1993

|  20-|   20.40  03/14/1975

|-----|   19.73  04/04/2000

|-----|   19.53  03/30/1991

19.00 - MODERATE FLOODING. WATER IS COVERING ALABAMA STATE ROUTE 65 ABOUT TWO MILES NORTH OF    |-----|   18.87  12/15/2001

U.S. HIGHWAY 72. SEVERAL COUNTY ROADS IN PAINT ROCK VALLEY ARE FLOODED...INCLUDING      |-----|   18.53  03/08/1996

JACKSON COUNTY ROAD 20.                                                                 |  18-|   18.35  01/20/1987

|-----|   17.66  02/23/2003

|-----|   17.57  03/21/2001

|-----|   17.10  12/22/1992

|-----|   16.80  02/18/2001

|  16-|   16.24  11/05/2004

16.00 - FLOOD STAGE. FLOOD WATERS AFFECT MOSTLY BOTTOMLAND ALONG THE RIVER...INCLUDING          |-----|   16.00  12/20/1995

LOW-LYING FARM AND PASTURELANDS.                                                        |-----|   15.38  12/21/1995

|-----|

|-----|   14.43  01/13/1996

|  14-|   14.02  01/03/1996

14.00 - THE BUTLER BOTTOM LOWLANDS NEAR THE RIVER ARE FLOODED. HIGH WATERS ARE APPROACHING      |-----|   13.85  03/29/1996

COUNTY ROAD 20 NORTH OF THE TOWN OF PAINT ROCK.                                         |-----|

|-----|

|-----|   12.44  02/10/1996

|  12-|

12.00 - SOME MINOR OVERFLOW OF FARMLAND BEGINS AT HIGHER STAGES.                                |-----|

|-----|

|-----|

|-----|

|  10-|

|-----|

|-----|

|-----|

|-----|

|   8-|

REACH: 20 US TO 4 DS                                                                   	ELEVATION ZERO:  570.95

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                     NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

1  Jackson County EMA                                 256-574-9344

Director:  Victor Manning

2  Jackson County SO                                  256-574-2610

3  Madison County EMA                                 256-427-5130

Director:  John Rusty Russell

LOCATION: Paint Rock River NEAR Woodville, AL                       Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WDVA1                          HSA: HUN                    NWS FORM E-19 PAGE 10: CONTACTS

Gage house at Woodville.

Flooding on Highway 65 near Paint Rock.