3 September, 2002

TO: DISTRIBUTION
FROM: C NEUMEYER
SUBJECT:  CTF DESIGN POINT STUDIES

This memo provides documentation of the results of design point studies for a Component Test Facility (CTF) along with a description of the methodology used.

This work is acknowledged to rely heavily on the physics algorithms developed by C. Kessel and S. Jardin along with numerous technical discussions with M. Peng and C. Kessel.

The 0-d physics algorithms along with various physics constraints and engineering equations were programmed into an EXCEL spreadsheet, and the EXCEL Solver was used to arrive at design point optimums, given optimization criteria and constraints. The near term objective was to characterize possible CTF design points. The long term objective was to identify the important issues, and to develop and document a means for continuation of the ST development path studies.

On the engineering side, the following areas deserve attention in the future:

- Develop a MATLAB version of the calculations.

- Perform more detailed studies of the TF inner leg, including first wall and joints to current return path. Investigate options for first wall and copper alloy materials, cooling passage design, fabrication technique, etc.

- Study options for the TF power supply including homopolar generator.

- Determine PF requirements, investigate options for PF coils, and adjust power consumption accordingly.

- Develop concept design for first wall/blanket/shield, perform neutronics calculations and/or adapt results of prior calculations by others to improve modeling of heat loads and first wall/blanket/shield geometry assumptions.

- Refine estimates of efficiency and power consumption of the various elements of the power supply, heating, power conversion, and balance of plant systems, over the range of typical to high-efficiency systems.

### Summary of Results

Several optimization scans were performed using physics constraints derived from two separate sources, namely J. Menard and C. Wong.  The Menard limits are based on ideal theoretical MHD stability whereas the Wong limits are derived from DIID experience. The scans performed are summarized in Table 1.

Table 1: Summary of Cases

| Case | Electricity Generation | Optimization Criteria | R0(m) | A | Nwall (MW/m2) | HH |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | No | Maximize neutrons/sec/watt | 1.5 | 1.4-2.0 | 1.5 | 1.8 |
| 2 | No | Maximize neutrons/sec/watt | 1.5 | 1.5 | 1.5 | 1.4-1.8 |
| 3 | Yes | Maximize net electric power | 2.5 | 1.4-2.0 | 2.5 | 1.8 |
| 4 | Yes | Maximize net electric power | 2.5 | 1.5 | 2.5 | 1.4-1.8 |

Results are summarized in the following figures and tables.

Case 1: Optimized for n/sec/watt R=1.5m, Nwall=1.5MW/m2, Varying A

Fig. 1: Neutron Production Efficiency vs. A

Fig. 2: Electrical Demand vs. A

Table 2: Design Points based on Menard Constraints (Optimize n/sec/watt, Varying A)

| R0 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 1.400 | 1.500 | 1.600 | 1.700 | 1.800 | 1.900 | 2.000 |
| kappa | 3.612 | 3.489 | 3.382 | 3.288 | 3.204 | 3.128 | 3.060 |
| delta | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 |
| qMHD | 12.348 | 9.540 | 7.962 | 6.978 | 6.315 | 5.841 | 5.486 |
| qcyl | 2.94 | 2.80 | 2.72 | 2.66 | 2.63 | 2.60 | 2.58 |
| qcyl/qcyl(A) | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% |
| Bt | 1.527 | 1.651 | 1.791 | 1.939 | 2.095 | 2.260 | 2.432 |
| fH20 | 11.0% | 8.7% | 7.5% | 6.7% | 6.1% | 5.7% | 5.4% |
| TH20max | 112.5 | 88.8 | 77.5 | 71.1 | 67.1 | 64.3 | 62.3 |
| TCumax | 143.2 | 106.1 | 91.5 | 83.0 | 77.6 | 73.8 | 71.1 |
| Sigmax | 48.6 | 38.4 | 33.8 | 31.6 | 30.8 | 30.9 | 31.5 |
| Javgtf | 3.38E+07 | 2.46E+07 | 2.00E+07 | 1.73E+07 | 1.56E+07 | 1.45E+07 | 1.37E+07 |
| W_tf | 315.8 | 352.9 | 398.9 | 451.6 | 511.1 | 578.1 | 653.4 |
| Ip | 13.958 | 12.930 | 11.999 | 11.150 | 10.394 | 9.734 | 9.160 |
| Beta_N | 6.84% | 6.58% | 6.35% | 6.18% | 6.03% | 5.89% | 5.74% |
| Beta_N/Beta_N(A) | 78.3% | 76.9% | 76.4% | 76.5% | 77.0% | 77.4% | 77.5% |
| Beta_T | 58.4% | 51.5% | 45.4% | 40.3% | 35.9% | 32.1% | 28.8% |
| Beta_P | 140.7% | 138.3% | 138.1% | 140.0% | 142.7% | 145.5% | 147.9% |
| xne | 2.12E+20 | 2.11E+20 | 2.17E+20 | 2.28E+20 | 2.43E+20 | 2.60E+20 | 2.75E+20 |
| fGW | 60.6% | 56.9% | 55.5% | 55.9% | 57.1% | 58.5% | 59.6% |
| alpha_n(A) | 0.213 | 0.220 | 0.226 | 0.232 | 0.237 | 0.241 | 0.245 |
| alpha_T(A) | 0.213 | 0.220 | 0.226 | 0.232 | 0.237 | 0.241 | 0.245 |
| fBS | 76.5% | 75.0% | 74.9% | 75.8% | 77.4% | 79.0% | 80.4% |
| Tempavg | 8.860 | 9.182 | 9.268 | 9.155 | 8.941 | 8.718 | 8.528 |
| HH | 1.800 | 1.800 | 1.800 | 1.800 | 1.800 | 1.800 | 1.800 |
| Tau_E*HH | 1.480 | 1.346 | 1.256 | 1.195 | 1.153 | 1.121 | 1.095 |
| Q | 3.837 | 3.730 | 3.638 | 3.558 | 3.494 | 3.447 | 3.418 |
| P_Brem | 15.9 | 13.5 | 12.3 | 11.7 | 11.4 | 11.3 | 11.1 |
| P_aux | 47.1 | 44.6 | 42.3 | 40.3 | 38.4 | 36.5 | 34.7 |
| P_fusion | 180.7 | 166.3 | 154.1 | 143.4 | 134.1 | 125.9 | 118.6 |
| P_alpha | 36.1 | 33.3 | 30.8 | 28.7 | 26.8 | 25.2 | 23.7 |
| Eta_CD | 0.22 | 0.23 | 0.23 | 0.23 | 0.22 | 0.22 | 0.21 |
| P_CD | 47.1 | 44.6 | 42.3 | 40.3 | 38.4 | 36.5 | 34.7 |
| P_CD/P_aux | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% |
| P_aux_input | 104.6 | 99.1 | 94.1 | 89.6 | 85.3 | 81.2 | 77.1 |
| ∑P_tf | 105.3 | 80.7 | 70.4 | 65.8 | 63.9 | 63.9 | 65.0 |
| P_bop | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 |
| ∑P_elec input | 229.9 | 199.8 | 184.6 | 175.3 | 169.3 | 165.0 | 162.1 |
| P_elec gen | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| P_net elec | -229.9 | -199.8 | -184.6 | -175.3 | -169.3 | -165.0 | -162.1 |
| Xnwall | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 |
| n/s/W | 2.92E+11 | 3.06E+11 | 3.03E+11 | 2.93E+11 | 2.81E+11 | 2.68E+11 | 2.55E+11 |

Table 3: Design Points based on Wong Constraints  (Optimize n/sec/watt, Varying A)

| R0 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 1.400 | 1.500 | 1.600 | 1.700 | 1.800 | 1.900 | 2.000 |
| kappa | 3.044 | 2.913 | 2.799 | 2.698 | 2.608 | 2.528 | 2.456 |
| delta | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 |
| qMHD | 10.580 | 8.755 | 7.678 | 6.980 | 6.500 | 6.152 | 5.890 |
| qcyl | 2.54 | 2.60 | 2.65 | 2.70 | 2.74 | 2.78 | 2.81 |
| qcyl/qcyl(A) | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% |
| Bt | 1.705 | 1.972 | 2.249 | 2.533 | 2.820 | 3.112 | 3.407 |
| fH20 | 11.5% | 9.4% | 8.3% | 7.6% | 7.1% | 6.7% | 6.4% |
| TH20max | 111.8 | 91.8 | 81.4 | 75.3 | 71.5 | 69.1 | 67.4 |
| TCumax | 150.0 | 115.0 | 98.2 | 88.9 | 83.1 | 79.6 | 77.0 |
| Sigmax | 60.6 | 54.7 | 53.3 | 53.9 | 55.8 | 58.5 | 61.9 |
| Javgtf | 3.77E+07 | 2.94E+07 | 2.51E+07 | 2.26E+07 | 2.10E+07 | 1.99E+07 | 1.92E+07 |
| W_tf | 360.8 | 461.9 | 578.5 | 709.3 | 854.6 | 1014.2 | 1189.2 |
| Ip | 13.182 | 12.004 | 10.984 | 10.086 | 9.295 | 8.600 | 7.989 |
| Beta_N | 6.76% | 6.23% | 5.83% | 5.53% | 5.31% | 5.14% | 5.00% |
| Beta_N/Beta_N(A) | 84.4% | 82.0% | 80.5% | 80.0% | 80.0% | 80.5% | 81.1% |
| Beta_T | 48.8% | 37.9% | 30.4% | 25.0% | 21.0% | 18.0% | 15.6% |
| Beta_P | 120.2% | 121.3% | 123.6% | 126.9% | 131.0% | 135.7% | 140.6% |
| xne | 2.27E+20 | 2.29E+20 | 2.37E+20 | 2.48E+20 | 2.63E+20 | 2.80E+20 | 2.98E+20 |
| fGW | 69.7% | 67.5% | 67.0% | 67.7% | 69.4% | 71.6% | 74.1% |
| alpha_n(A) | 0.250 | 0.250 | 0.250 | 0.250 | 0.250 | 0.250 | 0.250 |
| alpha_T(A) | 0.250 | 0.250 | 0.250 | 0.250 | 0.250 | 0.250 | 0.250 |
| fBS | 75.7% | 73.6% | 72.4% | 71.9% | 72.0% | 72.5% | 73.1% |
| Tempavg | 8.632 | 8.863 | 8.940 | 8.890 | 8.758 | 8.582 | 8.394 |
| HH | 1.800 | 1.800 | 1.800 | 1.800 | 1.800 | 1.800 | 1.800 |
| Tau_E*HH | 1.273 | 1.134 | 1.030 | 0.947 | 0.879 | 0.822 | 0.773 |
| Q | 3.354 | 3.155 | 2.974 | 2.807 | 2.654 | 2.516 | 2.391 |
| P_Brem | 15.5 | 13.4 | 12.1 | 11.3 | 10.8 | 10.5 | 10.3 |
| P_aux | 50.4 | 49.2 | 48.2 | 47.5 | 46.8 | 46.3 | 45.8 |
| P_fusion | 169.2 | 155.3 | 143.5 | 133.2 | 124.3 | 116.4 | 109.5 |
| P_alpha | 33.8 | 31.1 | 28.7 | 26.6 | 24.9 | 23.3 | 21.9 |
| Eta_CD | 0.22 | 0.22 | 0.22 | 0.22 | 0.22 | 0.21 | 0.21 |
| P_CD | 50.4 | 49.2 | 48.2 | 47.5 | 46.8 | 46.3 | 45.8 |
| P_CD/P_aux | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% |
| P_aux_input | 112.1 | 109.4 | 107.2 | 105.5 | 104.0 | 102.8 | 101.7 |
| ∑P_tf | 114.7 | 100.4 | 96.4 | 96.8 | 99.5 | 103.8 | 109.2 |
| P_bop | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 |
| ∑P_elec input | 246.7 | 229.8 | 223.6 | 222.3 | 223.6 | 226.6 | 230.9 |
| P_elec gen | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| P_net elec | -246.7 | -229.8 | -223.6 | -222.3 | -223.6 | -226.6 | -230.9 |
| Xnwall | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 |
| n/s/W | 2.56E+11 | 2.49E+11 | 2.33E+11 | 2.16E+11 | 1.98E+11 | 1.82E+11 | 1.66E+11 |

Case 2: Optimized for n/sec/watt R=1.5m, Nwall=1.5MW/m2, Varying HH

Table 4: Menard /Wong Constraints (Optimize n/sec/watt, Fixed A, Varying HH)

|  | Menard | Menard | Menard | Wong | Wong | Wong |
| --- | --- | --- | --- | --- | --- | --- |
| R0 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 |
| A | 1.500 | 1.500 | 1.500 | 1.500 | 1.500 | 2.000 |
| kappa | 3.489 | 3.489 | 3.489 | 2.913 | 2.913 | 2.456 |
| delta | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 | 0.600 |
| qMHD | 9.540 | 9.540 | 9.540 | 8.755 | 8.755 | 5.890 |
| qcyl | 2.80 | 2.80 | 2.80 | 2.60 | 2.60 | 2.81 |
| qcyl/qcyl(A) | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% |
| Bt | 1.651 | 1.795 | 1.997 | 1.972 | 2.011 | 4.002 |
| fH20 | 8.7% | 9.2% | 9.9% | 9.4% | 9.5% | 7.2% |
| TH20max | 88.8 | 92.6 | 98.4 | 91.8 | 92.8 | 72.4 |
| TCumax | 106.1 | 111.9 | 121.3 | 115.0 | 116.8 | 83.9 |
| Sigmax | 38.4 | 45.4 | 56.1 | 54.7 | 56.9 | 85.4 |
| Javgtf | 2.46E+07 | 2.68E+07 | 2.98E+07 | 2.94E+07 | 3.00E+07 | 2.26E+07 |
| W_tf | 352.9 | 417.8 | 518.2 | 461.9 | 480.4 | 1651.2 |
| Ip | 12.930 | 14.056 | 15.639 | 12.004 | 12.240 | 9.387 |
| Beta_N | 6.58% | 5.38% | 4.28% | 6.23% | 6.24% | 3.45% |
| Beta_N/Beta_N(A) | 76.9% | 63.0% | 50.1% | 82.0% | 82.1% | 55.9% |
| Beta_T | 51.5% | 42.1% | 33.5% | 37.9% | 38.0% | 10.8% |
| Beta_P | 138.3% | 113.1% | 90.0% | 121.3% | 121.6% | 96.8% |
| xne | 2.11E+20 | 1.79E+20 | 1.60E+20 | 2.29E+20 | 2.75E+20 | 2.40E+20 |
| fGW | 56.9% | 44.4% | 35.7% | 67.5% | 79.3% | 50.9% |
| alpha_n(A) | 0.220 | 0.220 | 0.220 | 0.250 | 0.250 | 0.250 |
| alpha_T(A) | 0.220 | 0.220 | 0.220 | 0.250 | 0.250 | 0.250 |
| fBS | 75.0% | 61.4% | 48.8% | 73.6% | 73.7% | 50.3% |
| Tempavg | 9.182 | 10.469 | 11.495 | 8.863 | 7.691 | 9.865 |
| HH | 1.800 | 1.600 | 1.400 | 1.800 | 1.600 | 1.400 |
| Tau_E*HH | 1.346 | 1.066 | 0.900 | 1.134 | 0.962 | 0.509 |
| Q | 3.730 | 2.988 | 2.483 | 3.155 | 2.254 | 1.605 |
| P_Brem | 13.5 | 10.4 | 8.7 | 13.4 | 17.8 | 7.3 |
| P_aux | 44.6 | 55.7 | 67.0 | 49.2 | 68.9 | 68.2 |
| P_fusion | 166.3 | 166.3 | 166.3 | 155.3 | 155.3 | 109.5 |
| P_alpha | 33.3 | 33.3 | 33.3 | 31.1 | 31.1 | 21.9 |
| Eta_CD | 0.23 | 0.26 | 0.29 | 0.22 | 0.19 | 0.25 |
| P_CD | 44.6 | 55.7 | 67.0 | 49.2 | 68.9 | 68.2 |
| P_CD/P_aux | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% |
| P_aux_input | 99.1 | 123.7 | 148.9 | 109.4 | 153.1 | 151.5 |
| ∑P_tf | 80.7 | 95.0 | 117.4 | 100.4 | 104.4 | 148.3 |
| P_bop | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 |
| ∑P_elec input | 199.8 | 238.7 | 286.3 | 229.8 | 277.4 | 319.8 |
| P_elec gen | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| P_net elec | -199.8 | -238.7 | -286.3 | -229.8 | -277.4 | -319.8 |
| Xnwall | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 |
| n/s/W | 3.06E+11 | 2.56E+11 | 2.13E+11 | 2.49E+11 | 2.06E+11 | 1.20E+11 |

Fig. 1: Maximum Pnet vs. A

Summary Engineering Assumptions

- 10 cm shielding on inner leg

- Glidcop inner leg at 87% IACS conductivity

- 15% coolant fraction in inner leg

- Radius of ends of inner leg flared beyond radius of central region by ∆R = (1-delta)*a

- Flaring approximated by step change in inner leg radius beginning at Z=+/- 0.9*kappa*a

- Height of inner leg equal to kappa*a + 4.0m

- Current return via aluminum VV shell

- Outer shell horizontal to R=R0+a, then angled toward midplane ending at R=R0+a+2.5m, Z=+/-kappa*a, then vertical to midplane

- Outer shell current density equal to 1.5kA/cm^2 in horizontal section, 1.25kA/cm^2 in angled section, and 1.0kA/cm^2 in vertical section.

- TF power supply efficiency 95%

- Aux Heating/CD efficiency 45%

- Electric power required for balance of plant equal to 10% of generated electric power

- Superconducting PF coils (P=0, refrigeration power assumed include in balance of plant)

- Neutron flux absorbed by center stack based on solid angle with origin at R0+a/3 (see figure following)

- After center stack shadowing, 90% of remaining neutrons incident with blanket Efficiency of power conversion of thermal to electric power equal to 35%

Fig. 3: Fraction of 14MeV Source Neutrons Intercepted by Center Stack

## Summary Physics Constraints

Table 5: Summary of Physics Constraints

| Variable | Menard | Wong |
| --- | --- | --- |
| Max kappa(A) | (1.46155) + (4.13281 * ) + (-2.57812 * 2) + (1.41016 * 3) | 1.082+2.747/A |
| Min qcyl(A) | (-0.115479) + (14.5293 * ) + (-27.4492 * 2) + (18.334 * 3) | 1.21+1.3*A-0.25*A2 |
| alpha_n(A) = alpha_T(A) | (0.64-0.3*)/2 | 0.25 |
| Peakfactor | [∫(1-(x)2)alpha_T(1-(x)2)alpha_ndx]-1, (x=r/a) | [∫(1-(x)2)alpha_T(1-(x)2)alpha_ndx]-1 (x=r/a) |
| Max Beta_N(A) | ((6.96436) + (-14.043 * ) + (45.5 * 2) + (-31.3086 * 3))/100 | (3.09+3.35/A+3.87/A0.5)*(/3)0.5/ peakfactor0.5 |
| kbs | 0.344+0.195*A | 0.6783+0.0446/A |
| fbs | Kbs*Beta_P* peakfactor0.25/A0.5 | Kbs*Beta_P* peakfactor0.25/A0.5 |
| Eta_CD | 0.025*<T> | 0.025*<T> |

### Detailed Methodology

Zero-d physics algorithms along with various engineering equations were programmed into an EXCEL spreadsheet, and the EXCEL Solver was used to arrive at design point optimums, given optimization criteria and constraints. The following is a description of the basis for this work, with an explanation of each of the major variables, in the same order as the calculation sequence.

Plasma Shape Variables (R0, a A, 

Plasma cross sectional shape (95% flux surface, containing 95% of the plasma poloidal magnetic flux) is described by...

where (see Fig. 4) ...

R0  = major radius (m)

a = minor radius (m)

A = aspect ratio = R0 /a

= inverse aspect ratio = 1/A

= elongation

= Triangularity

= poloidal angle

Fig. 4: Plasma Cross Sectional Shape

Elongation ) Aspect Ratio Dependance

According to the MHD stability studies by Menard1 the maximum elongation as a function of inverse aspect ratio is…

max() = 1.46155 + 4.13281 *  -2.57812 * 2 + 1.41016 * 3

Similarly, according to Wong2 the maximum elongation as a function of aspect ratio is…

max() = 1.082+2.747/A

A comparison of these results is given in Fig. 5.

Fig. 5: Max. Elongation vs. A

# MHD Safety Factor

The MHD safety factor, number of toroidal rotations per poloidal rotation of a field line on the 95% flux surface, is expressed in two forms, namely qcyl and qMHD, which are defined as follows….

where…

BT  = vacuum toroidal field at R0  (T)

Ip  = plasma current  (MA)

The calculations described herein rely primarily on qcyl and report qMHD as an output, for information only.

MHD Safety Factor Aspect Ratio Dependance

According to the MHD stability studies by Menard1 the minimum safety factor as a function of aspect ratio is…

qcyl min(A) = 12.259-13.58*A+6.4286* A2-1.0417* A3

Note: Menard prescribed Tmax(), Nmax(), and max(). The writer extracted qcyl min(A)  according to …

and

According to Wong2 the minimum safety factor as a function of aspect ratio is…

qcyl min(A) = 1.21+1.3*A-0.25*A2

A comparison of these results is given in Fig. 6.

Fig. 6: Safety Factor vs. A

Toroidal Field Inner Leg

The first wall is assumed 10 cm thick, so the radial build of the TF inner leg in the midplane region is…

The radius of the inner leg in the end regions was set to…

The height of the inner leg above the midplane is assumed equal to the height of the plasma plus 4.0m, allowing for divertor, blanket, and shield…

Glidcop AL-25 material, =87% IACS, was assumed for the inner leg, based upon its radiation resistance.  The inner leg is modeled using 8 sections as depicted in Fig. 8, with water flowing in one end and out the other, heating up as the sections are traversed.

A water inlet temperature of 35oC and flow velocity of 10m/s were assumed.  The fraction of cross section containing water is chosen by the optimizer. The number of water passages per unit area is assumed equal to 500/m2, similar to ARIES-ST4, but less than prior VNS studies which were of order 2000/m2. Thus with the water cross sectional area and number of passages specified the wetted perimeter of the cooling passages is determined.

Fig. 8: TF Inner Leg

In addition to ohmic dissipation, nuclear heating is added at a rate equal to the average neutron wall loading times the surface area. This is conservative because 1) much of the heating would be received and removed via the first wall armor, and 2) the Cu is partially transparent to the neutrons. The flaring is set to 60o with respect to horizontal, with the flaring starting at 90% of the plasma height.

The thermal resistance due to the film effect and the mass flow are computed, using water properties which are computed as a function of temperature. Limits on copper and water temperature were typically set at 150oC.

Triaxial and combined (Von Mises) stresses in the inner leg are computed as follows…

where:

r = radius within conductor			a = outer radius of conductor

 = Poission’s ratio = 0.34 			Bmax = B at  r=a, Bma = µ0ITF/2a

Vertical tension is assumed equal to zero. However the above result was multiplied by a factor of 2.0 to account for the cooling passages in the conductor. An appropriate limit for Glidcop at 150oC is 100MPa.

Toroidal Field Outer Leg Return

The TF current is assumed to be returned through the outer VV shell which is constructed of aluminum, consisting of horizontal, angled, and vertical sections operating at current densities of 150, 125, and 100A/cm2, respectively. This is similar in concept to the VNS and ARIES-ST designs. The thickness of the horizontal, angled, and vertical sections is tailored to match the specified current density. Dimensions of the outer leg return circuit are chosen such that a region with 2.0m thickness is reserved for the first wall, blanket, and shield components. See Fig. 9.

Fig. 9: TF Cross Section, showing Inner Leg, Outer Leg Return,

and 2.0m Space Allocation for First Wall /Blanket/Shield

(R0=2.5m,A=1.5,=3.5,=0.6)

The horizontal section extends out to the plasma edge at radius R0+a. The height of the vertical section is equal to the plasma height 2**a. The radius to the centerline of the vertical section is located 2.5m beyond the plasma edge at radius R0+a+2.5m to allow for first wall/blanket/shield.

# Determination of Toroidal Field, Current, Input Power

The optimizer adjusts the current density in the TF inner legs along with the fraction of cross-sectional area containing water (fW) to adjust BT according to…

Total TF power consumption is equal to the sum of the dissipation in the inner and outer legs divided by the efficiency of the power supply system, assumed to be 95%...

# Determination of Plasma Current

With R0,a,, and qcyl determined the plasma current (in MA) is calculated according to...

# Poloidal Field Requirements

PF coils are assumed superconducting, so their input power is assumed equal to zero. Refrigeration power requirements are assumed lumped with balance of plant power.

#### Density and Temperature Profiles

Spatial distribution of temperature and density across the plasma cross section is assumed to be parabolic according to…

where…

r = variable in minor radius

a = minor radius of plasma = R0/A

T0,n0 = central peak temperature and density at r=0

T, N = shape exponents on temperature and density

It is noted that for these functions the peak to average ratios are equal to…

…and the line average to volume average ratios are equal to…

According to Menard the appropriate values for the exponents, consistent with his analysis, are…

According to the Wong assumption…

# Beta Limits and Aspect Ratio Dependence

According to Menard an appropriate limit on N is as follows…

According to Wong the N limit depends on A, , and pressure peaking factor. The peaking factor is as follows…

…where x=r/a

Then the N limit is as follows…

A comparison of these results is given in Fig. 10.

Fig. 10: Max. N vs. A

The optimizer chooses an actual value for N which must be ≤ Nmax. Then, with N and other variables previously determined, T can P can be calculated based on their definitions as follows…

Finally, the volume averaged pressure is…

# Bootstrap Current Fraction

Bootstrap current fraction fBS is dependant on P and aspect ratio as follows…

…where X is a function containing terms related to shape and profile. In the work described herein we apply a curve fit function X = kBS(A)*Peakfactor0.25 which results in fBS = 0.9 for the Wong case and fBS = 0.99 for the Menard case since these were the applicable bootstrap fractions for the MHD stability analysis performed. Therefore fBS is calculated as follows…

where for Menard…

and for Wong…

A comparison of these results is given in Fig. 11.

Fig. 11: Bootstrap Coefficient vs. A

Current Drive

The maximum current drive efficiency is assumed to be temperature dependant2 as follows....

where...

CDmax = maximum efficiency in units Ampere/Watt-m2

<T> = volume average temperature in keV, assume Ti=Te

The current to be driven is Ip*(1-fBS), and the current drive power (MW) requirement is...

…where ne is the electron density. Neutral beam injection (NBI) is assumed to provide the auxiliary heating power (Paux) and current drive power. The solver is constrained in such a way that CD≤ CDmax and PCD ≤  Paux.

Density

Line average electron density is related to the fraction of Greenwald Limit fGW as follows…

Electron density (volume average) is…

Helium ash density (volume average) is calculated as follows:

For power balance, total power into the plasma equals power out …

where…

P = power in  particles		Paux = auxiliary heating power

Prad = radiated power			Pfusion = total fusion power

Q = fusion power gain 		frad = radiation fraction = Prad/P

W = stored energy			E = energy confinement time

For  particle balance, the rate of  production from fusion reactions must equal the rate of  particle loss…

…where

W = energy per  particle, equal to 3.52MeV*1.6e-13Joule/MeV=5.63e-13Joule

*p=  particle confinement time after adjusting for recycling

The stored energy is related to the pressure as follows…

Rearranging and combining the prior three equations yields the following expression for helium ash density…

The ratio *p/E is an input variable assumed equal to 5.0.

For impurities, Be is assumed the dominant species (Zimp=4) at a concentration fimp = 6%.

For charge neutrality, with Z=2 for He…

The impurity density (volume average) is…

The density (volume average) of H species (50:50 DT mix) is then calculated as follows…

The total particle density (volume average) is then…

Temperature

With the volume average density determined the peak temperature can be backed-out from the pressure as follows…

Note: 1.6 x 10-19 Joule/eV

Radiation

The effective ionic charge Zeff is…

Power loss (MW), assumed to arise exclusively from Bremsstrahlung radiation is…

Alpha Power

Alpha power is calculated per the following integral…

where…

a0 = -23.836	a* = -22.712	a1 = -0.09393	a2 = 7.994e-4	a3 = -3.144e-6

As depicted in Fig. 12, the incremental volume ∆V is…

where R is the radius from the plasma center at R0.

Fig. 12: P Integration

# Plasma Stored Energy

The plasma thermal energy is …

Energy Confinement Time

Energy confinement time is calculated based on the ITER 98[y,2] scaling…

where  is the line average electron density in units 1019/m3 and M is the average mass number, equal to 2.5 for a 50:50 DT mix.

A confinement enhancement factor HH is introduced and used in the power balance equation as follows…

So, the effective confinement time is…

Neutron Wall Loading

Neutron wall loading is based on the surface area of the plasma…

Gross Thermal Power

Electricity production is assumed derived from the power in the fusion neutrons and the radiated power to the first wall. This includes energy multiplication which takes place in the blanket due to reactions involving the neutrons and the Li isotopes Energy flow through the SOL to the divertors, and other low grade heat such as dissipation in the magnets is not recovered. However, a fraction of the power from the neutrons is not captured by the blanket due to absorption by the center stack and due to the fact that the blanket does not cover 100% of the area of the plasma.

The fraction of neutrons incident on the narrow midplane region of the center stack is…

where  and  are angles in the toroidal and poloidal planes which correspond to the intersection of a cylinder (the center stack) and a unit sphere with center at the effective average point source of neutron production, which is assumed located a distance a/3 beyond R0. See Fig. 13. The angles  and  are…

where Rfw is the radius of the first wall and ∆Ztfmid is the height of the narrow midplane section of the center stack.

Fig. 13: Calculation of Solid Angle of Center Stack

Then the total useful thermal power is…

where…

fS = fraction of surface area covered by blanket (assumed = 0.9)

fBEM = blanket energy multiplication factor (assumed =1.2)

Electric Power Production

Thermal to electrical energy conversion efficiency EC is assumed 35%, so the gross electrical power production is…

Operation of the “balance of plant” is assumed to consume a fraction (fBOP=10%) of the gross electric power production, so the net electric power is…

Variables Adjustable by Solver

Typically the Solver is set up to adjust the following variables to obtain a solution…

frad, fGW, N, qcyl, Pfusion, CD, JTF, fW

In other cases more variables may be added to this list, such as R0 or A.

Solver Constraints for Valid Solutions

In obtaining a solution the Solver iterates to satisfy the following constraints which are required for a mathematically valid solution:

- Value of frad used to calculate E, nHe, Ptot and subsequent dependent variables must be equal to ratio of calculated values Pbrem/P.

- Value of Pfusion used to calculate Q and subsequent dependent variables must be equal to calculated value 5*P.

- Value CD must be  ≤  CDmax (T) = 0.025<T>

- Value of PCD must be ≤ Paux

Other Solver Constraints

The following additional constraints are applied to ensure that physics and engineering limits are realistic…

- N ≤ Nmax

- qcyl ≥ qcylmin

- 0.1 ≤ fBS ≤ 0.99

- 0.1 ≤ fGW ≤ 1

- TF ≤ 100MPa

- TTFCu ≤ 150C

- TTFH20 ≤ 150C

- 0.05 ≤ fW ≤ 0.3

Additional constraints are sometimes added to limit the solution to a particular range of interest such as:

- HH = or ≤  an input value

- Nwall = or ≤ an input value

# Footnotes

S. Jardin et al, Systems Analysis of a Compact Next Step Burning Plasma Experiment, PPPL-3666 (2002), to appear in Fusion Engineering and Design

J. Menard e-mail correspondance of 7/23/02 and 7/25/02 and draft manuscript “Ideal MHD Stability Limits of Advanced Tokamak Plasmas and Implications for the ST”

C. Wong et al, “Toroidal Reactor Designs as a Function of Aspect Ratio and Elongation”, Nuclear Fusion, 42 (2002) 547-556

S. Jardin et al, Systems Analysis of a Compact Next Step Burning Plasma Experiment, PPPL-3666 (2002), to appear in Fusion Engineering and Design

Toroidal Field Coil Design for ARIES-ST”, W Reiersen et al, 17th SOFE, San Diego

“Special Issue: ST VNS and Applications”, Fusion Engineering Design, Vol 45 (1999) No 3

“Spherical Torus Center Stack Design”, C Neumeyer et al, 19th SOFE