TC4 ER-2 Science Flight: July 29, 2007

Tentative Flight Plan

Flight Scientists: P. Newman, S. Platnick

Sortie: 07-9021

Pilot:	Denis Steele

Takeoff (MROC):	1200 UTC (6:00 AM local)

Landing (MROC):	1745 UTC (11:45 AM local)

Duration: 5:45

Objectives:

- To investigate marine stratus near the equator in support of Terra/CloudSat.

- To investigate volcanic SO2 emissions in support of OMI

- Underfly Terra with ER-2/DC-8, ER-2 aligned with track

Satellite Coordination:

The Terra overpass occurs at approximately 1556 UT (a heading of 192.05˚) while the ER-2 is expected to be south of Costa Rica near the equator (see map of waypoints). The image below shows the Terra overpass as the blue (Douglas Spangenberg, LaRC).

The Aqua, Cloudsat/Calipso, Aura overpasses occur 1853, 1854, and 1909 UT respectively near the equator near Ecuador.  The TRMM overpass is also close to Costa Rica, but occurs prior to the ER-2 launch at 1052 UT.

Flight Plan Summary (see map):

Takeoff at 1200 UT (6 AM local time).  The ER-2 initially flies S over the Pacific towards a region where  (waypoint 3 on the map) marine stratus is expected.  The ER-2 will then fly NW along a line (3(4) in order to link up with the DC-8 at approximately 1410 UT.  After reaching 4, the ER-2 will fly reverse course and fly a line southeast line to waypoint 5 (above the DC-8 and following a regular jetway path).   The ER-2 will again reverse course at waypoint 5 and fly back to waypoint 4.  At 1544 the ER-2 will turn onto a heading of 11.95 to parallel the Terra track.  Following the Terra overpass, the ER-2 will return to MROC (plot courtesy of Chuck Bardeen).

grey line = ER-2 flight track

color image: low level cloud fraction (1800 UT)

yellow wind barbs (m/s) for 500 hPa.

Expected Cloud Conditions during flight:

The track 4(5 is set in a marine stratus region. The forecast map (see above) shows expected low level cloud cover.  The 500 hPa (mid-troposphere) wind pattern shows weak SE flow.

Proposed Plan:

Proposed Waypoints:

WP		Lat		Lon		ETA

MROC		10o 00'N      	84o 13'W      	14:00

ER-2 Science Instrument Payload and Status:

| Instrument | Status | Notes |
| --- | --- | --- |
| CPL Cloud Physics Lidar |  |  |
| CRS Cloud Radar System |  |  |
| EDOP ER-2 Doppler Radar |  |  |
| AMPR Advanced Microwave Precipitation Radiometer |  |  |
| CoSSIR Compact Scanning Sub-mm wave Imaging Radiometer |  |  |
| MAS MODIS Airborne Simulator |  |  |
| S-HIS Scanning High Resolution Interferometer |  |  |
| IR Radiometer Broadband flux radiometer (nadir & zenith) |  |  |
| SSFR Solar Spectral Flux Radiometer (nadir & zenith) |  |  |
| MVIS video camera |  |  |
| MTP Microwave Temperature Profiler |  |  |

## G = good; P = partial data collected; F = failure, no data