NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 01/09/2005, 12/20/2006

LOCATION: Decatur

STREAM: Tennessee River

BASIN: Tennessee                        HSA: HUN

REFERENCES:

FROM USGS DESCRIPTION OF GAGING STATION.

ZERO DATUM BASED ON WHITESBURG ZERO DATUM. ACTUAL MSL HEIGHT IS LOWER.

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level	TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: DECA1

NWS INDEX NUMBER:

USGS NUMBER: 03577150

MAP OF GAGE LOCATION

LATITUDE: 34 36 47  		SOURCE: USGS WATER YEAR BOOK

LONGITUDE: 86 58 26

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:  549.000         VERTICAL DATUM: NGVD

LEVELING AGENCY AND DATE:                        CHECKBAR:

RATING AGENCY:

BENCHMARK     DESCRIPTION                                                                   GAGE ZERO      DATUM

----------------------------------------------------------------------------------------    ---------     -------

RM-1          STANDARD USGS MARK TABLET IN THE TOP OF RIGHT WALL OF NORTH BASCULE PIER          8.260     557.260

OF THE HIGHWAY BRIDGE. IT IS ONE FOOT FROM THE RIGHT EDGE OF THE PIER AND

10 FT UPSTREAM/10 FT TO THE RIGHT OF RIGHT UPSTREAM CORNER OF THE GAGE

HOUSE. (557.26 MSL)

RM-3          COPPER BOLT SET IN TOP OF THE DRAW PIER OF THE RAILROAD BRIDGE, 1/2 MILE         14.893     563.893

DOWNSTREAM FROM THE GAGE. SET 6 INCHES BACK FROM THE DS SIDE OF THE PIER,

BETWEEN THE SIDES OF AN IRON LADDER, DIRECTLY OVER OLD USWB GAGE.

(563.893)

RM-4          CROSS CUT ON THE BRIDGE SEAT STONE 1 FOOT FROM THE DS END OF THE LEFT            18.961     567.961

ABUTMENT OF THE RAILROAD BRIDGE, 1/2 MILE DS OF THE GAGE. (567.961)

RM-6          STANDARD USGS BRONZE TABLET SET IN THE BASE OF THE GAGE HOUSE STEPS IN            9.998     558.998

FRONT OF DOOR.

RM-7          BOLT SET IN THE TOP OF THE LEFT HORIZONTAL CONCRETE STRUT IN THE LEFT BANK        5.771     554.771

PIER OF THE HIGHWAY BRIDGE...ONE FOOT UPSTREAM FROM THE INSIDE FACE OF

THE DS PIER WALL. (554.771)

RM-8          (8/21/06) 3/8 INCH LAG BOLT IN UTILITY POLE 25 FEET SOUTH OF GAGE HOUSE.         11.374     560.374

RM-9          (8/21/06) 3/8 INCH LAG BOLT IN STREAMWARD SIDE OF 4X6 HOLDING 1ST STAFF.          7.903     556.903

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID: 17C1B6FA                TYPE OF TELEMETRY:

OWNER: USGS                                OWNER:

REPORT TIME: 03:55                        PHONE NUMBER:

INTERVAL: 240                              INTERVAL:

PAYOR/COST OF LINE:  / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- ------------------------------------------------------

Unk         TVA         TVA         12/01/1926 09/30/1990

pres trans  USGS        USGS        10/01/1990            USGS WATER STAGE RECORDER WITH DCP.  TOOK OVER 									  OPERATION FROM TVA.

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

Unk                       TVA         12/01/1926       09/30/1990

pres trans                USGS        10/01/1990

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

549.000                              10/01/1936

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 10.00    ACTION STAGE: 9.00      BANKFULL STAGE:

FLOOD FLOW:           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ----------------------------------------------

03/15/1867 UNDEF   14.80

03/18/1973 UNDEF    9.97

08/13/2001 UNDEF    8.07

02/18/2003 16:45    8.23

05/10/2003 12:30   10.29

02/08/2004 11:00    8.09

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 5: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

12/08/1962    -0.10

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH: 305.1      DRAINAGE AREA: 26900.0     POOL STAGE:

STREAM BED: WIDE DUE TO WHEELER LAKE.

REACH: APPROX 7 MI US TO 3 MI DS.

REGULATION: REGULATED BY GUNTERSVILLE DAM UPSTREAM AND WHEELER DAM

DOWNSTREAM.

DIVERSION: NONE.

WINTER: NONE.

TOPOGRAPHY: FLATLAND RIVER VALLEY.

REMARKS: NONE.

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  ---------------------------------------------------------------------------------------------

9.00  ACTION STAGE. WATER BEGINS TO BACK UP FROM THE TENNESSEE RIVER INTO TRIBUTARIES. FLOODING OF 		       A ROADSIDE PARK ON THE LIMESTONE COUNTY BANK OF THE RIVER ON US 31 IS OCCURRING.

10.00  FLOOD STAGE. PORTIONS OF MARKET STREET AND COUNTRY CLUB ROAD IN DECATUR ARE COVERED BY		       WATER...AND A PORTION OF POINT MALLARD PARK FLOODS. FLOODING ALSO AFFECTS LOW LYING AREAS OF	       LIMESTONE COUNTY WITHIN THE WHEELER WILDLIFE REFUGE.

10.29  RECORD FLOOD (POST-DAM). OCCURRED ON 05/10/2003. THIS IS THE HIGHEST FLOOD ON RECORD SINCE 		       THE INSTALLATION OF DAMS AT WHEELER AND GUNTERSVILLE.

12.00  MODERATE FLOODING. EXTENSIVE BACKWATER FLOODING IS OCCURRING ON FLINT CREEK AND SWAN CREEK	    	NEAR DECATUR. FLOODWATERS MAY THREATEN HOMES ALONG THE RIVER EDGE...AND CAUSE ROAD CLOSURES.

14.00  MAJOR FLOODING. MAJOR TRIBUTARY FLOODING IS OCCURRING DUE TO BACKWATER. SIGNIFICANT PORTIONS  	OF THE CITY OF DECATUR...NEAR THE TENNESSEE RIVER AND FLINT CREEK...ARE FLOODED. POINT 	MALLARD PARKWAY BETWEEN US 31 AND PRICEVILLE IS COMPLETELY FLOODED AND CLOSED. PORTIONS OF 	SOUTHERN LIMESTONE COUNTY NEAR WHEELER LAKE ARE FLOODED.

14.80  RECORD FLOOD (PRE-DAM). OCCURRED ON 03/15/1867 (BEFORE THE INSTALLATION OF DAMS ALONG THE				TENNESSEE RIVER).

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  16-|

|-----|

|-----|

|-----|

|-----|

|  15-|

|-----|

14.80 - RECORD FLOOD (PRE-DAM). OCCURRED ON 03/15/1867 (BEFORE THE INSTALLATION OF DAMS ALONG   |-----|   14.80  03/15/1867

THE TENNESSEE RIVER).                                                                   |-----|

|-----|

|  14-|

14.00 - MAJOR FLOODING. MAJOR TRIBUTARY FLOODING IS OCCURRING DUE TO BACKWATER. SIGNIFICANT     |-----|

PORTIONS OF THE CITY OF DECATUR...NEAR THE TENNESSEE RIVER AND FLINT CREEK...ARE        |-----|

FLOODED. POINT MALLARD PARKWAY BETWEEN US 31 AND PRICEVILLE IS COMPLETELY FLOODED       |-----|

AND CLOSED. PORTIONS OF SOUTHERN LIMESTONE COUNTY NEAR WHEELER LAKE ARE FLOODED.        |-----|

|  13-|

|-----|

|-----|

|-----|

|-----|

|  12-|

12.00 - MODERATE FLOODING. EXTENSIVE BACKWATER FLOODING IS OCCURRING ON FLINT CREEK AND SWAN    |-----|

CREEK NEAR DECATUR. FLOODWATERS MAY THREATEN HOMES ALONG THE RIVER EDGE...AND CAUSE     |-----|

ROAD CLOSURES.                                                                          |-----|

|-----|

|  11-|

|-----|

|-----|

|-----|

10.29 - RECORD FLOOD (POST-DAM). OCCURRED ON 05/10/2003. THIS IS THE HIGHEST FLOOD ON RECORD    |-----|   10.29  05/10/2003

SINCE THE INSTALLATION OF DAMS AT WHEELER AND GUNTERSVILLE.                             |  10-|

10.00 - FLOOD STAGE. PORTIONS OF MARKET STREET AND COUNTRY CLUB ROAD IN DECATUR ARE COVERED     |-----|    9.97  03/18/1973

BY WATER...AND A PORTION OF POINT MALLARD PARK FLOODS. FLOODING ALSO AFFECTS LOW        |-----|

LYING AREAS OF LIMESTONE COUNTY WITHIN THE WHEELER WILDLIFE REFUGE.                     |-----|

|-----|

|   9-|

9.00 - ACTION STAGE. WATER BEGINS TO BACK UP FROM THE TENNESSEE RIVER INTO TRIBUTARIES.        |-----|

FLOODING OF A ROADSIDE PARK ON THE LIMESTONE COUNTY BANK OF THE RIVER ON US 31 IS       |-----|

OCCURRING.                                                                              |-----|

|-----|    8.23  02/18/2003

|   8-|    8.09  02/08/2004

|-----|

|-----|

|-----|

|-----|

|   7-|

|-----|

|-----|

|-----|

REACH: APPROX 7 MI US TO 3 MI DS.                                                      	ELEVATION ZERO:  549.00

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                     NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

1  Morgan County EMA                                  256-351-4620

Director:  Eddie Hicks

LOCATION: Tennessee River AT Decatur, AL                            Revised, Printed Dates: 01/09/2005, 12/20/2006

ID: DECA1                          HSA: HUN                    NWS FORM E-19 PAGE 10: CONTACTS

Photos not available at this time.