THE MARINE GEOPHYSICAL DATA EXCHANGE FORMAT - "MGD77"

(Bathymetry, Magnetics, and Gravity)

NATIONAL GEOPHYSICAL DATA CENTER

NATIONAL ENVIRONMENTAL SATELLITE, DATA, AND INFORMATION SERVICE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

U.S. DEPARTMENT OF COMMERCE

KEY TO GEOPHYSICAL RECORDS DOCUMENTATION NO. 10 (REVISED)

COMPILED BY THE MGD77 TASK GROUP

Allen M. Hittelman, Chairman

Robert C. Groman

Richard T. Haworth

Troy L. Holcombe

Graig McHendrie

Stuart M. Smith

National Geophysical Data Center

Boulder, Colorado

September 1977

December 1981 (Revised by Dan Metzger)

February 1989 (Revised by Dan Metzger)

January  1993 (Revised by Dan Metzger)

October  1995 (Revised by Dan Metzger)

August   1998 (Revised by Dan Metzger)

### Table Of Contents

INTRODUCTION...............................................I

GENERAL DESCRIPTION.......................................II

THE HEADER RECORD........................................III

THE DATA RECORD...........................................IV

10-DEGREE IDENTIFIER CODE.........................APPENDIX A

NGDC CONTACTS.....................................APPENDIX B

I.                      INTRODUCTION

In January of 1977, a group of 24 geophysical data

managers from academia, government, industry and foreign

countries participated in a workshop at the National

Geophysical Data Center (NGDC) in Boulder, Colorado.  The

"Workshop for Marine Geophysical Data Formats" established

the basic outline of a new format for the exchange of

digital underway geophysics data.  A six member task force

was formed to work with NGDC in implementing the decisions

of the workshop into the new format.  By the end of 1977 the

"MGD77" format was being disseminated by NGDC as its

standard exchange format.

The "MGD77" format has experienced much success over

the past 15 years.  It has been sanctioned by the Intergov-

ernmental Oceanographic Commission (IOC) as an accepted

standard for international data exchange, and it has been

translated into French, Japanese, and Russian.  Most con-

tributors of data to NGDC now send transfer data over the

internet in the "MGD77" format.

This newest revision makes the MGD77 format "Year 2000

Compliant", ensuring it's success into 21st Century.

II.                  GENERAL DESCRIPTION

The digital format presented, and referred to as

"MGD77", is an exchange format for marine geophysical data

(bathymetry, magnetics, and gravity)  It is intended to be

used for the transmission of data to and from a data center

and may be useful for the exchange of data to and from a

data center and may be useful for the exchange of data

between marine institutions.  Data is to be exchanged in

files, one file per survey operation.  Generally each survey

operation is a port-to-port operation of a survey vessel,

but in some cases several port-to-port operations of the

same vessel are combined in single survey operation,

especially if this is the manner of organizing the data at

the contributing institution.  Data may be exchanged on via

the Internet or on various mass storage devices such as 8mm

or 9 track tapes, removable disks.  The National Geophysical

Data Center uses CD-ROM disks as its chief method of distribution

of these data.

Data Exchange

1. For exchange of MGD77 data via mass storage files on

magnetic or optical media participants shall establish type

and format of the media to be exchanged.

2. Each survey operation shall be contained in one file

with Header and Data Records, or in 2 files, one Header

file and one Data Record file.  If  the media is too small

to contain one survey the data may be continued on a second

media.

3. Each survey operation shall have one MGD77 Header

consisting of 24 80-character logical records.

4. The MGD77 data records are sequentially and chronologically

organized until the end of the file.  The data records are 120

logical characters.

5. A survey is defined as all observations that conveniently

constitute a survey operation (e.g., a port-to-port survey or

in some cases several surveys).  A survey file(s) ideally

should not span two media.

6. For sequential files, the MGD77 Header shall consist of

24 sequential records of 80 logical characters each separated

by an end-of-record character(s) and, if the data records are

in the same file, the Header shall be at the beginning of the

file.  The MGD77 Data Records shall be 120 logical characters

each.

7. 9 Track tapes should be recorded as ASCI 1600 or 6250 BPI.

The tape structure consists of physical records of 1920

characters each, a header followed by data records, separated

by inter-record gaps (IRG) and organized into files. The files

are separated by end-of-file (EOF) marks (sometimes called

tape marks).

III.                  THE HEADER RECORD

The purpose of the Header Record is to document both

the content and structure of the geophysical data contained

within subsequent data records.  In general, documentation

that is constant throughout the survey will be in the Header

Record, while documentation that is variable will be in the

Data Records.

For sequential files, the MGD77 Header consists of 24

80-character sequential records.  For 9 track magnetic tapes

the MGD77 Header is a physical record (block) consisting of

1,920 characters. In both cases the data records follow

immediately with no intervening end-of-file marks.

The Header Record contains fields which are both fixed

and freely formatted.  All field lengths within the Header

that have not been coded with information should be blank-

filled, and all plain language statements should be left-

justified.  The Header consists of a "sequence" of twenty-

four 80-character images.  The field lengths within the

Header Records are designed to allow one to read the

information (from magnetic tapes) as a series of 120-

character logical records -- the same logical record length

as the data records.

To help the marine geophysical community prepare this

documentation, a coding pad is available free of charge from

the National Geophysical Data Center.

Format Conventions for the Header Record:

1. All decimal points are implied.

2. Leading zeros and blanks are equivalent.

3. Unknown or unused fields are to be blank filled.

4. All "corrections", such as time zone, diurnal magnetics,

and Eotvos, are understood to be added (e.g., time-zone

correction is the number of hours which must be added

to the recorded time to determine GMT).

*** CHANGES SINCE LAST REVISION ***

Several changes in the MGD77 Header were required in order to

make the format "Year 2000 Compliant" (Y2K Compliant):

SEQUENCE   DESCRIPTOR           CHANGE

______________________________________________-

01         RECORD TYPE           Change from "1" to "4"

01         FILE CREATION DATE    Change to include century

From 6 digits (col 32-37)

to 8 digits (col 32-39)

01         SOURCE INSTITUTION    Change from 41 chars (col 38-78)

to 39 chars (col 40-78)

04         SURVEY DEPARTURE DATE Change to include century

From 6 digits (col 1-6)

to 8 digits (col 1-8)

04         PORT OF DEPARTURE     Change from 34 chars (col 7-40)

to 32 chars (col 9-40)

04         SURVEY ARRIVAL DATE   Change to include century

From 6 digits (col 41-46)

to 8 digits (col 41-48)

04         PORT OF ARRIVAL       Change from 32 chars (col 47-78)

to 30 chars (col 49-78)

The following is a detailed description of the Header Record.

Fields can be of type integer, real or character.  Fields that

represent whole numbers are integers  Fields that contain a

decimal component are real, and fields that are alphanumeric

are character.

Character	Field

Nos. 	Length	Type     Description

_____________________________________________________

Sequence No. 1

1	1	int      RECORD TYPE - Set to "4" (Header)

nnccIDENT2

2-9	8	char     SURVEY IDENTIFIER

nnccCRUISE                   Identifier supplied by the contributing

organization, else given by NGDC in

a manner which represents the data.

Identical to that in data record.

10-14	5	char     FORMAT ACRONYM - Set to"MGD77"

nnccACRNYM

15-22	8	int      DATA CENTER FILE NUMBER

nnccDCFNUM                   Survey identifier bestowed by the data

nnccHDNUM1                   center.  First 2 chars indicate the

nnccHDNUM2                   source, first 4 indicate platform.

nnccDANUM

27-31	5	int      PARAMETERS SURVEYED CODE

Status of geophysical parameters for

this survey.

COLUMN  PARAMETER SURVEYED

nnccBATHCD/nnccBATHX        27      bathymetry (e.g., 12

kHz or 3.5 kHz used

for bathymetry)

nnccMAGCD/nnccMAGX           28      magnetics

nnccGRAVCD/nnccGRAVX         29      gravity

nnccHRSSCD/nnccHRSSX         30      high-resolution seismics

(e.g., 3.5 kHz)

nnccDPSSCD/nnccDPSSX         31      deep penetration seismics

(e.g., large airgun)

CODE - (for columns 27-31)

0 or blank - unspecified

1 - Parameter NOT surveyed

3 - Parameter surveyed,

not contained in file

5 - Parameter surveyed,

contained in file

32-39	8	int      FILE CREATION DATE (YYYYMMDD)

nnccDATE2                    Date data records were last

altered (including century).

40-78	39	char     SOURCE INSTITUTION

nnccINST                     Organization which collected the

data. Include contributor if different

from collector.

79-80	2	int      SEQUENCE NUMBER - Set to "01"

nnccSEQ1

Sequence No. 2

1-18	18	char     COUNTRY

nnccCNTRY

19-39	21	char     PLATFORM NAME

nnccPLTFRM

40	1	int      PLATFORM TYPE CODE

nnccPLTCD                    0 - Unspecified

nnccPLTX                     1 - Surface ship

2 - Submersible ship

3 - Aircraft

4 - Buoy

5 - Mobile land

6 - Fixed land

7 - Deep tow

8 - Anchored seafloor instrument

9 - Other, specify

41-46       6       char     PLATFORM TYPE

nnccPLTTP               (e.g., "SHIP","PLANE", "SUB", etc.)

47-78       32      char     CHIEF SCIENTIST(S)

nnccSCI

79-80       2       int      SEQUENCE NUMBER - Set to "02"

nnccSEQ2

Sequence No. 3

1-58        58      char     PROJECT

nnccPROJ                     (e.g., "SURVOPS 6-69",

"INDOPAC, Leg3")

59-78       20      char     FUNDING

nnccFUND                     (i.e. agency or institution)

79-80       2       int      SEQUENCE NUMBER - Set to "03"

nnccSEQ3

Sequence No. 4

1-8         8       int      SURVEY DEPARTURE DATE (YYYYMMDD)

nnccDPDT

9-40        32      char     PORT OF DEPARTURE

nnccDPPRT                    (i.e. city, country)

41-48       8       int      SURVEY ARRIVAL DATE (YYYYMMDD)

nnccARDT

49-78       30      char     PORT OF ARRIVAL

nnccARPRT                    (i.e. city, country)

79-80       2       int      SEQUENCE NUMBER - Set to "04"

nnccSEQ4

Sequence No. 5

1-40        40      char     NAVIGATION INSTRUMENTATION

nnccNAVIN                    (e.g. "SAT/LORAN A/SEXTANT")

41-78       38      char     GEODETIC DATUM/POSITION

nnccNAVMTH                   DETERMINATION METHOD

(e.g. "WGS84/PRIM - SATELLITE,

SEC-LORAN A")

79-80       2       int      SEQUENCE NUMBER - Set to "05"

nnccSEQ5

Sequence No. 6

1-40        40      char     BATHYMETRY INSTRUMENTATION

nnccBATHIN                   Include information such as

frequency, beam width, and sweep

speed of recorder.

41-78       38      char     ADDITIONAL FORMS OF BATHYMETRIC DATA

nnccBATHDA                   (e.g., "MICROFILM",

"ANALOG RECORDS")

79-80       2       int      SEQUENCE NUMBER - Set to "06"

nnccSEQ6

Sequence No. 7

1-40        40      char     MAGNETICS INSTRUMENTATION

nnccMAGIN                    (e.g., "PROTON PRECESSION

MAG-GEOMETRICS G-801")

41-78       38      char     ADDITIONAL FORMS OF MAGNETICS DATA

nnccMAGDA                    (e.g., "PUNCH TAPE",

"ANALOG RECORDS")

79-80       2       int      SEQUENCE NUMBER - Set to "07"

nnccSEQ7

Sequence No. 8

1-40        40      char     GRAVITY INSTRUMENTATION

nnccGRAVIN                   (e.g., "L and R S-26")

41-78       38      char     ADDITIONAL FORMS OF GRAVITY DATA

nnccGRAVDA                   (e.g., "MICROFILM", "ANALOG

RECORDS")

79-80       2       int      SEQUENCE NUMBER - Set to "08"

nnccSEQ8

Sequence No. 9

1-40        40      char     SEISMIC INSTRUMENTATION

nnccSEISIN                   Include the size of the sound

source, the recording frequency

filters, and the number of

channels (e.g., "1700 cu. in.,

AIRGUN, 8-62 Hz, 36 CHANNELS")

41-78       38      char     FORMATS OF SEISMIC DATA

nnccSEISDA                   (e.g., "DIGITAL", "MICROFILM",

"NEGATIVES", etc.)

79-80       2       int      SEQUENCE NUMBER - Set to "09"

nnccSEQ9

Sequence No. 10

1           1       char     FORMAT TYPE

nnccFORMAT                   Set to "A", which means format

contains integers, floating points,

and alphanumerics

2-75        74      char     FORMAT DESCRIPTION

nnccFRTRN1                   This is one method of reading

nnccFILL1                    (not writing) the data in FORTRAN.

Set to the following:

"(I1,A8,F5.2,4I2,F5.3,F8.5,F9.5,I1,F6.4,

F6.1,I2,I1,3F6.1,I1,F5.1,F6.0,F7.1,"

(NOTE: continued in sequence no. 11)

79-80       2        int     SEQUENCE NUMBER - Set to "10"

nnccSEQ10

Sequence No. 11

1-17        17      char     FORMAT DESCRIPTION

nnccFRTRN2                   Continued, set to following:

nnccFILL2                    "F6.1,F5.1,A5,A6,I1)"

41-43       3       int      TOPMOST LATITUDE OF SURVEY  **

nnccLATTOP                   (to next whole degree)

44-46       3       int      BOTTOMMOST LATITUDE

nnccLATBOT

47-50       4       int      LEFTMOST LONGITUDE

nnccLONGLT

51-54       4       int      RIGHTMOST LONGITUDE

nnccLONGRT

nnccFILL3

79-80       2       int      SEQUENCE NUMBER - Set to "11"

nnccSEQ11

Sequence No. 12

1-3         3       real     GENERAL DIGITIZING RATE OF

nnccDIGRT1                   BATHYMETRY

In tenths of minutes.

The rate which is present within

the data records (e.g., if values were

coded every 5 minutes, set to "050")

4-15        12      char     GENERAL SAMPLING RATE OF

nnccSMPRT1                   BATHYMETRY

This rate is instrumentation dependent

(e.g., "1/SECOND")

16-20       5       real     ASSUMED SOUND VELOCITY

nnccSNDVEL                   In tenths of meters per second.

Historically, in the U.S., this

speed has been 800 fathoms/sec,

which equals 1463.0 meters/sec.;

however, some recorders have a

calibration of 1500 meters/sec

(e.g., "14630")

21-22       2       int      BATHYMETRIC DATUM CODE -

nnccBATHDM                   00 - No correction applied (sea level)

nnccBATHDMX                  01 - Lowest normal low water

02 - Mean lower low water

03 - Lowest low water

04 - Mean lower low water spring

05 - Indian spring low water

06 - Mean low water spring

07 - Mean sea level

08 - Mean low water

09 - Equatorial spring low water

10 - Tropic lower low water

11 - Lowest astronomical tide

88 - Other, specify in

additional documentation

23-78       56      char     INTERPOLATION SCHEME

nnccINTRPL                   This field allows for a description

of the interpolation scheme used,

should some of the data records contain

interpolated values (e.g., "5-MINUTE

INTERVALS AND PEAKS AND TROUGHS").

79-80       2       int      SEQUENCE NUMBER - Set to "12"

nnccSEQ12

Sequence No. 13

1-3         3       real     GENERAL DIGITIZING RATE OF

nnccDIGRT2                   MAGNETICS

In tenths of minutes.

The rate which is present

within the data records.

4-5         2       int      GENERAL SAMPLING RATE OF

nnccSMPRT2                   MAGNETICS

In seconds.

This rate isinstrumentation dependent

(e.g., if the pulse rate is every 3 sec,

set to "03")

6-9         4       int      MAGNETIC SENSOR TOW DISTANCE

nnccSENDST                   In meters.

The distance from the navigation

reference to the leading sensor.

10-14       5       real     SENSOR DEPTH

nnccSENDTH                   In tenths of meters.

This is the estimated depth of the

lead magnetic sensor.

15-17       3       int      HORIZONTAL SENSOR SEPARATION

nnccSENSEP                   In meters.

If two sensors are used.

18-19       2       int      REFERENCE FIELD CODE - This is the

nnccREFCD                    reference field used to determine

the residual magnetics:

00 - Unused

01 - AWC 70

02 - AWC 75

03 - IGRF-65

04 - IGRF-75

05 - GSFC-1266

06 - GSFC (POGO) 0674

07 - UK 75

08 - POGO 0368

09 - POGO 1068

10 - POGO 0869

11 - IGRF-80

12 - IGRF-85

13 - IGRF-90

88 - Other, specify

20-31       12      char     REFERENCE FIELD

nnccREFFLD                   (e.g., "IGRF-85")

32-78       47      char     METHOD OF APPLYING RESIDUAL FIELD

nnccRESFLD                   The procedure used in applying

this reduction to the data

(e.g., "LINEAR INTERP. in

60-mile SQUARE")

79-80       2       int      SEQUENCE NUMBER - Set to "13"

nnccSEQ13

Sequence No. 14

1-3         3       real     GENERAL DIGITIZING RATE OF  GRAVITY

nnccDIGRT3                   In tenths of minutes.

The rate present within the data records

4-5         2       int      GENERAL SAMPLING RATE OF GRAVITY

nnccSMPRT3                   In seconds.

This rate is instrumentation dependent.

If recordingis continuous, set to "00"

6           1       int      THEORETICAL GRAVITY FORMULA CODE

nnccTGFMCD                   1 - Heiskanen 1924

2 - International 1930

3 - IAG System 1967

4 - IAG System 1980

8 - Other, specify

7-23        17      char     THEORETICAL GRAVITY FORMULA

nnccTGFM                     (e.g., "INTERNATIONAL '30", "IAG

SYSTEM (1967)", etc.)

24          1       int      REFERENCE SYSTEM CODE

nnccRFSYCD                   Identifies the reference field:

1 - Local system, specify

2 - Potsdam system

3 - System IGSN 71

9 - Other, specify

25-40       16      char     REFERENCE SYSTEM

nnccRFSY                     (e.g., "POTSDAM SYSTEM",

"SYSTEM IGSN 71", etc.)

41-78       38      char     CORRECTIONS APPLIED

nnccCORRCT                   Drift, tare and bias corrections

applied. (e.g., "+0.075 MGAL PER DAY")

79-80       2       int      SEQUENCE NUMBER - Set to "14"

nnccSEQ14

Sequence No. 15

1-7         7       real     DEPARTURE BASE STATION GRAVITY

nnccDGRVBS                   In tenths of milligals.

At sea level (Network value preferred.)

8-40        33      char     DEPARTURE BASE STATION DESCRIPTION

nnccDGRVDS                   Indicates name and number of station

41-47       7       real     ARRIVAL BASE STATION GRAVITY

nnccAGRVBS                   In tenths of milligals.

At sea level (Network value preferred.)

48-78       31      char     ARRIVAL BASE STATION DESCRIPTION

nnccAGRVDS                   Indicates name and number of station

79-80       2       int      SEQUENCE NUMBER - Set to "15"

nnccSEQ15

Sequence No. 16

1-2         2       int      NUMBER OF 10-DEGREE IDENTIFIERS    **

nnccAREAID                   This is the number of 4-digit

nnccFILL4                    10-degree identifiers, excluding

the "9999" flag, which will

follow this field. (see APPENDIX B)

4-78        75      int      10-DEGREE IDENTIFIERS - This is a

nnccAEREAF1                  series of 4-digit codes,separated by

commas, which identify the 10-degree

squares through which the survey

collected data (see APPENDIX B).

Code "9999" after last identifier.

79-80       2       int      SEQUENCE NUMBER - Set to "16"

nnccSEQ16

Sequence No. 17

1-75        75      int      10-DEGREE IDENTIFIERS

nnccAREAF2                   Continued

79-80       2       int      SEQUENCE NUMBER - Set to "17"

nnccSEQ17

Sequence Nos. 18-24

1-78        78      char     ADDITIONAL DOCUMENTATION

nnccADD18… NnccADD24         information concerning this survey

not contained in header fields.

79-80       2       int      SEQUENCE NUMBER ("18" thru "24")

nnccSEQ18… nnccSEQ24

______________

** Fields 41-54 in sequence Number 11 and Fields 1-78 in

sequence numbers 16 and 17 may be blank filled by the

contributing institution.  The data center can determine

these numbers by a computer search of the latitudes and

longitudes within the MGD77 file.

IV.                    THE DATA RECORD

The data record presents underway marine geophysical

data in a correlative manner.  Geophysical data (bathymetry,

magnetics, and gravity) and seismic identification (shot-point

identification) are presented with a corresponding time and

position.  Documentation that is variable throughout the

survey also is included within each data record.  If primary

navigation exists at a juncture where no geophysical data

are present, this record should be included with the data

parameter fields left unused (9s filled).

The logical record length is 120 characters and the

blocking factor is 16 logical records per physical record

(i.e., 1,920 characters).

*** CHANGES SINCE LAST REVISION ***

Several changes in the MGD77 Record were required in order to

make the format "Year 2000 Compliant" (Y2K Compliant):

DESCRIPTOR              CHANGE

______________________________________________-

DATA-RECORD TYPE        Change from "3" to "5"

(col 1)

TIME ZONE CORRECTION    Change from hundredths of hours to hours

From 5 digits (col 10-14)

to 3 digits (col 10-12)

YEAR                    Change to include century

From 2 digits (col 15-16)

to 4 digits (col 13-16)

Format Conventions:

1. All decimal points are implied.

2. Leading zeros and blanks are equivalent.

3. Unknown or unused fields are to be filled with 9s

(DO NOT BLANK FILL).

4. All "corrections", such as time zone, diurnal

magnetics, and Eotvos, are understood to be added

(e.g., time-zone correction is the number of hours

which must be added to the recorded time to

determine GMT).

Length

Character   of      Fortran

Nos.        Field   code     Description

____________________________________________________________

1           1       int      DATA RECORD TYPE

nnccIDENT                    Set to "5" for data record.

2-9         8       char     SURVEY IDENTIFIER

nnccCRUISE                   Identifier supplied by the contributing

organization, else given by NGDC in

a manner which represents the data.

Identical to that in header record.

10-12       3       int      TIME-ZONE CORRECTION

nnccTZ                       Corrects time (in characters 13-27)

to GMT when added: equals zero when

time is GMT.  Timezone normally falls

between -13 and +12 inclusively.

13-16       4       int      YEAR

nnccDATE                     including century (e.g. 1972)

17-18       2       int      MONTH

(e.g. May is represented as 05)

19-20       2       int      DAY

Day of month

21-22       2       int      HOUR

nnccTIME                     Hour of day

23-27       5       real     MINUTES X 1000

28-35       8       real     LATITUDE X 100000

+ = North; - = South

Between -9000000 and 9000000

36-44       9       real     LONGITUDE X 100000

+ = East; - = West

Between -18000000 and 18000000

45          1       int      POSITION TYPE CODE

nnccPSTN                     Indicates how lat/lon was obtained:

nnccPSTNX                    1 = Observed fix

3 = Interpolated

9 = Unspecified

46-51       6       real     BATHYMETRY, 2- WAY TRAVELTIME

nnccBTRVL                    In ten-thousandths of seconds.

Corrected for transducer depth and

other such corrections, especially in

shallow water

52-57       6       real     BATHYMETRY, CORRECTED DEPTH

nnccBDPTH                    In tenths of meters.

58-59       2       int      BATHYMETRIC CORRECTION CODE

nnccBCORCD                   This code details the procedure

nnccBCORX                    used for determining the sound

velocity correction to depth:

01-55  Matthews' Zones with zone

59     Matthews' Zones, no zone

60     S. Kuwahara Formula

61     Wilson Formula

62     Del Grosso Formula

63     Carter's Tables

88     Other (see Add. Doc.)

99     Unspecified

60          1       int      BATHYMETRIC TYPE CODE

nnccTYPCD                    Indicates how the data record's

nnccBTYPX                    bathymetric value was obtained:

1 =    Observed

3 =    Interpolated (Header Seq. 12)

9 =    Unspecified

61-66       6       real     MAGNETICS TOTAL FIELD, 1ST SENSOR

nnccMTOT1                    In tenths of nanoteslas (gammas).

For leading sensor.  Use this field

for single sensor.

67-72       6       real     MAGNETICS TOTAL FIELD, 2ND SENSOR

nnccMTOT2                    In tenths of nanoteslas (gammas).

For trailing sensor.

73-78       6       real     MAGNETICS RESIDUAL FIELD

nnccMRES                     In tenths of nanoteslas (gammas).

The reference field used is in

Header Seq. 13.

79          1       int      SENSOR FOR RESIDUAL FIELD

nnccMRESS                    1 = 1st or leading sensor

nnccMRESX                    2 = 2nd or trailing sensor

9 = Unspecified

80-84       5       real     MAGNETICS DIURNAL CORRECTION -

nnccMDI                      In tenths of nanoteslas (gammas).

(In nanoteslas) if 9-filled

(i.e., set to "+9999"), total

and residual fields are assumed

to be uncorrected; if used,

total and residuals are assumed

to have been already corrected.

85-90       6       F6.0     DEPTH OR ALTITUDE OF MAGNETICS SENSOR

nnccMDPTH                    In meters.

+ = Below sealevel

- = Above sealevel

91-97       7       real     OBSERVED GRAVITY

nnccGOBS                     In tenths of milligals.

Corrected for Eotvos, drift, and

tares

98-103      6       real     EOTVOS CORRECTION

nnccGEOTV                    In tenths of milligals.

E = 7.5 V cos phi sin alpha +

0.0042 V*V

104-108     5       real     FREE-AIR ANOMALY

nnccGFAIR                    In tenths of milligals.

Free-air Anomaly = G(observed) -

G(theoretical)

109-113     5       char     SEISMIC LINE NUMBER

nnccSLINE                    Used for cross referencing with

seismic data.

114-119     6       char     SEISMIC SHOT-POINT NUMBER

nnccSSHOT

120         1       int      QUALITY CODE FOR NAVIGATION -

nnccQC                       5 - Suspected, by the

nnccQCX                      originating institution

6 - Suspected, by the data

center

9 - No identifiable problem

found

(NOTE - Institution will most

frequently 9-fill this field;

however, should they wish to

code a "5", the data center will

not contradict.  The data

center's quality control

program, which performs (among

other checks) a vectorial

analysis of the navigation, is

available in a printout form

upon request.)

____________________________________________________________

APPENDIX B      10-DEGREE-SQUARE IDENTIFIER CODE

A 10-degree-square area can be easily identified by

constructing a four-digit number.  The components of this

number, in order of their construction are described as

follows:

Quadrant - A one-digit number identifies the quadrant of the

world with the following significance to each digit:

1st digit = Quadrant number

Qc Code         Latitude        Longitude

_______         ________        _________

1            North           East

3            South           East

5            South           West

7            North           West

10-Degree Square - The next three digits identify a unique

10-degree square; thus, the significant digits consist of:

2nd digit = Tens digit of degrees latitude

3rd digit = Hundreds digit of degrees longitude

4th digit = Tens digit of degrees longitude

10-DEGREE SQ IDENT. CODE

________________________

EXAMPLES:                                Qc   Lat  Long Long

(i) 37 degrees 48'S, 4 degrees 13'E    3    3    0    0

(ii) 21.6 degrees S, 14.3 degrees W     5    2    0    1

(iii) 34 degrees 28'N, 143 degrees 27'W  7    3    1    4

(iv) 75 degrees N, 43 degrees E         1    7    0    4

___________________________________________________________

APPENDIX B       NGDC CONTACTS

Dan Metzger: (303) 497-6542  dmetzger@ngdc.noaa.gov

or

John Campagnoli : (303) 497-3158  jcampagnoli@ngdc.noaa.gov

National Geophysical Data Center

NOAA, E/GC3

325 Broadway

Boulder, CO 80303-3328

TELEX 592811 NOAA MASC BDR

FAX (303) 497-6513

____________________________________________________________