TO:	EPA Docket No. EPA-HQ-OAR-2003-0146

FROM:	Bob Lucas, EPA/SPPD

DATE:	August 6, 2007

SUBJECT:	Average Refinery Stream Composition

I.	Purpose

This memorandum documents the overall average refinery waste stream compositions used in estimating the impacts of various control options considered for petroleum refineries.

II.	Average Refinery Stream Compositions

During the development of 40 CRF part 63, subpart CC (commonly referred to as Refinery MACT 1), average waste stream composition data were collected.  These data are summarized in a memorandum in a letter for Patrick Murphy to James Durham (Murphy, 1993).  The average individual process stream compositions as reported by Murphy are reproduced in Table 1 of this memorandum.  However, in Table 1 we report a different overall average refinery process stream composition.  The overall average composition developed by Murphy used a direct arithmetic average concentration of the reported streams.  However, alkylate production, for example, is only a small fraction of the crude throughput.  In the current analysis, production and capacity data from the EIA (EIA, 2006a and 2006b) were used to develop an overall, weighted-average composition.  Since production and capacity data were reported on a volume basis (e.g., barrels per day) and the concentrations were reported on a mass basis (i.e., weight percent) the density of the streams were used to develop a mass weighted-average concentration for the petroleum refinery process streams.  The data used to estimate the weighted-average concentrations as well as the results of this calculation are presented in Table 1.

# III.	References

EIA. 2006a. Petroleum Supply Annual 2005. Prepared by the Energy Information Administration, Washington, DC. October 23.

EIA. 2006b. Refinery Capacity Report 2006. Prepared by the Energy Information Administration, Washington, DC. June 15.

Murphy, P.  1993.  Letter from P. Murphy (Radian) to J. Durham (EPA).   Average Weight Percent HAPs in Refinery Streams.  Providing emission estimates for Petroleum Refinery MACT I (Subpart CC).  August 10, 1993.

Table 1.  Average Petroleum Refinery Stream Compositions

|  | Concentration of Refinery Process Stream (wt %)1 | Calculated Weighted Average Conc. (wt %) |
| --- | --- | --- |
|  | Gasoline | Alkylate | Crude oil | Reformate | Naphtha |  |
| HAP | Liquid | Vapor | Liquid | Vapor | Liquid | Vapor | Liquid | Vapor | Liquid | Vapor | Liquid | Vapor |
| 2,2,4-Trimethylpentane | 4.72 | 0.953 | 35.4 | 9.4 | 0.263 | 0.247 | 1.36 | 0.509 | 0.799 | 0.355 | 2.457 | 0.707 |
| Benzene | 1.61 | 0.626 | 0.118 | 0.061 | 0.446 | 0.807 | 4.61 | 3.32 | 1.244 | 1.06 | 1.212 | 1.024 |
| Biphenyl | 0.01 | 0 | 0 | 0 | 0.061 | 0.00002 | 0.025 | 0 | 0 | 0 | 0.037 | 0.000 |
| Cresols | 0.789 | 0.00065 | 0 | 0 | 0.218 | 0.0008 | 0.141 | 0.0002 | 0.0191 | 0.00003 | 0.315 | 0.001 |
| Cumene | 0.849 | 0.01565 | 0.004 | 0.0001 | 0.126 | 0.0108 | 0.968 | 0.033 | 0.91 | 0.0368 | 0.460 | 0.017 |
| Ethylbenzene | 1.605 | 0.0631 | 0.011 | 0.0006 | 0.346 | 0.0633 | 3.73 | 0.272 | 1.366 | 0.118 | 1.079 | 0.088 |
| Hexane | 7.138 | 4.428 | 3.22 | 2.63 | 2.46 | 7.11 | 3.9 | 4.48 | 7.53 | 10.27 | 4.260 | 6.440 |
| Methyl tertiary butyl ether | 3.54 | 3.62 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.821 | 0.839 |
| Naphthalene | 0.444 | 0.0006 | 0.012 | 0.00002 | 0.219 | 0.00125 | 0.798 | 0.0018 | 0.399 | 0.0011 | 0.343 | 0.001 |
| Phenol | 0.0551 | 0.0001 | 0 | 0 | 0.323 | 0.0031 | 0.0276 | 0.0001 | 0.066 | 0.0003 | 0.194 | 0.002 |
| Styrene | 3.528 | 0.0882 | 0 | 0 | 0 | 0 | 0.0907 | 0.0042 | 0 | 0 | 0.827 | 0.021 |
| Toluene | 7.21 | 0.842 | 0.503 | 0.077 | 0.878 | 0.477 | 14.54 | 3.14 | 5.05 | 1.295 | 4.161 | 0.907 |
| Xylene | 7.17 | 0.235 | 0.0212 | 0.0009 | 1.42 | 0.216 | 13.79 | 0.8367 | 5.49 | 0.395 | 4.398 | 0.296 |
| Total Organic HAP | 38.67 | 10.87 | 39.29 | 12.17 | 6.76 | 8.94 | 43.98 | 12.60 | 22.87 | 13.53 | 20.56 | 10.34 |
| Density2 | 0.74 |  | 0.692 |  | 0.88 |  | 0.79 |  | 0.79 |  |  |  |
| EIA Petroleum Annual 2006 (2005 data), bbl/cd3 | 7901893 |  |  |  | 15220088 |  |  |  |  |  |  |  |
| EIA Refinery Capacity Report 2006, bbl/sd4 |  |  | 1238479 |  | 18307502 |  | 3859070 |  |  |  |  |  |
| Calculated stream day capacity utilization5 |  |  |  |  | 0.83136 |  |  |  |  |  |  |  |
| Calculated Production, bbl/cd (bbl/sd×0.83136) |  |  | 1029619 |  |  |  | 3208269 |  | 3461132 |  |  |  |
| Weighting Factor Used6 | 0.4366 |  | 0.0532 |  | 1 |  | 0.1892 |  | 0.2041 |  |  |  |

1Source of individual process stream concentration data:  letter from Patrick Murphy (Radian) to James Durham (EPA), August 10, 1993

2Gasoline and naphtha densities from product MSDS sheets; alkylate density assumed to be density of 2,2,4-trimethylpentane; reformate density assumed equal to naphtha; crude density based on mid-range of medium crude (API gravity of 30 degrees API).

3Gasoline production is net production of Finished Motor Gasoline from Table 18 minus net inputs of Motor Gasoline Blending Components from Table 17 of EPA, 2006a; crude throughput from net inputs in Table 17 of EPA, 2006a.

4Capacity data for crude distillation, alkylation, and catalytic reforming units reported in EPA 2006b.

5Stream day to actual calendar day capacity utilization factor based on crude throughput data:  15,220,088/18,307,502 = 0.83136.

6Weighting factor = (Stream Production (bb/cd) × Stream Density) / (Crude Production (bbl/cd) × Crude Density).