# TRUCK MOUNTED AERIAL LIFT

Solicitation 08SQ170865

# 1.0	PURPOSE

The intent of this Invitation for Bid and resulting contract is to rent one (1) truck mounted articulated/telescopic aerial lift for the Bureau of Reclamation located at Grand Coulee Dam, WA.  The Government requires the rental of one (1) truck mounted articulated/telescopic aerial lift for a one month period beginning September 15, 2008 delivered FOB Destination to Grand Coulee Power Office, Grand Coulee, WA 99133.

Contractor is responsible for delivering and pickup when notified.  Equipment must arrive and be off-loaded and ready to operate by 8:00 AM, Sept 15, 2008, and be removed from the Government premises within ten (10) days after expiration of the rental period.  The equipment will be used for access to high voltage electrical towers.   Access to the scabland side-hill towers is limited to rough access roads with some construction pads immediately adjacent to the tower bases and centered under the power line conductors.  Upper cross-arms on these towers range in height from 107 to 179 feet.

Rental rate per month of use shall include the cost of all scheduled maintenance, repair parts, and cost to repair equipment unless the repairs are due to operator negligence or misuse.   The equipment shall be serviced and in good working condition.  Equipment furnished shall be new or used and must meet applicable safety requirements.  Any unsafe conditions as determined by the Bureau of Reclamation shall be sufficient grounds for rejecting a piece of equipment at no expense to the Bureau of Reclamation.  The truck to be supplied by the Contractor will be a truck mounted articulated/telescopic aerial lift.  The Contractor shall be responsible to supply and deliver a serviced and “ready for operation” lift to the Grand Coulee Project.  Fueling and daily maintenance (greasing and oiling) shall be the Government’s responsibility.  The Contractor shall provide the Government with a checklist of daily requirements consisting of fueling and essential lubrication.  The Government requires the Contractor to provide correction of mechanical problems of equipment during the term of the contract.  Time for repair of equipment shall not be considered as performance time.  Repair time shall extend the monthly end date for the time it takes to make the repairs.  Equipment that is to be replaced due to breakdown, for which the Government is not at fault, shall be replaced with no Delivery and Pick-up charge to the Government.  Such equipment shall be repaired or replaced by a comparable item of equipment within 5 working days from the date of breakdown.

Operator training shall be conducted at the Grand Coulee Power Office site for 3 Government employees.

Bidders shall indicate if they comply with each specification below.  This chart shall be returned with your bid.  Failure to return, with your bid, may result in your bid being rejected as non-responsive.

| Description | YES | NO | OFFERED |
| --- | --- | --- | --- |
| CARRIER: Capable of normal 60+ mph highway speeds. |  |  |  |
| Engine: Shall be diesel, and deliver at least 330 net S.A.E. horsepower. |  |  |  |
| Weight: Minimum of 70,000 lbs. GVW. |  |  |  |
| Hour Meter: Working service hour meter available. |  |  |  |
| Transmission: Transfer case available. |  |  |  |
| Power Steering: Power steering available. |  |  |  |
| Engine Brake: Engine brake available. |  |  |  |
| MUFFLER: Spark arresting muffler available. |  |  |  |
| BACKUP ALARM: Backup alarm to meet OSHA standards available. |  |  |  |
| Drive System: Minimum 6-wheel drive available. |  |  |  |
| Upper and Lower Control Stations: Upper and lower level control stations available. |  |  |  |
| Lower Control Station: Lower control station has the ability to over-ride the controls located at the basket, if necessary. |  |  |  |
| Emergency Lowering System: Emergency lowering system available. |  |  |  |
| Control Dampening: Slow speed dampening available. |  |  |  |
| Pedestal: Unit is pedestal mounted on a truck chassis. |  |  |  |
| Boom: Articulated/Telescope type with the ability to telescope hydraulically under full load regardless of angle. |  |  |  |
| Platform Height: Unit has a platform height of at least 175’. |  |  |  |
| Working Outreach: Unit has a working outreach of 70’. |  |  |  |
| Work Platform: Minimum two-man, with leveling system with a minimum rated capacity of 1,000 lbs. available. Platform will be equipped with safety lanyard anchor points. Basket will be secured and cushioned by manual friction brakes and shock absorbers or equal. |  |  |  |
| Boom Elevation Range: Boom elevation range available which will allow the operator to enter and leave basket from ground. |  |  |  |
| Turntable Rotation: 360 degree turntable rotation. |  |  |  |
| Transport Length: Transport length is less than 46’. |  |  |  |
| Outriggers: Equipped with a minimum of two (2) sets of hydraulically powered outriggers which will be operated from its own control station. If the manufacturer recommends a front outrigger it will also be provided. |  |  |  |
| Dual Outrigger Controls: Dual operator control stations with outrigger and stabilizer controls, engine start/stop, foot throttle, signal horn, boom-angle indicator, bubble levels, load chart and range diagram available. |  |  |  |
| One Sided Outrigger Operation: Capable of one-sided outrigger operation. |  |  |  |
| REGULATIONS: Machine will comply with all applicable OSHA and ANSI standards, and are designed for ease of set-up and operation. |  |  |  |
| Load Rating Chart: Mandatory inclusion of a Range Diagram with Full Spread Configuration which includes boom length in feet and operating radius from centerline of rotation in feet; Fully Extended Outrigger Configuration chart; Range Diagram for Intermediate Spread Configuration which includes boom length in feet and operating radius from centerline of rotation in feet; Intermediate Spread Configuration chart; Allowable Line Pull Chart; and an Area of Operation chart. |  |  |  |
| MANUALS: One set of each of operator’s manual, and service manual available. |  |  |  |
| DELIVERY: Delivery within in the required time frame to the Grand Coulee Power Office, Grand Coulee, WA available. |  |  |  |
| TRAINING: Minimum of an eight-hour training session to Project Personnel on the operation and maintenance of the unit including safety procedures available. |  |  |  |