Audio Conferencing Service (ACS) Cutover Checklist

GSA Transition Coordination Center

27 July 2007

Prepared for the

GENERAL SERVICES ADMINISTRATION

Networx Support Services

10304 Eaton Place

Fairfax, VA  22030

Contract Number GS00T03AHD0007

Order Number GST007NS0023

Audio Conferencing Cutover Checklist

I. Functional Definition

Audio Conferencing Service (ACS) enables participants to engage in multi-point audio conference calls. The audio connection from the conference participants to the ACS conference-bridge is provided by services, such as Voice Services (VS), Cellular/PCS Service (CPCS), voice over Frame Relay Service (FRS), voice over Asynchronous Transfer Mode Service (ATMS), and Voice over IP Transport Service (VoIPTS).

Applicable Audio Conferencing Standards include:

1. ANSI T1.101 for T1

2. ANSI T1.607 and 610 for ISDN

3. ANSI SS7, and enhanced SS7 standards for interworking (e.g., address translation) between circuit-   switched network and IP network.

4. Telcordia Notes on the Networks (SR-TSV-2275), currently Issue 4, October

2000

5. IETF RFC 3661 through 3665 for SIP (Session Initiation Protocol)

6. IETF RFC 3435 for MGCP (Media Control Gateway Protocol)

7. ITU-TSS H.323/225/245/248 (enhanced for VoIP)

II.	Networx Performance Requirements

Audio Conferencing Service Performance Metrics

| Key Performance Indicator (KPI) | Service Level Performance Standard (Threshold) | Performance Standard (Threshold) | Acceptable Quality Level (AQL) | How Measured |
| --- | --- | --- | --- | --- |
| Availability | Routine | 99.5% | ≥ 99.5% | ACS availability is calculated as a percentage of the total reporting interval time that ACS is operationally available to the Agency. Availability is computed by the standard formula: |
| Time to Restore | With Dispatch | 8 hours | ≤ 8 hours | The Networx Vendor will calculate Time to Restore (TTR) as the elapsed time between the time a service outage is recorded in the Trouble Management System and the time the service is restored minus any (1) time due to scheduled network configuration change or planned maintenance or (2) time, as agreed to by the Government, that the service restoration of the service cannot be worked due to Government caused delays. Examples of Government caused delays include: 1) the customer was not available to allow the contractor to access the Service Delivery Point or other customer-controlled space or interface; 2) the customer gave the contractor an incorrect address for the SDP; 3) the customer failed to inform the contractor that a security clearance was required to access the SDP or customer-controlled space; 4) or the Government required service at a remote site and agreed that a longer transit time was required. |
|  | Without Dispatch | 4 hours | ≤ 4 hours |  |
| GOS (Operator Assistance Response Delay) | Routine 54 seconds | 54 seconds | ≤ 54 seconds | GOS (Operator Assistance Response Delay) is the delay experienced by conference participants to receive operator assistance during a conference. Delay is measured as the interval between the end of signaling (e.g., dialing for operator assistance) and the receipt of voice response from the operator |

Interfaces

Unless marked optional the contractor shall support audio connection to the conference bridge from these services: VS, IPTelS, FRS (VoFR), ATMS (VoATM), and CPCS.

Audio Conferencing Service Checklist*

*Use in conjunction with Generic Cutover Checklist

| PRE-CUTOVER |  | STATUS |
| --- | --- | --- |
| Administrative | Has an Agency Hierarchy Code (AHC) been provided to the Networx vendor? |  |
|  | Have Local Government Contacts (recommend at least two per location) been identified and contact information provided? |  |
|  | Has a Project Specific Transition Plan Identifier been assigned? |  |
|  | Note (P_OPS) in the Agency Service Request Number (ASRN) if this is parallel service |  |
| Pre-Ordering/Design Decisions | Determine the Parallel Operations Period – all orders for parallel service will have to be so noted in the ASRN. |  |
| User Training | Trouble Reporting – The Networx contract requires that Attendant assistance shall be available at any time during an audio conference. The use of all other features should also be included in a training package. |  |
| Installation | No installation required. An authorization code from the Networx vendor is all that is required. |  |
|  | Parallel Operation/Fallback Plan – The plan would be to simply not issue a disconnect order for the FTS2001 authorization code until such time that the Agency is satisfied with the performance of the Networx service. |  |
| Execute Tests | The Networx vendors are required to submit to GSA a Networx Services Verification Test Plan to GSA no later than 60 days after Notice to Proceed. As a requirement of this plan the Networx vendor is required to submit as an attachment to the Networx Services Verification Test Plan a service-specific test plan no later than 15 calendar days after the contractor issues the service Order Confirmation for the initial order of the service under the Networx contract. This plan is to include how the vendors will test the service upon initial delivery to the Agency. It is recommended that each Agency test the access methods (see Interfaces above) and the features they plan on utilizing. |  |
| Conduct Pre-Cutover Testing | See Examples Below of a Networx Vendor Networx Services Verification Test Plan: Have the Agency LGC or Network Management Organization and Networx vendor reviewed the results of this testing to insure all is ready for the actual cutover? |  |

Audio Conferencing Service Features

The Agency should insure that all of the features and functions ordered with the service were delivered and are operational within the seventy two hour acceptance window. The Networx vendors are to perform verification testing on the service for each order at the initial service delivery to an Agency per the Networx service verification test plan.

ID Number	Name of Feature 	Description

1 		Audio recording of call 	The contractor shall allow recording of conference call into a

storage- media (e.g., disc or cassette tape) for later replay.

2 		Access Controlled Call 	The contractor shall allow the conference leader to prevent

Operator from monitoring the call as well as additional/late participants from joining the call

3 		Language translation	The contractor shall provide language translation to English from

other languages (e.g., Spanish) for transcription of pre-recorded

audio conference.

4 		Moderator led questions The contractor shall provide conference moderator led questions

and answers only.

5 		Participant list report	The contractor shall provide a report of all participants in the

conference.

6 		Password screening	The contractor shall screen password for joining a conference to

authorized participants only.

7 		Replay of pre-recorded	The contractor shall allow, under password protection, replaying

audio conference	of pre-recorded audio conference at a later time and shall allow

remote control of the recording with keypad access to functions like pause, rewind, and fast-forward.

8 		Transcription of 		The contractor shall provide transcription of pre-recorded audio

Prerecorded audio	call

call

9 		Temporary blocking of	The contractor shall allow temporarily blocking audio conference

ports in order to remove a sub-set of participants/users from the

conference.

10 		Secured Audio		The contractor shall support voice conferencing capability for

Conference		sensitive voice conferences with end-user encryption to support

discussions of a sensitive-but-unclassified (SBU) nature between

multiple locations with protection from unauthorized interception

(i.e., eavesdropping).

[Note. Government furnished encryption unit at the SDP will be

based on commercially available encryption devices (Standard:

NIST DES/AES). The contractor must synchronize encryption key of similar encryption unit(s) of the audio conference bridge before each conference.

| FINAL CUTOVER |  |  |
| --- | --- | --- |
| Communicate schedule and status with stakeholders |  |  |
| Obtain authorization to proceed or delay | GO/NO-GO notification |  |
| Activate new service(s) |  |  |
| Conduct acceptance test |  |  |
| The Agency should notify the Networx vendor and TCC of rejection of service within 72 hours of cutover | Acceptance period of 72 hours begins upon receipt of the Service Order Completion Notice (SOCN) |  |
| Begin production |  |  |
| Deactivate legacy service |  |  |
| Obtain signoffs for cutover completion |  |  |

Transition Cutover Contact List

Agency Name: _______________________________________

Local Government Contact Personnel:

Name: __________________________		Name: ____________________________

Title/Function: ___________________		Title/Function:______________________

Location: _______________________		Location: __________________________

Mobile #: _______________________		Mobile #:__________________________

Office #: ________________________		Office #: ___________________________

Email: __________________________		Email: _____________________________

Networx Vendor: _______________________________________________

Networx Vendor Key Contact Personnel:

Name: __________________________		Name: ____________________________

Title/Function: ___________________		Title/Function:______________________

Location: _______________________		Location: __________________________

Mobile #: _______________________		Mobile #:__________________________

Office #: ________________________		Office #: ___________________________

Email: __________________________		Email: _____________________________

### CUTOVER ISSUES LOG

| ISSUE # | INITIATOR | ISSUE SUMMARY |
| --- | --- | --- |
| Priority/Impact | Owner | Target Resolution Date |
| Status | Status Date | Resolution |