(Part 4 of 4)

Radiological Training for Tritium Facilities

Student's Guide

Coordinated and Conducted

for

Office of Health, Safety and Security

U.S. Department of Energy

This page intentionally left blank.

Course Objectives:	EO1	IDENTIFY the following properties of tritium:

-	physical/chemical

-	radioactive.

EO2	IDENTIFY sources of tritium:

-	natural

-	by-product

-	weapons.

EO3	IDENTIFY uses of tritium:

-	weapons applications

-	research

-	fusion energy production

-	industrial/commercial.

EO4	IDENTIFY modes of tritium exposure:

-	inhalation

-	ingestion

-	absorption

-	injection/wound.

EO5	IDENTIFY the biological effects of tritium:

-	biological half-life

-	dose.

EO6	IDENTIFY the radiological control methods for tritium:

-	engineered

-	administrative

-	surface contamination limits

-	personnel protective equipment

-	application of ALARA principles.

EO7	IDENTIFY methods for monitoring for tritium:

-	air sampling for worker safety

-	contamination surveys

-	bioassay.

EO8	IDENTIFY tritium waste minimization and handling

techniques.  (Site-Specific)

E09	IDENTIFY alarms and proper response to abnormal

conditions in the tritium facility. (Site-Specific)

| I. | PROPERTIES OF TRITIUM - What is tritium? Tritium is a radioactive isotope of hydrogen (H). Hydrogen is the lightest and most abundant element in the universe. Hydrogen has only one proton in its nucleus. Tritium has, in addition to the single proton, two neutrons in its nucleus. This makes it three times heavier than the most common form of hydrogen. |  |
| --- | --- | --- |
|  | A. Isotopes of Hydrogen 1. Protium (H) (99.985% natural abundance) 2. Deuterium = hydrogen + 1 neutron (D) (0.015% natural abundance) 3. Tritium = hydrogen + 2 neutrons (T) |  |
|  | B. Symbol for Tritium Tritium is designated as: |  |
|  | C. Chemical Properties of Hydrogen/Tritium Tritium "behaves" just like hydrogen chemically because it has one proton and one electron like ordinary hydrogen. |  |

| 1. Substitution Tritium atoms can easily substitute for hydrogen atoms. Examples: a. elemental hydrogen (tritium gas, HT, DT, or T2) b. tritiated water (tritium oxide: HTO, DTO, or T2O) c. organically bound tritium: These compounds may result in more dose per intake than tritiated water. d. metals and tritium (metal tritides): These compounds may result in more dose per intake than tritiated water. Accordingly, additional controls may be needed, such as special air monitoring or enhanced personnel protective equipment. |  |
| --- | --- |
| 2. Solubility Exchanges with hydrogen in organic and other materials (oils, plastics, etc.) 3. Flammability Tritium gas is flammable and can explode under certain conditions. |  |

| D. Physical Properties 1. Diffusion Tritium gas is lighter than air and diffuses rapidly in air. |  |
| --- | --- |
| 2. Permeability Tritium gas permeates through most materials, that is, it travels through them by way of spaces or interstices in them. The rate depends upon the material and its thickness. Tritium's radioactive, chemically reducing and diffusive properties result in degradation of many useful polymeric materials, pump oils, plastics, and o-rings. This can cause loss of mechanical functions in certain situations within a short period of time. |  |
| E. Radioactive Decay of Tritium Tritium "decays" by emitting a beta particle and becoming an atom of helium. |  |

| 1. Beta Energy A very low energy beta is emitted. |  |
| --- | --- |
| 2. Beta Range Tritium is not an "external" radiation hazard. |  |
| a. Travels less than 1/4 inch in air b. Cannot penetrate through the dead layer of the skin c. Cannot penetrate clothing or gloves |  |
| 3. Half-life Radioactive half-life = 12.3 years. |  |
| F. X-Ray Production Tritium betas can produce low energy x rays. Because the beta particle is of such low energy the x rays it may produce are not very penetrating and are not normally considered a hazard. |  |

| G. Fusion Fusion is the process of two nuclei joining together. The energy source in most stars is nuclear fusion of hydrogen isotopes. |  |
| --- | --- |
| SOURCES AND USES OF TRITIUM How is tritium produced and what is it used for? A. Sources of Tritium There are three primary sources of tritium in our environment. Tritium is present in our environment from both man-made and natural sources as discussed below. Natural tritium is indistinguishable from man-made tritium. 1. Natural Sources Tritium occurs naturally. It is formed by the reactions between cosmic rays and the nitrogen in the upper atmosphere. Nitrogen makes up 80% of the earths atmosphere. Cosmic rays generate approximately 4 million curies of tritium per year. With tritium being continually produced and at the same time decaying, the natural tritium in our environment is about 70 million curies. |  |

| 2. By-Product of Reactor Sources a. Lithium-7 captures a neutron and decays with tritium as a product. b. Boron captures a neutron and decays with tritium as a product. c. Activation of deuterium in water. d. Ternary fission - A fission resulting in three fission products, one of which is tritium. This process has a 0.1% yield. |  |
| --- | --- |
| The production of tritium from power reactors around the world is less than one-half that naturally formed (approximately 1 to 2 million curies a year). |  |
| 3. Weapons Testing as a Source The amount of tritium in the world from weapons testing has been steadily declining since the 1970's when atmospheric testing was curtailed. |  |
| Atmospheric testing from 1945-1975 produced about 8 billion curies. This has decayed to about 400 million curies. |  |

| 4. DOE Production of Tritium DOE has produced tritium at the Savannah River Site with the use of a reactor. Tritium is commercially available from from Canada and the European Community for non-weapons use. |  |
| --- | --- |
| B. Uses of Tritium 1. Consumer Products a. Gaseous tritium light sources - exit signs (1 Ci to tens of Ci's) - aviation landing aids (30-165 Ci per light) (1 curie of tritium has a mass of approximately 0.1 mg) |  |
| b. Luminizing industry: Self-luminous compounds for dials (several mCi's) and controls as well as other general industry uses. |  |
| 2. Research - Tritium Labeling Tracers for medical and laboratory research. |  |
| 3. Department of Energy a. Weapons development and applications b. Fusion energy: As a fuel source |  |

| III. | MODES OF EXPOSURE AND BIOLOGICAL BEHAVIOR OF TRITIUM - How can I be exposed to tritium and what would it do to me? |  |
| --- | --- | --- |
|  | A. External Dose - Tritium is not an external hazard. - Tritium is not a dose concern if it is located outside the body. - Tritium betas will not penetrate a dosimeter. - We are interested only in tritium inside the body. |  |
|  | B. Internal Dose Tritium is an "internal" radiation hazard. |  |
|  | C. Modes of Exposure Tritium can deliver a radiation dose if it gets inside our bodies. Modes of entry include: - inhalation - absorption - injection (cuts/wounds) - ingestion |  |

|  | 1. Inhalation a. Tritium gas: is only slightly incorporated into the body when inhaled. Most tritium gas inhaled is subsequently exhaled. There are other chemical and physical processes to convert tritium gas to tritiated water. b. Tritiated water vapor: Nearly 100% of tritiated water vapor inhaled is incorporated into body fluids/tissues. c. Hazard: Exposure to tritiated water is approximately 25,000 times more hazardous than exposure to elemental tritium gas. d. Special Tritium Compounds: consist of organically bound tritium and tritium particulate aerosols. Exposure to organically bound tritium can be up to approximately 13 times more hazardous than exposure to HTO. Exposure to tritium particulate aerosols can deliver up to approximately 20 times more dose to the whole body than exposure to HTO. The dose to the lungs from tritium particulate aerosols could be 2 orders of magnitude higher than from HTO. |  |
| --- | --- | --- |
|  | 2. Ingestion Ingestion may occur by eating, drinking, chewing tobacco, and applying makeup where tritium contamination is present. Always wash hands thoroughly when leaving areas where there is a potential for contamination, and never eat, drink etc. where tritium contamination may be present. |  |

| 3. Absorption Absorption is also a hazard because an individual can receive, in certain situations, 1/3 of their uptake from absorption through the skin if not properly using personal protective equipment. a. Tritium gas: There is negligible skin absorption for tritium gas. b. Tritiated water: Tritiated water can be absorbed through the skin. It has been observed that moisture on hands enhances absorption. c. Solvents: Some solvents (organically bound tritium) can also go through the skin. Tritium will penetrate gloves, therefore gloves must be changed at a prescribed routine basis. |  |
| --- | --- |
| D. Biological Behavior of Uptakes of Tritium Tritiated water in the body acts just like water. |  |
| 1. Distribution Tritiated water is rapidly and uniformly distributed throughout the entire body. The Committed Effective Dose Equivalent (CEDE) from an uptake of one curie of tritiated water is 63 rem. Soluble organically bound tritium behaves in the body in a similar manner. Stable tritium particulate aerosols and insoluble organically bound tritium behave in the body in a similar manner as the particulate to which the tritium is bound. |  |

|  | 2. Biological Half-life Half of the HTO is eliminated from the body in about 10 days. Through normal biological processes, it would take 70 days or more to eliminate 99% of the assimilated tritiated water. Stable tritium particulate aerosols and insoluble organically bound tritium behave in the body in a similar manner as the particulate to which the tritium is bound and would have a longer half life. |  |
| --- | --- | --- |
|  | E. Medical Treatment The biological half-life can be shortened by increasing the water elimination in the body. Therefore, individuals who have uptakes of tritium are encouraged to drink water. Drinking copious amounts of water should not be done without a physician's guidance. Certain medical conditions may be affected by liquid intake. |  |
| IV. | RADIOLOGICAL CONTROLS FOR TRITIUM - How can I protect myself from exposures to tritium? Tritium can be present in a variety of chemical forms. Ongoing research indicates that the form of tritium which gives the highest dose (per unit intake) is tritium particulate aerosols. However, these compounds are not found in the quantities and various locations as tritiated water. If we can rule out special tritium compounds as being of concern, we assume it may be tritiated water. The preferred hierarchy of control is as follows: - engineered - administrative - personal protective equipment |  |

| A. Engineered Controls 1. Containment and Confinement Containment or confinement is a series of physical barriers, minimizes exposure of workers. |  |
| --- | --- |
| Confinements such as glove boxes are almost always used when handling large quantities of tritium. However, hoods are acceptable for handling small quantities, such as in a laboratory. |  |
| 2. Airflow Maintaining negative ventilation is essential for the safe operation of a tritium facility. Airflow should be from areas of LEAST to MOST contamination. |  |
| 3. Local Exhaust Ventilation The primary advantage of local exhaust ventilation techniques is the removal of airborne tritium, regardless of its release rate or chemical or physical form. In addition, these techniques use relatively low volume rates compared to normal ventilation requirements. |  |

| 4. Dilution Ventilation Dilution ventilation is the once-through flow technique of exchanging outside air for inside air for comfort and the reduction of airborne sources. 5. Storage Tritium can be stored in storage beds. Metal tritide and uranium hydride are the most common for these storage systems. Tritium is generally released by heating the metal tritide. |  |
| --- | --- |
| B. Administrative Controls There are many administrative controls to reduce doses. The following are just a few that should apply to all sites: - limitation of access time - procedures/RWPs - postings For tritium and tritium compounds, 10 CFR 835 Appendix D requires posting contamination areas based on removable contamination values of 10,000 dpm/100cm2. |  |

| C. | Personal Protective Equipment 1. Air Supplied Suits Because of the absorption through the skin associated with the use of respirators and other breathing apparatus, air-supplied plastic suits that completely enclose the body are widely used by facilities that handle large quantities of tritium. |  |
| --- | --- | --- |
|  | 2. Protective Clothing Protective clothing (PC), or anti-contamination clothing (anti-Cs), is used to minimize the spread of contamination from contaminated to clean areas. In many operations, the hands and forearms of workers are vulnerable to contact with tritium surface contamination. The proper selection of gloves and glove materials is important. In many instances a plastic/water proof suit is required. |  |
| V. | MONITORING FOR TRITIUM - How do I know if tritium is present? |  |

| A. Personnel Monitoring 1. External Dose Dosimeters are not typically used to monitor for radiological doses resulting from tritium. The weak energy beta radiation will not penetrate the dosimeter. insert any site specific monitoring procedures) |  |
| --- | --- |
| 2. Internal Dose The best method used to determine if an individual has an uptake of HTO or soluble organically bound tritium is by bioassay (urinalysis). Routine urine samples, collected at some predetermined frequency and counted for the tritium content, provide a very sensitive measurement of tritium in the body. This is especially true if the time of uptake is known. Air sampling results may be used to assess dose from other types of special tritium compounds. |  |
| 3. Routine Versus Non-Routine Bioassay Monitoring a. Routine: Routine urinalysis is conducted on a preset periodic basis. b. Non-routine or Special: Non-routine bioassay is done whenever a potential exposure to tritium is suspected. (insert site specific bioassay procedures) |  |
| B. Workplace Monitoring Air monitoring and surface contamination surveys are used to verify that loose contamination is not present. They provide an early indication of potential problems. |  |
| 1. Airborne Tritium Monitoring Airborne tritium monitoring is used for: a. Prompt detection of airborne contamination for worker protection; b. Determination of the status of processes; and c. Identification of any leaks in primary or secondary containments or confinements. |  |
| 2. Contamination Surveys Despite contamination control measures, tritium is easily spread. All workplaces shall be surveyed for contamination levels on a regularly scheduled basis. The frequency of such surveys will depend on the potential for dispersement of the tritium-contaminated material in the area and the quantity of tritium in the area. During routine surveys, all work enclosures, work surfaces, floors, equipment, etc., within the workplace should be surveyed. |  |

|  | At the surface contamination levels in 10 CFR 835 Appendix d, tritium is difficult to measure directly because the low-energy beta is readily absorbed in air and the window of the detector. Normal frisking methods (use of pancake probe) will not detect tritiated water. Surfaces are normally wiped (smeared) with a small paper, either dry or moistened, which will pick up loose tritiated material. The wipe is then normally counted by liquid scintillation techniques. |  |
| --- | --- | --- |
| VI. | TRITIUM WASTE MINIMIZATION AND HANDLING- Why is it important and how do you minimize tritium waste? (insert site specific controls) Methods below are given as a reference only. A. Minimizing Tritium-Contaminated Waste |  |
|  | 1. Avoid generating wastes by not bringing unnecessary material into the controlled area. |  |
|  | 2. Whenever possible, avoid use of porous materials or those known to be highly permeable to tritium. |  |
|  | 3. Designate an area to store contaminated tools for reuse or consider all tools in the area to be contaminated. |  |

|  | 4. Plan work so that, whenever possible, construction and clean maintenance can be done in a clean area. 5. When transporting items contaminated with tritium, adequate contamination control such as wrapping in plastic or placing in sealed containers should be considered. |  |
| --- | --- | --- |
|  | B. Minimizing Mixed Waste (insert site specific controls) Methods below are given as a reference only. |  |
|  | 1. Use non-hazardous cleaning materials for decontamination whenever possible. |  |
|  | 2. Segregate radioactive-only from hazardous-only at the source. |  |
|  | 3. Explore the use of other materials which are non-hazardous for use in radiological areas to prevent the generation of mixed waste. |  |
| VII. | RESPONSE TO ABNORMAL CONDITIONS IN THE TRITIUM FACILITY- What should I do in an emergency involving tritium? To properly deal with unexpected adverse situations occurring in a tritium facility, a well-thought-out response program and personnel trained to execute the response should be in place. |  |

|  | A. Abnormal Conditions Abnormal conditions in a tritium facility could include: - fire/explosion - natural disaster - tritium releases - other hazards Personnel found contaminated should follow site specific decontamination procedures which would typically include showering with cold water and the use of mild detergents. |  |
| --- | --- | --- |
|  | B. Facility Alarms (insert site specific alarms and emergency response procedures) C. Facility Emergency Responses (insert site specific alarms and emergency response procedures) |  |
| VIII. | LESSONS LEARNED (insert site specific lessons learned) |  |
| IX. | SUMMARY AND REVIEW |  |

CONCLUDING MATERIAL

Review Activity: 				Preparing Activity:

DOE Field Offices 				DOE-HS-11

DP 	RF 					Peter V. O’Connell, CHP, 301 903 5641

HSS 	ID 					Project Number:

EM 	SR 					TRNG-0020

NE 	OH

SC 	RL

GC

IA

RW

NN

National Laboratories Operations Offices

BNL 	AL

LLNL 	NV

LANL 	OAK

PNL 	OR

Sandia 	CH

ANL

New Brunswick

ORNL

SRNL

Area Offices

Amarillo Area Office

Kirtland Area Office

Princeton Area Office

Fernald Area Office

Kansas City Area Office

Miamisburg Area Office