A Cavity-Enhanced, Optical-Heterodyne Spectrometer and Its Relevance to Future Titan Exploration

Pin Chen

Science Division

Jet Propulsion Laboratory, California Institute of Technology

M/S 183-301, 4800 Oak Grove Drive, Pasadena, CA  91109

USA

pin.chen@jpl.nasa.gov

David J. Robichaud

Division of Chemistry and Chemical Engineering

California Institute of Technology

USA

Mitchio Okumura

Division of Chemistry and Chemical Engineering

California Institute of Technology

USA

Yuk L. Yung

Division of Geological and Planetary Sciences

California Institute of Technology

USA

Atmospheric in-situ measurements of trace gases, stable-isotopic compositions, and aerosol optical properties can provide valuable constraints/information regarding sources of key volatiles (including methane) on Titan, origin of Titan’s atmosphere, nature of Titan’s haze, and the photochemical environment in Titan’s atmosphere.  Development is underway to apply a new optical technique, noise-immune cavity-enhanced optical-heterodyne spectroscopy (NICE-OHMS, pioneered by Ye, Hall, and co-workers), to the detection of trace gases and isotopic analysis in planetary atmospheres using near IR spectroscopy, and to the optical characterization of aerosols.  This instrument technique combines the path-length advantage of cavity enhanced methods with the noise suppression advantage of an innovative heterodyne detection scheme to yield unprecedented sensitivity.  A NICE-OHMS spectrometer for studies of CO, CH4, and aerosols has been constructed, and its operation, figures-of-merit, development, and considerations relevant to future Titan exploration will be discussed.