QUESTIONNAIRE FOR MID-ATLANTIC REGION PCEF ABOUT

DESIGN CONSIDERATIONS FOR PRESTRESSED CONCRETE MEMBERS

State: ______________

1.	Type of strands patterns at end of girders used within your state:

Check ALL that apply:

|  | Allow in current specifications | Have used in the past 10 years |
| --- | --- | --- |
| Straight |  |  |
| Straight and Draped |  |  |
| Straight with unbonding |  |  |
| Combination: Straight, draped and unbonded |  |  |

DESCRIBE CRITERIA:

2.	Type of strands used within your state:

Check those that apply:

|  | Allow in current specifications | Have used in the past 10 years |
| --- | --- | --- |
| ½ “ diameter strands – low relaxation |  |  |
| ½ “ diameter strands – stress relieved |  |  |
| ½ “ diameter strands (Special 0.167 in2) low relaxation |  |  |
| ½ “ diameter strands (Special 0.167 in2) stress relieved |  |  |
| 0.6“ diameter strands – low relaxation |  |  |
| 0.6“ diameter strands – stress relieved |  |  |
| 7/16” diameter strands – low relaxation |  |  |
| 7/16” diameter strands – stress relieved |  |  |

DESCRIBE CRITERIA:

3.	Standard spacing of strands used in standards in your state:

  - 2” spacing	for ½“ strands		Yes ______	No ______

  - 2” spacing	for 0.6“ strands	Yes ______	No ______

  - Other				Yes ______	No ______

DESCRIBE CRITERIA:

- Does the specification and/or state practices limit the amount of unbonding strands allowed at specific locations in the beams?

  - 25% of strands		Yes ______	No ______

  - 25% at ⅓, ⅓, and ⅓ *	Yes ______	No ______

  - 25% at ½, and ½ **	Yes ______	No ______

  - Other			Yes ______	No ______

*	25% with maximum of ⅓ of debonded strands terminating at each location.

**	25% with maximum of ½ of debonded strands terminating at each location.

DESCRIBE CRITERIA:

- Does the specification and/or state practices limit the location of unbonded strands?

  - Interior strands only				Yes ______	No ______

  - Interior strands distributed uniformly 		Yes ______	No ______

  - Int. & Ext. strands distributed uniformly 		Yes ______	No ______

  - Other						Yes ______	No ______

DESCRIBE CRITERIA:

- What is the allowable tension stress in the precompressed tension zone (i.e., at or very near midspan at the bottom of the girder)?

  - Zero tension		Yes ______	No ______

  - 3*sqrt(f’c)			Yes ______	No ______

  - 6*sqrt(f’c)			Yes ______	No ______

DESCRIBE CRITERIA:

- Does the amount of allowable tension in the precompressed tension zone differ according to environment?

| Environment Type | Zero Tension | 3*sqrt(f’c) | 6*sqrt(f’c) |
| --- | --- | --- | --- |
| Normal Environment |  |  |  |
| Severe Environment |  |  |  |
| Other |  |  |  |

DESCRIBE CRITERIA:

- What criteria (if any) does the state have for determining the spacing of diaphragms?

  - Midspan and/or maximum of 40’	 	Yes ______	No ______

  - Midspan and/or maximum of 60’		Yes ______	No ______

  - Midspan and/or maximum of 80’		Yes ______	No ______

DESCRIBE CRITERIA:

- What type of stirrup reinforcement is specified/allowed to minimize tripping hazards on the top of the prestressed concrete girder?

  - Pin type stirrups				Yes ______	No ______

  - 2 - 90º type stirrups			Yes ______	No ______

  - Bulb Tee with top tie bar w/ 90º bend 	Yes ______	No ______

  - Bulb Tee with top tie bar w/180º  bend	Yes ______	No ______

  - Other					Yes ______	No ______

DESCRIBE CRITERIA:

Contact Person:	Rodolfo (Rudy) F. Maruri

Virginia Division

Assistant Division Bridge Engineer

Telephone No.: 	(804) 775-3361

Email Address: 	rodolfo.maruri@fhwa.dot.gov

AND/OR

Claude S. Napier

Virginia Division

Division Bridge Engineer

Telephone No.: 	(804) 775-3363

Email Address: 	claude.napier@fhwa.dot.gov

Thank you for completing the questionnaire.   A summary of compiled results will be presented at the PCEF Committee meeting