Baffle slice calculations

M. Sholl

23 February 2004

The SNAP telescope entrance is a sliced cylinder.  This provides shading from the sun for various observation angles.  The slice angle α is chosen to preclude direct solar illumination of the slice front face.  Let the normal vector to the surface of the slice be C.  The angle of body coordinate direction X with the solar vector S is defined by Euler rotations about the Z axis (Phi) and Y axis (Theta).  Because Euler rotations produce pseudovectors, the order of rotation about Phi and Theta determine the orientation of S.  The front face of the telescope is illuminated when the dot product of S and C is positive.  One therefore determines Alpha by solving for C (dot) S = 0.

Preliminaries: rotation matrices

An arbitrary vector V rotated angle Phi about the Y axis transforms to V’ as follows:

while an arbitrary vector V rotated angle Theta about the Z axis transforms to V’ as follows:

Compute vector C

The vector C is computed by rotating a unit Z direction vector about the Y axis by an angle –Alpha as follows:

(1)

Two possibilities for computing vector S

- Rotate about Z axis first

(2)

- Rotate about Y axis first

(3)

Compute dot products

Compute dot products between (1) and (2), and (1) and (3).

Sin(α)cos(θ)cosφ(φ)+cos(α)(-sin(φ))cos(θ)=0 	implies α= φ		       	       (4)

sin(α)cos(θ)cosφ(φ)+cos(α)(-sin(φ))=0		implies tan(α)=tan(φ)/cos(θ)	       (5)

Of (4) and (5), (5) is the most restrictive on α, and will therefore be adopted.  Note,  case (4) does not depend on roll angle θ.

Results

See 2/20/2004 P. Jelinsky Addendum to SNAP L2 Orbit Scattering Angles for near Ecliptic Pole Pointings memo.  Two possible angles φ are under consideration for pointing off the ecliptic pole: 20º and 25º.  Table 1 shows derived baffle slice angles α (using Equation (5)) required for Sun, Earth and Moonlight exclusion from the entrance into the baffle.

Table 1: Baffle slice angles for Earth/Moon from L2

Table 1 shows that required baffle slice angles increase dramatically from ~35º if Earth/Moon exclusion is considered necessary.  Illumination levels from the Moon and Earth are small relative to that produced by the sun.  This is due primarily to the small unshadowed regions visible from L2.  See 1/23/2004 P. Jelinsky SNAP L2 Orbit Scattering Angles.  The maximum illumination of the Moon and Earth disks from L2 are given in Table 2.

|  | Earth | Moon |
| --- | --- | --- |
| Halo | 5.3% | 12.4% |
| Lissajous | 1.5% | 5.3% |

Table 2: Earth/Moon disk illumination from L2

Because a baffle slice angle α will likely be chosen to exclude sunlight, but not Earth or Moonlight, occasional Earth/Moon stray light will need to be analyzed for impact on the overall observing schedule.

Conclusions

With the caveat that Earth/Moon stray light cases require consideration in the overall observation plan, the baffle slice angle should be set at 34º for interim design and analytical calculations.