NATIONAL HIGHWAY TRAFFIC SAFETY ADMINISTRATION

Office of Vehicle Safety Compliance

COMPLIANCE STATUS REPORT

REPORT DATE: JUNE 2006

The following definitions are essential to the interpretation of the report:

# INVESTIGATIONS —

CT (Compliance Test) — Investigations initiated based on the results of scheduled compliance test programs.

CI Number — OVSC Compliance Investigation Number (such as "CI-208-020320")

The CI number identifies FMVSS 208 with a test failure date of March 20, 2002.  A compliance investigation is established when there is a reasonable expectation that a noncompliance may exist.

PE Number — OVSC Preliminary Evaluation Number (such as "PE-214-020320")

The PE number identifies FMVSS 214 with a test failure date, inspection date, complaint date, etc., of March 20, 2002.  A preliminary evaluation action is taken to gather additional information in cases where there is only a possibility of a noncompliance.

The following types of investigations initiated as a result of information obtained from sources other than scheduled compliance test programs such as consumer complaints, industry disclosures, articles in the news media, etc:

IN (Inspection)		CP (Complaint)		MD (Manufacturer Defect)

ID (Part 574)		MI (Manufacturer Inquiry)

COMPLIANCE TESTING —

TEST PROGRAM — Tests conducted in accordance with scheduled compliance test programs

RETEST — Retesting of items that have initially failed during a scheduled compliance test program

RESPONSIVE — Not a part of a scheduled compliance test program but consists of special testing, consumer complaint testing, etc.

COMPLIANCE TESTING LEGEND —

The following identifiers are used:

STD - Federal Motor Vehicle Safety Standard (FMVSS) or Regulation (i.e., Part 575, Part 567)

LAB - Testing laboratory under contract to OVSC

GRP - Test report group number. The following identifiers are found in the last character of the GRP number for those tests other than SCHEDULED compliance tests:  R – Retest, T - Response test

SPECIAL CASES: FMVSS 109 - S=Test Program, R=Retest, C=Responsive

FMVSS 119 - A=Test Program, B=Retest, C=Responsive

US MFR/US DISTRIBUTOR - Manufacturer or distributor of motor vehicle or equipment item

MAKE - Make of motor vehicle or equipment item

MODEL - Information for motor vehicle or equipment item

STYLE/COMPONENT - Information for motor vehicle or equipment item

IDENTIFICATION NUMBER - Tire identification number

MY - Motor vehicle model year

HS NO. - Test report number used by the NHTSA Technical Information Services for identification purposes

RESULT - Test results (PASS or FAIL)

FAIL - P: performance failure

FAIL - I:  inspection failure

FAIL - L: labeling or instruction failure

| FEDERAL MOTOR VEHICLE SAFETY STANDARDS |
| --- |
| No. | STD | FMVSS TITLE | TYPE | MODE |
| 1 | 101 | Controls and Displays (Inspection) | Vehicle | Insp.-1 |
| 2 | 102 | Transmission Shift Lever Sequence, etc. (I) | Vehicle | Insp.-2 |
| 3 | 103 | Windshield Defrosting & Defogging Systems | Vehicle-1 | TEST |
| 4 | 104 | Windshield Wiping & Washing Systems | Vehicle-2 | TEST |
| 5 | 105 | Hydraulic Brake System | Vehicle-3 | TEST |
| 6 | 106 | Brake Hoses | Equip.-1 | TEST |
| 7 | 108 | Lamps, Reflective Devices, etc. | Equip.-2 | TEST |
| 8 | 109 | Passenger Car New Pneumatic Tires | Equip.-3 | TEST |
| 9 | 110 | Passenger Car Tire Selection & Rims | Vehicle-4 | TEST |
| 10 | 111 | Rearview Mirrors | Vehicle-5 | TEST |
| 11 | 113 | Hood Latch Systems (Inspection) | Vehicle | Insp.-3 |
| 12 | 114 | Theft Protection | Vehicle-6 | TEST |
| 13 | 116 | Hydraulic Brake Fluids | Equip.-4 | TEST |
| 14 | 117 | Retreaded Pneumatic Tires (Inspection) | Equipment | Insp.-4 |
| 15 | 118 | Power Operated Window Systems | Vehicle-7 | TEST |
| 16 | 119 | Truck/Bus New Pneumatic Tires | Equip.-5 | TEST |
| 17 | 120 | Truck/Bus Tire Selection & Rims | Vehicle-8 | TEST |
| 18 | 121 | Air Brake Systems | Vehicle-9 | TEST |
| 19 | 122 | Motorcycle Brake Systems | Vehicle-10 | TEST |
| 20 | 123 | Motorcycle Controls & Displays (Inspection) | Vehicle | Insp.-5 |
| 21 | 124 | Accelerator Control Systems | Vehicle-11 | TEST |
| 22 | 125 | Warning Devices | Equip.-6 | TEST |
| 23 | 129 | Passenger Car New Non-Pneumatic Tires | Equip.-7 | TEST |
| 24 | 131 | School Bus Pedestrian Safety Devices | Vehicle-12 | TEST |
| 25 | 135 | Passenger Car Brake Systems | Vehicle-13 | TEST |
| 26 | 201 | Occupant Protection in Interior Impact | Vehicle-14 | TEST |
| 27 | 202 | Head Restraints | Vehicle-15 | TEST |
| 28 | 203 | Impact Prot. for Driver from Strg. Control | Vehicle-16 | TEST |
| 29 | 204 | Steering Control Rearward Displacement | Vehicle-17 | TEST |
| 30 | 205 | Glazing Materials (Inspection) | Equipment | Insp.-6 |
| 31 | 206 | Door Locks & Door Retention Components | Equip.-8 | TEST |
| 32 | 207 | Seating Systems | Vehicle-18 | TEST |
| 33 | 208 | Occupant Crash Protection | Vehicle-19 | TEST |
| 34 | 209 | Seat Belt Assemblies | Equip.-9 | TEST |
| 35 | 210 | Seat Belt Assembly Anchorages | Vehicle-20 | TEST |
| 36 | 212 | Windshield Mounting | Vehicle-21 | TEST |
| 37 | 213 | Child Restraint Systems | Equip.-10 | TEST |
| 38 | 214 | Side Impact Protection | Vehicle-22 | TEST |
| 39 | 216 | Roof Crush Resistance | Vehicle-23 | TEST |
| 40 | 217 | Bus Window Retention & Release | Vehicle-24 | TEST |
| 41 | 218 | Motorcycle Helmets | Equip.-11 | TEST |
| 42 | 219 | Windshield Zone Intrusion | Vehicle-25 | TEST |
| 43 | 220 | School Bus Rollover Protection | Vehicle-26 | TEST |
| 44 | 221 | School Bus Body Joint Strength | Vehicle-27 | TEST |
| 45 | 222 | School Bus Passenger Seating | Vehicle-28 | TEST |
| 46 | 223 | Rear Impact Guards | Equip.-12 | TEST |
| 47 | 224 | Rear Impact Protection (Inspection) | Vehicle | Insp.-7 |
| 48 | 225 | Child Restraint Anchorage Systems | Vehicle-29 | TEST |
| 49 | 301 | Fuel System Integrity | Vehicle-30 | TEST |
| 50 | 302 | Flammability of Interior Materials | Equip.-13 | TEST |
| 51 | 303 | Fuel System Integrity of CNG Vehicles | Vehicle-31 | TEST |
| 52 | 304 | CNG Fuel Container Integrity | Equip.-14 | TEST |
| 53 | 305 | Electric Vehicles | Vehicle-32 | TEST |
| 54 | 401 | Interior truck Release | Vehicle | TEST |
| 55 | 500 | Low Speed Vehicle Requirements | Vehicle-33 | TEST |
| SUMMARY: 34 vehicle standards, 14 equipment standards, 7 inspection standards |

REPORTS ACCEPTED DURING MAY 2006 FOR FY 2006 TEST PROGRAM

A “FAIL” result is the first indication of a possible non-compliance issue that will undergo further analysis by NHTSA.  Consumers should continue to use a vehicle or equipment item unless notified by the manufacturer to stop.

| STD | LAB/ GRP | MFR/ DISTRIB | MY/MAKE/ MODEL/STYLE | RESULT/ HS NO. |
| --- | --- | --- | --- | --- |
| 106 | ITS 001 | PONTIAC | 2006 PONTIAC GTO BRAKE HOSE | PASS 638217 |
| 106 | ITS 002 | FORD | 2006 FORD FREESTYLE BRAKE HOSE | PASS 638218 |
| 106 | ITS 003 | JP GROUP A/S | 2006 JP GROUP A/S BRAKE HOSE | PASS 638223 |
| 106 | ITS 004 | JP GROUP A/S | 2006 JP GROUP A/S BRAKE HOSE | FAIL-P 638224 |
| 108 | CAN 002 | MAXZONE | 2002 DEPO FORD F-150 LAMPS | FAIL-P 638269 |
| 108 | CAN 003 | SABRY LEE | 2003 EAGLE EYES FORD F-150 LAMPS | FAIL-P 638267 |
| 108 | CAN 004 | GMC | 2002 GUIDE CHEVROLET SILVERADO LAMPS | FAIL-P 638245 |
| 118 | KAR 001 | KIA | 2006 KIA SPORTAGE MPV 4-DOOR | PASS 638287 |
| 206 | KAR 002 | BMW | 2006 BMW 750LI DOOR LATCH/HINGE | PASS 638208 |
| 206 | KAR 003 | MAZDA | 2006 MAZDA MX-5 MIATA DOOR LATCH/HINGE | PASS 638209 |
| 206 | KAR 008 | MAZDA | 2006 MAZDA MAZDA5 DOOR LATCH/HINGE | PASS 638210 |
| 206 | KAR 009 | DAIMLER/ CHRYSLER | 2006 MERCEDES-BENZ CLS500 DOOR LATCH/HINGE | PASS 638254 |
| 206 | KAR 012 | TOYOTA | 2006 TOYOTA MATRIX DOOR LATCH/HINGE | PASS 638211 |
| 206 | KAR 013 | TOYOTA | 2006 TOYOTA MATRIX DOOR LATCH/HINGE | PASS 638212 |
| 206 | KAR 014 | TOYOTA | 2006 TOYOTA 4-RUNNER DOOR LATCH/HINGE | PASS 638213 |
| 206 | KAR 015 | TOYOTA | 2006 TOYOTA 4-RUNNER DOOR LATCH/HINGE | PASS 638214 |
| 206 | MGA 015 | HONDA | 2006 ACURA MDX DOOR LATCH/HINGE | PASS 638188 |
| 209 | DTB 012 | KIA | 2006 KIA SEDONA (VQ) FRONT SEAT BELT ASSY. | PASS 638189 |
| 213 | UST 001 | BRITAX | 2006 BRITAX COMPANION CHILD RESTRAINT | PASS 638215 |
| 213 | UST 003 | BRITAX | 2006 BRITAX ROUNDABOUT CHILD RESTRAINT | PASS 638216 |

REPORTS ACCEPTED DURING MAY 2006 FOR FY 2006 TEST PROGRAM

A “FAIL” result is the first indication of a possible non-compliance issue that will undergo further analysis by NHTSA.  Consumers should continue to use a vehicle or equipment item unless notified by the manufacturer to stop.

| STD | LAB/ GRP | MFR/ DISTRIB | MY/MAKE/ MODEL/STYLE | RESULT/ HS NO. |
| --- | --- | --- | --- | --- |
| 213 | UST 004 | BRITAX | 2006 BRITAX MARATHON CHILD RESTRAINT | PASS 638219 |
| 213 | UST 005 | BRITAX | 2006 BRITAX DECATHLON CHILD RESTRAINT | PASS 638220 |
| 213 | UST 006 | BRITAX | 2006 BRITAX BOULEVARD CHILD RESTRAINT | PASS 638221 |
| 213 | UST 007 | BRITAX | 2006 BRITAX REGENT CHILD RESTRAINT | PASS 638222 |
| 213 | UST 012 | DOREL | 2006 SAFETY 1ST DESIGNER 22 CHILD RESTRAINT | PASS 638228 |
| 213 | UST 013 | DOREL | 2006 COSCO ARRIVA W/BASE CHILD RESTRAINT | PASS 638229 |
| 213 | UST 014 | DOREL | 2006 COSCO ARRIVA CHILD RESTRAINT | PASS 638230 |
| 213 | UST 015 | DOREL | 2006 COSCO DREAM RIDE SE CHILD RESTRAINT | PASS 638231 |
| 213 | UST 016 | DOREL | 2006 COSCO FIRST RIDE DX CHILD RESTRAINT | PASS 638232 |
| 213 | UST 017 | DOREL | 2006 COSCO TOURIVA 5 PT CHILD RESTRAINT | PASS 638239 |
| 213 | UST 018 | DOREL | 2006 SAFETY 1ST ENSPIRA 5 PT CHILD RESTRAINT | PASS 638240 |
| 213 | UST 019 | DOREL | 2006 SAFET 1ST INTERA CHILD RESTRAINT | PASS 638241 |
| 213 | UST 021 | DOREL | 2006 COSCO ALPHA OMEGA CHILD RESTRAINT | PASS 638242 |
| 213 | UST 023 | DOREL | 2006 COSCO SCENERA OHB CHILD RESTRAINT | PASS 638233 |
| 213 | UST 039 | GRACO | 2006 GRACO ASSURA CHILD RESTRAINT | PASS 638256 |
| 213 | UST 040 | GRACO | 2006 GRACO ASSURA CHILD RESTRAINT | PASS 638257 |
| 213 | UST 041 | GRACO | 2006 GRACO SNUGRIDE CHILD RESTRAINT | PASS 638258 |
| 213 | UST 042 | GRACO | 2006 GRACO SNUGRIDE CHILD RESTRAINT | PASS 638259 |
| 213 | UST 043 | GRACO | 2006 GRACO COMFORT SPORT CHILD RESTRAINT | PASS 638260 |
| 213 | UST 044 | GRACO | 2006 GRACO CHERISHED CARGO CHILD RESTRAINT | PASS 638261 |
| 213 | UST 045 | GRACO | 2006 GRACO TRESURED CARGO CHILD RESTRAINT | PASS 638262 |
| 213 | UST 047 | PEG PEREGO | 2006 PEG PEREGO PRIMO VIAGGIO CHILD RESTRAINT | PASS 638288 |
| 213 | UST 050 | RECARO | 2006 RECARO YOUNG SPORT CHILD RESTRAINT | PASS 638265 |

REPORTS ACCEPTED DURING MAY 2006 FOR FY 2006 TEST PROGRAM

A “FAIL” result is the first indication of a possible non-compliance issue that will undergo further analysis by NHTSA.  Consumers should continue to use a vehicle or equipment item unless notified by the manufacturer to stop.

| STD | LAB/ GRP | MFR/ DISTRIB | MY/MAKE/ MODEL/STYLE | RESULT/ HS NO. |
| --- | --- | --- | --- | --- |
| 213 | UST 053 | DOREL | 2006 COSCO SCENERA CHILD RESTRAINT | PASS 638234 |
| 213 | UST 054 | DOREL | 2006 COSCO SUMMIT DELUXE CHILD RESTRAINT | PASS 638235 |
| 213 | UST 055 | DOREL | 2006 EDDIE BAUER COMFORT CHILD RESTRAINT | PASS 638236 |
| 213 | UST 056 | DOREL | 2006 SAFETY 1ST ENSPIRA OHB CHILD RESTRAINT | PASS 638237 |
| 213 | UST 057 | DOREL | 2006 EDDIE BAUER COMFORT INFANT CHILD RESTRAINT | PASS 638238 |
| 214 | CAL 002 | KIA | 2006 KIA SEDONA MINIVAN | PASS 638227 |
| 214 | CAL 003 | BMW | 2006 BMW 325I 4-DOOR SEDAN | PASS 638244 |
| 218 | UST 004 | KBC | 2006 FOX TRACER PRO COMP. FACIAL MOTORCYCLE HELMET | PASS 638271 |
| 218 | UST 005 | FULMER HELMETS | 2006 FULMER AF-M MODUS COMP. FACIAL MOTORCYCLE HELMET | FAIL-P 638272 |
| 301 | CAL 001 | DAIMLER/ CHRYSLER | 2003 DODGE BRAUN ENTERVAN CONVERSION VAN | PASS 638255 |

COMPLIANCE INVESTIGATIONS (CIs) IN PROGRESS THROUGH MAY 2006

(CI NUMBER SYSTEM EXAMPLE: “CI-208-041220” FOR FMVSS 208 WITH A

TEST FAILURE DATE OF DECEMBER 20, 2004)

# NONE

## CIs OPENED SINCE LAST REPORT

###### NONE

# CIs CLOSED SINCE LAST REPORT

###### NONE

CAUSE:

PE Petition

CT Compliance Test

IN Inspection

CP Complaint

ID Part 574

MI Mfgr. Inquiry

MD Mfgr. Defect

#### PRELIMINARY EVALUATION INVESTIGATIONS (PEs) IN PROGRESS THROUGH MAY 2006

(PE NUMBER SYSTEM EXAMPLE: “PE-208-041220” FOR FMVSS 208 WITH A

TEST FAILURE DATE OF DECEMBER 20, 2004)

| PE NO. | MFR/MY/MAKE/MODEL/FAILURE | CAUSE |
| --- | --- | --- |
| PE-201-050325 | General Motors Corp./2005 Buick Lactosse/Upper roof rail target ( Ur2):1164 HIC<1000 HIC | CT |
| PE-208-050721 | Volvo North America Corp./2005 Volvo S40/Data request/Passenger failed Nij | CT |

PEs OPENED SINCE LAST REPORT

NONE

## PEs CLOSED SINCE LAST REPORT

NONE

CAUSE:

PE Petition

CT Compliance Test

IN Inspection

CP Complaint

ID Part 574

MI Mfgr. Inquiry

MD Mfgr. Defect

# Footnotes

Under review - failed inspection.

Under review - photometry failure in lower beam.

Under review - photometry failure in upper and lower beam.

Under review - lower beam failed multiple test points.

Under review, Failed penetration - 1st strike; Crown Region