Project Number:  AW-2271

Contract Number:  TW-0663

November 4, 1994

SPECIAL SPECIFICATION

SECTION 10100

VISUAL DISPLAY BOARDS

Page

PART 1 - GENERAL

1.01	Description Of Work	2

1.02	Quality Assurance	2

1.03	Submittals	2

1.04	Product Delivery, Storage And Handling	3

1.05	Warranty	3

1.06	Manufacturers	3

PART 2 - PRODUCTS

2.01	Marker Boards	3

2.02	Tackboards	4

2.03	Trim And Accessories	5

PART 3 - EXECUTION

3.01	Surface Conditions	5

3.02	Installation	6

3.03	Adjust And Clean	6

SPECIAL SPECIFICATION

SECTION 10100

VISUAL DISPLAY BOARDS

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	Work included:  Provide dry marker boards and tackboards where shown on the drawings, as specified herein, and as needed for a complete and proper installation.

B.	Related Work:

1.	Documents affecting work of this section include, but are not necessarily limited to sections in Division 1 of these specifications.

2.	Provide all blocking, and other means of construction necessary to complete the work in a first class manner.

1.02	QUALITY ASSURANCE

A.	Use adequate numbers of skilled workmen who are thoroughly trained and experienced in the necessary crafts and who are completely familiar with the specified requirements and methods needed for proper performance of the work of this section.

B.	Workmanship and materials shall meet requirements and recommendations of the Porcelain Enamel Institute (PEI) and the American Society for Testing and Materials (ASTM).

C.	All materials used shall contain asbestos fibers.

1.03	SUBMITTALS

A.	Manufacturer's specifications and other data needed to prove compliance with the specified requirements;

B.	Shop drawings in sufficient detail to show fabrication, installation, anchorage, and interface of the work of this section with the work of adjacent trades;

C.	Manufacturer's recommended installation procedures which, when approved by the SDR, will become the basis for accepting or rejecting actual installation procedures used on the work.

1.04	PRODUCT DELIVERY, STORAGE AND HANDLING

A.	Deliver in manufacturer's standard packaging unopened and undamaged. Evidence of damage upon delivery will indicate that the items are unacceptable.

B.	Store in an area protected from weather and construction damage.

1.05	WARRANTY

A.	Dry Marker Board:  Provide manufacturer's written warranty against warpage, delamination, or any defect where the dry writing surface does not retain its original writing and erasing qualities, and to repair or replace any work which proves to be defective in workmanship or material, for the lifetime of the building.

B.	Tackboards:  Provide manufacturer's written warranty against defects, lamination and general workmanship for one (1) year.

1.06	MANUFACTURERS

Acceptable Manufacturers:

Claridge Products and Equipment, Inc.

Carolina Chalkboard Co.

Greensteel, Inc.

Alliance Wall Corp.

Nelson-Adams Co.

Capaul Corp.

Other manufacturers approved in advance by the SDR.

PART 2 - PRODUCTS

2.01	DRY MARKER BOARDS

A.	All dry marker boards shall be porcelain enamel steel manufactured to exceed the performance specifications for porcelain enamel boards S104 of the Porcelain Institute.  The dry marker boards shall be capable of supporting papers by means of magnets.  The writing surfaces shall resist wear and damage from shock and abrasion and shall not dent, shatter or crack.  The surfaces shall retain their original color, writing, and erasing qualities and shall not become glossy or shiny in normal use.  The reflectance factor shall not be less than 15% nor more than 20% as recommended by the American Illuminating Engineering Society.

B.	Provide dry marker boards 4'-0" x 6'-0" in the locations shown on the drawings, and with the following attributes.

1.	Porcelain On Metal:  Balanced, high pressure laminated, 3 ply construction, with facing sheet, core, and backing.  Provide marker boards which meet standards for wearability established in Test Method CB-1 (t) by Porcelain Enamel Institute, Inc., and as follows:

2.	Facing Sheet:  Fired vitreous porcelain enamel writing surface not less than 0.0025" over enameling grade steel which has been aluminized or primed on both surfaces.

3.	Porcelain Enamel:  Standard matte finish.

4.	Core:  1/2" particleboard or equal.

5.	Backing Sheet:  Manufacturer's standard 0.005" thick aluminum.

6.	Laminating Adhesive:  Manufacturer's standard moisture resistant, flexible thermoplastic type, developed for this purpose with no unbonded areas.

7.	Chalk Trough:  Furnish manufacturer's standard continuous aluminum chalk troughs for each marker board.  Box type, with slanted front and cast aluminum end closures, contoured to match marker tray.

8.	Color as selected by SDR from manufacturer's standard range of colors.

C.	Edges and Butt  Joints:

1.	All edges and butt joints shall be porcelain enamel.

2.	Joints:  Where vertical joints occur, a fourteen (14) gauge continuous concealed steel spline shall be fitted tightly into grooves in the core material.  All rabbeting to be done at the factory so as to give a smooth butt joint.  Exposed metal joint covers will not be acceptable.

2.02	TACKBOARDS

Provide tackboards 6'-0" long by 4'-0" high in the locations and configurations and curves shown on the drawings, and with the following attributes.

A.	Equal to Solutions 200 Wall Panels, by Capaul Corp., or approved equal, 3/4" tackboard, of 10 lb. high density fiberglass bonded to honeycomb.

B.	Trim:  Factory installed, Z-bar clip angle mounted.

C.	Fire Rated Core:  Class A per ASTM E-84

D.	Fabric:  Class A per ASTM E-84

E.	Adhesive:  Class A per ASTM E-84

F.	Edge to be beveled, PVC reinforced, fabric wrapped all four (4) sides. Provide J-mold for bottom edge in fabric wrapped to match finish.

G.	Finish:  Guilford of Main FR701 polyester fabrics or approved equal, color as selected by SDR.

2.03	TRIM AND ACCESSORIES

A.	General:

1.	Fabricate frames and trim of not less than 0.062" thick aluminum alloy, size and shape as shown, to suit type of installation.  Provide straight, single length units wherever possible and keep joints to a minimum.  Miter corners to neat, hairline closure.  Furnish exposed aluminum trim, accessories, and fasteners with satin anodized finish AA-M31231.

2.	Provide manufacturer's standard trim units, Type AX Series by Greensteel, or approved equal.  Provide integral continuous concealed hanger bar support at top, angle clips at bottom.

3.	When structural support accessories are required for marker and tackboards in addition to normal trim, provide such additional support or modify trim as required to provide necessary support.  See paragraph C. below.

B.	Maprail:  Furnish integral maprails at the tops of all marker board units and at other locations indicated on the drawings.  The following accessories shall be furnished for each maprail:

1.	Display Rail:  Continuous cork approximately 2" wide, integral with maprail.

2.	Manufacturer Standard End Stop:  One at each end of maprails.

3.	Map hooks with flexible metal clips, 1201T combination map hook and paper holder by Greensteel, or approved equal; 10 required at each marker.

C.	Other Materials:  Provide all other materials, not specifically described but required for a complete and proper installation, as selected by the contractor subject to the review of the SDR.

PART 3 - EXECUTION

3.01	SURFACE CONDITIONS

A.	Examine the areas and conditions under which work of this section will be performed.  Correct conditions detrimental to timely and proper completion of the work.  Do not proceed until unsatisfactory conditions are corrected.

B.	Provide blocking in wall to receive units.  Verify heights prior to installing blocking.  Fire rate blocking as required by type of construction.

3.02	INSTALLATION

A.	Install the work of this section in strict accordance with the original design, the approved shop drawings, and the manufacturer's recommended installation procedures as approved by the SDR, anchoring all components firmly into position for long life under hard use.

B.	Keep perimeter lines straight, plumb, and level.  Provide all grounds, clips, backing materials, adhesives, brackets, anchors, trim and accessories necessary for a complete installation.

C.	Anchor all components securely using tamper-proof fasteners, where accessible or with completely concealed continuous hangers.

D.	Coordinate job site assembled units with grounds, trim, and accessories.  Join all parts with a neat, precision fit.

E.	Bottom edge of tackboards terminating at bases shall be protected with a "J" molding.  Set molding horizontally prior to installing tackboards.

3.03	ADJUST AND CLEAN

Inspect all work at completion and replace any damaged units at no additional cost to the owner.

END OF SECTION