MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A07563 | In-Flight Anomaly Number -- | Contractor Report Number E-080 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title RSS BATTERY VOLTAGE SENSOR, SHORT TO GROUND |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (2) B (X) C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT-4 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE ELECTRICAL CABLE | PART# 80931003704-059 | SER/LOT# 0000091 | MANUFACTURER MMC |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause MP - MFG-PRC |
| System ELECTRICAL | Defect DC - BROKEN | Material E - EL C/W | Work Contact R. LUNDEN | Fail Date 11/03/1983 |
| Received at MSFC 11/16/1983 | Date Isolated -- | FMEA Reference 3.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text LWT-3 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 10/11/1984 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design G. PLATT | Chief Engineer -- | S & MA D. NEWMAN | Project R. ABRAHAM | Project MGR -- |
| Approval |
| Design G. PLATT | Chief Engineer -- | S & MA D. NEWMAN | Project J. BREWER | Project MGR -- |
| PAC Assignee M. GLASS | PAC Review Complete MG | MSFC Closure Date 11/19/1984 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A "SHORT TO GROUND" ELECTRICAL FAILURE OCCURRED IN THE RANGE SAFETY SYSTEM ON LWT-4 WHILE ON LAUNCH PAD AT KSC |
| Contractor Investigation/Resolution CAUSE - FAILURE WAS DUE TO CABLE INSULATION DAMAGE, DISCOVERED DURING TROUBLESHOOTING OF RSS BATTERYCIRCUIT. INDICATED 0.6 VOLTS WHEN SHOULD INDICATE 37 VOLTS. 11/21/83 PRB STATUS - F.A. CONTINUING, INVESTIGATING WIRE DAMAGE & FAB. PROCESS. 1/17/84 - STS-11, LWT-3, LAUNCH CONSTRAINT IS LIFTED BASED ON THE FOLLOWING RATIONALE: ANALYSIS HASDETERMINED THE ONLY FLIGHT SAFETY ISSUES ARE SRB IGNITION & SEPARATION. THESE FUNCTIONS CANNOT BE CHECKED DURING FINAL LAUNCH PREPARATIONS, AND ANY ENSUING SHORT (CAUSED BY MOISTURE COMBINED WITH A WIRE DEFECT) COULD NOT BE DETECTED DURING THIS PERIOD OF TIME. RATIONALE FOR ACCEPTANCE FOR FLIGHT WITH THESE CONDITIONS ARE: (A) COMPLETE REDUNDANCY FOR THESE FUNCTIONS FOR BOTH RIGHT AND LEFT SRB'S (B) PROBABILITY OF TWO (2) DEFECTS OCCURRING & BEING COMBINED WITH MOISTURE RESULTING IN TWO (2) SHORTS CAUSING LOSS OF ONE FUNCTION IS 4 OUT OF 100,000. (C) REVIEW OF ET CABLE TRAY HOUSING SRB FUNCTIONS INDICATES THAT NO WATER WOULD BE ALLOWED TO ACCUMULATE DUE TO DRAIN PROVISIONS. (D) PRELAUNCH TESTING HAS REVEALED NO EVIDENCE OF WIRING DEFECTS. (E) CONTINUED TESTING OF OTHER ET/SRB FUNCTIONS USING THE SAME WIRE AND EXPOSED TO THE SAME ENVIRONMENTAL CONDITIONS WILL SERVE AS AN INDICATOR OF WIRING INTEGRITY. THE RATIONALE AS STATED ABOVE AND THE SUCCESSFUL PERFORMANCE OF NINE OTHER ET'S BUILT SIMILARLY AREBASIS FOR LIFTING STS-11, ET-10, LWT-3 LAUNCH CONSTRAINT. THIS CHANGE HAS BEEN CO-ORDINATED WITH THE ET PROJECT OFFICE. G. P. BRIDWELL 1/27/84 1/30/84 - (ADDED PER MR BRIDWELL'S REQUEST) ADDITIONAL RATIONALE FOR LIFTING STS-11, LWT-3, LAUNCH CONSTRAINT PROVIDED BY MMC STATES: WIRE TESTS SHOW PUNCTURED WIRES SUBMERGED IN A SALINE/WATER SOLUTION REQUIRED FROM 10 TO 2,600 MINUTES (AVG. 90 MIN.) FOR A HARD SHORT (LESS THAN 1050 OHMS RESISTANCE TO GRN) TO OCCUR. SRB FIRE COMMAND PULSES ARE 14.6 MILLISECS. THEREFORE NO KNOWN FAILURE MECHANISM EXISTS ATER TEST JUST PRIOR TO LAUNCH 2/23/84 - CONSTRAINT FOR STS-13 IS LIFTED BASED ON SAME RATIONALE AS STATED ABOVE FOR STS-11, LWT-3;ADDITIONALLY, A SINGLE FAILURE OF WIRING WILL NOT INHIBIT SRB IGNITION CIRCUITS OR SRB SEPARATION CIRCUITS DUE TO REDUNDANCY. THIS CHANGE HAS BEEN COORDINATED WITH THE E.T. PROJECT OFFICE - ____G. P. BRIDWELL 2-24-84____. 3/8/84 PRB STATUS - NOT DISCUSSED IN DETAIL (PREVIOUSLY REVIEWED AT PRB'S & FRR'S). NO CONSTRAINT TO ANY ET. ALL ET WIRE & CABLES ARE SUBJECTED TO SEVERAL TESTS. DELAY IN CLOSING CAPS DUE TO MMC TOOLING & FACILITY CHANGES. MR M. PESSIN/SA32 REQUESTED MMC TO EFFECT IMMEDIATE IN-HOUSE COORDI- NATION TO EXPEDITE THE FACILITY (WORK TABLES) CHANGES & IF THERE IS A PROB TO CONTACT HIM AS HE CONSIDERS THIS TO BE AN URGENT ISSUE. 4/19/84 - LAUNCH CONSTRAINT FOR STS-14, LWT-6, IS LIFTED BASED ON THE SAME RATIONALE AS PREVIOUSLY STATED FOR STS-11 & 13. THIS CHANGE HAS BEEN COORDINATED WITH THE ET PROJECT OFFICE - ___G. P. BRIDWELL__. 9/6/84 - PRB STATUS, PER MMC ALL R/C ACTIONS COMPLETED; CAPS TO BE SUBMITTED TO MSFC BY 9-11-84. 9/13/84 - LAUNCH CONSTRAINT FOR STS-17, LWT-8, IS LIFTED ON RATIONALE AS PREVIOUSLY STATED FOR STS-1& 13. THIS DECISION HAS BEEN CO-ORDINATED WITH THE ET PROJECT OFFICE - ____G. P BRIDWELL___. 10/15/84 RESOLUTION - AS A RESULT OF THE ORIGINAL ON THE LAUNCH PAD FAILURE, A SWEEPING REVIEW OF ALL FACTORS THAT COULD AFFECT RELIABILITY OF WIRE HARNESSES WAS CONDUCTED. THE PRODUCTION CYCLE FROM MFR'G OF THE WIRE THRU THE SHIPPING OF THE COMPLETED E.T. WAS COVERED SIGNIFICANT IMPROVE- MENTS WERE INCORP'D AS DETAILED IN CAPS C/A DISCUSSION. RECURRENCE CONTROL - INCLUDED IMPROVED HANDLING OF WIRE, IMPROVED TOOLING, IMPROVED WORKING TRAIN- ING/CERTIFICATION, DESIGN CHANGES IN CRITIAL CIRCUITS, IMPROVED CABLE TRAY DRAINAGE, AND IMPROVED CABLE TESTING METHODS (REF OPERATIONS DIRECTIVE 203050 SUP L ET/MGT-286 REV 002) |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A07563 | IFA# -- | Contractor RPT# E-080 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80931003704-059 | Asmnt Part Name ELECTRICAL CABLE | Asmnt Serial/Lot# 91 |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MP - MFG-PRC | FAIL MODE EL - SHORT |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |