Intelligent Transportation Systems (ITS)

Commercial Vehicle Operations (CVO)

POR-98-7121

Draft Version D.1

July 1998

Prepared for

US Department of Transportation

Federal Highway Administration

400 Seventh Street, SW

Washington, DC  20590

Prepared by

The Johns Hopkins University

Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, MD  20723-6099

Please note that this is a Draft Issue

It is important to note that this is a draft document.  The document is incomplete and contains sections that have not been reviewed externally.  The material presented herein will undergo several iterations of review and comment before a baseline version is published.

If there are any comments or questions about this document, please address them to:

The Johns Hopkins University Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, Maryland 20723-6099

Attention:  James H. Polaha (Building 24-E296)

Phone:		(240) 228-3361

FAX:		(240) 228-6198

E-Mail:	James.Polaha@jhuapl.edu

Acknowledgments

The author would like to acknowledge the help of the Software Engineering and Operations (PSE) Group at JHU/APL in completing Chapter 1.  Some information in this chapter was obtained from the Software Engineering Standards, Configuration Management and Change Control; June 15, 1996; Standard #10; Version 3.0.

The use of two IEEE Standards proved to be valuable as well:

1)	IEEE Std 610.12-1990, IEEE Standard Glossary of Software Engineering Terminology

2)	IEEE Std 828-1990, IEEE Standard for Software Configuration Management Plans (ANSI)

Thanks also to the Virginia and Maryland State Agencies for their help in obtaining the hardware and software configuration data.

TABLE OF CONTENTS

1.	Configuration Management and Change Control	1

1.1	Introduction	1

1.1.1	Definition	1

1.1.2	Purpose	1

1.1.3	Scope	1

1.2	Content of Standard	1

1.2.1	Configuration Management	1

1.2.2	Configuration Control Board	1

1.2.3	Configuration Management Activities	3

1.2.3.1	Configuration Items	3

1.2.3.2	Configuration Identification	3

1.2.3.3	Configuration Control	4

1.2.3.4	Configuration Status Accounting	4

1.2.3.5	Configuration Audits and Reviews	4

2.	Audit Trails	4

2.1	CVISN System Activity Log	4

2.2	CVISN Change Request Form (CRF)	4

2.3	CVISN System Maintenance Log	5

3.	CVISN Hardware and Software Configuration Items	5

4.	Glossary of Terminology	6

5.	APPENDIX A: Applied Physics Laboratory CVISN Equipment	18

5.1	Applied Physics Laboratory Primary CVISN Server Configuration	18

5.2	Applied Physics Laboratory Secondary CVISN Server Configuration	23

5.3	Applied Physics Laboratory Common CVISN Server Configuration	27

6.	APPENDIX B: Virginia CVISN Equipment	30

6.1	Virginia Primary CVISN Server Configuration	30

6.2	Virginia Secondary CVISN Server Configuration	33

6.3	Virginia Common CVISN Server Configuration	37

6.4	Virginia First CVISN Client Configuration	39

6.5	Virginia Second CVISN Client Configuration	43

6.6	Virginia Third CVISN Client Configuration	47

6.7	Virginia Fourth CVISN Client Configuration	51

6.8	Virginia First CVISN CATS Client Configuration	55

6.9	Virginia Second CVISN CATS Client Configuration	59

6.10	Virginia CVISN Pilot Computer Client Configuration	63

7.	APPENDIX C: Maryland CVISN Equipment	68

7.1	Maryland Primary CVISN Server Configuration	68

7.2	Maryland Secondary CVISN Server Configuration	71

8.	APPENDIX D: Applied Physics Laboratory System Files and Directories	76

8.1	CVIEW System Files and Directories	76

8.2	OPCON (Operator’s Console) System Files and Directories	79

8.2.1	Hardware Requirements	79

8.2.2	Software Requirements	80

8.2.3	Network Requirements	80

9.	APPENDIX E: RS Information Systems Software Configuration Items Electronic Credentialing Subsystem (CATS, SATS, CI)	84

10.	APPENDIX F: IDT Software Configuration Items (CAT, CI)	86

List of Figures

Figure 1: CVISN System Activity Log Entry Page	10

Figure 2: CVISN Change Request Form (CRF) [obverse]	13

Figure 3: CVISN Change Request Form (CRF) [reverse]	14

Figure 4: CVISN System Maintenance Log Page	15

List of Tables

Table 1: JHU/APL Safety Systems CCB Members	2

Table 2: JHU/APL Electronic Screening CCB Members	2

Table 3: JHU/APL Credentialing CCB Members	2

Table 4: Maryland Safety Systems and Electronic Screening CCB Members	2

Table 5: Maryland Credentialing CCB Members	2

Table 6: Virginia Safety Systems and Electronic Screening CCB Members	3

Table 7: Virginia Credentialing CCB Members	3

Table 8:  APL Primary CVISN Server Hardware Configuration	19

Table 9:  APL Primary CVISN Server Software Configuration	20

Table 10:  APL Secondary CVISN Server Hardware Configuration	25

Table 11:  APL Secondary CVISN Server Software Configuration	26

Table 12:  APL Common CVISN Servers Hardware Configuration	27

Table 13:  VA Primary CVISN Server Hardware Configuration (System Number 1700)	31

Table 14:  VA Primary CVISN Server Software Configuration	32

Table 15:  VA Secondary CVISN Server Hardware Configuration (System Number 1701)	35

Table 16:  VA Secondary CVISN Server Software Configuration	36

Table 17:  VA Common CVISN Servers Hardware Configuration (includes System Number 1646)	37

Table 18:  VA First CVISN Client Hardware Configuration (System Number 1639)	41

Table 19:  VA First CVISN Client Software Configuration	42

Table 20:  VA Second CVISN Client Hardware Configuration (System Number 1640)	45

Table 21:  VA Second CVISN Client Software Configuration	46

Table 22:  VA Third CVISN Client Hardware Configuration (System Number 1641)	49

Table 23:  VA Third CVISN Client Software Configuration	50

Table 24:  VA Fourth CVISN Client Hardware Configuration (System Number 1642)	53

Table 25:  VA Fourth CVISN Client Software Configuration	54

Table 26:  VA First CVISN CATS Client Hardware Configuration (System Number 1643)	57

Table 27:  VA First CVISN CATS Client Software Configuration	58

Table 28:  VA Second CVISN CATS Client Hardware Configuration (System Number 1645)	61

Table 29:  VA Second CVISN CATS Client Software Configuration	62

Table 30:  VA CVISN Pilot Computer Client Hardware Configuration (System Number 1644)	65

Table 31:  VA CVISN Pilot Computer Client Software Configuration	66

Table 32:  MD Primary CVISN Server Hardware Configuration	69

Table 33:  MD Primary CVISN Server Software Configuration	70

Table 34:  MD Secondary CVISN Server Hardware Configuration	73

Table 35:  MD Secondary CVISN Server Software Configuration	74

Table 36:  APL CVIEW System Files and Directories	76

Table 37:  APL OPCON System Files and Directories	80

This Page Intentionally Blank

# Configuration Management and Change Control

## Introduction

### Definition

Configuration Management (CM) serves as a means of establishing procedures and directives to be used in controlling the Commercial Vehicle Information Systems and Networks (CVISN) server hardware and software.  The procedures established are intended to support all system developers and to provide a framework through which CM principles may be applied.  Change Control, as defined in this document, is the process of controlling the hardware and software through all its changes.

### Purpose

The purpose of the Configuration Management and Change Control standard is to describe how to manage change approval and to control hardware modifications and software versions for all parties concerned.

The procedures will form the basis for:

1.	identifying the configuration management items

2.	controlling changes to configuration items

3.	establishing and maintaining status of changes and implementations

4.	allowing approval of all changes

### Scope

This document covers all hardware and software residing on the CVISN Prototype Servers and Workstations located in Maryland and Virginia and at The Johns Hopkins University Applied Physics Laboratory (JHU/APL).

## Content of Standard

### Configuration Management

Configuration Management is a discipline applying technical and administrative direction and surveillance to identify and document characteristics of a configuration item (CI). A Configuration Item is the hardware, software, or design that is under control.  The Configuration Management process will be administered with the aid of a Configuration Management System.  This system will be used to identify, control, audit, and review all configuration items.  Configuration Control Boards (CCBs) manage the process.  The CCB is a team of technical and program management representatives who are responsible for evaluating and recommending corrective actions for controlled configuration items.

The Configuration Items that this document manages are described in Appendices A-D.  These sections include Configuration Items for The Johns Hopkins University Applied Physics Laboratory, Virginia, and Maryland CVISN Prototype Servers and Workstations.

### Configuration Control Board

Configuration Items are managed by the CCB.  Each CI modification must be approved by the CCB.

Currently, CCBs have been established in the areas of Safety Systems, Electronic Screening and Credentialing and are composed of the following individuals:

Table 1: JHU/APL Safety Systems CCB Members

| Name | Org | Project Area | Phone Number | E-mail Address |
| --- | --- | --- | --- | --- |
| Paul D. North | JHU/APL | Safety Systems Program Manager | (443) 778-6627 | Paul.North@jhuapl.edu |
| Alan A. Mick | JHU/APL | SAFER Project Manager | (443) 778-7386 | Alan.Mick@jhuapl.edu |
| James H. Polaha | JHU/APL | CVIEW Project Manager | (443) 778-3361 | James.Polaha@jhuapl.edu |
| Robert H. Goldfarb | JHU/APL | Project Team Member | (443) 778-7635 | Robert.Goldfarb@jhuapl.edu |
| Onna B. Roberts | JHU/APL | Project Team Member | (443) 778-4615 | Onna.Roberts@jhuapl.edu |

Table 2: JHU/APL Electronic Screening CCB Members

| Name | Org | Project Area | Phone Number | E-mail Address |
| --- | --- | --- | --- | --- |
| Karen S. Smith | JHU/APL | Screening | (443) 778-8747 | Karen.Smith@jhuapl.edu |
| Janet A. Spedden | JHU/APL | Screening | (443) 778-8959 | Janet.Spedden@jhuapl.edu |

Table 3: JHU/APL Credentialing CCB Members

| Name | Org | Project Area | Phone Number | E-mail Address |
| --- | --- | --- | --- | --- |
| Karen S. Smith | JHU/APL | Prototype Manager | (443) 778-8747 | Karen.Smith@jhuapl.edu |
| Thomas W. Hormby | JHU/APL | CAT/CI | (443) 778-8572 | Tom.Hormby@jhuapl.edu |

Table 4: Maryland Safety Systems and Electronic Screening CCB Members

| Name | Org | Project Area | Phone Number | E-mail Address |
| --- | --- | --- | --- | --- |
| Ronald G. Ward | MD MVA | Communications Software Support Manager | (410) 768-7607 | Dtrgw@mdot.state.md.us |
| Kim Meiklejohn | MD MVA | MD CCB POC | (410) 768-7560 | Dmkam@mdot.state.md.us |
| Louis Wells | MD MVA | Data Processing Manager | (410) 768-7325 | Dplcw@mdot.state.md.us |
| Thomas W. Hormby | JHU/APL | CAT/CI | (443) 778-8572 | Tom.Hormby@jhuapl.edu |
| DJ Waddell | JHU/APL | MD System Architect | (443) 778-5878 | Richard.Waddell@jhuapl.edu |
| Karen S. Smith | JHU/APL | Prototype State Advisor | (443) 778-8747 | Karen.Smith@jhuapl.edu |

Table 5: Maryland Credentialing CCB Members

| Name | Org | Project Area | Phone Number | E-mail Address |
| --- | --- | --- | --- | --- |
| Ronald G. Ward | MD MVA | Communications Software Support Manager | (410) 768-7607 | Dtrgw@mdot.state.md.us |
| Kim Meiklejohn | MD MVA | MD CCB POC | (410) 768-7560 | Dmkam@mdot.state.md.us |
| Louis Wells | MD MVA | Data Processing Manager | (410) 768-7325 | Dplcw@mdot.state.md.us |
| Thomas W. Hormby | JHU/APL | CAT/CI | (443) 778-8572 | Tom.Hormby@jhuapl.edu |
| DJ Waddell | JHU/APL | MD System Architect | (443) 778-5878 | Richard.Waddell@jhuapl.edu |
| Karen S. Smith | JHU/APL | Prototype State Advisor | (443) 778-8747 | Karen.Smith@jhuapl.edu |

Table 6: Virginia Safety Systems and Electronic Screening CCB Members

| Name | Org | Project Area | Phone Number | E-Mail Address |
| --- | --- | --- | --- | --- |
| Dave Hajduk | RSIS | System Architect | (804) 367-1863 | dhajduk@erols.com |
| Herb Bridges | VA | Enforcement | (804)378-3487 | none |
| C. T. Wicker | VA VDOT | Roadside Technical | (804)236-3585 | cwicker.vdot@state.va.us |
| Lynn Sivels | VA VDOT | Roadside Operations | (804) 786-3950 | lsivels.vdot@state.va.us |
| Dave Williams | VA DMV | VA CCB POC | (804) 367-1587 | dmvdxw@richmond.infi.net |

Table 7: Virginia Credentialing CCB Members

| Name | Org | Project Area | Phone Number | E-Mail Address |
| --- | --- | --- | --- | --- |
| Dave Hajduk | RSIS | System Architect | (804) 367-1863 | dhajduk@erols.com |
| Charlotte M. Ladd | VA DMV | Credentialing Technical | (804) 367-8383 | dmvchl@richmond.infi.net |
| Julian Fitzgerald | VA DMV | Credentialing Operations | (804) 367-9157 | none |
| Judy L. Vesely | VA DMV | Credentialing Operations | (804) 367-0130 | dmvjlv@richmond.infi.net |
| Dave Williams | VA DMV | VA CCB POC | (804) 367-1587 | dmvdxw@richmond.infi.net |

### Configuration Management Activities

#### Configuration Items

The CCB will determine the configuration items.  Once established, the hardware and software will be controlled at the item level.  That means that changes will result in new versions of software or modifications/upgrades to hardware at an item level, not a subset of an item.

For example, the 33.6/28.8 Kbps external modems listed in Table 8:  APL Primary CVISN Server Hardware Configuration are considered hardware configuration items (HWCI), but the integrated 32-bit fast-wide SCSI-2 storage controller (also listed in the table) is NOT a HWCI since it is a sub-item under the personal computer HWCI.

As a software example, the IMH_SERV.exe file listed in Table 36:  APL CVIEW System Files and Directories are computer software configuration items (CSCI), but the modules within the executable are NOT a CSCI since they are not under configuration management.

To manage HWCIs and CSCIs, there must be an established configuration management process (CMP).  This process includes baselining, configuration identification, configuration control, configuration status accounting, and configuration auditing.  Once a baseline is established, any future modifications to the baseline must be requested through the appropriate CCB and the proposed modification will then be evaluated and either approved, disapproved, or deferred.  Change requestors will be notified of CCB decisions.

#### Configuration Identification

Configuration identification activities shall identify, name, and describe the documented physical and functional characteristics of the HWCI and CSCI.  The documents are acquired for configuration control.  Controlled items may be intermediate or final outputs (such as executable code, source code, user documentation, program listings, data bases, test cases, test plans, specifications, and management plans) and elements of the support environment (such as compilers, operating systems, programming tools, and test beds).

#### Configuration Control

Configuration control activities involve evaluating, approving or disapproving changes to baselined CIs.  Changes encompass both error correction and enhancement.  The degree of formality necessary for the change process depends on the affected project baseline and on the impact of the change within the configuration structure.

#### Configuration Status Accounting

Configuration status accounting activities involve recording and reporting the status of project CIs.

#### Configuration Audits and Reviews

Configuration audits determine to what extent the actual CI reflects the required physical and functional characteristics.  Configuration reviews are management tools for establishing a baseline.

# Audit Trails

System audit trails are designed to monitor various types of system activity which include general server/workstation activity, request change activity, and maintenance activity.  These activities are monitored using the CVISN System Activity Log, CVISN Change Request Form (CRF), and CVISN System Maintenance Log, respectively.

## CVISN System Activity Log

The system users manually maintain the activity log.  Entries will be made in the activity log when a user begins and ends a computer session.  A blank Activity Log is shown in Figure 1: CVISN System Activity Log Entry Page.  The column titles and information to be completed are:

1.	Entry Number - a sequential number entered by the user for purposes of tracking entries

2.	Date - the date in month/day/year format (MM/DD/YY) entered by the user

3.	User ID or Account ID - the user’s ID with which they logged onto the system

4.	Full Printed Name - the user’s full printed name

5.	Start Time - the local time when the user began work on the system in hours:minutes format (HH:MM)

6.	Brief Description of Work - A concise statement of the current work or task the user is performing.

7.	Stop Time - the local time when the user completed work on the system in hours:minutes format (HH:MM)

The last column (Review) will be completed by the cognizant CCB member responsible for periodic reviews of the activity log.

## CVISN Change Request Form (CRF)

The obverse and reverse sides of a CRF are shown in Figure 2 and Figure 3, respectively.  Any user should complete the CRF when a hardware or software change request is submitted.  The user must complete side one of the form, including the header information (NOT the CRF Number field), Part 1 of 5 of the CRF (Change), and submit the CRF to the appropriate CCB.  The CCB will assign a person to analyze the request and complete Part 2 of 5 of the CRF (Analysis).  The CRF will be then forwarded to the person responsible for making necessary system modifications who will complete Part 3 of 5 of the CRF (Correction).  The CCB will notify the request originator of applied modifications after which Part 4 of 5 (Test or Review) will be completed by the person responsible for the modification.  Part 5 of 5 (Release) will be completed by both a development site tester, where the change request was initially corrected, and a field site tester, where the change request originated.

These forms are retained for the lifetime of the system and provide one of the primary sources of information on hardware and software change requests and modifications.

## CVISN System Maintenance Log

Users performing hardware or software maintenance or modifications to the CVISN servers must complete a system maintenance log.  A sample of the CVISN System Maintenance Log is shown in Figure 4.

The following steps must be followed in order to perform maintenance or apply modifications to the CVISN Server hardware or software.

- Prior arrangements must be made with the party responsible for site maintenance/modification activities (as listed in Tables 1-7) before maintenance and/or modifications are applied.

- These arrangements must be made and confirmed at least one working day before the actual hardware or software is modified.

- Upon arrival at the CVISN System site, the user who will perform the maintenance or apply the modifications must notify the responsible party specified above.

- If the user making the modifications cannot satisfy all the above criteria, the work will not be performed.

- The user must complete the CVISN System Maintenance Log after performing maintenance/modification activities.

These logs are retained for the lifetime of the equipment and provide one of the primary sources of information on hardware and software changes and modifications.

# CVISN Hardware and Software Configuration Items

The material in Appendices A through D includes the Configuration Items (CI) for the CVISN Prototype hardware and software.  These include JHU/APL, Maryland and Virginia hardware and COTS software, and JHU/APL developed software.  A description of CIs for software developed by RSIS and IDT will be provided by the individual companies and included in this document (see Appendices E and F).

# Glossary of Terminology

The terms in this glossary are defined in the IEEE Std. 610.12-1990, IEEE Standard Glossary of Software Engineering Terminology.

allocated baseline.  In configuration management, the initial approved specifications governing the development of configuration items that are part of a higher level configuration item.  Contrast with: developmental configuration; functional baseline; product baseline.  See also: allocated configuration identification.

allocated configuration identification.  In configuration management, the current approved specifications governing the development of configuration items that are part of a higher level configuration item.  Each specification defines the functional characteristics that are allocated from those of the higher level configuration item, establishes the tests required to demonstrate achievement of its allocated functional characteristics, delineates necessary interface requirements with other associated configuration items, and establishes design constraints, if any.  Contrast with: functional configuration identification; product configuration identification.  See also: allocated baseline.

baseline.  (1) A specification or product that has been formally reviewed and agreed upon, that thereafter serves as the basis for further development, and that can be changed only through formal change control procedure.

(2) A document or a set of such documents formally designated and fixed at a specific time during the life cycle of a configuration item.  Note: Baselines, plus approved changes from those baselines, constitute the current configuration identification.  See also: allocated baseline; developmental configuration; functional baseline; product baseline.

(3) Any agreement or result designated and fixed at a given time, from which changes require justification and approval.

CCB.  (1) Acronym for configuration control board.

(2) Acronym for change control board.

change control.  See: configuration control.

change control board.  See: configuration control board.

CI.  Acronym for configuration item.

CM.  Acronym for configuration management.

computer software component (CSC).  A functionally or logically distinct part of a computer software configuration item, typically an aggregate of two or more software units.

computer software configuration item (CSCI).  An aggregation of software that is designated for configuration management and treated as a single entity in the configuration management process.  Contrast with: hardware configuration item.  See also: configuration item.

configuration.  (1) The arrangement of a computer system or component as defined by the number, nature, and interconnections of its constituent parts.

(2) In configuration management, the functional and physical characteristics of hardware or software as set forth in technical documentation or achieved in a product.  See also: configuration item; form, fit, and function; version.

configuration audit.  See: functional configuration audit; physical configuration audit.

configuration control.  An element of configuration management, consisting of the evaluation, coordination, approval or disapproval, and implementation of changes to configuration items after formal establishment of their configuration identification.  Syn: change control.  Contrast with: configuration identification; configuration status accounting.  See also: configuration control board; deviation; engineering change; interface control; notice of revision; specification change notice; waiver.

configuration control board (CCB).  A group of people responsible for evaluating and approving or disapproving proposed changes to configuration items, and for ensuring implementation of approved changes.  Syn: change control board.  See also: configuration control.

configuration identification.  (1) An element of configuration management, consisting of selecting the configuration items for a system and recording their functional and physical characteristics in technical documentation.  Contrast with: configuration control; configuration status accounting.

(2) The current approved technical documentation for a configuration item as set forth in specifications, drawings, associated lists, and documents referenced therein.  See also: allocated configuration identification; functional configuration identification; product configuration identification; baseline.

configuration index.  A document used in configuration management, providing an accounting of the configuration items that make up a product.  See also: configuration item development record; configuration status accounting.

configuration item (CI).  An aggregation of hardware, software, or both, that is designated for configuration management and treated as a single entity in the configuration management process.  See also: hardware configuration item; computer software configuration item; configuration identification; critical item.

configuration management (CM).  A discipline applying technical and administrative direction and surveillance to: identify and document the functional and physical characteristics of a configuration item, record and report change processing and implementation status, and verify compliance with specified requirements.  See also: baseline; configuration identification; configuration control; configuration status accounting; configuration audit.

configuration status accounting.  An element of configuration management, consisting of the recording and reporting of information needed to manage a configuration effectively.  This information includes a listing of the approved configuration identification, the status of proposed changes to the configuration, and the implementation status of approved changes.  Contrast with: configuration control; configuration identification.  See also: configuration index; configuration item development record.

critical item.  In configuration management, an item within a configuration item that, because of special engineering or logistic considerations, requires an approved specification to establish technical or inventory control at the component level.

developmental configuration.  In configuration management, the software and associated technical documentation that defines the evolving configuration of a computer software configuration item during development.  Note: The developmental configuration is under the developer’s control, and therefore is not called a baseline.  Contrast with: allocated baseline; functional baseline; product baseline.

deviation.  (1) A departure from a specified requirement.

(2) A written authorization, granted prior to the manufacture of an item, to depart from a particular performance or deign requirement for a specific number of units or a specific period of time.  Note: Unlike an engineering change, a deviation does not require revision of the documentation defining the affected item.  See also: configuration control.  Contrast with: engineering change; waiver.

engineering change.  In configuration management, an alteration in the configuration of a configuration item or other designated item after formal establishment of its configuration identification.  See also: configuration control; engineering change proposal.  Contrast with: deviation; waiver.

engineering change proposal (ECP).  In configuration management, a proposed engineering change and the documentation by which the change is described and suggested.  See also: configuration control.

form, fit, and function.  In configuration management,  that configuration comprising the physical and functional characteristics of an item as an entity, but not including any characteristics of the elements making up the item.  See also: configuration identification.

functional baseline.  In configuration management, the initial approved technical documentation for a configuration item.  Contrast with: allocated baseline; developmental configuration; product baseline.

functional configuration audit (FCA).  An audit conducted to verify that the development of a configuration item had been completed satisfactorily, that the item has achieved the performance and functional characteristics specified in the functional or allocated configuration identification, and that its operational and support documents are complete and satisfactory.  See also: configuration management; physical configuration audit.

functional configuration identification.  In configuration management, the current approved technical documentation for a configuration item.  It prescribes all necessary functional characteristics, the tests required to demonstrate achievement of specified functional characteristics, the necessary interface characteristics with associated configuration items, the configuration item’s key functional characteristics and its key lower level configuration items, if any, and design constraints.  Contrast with: allocated configuration identification; product configuration identification.  See also: functional baseline.

hardware configuration item (HWCI).  An aggregation of hardware that is designated for configuration management and treated as a single entity in the configuration management process.  Contrast with: computer software configuration item.  See also: configuration item.

interface control.  (1) (IEEE Std 828-1983) In configuration management, the process of: (a) identifying all functional and physical characteristics relevant to the interfacing of two or more configuration items provided by one or more organizations, and (b) ensuring that proposed changes to these characteristics are evaluated and approved prior to implementation.

(2) (DoD usage) In Configuration management, the administrative and technical procedures and documentation necessary to identify functional and physical characteristics between and within configuration items provided by different developers, and to resolve problems concerning the specified interfaces.  See also: configuration control.

notice of revision (NOR).  A form used in configuration management to propose revisions to a drawing or list, and, after approval, to notify users that the drawing or list has been , or will be, revised accordingly.  See also: configuration control; engineering change; specification change notice.

physical configuration audit (PCA).  An audit conducted to verify that a configuration item, as built, conforms to the technical documentation that defines it.  See also: functional configuration audit.

product baseline.  In configuration management, the initial approved technical documentation (including, for software, the source code listing) defining a configuration item during the production, operation, maintenance, and logistic support of its life cycle.  Contrast with: allocated baseline; developmental configuration; functional baseline.  See also: product configuration identification.

product configuration identification.  The current approved or conditionally approved technical documentation defining a configuration item during the production, operation, maintenance, and logistic support phases of its life cycle.  It prescribes all necessary physical or form, fit, and function characteristics of a configuration item, the selected functional characteristics designated for production acceptance testing, and the production acceptance tests.  Contrast with: allocated configuration identification; functional configuration identification.  See also: product baseline.

SCN.  Acronym for specification change notice.

software configuration management.  See: configuration management.

specification change notice (SCN).  A document used in configuration management to propose, transmit, and record changes to a specification.  See also: configuration control; engineering change; notice of revision.

version.  (1) An initial release or re-release of a computer software configuration item, associated with a complete compilation or recompilation of the computer software configuration item.

(2) An initial release or complete re-release of a document, as opposed to a revision resulting from issuing change pages to a previous release.

See also: configuration control; version description document.

waiver.  A written authorization to accept a configuration item or other designated item which, during production or after having been submitted for inspection, is found to depart from specified requirements, but is nevertheless considered suitable for use as is or after rework by an approved method.  See also: configuration control.  Contrast with: deviation; engineering change.

| Entry Number | Date | User ID or Account ID | Full Printed Name | Start Time | Brief Description of Work (include any CRF numbers, documentation references, etc.) | Stop Time | Review |
| --- | --- | --- | --- | --- | --- | --- | --- |

Figure 1: CVISN System Activity Log Entry Page

Change Request Date:  ________________			CRF Number:  ________________

Requestor’s Full Printed Name:  _______________________________  Organization:  _______

Requestor’s Phone Number:  (  __  __  __  )  __  __  __      __  __  __  __  ext. __  __  __  __  __

Requestor’s FAX Number:  (  __  __  __  )  __  __  __      __  __  __  __

Requestor’s E-Mail Address:  _____________________________________________________

Priority (as perceived by the requestor):         HIGH         MEDIUM         LOW         (circle one)

Product:  ________________________________	Attachments:    Yes     No    (circle one)

Location where the change request was detected:  _____________________________________

If it is a software change, please provide the software package and build/version number.

If it is a documentation change, please provide the document title, version, and date.

Title: ______________________________Version #: _________ Date: _________TS #:  _____

Part 1 of 5: CHANGE

(Describe the change requested below and attach additional pages if necessary.  Please describe what you were doing and what you want changed.  Use a new form for each change requested.)

Figure 2: CVISN Change Request Form (CRF) [obverse]

Part 2 of 5: ANALYSIS	CRF Number:  ______________	CCB:  ______________________________

Change Title:  ________________________________________________________________________________

Priority (as assigned by the CCB):  H  M  L			Assigned to:  _______________________________

(	Error

(	Enhancement

(	Not in Error – Explain and Return to Originator

(	Insufficient Information for Analysis – See Explanation below

(	Previously Reported on CRF Number __________

(	Other – Explain below

Explanation:

Estimated Cost: :

Approval of Proposed Change: (CCB USE ONLY)

( Approve ( Disapprove ( Defer Authorized by: _______________

DATE: _______________

Does this change have an external impact?     YES     NO     (circle one)

This problem affects the following field sites:  APL MD SAIC VA Other _______________ (circle all that apply)

Corrective Action Organization:    APL    IDT    MD    RSIS    SAIC    VA    Other  _______________ (circle one)

Analysis Performed by:  ____________________________________  Date:  ____________________

Part 3 of 5: CORRECTION (Attach suggested test case information, if it applies.)

Describe change here and provide info about test cases performed

Change:

Actual Cost:

Work Performed by (Signature): ____________________________________  Date: ____________________

Part 4 of 5: TEST or REVIEW (Demonstrate change in test environment -- attach test case info.)

Describe the testing that was performed

Assigned Tester Response:

Approval to Promote: (CCB USE ONLY)

CCB: ________________

DATE: ______________

Verified by Development Site Tester (Signature): _______________________________  Date: _______________

Part 5 of 5: RELEASE (Provide software or documentation release information in this section)

Product:  _______________________________________	Release Date: ____________________

Version Number:  _________________________________	Build Number:  _____________________________

Release Site(s):  _______________________________________________________________________________

Work Performed by (Signature): ____________________________________  Date: ____________________

Verified by Field Site Tester (Signature): _______________________________  Date: ____________________

Figure 3: CVISN Change Request Form (CRF) [reverse]

| Entry/Tracking Number |  |
| --- | --- |
| Date |  |
| Printed Name (First and Last) |  |
| Phone Number (including area code) |  |
| Organization (APL, MD, RSIS, SAIC, VA, etc.) |  |
| Machine Name (Server or Workstation Name) |  |
| Project (SAFER, CVIEW, CI, SafeVUE, etc.) |  |
| Hardware or Software Issue |  |
| Install (Was any HW or SW installed? Which? What version? How? If it was HW, please include the Manufacturer, Vendor, Model Number, Serial Number, and Part Number.) | Manufacturer: _________________________ Vendor: __________________ Model #: __________________________ Part #: _______________________ Serial #: ________________________________________________________ |
| Modify (Was any HW or SW modified? Which? What version? How?) |  |
| Problem (Was there a problem? Was there a CRF number? Was it resolved? Does it need to be resolved? Is there a maintenance contract? If so, who is the contact person?) |  |
| Resolution (Issue, Change, or Problem Resolution) |  |

Figure 4: CVISN System Maintenance Log Page

This Page Intentionally Blank

APPENDIX A: APL Hardware and Software Configuration Items

# APPENDIX A: Applied Physics Laboratory CVISN Equipment

## Applied Physics Laboratory Primary CVISN Server Configuration

MACHINE NAME:				APLCVISN1

PRIMARY OR SECONDARY:		Primary Server

HARDWARE LOCATION:		The Johns Hopkins University Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, Maryland 20723-6099

Building 8, Room 73

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS:				128.244.23.10

IP DOMAIN NAME:			TRANS.JHUAPL.EDU

NT DOMAIN NAME:			CVISNNET

MODEM PHONE NUMBER(S):		(443) 778-3343

(443) 778-3393

PRIMARY POINT OF CONTACT:	James Polaha

Phone:	(443) 778-3361

Fax:	(443) 778-6198

E-Mail:	James.Polaha@jhuapl.edu

Table 8:  APL Primary CVISN Server Hardware Configuration

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number |
| --- | --- | --- | --- | --- | --- | --- |
| personal computer | 1 | Compaq |  | ProLiant 5000 6/200 Model 1 | D623HVN10589??? | 219200-001??? |
| standard features: |  |  |  |  |  |  |
| Intel Pentium Pro 200 MHz microprocessor |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |
| 256 MB RAM |  |  |  |  |  |  |
| 8 total I/O expansion slots (7 available) |  |  |  |  |  |  |
| {7 PCI (6 available), 3 EISA, 2 shared PCI/EISA} |  |  |  |  |  |  |
| Netelligent 10/100 TX PCI UTP network interface controller |  |  |  |  |  |  |
| integrated 32-bit fast-wide SCSI-2 storage controller |  |  |  |  |  |  |
| integrated 1024x768, 16-color non-interlaced video system |  |  |  |  |  |  |
| internal quad-speed CD-ROM drive |  | Compaq |  | CRD-254V |  |  |
| keyboard |  | Compaq |  | RT101 | 1GD39DG03661 | 120375-001B |
| mouse |  | Compaq |  | M-S34-6MD | 1D75BDEF0Q3X | 141189-201 |
| internal options: |  |  |  |  |  |  |
| Pentium Pro 200/256K Kit | 1 | Compaq |  |  |  | 228411-001 |
| 4.3 GB Drive | 4 | Compaq |  | Fast-Wide SCSI-2 |  | 199598-001 |
| SMART-2 array controller/P3 | 1 | Compaq |  |  |  | 194753-001 |
| 2/8 GB DAT tape drive (4mm) | 1 | ARCHIVE |  | Python 27871-XXX |  | 140219-001 |
| PC/8E ports model | 1 | Digi |  |  |  | 700-00738 |
| Fast EtherLink XL PCI Ethernet Network Interface Card | 1 | 3Com |  | 10/100BASE-TX |  | 3C905-TX |
| 33.6/28.8 Kbps external modem | 1 | US Robotics |  | Courier V.Everything | 20XOB6D6RQ40 | 80-001224-02 |
| 33.6/28.8 Kbps external modem | 1 | US Robotics |  | Courier V.Everything | 20XOB6F6S452 | 80-001224-02 |
| 151FS color monitor | 1 | Compaq |  | 444 | 550BA11AG895 | 147265-601 |
| Uninterruptable Power Supply (UPS) | 1 | APC |  | SU1000NET | WS9736143607 |  |
| printer | 1 | Hewlett Packard |  | C3155A | USHB009247 | 5MP |

Table 9:  APL Primary CVISN Server Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Borland Local Interbase Server |  |  | Borland |  | INT1342WWFS180 |  |  |  |
| Distinct TCP/IP for Windows Run Time Extensions - 32 bit |  | 1 | Distinct | Distinct Corporation | T32-106 | 1.3 | S000000010007787 | 91-E7-09 |
| Distinct TCP/IP for Windows SDK - Standard Edition - 32 bit | 1 |  | Distinct | Distinct Corporation | T32-102 | 1.0 | P000000010004953 | 8E-E7-32 |
| Microsoft Windows NT Server with 5 client licenses | 1 |  | Microsoft | Microsoft Corporation | 94338 | 4.0 | 001012M1004E106229 |  |
| NTMail | 1 |  | Internet Shopper Ltd. | Internet Shopper Ltd. |  | 3.02.10 | QS0780/A (-) | BwY7MAYEC*Js |
| ODBC Driver Support | 1 |  | DataDirect | Intersolv Inc. |  |  |  |  |
| ODBC Single Driver WINNT/WIN95 (Oracle Database) | 1 |  | DataDirect | Intersolv Inc. | DDOPNDRV | 3.0.00G | 110000011130 | none |
| Oracle7 Workgroup Server for Windows NT | 1 |  | Oracle | Oracle Corporation | A47900-3 | 7.3.2.2.1 |  | none |
| PaperFree EDI Translator Desktop Workstation Run Time | 1 |  | PaperFree Systems Inc. | PaperFree Systems Inc. | P212 | WIN-RTP-WIN95 Runtime (DLL version |  |  |
| PaperFree EDI WinRTP upgrades | 1 |  | PaperFree Systems Inc. | PaperFree Systems Inc. | P12 |  | SQGB000A2B74796 |  |
| Powerbuilder Professional | 1 |  | Powersoft |  | P60014 | 5.0 |  |  |
| Hot Metal Pro |  | 1 | SoftQuad |  |  | 3.0 |  |  |
| Netscape Navigator |  | 1 | Netscape | Netscape Communications Corp. | 41-01666-00 | 2.0 | PE-200A03526437930 |  |
| Borland Delphi Developer 32 bit and 16 bit |  | 1 | Borland Int’l | Delphi |  | 2.0 | HDB1320WW10182 |  |
| Backup Exec |  | 1 | Seagate Software Inc. | Arcada |  | 6.1 | 0-9-424-6-000-1-047294 |  |
| Microsoft Office Standard |  | 1 | Microsoft | Microsoft Corporation |  | 7.0A | 021-056V700 | 425-0118013 |
| Microsoft Visual C++ Professional Subscription |  | 1 | Microsoft | Microsoft Corporation | M122 073 | 4.2 | 90118 | 411-0266876 |
| Microsoft Visual SourceSafe |  | 1 | Microsoft | Microsoft Corporation | 64519 | 4.0 | 007B58805209600144 | 411-0030657 |
| Microsoft Visual SourceSafe (Upgrade Offer) |  | 1 | Microsoft | Microsoft Corporation | 64520 | 4.0 | 324-056-007 | 411-0050691 |
| Microsoft Visual Test |  | 1 | Microsoft | Microsoft Corporation | 64600 | 4.0 | 163-056-008 | 411-0134033 |
| Oracle Developer 2000 |  | 1 | Oracle | Oracle Inc. | A32000-5 |  | 1042-1157 |  |

## Applied Physics Laboratory Secondary CVISN Server Configuration

MACHINE NAME:				APLCVISN2

PRIMARY OR SECONDARY:		Secondary Server

HARDWARE LOCATION:		The Johns Hopkins University Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, Maryland 20723-6099

Building 8, Room 73

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS:				128.244.23.12

IP DOMAIN NAME:			TRANS.JHUAPL.EDU

NT DOMAIN NAME:			CVISNNET

MODEM PHONE NUMBER(S):		(443) 778-3351

(443) 778-3352

PRIMARY POINT OF CONTACT:	James Polaha

Phone:	(443) 778-3361

Fax:	(443) 778-6198

E-Mail:	James.Polaha@jhuapl.edu

Table 10:  APL Secondary CVISN Server Hardware Configuration

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number |
| --- | --- | --- | --- | --- | --- | --- |
| personal computer | 1 | Compaq |  | ProLiant 5000 6/200 Model 1 | D623HVN10589??? | 219200-001??? |
| standard features: |  |  |  |  |  |  |
| Intel Pentium Pro 200 MHz microprocessor |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |
| 128 MB RAM |  |  |  |  |  |  |
| 8 total I/O expansion slots (7 available) |  |  |  |  |  |  |
| {7 PCI (6 available), 3 EISA, 2 shared PCI/EISA} |  |  |  |  |  |  |
| Netelligent 10/100 TX PCI UTP network interface controller |  |  |  |  |  |  |
| integrated 32-bit fast-wide SCSI-2 storage controller |  |  |  |  |  |  |
| integrated 1024x768, 16-color non-interlaced video system |  |  |  |  |  |  |
| internal quad-speed CD-ROM drive |  | Compaq |  | CRD-254V |  |  |
| keyboard |  | Compaq |  | RT101 | 1GD39DG03656 | 120375-001B |
| mouse |  | Compaq |  | M-S34-6MD | 1D75BDEF13PW | 141189-201 |
| internal options: |  |  |  |  |  |  |
| Pentium Pro 200/256K Kit | 1 | Compaq |  |  |  | 228411-001 |
| 4.3 GB Drive | 4 | Compaq |  | Fast-Wide SCSI-2 |  | 199598-001 |
| SMART-2 array controller/P3 | 1 | Compaq |  |  |  | 194753-001 |
| 2/8 GB DAT tape drive (4mm) | 1 | ARCHIVE |  | Python 27871-XXX |  | 140219-001 |
| PC/8E ports model | 1 | Digi |  |  |  | 700-00738 |
| Fast EtherLink XL PCI Ethernet Network Interface Card | 1 | 3Com |  | 10/100BASE-TX |  | 3C905-TX |
| 33.6/28.8 Kbps external modem | 1 | US Robotics |  | Courier V.Everything | 20XOB6F6S4F4 | 80-001224-02 |
| 33.6/28.8 Kbps external modem | 1 | US Robotics |  | Courier V.Everything | 20XOB6F6S43G | 80-001224-02 |
| 151FS color monitor | 1 | Compaq |  | 444 | 550BA11AG575 | 147265-601 |
| Uninterruptable Power Supply (UPS) | 1 | APC |  | SU1000NET | WS9736143608 |  |
| printer | 1 | Hewlett Packard |  | C3155A | USHB009247 | 5MP |

Table 11:  APL Secondary CVISN Server Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Borland Local Interbase Server |  |  | Borland |  | INT1342WWFS180 |  |  |  |
| Distinct TCP/IP for Windows Run Time Extensions - 32 bit | 1 |  | Distinct | Distinct Corporation | T32-106 | 1.2 | S000000010005858 | ??? |
| Distinct TCP/IP for Windows Run Time Extensions - 32 bit |  | 1 | Distinct | Distinct Corporation | T32-106 | 1.3 | S000000010007788 | 21-67-22 |
| Microsoft Windows NT Server with 5 client licenses | 1 |  | Microsoft | Microsoft Corporation | 94338 | 4.0 | 001012M1004E106158 |  |
| NTMail | 1 |  | Internet Shopper Ltd. | Internet Shopper Ltd. |  | 3.02.10 | QS0780/B (-) | BwY7MAQtG*J] |
| ODBC Driver Support | 1 |  | DataDirect | Intersolv Inc. |  |  |  |  |
| ODBC Single Driver WINNT/WIN95 (Oracle Database) | 1 |  | DataDirect | Intersolv Inc. | DDOPNDRV | 3.0.00G | 110000011130 | none |
| Oracle7 Workgroup Server for Windows NT | 1 |  | Oracle | Oracle Corporation | A47900-3 | 7.3.2.2.1 |  | none |
| PaperFree EDI Translator Desktop Workstation Run Time | 1 |  | PaperFree Systems Inc. | PaperFree Systems Inc. | P212 | WIN-RTP-WIN95 Runtime (DLL version) |  |  |
| PaperFree EDI WinRTP upgrades | 1 |  | PaperFree Systems Inc. | PaperFree Systems Inc. | P12 |  |  |  |
| Powerbuilder Professional Deployment Kit | 1 |  | Powersoft |  | P60014 | 5.0 |  |  |
| Hot Metal Pro |  | 1 |  |  |  |  |  |  |
| Netscape Navigator |  | 1 |  | Netscape Communications Corp. |  |  |  |  |
| Borland Delphi |  | 1 |  |  |  |  |  |  |
| Backup Exec |  | 1 |  |  |  |  |  |  |
| Microsoft Office Standard |  | 1 | Microsoft | Microsoft Corporation |  | 7.0A | 021-056V700 | 425-0118013 |
| Microsoft Visual C++ Professional Subscription |  | 1 | Microsoft | Microsoft Corporation | M122 073 | 4.2 | 90118 | 411-0266876 |
| Microsoft Visual SourceSafe |  | 1 | Microsoft | Microsoft Corporation | 64519 | 4.0 | 007B58805209600144 | 411-0030657 |
| Microsoft Visual SourceSafe (Upgrade Offer) |  | 1 | Microsoft | Microsoft Corporation | 64520 | 4.0 |  |  |
| Microsoft Visual Test |  | 1 | Microsoft | Microsoft Corporation | 64600 | 4.0 |  |  |

## Applied Physics Laboratory Common CVISN Server Configuration

COMMON HARDWARE EQUIPMENT:		Applied Physics Laboratory CVISN Servers

LOCATION:					The Johns Hopkins University Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, Maryland 20723-6099

Building 8, Room 73

Table 12:  APL Common CVISN Servers Hardware Configuration

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number |
| --- | --- | --- | --- | --- | --- | --- |
| Ethernet 5 Port Workgroup Hub | 1 | Linksys |  | EW5HUB | none |  |

APPENDIX B: Virginia Hardware and Software Configuration Items

# APPENDIX B: Virginia CVISN Equipment

## Virginia Primary CVISN Server Configuration

MACHINE NAME:				VADMVCVIEW1

PRIMARY OR SECONDARY:		Primary Server

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.220

172.16.38.221-239

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		(804) 367-1541 COM3

(804) 367-1548 COM4

(804) 367-1948 COM5

(804) 367-1949 COM6

NOTE:  All four phone lines are on the primary server.

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 13:  VA Primary CVISN Server Hardware Configuration (System Number 1700)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Compaq |  | ProLiant 5000 6/200 | SD622HVN10581 | 219200-001 | 0014108 | 0669 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium Pro 200 MHz microprocessor |  |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |  |
| 64 MB RAM (expandable to 1 GB) |  |  |  |  |  |  |  |  |
| 8 total I/O expansion slots (7 available) |  |  |  |  |  |  |  |  |
| {7 PCI (6 available), 3 EISA, 2 shared PCI/EISA} |  |  |  |  |  |  |  |  |
| Netelligent 10/100 TX PCI UTP network interface controller |  |  |  |  |  |  |  |  |
| integrated 32-bit fast-wide SCSI-2 storage controller |  |  |  |  |  |  |  |  |
| integrated 1024x768, 16-color non-interlaced video system |  |  |  |  |  |  |  |  |
| internal quad-speed CD-ROM drive |  | Compaq |  | CRD-254V |  |  |  |  |
| keyboard |  | Compaq |  | RT101 | 1GD39DE40959 | 120375-001B |  |  |
| mouse |  | Compaq |  | M-S34-6MD | 1D75BDEF067Y | 141189-201 |  |  |
| internal options: |  |  |  |  |  |  |  |  |
| Pentium Pro 200/256K Kit | 1 | Compaq |  |  |  | 228411-001 |  |  |
| 4.3 GB Drive | 4 | Compaq |  | Fast-Wide SCSI-2 |  | 146742-005 |  |  |
| SMART-2 array controller/P3 | 1 | Compaq |  |  |  | 194753-001 |  |  |
| 2/8 GB DAT tape drive (4mm) | 1 | ARCHIVE |  | Python 27871-XXX |  | 142019-001 |  |  |
| Ingram Digi Acceleport 8E ISA DB25 | 1 | Digi | inacom |  |  | I303494 |  |  |
| Token Ring Card | 1 | Madge |  | Smart 16/4 PCI Ringnode (bus master) |  | 51-02 |  |  |
| 151FS color monitor | 1 | Compaq |  | 444 | 621BA11AC342 | 147250-601 | 0013497 | 0669 |
| Uninterruptable Power Supply | 1 | APC | inacom | Back-UPS Pro 650 | 96077294957 | BP650 |  | 0669 |
| 28.8 external modem for modem pool (P1) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-2254 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P2) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-2305 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P3) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-1636 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P4) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60904-1079 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P5) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60904-1196 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P6) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-1399 | I319822 |  | 0669 |

Table 14:  VA Primary CVISN Server Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows NT Server with WEB support 3.51 |  | 1 | Compaq | inacom | 187066-006 | 3.51 |  |  | 0669 |
| Windown NT Server 4.0 | 1 |  | Microsoft | Ingram |  |  |  |  | 1399 |
| Mercator run-time engine | 1 |  | TSI | TSI |  | 1.3D |  |  | 1069 |
| Sybase SQL Anywhere - 5 User License | 1 |  |  |  |  |  |  |  |  |
| Oracle 7 Workgroup Server - 5 User License | 1 |  | Oracle | Oracle |  | 7.2 |  |  | 0684 |
| Oracle Workgroup Support |  | 1 | Oracle | Oracle |  |  | CSI#1165661 |  | 0684 1443 |
| Oracle Programmer 2000 |  | 1 | Oracle | Oracle |  | 7.2 |  |  | 0684 |
| Oracle Programmer 2000 Support |  | 1 | Oracle | Oracle |  |  | CSI#1165661 |  | 0684 |
| Oracle Developer 2000 |  | 1 | Oracle | Oracle |  | 1.3 |  |  | 0684 |
| Oracle Developer support |  | 1 | Oracle | Oracle |  |  | CSI#1165661 |  | 0684 |
| MS Visual C++ Professional Subscription |  | 1 | Microsoft | MicroAge | MCS-K-78334 | 4 |  |  | 0692 |
| Microsoft Office for NT |  | 1 | Microsoft | MicroAge | MCS-K-72722 | 7 |  |  | 0692 |
| Hot Metal Pro |  | 1 | SoftQuad | Software in a Week | I909001 | 3 |  |  | 0696 |
| Backup Exec NT |  | 1 | Microsoft | Software in a Week | I353543 | 6.1 |  |  | 0696 |
| NT Mail - SMTP/POP | 1 |  |  |  |  |  |  |  | 0772 |
| MS Visual Source Safe |  | 1 | Microsoft | MicroAge | MCS-K-78350 | 4 |  |  | 0692 |
| MS Visual Test |  | 1 | Microsoft | MicroAge | MCS-K-78227 | 4 |  |  | 0692 |
| Popkin System Architect / WIN NT |  | 1 | Popkin | Software in a Week |  |  |  |  | 0696 |
| Support for Popkin |  | 1 | Popkin | Software in a Week |  |  |  |  | 0696 |
| Key Lock device for Popkin |  | 1 | Popkin | Software in a Week |  |  |  |  | 0696 |

## Virginia Secondary CVISN Server Configuration

MACHINE NAME:				VADMVCVIEW2

PRIMARY OR SECONDARY:		Secondary Server

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.240

172.16.38.241-254

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		(804) 367-1541 COM3

(804) 367-1548 COM4

(804) 367-1948 COM5

(804) 367-1949 COM6

NOTE:  All four phone lines are on the primary server.

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 15:  VA Secondary CVISN Server Hardware Configuration (System Number 1701)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Compaq |  | ProLiant 5000 6/200 | SD622HVN10714 | 219200-001 | 0013445 | 0669 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium Pro 200 MHz microprocessor |  |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |  |
| 64 MB RAM (expandable to 1 GB) |  |  |  |  |  |  |  |  |
| 8 total I/O expansion slots (7 available) |  |  |  |  |  |  |  |  |
| {7 PCI (6 available), 3 EISA, 2 shared PCI/EISA} |  |  |  |  |  |  |  |  |
| Netelligent 10/100 TX PCI UTP network interface controller |  |  |  |  |  |  |  |  |
| integrated 32-bit fast-wide SCSI-2 storage controller |  |  |  |  |  |  |  |  |
| integrated 1024x768, 16-color non-interlaced video system |  |  |  |  |  |  |  |  |
| internal quad-speed CD-ROM drive |  | Compaq |  | CRD-254V |  |  |  |  |
| keyboard |  | Compaq |  | RT101 | 1GD39DE40959 | 120375-001B |  |  |
| mouse |  | Compaq |  | M-S34-6MD | 1D75BDEF067Y | 141189-201 |  |  |
| internal options: |  |  |  |  |  |  |  |  |
| Pentium Pro 200/256K Kit | 1 | Compaq |  |  |  | 228411-001 |  |  |
| 4.3 GB Drive | 4 | Compaq |  | Fast-Wide SCSI-2 |  | 146742-005 |  |  |
| SMART-2 array controller/P3 | 1 | Compaq |  |  |  | 194753-001 |  |  |
| 2/8 GB DAT tape drive (4mm) | 1 | ARCHIVE |  | Python 27871-XXX |  | 142019-001 |  |  |
| Ingram Digi Acceleport 8E ISA DB25 | 1 | Digi | inacom |  |  | I303494 |  |  |
| Token Ring Card | 1 | Madge |  | Smart 16/4 PCI Ringnode (bus master) |  | 51-02 |  |  |
| 151FS color monitor | 1 | Compaq |  | 444 | 621BA11AA885 | 147250-601 | 0014110 | 0669 |
| Uninterruptable Power Supply | 1 | APC | inacom | Back-UPS Pro 650 | 96077294957 | BP650 |  | 0669 |
| 28.8 external modem for modem pool (P1) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-1881 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P2) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-0109 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P3) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-0961 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P4) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-0842 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P5) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-1707 | I319822 |  | 0669 |
| 28.8 external modem for modem pool (P6) | 1 | Practical Peripherals |  | PM 288 MT II V.34 | A1037800-60807-1002 | I319822 |  | 0669 |

Table 16:  VA Secondary CVISN Server Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows NT Server with WEB support 3.51 |  | 1 | Compaq | inacom | 187066-006 | 3.51 |  |  | 0669 |
| Windown NT Server 4.0 | 1 |  | Microsoft | Ingram |  |  |  |  | 1399 |
| Mercator run-time engine | 1 |  | TSI | TSI |  | 1.3D |  |  | 1069 |
| Sybase SQL Anywhere - 5 User License | 1 |  |  |  |  |  |  |  |  |
| Oracle 7 Workgroup Server - 5 User License | 1 |  | Oracle | Oracle |  | 7.2 |  |  | 0684 |
| Oracle Workgroup Support |  | 1 | Oracle | Oracle |  |  | CSI#1165661 |  | 0684 1443 |
| Oracle Programmer 2000 |  | 1 | Oracle | Oracle |  | 7.2 |  |  | 0684 |
| Oracle Programmer 2000 Support |  | 1 | Oracle | Oracle |  |  | CSI#1165661 |  | 0684 |
| Oracle Developer 2000 |  | 1 | Oracle | Oracle |  | 1.3 |  |  | 0684 |
| Oracle Developer support |  | 1 | Oracle | Oracle |  |  | CSI#1165661 |  | 0684 |
| MS Visual C++ Professional Subscription |  | 1 | Microsoft | MicroAge | MCS-K-78334 | 4 |  |  | 0692 |
| Microsoft Office for NT |  | 1 | Microsoft | MicroAge | MCS-K-72722 | 7 |  |  | 0692 |
| Hot Metal Pro |  | 1 | SoftQuad | Software in a Week | I909001 | 3 |  |  | 0696 |
| Backup Exec NT |  | 1 | Microsoft | Software in a Week | I353543 | 6.1 |  |  | 0696 |
| NT Mail - SMTP/POP | 1 |  |  |  |  |  |  |  | 0772 |
| MS Visual Source Safe |  | 1 | Microsoft | MicroAge | MCS-K-78350 | 4 |  |  | 0692 |
| MS Visual Test |  | 1 | Microsoft | MicroAge | MCS-K-78227 | 4 |  |  | 0692 |
| Popkin System Architect / WIN NT |  | 1 | Popkin | Software in a Week |  |  |  |  | 0696 |
| Support for Popkin |  | 1 | Popkin | Software in a Week |  |  |  |  | 0696 |
| Key Lock device for Popkin |  | 1 | Popkin | Software in a Week |  |  |  |  | 0696 |

## Virginia Common CVISN Server Configuration

COMMON HARDWARE EQUIPMENT:		VA CVISN Servers

LOCATION:					Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

Table 17:  VA Common CVISN Servers Hardware Configuration (includes System Number 1646)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Token Ring Multi-station Access Unit (MAU) | 2 | Proteon | inacom | P7228 | 50778704806 | I126232 |  | 0669 |
| Storage Express II XLC comprised of: (System Number 1646) | 1 | Intel | Intelligent Decisions |  |  |  | 0014111 |  |
| Storage Express II XLC (Part 1 of 2) |  |  |  | LDS 2430 | A05765114 | 636094-001 |  | 0669 |
| Storage Express II XLC (Part 2 of 2) |  |  |  | LDS 2430 | A05765114 | 630928-001 |  | 0841 |
| Storage Express II XLC autochanger magazine |  |  |  |  |  | DSSMS48MAG |  | 0817 |
| StorageExpress Token Ring Card | 1 | Intel | inacom |  |  | SMS22TRU |  | 0669 |
| StorageExpress Tape Kit (5 tapes and cleaner) | 1 | Intel |  |  |  | SMS48TAK |  | 0669 |
| DDS-1 DAT tapes | 5 | Hewlett Packard | GBC/Globelle | 2.0Gbyte Capicity |  | HWP32426 |  | 0757 |
| DLT Kit | 1 | DLT tapes | inacom |  |  | SMS2040TAK |  | 0669 |
| DLT Peripheral | 1 | DLT peripheral | inacom |  |  | SMS00PB |  | 0669 |
| MAU power supplies | 2 | Proteon | inacom | P7901 |  |  |  | 0739 |
| MAU power supplies | 2 | Proteon | inacom |  |  | I126219 |  | 0732 |
| IEEE-1284 Centronics cables | 2 |  | GBC/Globelle | DB25M/C36M |  | CEN47336 |  | 0757 |

## Virginia First CVISN Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 18:  VA First CVISN Client Hardware Configuration (System Number 1639)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Compaq |  | DeskPro 4000 5133 MT 1.62G/32M | S6628BBK2P269 | 247310-002 | 0015659 | 0685 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 133 MHz microprocessor |  |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |  |
| 32MB RAM |  |  |  |  |  |  |  |  |
| 3.5” 1.44MB Floppy drive |  |  |  |  |  |  |  |  |
| 2MB EDO Graphics Memory |  |  |  |  |  |  |  |  |
| 1.5 GB Hard Drive |  |  |  |  |  |  |  |  |
| keyboard |  | Compaq |  | RT101 |  |  |  |  |
| mouse |  | Compaq |  | M-S34-6MD |  |  |  |  |
| internal options: |  |  |  |  |  |  |  |  |
| 8x IDE CD-ROM drive | 1 | Compaq | inacom | CRD-254V |  | 185262-001 |  | 0685 |
| 2/8GB DAT drive | 1 | Compaq | inacom |  |  | 142019-001 |  | 0685 |
| 28.8 Internal Data/fax modem | 1 | Compaq | inacom |  |  | 259213-001 |  | 0685 |
| Plug.Play SCSI Controller | 1 | Compaq | inacom |  |  | 1877749-001 |  | 0685 |
| Plug/Play Token Ring Network adaptor | 1 | Madge | inacom |  |  | 22-04 |  | 0685 |
| Token Ring Card | 1 | JetDirect | Ingram | EX Plus3 |  | J2594A |  | 0748 |
| HP JetDirect EX Plus Print Server | 1 | Hewlett Packard | inacom |  | SG63030184 | J2591A | 0015662 | 0685 |
| 151FS color monitor | 1 | Compaq |  | 444 | S612BA11AC523 | 147250-601 | 0015660 | 0685 |
| HP Laserjet 5MP 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 5MP | USHB027061 | C3155A | 0015661 | 0685 |

Table 19:  VA First CVISN Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NT Workstation |  | 1 | Microsoft | MicroAge | MCS-K-77422 | 3.51 |  |  | 0692 |
| NT Workstation | 1 |  | Microsoft |  |  | 4.0 |  |  | 1399 |
| Microsoft Office for NT | 1 |  | Microsoft | MicroAge | MCS-K-72722 | 7.0 |  |  | 0692 |
| Netscape Navigator |  | 1 |  | Software in a Week | I482557 | 2.0 |  |  | 0696 |
| Compaq Support Software CD-ROM |  | 1 | Compaq | inacom | 272505-001 |  |  |  | 0685 |
| RSIS SATS | 1 |  | FHWA | RS Information Systems |  | VA0.1 |  |  |  |

## Virginia Second CVISN Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 20:  VA Second CVISN Client Hardware Configuration (System Number 1640)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Compaq |  | DeskPro 4000 5133 MT 1.62G/32M | S6628BBK2P479 | 247310-002 | 0015663 | 0685 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 133 MHz microprocessor |  |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |  |
| 32MB RAM |  |  |  |  |  |  |  |  |
| 3.5” 1.44MB Floppy drive |  |  |  |  |  |  |  |  |
| 2MB EDO Graphics Memory |  |  |  |  |  |  |  |  |
| 1.5 GB Hard Drive |  |  |  |  |  |  |  |  |
| keyboard |  | Compaq |  | RT101 |  |  |  |  |
| mouse |  | Compaq |  | M-S34-6MD |  |  |  |  |
| internal options: |  |  |  |  |  |  |  |  |
| 8x IDE CD-ROM drive | 1 | Compaq | inacom | CRD-254V |  | 185262-001 |  | 0685 |
| 2/8GB DAT drive | 1 | Compaq | inacom |  |  | 142019-001 |  | 0685 |
| 28.8 Internal Data/fax modem | 1 | Compaq | inacom |  |  | 259213-001 |  | 0685 |
| Plug.Play SCSI Controller | 1 | Compaq | inacom |  |  | 1877749-001 |  | 0685 |
| Plug/Play Token Ring Network adaptor | 1 | Madge | inacom |  |  | 22-04 |  | 0685 |
| Token Ring Card | 1 | JetDirect | Ingram | EX Plus3 |  | J2594A |  | 0748 |
| HP JetDirect EX Plus Print Server | 1 | Hewlett Packard | inacom |  |  | J2591A |  | 0685 |
| 151FS color monitor | 1 | Compaq |  | 444 | S621BA11AC247 | 147250-601 | 0015664 | 0685 |
| HP Laserjet 5MP 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 5MP | USHB027373 | C3155A | 0015665 | 0685 |

Table 21:  VA Second CVISN Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NT Workstation |  | 1 | Microsoft | MicroAge | MCS-K-77422 | 3.51 |  |  | 0692 |
| NT Workstation | 1 |  | Microsoft |  |  | 4.0 |  |  | 1399 |
| Microsoft Office for NT | 1 |  | Microsoft | MicroAge | MCS-K-72722 | 7.0 |  |  | 0692 |
| Netscape Navigator |  | 1 |  | Software in a Week | I482557 | 2.0 |  |  | 0696 |
| Compaq Support Software CD-ROM |  | 1 | Compaq | inacom | 272505-001 |  |  |  | 0685 |
| RSIS SATS | 1 |  | FHWA | RS Information Systems |  | VA0.1 |  |  |  |

## Virginia Third CVISN Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 22:  VA Third CVISN Client Hardware Configuration (System Number 1641)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Compaq |  | DeskPro 4000 5133 MT 1.62G/32M | S6628BBK2P415 | 247310-002 | 0015667 | 0685 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 133 MHz microprocessor |  |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |  |
| 32MB RAM |  |  |  |  |  |  |  |  |
| 3.5” 1.44MB Floppy drive |  |  |  |  |  |  |  |  |
| 2MB EDO Graphics Memory |  |  |  |  |  |  |  |  |
| 1.5 GB Hard Drive |  |  |  |  |  |  |  |  |
| keyboard |  | Compaq |  | RT101 |  |  |  |  |
| mouse |  | Compaq |  | M-S34-6MD |  |  |  |  |
| internal options: |  |  |  |  |  |  |  |  |
| 8x IDE CD-ROM drive | 1 | Compaq | inacom | CRD-254V |  | 185262-001 |  | 0685 |
| 2/8GB DAT drive | 1 | Compaq | inacom |  |  | 142019-001 |  | 0685 |
| 28.8 Internal Data/fax modem | 1 | Compaq | inacom |  |  | 259213-001 |  | 0685 |
| Plug.Play SCSI Controller | 1 | Compaq | inacom |  |  | 1877749-001 |  | 0685 |
| Plug/Play Token Ring Network adaptor | 1 | Madge | inacom |  |  | 22-04 |  | 0685 |
| Token Ring Card | 1 | JetDirect | Ingram | EX Plus3 |  | J2594A |  | 0748 |
| HP JetDirect EX Plus Print Server | 1 | Hewlett Packard | inacom |  |  | J2591A |  | 0685 |
| 151FS color monitor | 1 | Compaq |  | 444 | S621BA11AC262 | 147250-601 | 0015668 | 0685 |
| HP Laserjet 5MP 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 5MP | USHB027108 | C3155A | 0015669 | 0685 |

Table 23:  VA Third CVISN Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NT Workstation |  | 1 | Microsoft | MicroAge | MCS-K-77422 | 3.51 |  |  | 0692 |
| NT Workstation | 1 |  | Microsoft |  |  | 4.0 |  |  | 1399 |
| Microsoft Office for NT | 1 |  | Microsoft | MicroAge | MCS-K-72722 | 7.0 |  |  | 0692 |
| Netscape Navigator |  | 1 |  | Software in a Week | I482557 | 2.0 |  |  | 0696 |
| Compaq Support Software CD-ROM |  | 1 | Compaq | inacom | 272505-001 |  |  |  | 0685 |
| RSIS SATS | 1 |  | FHWA | RS Information Systems |  | VA0.1 |  |  |  |

## Virginia Fourth CVISN Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 24:  VA Fourth CVISN Client Hardware Configuration (System Number 1642)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Compaq |  | DeskPro 4000 5133 MT 1.62G/32M | S6629BBK2P729 | 247310-002 | 0015671 | 0685 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 133 MHz microprocessor |  |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |  |
| 32MB RAM |  |  |  |  |  |  |  |  |
| 3.5” 1.44MB Floppy drive |  |  |  |  |  |  |  |  |
| 2MB EDO Graphics Memory |  |  |  |  |  |  |  |  |
| 1.5 GB Hard Drive |  |  |  |  |  |  |  |  |
| keyboard |  | Compaq |  | RT101 |  |  |  |  |
| mouse |  | Compaq |  | M-S34-6MD |  |  |  |  |
| internal options: |  |  |  |  |  |  |  |  |
| 8x IDE CD-ROM drive | 1 | Compaq | inacom | CRD-254V |  | 185262-001 |  | 0685 |
| 2/8GB DAT drive | 1 | Compaq | inacom |  |  | 142019-001 |  | 0685 |
| 28.8 Internal Data/fax modem | 1 | Compaq | inacom |  |  | 259213-001 |  | 0685 |
| Plug.Play SCSI Controller | 1 | Compaq | inacom |  |  | 1877749-001 |  | 0685 |
| Plug/Play Token Ring Network adaptor | 1 | Madge | inacom |  |  | 22-04 |  | 0685 |
| Token Ring Card | 1 | JetDirect | Ingram | EX Plus3 |  | J2594A |  | 0748 |
| HP JetDirect EX Plus Print Server | 1 | Hewlett Packard | inacom |  | SG63010136 | J2591A | 0015670 | 0685 |
| 151FS color monitor | 1 | Compaq |  | 444 | S621BA11AC261 | 147250-601 | 0015672 | 0685 |
| HP Laserjet 5MP 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 5MP | USHB027094 | C3155A | 0015673 | 0685 |

Table 25:  VA Fourth CVISN Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NT Workstation |  | 1 | Microsoft | MicroAge | MCS-K-77422 | 3.51 |  |  | 0692 |
| NT Workstation | 1 |  | Microsoft |  |  | 4 |  |  | 1399 |
| Microsoft Office for NT | 1 |  | Microsoft | MicroAge | MCS-K-72722 | 7 |  |  | 0692 |
| Netscape Navigator |  | 1 |  | Software in a Week | I482557 | 2 |  |  | 0696 |
| Compaq Support Software CD-ROM |  | 1 | Compaq | inacom | 272505-001 |  |  |  | 0685 |
| RSIS SATS | 1 |  | FHWA | RS Information Systems |  | VA0.1 |  |  |  |

## Virginia First CVISN CATS Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 26:  VA First CVISN CATS Client Hardware Configuration (System Number 1643)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Micron |  |  | 6478680001 |  | 0015675 | 0690 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 166 MHz microprocessor |  |  |  |  |  |  |  |  |
| 512 KB Pipeline cache |  |  |  |  |  |  |  |  |
| 16 MB RAM 92-2m x 32 SIMMS) |  |  |  |  |  |  |  |  |
| 1.0GB EIDE Hard Drive |  |  |  |  |  |  |  |  |
| 1.44 MB 3.5” Floppy Drive |  |  |  |  |  |  |  |  |
| 8x EIDE CD-ROM drive |  |  |  |  |  |  |  |  |
| 104 key enhanced PS2 keyboard |  |  |  |  |  |  |  |  |
| MS Windows95 |  |  |  |  |  |  |  |  |
| SCM SoundBlaster16 w/007 |  |  |  |  |  |  |  |  |
| Microsoft mouse |  |  |  |  |  |  |  |  |
| First year on-site warranty |  |  |  |  |  |  |  |  |
| 28.2 Modem kit for Win95 |  |  |  |  |  |  |  |  |
| 15” color monitor |  |  |  |  | 621007R101189J |  | 0015676 |  |
| HP Laserjet 5MP 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 5MP | USHB027023 | C3155A | 0015677 | 0685 |

Table 27:  VA First CVISN CATS Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows95 | 1 |  | Microsoft | Micron |  |  |  |  | 0690 |
| Mercator run-time engine | 1 |  | TSI | TSI |  | 1.3D |  |  | 0690 |
| RSIS CATS | 1 |  | FHWA | RS Information Systems |  | VA0.1 |  |  |  |

## Virginia Second CVISN CATS Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 28:  VA Second CVISN CATS Client Hardware Configuration (System Number 1645)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Micron |  |  | 6478680002 |  | 0015675 | 0690 |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 166 MHz microprocessor |  |  |  |  |  |  |  |  |
| 512 KB Pipeline cache |  |  |  |  |  |  |  |  |
| 16 MB RAM 92-2m x 32 SIMMS) |  |  |  |  |  |  |  |  |
| 1.0GB EIDE Hard Drive |  |  |  |  |  |  |  |  |
| 1.44 MB 3.5” Floppy Drive |  |  |  |  |  |  |  |  |
| 8x EIDE CD-ROM drive |  |  |  |  |  |  |  |  |
| 104 key enhanced PS2 keyboard |  |  |  |  |  |  |  |  |
| MS Windows95 |  |  |  |  |  |  |  |  |
| SCM SoundBlaster16 w/007 |  |  |  |  |  |  |  |  |
| Microsoft mouse |  |  |  |  |  |  |  |  |
| First year on-site warranty |  |  |  |  |  |  |  |  |
| 28.2 Modem kit for Win95 |  |  |  |  |  |  |  |  |
| 15” color monitor |  |  |  |  | 621007R101189 |  | 0016750 |  |
| HP Laserjet 5MP 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 5MP | USHB027101 | C3155A | 0016748 | 0685 |

Table 29:  VA Second CVISN CATS Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows95 | 1 |  | Microsoft | Micron |  |  |  |  | 0690 |
| Mercator run-time engine | 1 |  | TSI | TSI |  | 1.3D |  |  | 0690 |
| RSIS CATS | 1 |  | FHWA | RS Information Systems |  | VA0.1 |  |  |  |

## Virginia CVISN Pilot Computer Client Configuration

MACHINE NAME:				TBD

HARDWARE LOCATION:		Department of Motor Vehicles

Commonwealth of Virginia

2300 West Broad Street

Richmond, Virginia 23269

Network Support Center - Computer Room

(Floor 2, Room 261)

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				172.16.38.TBD

IP DOMAIN NAME:			DMV.STATE.VA.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		TBD

PRIMARY POINT OF CONTACT:	Dave Hajduk

Phone:	(804) 367-1863

Fax:	(804) 367-1123

E-Mail:	dhajduk@erols.com

Table 30:  VA CVISN Pilot Computer Client Hardware Configuration (System Number 1644)

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Personal computer | 1 | Micron |  |  | 6986020001 |  | 0015678 |  |
| standard features: |  |  |  |  |  |  |  |  |
| Intel Pentium 166 MHz microprocessor |  |  |  |  |  |  |  |  |
| 512 KB Pipeline cache |  |  |  |  |  |  |  |  |
| 16 MB RAM 92-2m x 32 SIMMS) |  |  |  |  |  |  |  |  |
| 1.0GB EIDE Hard Drive |  |  |  |  |  |  |  |  |
| 1.44 MB 3.5” Floppy Drive |  |  |  |  |  |  |  |  |
| 8x EIDE CD-ROM drive |  |  |  |  |  |  |  |  |
| 104 key enhanced PS2 keyboard |  |  |  |  |  |  |  |  |
| MS Windows95 |  |  |  |  |  |  |  |  |
| SCM SoundBlaster16 w/007 |  |  |  |  |  |  |  |  |
| Microsoft mouse |  |  |  |  |  |  |  |  |
| First year on-site warranty |  |  |  |  |  |  |  |  |
| 28.2 Modem kit for Win95 |  |  |  |  |  |  |  |  |
| 15” color monitor |  |  |  |  | 62700CR201676A |  | 0015679 |  |
| HP Laserjet 6P 600dpi 6 ppm | 1 | Hewlett Packard | inacom | 6P | USBB04189 | C3155A | 0015680 |  |

Table 31:  VA CVISN Pilot Computer Client Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows WorkGroup 3.11 | 1 |  | Microsoft | Micron |  | 3.11 |  |  | 0690 |
| MS Office Professional | 1 |  | Microsoft |  |  |  |  |  |  |

APPENDIX C: Maryland Hardware and Software Configuration Items

# APPENDIX C: Maryland CVISN Equipment

## Maryland Primary CVISN Server Configuration

MACHINE NAME:				MVACVISN

PRIMARY OR SECONDARY:		Primary Server

HARDWARE LOCATION:		Office of Information Resources, Room 204

Motor Vehicle Administration

One Orchard Road

Glenn Burnie, Maryland 21060

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				32.77.222.114

255.255.255.240	IP Mask

32.77.222.112	IP Gateway

IP DOMAIN NAME:			MDOT.STATE.MD.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		(410) 424-3150

PRIMARY POINT OF CONTACT:	Kim Meiklejohn

Phone:	(410) 768-7560

Fax:	(410) 761-1545

E-Mail:	dmkam@mdot.state.md.us

Table 32:  MD Primary CVISN Server Hardware Configuration

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number State of Maryland |
| --- | --- | --- | --- | --- | --- | --- | --- |
| personal computer | 1 | Compaq |  | ProLiant 5000 6/200 Model 1 | D622HVN10522 | 221067-002 | 28293 |
| standard features: |  |  |  |  |  |  |  |
| Intel Pentium Pro 200 MHz microprocessor |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |
| 320 MB RAM |  |  |  |  |  |  |  |
| 8 total I/O expansion slots (7 available) |  |  |  |  |  |  |  |
| {7 PCI (6 available), 3 EISA, 2 shared PCI/EISA} |  |  |  |  |  |  |  |
| Netelligent 10/100 TX PCI UTP network interface controller |  |  |  |  |  |  |  |
| integrated 32-bit fast-wide SCSI-2 storage controller |  |  |  |  |  |  |  |
| integrated 1024x768, 16-color non-interlaced video system |  |  |  |  |  |  |  |
| 1.44Mb Floppy disk drive (internal) |  | Compaq |  |  |  | 144207-201 |  |
| internal quad-speed CD-ROM drive |  | Compaq |  | CRD-254V |  |  |  |
| keyboard |  | Compaq |  | RT101 | 1GD39DG06586 | 120375-001B |  |
| mouse |  | Compaq |  | M-S34-6MD | 1D75BDEF08JK | 141189-201 |  |
| internal options: |  |  |  |  |  |  |  |
| Pentium Pro 200/256K Kit | 1 | Compaq |  |  |  | 228411-001 |  |
| 4.3 GB Drive | 4 | Compaq |  | Fast-Wide SCSI-2 |  | 199598-001 |  |
| SMART-2 array controller/P3 | 1 | Compaq |  |  |  | 194753-001 |  |
| 2/8 GB DAT tape drive (4mm) | 1 | ARCHIVE |  | Python 27871-XXX |  | 140219-001 |  |
| Ingram Digi Acceleport 8E ISA DB25 | 1 | Digi | inacom |  |  | I303494 |  |
| Netelligent 10/100 TX PCI UTP network interface controller | 1 | Compaq |  | 10/100BASE-TX 3C905-TX |  | 169845-001 |  |
| Ethernet network interface card EtherLink XL | 1 | 3COM |  | PCI Combo (BNC, RJ-45, and AUI) | M6MP133A372 | 3C900-COMBO |  |
| 151FS color monitor | 1 | Compaq |  | 444 | 621BA11KC204 | 147265-601 |  |
| Uninterruptable Power Supply | 1 | APC |  | Back-UPS Pro 650 |  | BP650 |  |
| 28.8 external modem for modem pool (P1) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28311 |
| 28.8 external modem for modem pool (P2) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28312 |
| 28.8 external modem for modem pool (P3) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28313 |
| 28.8 external modem for modem pool (P4) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28314 |
| 28.8 external modem for modem pool (P5) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28315 |
| 28.8 external modem for modem pool (P6) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28316 |

Table 33:  MD Primary CVISN Server Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows NT Server System Software with WEB support 3.51 |  | 1 | Compaq |  | 236-075V351 | 3.51 |  |  |  |
| Windows NT Server 4.0 | 1 |  | Microsoft |  | 227-00126 | 4.0 |  |  |  |
| Oracle 7 Workgroup Server - 5 Concurrent User Licenses | 1 |  | Oracle |  | A47900-5 | Release 7.3 7.3.3.0.0.0 |  |  |  |
| Oracle Workgroup Support |  | 1 | Oracle |  |  |  |  |  |  |
| Oracle Support Notes |  | 1 | Oracle |  |  | 2.0.0.0 - Apr 97 |  |  |  |
| Oracle Programmer 2000 |  | 1 | Oracle |  | A48466-1 | 7.3.3 |  |  |  |
| Oracle Programmer 2000 Support |  | 1 | Oracle |  |  |  |  |  |  |
| Oracle Developer 2000 |  | 1 | Oracle |  | A53488-01 | 1.4W |  |  |  |
| Oracle Developer 2000 Support |  | 1 | Oracle |  |  |  |  |  |  |
| MS Visual C++ Professional Subscription |  | 1 | Microsoft |  | 048-05V400 |  |  |  |  |
| Microsoft Office for NT |  | 1 | Microsoft |  |  |  |  |  |  |
| Hot Metal Pro - Web Authoring Tool |  | 1 | SoftQuad |  | 6 11278 11105 5 |  |  |  |  |
| Backup Software for NT - Backup Exec NT |  | 1 | Microsoft |  | BENTSE-RU000-611 | 6.11 | 09-4244-0009-096315 |  |  |
| Mail System - NT Mail - SMTP/POP | 1 |  | Microsoft |  |  |  |  |  |  |
| MS Visual Source Safe |  | 1 | Microsoft |  |  | 324-056V400 |  |  |  |
| MS Visual Test |  | 1 | Microsoft |  |  | 163-056V400 |  |  |  |
| Popkin System Architect |  | 1 | Popkin |  |  |  |  |  |  |
| Support for Popkin |  | 1 | Popkin |  |  |  |  |  |  |
| Distinct TCP/IP Extensions for Windows Runtime Extensions 32-bit |  | 1 |  |  | T32-106 | 1.30 | S000000010007836 | 3C-A7-CB |  |
| Paper Free |  | 1 | Paper Free Systems, Inc. |  |  | 2.0 |  |  |  |

## Maryland Secondary CVISN Server Configuration

MACHINE NAME:				MVACVIEW

PRIMARY OR SECONDARY:		Secondary Server

HARWARE LOCATION:			Office of Information Resources, Room 204

Motor Vehicle Administration

One Orchard Road

Glenn Burnie, Maryland 21060

SOFTWARE LOCATION:			Same as Hardware

IP ADDRESS(ES):				32.77.222.115

255.255.255.240	IP Mask

32.77.222.112	IP Gateway

IP DOMAIN NAME:			MDOT.STATE.MD.US

NT DOMAIN NAME:			CVISN

MODEM PHONE NUMBER(S):		(410) 424-3149

PRIMARY POINT OF CONTACT:	Kim Meiklejohn

Phone:	(410) 768-7560

Fax:	(410) 761-1545

E-Mail:	dmkam@mdot.state.md.us

Table 34:  MD Secondary CVISN Server Hardware Configuration

| Item Description | Qty | Manufacturer | Vendor | Model Number | Serial Number | Part Number | Property Number State of Maryland |
| --- | --- | --- | --- | --- | --- | --- | --- |
| personal computer | 1 | Compaq |  | ProLiant 5000 6/200 Model 1 | D622HVN10490 | 221067-002 | 28294 |
| standard features: |  |  |  |  |  |  |  |
| Intel Pentium Pro 200 MHz microprocessor |  |  |  |  |  |  |  |
| 256 KB high-speed 4-way set associative cache |  |  |  |  |  |  |  |
| 320 MB RAM |  |  |  |  |  |  |  |
| 8 total I/O expansion slots (7 available) |  |  |  |  |  |  |  |
| {7 PCI (6 available), 3 EISA, 2 shared PCI/EISA} |  |  |  |  |  |  |  |
| Netelligent 10/100 TX PCI UTP network interface controller |  |  |  |  |  |  |  |
| integrated 32-bit fast-wide SCSI-2 storage controller |  |  |  |  |  |  |  |
| integrated 1024x768, 16-color non-interlaced video system |  |  |  |  |  |  |  |
| 1.44Mb Floppy disk drive (internal) |  | Compaq |  |  |  | 144207-201 |  |
| internal quad-speed CD-ROM drive |  | Compaq |  | CRD-254V |  |  |  |
| keyboard |  | Compaq |  | RT101 | 1GD39DG06568 | 120375-001B |  |
| mouse |  | Compaq |  | M-S34-6MD | 1D75BDEF2VQH | 141189-201 |  |
| internal options: |  |  |  |  |  |  |  |
| Pentium Pro 200/256K Kit | 1 | Compaq |  |  |  | 228411-001 |  |
| 4.3 GB Drive | 4 | Compaq |  | Fast-Wide SCSI-2 |  | 199598-001 |  |
| SMART-2 array controller/P3 | 1 | Compaq |  |  |  | 194753-001 |  |
| 2/8 GB DAT tape drive (4mm) | 1 | ARCHIVE |  | Python 27871-XXX |  | 140219-001 |  |
| PC/8E ports model | 1 | Digi |  |  |  | 700-00738 |  |
| Netelligent 10/100 TX PCI UTP network interface controller | 1 | Compaq |  | 10/100BASE-TX 3C905-TX |  | 169845-001 |  |
| Ethernet network interface card EtherLink XL | 1 | 3COM |  | PCI Combo (BNC, RJ-45, and AUI) | M6MP16406D9 | 3C900-COMBO |  |
| 151FS color monitor | 1 | Compaq |  | 444 | 621BA11AC199 | 147265-601 |  |
| Uninterruptable Power Supply | 1 | APC |  | Back-UPS Pro 650 |  | BP650 |  |
| 28.8 external modem for modem pool (P1) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28305 |
| 28.8 external modem for modem pool (P2) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28306 |
| 28.8 external modem for modem pool (P3) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28307 |
| 28.8 external modem for modem pool (P4) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28308 |
| 28.8 external modem for modem pool (P5) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28309 |
| 28.8 external modem for modem pool (P6) | 1 | US Robotics |  | Courier V.Everything | 20X0B6D6RVGO | 80-001224-02 | 28310 |

Table 35:  MD Secondary CVISN Server Software Configuration

| Item Description | Qty Installed | Qty On-hand | Manufacturer | Vendor | Part Number | Version Number | License or Serial Number | Key Code | P.O. Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Windows NT Server System Software with WEB support 3.51 |  | 1 | Compaq |  | 236-075V351 | 3.51 |  |  |  |
| Windows NT Server 4.0 | 1 |  | Microsoft |  | 227-00126 | 4.0 |  |  |  |
| Oracle 7 Workgroup Server - 5 Concurrent User Licenses | 1 |  | Oracle |  | A47900-5 | Release 7.3 7.3.3.0.0.0 |  |  |  |
| Oracle Workgroup Support |  | 1 | Oracle |  |  |  |  |  |  |
| Oracle Support Notes |  | 1 | Oracle |  |  | 2.0.0.0 - Apr 97 |  |  |  |
| Oracle Programmer 2000 |  | 1 | Oracle |  | A48466-1 | 7.3.3 |  |  |  |
| Oracle Programmer 2000 Update |  | 1 | Oracle |  | A48466-3 | 7.3.3 |  |  |  |
| Oracle Programmer 2000 Support |  | 1 | Oracle |  |  |  |  |  |  |
| Oracle Developer 2000 |  | 1 | Oracle |  | A53488-01 | 1.4W |  |  |  |
| Oracle Developer 2000 Support |  | 1 | Oracle |  |  |  |  |  |  |
| MS Visual C++ Professional Subscription |  | 1 | Microsoft |  | 048-05V400 |  |  |  |  |
| Microsoft Office for NT |  | 1 | Microsoft |  |  |  |  |  |  |
| Hot Metal Pro - Web Authoring Tool |  | 1 | SoftQuad |  | 6 11278 11105 5 |  |  |  |  |
| Backup Software for NT - Backup Exec NT |  | 1 | Microsoft |  | BENTSE-RU000-611 | 6.11 | 01-4247-0003-096133 |  |  |
| Mail System - NT Mail - SMTP/POP | 1 |  | Microsoft |  |  |  |  |  |  |
| MS Visual Source Safe |  | 1 | Microsoft |  |  | 324-056V400 |  |  |  |
| MS Visual Test |  | 1 | Microsoft |  |  | 163-056V400 |  |  |  |
| Popkin System Architect |  | 1 | Popkin |  |  |  |  |  |  |
| Support for Popkin |  | 1 | Popkin |  |  |  |  |  |  |
| Distinct TCP/IP Extensions for Windows Runtime Extensions 32-bit |  | 1 |  |  | T32-106 | 1.30 | S000000010007837 | 4C-67-1S |  |
| Paper Free |  | 1 | Paper Free Systems, Inc. |  |  | 2.0 |  |  |  |

APPENDIX D: Commercial Vehicle Information Exchange Window (CVIEW) Software Configuration Items

# APPENDIX D: Applied Physics Laboratory System Files and Directories

## CVIEW System Files and Directories

The APL CVIEW system files and directories are listed in Table 36:  APL CVIEW System Files and Directories.  All files are shown.

Table 36:  APL CVIEW System Files and Directories

| Directory | File | Date | Size | Description |
| --- | --- | --- | --- | --- |
| C:\Cview\Bin | DUNZIP32.DLL | 07/29/97 02:51p | 100,352 |  |
| C:\Cview\Bin | DZIP32.DLL | 07/29/97 02:51p | 123,392 |  |
| C:\Cview\Bin | IMH_CMDLN.exe | 07/29/97 02:51p | 580,608 |  |
| C:\Cview\Bin | IMH_SERV.exe | 07/29/97 02:51p | 582,144 |  |
| C:\Cview\Bin | IOT32.dll | 07/29/97 02:51p | 308,736 |  |
| C:\Cview\Bin | MBX.dll | 07/29/97 02:51p | 157,184 |  |
| C:\Cview\Bin | SendList.exe | 07/29/97 02:51p | 240,640 |  |
| C:\Cview\Bin | Send_Concurrent.exe | 07/29/97 02:51p | 160,256 |  |
| C:\Cview\Bin | ServiceDelete.exe | 07/29/97 02:51p | 71,680 |  |
| C:\Cview\Bin | ServiceInstall.exe | 07/29/97 02:51p | 71,680 |  |
| C:\Cview\Bin | winmbx.ini | 09/05/97 04:03p | 545 |  |
| C:\Cview\Bin | wrm32c.dll | 07/29/97 02:51p | 290,816 |  |
| C:\Cview\Edi\Inbound | 285_VIN.MAP | 07/29/97 05:43p | 492,189 |  |
| C:\Cview\Edi\Inbound | 824_IN.MAP | 07/29/97 05:43p | 53,022 |  |
| C:\Cview\Edi\Inbound | DE_1065.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_1065.XRF | 07/29/97 05:43p | 439 |  |
| C:\Cview\Edi\Inbound | DE_1073.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_1073.XRF | 07/29/97 05:43p | 439 |  |
| C:\Cview\Edi\Inbound | DE_1160.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_1160.XRF | 07/29/97 05:43p | 1,007 |  |
| C:\Cview\Edi\Inbound | DE_1250.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_1250.XRF | 07/29/97 05:43p | 376 |  |
| C:\Cview\Edi\Inbound | DE_1270.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_1270.XRF | 07/29/97 05:43p | 2,326 |  |
| C:\Cview\Edi\Inbound | DE_128.NDX | 07/29/97 05:43p | 19,968 |  |
| C:\Cview\Edi\Inbound | DE_128.XRF | 07/29/97 05:43p | 81,376 |  |
| C:\Cview\Edi\Inbound | DE_128S.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_128S.XRF | 07/29/97 05:43p | 1,426 |  |
| C:\Cview\Edi\Inbound | DE_26.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_26.XRF | 07/29/97 05:43p | 751 |  |
| C:\Cview\Edi\Inbound | DE_355.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_355.XRF | 07/29/97 05:43p | 372 |  |
| C:\Cview\Edi\Inbound | DE_374.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_374.XRF | 07/29/97 05:43p | 1,501 |  |
| C:\Cview\Edi\Inbound | DE_559.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_559.XRF | 07/29/97 05:43p | 299 |  |
| C:\Cview\Edi\Inbound | DE_623.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_623.XRF | 07/29/97 05:43p | 299 |  |
| C:\Cview\Edi\Inbound | DE_673.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_673.XRF | 07/29/97 05:43p | 518 |  |
| C:\Cview\Edi\Inbound | DE_98.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | DE_98.XRF | 07/29/97 05:43p | 1,394 |  |
| C:\Cview\Edi\Inbound | T00.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T00.XRF | 07/29/97 05:43p | 751 |  |
| C:\Cview\Edi\Inbound | T01.NDX | 07/29/97 05:43p | 2,048 |  |
| C:\Cview\Edi\Inbound | T01.XRF | 07/29/97 05:43p | 2,776 |  |
| C:\Cview\Edi\Inbound | T03.NDX | 07/29/97 05:43p | 2,048 |  |
| C:\Cview\Edi\Inbound | T03.XRF | 07/29/97 05:43p | 2,776 |  |
| C:\Cview\Edi\Inbound | T04.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T04.XRF | 07/29/97 05:43p | 901 |  |
| C:\Cview\Edi\Inbound | T05A.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T05A.XRF | 07/29/97 05:43p | 601 |  |
| C:\Cview\Edi\Inbound | T06.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T06.XRF | 07/29/97 05:43p | 826 |  |
| C:\Cview\Edi\Inbound | T07.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T07.XRF | 07/29/97 05:43p | 1,612 |  |
| C:\Cview\Edi\Inbound | T08.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T08.XRF | 07/29/97 05:43p | 1,576 |  |
| C:\Cview\Edi\Inbound | T15.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T15.XRF | 07/29/97 05:43p | 976 |  |
| C:\Cview\Edi\Inbound | T20.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T20.XRF | 07/29/97 05:43p | 372 |  |
| C:\Cview\Edi\Inbound | T21.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T21.XRF | 07/29/97 05:43p | 601 |  |
| C:\Cview\Edi\Inbound | T24.NDX | 07/29/97 05:43p | 2,560 |  |
| C:\Cview\Edi\Inbound | T24.XRF | 07/29/97 05:43p | 6,901 |  |
| C:\Cview\Edi\Inbound | T25.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Inbound | T25.XRF | 07/29/97 05:43p | 301 |  |
| C:\Cview\Edi\Outbound | 285_VOUT.MAP | 07/29/97 05:43p | 363,236 |  |
| C:\Cview\Edi\Outbound | 285_VOUT.MAP | 07/29/97 05:43p | 66,142 |  |
| C:\Cview\Edi\Outbound | COMM_NUM.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | COMM_NUM.XRF | 07/29/97 05:43p | 445 |  |
| C:\Cview\Edi\Outbound | CONTACT.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | CONTACT.XRF | 07/29/97 05:43p | 299 |  |
| C:\Cview\Edi\Outbound | COUNTRY.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | COUNTRY.XRF | 07/29/97 05:43p | 445 |  |
| C:\Cview\Edi\Outbound | DATACAT.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | DATACAT.XRF | 07/29/97 05:43p | 1,351 |  |
| C:\Cview\Edi\Outbound | DATATABS.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | DATATABS.XRF | 07/29/97 05:43p | 2,401 |  |
| C:\Cview\Edi\Outbound | DE_1065.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | DE_1065.XRF | 07/29/97 05:43p | 439 |  |
| C:\Cview\Edi\Outbound | DT_FORM.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | DT_FORM.XRF | 07/29/97 05:43p | 301 |  |
| C:\Cview\Edi\Outbound | DT_QUAL.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | DT_QUAL.XRF | 07/29/97 05:43p | 901 |  |
| C:\Cview\Edi\Outbound | ENTITYID.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | ENTITYID.XRF | 07/29/97 05:43p | 372 |  |
| C:\Cview\Edi\Outbound | JUR_CODE.NDX | 07/29/97 05:43p | 2,560 |  |
| C:\Cview\Edi\Outbound | JUR_CODE.XRF | 07/29/97 05:43p | 5,077 |  |
| C:\Cview\Edi\Outbound | MCENTITY.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | MCENTITY.XRF | 07/29/97 05:43p | 514 |  |
| C:\Cview\Edi\Outbound | N9_ID.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | N9_ID.XRF | 07/29/97 05:43p | 976 |  |
| C:\Cview\Edi\Outbound | NM1_ENT.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | NM1_ENT.XRF | 07/29/97 05:43p | 883 |  |
| C:\Cview\Edi\Outbound | NM1_ID.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | NM1_ID.XRF | 07/29/97 05:43p | 299 |  |
| C:\Cview\Edi\Outbound | NTE_CODE.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | NTE_CODE.XRF | 07/29/97 05:43p | 601 |  |
| C:\Cview\Edi\Outbound | PURPOSE.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | PURPOSE.XRF | 07/29/97 05:43p | 445 |  |
| C:\Cview\Edi\Outbound | QUANTITY.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | QUANTITY.XRF | 07/29/97 05:43p | 372 |  |
| C:\Cview\Edi\Outbound | REF_ID.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | REF_ID.XRF | 07/29/97 05:43p | 676 |  |
| C:\Cview\Edi\Outbound | TIMEZONE.NDX | 07/29/97 05:43p | 2,048 |  |
| C:\Cview\Edi\Outbound | TIMEZONE.XRF | 07/29/97 05:43p | 3,511 |  |
| C:\Cview\Edi\Outbound | VALID_TS.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Outbound | VALID_TS.XRF | 07/29/97 05:43p | 301 |  |
| C:\Cview\Edi\TPartner | CUSTGSID.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Tpartner | CUSTNO.NDX | 07/29/97 05:43p | 1,024 |  |
| C:\Cview\Edi\Tpartner | CUSTOMER.DBF | 09/06/97 04:04p | 2,352 |  |
| C:\Cview\Edi\Tpartner | TRADSTAT.dbf | 09/06/97 04:04p | 2,418 |  |
| C:\Cview\Edi\Tpartner | TRADSTAT.NDX | 07/29/97 05:43p | 2,048 |  |
| C:\Cview\Edi\Tpartner | WIXSET.DAT | 07/29/97 05:43p | 145 |  |
| C:\Cview\Opcon | DeIsL1.isu | 08/01/97 01:20p | 11,269 |  |
| C:\Cview\Opcon | DLLACCT.dll | 07/30/97 11:45a | 126,464 |  |
| C:\Cview\Opcon | ELWrapperDLL.dll | 07/30/97 11:45a | 49,152 |  |
| C:\Cview\Opcon | Events.db | 07/30/97 11:45a | 4,096 |  |
| C:\Cview\Opcon | OPCON.exe | 07/31/97 11:47a | 1,233,408 |  |
| C:\Cview\Opcon | OPCON.GDB | 08/01/97 03:11p | 709,632 |  |
| C:\Cview\Opcon | opcon.ico | 07/30/97 11:45a | 766 |  |
| C:\Cview\Opcon | setup.bat | 08/01/97 01:26p | 872 |  |
| C:\Cview\Opcon | slp.dll | 07/30/97 11:46a | 59,904 |  |
| C:\Cview\Opcon | sqlnet.log | 08/01/97 01:39p | 546 |  |
| C:\Cview\Opcon | Tool_Menu_Revised.db | 07/30/97 11:45a | 2,048 |  |
| C:\Cview\Opcon | _DEISREG.ISR | 08/01/97 01:19p | 654 |  |
| C:\Cview\Opcon | _ISREG32.DLL | 04/23/97 02:16a | 40,960 |  |
| C:\Cview\Opcon\Setup | account_manager.sql | 08/01/97 02:40p | 7,489 |  |
| C:\Cview\Opcon\Setup | addSAFERGroup.exe | 07/30/97 11:45a | 89,088 |  |
| C:\Cview\Opcon\Setup | deleteSAFERGroup.exe | 07/30/97 11:45a | 89,088 |  |
| C:\Cview\Opcon\Setup | OPCON.sql | 07/30/97 11:45a | 720 |  |
| C:\Cview\Opcon\Setup | QUERY_TEMPLATE.sql | 07/30/97 11:45a | 643 |  |
| C:\Cview\Opcon\Setup | setup.log | 07/30/97 11:45a | 4,181 |  |
| C:\Cview\Opcon\Setup | SLP_REF.SQL | 07/30/97 11:45a | 4,080 |  |
| C:\Cview\Opcon\Setup | sys-test.rtf | 07/30/97 11:45a | 134,817 |  |
| C:\Cview\SQL | create_bank.sql | 07/29/97 05:43p | 587 |  |
| C:\Cview\SQL | create_org_account.sql | 07/29/97 05:43p | 1,561 |  |
| C:\Cview\SQL | create_sendlist_table.sql | 07/29/97 05:43p | 441 |  |
| C:\Cview\SQL | create_subscriber_parms.sql | 07/29/97 05:43p | 478 |  |
| C:\Cview\SQL | create_subscription.sql | 07/29/97 05:43p | 901 |  |
| C:\Cview\SQL | create_subscription_user.sql | 07/29/97 05:43p | 1,186 |  |
| C:\Cview\SQL | create_user_account.sql | 07/29/97 05:43p | 1,678 |  |
| C:\Cview\SQL | CS01_CT.SQL | 07/29/97 05:43p | 10,524 |  |
| C:\Cview\SQL | CS02_CT.SQL | 07/29/97 05:43p | 275 |  |
| C:\Cview\SQL | CS03_CT.SQL | 07/29/97 05:43p | 213 |  |
| C:\Cview\SQL | CS04_CT.SQL | 07/29/97 05:43p | 339 |  |
| C:\Cview\SQL | CS05_CT.SQL | 07/29/97 05:43p | 224 |  |
| C:\Cview\SQL | CSIDX2_CI.SQL | 07/29/97 05:43p | 349 |  |
| C:\Cview\SQL | CSIDX_CI.SQL | 07/29/97 05:43p | 664 |  |
| C:\Cview\SQL | SAFER_ENV.SQL | 07/29/97 05:43p | 3,119 |  |
| C:\Cview\SQL | SAFER_ENV_Upgrade.SQL | 07/29/97 05:43p | 1,074 |  |
|  | status_trigger.sql | 07/29/97 05:43p | 1,518 |  |
| C:\Cview\TestScripts | add_edwards.sql | 07/29/97 05:43p | 114 |  |
| C:\Cview\TestScripts | add_parms.sql | 07/29/97 05:43p | 784 |  |
| C:\Cview\TestScripts | add_rocparms.sql | 07/29/97 05:43p | 572 |  |
| C:\Cview\TestScripts | add_rocparms.sql | 07/29/97 05:43p | 114 |  |
| C:\Cview\TestScripts | cleanup.sql | 07/29/97 05:43p | 1,680 |  |
| C:\Cview\TestScripts | create_subscriber.sql | 07/29/97 05:43p | 1,250 |  |
| C:\Cview\TestScripts | create_subscription_user.sql | 07/29/97 05:43p | 334 |  |
| C:\Cview\TestScripts | del_records.sql | 07/29/97 05:43p | 152 |  |
| C:\Cview\TestScripts | edi_req0.txt | 07/29/97 05:43p | 402 |  |
| C:\Cview\TestScripts | mdvatest.txt | 09/05/97 10:22a | 106 |  |
| C:\Cview\TestScripts | parm_list.sql | 07/29/97 05:43p | 1,007 |  |
| C:\Cview\TestScripts | sub_user_parms.sql | 07/29/97 05:43p | 121 |  |
| C:\Cview\TestScripts | vatest.sql | 07/29/97 05:43p | 1,486 |  |
| C:\Cview\TestScripts | va_dots.sql | 07/29/97 05:43p | 228 |  |
| C:\Cview\Winnt-Proxy | win.ini | 07/29/97 05:43p | 798 |  |

## OPCON (Operator’s Console) System Files and Directories

The APL CVIEW system files and directories are listed in Table 37:  APL OPCON System Files and Directories.  All files are shown.

### Hardware Requirements

- Standard hardware package recommended for CVIEW

- 10 MB of available hard disk space for OPCON

- Super VGA, 256-Color monitor with screen resolution of at least 640 x 480

- Microsoft Mouse or compatible pointing device

- Standard 101-key keyboard

- 3.5” 1.44 MB disk drive

- Operating Network Interface (if OPCON is not being installed on the server which has the CVIEW database installed on it.

### Software Requirements

- Microsoft Windows NT version 4.0 or later

- Oracle Workgroup 7.3

- Oracle SQL*Net Client

- Oracle SQL Plus 3.3

### Network Requirements

- Windows NT must be installed to support TCP/IP service.

Table 37:  APL OPCON System Files and Directories

| Directory | File | Description | Version |
| --- | --- | --- | --- |
| %system% | ADM_MESSAGE.DLL | Providing Event Logging message file (must be in the System directory) | 1.1.2.1 |
| %cview_root%\opcon | CORENT23.DLL | Providing SAFER Account Manager Functionality | 1.1.2.1 |
| %cview_root%\opcon | DLLACCT.DLL | Providing Event Logging ability | 1.1.2.1 |
| %cview_root%\opcon | ELWrapper.DLL | For local processing of Subscription events | 1.1.2.1 |
| %cview_root%\opcon | EVENTS.DB | For local processing of Subscription events | 1.1.2.1 |
| %system% | MSVCRT10.DLL | Microsoft Visual C Runtime Library 1.0 | 1.1.2.1 |
| %cview_root%\opcon | OPCON.EXE | OPCON application file | 1.1.2.1 |
| %cview_root%\opcon | OPCON.GDB | Holding local CVIEW database | 1.1.2.1 |
| %system% | ORANT71.DLL | Vendor specific DLL for Oracle | 1.1.2.1 |
| %system% | RASSAPI.DLL | Providing Remote Access Service Functionality | 1.1.2.1 |
| %cview_root%\opcon\setup | SETUP.BAT | OPCON Environment Loader Batch File | 1.1.2.1 |
| %cview_root%\opcon | SLP.DLL | Providing CVIEW Subcription Functionality | 1.1.2.1 |
| %cview_root%\opcon | SUBSCRIBED_USER.DB | Providing temporary storage for processing subscribed users | 1.1.2.1 |
| %cview_root%\opcon | Tool_Menu_Revised.DB | Providing lists of tools OPCON can activate | 1.1.2.1 |
| %cview_root%\opcon | SETUP.BAT |  | 1.1.2.1 |
| %cview_root%\opcon\setup | ACCOUNT_MANAGER.SQL | An SQL script for ACCOUNT MANAGER related tables | 1.1.2.1 |
| %cview_root%\opcon\setup | BANK.SQL | Providing an SQL script to create the BANK table and related indices in the database | 1.1.2.1 |
| %cview_root%\opcon\setup | OPCON.SQL | An SQL script that launches SAL scripts for subscription-related tables and ACCOUNT_MANAGER.SQL | 1.1.2.1 |
| %cview_root%\opcon\setup | ORG_ACCOUNT.SQL | Providing an SQL script to create the ORG_ACCOUNT table and related indices in the database | 1.1.2.1 |
| %cview_root%\opcon\setup | SLP_REF.SQL | Providing an SQL script for the SLP reference table | 1.1.2.1 |
| %cview_root%\opcon\setup | statusTrigger.SQL | Providing an SQL script to create a trigger to maintain organization’s and user’s status updates | 1.1.2.1 |
| %cview_root%\opcon\setup | USER_ACCOUNT.SQL | Providing an SQL script to create the USER_ACCOUNT table and related indices in the database | 1.1.2.1 |
| %cview_root%\opcon\borland | BDE | Providing a database engine for OPCON’s operations | 1.1.2.1 |

This Page Intentionally Blank

APPENDIX E: RS Information Systems Software Configuration Items Electronic Credentialing Subsystem (CATS, SATS, CI)

# APPENDIX E: RS Information Systems Software Configuration Items Electronic Credentialing Subsystem (CATS, SATS, CI)

To Be Supplied by RS Information Systems

APPENDIX F: IDT Software Configuration Items (CAT, CI)

# APPENDIX F: IDT Software Configuration Items (CAT, CI)

To Be Supplied by IDT

# Text boxes

CVISN Prototype Server and Workstation Configuration Management Document