The International GLONASS Experiment

(IGEX-98): Organization, Preliminary Results and Future Plans

James A. Slater, National Imagery and Mapping Agency, USA

Pascal Willis, Institut Géographique National, France

Gerhard Beutler, Astronomical Institute, University of Berne, Switzerland

Werner Gurtner, Astronomical Institute, University of Berne, Switzerland

Wlodzimierz Lewandowski, Bureau International des Poids et Mesures, France

Carey Noll, NASA Goddard Space Flight Center, USA

Robert Weber, University of Technology Vienna, Austria

Ruth E. Neilan, Jet Propulsion Laboratory, USA

Guenter Hein, Institute of Geodesy and Navigation, University FAF Munich , Germany

BIOGRAPHY

James A. Slater has been actively involved in developmental work, program management and policy issues related to satellite geodesy, GPS and WGS 84 since 1980 at the (U.S.) National Imagery and Mapping Agency, and co-chairs the ION GLONASS-GPS Interoperability Working Group.

Pascal Willis has worked in the field of geodesy at the Institut Géographique National since 1983. After a Doctoral dissertation on geodetic applications of GPS, he has been doing research work on other satellite systems such as DORIS (for which he is the Coordinator for the International Earth Rotation Service). He chairs the International Association of Geodesy Sub-commission on Microwave Satellite Systems and the IGEX-98 Steering Committee.

Gerhard Beutler is Director of the Center for Orbit Determination in Europe (CODE) at the University of Berne, Switzerland and former Chair of the International GPS Service Governing Board. He has a Ph.D. in astronomy from the University of Berne.

Werner Gurtner received his Ph.D. from the Swiss Federal Institute of Technology working on an astro-geodetic geoid of Switzerland.  He currently is on the staff of the Astronomical Institute, University of Berne where he is the manager of the Zimmerwald Geodynamical Observatory.

Wlodzimierz Lewandowski has a Doctorate in geographical science from the Institut Géographique National.  He is a physicist in the Time Section of the Bureau International des Poids et Mesures in Sèvres, where he helps evaluate and disseminate International Atomic Time (TAI) and Coordinated Universal Time (UTC). He is studying the use of space techniques, especially GPS and GLONASS, for ultra-accurate time transfer, and currently chairs the Timing Subcommittee of the Civil GPS Service Interface Committee.

Carey Noll is the manager of NASA's Crustal Dynamics Data Information System (CDDIS) at Goddard Space Flight Center in Greenbelt, Maryland.  She is the Data Flow Coordinator for IGEX-98.

## Robert Weber is in the Department of Theoretical Geodesy, at the University of Technology, Vienna, Austria.  He has a Ph.D. from the same institution, and is currently using GPS data to study Earth rotation. He is the Analysis Center Coordinator for IGEX-98 and chairs an IAG study group on regional permanent arrays.

Ruth E. Neilan is Director of the IGS Central Bureau at the Jet Propulsion Laboratory in Pasadena, California. She has a M.S. degree in Civil and Environmental Engineering from the University of Wisconsin-Madison and has been involved in the coordination and establishment of the GPS Global Network since 1987.

Guenter Hein is Full Professor and Director of the Institute of Geodesy and Navigation of the University FAF Munich. He has been working with GPS since 1983 and with GLONASS since 1990 in several research projects.

ABSTRACT

When considering future global navigation satellite systems, the interoperability and seamless use of several constellations is an important aspect.  The International GLONASS Experiment (IGEX-98) was organized to address these interoperability issues between GLONASS and GPS.  From October 1998 to April 1999, approximately 60 stations in over 25 countries collected GLONASS tracking data in the first global campaign organized to investigate GLONASS.  The experiment was made possible through the voluntary cooperation of dozens of organizations that tracked the satellites, supplied equipment, archived and distributed data, and produced the results described here.  Observations were made continuously at each station, converted to RINEX format, and transmitted to one of two data centers in France and the United States.  These data have been used by numerous organizations to determine precise GLONASS orbits, examine the relationship between the PZ-90 and WGS 84 terrestrial reference frames, compute station positions and GLONASS-GPS time offsets, perform time transfer, evaluate receiver performance, and develop and test new software. The paper summarizes the preliminary results of the campaign and notes the impacts of the experiment on the ability to use GLONASS for scientific and practical applications.  Due to the success of the campaign, plans are underway for continuing the global data collection and analysis.

### INTRODUCTION

The International GLONASS Experiment (IGEX-98) was conducted between October 19, 1998 and April 19, 1999.  This experiment was the first internationally-coordinated tracking and analysis campaign dedicated to the Russian GLONASS satellites.  During the campaign, GLONASS receivers were operated at 61 sites in 26 countries (or territories).  In addition, the International Laser Ranging Service helped coordinate an unprecedented amount of laser tracking of the GLONASS satellites, each of which is equipped with laser retroreflectors.  Nine of the satellites were chosen for concentrated tracking.  Thirty satellite laser ranging (SLR) observatories in 15 countries participated.

IGEX-98 was co-sponsored by the International Association of Geodesy (Commission VIII, International Coordination of Space Techniques for Geodesy and Geodynamics), the International GPS Service (IGS), the Institute of Navigation (ION), and the International Earth Rotation Service.  A Steering Committee with members from these organizations, chaired by Dr. Pascal Willis of the Institut Géographique National, organized and managed the experiment. [Willis et al., 1998]  By taking advantage of the international community’s extensive experience with GPS campaigns and the infrastructure that already existed within the IGS, the Steering Committee was able to organize the experiment relatively quickly.  Requirements for station monumentation, receivers, documentation, satellite tracking protocols, data formats, data transmission, data archiving, and an IGEX e-mail message system were developed and put in place. [Slater et al., 1998; Willis et al., 1998; Willis et al., 1999]

Receiver manufacturers cooperated by producing enough dual-frequency combined GLONASS and GPS receivers to support the participating organizations.  A number of receivers were lent to Russian organizations to help support Russian participation.  Global data centers at the NASA Goddard Space Flight Center in the U.S. and the Institut Géographique National (IGN) in France archived all of the GLONASS receiver tracking data.

A number of organizations modified their GPS and SLR software to handle GLONASS data.  Precise post-processed orbits were produced at the sub-meter level for all the operational GLONASS satellites from the GLONASS receiver data and, where possible, independently from the SLR data.  A weighted combination of the individual precise orbits was also produced by an Analysis Center Coordinator at the University of Technology, Vienna.

The precise orbits generated during the campaign facilitated other applications including time transfer, datum transformations between the Russian PZ-90 reference system and WGS 84 (or ITRF96), and geodetic positioning.  This paper describes the motivation for the experiment, its operational aspects, and the results that have been produced thus far.  Maintenance of a “permanent” global tracking network, from a subset of the IGEX-98 stations, and continued production of precise GLONASS orbits are discussed as possible follow-on activities by the international community.  All of the results discussed here were reported at the IGEX-98 Workshop held on September 13-14, 1999 in Nashville, Tennessee. [Slater et al., 1999]

MOTIVATION

‘Why GLONASS’ and ‘why now’ are the two questions that come to mind regarding the motivation behind this GLONASS campaign.  The fact that GLONASS existed was the first and most obvious consideration.  There were over a dozen operational satellites in orbit with characteristics very similar to those of GPS.  [GLONASS, 1995; Langley, 1997] This immediately provided a way to experiment with a realization of a Global Navigation Satellite System (GNSS).  Both the navigation and the scientific communities had an interest in exploring the possible benefits of a 36 or more satellite constellation, and therefore had an interest in resolving any interoperability problems that existed.  [Misra and Slater, 1998; Senus and Misra, 1996; Slater and Misra, 1997; Zarraoa et al., 1998]  One immediate application of combined GPS and GLONASS receivers is real-time navigation of space platforms. [Klyushnikov et al., 1999]  Another is atmospheric monitoring and research.

The availability of commercial receiver technology was no longer an impediment.  Several manufacturers were marketing combined GPS-GLONASS receivers for positioning and timing applications, and dual-frequency geodetic-quality receivers could be obtained at a reasonable cost.  Furthermore, data and hardware standards that had been established for GPS applications could be readily adapted for GLONASS.

One of the attractions of GLONASS to the civil (non-military) user is direct access to the P-code.  Unlike GPS, GLONASS signals are unencumbered by Selective Availability and anti-spoofing corruptions.  The GLONASS P-code has a resolution five times better than the GPS C/A-code (the only code directly available to the civil user).  This is particularly useful to the timing community. [Azoubib and Lewandowski, 1998]

Differences between GLONASS’s PZ-90 reference frame and GPS’s WGS 84 reference frame remained a problem.  Attempts had been made to relate PZ-90 to WGS 84 (and the International Terrestrial Reference Frame (ITRF)) on a local and regional basis, but no global solution existed. [Bazlov et al., 1999; Misra et al., 1996; Rossbach et al., 1996]  In addition, GLONASS employed UTC(SU) as its time reference, while GPS used UTC(USNO); therefore, time synchronization was still an issue.

Exploitation of GLONASS for many applications requires a global tracking network and availability of precise orbits for the satellites.  Neither of these had been attempted before.  However, because of the operational capabilities of the IGS, the infrastructure was in place to deploy receivers, and collect, archive and analyze the data. [Beutler et al., 1999]  The benefits of this expanded constellation to the scientific community are essentially more observations per unit time and a higher density of observations.  This means more robustness, independence and redundancy of measurements, and better temporal and spatial resolution.  Because of the similarity between GPS and GLONASS, it was relatively easy to assimilate the GLONASS data into existing GPS processing schemes.  Furthermore, SLR observations of GLONASS satellites can be used for independent quality control and validation of other results.  Note that most applications are considering GLONASS as an augmentation to GPS and not as a stand-alone system. Thus, the number of GLONASS satellites is not a limiting factor in most of this work.

Lastly, GLONASS had an uncertain future.  Many of the satellites are well beyond their design lives and could fail at any time.  Three replacement satellites were successfully launched halfway into the campaign, maintaining a constellation of about 14 satellites for operational use.  Postponing the experiment may have resulted in a reduced constellation to work with.

### OBJECTIVES

The IGEX Steering Committee established a list of objectives for the experiment. [Willis et al., 1999]  The foundation for much of the work that would follow was the establishment of a global tracking network.  GLONASS tracking stations were required to be collocated with GPS stations (with well-defined ITRF96 coordinates), monumented and documented.  The network’s task was the collection of a continuous, globally-distributed data set over a long time period.

In parallel with this, SLR stations around the world were requested to track a subset of the GLONASS satellites to provide an independent data set for orbit evaluation.  These activities then supported the remaining objectives: (a) precise orbit determination, (b) receiver evaluation, (c) software development, (d) geodetic positioning, (e) reference frame comparisons, and (f) time and time transfer applications.  It was also hoped that this work would be a stimulus for other applications and developments.

#### NETWORK OPERATIONS

The global network of GLONASS and SLR stations that supported the IGEX-98 experiment is shown in figure 1.  GLONASS receivers were deployed at 61 sites in 26 countries (or territories).  Several of the sites had more than one GLONASS receiver operating.  Every station was required to have a dual-frequency GPS receiver, in part to ensure that good ITRF coordinates were determined for the station location.  The stations that operated GLONASS receivers during the tracking campaign are listed in table 1.  Receivers from Ashtech, MAN, Javad Positioning Systems and 3S Navigation were the predominant receivers used.  Two older Trimble 4000 SGL single-frequency receivers that had been produced in limited quantities for Russia were operated, and one prototype receiver developed for the European Space Agency by the Institute of Satellite Navigation at the University of Leeds was tested as well.  A total of 48 dual-frequency and 20 single-frequency GLONASS receivers formed the global tracking network. (See table 2.)

In addition, the International Laser Ranging Service (ILRS) helped organize the SLR stations worldwide to track nine GLONASS satellites, three in each of the three orbit planes, during the campaign.  (Only three GLONASS satellites were being observed on a regular basis prior to the campaign.)  The satellites chosen are listed below by slot and plane number (SLR satellite number is in parentheses):

Plane 1:  Slots 3 (68), 4  (70), 6 (69)

Plane 2:  Slots 9 (79), 12 (65), 16 (66)

Plane 3:  Slots 17 (62), 20 (71), 22 (72)

| Table 1. IGEX-98 GLONASS Receiver Stations and Data Holdings |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| October 19,1998 - April 19,1999 |  |  |  |  |  |  |  |
| Country | Station Location/Name | Station ID | Latitude | Longitude |  | Receiver Model | No. Days |
| Antarctica | McMurdo Stn./Crary Science Lab | CRAR | -77°51' | 166°40' |  | Javad Legacy GGD | 43 |
| Argentina | Rio Grande | RIOZ | -53°47' | -67°45' |  | MAN NR-R124 | 141 |
| Australia | Brisbane | SUNM | -27°29' | 153°02' |  | Javad Legacy GGD | 90 |
| Australia | Canberra/ Stromlo | STRR | -35°19' | 149°01' |  | Ashtech Z18 | 123 |
| Australia | Hobart | HOBR | -42°48' | 147°26' |  | Ashtech GG24 | 3 |
| Australia | Lindfield/Lindfield NML2 | LINR | -33°50' | 151°12' |  | 3S Nav R100/30T | 90 |
| Australia | Perth/ Bellevue 157 | BELR | -31°53' | 116°00' |  | Ashtech GG24 | 27 |
| Australia | Yaragadee/ AU053 | YARR | -29°03' | 115°21' |  | Ashtech Z18 | 137 |
| Austria | Graz/Graz-Lustbuehel | GRAB | 47°06' | 15°30' |  | Ashtech Z18 | 115 |
| Austria | Innsbruck | IBK1 | 47°16' | 11°21' |  | Ashtech GG24 | 120 |
| Austria | Mattersburg | MTBG | 47°44' | 16°24' |  | Ashtech GG24 | 137 |
| Belgium | Brussels | BRUG | 50°48' | 4°22' |  | 3S Nav R100/30T | 154 |
| Chile | Santiago | SANG | -33°09' | -70°40' |  | 3S Nav R100/40 | 156 |
| China | Hong Kong | HKPU | 22°18' | 114°11' |  | Ashtech GG24 | 4 |
| France | Brest/Brest-EPHOM | BRSG | 48°24' | -4°30' |  | Martech Mira 24 | 156 |
| France | Brest/Brest-EPHOM | BRST | 48°24' | -4°30' |  | Martech Mira 24 | 156 |
| France | Grasse/ Caussols | GRAC | 43°45' | 6°55' |  | Martech Mira 24 | 119 |
| France | Sèvres/BIPM | BIPD | 48°50' | 2°13' |  | 3S Nav R100/30T | 144 |
| France | Vernon | LRBA | 49°06' | 1°30' |  | Ashtech Z18 | 138 |
| Gabon | N'Koltang | NKLG | 0°13' | 9°24' |  | Ashtech Z18 | 37 |
| Germany | Neubiberg | BLVA | 48°08' | 11°35' |  | 3S Nav R101+R100 | 10 |
| Germany | Neustrelitz/ DLR DFD Neustrelitz | NTZ1 | 53°20' | 13°04' |  | 3S Nav R101 | 183 |
| Germany | Oberpfaffenhofen | DLRA | 48°05' | 11°17' |  | 3S Nav R100/40T | 132 |
| Germany | Koetzting/Wettzell | WTZG | 49°09' | 12°53' |  | 3S Nav R101+R100 | 123 |
| Germany | Koetzting/Wettzell | WTZZ | 49°09' | 12°53' |  | Ashtech Z18 | 68 |
| Greenland | Thule Airbase | THU2 | 76°32' | -68°50' |  | Ashtech Z18 | 112 |
| Iceland | Reykjavik | REYZ | 64°08' | -21°57' |  | Ashtech Z18 | 85 |
| India | New Delhi | NPLI | 28°38' | 77°10' |  | 3S Nav GNSS-300T | 2 |
| Japan | Mitaka/ Mitaka A Site | MTKA | 35°41' | 139°34' |  | Ashtech Z18 | 127 |
| Japan | Tsukuba/ Tsukuba A | TSKA | 36°06' | 140°05' |  | Ashtech Z18 | 136 |
| Kyrgyzstan | Bishkek | BISZ | 42°53' | 74°36' |  | MAN NR-R124 | 147 |
| La Reunion | La Reunion | REUN | -21°12' | 55°34' |  | Ashtech Z18 | 64 |
| Netherlands | Delft | DLFT | 51°59' | 4°23' |  | Ashtech GG24 | 120 |
| Netherlands | Delft | DLFT | 51°59' | 4°23' |  | Javad Legacy GGD | 53 |
| Netherlands | Delft/ VSL-Delft | VSLD | 52°00' | 4°23' |  | 3S Nav R100/40T | 165 |
| Poland | Borowiec | BORG | 52°17' | 17°04' |  | 3S Nav R100/30T | 167 |
| Russia | Ekaterinburg | EKAT | 57°02' | 59°33' |  | Javad Legacy | 8 |
| Russia | Irkutsk | IRKG | 52°13' | 104°19' |  | Trimble 4000SGL | 169 |
| Russia | Irkutsk | IRKZ | 52°13' | 104°19' |  | Ashtech Z18 | 174 |
| Russia | Khabarovsk | KHAB | 48°31' | 135°02' |  | Ashtech Z18 | 150 |
| Russia | Magadan | MAGD | 59°35' | 150°48' |  | Javad Legacy | 54 |
| Russia | Mendeleevo | MDVG | 56°02' | 37°13' |  | Trimble 4000SGL | 118 |
| Russia | Mendeleevo | MDVZ | 56°02' | 37°13' |  | Ashtech Z18 | 181 |
| Russia | Petropavlovsk-Kamchatskiy | PKST | 53°05' | 158°38' |  | Javad Legacy | 28 |
| Russia | Svetloe | SVT3 | 60°32' | 29°47' |  | Javad Legacy | 34 |
| Russia | Yakutsk | YAKT | 62°02' | 129°41' |  | Javad Legacy | 52 |
| Russia | Zvenigorod | ZWEG | 55°42' | 36°46' |  | Ashtech GG24 | 79 |
| South Africa | Pretoria | CSIR | -25°45' | 28°17' |  | 3S Nav R100/30T | 165 |
| South Africa | Sutherland | SUTG | -32°24' | 20°49' |  | MAN NR-R124 | 136 |
| Sweden | Kiruna | KR0G | 67°53' | 21°04' |  | Ashtech Z18 | 170 |
| Sweden | Maartsbo | MR6G | 60°36' | 17°16' |  | Ashtech GG24 | 177 |
| Sweden | Onsala | OS0G | 57°24' | 11°56' |  | Ashtech Z18 | 163 |
| Sweden | Visby | VS0G | 57°39' | 18°22' |  | Ashtech GG24 | 169 |
| Switzerland | Zimmerwald/ZimmerwaldGPS87E | ZIMJ | 46°53' | 7°28' |  | Javad Legacy | 48 |
| Switzerland | Zimmerwald/Zimmerwald GPS97 | ZIMZ | 46°53' | 7°28' |  | Ashtech Z18 | 172 |
| Taiwan | Taiwan | NCKU | 23°00' | 120°13' |  | Ashtech GG24(2) | 117 |
| UK | Herstmonceux | HERP | 50°52' | 0°20' |  | 3S Nav R100/40 | 151 |
| UK | Leeds | LDS1 | 53°49' | -1°33' |  | ESA/ISN GNSS | 181 |
| UK | Leeds | LDS3 | 53°49' | -1°33' |  | Ashtech GG24 | 180 |
| UK | Teddington | NPLC | 51°25' | -0°20' |  | 3S Nav R100/40T | 131 |
| UK | Gr. Yarmouth/Great Yarmouth 2 | GTY2 | 52°35' | 1°44' |  | Ashtech GG24 | 74 |
| USA | Gainesville | GATR | 29°29' | -82°21' |  | Javad Legacy GGD | 120 |
| USA | Greenbelt | GODZ | 39°01' | -76°50' |  | Ashtech Z18 | 170 |
| USA | Irvine | 3SNA | 33°41' | -117°52' |  | 3S Nav R100/40T | 139 |
| USA | Lexington/ MIT/LL South Lab | SL1X | 42°28' | -71°16' |  | Ashtech Z18 | 172 |
| USA | Ft. Davis/McDonald Observatory | MDOA | 30°41' | -104°01' |  | Javad Legacy | 138 |
| USA | Washington, DC | USNX | 38°55' | -77°04' |  | 3S Nav R100/30T | 166 |

Table 2. Numbers and Types of GLONASS

Receivers Deployed

_________________________________________

3S Navigation R100 (various models)	12

3S Navigation R101	  1

3S Navigation R101/R100	  2

3S Navigation GNSS-300T	  1

Ashtech GG24 (including Martech MIRA 24)*	15

Ashtech Z-18	20

ESA/ISN GNSS	  1

Javad Positioning Systems Legacy	11

MAN NR-R124*	  3

Trimble 4000 SGL*	  2

##### TOTAL	68

*Single frequency.

Some of the other GLONASS satellites were also tracked. The 30 SLR stations that participated are shown in table 3.

Operational data centers transmitted data from one or more stations to regional or Global Data Centers.  Operational centers that collected data from multiple stations included Deutsche Forschungsanstalt fuer Luft-und Raumfahrt (DLR), European Space Agency (ESA), GeoForschungsZentrum (GFZ), and National Cheng Kung University (NCKU).  Regional centers were located at the Australian Surveying and Land Information Group (AUSLIG) and Bundesamt fuer Kartographie und Geodaesie (BKG).  The two Global Data Centers were at NASA Goddard Space Flight Center’s Crustal Dynamics Data Information System (CDDIS) and the IGN.  The goal was for data to be transmitted once a day to the Global Data Centers within 48 hours after collection at the

| Table 3. IGEX-98 Satellite Laser Ranging Observatories and Data Holdings |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| October 19, 1998 - April 19, 1999 |  |  |  |  |  |  |  |
|  |  | Station Location/ | Station |  |  | No. of |  |
|  | Country | Name | ID | Latitude | Longitude | Passes |  |
|  | Australia | Mount Stromlo | 7849 | -35°19' | 149°01' | 535 |  |
|  | Australia | Orroral | 7843 | -35°38' | 148°56' | 78 |  |
|  | Australia | Yaragadee | 7090 | -29°03' | 115°21' | 1,073 |  |
|  | Austria | Graz | 7839 | 47°04' | 15°30' | 601 |  |
|  | China | Beijing | 7249 | 39°36' | 115°54' | 39 |  |
|  | China | Changchun | 7237 | 43°50' | 125°20' | 386 |  |
|  | China | Kunming | 7820 | 25°02' | 102°48' | 35 |  |
|  | China | Shanghai | 7837 | 31°06' | 121°12' | 169 |  |
|  | China | Wuhan | 7236 | 30°35' | 114°19' | 26 |  |
|  | Finland | Metsahovi | 7806 | 60°13' | 24°24' | 1 |  |
|  | France | Grasse | 7835 | 43°45' | 6°55' | 1 |  |
|  | France | Grasse (LLR) | 7845 | 43°45' | 6°55' | 608 |  |
|  | Germany | Potsdam | 7836 | 52°17' | 17°05' | 101 |  |
|  | Germany | Wettzell | 8834 | 49°09' | 12°53' | 417 |  |
|  | Japan | Kashima | 7335 | 35°57' | 140°40' | 4 |  |
|  | Japan | Koganei | 7328 | 35°26' | 139°17' | 17 |  |
|  | Japan | Miura | 7337 | 35°05' | 139°22' | 2 |  |
|  | Japan | Simosato | 7838 | 33°34' | 135°56' | 3 |  |
|  | Japan | Tateyama | 7339 | 34°35' | 139°30' | 19 |  |
|  | Poland | Borowiec | 7811 | 52°17' | 17°05' | 26 |  |
|  | Russia | Komsomolsk-Na-Amure | 1868 | 50°52' | 136°59' | 33 |  |
|  | Switzerland | Zimmerwald | 7810 | 46°53' | 6°55' | 230 |  |
|  | Tahiti | Papeete | 7124 | -17°35' | -149°36' | 42 |  |
|  | Ukraine | Simeiz | 1873 | 44°16' | 33°36' | 2 |  |
|  | UK | Herstmonceux | 7840 | 50°52' | 0°20' | 413 |  |
|  | USA | Greenbelt | 7105 | 39°01' | -76°50' | 360 |  |
|  | USA | Haleakala | 7210 | 20°43' | -156°15' | 225 |  |
|  | USA | McDonald | 7080 | 30°41' | -104°01' | 245 |  |
|  | USA | Monument Peak | 7110 | 32°54' | -116°25' | 896 |  |
|  | Uzbekistan | Maidanak | 1864 | 38°41' | 66°56' | 52 |  |

operational stations.  Daily files containing RINEX-formatted  [Gurtner, 1994] GPS and GLONASS observations collected at a 30 second sampling rate and navigation messages were archived at the global centers for the entire six-month campaign.  CDDIS also archived the SLR observations during IGEX.  Analysis Centers downloaded the station data from the Global Data Centers for orbit determination and other applications.  In turn, the Analysis Centers uploaded computed GLONASS orbits and clock information, Earth rotation parameters, and station coordinates to the Global Data Centers.  The orbits are in SP3 format [Remondi, 1989] and the station coordinates are in SINEX format [Blewitt et al., 1995].

As might have been expected, a number of operational problems occurred during the tracking campaign.  Some manufacturers’ firmware had problems in a continuous operational environment and had to be fixed by the manufacturers during the campaign.  Several stations experienced repeated failures.  Some file formatting and naming convention problems were discovered.  Site logs describing station location, equipment and ties to other geodetic control on the site were received for most stations; however, some were never submitted or are incomplete.

About 20 different RINEX converters and versions were used in the campaign.  Several problems were found including incorrect time tagging of data and incorrect field sizes for observations.  All of these problems were fixed by the manufacturers, when they were identified during the network operations.

Information exchange among the participants was greatly helped by an Internet mail system “IGEX-mail” through which 300 messages were distributed during the campaign.  Web sites at ION (http://www.ion.org/workgroup.html) and at IGN (http://lareg.ensg.ign.fr/IGEX) posted IGEX information throughout the campaign.

#### PRECISE ORBIT AND CLOCK DETERMINATION

One of the major accomplishments of the IGEX was production of precise ephemerides for all the operational GLONASS satellites for every day of the campaign.  Seven organizations independently generated precise GLONASS orbits from the GLONASS receiver tracking data.  Four organizations used the SLR observations to compute GLONASS orbits.  In addition, “refined” orbits were generated at the University of Technology, Vienna through a weighted combination of a subset of the precise orbits that were being routinely produced.  Table 4 lists the organizations that computed orbits and, when known, the software used.

Six of these groups – BKG, CODE, ESA, GFZ, JPL and MCC – were able to deliver, more or less regularly, precise

Table 4. Organizations Generating Precise

GLONASS Orbits

_______________________________________________

Organization 	Data Type	Software

BKG	Phase	Bernese

CODE	Phase	Bernese

ESA/ESOC1	Phase/Code	BAHN

GFZ	Phase	EPOS.P

NASA Jet Propulsion Lab	Phase/Code	GIPSY/OASIS

U. of Olsztyn, Poland	Phase/Code	TOP

U. of Texas CSR1	Phase	GIPSY/OASIS

AUSLIG	SLR	MICROCOSM

NERC1	SLR	SATAN

Russian MCC/GEO-ZUP1	SLR

U. of Texas CSR1	SLR	UTOPIA

U. of Technology, Vienna	Combined

1ESA/ESOC = European Space Agency/European Space Operations Center; CSR = Center for Space Research; NERC = United Kingdom SLR facility; MCC = Mission Control Center.

orbits and station coordinate solutions.  Of these, the MCC solution is the only one based solely on laser ranging measurements.  Although these Analysis Centers used different data types (undifferenced vs. double-differenced observations), different parameterizations of the force field, and different fit spans (3-8 days), all of them were able to estimate from the start GLONASS orbits well below the meter level.  This was one of the goals of the experiment.  For example, ESA used 72 hours of carrier phase and pseudorange data from 32 IGEX GLONASS receivers and 14 GPS stations from the IGS network for orbit computation.  Twenty-four-hour orbit overlaps with the preceding 72-hour spans were used to evaluate orbit precision.  ESA used the GPS orbits and satellite clocks produced for IGS as constraints in its GLONASS orbit determination processing.   Similarly, GFZ used 72 hours of carrier phase data from both dual-frequency and single-frequency GLONASS receivers with constrained GPS orbits from IGS to compute GLONASS orbits.  Six-hour orbit overlaps with the previous fit were used to judge orbit quality.  JPL also employed a 72-hour fit span to derive a solution, which was compared to the solution from the previous span using a 6-hour overlap.  Table 5 shows sample orbit overlap statistics from ESA, GFZ and JPL as daily RMS values averaged over 13 satellites for which each of these three organizations computed orbits.  These numbers are a good indication of the repeatability of the orbits from day to day.

Table 5. Sample Repeatability of GLONASS Orbits

for GPS Week 1000 (7-13 March 1999)

____________________________________________

Average Overlap RMS (cm) Over All Satellites1

7 Mar	8 Mar	9 Mar	10 Mar	11 Mar	12 Mar	13 Mar

ESA	27	21	21	19	20	20	18

GFZ	66	71	110	99	80	150	--2

JPL	31	17	12	11	10	11	--2

1Computed for 13 GLONASS satellites: Slot nos. 1, 3, 4, 6, 7, 8, 9,

11, 13, 16, 17, 20, 22.

2No overlap data.

In general, over the entire campaign, solutions were consistent at the 20-30 cm level.  At the University of Technology, Vienna, the precise orbits submitted by the six Analysis Centers noted above were combined into one final solution.  This was done by applying small reference frame corrections and then calculating a weighted mean for each satellite from the independent solutions of the six Analysis Centers.  The weights are based on the results of a 7-day fit that is performed by the Analysis Coordinator, to the daily orbit solutions for each satellite for each Analysis Center.   At this time, the broadcast satellite clock values are being used with the orbits until better values can be derived.

The accuracy of the orbits computed from the GLONASS receiver data can be evaluated by using the SLR observations.  The NERC SLR facility in the U.K. computed 7-day orbits from the SLR measurements, which gave post-fit residual RMS values of about 6-10 cm.  These orbits were then compared to orbits derived by CODE from the GLONASS receiver data.  The SLR and receiver-derived orbits compared at the one-meter level in the along-track and cross-track directions, and at about the 20-cm level radially.  The along-track and cross-track differences may be due to systematic biases between the two systems.  AUSLIG found RMS differences between SLR orbits and CODE’s orbits in the 8-9 cm range radially and 50 cm range in the along-track direction.  Similar results were obtained by the University of Texas CSR.  A direct comparison done by CODE between its microwave GLONASS orbits and the raw SLR range data revealed an average range bias of 4 cm and an RMS difference of 16 cm.

#### RELATIONSHIPS BETWEEN REFERENCE FRAMES

Two methods are generally used to quantitatively relate one reference frame to another.  One requires knowledge of a set of ground (antenna) positions in both reference frames.  Thus, for example, the PZ-90 coordinates of the ground positions could be mathematically related to the WGS 84 coordinates of the same positions.  The resulting transformation parameters can then be used to convert other point positions from one coordinate system to the other when needed.  The second method relies on comparisons of satellite orbits which are defined independently in two different reference frames, and which then can be mathematically related to one another.  A 7-parameter transformation is usually employed to derive three translation and three rotation parameters, and one scale parameter.  PZ-90 coordinates are not available for most places outside the Former Soviet Union.  Therefore, most attempts to compute transformations have been based on the orbit approach.  BKG, JPL and MCC all used the orbit approach.  BKG computed daily values for transformation parameters using its precise GLONASS orbits and the broadcast orbits.  A rotation about the z-axis of 0.3–0.4 arcseconds was found to be the most significant parameter.  JPL obtained the same result after smoothing the broadcast orbits and then comparing them to JPL’s precise ITRF96 orbits.  The MCC computed precise ITRF94 orbits based on SLR data, which they then compared to the broadcast orbits.  They noted that the transformation parameters seem to vary periodically and attribute this to errors in the Earth Orientation values used to generate GLONASS broadcast orbits.  A 0.3-0.4 arcsecond z-axis rotation and a 1.1 m z-translation are the dominant parameters in their proposed transformation.  The station positioning method was used by IGN to derive results similar to the MCC’s.  IfEN GmbH employed an alternative method for computing transformation parameters, that involved incorporating the transformation parameters directly in the range observation equations. Using the known ITRF station positions and the broadcast PZ-90 satellite positions with the pseudorange observations, the transformation parameters were obtained by solving these range equations.  The z-axis rotation was again the most significant parameter.  Note that the accuracy attainable with any of these methods is limited by the accuracy of the broadcast PZ-90 satellite positions.

#### TIME TRANSFER APPLICATIONS

IGEX-98 was well received by the international time metrology community, as the results of this experiment are contributing greatly to research on the best use of the GLONASS constellation for international time transfer.  The international time scales – International Atomic Time (TAI) and Coordinated Universal Time (UTC) – are based on data from some 220 atomic clocks located in about 50 time laboratories around the world. Today, the sole method of comparing these clocks to provide data for TAI is the GPS C/A-code common-view technique. [Lewandowski et al., 1996]  The performance of this technique barely covers present needs, and will not be sufficient in the near future to compare the new generation of clocks.  Thus, the time metrology community is engaged in a number of studies of new time transfer techniques, among which is the use of GLONASS or combined GPS and GLONASS systems.  A gain of a factor of 4 for time transfer stability was observed with a GPS+GLONASS multi-channel link compared to a one-channel GPS link.

In order to take full advantage of GLONASS capabilities for intercontinental time transfer, however, the use of post-processed precise ephemerides is necessary, as it is for GPS applications.  An uncertainty of about 2 ns or better is achievable for intercontinental GLONASS time transfer when using IGEX precise ephemerides, and only about 10 ns when using broadcast ephemerides.  An international effort is currently under way to calibrate GLONASS timing receivers around the world.  When this is completed, the timing community will be able to apply these techniques in earnest.

### FUTURE DIRECTIONS

Since April 20, 1999, the IGEX activities have continued on a “best effort” basis.  A global network of about 20 combined GLONASS/GPS dual-frequency receivers is still tracking GLONASS satellites on a routine basis.  The ILRS network continues to track three GLONASS satellites routinely.  These data are being forwarded to the Global Data Centers, and several of the Analysis Centers continue to produce precise orbits that are publicly available from the Data Centers.  These orbits are in the same reference frame as the GPS orbits produced by the IGS.

Although the future of GLONASS is uncertain, it is clear that the technology, methodology and organizations are in place to collect and process GLONASS data.  GLONASS data, when combined with GPS data, are a valuable resource for satellite geodesy, definition of the terrestrial reference system, time transfer, navigation, and atmospheric research.  Participants in the IGEX-98 Workshop in Nashville voted overwhelmingly in favor of continuing global, internationally-coordinated tracking and orbit determination for GLONASS for a four-year period ending in 2003.  This new pilot service should be organized under the auspices of the IGS.  If successful, the GLONASS pilot service should eventually be merged with GPS into one dual service within the IGS.  A new Call for Participation will be issued in January 2000.

#### CONCLUSIONS

IGEX-98 was a great success.  The results of the project exceeded expectations.  All of the major problems that previously stood in the way of exploiting GLONASS were overcome.  Receivers, a global tracking network, data exchange formats, software, precise orbits and datum transformations were produced for this experiment. More than 60 receivers located in 26 countries and 30 SLR observatories in 15 countries contributed data during the 6-month campaign.  Eleven different organizations computed precise orbits for GLONASS satellites from these data and achieved accuracies of 20-50 cm consistently.  The SLR data were crucial in verifying the microwave receiver-derived orbits.  More work needs to be done to improve modeling of solar radiation pressure and other non-gravitational forces, as well as to explain small systematic biases between SLR- and receiver-based orbits.  A number of independent comparisons of PZ-90 and ITRF orbits and station coordinates confirmed a difference of about 0.3-0.4 arcseconds in rotation about the z-axis and a possible 1.0 meter translation in the z-direction.

It would not have been possible to organize and successfully execute this experiment in such a short period of time without the GPS infrastructure that has been developed during the last 20 years.  The IGS provided a backbone for the entire campaign, through its operational tracking network, protocols for data communication and formats, and its analysis centers and data centers.  This combined with the collective expertise of the GPS and GLONASS communities enabled us to meet the objectives that we originally set forth.

Most users view GLONASS as an augmentation to GPS and not a stand-alone system at this time.  As such, the two systems form a 36-satellite constellation.  Since receivers, orbit determination software and a tracking network now exist for GLONASS and GPS in a common reference frame, it should be possible to take advantage of the combined satellite systems for many different applications.  The timing community is already using the precise orbits to enhance intercontinental time transfer.  The global tracking network was called upon twice during the campaign to provide information for special purposes – once to help the Russians pinpoint the time that one of the satellites stopped transmitting while it was out of view of Russian ground stations, and another time to provide high sampling rate data for ionospheric studies during the solar eclipse in August.  The experience gained here will lay the groundwork for using any future global navigation satellites, such as the proposed European Galileo system, in combination with GPS.  Due to continued interest in using GLONASS by many of the IGEX participants, plans are under way to continue the IGEX effort as a pilot operational service within the IGS on a test basis beginning next year.

#### ACKNOWLEDGMENTS

The success of this experiment was due to the work of many dedicated individuals and organizations around the world that voluntarily collaborated on this project.  We are indebted to Dr. Pratap Misra, Chair of the ION GLONASS-GPS Interoperability Working Group, and ION for providing a forum for discussion of GLONASS and for directly assisting with Russian participation in these activities.  We appreciate the efforts of receiver manufacturers to make sure receivers were available to all those who wanted to participate in the campaign.  The authors also wish to thank David  Hansen of the National Imagery and Mapping Agency who created and maintained the ION IGEX web site during the entire experiment.

REFERENCES

Azoubib, J. and W. Lewandowski, A Test of GLONASS P-Code Time Transfer, Proc. ION GPS-98, Nashville, September 15-18, 1998, pp.1729-1736 (1998).

Bazlov, Y. A., V. F. Galazin, B. L. Kaplan, V. G. Maksimov and V. P. Rogozin, GLONASS to GPS, A New Coordinate Transformation, GPS World, 10, 1, pp. 54-58 (1999).

Beutler, G., M. Rothacher, S. Schaer, T. Springer, J. Kouba, and R. E. Neilan, The International GPS Service (IGS), an interdisciplinary service in support of Earth sciences, 32nd COSPAR Scientific Assembly, Nagoya, Japan, July 1998, Adv. Space Res., 23, 4, pp. 631-653 (1999).

Blewitt, G., Y. Bock and J. Kouba, Constructing the IGS Polyhedron by Distributed Processing, Proc. IGS Workshop on the Densification of the IERS Terrestrial Reference Frame Through Regional GPS Networks, J. F. Zumberge and R. Liu, Eds., JPL, Pasadena, Nov. 30 – Dec. 2, 1994, pp. 21-37 (1995).

Gurtner, W., RINEX: The Receiver-Independent Exchange Format, GPS World, 5, 7, pp. 48-52 (1994).

GLONASS Interface Control Document, International Civil Aviation Organization, (ICAO), GNSSP/2-WP/66, Montreal, Canada, 14 November 1995 (1995).

Klyushnikov, S., S. Filatchenkov, N. Mikhailov, S. Pospelov, and M. Vasilyev, “Soyuz”-“Mir” Orbital Flight GPS/GLONASS Experiment: First Results, presented at 6th St. Petersburg Int. Conf. on Integrated Navigation Systems, St. Petersburg, Russia, May 24-26, 1999 (1999).

Langley, R.B., GLONASS: Review and Update, GPS World, 8, 7, pp. 46-51 (1997).

Lewandowski, W., J. Danaher and W. J. Klepczynski, Experiment Using GPS/GLONASS, Common-View Time Transfer Between Europe and North America, Proc. ION GPS-96, Kansas City, September 17-20, 1996, pp. 271-277 (1996).

Misra, P., R. Abbot and E. Gaposchkin, Integrated Use of GPS and GLONASS: Transformation Between WGS 84 and PZ-90, Proc. ION GPS-96, Kansas City, September, 17-20, 1996, pp. 307-314 (1996)

Misra, P. and J. Slater, A Report on the Third Meeting of the GLONASS-GPS Interoperability Working Group, Proc. ION GPS-98, Nashville, September 15-18, 1998, pp.2103-2106 (1998).

Remondi, B. W., Extending the National Geodetic Survey Standard Orbit Formats, NOAA Tech. Report NOS 133 NGS 46 (1989).

Rossbach, U., H. Habrich, and N. Zarraoa, Transformation Parameters Between, PZ-90 and WGS-84, Proc. ION GPS-96, Kansas City, September 17-20, 1996, pp. 279-285 (1996).

Senus, W. and P. Misra, A Report on the First Meeting of the GLONASS-GPS Interoperability Working Group, Proc. ION GPS-96, Kansas City, September 17-20, 1996, pp. 1929-1930 (1996).

Slater, J. and P. Misra, A Report on the Second Meeting of the GLONASS-GPS Interoperability Working Group, Proc. ION GPS-97, Kansas City, September 16-19, 1997, pp.1893-1894 (1997).

Slater, J., P. Willis, W. Gurtner, C. Noll, G. Beutler, G. Hein, R. E. Neilan, The International GLONASS Experiment (IGEX-98), Proc. ION GPS-98, Nashville, September 15-18, 1998, pp.1637-1644 (1998).

Slater, J. A., C. Noll and K. Gowey, Eds., Proc. International GLONASS Experiment 1998 (IGEX-98) Workshop, Nashville, Sept. 13-14, 1999, in preparation (1999).

Willis, P., G. Beutler, W. Gurtner, G. Hein, R. Neilan and J. Slater, International Call for Participation to the IGEX-98 campaign, J. of Geodesy, 72, 5, p. 313 (1998).

Willis, P., G. Beutler, W. Gurtner, G. Hein, R. E. Neilan, C. Noll, and J. Slater, IGEX: International GLONASS Experiment - Scientific Objectives and Preparation, 32nd COSPAR Scientific Assembly, Nagoya, Japan, July 1998, Adv. in Space Res., 23, 4, pp. 659-663  (1999).

Zarraoa N., W. Mai, E. Sardon, and A. Jungstand, Preliminary evaluation of the Russian GLONASS system as a potential geodetic tool, J. of Geodesy, 72, 6, pp. 356-363 (1998).

# Text boxes

Figure 1. GLONASS Receiver Stations and SLR Observatories that participated in IGEX-98.

Figure 1. GLONASS receiver stations and SLR observatories that participated in IGEX-98.