PDF Analysis System

Stand-Alone Version

Table of Contents

PDF Analysis System – Stand Alone Installation	1

Introduction	1

Quick Install	1

Audience	1

Scope	1

Acknowledgments	1

Authorship	1

References	2

PDF Analysis System Overview	3

Description	3

Requirements	3

Hardware	3

Software	4

PDF Source Code Organization	4

Input and Output Files	5

Input	5

Output	6

System Configuration	7

Data Directories	7

MiniSeed Data Directory and Files	7

Response File Directory	8

Web Directory	8

Script Variables	9

Source Code Header File Modification	9

System Compilation and Installation	10

Compilation	10

Compiler Options	10

Installation	11

PDF System Execution	12

Channel-Specific Shell Script	12

Overall Execution	12

Execution Features	12

Error Processing	13

Release Notes	14

Current Limitations	14

Version Control	14

Version 1.1	14

Appdendix I – File Formats	15

Djjj.bin File	15

Hour.idx File	15

Hjjj.bin File	15

PDFAnalysis.bin File	15

PDFAnalysis.inf File	16

PDFanalysis.sts File	16

PDFAnalysisSR.bin File	17

Appendix II – Installation and Configuration Checklist	18

# PDF Analysis System – Stand Alone Installation

## Introduction

Following from the successful implementation of the NEIC PDF Analysis System, both at the IRIS DMC in Seattle, WA, and at the NEIC in Golden, CO, it is desired to provide the system to the seismic community at large in a stand-alone form.  This, to allow other users of the seismic community the opportunity to perform their own analyses against data sets not being held by either of these two data centers.

## Quick Install

If the time required to read and understand this document in totality is unavailable (but you’d like it installed and working as quickly as possible), you must at least read the sections System Configuration, System Compilation and Installation, and PDF System Execution and follow the steps outlined there.  Where problems occur, be certain to consult the other various sections of this document that may provide further information to solve your issue.

## Audience

This document is intended for all users of the siesmic community with an interest in producing noise analyses of seismic data following the algorithm laid out by Buland and McNamara of the USGS NEIC of Golden, Co.

## Scope

This document is limited to the technical aspects of the PDF Analysis System: installation, configuration and execution.  As such, it does not treat the functional aspects of the system: methodologies, algorithm, philosophy, interpretation possibilities, usage of results, etc.  For a complete discussion of these and more, please consult the various documents listed below.

## Acknowledgments

The following parties have significantly contributed to the development of this system and are hereby acknowledged thus:

| Party | Contribution |
| --- | --- |
| Ray Buland and Daniel McNamara (of USGS NEIC, Golden, CO) | Provided the original algorithm and proof-of-concept implementation |
| USGS NEIC | Provided the funds for original development of algorithm. |
| NSF | Provided funds for original system development of generic implementation at the IRIS Data Management Center (Seattle, WA). |
| IRIS | Sponsored the development of the generic implementation at the DMC. |
| Bruce Weertman (of IRIS) | Responsible for integration of the PDF system within the IRIS DMC’s Quack framework. |

## Authorship

Both this document and the PDF analysis system itself was written by Richard Boaz (of Boaz Consultancy: http://www.boazconsultancy.com).  Any and all comments and/or bug reports are welcome and are encouraged to be forwarded to riboaz@xs4all.nl.

## References

The following table provides various references which may be of interest to the reader:

| Description | Name | Location |
| --- | --- | --- |
| Original Abstract (Adobe pdf) | Ambient Noise Levels in the Continental United States | PDF Stand-Alone distribution docs directory |
| Power Point Presentation | Noise Based Detection Method for the ANSS | PDF Stand-Alone distribution docs directory |
| Discussion Paper (Adobe pdf) | Determining True Global Ambient Noise | PDF Stand-Alone distribution docs directory |
| PDF Analysis Interpretation (html document) | Ambient Noise Probability Density Functions | PDF Stand-Alone distribution docs directory |
| PDF Analyses at the USGS NEIC | USGS/ANSS Noise Monitor | http://geohazards.cr.usgs.gov/staffweb/mcnamara/ANSSPDFweb/ANSSPDFweb.html |
| PDF Analyses at the IRIS DMC | DMC QUACK Information Query | http://www.iris.washington.edu/servlet/quackquery/ |
| PDF Analyses at the IRIS DMC (US Array) | DMC QUACK Information Query | http://www.iris.washington.edu/servlet/quackquery_us |

# PDF Analysis System Overview

A new system for analyzing data quality is now available to the seismology community allowing users to evaluate the long-term seismic noise levels for any broadband seismic data channel.  The new noise processing software uses a probability density function (PDF) to display the distribution of seismic power spectral density (PSD) and has been implemented against the entire continuous data-stream held by IRIS at the DMC.

This noise processing system is unique in that there is no need to screen the data for  earthquakes, system glitches or general data artifacts, as is commonly done in seismic noise analysis.  Instead with this new analysis, system transients map into a low-level background probability while ambient noise conditions reveal themselves as high probability occurrances.  In fact, examination of artifacts related to station operation and episodic cultural noise allows us to estimate both the overall station quality and a baseline level of earth noise at each site.

PDF noise plots are useful for characterizing the current and past performance of existing broadband sensors, for detecting operational problems within the recording system, and for evaluating the overall quality of data for a particular station. The advantages of this new approach include:

- provides an analytical view representing the true ambient noise levels rather than a simple absolute minimum;

- provides an assessment of the overall health of the instrument/station; and,

- provides an assessment of the health of recording and telemetry systems.

Please see the document Ambient Noise Probability Density Functions for a more detailed discussion of the PDF plots themselves and their interpretation possibilities.

## Description

Quite simply, the PDF Analysis system is comprised of three separate processing components:

- An analysis program (written in C), responsible for producing analysis statistics for a single channel;

- A shell program (using GMT) to convert the analysis results produced in step 1 to a plot, in the form of a postscript format file;

- Image manipulation (using ImageMagick) commands to convert the postscript file created in step 2 to an actual graphical image (.png format).

Execution is provided in the form of a shell script per channel to analyze, responsible for calling each of these components in turn (see section PDF System Execution below for details).

## Requirements

### Hardware

No specific hardware requirements exist, per se.  The program will execute on any platform supporting a C compiler in addition to the other software requirements listed below.

Depending on which compile time output option is chosen (please see section System Compilation and Installation: Compilation: Compile Options for a complete discussion of these options and their effects), disk storage requirements are approximately the following (per channel analyzed):

| Output Option | Maximum Disk Storage Requirement |
| --- | --- |
| No Daily or Hourly .bin output | 5 Mb |
| Only Daily .bin output | 15 Mb |
| Both Daily and Hourly .bin output | 50 Mb |

### Software

The following table defines the software dependencies currently en force:

| Software | Version | Description | Available At |
| --- | --- | --- | --- |
| C Compiler | User preference | Compiler (program developed under gcc) | http://gcc.gnu.org/ |
| Scripting | Bash shell | Scripting tools | Local machine executing analysis |
| GMT | Latest available | Plotting tool | http://gmt.soest.hawaii.edu/ |
| ImageMagick | Latest available | Image manipulation tool | http://www.imagemagick.org/ |

## PDF Source Code Organization

The following table defines the directories and files which make up the source tree of the PDF Analysis System:

| Directory/File | Description |
| --- | --- |
| PDF | Root system directory |
| PDF/PROD | Production directory containing production relevant files |
| PDF/PROD/bin | Directory containing shells and executables, |
| PDF/PROD/script | Directory containing executable scripts |
| PDF/PROD/support | Directory containing all necessary production support files |
| PDF/PROD/helper | Directory containing helper scripts (system mgmt, etc.) |
| PDF/src | Directory holding all source code: PDF analysis program GMT plotting script Execution scripts |
| PDF/src/vx.x.x | Directory holding all source code for version x.x.x of the system |
| PDF/src/ vx.x.x/analysis | Source code directory of analysis program (C code) |
| PDF/src/ vx.x.x/analysis/mseed | Miniseed data file reader source code - as library to main() |
| PDF/src/ vx.x.x/analysis/resp | Instrument response interpreter source code - as library to main() |
| PDF/src/ vx.x.x/GMT | Directory holding GMT source code - scripts and support files |
| PDF/src/ vx.x.x/script | Directory holding execution scripts |

# Input and Output Files

## Input

The following table defines the directories and files which are required input, see sections System Configuration and PDF System Execution for full description of specification and use:

| Directory/File | Description |
| --- | --- |
| Data Directory | Directory holding the miniseed data files to be analyzed. N.B. All data files requiring analysis as part of a single execution must reside in this single directory. |
| Miniseed Data Files | Files to analyze, miniseed format only. |
| Analysis Directory | Directory holding all output files. See section Output for a complete description. |
| Response File Directory | Directory holding response files for channels being analyzed. See section System Configuration for a complete discussion on set-up. |
| RESP.NTW.STN.LOC.CHN | The file holding the response information for the instrument and channel. This must be formatted as for input to the evresp() function (format as produced by the rdseed program). Where: NTW is the network name STN is the station name LOC is the location identifier CHN is the channel identifier |

## Output

The following table defines the directories and files which are created in the course of the PDF Analysis execution.  All are located as subdirectories to the analysis directory defined in the section Input above and are automatically created in the course of execution.  Please consult Appendix I – File Formats for a detailed description of their contents.

| Directory/File | Description |
| --- | --- |
| NTW.STN.LOC.CHN.png | Graphical representation of analysis. |
| Yyyyy | Directory holding daily PSD .bin files, by year Where: yyyy is the year |
| Yyyyy/HOUR | Directory holding the hourly PSD .bin files |
| LOG | Directory holding the various log files created during the course of execution. |
| wrk | Directory holding various work files |
| Yyyyy/Djjj.bin | Files holding individual day's PSD analysis results (currently unused, for future use). Where: jjj is the julian day |
| Yyyyy/HOUR/hour.idx | Index file to Hjjj.bin file. |
| Yyyyy/HOUR/Hjjj.bin | Files holding individual hour's PSD analysis results (currently unused, for future use) |
| LOG/NTW.STN.LOC.CHN.log | Log file of analysis program. |
| LOG/plotGMT.log | Log file of GMT plotting program. |
| LOG/convert.log | Log file of ImageMagick convert program, nothing output for normal execution. |
| LOG/NTW.STN.LOC.CHN.yyyy.jjj.err | Analysis program error file, by year and julian day |
| LOG/PDFanalysis.skp | File listing those days when problems occurred, information only |
| wrk/PDFanalysis.bin | Cumulative dB-based .bin file, results to graph are contained here |
| wrk/PDFanalysis.inf | Information file holding various analysis settings |
| wrk/PDFanalysisSR.bin | Cumulative period-based .bin file. Where: SR is the sample rate of the channel |
| wrk/PDFanalysisSR.inf | Information file as before, sample-rate specific |
| wrk/PDFanalysis.sts | File holding various statistics for analysis results, input to GMT |
| wrk/PDFanalysis.ps | GMT postscript file output, deleted upon conversion to .png file. |
| wrk/pdf.grd | GMT temp file, deleted upon completion of GMT step. |

# System Configuration

Configuration of the PDF system amounts to the setup of various directories and script variables.  This section lays out these requirements for the PDF system setup to result in a successful installation and subsequent execution.  Failure to define these precisely as described herein will result in a non-functioning system.

Appendix II provides a checklist for each parameter and variable which must be defined as part of system setup.  Please print, define the values accordingly and supply them in their proper location.

## Data Directories

### MiniSeed Data Directory and Files

A directory is required to contain the miniseed data files to be analyzed.  This directory and the miniseed data files themselves must adhere to the following:

- All miniseed data files representing a single channel’s worth of waveform data, for all time, must be contained within the same directory.

- All miniseed data files must contain exactly (or as close to) one day’s worth of data, from 00:00 hours to 24:00 hours.

- The directory structure must conform to the following conventions:

DATAROOT/NTW/STN

Where

DATAROOT	is the root directory of the miniseed data files (script variable of such specified below)

NTW	is the name of the network

STN	is the name of the station

- The name of the miniseed file itself must conform to the following naming convention:

STN. NTW.LOC.CHN.yyyy.jjj

Where

STN	is the name of the station

NTW	is the name of the network

LOC	is the location identifier

CHN	is the channel identifier

yyyy	is the year of the data file

jjj	is the julian day of the data file

(N.B. Where no location identifier exists, field should be null.  This would render, for example, a filename for station ATKA and network AK as: ATKA.AK..BHE.2004.261)

Assuming your directory structure and miniseed data files do not naturally conform to these requirements, this directory structure and filenaming convention can be easily accommodated for through the following:

- Create the fixed directory structure itself: DATAROOT/NTW/STN

- For each miniseed data file, create softlinks (ln –s) to the actual/real miniseed data files such that the naming convention above is adhered to.

Further, this can be automated via a script rendering this requirement as trivial as possible.  Please see the script linkMseed.US (located in pdf/PROD/helper/linkmseed) for an example and modify as necessary.

N.B.  Because the filenaming convention uniquely identifies the channel of data, this directory may contain all miniseed data file for all channels of a station, i.e., it is not necessary to create separate directories for each channel, rather, a separate directory only for the station itself and containing the miniseed data files for all channels.

### Response File Directory

A directory must exist containing all response files used to deconvolve the signal back to absolute ground motion in the course of analysis.  This directory and the files themselves must adhere to the following:

- The directory itself may be specified as per user desires/requirements, no specific directory structure requirement exists.  The directory holding these response files must be specified in two places: in the script variable RESPDIR (see section Script Vaiables below), and within the PDFuser.h file of the PDF analysis program source code (see section Source Code Header File Modification below).

- The filename of the response file itself must conform to the following naming convention:

RESP.NTW.STN.LOC.CHN

Where

RESP	is exactly as specified: RESP

NTW	is the name of the network

STN	is the name of the station

LOC	is the location identifier

CHN		is the channel identifier

(N.B.  This naming convention follows from the response file output generated by the rdseed program.  And as before, where no location identifier exists, field should be null.)

- The internal format of the response file information must conform to the format produced by the rdseed program, subsequently readable by evresp().

### Web Directory

A directory must be created used to collect all .png files created during the course of execution.  The .png files themselves are contained in the analysis directory for the channel being analyzed, making collective viewing annoying since all are held within disparate directories.  This annoyance is alleviated through the existence of this directory.

Create a directory for these to be contained in and define this location in the .vars-user file.  With this directory, the last action in the course of analysis is for a softlink to be created in this directory pointing to the .png file found in the analysis directory.

Additionally, if it is desired to publish the results, it is this directory that can be made available to the web in whatever manner/means appropriate.

## Script Variables

The following script variables are installation-specific and must be pre-defined by the user and provided in the shell script file .vars-user (located in directory PDF) before the system can be installed.  Failure to do so will result in a non-functioning system.

| Script Variable Name | Description |
| --- | --- |
| PDFROOT | Root directory of PDF analysis system (directory holding the .vars-user file) |
| WEBDIR | Directory of collected .png files |
| RESPDIR | Directory holding response files |
| DATAROOT | Root directory of miniseed data files (parent to NTW/STN) |
| STATSROOT | Root directory of PDF analysis results/statistics |
| GMTROOT | GMT installation root directory |
| IMROOT | ImageMagick installation root directory |

## Source Code Header File Modification

The sole configuration requirement within the source code of the PDF analysis program is the following #define parameter to be specified:  (N.B. needless to say, this must be the same as defined as part of the Script Variables above.)

| #define parameter | Description | Location |
| --- | --- | --- |
| #define RESPDIR | Directory holding response files, inside quotes “”. | PDF/src/vx.x.x/analysis/PDFuser.h |

# System Compilation and Installation

## Compilation

Compilation of the PDF Analysis program employs straightforward C/Unix standards, i.e, a C compiler and make.  In addition to the analysis portion of the program, there are two subdirectories of libraries requiring compilation as well.  As such, a script is provided that will traverse each of these subdirectories, making the dependent libraries in turn.  This script is located in the PDF Analysis source directory and conforms to the following invocation specifications:

makesh [ clean | all ]

where

clean	will execute make clean, removing all dependant libraries and object files.

all	will execute make all in each directory of the PDF analysis program, creating all dependant libraries and object files necessary to ultimately link the PDF analysis executable.

Alternatively, the program may be built when installing the system as a whole, alleviating the need to compile and link by hand.  Please see the section Installation below for details.

### Compiler Options

Two compile-time options exist for the PDF Analysis program.  Namely, defining whether or not daily and/or hourly PSD information is output.  (Please see section Requirements: Hardware for detailed overall disk storage requirements.)

With daily PSD information output, cumulative .bin files are generated for each day analysed (amounting to ~30Kb/day/channel analysed).

With hourly PSD information output, .bin files are generated for each hour analysed (amounting to ~100Kb/day/channel analysed).

The system is delivered, by default, to output both daily and hourly .bin files.  Output of this data is anticipated to be used in future versions of the software, such that existence of these files will allow PDFs to be produced for specific user-defined time periods.  For example, a PDF graph representing only the months of January thru March; or a PDF graph representing all months but only between the hours of 6AM and 6PM.

If it is anticipated that these more specific sorts of analyses will be of interest, no action is required, both daily and hourly .bin files will be generated.

If this is not desired, or disk space is an issue, both daily and hourly .bin file generation may be suppressed.  The following table defines these compile time options:

| Compiler Option | Effect |
| --- | --- |
| -DNO_DAILY_PSD | No daily PSD .bin files output |
| -DNO_HOURLY_PSD | No hourly PSD .bin files output |

Either or both (they are mutually independent) of these options can be specified in the CFLAGS section of the Makefile for the main PDF Analysis program.  The resulting executable will subsequently NOT output incremental PSD information.

N.B.  Since these are compiler options, these settings have a system-wide influence, i.e., these options cannot be implemented on a per channel basis.  (One way around this, however, would be to install more than a single system.)

## Installation

Installation is provided via the shell script installPDF located in the directory PDF and provides for the following functionality:

- optionally compiles the PDF Analysis program, and

- copies all relevant files to the PROD directory.

And conforms to the following usages:

command:	installPDF –h

output:	Usage: install [-h] [make] version#

description:	prints the usage for the command.

command:	installPDF v1.1

output:	Copying v1.1 executables and support files to PROD dir…

description:	installs all relevant executables, scripts and support files for version# to the PROD directory structure.  (N.B. command line argument version# must be as specified in the PDF source directory structure.)

command:	installPDF make v1.1

output:	Compiling v1.1 PDF Analysis program…

Copying v1.1 executables and support files to PROD dir…

description:	as for command installPDF v1.1, however, cleans and compiles the PDF analysis program before copying and installing to the PROD directory structure (recommended for first install since no object files exist as part of delivery).

# PDF System Execution

System execution comes in the form of two scripts, executePDF and PDFscript (both located in PDF/PROD/bin).

PDFscript is a shell script template used to create the individual channel-specific execution script, this script ultimately responsible for the PDF analysis execution of a specific channel.

The executePDF script executes all channel-specific scripts located in PDF/PROD/script in turn.

## Channel-Specific Shell Script

Execution of the PDF Analysis System is provided in the form of a shell executable script (PDFscript) responsible for carrying out the three steps of execution described in section PDF Analysis System Overview: Description.  This execution script is created by replacing various strings in the generic file PDFscript with execution-specific values, thus creating a unique script for each channel to be analyzed.

This channel-specific executable shell can be easily created using the following shell script command:

makePDFscript NTW STN LOC CHN

where

NTW		is the network name
STN		is the station name
LOC		is the location identifier (use -- for no location)
CHN 		is the channel identifier

The will create the channel-specific script to be executed, named NTW.STN.LOC.CHN.sh and saved to the directory PDF/PROD/script. In addition, the analysis directory will also be created if it does not exist (assuming the STATSROOT directory exists).

Once this script has been created for a specific channel, it can be simply repeatedly executed (daily, weekly, monthly, as desired) to update the analysis results.

## Overall Execution

Executing the script executePDF will result in all scripts located in PDF/PROD/script to be executed in turn.  Specifically, it will execute all files having “.sh” as their filename suffix.  Thus, individual analyses can be turned on and off simply by renaming the suffix of the executable script in question.

A simple logfile of executePDF, detailing the channels analyzed, is generated and written to the file PDF/PROD/LOG/PDF.log.

Further, this process may be automated using the UNIX crontab command.  At specified times, merely execute the executePDF script and all analyses will be performed and updated.

## Execution Features

Please note the following features of the PDF analysis system:

- Analysis is performed against all data files found in the specified data directory only up to and until two days prior to analysis execution date.  This allows for systems where data availability can suffer up to two days of latency.

- The program does cross the day boundary to analyze the last hour of data held within the miniseed files.  As such, the last file identified for analysis is not fully analyzed; it is treated in subsequent executions.

- When crossing the day boundary, program assumes data is coincident if ending time and starting time of respective miniseed files differ by less than one sample (1) of time.  Where data is identified not to be coincident, an error message is output to the channel-specific log file.

## Error Processing

Error handling is very much dependent on the type of error encountered.  The following table lists the major errors that may be encountered, how each is handled, and suggested follow-up action.

| Error | Type | How Handled | User Follow-up |
| --- | --- | --- | --- |
| Response File not found | Fatal | Analysis execution suspended; error message written to Log file | Provide proper response file, verify naming convention is adhered to. |
| Response Information not found | Fatal | Analysis execution suspended; error message written to Log file | Provide file containing response information for appropriate date/time range, verify file format is adhered to. |
| Error reading miniseed data file | Non-fatal | Analysis execution skips this day of data; error message written to day-specific error file located in LOG directory of analysis output. | Determine if miniseed data file can be repaired. |
| Internal Processing Error | Fatal | Analysis execution suspended | Contact riboaz@xs4all.nl with all relevant information |
| No files ever found to analyze | Non-fatal | Program successfully executes but nothing analyzed | Verify miniseed directory structure and filenaming conventions are adhered to. |
| Unable to create or access directories | Fatal | Analysis execution suspended | Confirm existence and access permissions of directory in question. |

# Release Notes

## Current Limitations

The limitations are currently defined to be:

- unable to analyze long period channels, limited to 20 samples/sec or more;

- unable to provide analysis for user-defined time periods, only analysis of all data available is currently provided for;

- output provided to end-user currently limited to .png graphical file format;

- unable to analyze any data prior to the last day analyzed.  This means that the program cannot fill in gaps nor replace the results of previously analyzed data.  This will be treated in a future release.

## Version Control

This section defines the current and historical releases of the PDF Analysis System.

### Version 1.1

Release Date:	29-October-2004

Modifications

- Stand-alone version created and made available for general release.

# Appdendix I – File Formats

This appendix defines the formats of the various files produced by the PDF analysis system.

## Djjj.bin File

Definition:	Cumulative db-based .bin file holding daily PSD analyses for julian day jjj.

Directory:	Yyyyy

Internal Format:

- Data Format:	ASCII

- Individual lines each defining:

FREQ	POWER	#HITS

Where:

FREQ		is the frequency (in Hz)

POWER	is the power bin (in dB)

#HITS		is the number of times

## Hour.idx File

Definition:	Index file to Hjjj.bin file, index defined by julian day and HH:MM start time of PSD.

Directory:	Yyyyy/HOUR

Internal Format:

- Data Format:	ASCII

- Individual lines each containing:

JDAY	HH:MM	REF

Where:

JDAY		is the julian day
HH:MM	is the hour and minute start time of the PSD
REF		is the reference identifier, for accessing/extracting from the Hjjj.bin file

## Hjjj.bin File

Definition:	Cumulative db-based .bin file holding hourly PSD analyses for julian day jjj.

Directory:	wrk

Internal Format:

- Data Format:	ASCII

- Individual lines each containing:

REF	FREQ	POWER

Where:

REF		is the reference identifier from the hour.idx file
FREQ		is the frequency (in Hz)
POWER	is the power bin (in dB)

## PDFAnalysis.bin File

Definition:	Cumulative db-based .bin file holding overall PSD probabilities for julian day jjj.

Directory:	wrk

Internal Format:

- Data Format:	ASCII

- Individual lines each defining:

FREQ	POWER	PROB

Where:

FREQ		is the frequency (in seconds)

POWER	is the power bin (in dB)

PROB		is the normalized (to probability) number of hits

## PDFAnalysis.inf File

Definition:	Information file containing various settings/values pertaining to analysis.

Directory:	wrk

Internal Format:

- Data Format:	ASCII

- Individual lines each defining:

VALUE		:SETTING

- With the following SETTINGs currently being provide for, appearing in the following order:

| SETTING | Definition |
| --- | --- |
| Analysis Start Date | Start day of the analysis (format: YYYY:JJJ) |
| Analysis Stop Date | Stop day of the analysis (format: YYYY:JJJ) |
| Total Number of Days | Total number of days analyzed |
| Total Number of PSD's | Total number of PSD’s making up the analysis |
| Total Number of Problem Days | Total number of days encountering a problem (information only) |
| SAMPLE RATE | Sample rate of the channel |
| NETWORK | Network name |
| STATION | Station name |
| LOCATION | Location identifier |
| CHANNEL | Channel identifier |
| NYQUIST | Nyquist value for this analysis |

## PDFanalysis.sts File

Definition:	File holding various statistics for this analysis.

Directory:	wrk

Internal Format:

- Data Format:	ASCII

- Individual lines each defining:

FREQ	MIN	AVE	50%	90%	MAX	MODE

Where:

FREQ		is the frequency in question (in Hz)

MIN		is the minimum PSD value

AVE		is the average PSD value

50%		is the 50th percentile PSD value

90%		is the 90th percentile PSD value

MAX		is the maximum PSD value

MODE		is the mode PSD value (most common)

## PDFAnalysisSR.bin File

Definition:	Cumulative db-based .bin file holding overall PSD for julian day jjj.

Directory:	wrk

Internal Format:

- Data Format:	ASCII

- Individual lines each defining:

FREQ	POWER	PROB

Where:

FREQ		is the frequency (in Hz)

POWER	is the power bin (in dB)

PROB		is the number of hits for this bin

# Appendix II – Installation and Configuration Checklist

This appendix contains a table listing all of the required configuration parameters.  Please print this page, providing the appropriate values to be used.  Confirm that all values have been properly defined in the specified file(s).

| Config Parameter | Description | Where Specified | Value |
| --- | --- | --- | --- |
| PDFROOT | Root directory of PDF analysis system | PDF/.vars-user file |  |
| WEBDIR | Directory of .png files accessible from www | PDF/.vars-user file |  |
| RESPDIR | Directory containing response files | PDF/.vars-user file |  |
| DATAROOT | Root directory of miniseed data files | PDF/.vars-user file |  |
| STATSROOT | Root directory of PDF analysis results | PDF/.vars-user file |  |
| GMTROOT | GMT installation root directory | PDF/.vars-user file |  |
| IMROOT | ImageMagick installation root directory | PDF/.vars-user file |  |
| RESPDIR | Directory containing response files | PDF/src/vx.x.x/analysis/PDFuser.h |  |