Table of Contents

SECTION A – REQUIREMENTS AND PRICES	4

CONTRACT ACRONYMS	4

SCHEDULE OF SUPPLIES/SERVICES	5

A1  Item Requirement	5

A2  Item 1 Pricing	6

SECTION B – TECHNICAL SPECIFICATIONS	7

GENERAL REQUIREMENTS	7

B1   Scope of Contract	7

B2  Certifications	7

B3  Order of Precedence (Specifications)	7

B4   Contracts	7

EQUIPMENT REQUIREMENTS	7

B5   Condition of Equipment	7

B6  Aircraft Equipment Requirements	7

B7  Avionics Requirements	8

B8  Reserved	12

PERSONNEL REQUIREMENTS	12

B9  Pilot Requirements and Authority	12

B10   Pilot Qualifications	12

B11  Personnel  Duty  Limitations	13

B12  Flight Crewmembers Duty and Flight Limitations	13

B13  Relief Crew Requirement	13

OPERATIONS	13

B14  Pilot Authority and Responsibility	13

B15   Flight Operations	14

B16  Security of Aircraft and Equipment	14

B17  Personal Protective Equipment (PPE) for Flight Operations	15

B18  Exemption for Transportation of Hazardous Materials	15

B19  Fuel and Servicing Requirements	15

AIRCRAFT MAINTENANCE REQUIREMENTS	15

B20  General - Maintenance	15

B21  Airworthiness Directives (ADs) and Manufacturers Mandatory Service Bulletins (MMSBs)	16

B22  Manuals/Records	16

B23  Maintenance	16

B24  Maintenance Test Flight	16

B25  Time Between Overhaul (TBO) and Life-Limited Parts	16

B26   Weight and Balance	16

B27  Turbine Engine Power Assurance Checks (Turbine Engine Aircraft Only)	17

SECTION C – CONTRACT TERMS AND CONDITIONS	18

CONTRACT CLAUSES	18

C1  Contract Terms and Conditions – Commercial Items (52.212-4 OCT 2008) [Tailored SEPT 2005]	18

C2  Contract Terms and Conditions Required to Implement Statutes or Executive Orders-Commercial Items (52.212-5 OCT 2008)	20

ADDENDA TO CONTRACT TERMS AND CONDITIONS	23

C3  Inspection/Acceptance (52.212-4(a)), the following is added:	23

C4  Personal Identity Verification of Contractor Personnel (52.204-9 SEPT 2007)	24

C5   Availability of Funds (52.232-18 APR 1984)	24

C6  Aircraft Insurance	24

C7  Reserved	24

C8  Prework Meeting	24

C9 Authority of Government Representatives	24

ADMINISTRATIVE MATTERS	25

C10  Personnel Conduct	25

C11  Safety and Accident Prevention	25

C12  Mishaps	26

C13  Federal Airport and Airway Excise Taxes	27

C14   Economic Price Adjustment - Fuel	27

Fuel price obtained from: Million Air	27

CONTRACT PERIOD AND RENEWAL	28

C15  Contract Period	28

C16  Option to Extend the Term of the Contract (48 CFR 52.217-9, Mar 2000)	28

C17 Reserved	28

C18  Exclusive Use Period	28

C19   Mutual Extension of Exclusive Use Period	28

AVAILABILITY REQUIREMENTS	28

C20  Availability Requirements	28

C21  Schedule of Operations and Reaction Time	28

C22   Maintenance During Availability Period	29

C23  Unavailability and Damages	29

MEASUREMENT AND PAYMENT	29

C24  Daily Availability	29

C25  Flight Time	29

C26  Mobilization/Demobilization	29

C27  Additional Pay Items (from Schedule of Items)	30

C28  Government Miscellaneous Charges	31

BILLING AND REPORTING REQUIREMENTS	31

C29  Designated Agency Office and Payment Office	31

C30  Invoice Submissions	31

C31  Aircraft Use Report	31

C32  Contract Pricing	31

EXHIBITS	31

section d – instructions to offerors	40

INTRODUCTION	40

D1.  General Information	40

52.212-1 INSTRUCTIONS TO OFFERORS--COMMERCIAL ITEMS (JUN 2008) [Tailored]	40

D2 North American Industry Classification System (NAICS) Code and Small Business Size Standard	40

D3  Proposals	40

D4   Offer Contents	40

D5  Late Submissions, Modifications, Revisions, and Withdrawals of Offers	40

D6  Data Universal Numbering System (DUNS) Number)	40

D7  Special Notice to Offerors	41

EVALUATION OF PROPOSALS	41

D8  Offer Acceptability	41

D9  Evaluated Price	41

D10  Aircraft Capability	41

D11  Offeror Capability	41

D12  Tradeoff Analysis and Contractor Selection	42

D13  Notice of Award	42

section e – offeror’s representations, certifications and other statements	43

52.212-3 OFFEROR REPRESENTATIONS AND CERTIFICATIONS—COMMERCIAL ITEMS (JUN 2008)	43

SECTION E EXHIBITS	46

# SECTION A – REQUIREMENTS AND PRICES

# CONTRACT ACRONYMS

AC	Advisory Circular

AD	Airworthiness Directive

AMD	Aviation Management Directorate

A&P	airframe and power plant

APCO	Association of Public-Safety Communications Officials

ASM	Aviation Safety Manager

ASO	Aviation Safety Office

ASTM	American Society for Testing and Material

ATC	air traffic control

CFR	Code of Federal Regulations

CO	Contracting Officer

COR	Contracting Officer’s Representative

COTR	Contracting Officer’s Technical Representative

CFR	Code of Federal Regulations

CTCSS	continuous tone coded squelch system

DM	degrees/minutes/decimal minutes

DOI	Department of Interior

DOT	Department of Transportation

ELT	emergency locator transmitter

EPA	Environmental Protection Agency

ERG	Emergency Response Guidebook

FAA	Federal Aviation Administration

FAR	Federal Acquisition Regulations

FS	Forest Service

FTR	Federal Travel Regulations

GVW	gross vehicle weight

GPM	gallons per minute

GPS	global positioning system

HIGE	hover-in-ground effect

HOGE	hover-out-of-ground effect

IAT	interagency aviation training

ICAO	International Civil Aviation Organization

ICS	intercom system

IFR	instrument flight rules

IP	Institute of Petroleum

MMSB	Manufacturer’s Mandatory Service Bulletins

NBC	National Business Center

NFPA	National Fire Protection Association

NTSB	National Transportation Safety Board

NWCG	National Wildfire Coordinating Group

PA	public address system

PFD	personal flotation device

PIC	pilot-in-command

PPE	personal protective equipment

PSD	plastic sphere dispenser

PSI	pounds per square inch

PTT	push to talk

RFP	Request for Proposals

RPM	revolutions per minute

SFI	Safety Foundation Incorporated

STEP	Single-skid, Toe-In and Hover Exit/Entry Procedures

TBO	time between overhaul

TSO	technical service order

UL	Underwriter’s Laboratory

USDA	United States Department of Agriculture

VFR	visual flight rules

VNE	velocity never exceed

VOX	voice activation

VSWR	voltage standing wave ratio

# SCHEDULE OF SUPPLIES/SERVICES

## A1  Item Requirement

ITEM	DESCRIPTION

1 A1.	BID ITEMS

ITEM	DESCRIPTION

1-6.	Aircraft Requirement:		Twin-Engine, High Wing, IFR Airplane.

Crew Requirement For 		Pilot-in-Command (PIC), Relief PIC

Reporting Base:	Salt Lake City, UT: Runway length 16/34 – 12,000’, 17/35 – 9,596’, 14/32 – 4,892 Elevation 4,227’

Minimum Aircraft Characteristics:	--Seating for pilot plus three passengers, passenger seating removable for cargo hauling.

--Cruise speed of 165 knots True Air Speed (TAS) @ 8,000 ft -ISA plus 20 ºC

--Cruise endurance of 4 hours at 8,000 ft - ISA plus 20 ºC plus a 30-minute reserve.

--Payload of 780 pounds with fuel for 250 nautical miles plus VFR reserve @ 8,000 ft - ISA plus 20 ºC.

--Positive single engine rate of climb when equipped for the contract and carrying a pilot weighing 200 lb, one observer weighing 220 lb, fuel for 4 hours plus a 30-minute reserve, at 5,000 feet pressure altitude @ ISA plus 33 ºC.

Target Aircraft Characteristics:	--Turbine Powered.

--Cruise speed of 200 knots True Air Speed (TAS) @ 8,000 ft -ISA plus 20 ºC.

--Payload of 2,000 pounds with fuel for 250 nautical miles plus VFR reserve @ 8,000 ft - ISA plus 20 ºC.

--Minimum restrictions of outward visibility of the ground in level flight for the front seat observer and middle seat observer stations.

--Air conditioning.

--3 Panel-Mounted, Digital, Narrowband, VHF-FM Transceivers without Aux Port and Cable.

NOTE:  All Exhibits applicable to this solicitation are included at the end of Section C.

| ITEM X | VARIABLE PAY ITEMS | AMD-23 PAY ITEM CODE | QUANTITY | UNIT | LOWER 48 STATES UNIT PRICE |
| --- | --- | --- | --- | --- | --- |
| AC. | Extended Standby – Pilot | EP | INDEFINITE | HOUR | $ 47.00 |
| AD. | Subsistence Allowance | PD | INDEFINITE | Overnight | Per FTR Schedule |
| AE. | Contractor Miscellaneous Costs | SC | INDEFINITE | EACH | Actual Cost |

## A2  Item 1 Pricing

| DESIGNATED BASE Salt Lake City, UT | EXCLUSIVE USE PERIOD 90 calendar days | START DATE: June 07, 2009 (See C18.1) END DATE: September 04, 2009 |
| --- | --- | --- |

| OFFEROR NAME |  |
| --- | --- |
| AIRCRAFT FOR THIS PRICING SCHEDULE | Make/Model | FAA Registration # |

| ITEM | DESCRIPTION | PAY ITEM CODE | QUANTITY | UNIT | UNIT PRICE | EXTENDED AMOUNT |
| --- | --- | --- | --- | --- | --- | --- |
| 2009 1.AA. | 1st YEAR – 06/07/09 – 09/04/09 Price per day for availability | AV | 90 | DAYS | $ | $ |
| 1.AB. | Price per flight hour for estimated flight hours | FT | ESTIMATED 250 | FLIGHT HOURS | $ | $ |
| BASE YEAR – ESTIMATED TOTAL, AVAILABILITY AND FLIGHT HOURS – 1st year, 2009 | $ |
| 2010 2.AA. | 2nd YEAR - 06/07/10 – 09/04/10 Price per day for availability | AV | 90 | DAYS | $ | $ |
| 2.AB. | Price per flight hour for estimated flight hours | FT | ESTIMATED 250 | FLIGHT HOURS | $ | $ |
| 1st OPTION YEAR – ESTIMATED TOTAL, AVAILABILITY AND FLIGHT HOURS – 2nd YEAR, 2010 | $ |
| 2011 3.AA. | 3rd YEAR - 06/07/11 – 09/04/11 Price per day for availability | AV | 90 | DAYS | $ | $ |
| 3.AB. | Price per flight hour for estimated flight hours | FT | ESTIMATED 250 | FLIGHT HOURS | $ | $ |
| 2nd OPTION YEAR – ESTIMATED TOTAL, AVAILABILITY AND FLIGHT HOURS – 3RD YEAR, 2011 | $ |
| 2012 4.AA. | 4th YEAR - 06/07/12 – 09/04/12 Price per day for availability | AV | 90 | DAYS | $ | $ |
| 4.AB. | Price per flight hour for estimated flight hours | FT | ESTIMATED 250 | FLIGHT HOURS | $ | $ |
| 3rd OPTION YEAR – ESTIMATED TOTAL, AVAILABILITY AND FLIGHT HOURS – 4th YEAR, 2012 | $ |
| 2013 5.AA. | 5th YEAR - 06/07/13 – 09/04/13 Price per day for availability | AV | 90 | DAYS | $ | $ |
| 5.AB. | Price per flight hour for estimated flight hours | FT | ESTIMATED 250 | FLIGHT HOURS | $ | $ |
| 4th OPTION YEAR – ESTIMATED TOTAL, AVAILABILITY AND FLIGHT HOURS – 5th YEAR, 2013 | $ |
| ITEM 1 - ESTIMATED TOTAL PRICE – FIVE YEARS | $ |

# SECTION B – TECHNICAL SPECIFICATIONS

# GENERAL REQUIREMENTS

## B1   Scope of Contract

B1.1  The intent of this contract is to obtain fully Contractor operated and maintained exclusive use airplane flight services to transport personnel and/or cargo in support of Government missions.  Contractor services include provision of an airplane, personnel, fuel, and all other associated equipment as prescribed in this solicitation.  Missions are primarily in support of wildland fire management and may include, but are not limited to, air tactical supervision, fire detection, aerial reconnaissance, mapping, and other administrative and related resource activities.  The Government will direct aircraft to support its missions and objectives.

B1.2  The Government and Contractor must establish an effective working relationship to complete this contract successfully.  The Contractor’s employees’ cooperation, professionalism, and positive attitude toward aviation safety and accomplishment of the mission are an integral element of this relationship.

B1.3  The Government has interagency and cooperative agreements with other Federal and State agencies and private landholders and may dispatch aircraft under this contract for such cooperative use.

B1.4 During the exclusive use period and any subsequent extension, aircraft furnished shall be subject to the exclusive use and control of the Government 24 hours per day, seven days per  week.

## B2  Certifications

The Contractor must obtain and keep current all of the following required certificates and must ensure that contract aircraft are operated and maintained in compliance with those certificates at all times:

B2.1  A Title 14 of the Code of Federal Regulations (CFR) Part 135 Federal Aviation Administration (FAA) Air Carrier Certificate or Operating Certificate which authorizes the Contractor to operate in the category and class of aircraft and under flight conditions required by this contract (e.g., airplane, multiengine, visual flight rules (VFR), instrument flight rules (IFR), day/night, passengers, and cargo).

B2.2  The aircraft must be carried on the list required by 14 CFR Part 135.63 or Operations Specifications Part D, "Aircraft Listing," as appropriate.

B2.3 The contract aircraft must have a Standard Airworthiness Certificate.  Installation of any equipment required by this contract must be FAA approved.

## B3  Order of Precedence (Specifications)

In the event of inconsistencies within the technical specification, the following order will be used in such resolution:  (1) typed provisions of these specifications; (2) NBC AMD supplements and/or exhibits incorporated by reference; (3) 14 CFR incorporated by reference; (4) aircraft manufacturer's specifications; (5) other documents incorporated by reference.

## B4   Contracts

The Contractor must maintain a copy of the contract and all modifications in each contract aircraft throughout the performance period.

# EQUIPMENT REQUIREMENTS

## B5   Condition of Equipment

The Contractor-furnished aircraft and all other required equipment must be operable, free of damage, and in good repair.  Aircraft systems and components must be free of leaks, except where specified by the manufacturer.

B5.1  Prior to inspection and acceptance, the Contractor must permanently repair or replace all windows and windshields that have been temporarily repaired.  All windows and windshields must be maintained at all times and must be clean and free of scratches, cracks, crazing, distortion, repairs, or tinting which hinder visibility.

B5.2  The aircraft interior must be clean and neat with no unrepaired tears, rips, or other damage.  The exterior finish, including the paint, must be clean, neat, and in good condition.  Any corrosion must be within manufacturer or FAA acceptable limits.

B5.3   See the Unacceptable Lap Belt and Shoulder Harness Conditions Exhibit for lap belt and shoulder harness conditions that are not acceptable.

## B6  Aircraft Equipment Requirements

The Contractor must provide one fully compliant airplane that is equipped as shown below:

B6.1  A complete set of current aeronautical charts covering area of operations.

B6.2  One digital hour meter installed in a location visible by the pilot and front seat observer while seated.  The meter, comparable to a Hobbs meter measuring time-in-service in hours and tenths, activated by an air pressure switch, landing gear squat switch, or a 35 psi minimum oil pressure switch.  If an air pressure switch, it must be mounted forward of the propeller(s) or outboard of the propeller wash area in a position where the airflow from the propeller(s) is not sensed, to record flight time only.

B6.3  Free air temperature gauge.

B6.4  One set of individual lap belts for each installed seat.

B6.5  Shoulder harness with automatic or manual-locking inertia reel for each front seat occupant.  Shoulder straps and lap belts must fasten with one single-point, metal-to-metal, quick-release mechanism.  Heavy-duty (military-style) harnesses with fabric loop connecting the shoulder harness to the male portion of the lap belt buckle are acceptable.

B6.6  Fire extinguisher(s), as required by 14 CFR Part 135, must be a handheld bottle, minimum 2-B:C rating, mounted and accessible to the flight crew while seated. The fire extinguisher must be maintained in accordance with National Fire Protection Association (NFPA) 10: Standards for Portable Fire Extinguishers or the Contractor’s 135 operations manual.

B6.7  Dual controls for initial pilot performance evaluation.

B6.8  Aircraft lighting for night operation in accordance with 14 CFR Part 91.205(c), including instrument lights.

B6.9  A wing and tail strobe light system with an independent activating switch.

B6.10  High-visibility, pulsating, forward facing, conspicuity lighting.

B6.11  Cabin heater and window defogger.

B6.12  An accessory power source consisting of an MS 3112E-12-3S three-pin connector, accessible in the cabin.  Pin B must be airframe ground; pin A must be +28VDC (for 28-volt aircraft); and pin C must be +14VDC (for 14-volt aircraft).  The circuit must be protected by a 5-amp circuit protection.

B6.13  A first aid kit containing at least the items specified in the First Aid and Survival Kits Exhibit must be carried aboard the aircraft on all flights.

B6.14  A survival kit containing at least the items specified in the First Aid and Survival Kits Exhibit must be carried aboard the aircraft on all flights and must be included in weight and balance calculations.

B6.15  FAA-approved cargo restraints, cargo nets, and cargo straps for cargo tiedown in cabin and baggage compartment areas.

## B7  Avionics Requirements

B7.1  General

B7.1.1  The Contractor must provide, install, and maintain the following systems in accordance with the manufacturer's specifications and the installation and maintenance standards of Section B7.2.   Detailed avionics systems performance requirements are listed in Avionics Operational Test Standards (copies available upon request
from NBC AMD Avionics or at http://amd.nbc.gov/library/handbooks/aots.pdf).

B7.2  Avionics Installation and Maintenance Standards

B7.2.1  Strict adherence to the recommendations in FAA AC 43.13-1B Chapter 11, "Aircraft Electrical Systems," and Chapter 12, "Aircraft Avionics Systems," as well as AC 43.13-2A Chapter 1, "Structural Data," Chapter 2, "Radio Installation," and Chapter 3, "Antenna  Installation," is required.

B7.2.2  All avionics systems requiring an antenna must be installed with a properly matched, aircraft-certified antenna, unless otherwise specified.  Antennas must be polarized as required by the avionics system and must have a voltage standing wave ratio (VSWR) of 2.5 to 1 or better.

B7.2.3  The aircraft's static pressure system, altimeter instrument system, and automatic pressure altitude reporting system must be maintained in accordance with the IFR requirements of 14 CFR Part 91.411 and inspected and tested every 24 calendar months, as specified by 14 CFR Part 43, appendices E and F.

B7.2.4 Any “digital” aeronautical, mobile, or portable VHF-FM radios furnished to meet the requirements of this contract through December 31, 2009, must also be Association of Public-Safety Communications Officials (APCO) Project 25 (EIA/TIA-102) compliant.

B7.3   Communications Systems

B7.3.1 One automatic-portable/automatic-fixed or automatic-fixed emergency locator transmitter (ELT), certified to either Technical Standard Order (TSO)-C91a or TSO-C126, utilizing an external antenna and meeting the requirements of 14 CFR Part 91.207 (excluding section “e”). It must be installed in a conspicuous or marked location.

B7.3.2  Three panel-mounted VHF-AM (VHF-1, VHF-2, VHF-3) aeronautical transceivers, with at least two of the three units having a minimum of 760 channels covering 118.000 to 136.975 MHz and the other with a minimum of 720 channels covering the frequency range of 118.000 to 135.975 MHz, both with channels selectable in no greater than 25 kHz increments, and a minimum of 5 watts carrier output power, must be installed in the aircraft.  Each transceiver's operational controls must be mounted in a location which is readily visible and accessible to the pilot.

B7.3.3  Two VHF-FM multimode aeronautical transceiver(s) (FM-1/FM-2).  Each must provide selection of  both  narrowband (12.5 kHz) and wideband (25.0 kHz) bandwidth operation on each channel.  All frequencies must be used in the analog narrowband mode, unless the Government notifies the Contractor otherwise on a specific incident/project.

B7.3.3.1  Each transceiver’s operational frequency range must include the band of 150 to 174 MHz. The operator must be able to program any usable channels within that band while in flight.

B7.3.3.2  Each transceiver’s carrier output power must be 10 watts nominal value (original design specification). Each transceiver must be capable of displaying receiver and transmitter operating frequency and must provide both receiver and transmitter activation indicators for main and guard.  Simultaneous monitoring of both main (150-174 MHz) and guard (168.625 MHz) receivers is required. Single bandwidth guard receivers which operate in the wideband (25.0 kHz) mode are acceptable through December 31, 2009.   Scanning of the guard frequency is not acceptable.  The transceiver’s/encoder's operational controls must be located and arranged so that both the pilot and observer/copilot, when seated, have full and unrestricted movement of each control without interference from their clothing, the cockpit structure, or the flight controls.

B7.3.3.3  A Continuous Tone-Controlled Squelch System(s) (CTCSS) subaudible tone encoder (which may be an integral part of the transceiver), with the lowest 32 TIA/EIA-603 standard tone frequencies (from 67.0 to 203.5 Hz, less 69.3 Hz) being selectable, must be interfaced to each transceiver.

B7.3.3.4  Prior to performance under this contract, the transceiver/encoder system(s) must be programmed with Guard transmit and receive frequencies of 168.625 MHz, and a 110.9 Hz CTCSS tone on transmit only.   These values must remain programmed for the duration of performance under this contract.   The Guard channel must be constantly monitored prior to initial arrival on, during, and after departure from any Government project or incident.

B7.3.3.5  The following models of VHF-FM aeronautical transceivers are known to meet the above requirements, and are acceptable until December 31, 2009:

Eureka Radio ERS-96000NB w/external tone encoder

NAT (Northern Airborne Technology) NPX-136D (P-25 digital)

NAT (Northern Airborne Technology) NPX-138N-050

NAT(Northern Airborne Technology) NPX-138N-070

NAT(Northern Airborne Technology) NTX-138-050

Technisonics TFM-138 (serial number 1540 and up)

Technisonics TFM-138B/C/D, TFM-500 (all)

Technisonics TDFM-136 (P-25 digital) (all)

Wulfsberg  RT-5000/C-5000 with Guard option

Wulfsberg RT-9600N w/C-962A control head

Bendix-King/BK Radio model KFM-985 multimode transceivers do not meet the referenced requirements.

B7.3.3.6  Effective January 1, 2010, only “digital” VHF-FM radios which are APCO Project 25 (EIA/TIA-102) compliant will be acceptable on this contract.  The following models of VHF-FM aeronautical transceivers are known to meet those requirements:

NAT(Northern Airborne Technology) NPX-136D (P-25 digital)

Technisonics TDFM-136 (P-25 digital)

B7.3.3.6.1  Each digital VHF-FM radio furnished (both before and after January 1, 2010) must be equipped with a conveniently located programming port, which is protected from accidental damage via contact.  The ports must be hard-wired to each radio and must not require switching of any cables for utilization.  The Contractor must also furnish a cable, terminated in a standard USB plug and of adequate length, for connection of each port to a laptop computer.

B7.3.3.7  For Reno-Stead only. The Contractor must substitute a third VHF-FM aeronautical transceiver (FM-3) in lieu of the following AUX-FM requirements. FM-3 must meet the same requirements as specified above for the VHF-FM aeronautical transceivers (FM-1 and FM-2).

B7.3.4  Provisions for auxiliary VHF-FM (AUX-FM)  portable radio:

B7.3.4.1  An interface for installing and properly operating an auxiliary VHF-FM portable radio through the aircraft's audio control system(s).  The interface must consist of the appropriate wiring from the audio control system, terminated in an ITT/Cannon type MS3112E12-10S 10-pin connector conveniently located for use by the observer/copilot, and utilizing the contact assignments as specified by the FS/AMD Drawing A-17 Exhibit.

B7.3.4.2  One weatherproof, external, broadband antenna covering the 150-174 MHz band, with associated RG-58A/U (or equivalent) coaxial cable and connector, terminated in a bulkhead-mounted, female BNC connector (type UG-290A), conveniently located for use by the observer/copilot adjacent to the above 10-pin connector (Comant model CI-177 or equal).

B7.3.4.3  Mounting facilities for securely installing the auxiliary VHF-FM portable radio in the cockpit in accordance with the FAA AC 43.13-2A specifications. Locate and arrange the mounting facilities so that a seated observer/copilot has full and unrestricted movement of the radio's controls, without interference from the 18-inch adapter cable, clothing, cockpit structure, or flight controls.

B7.3.4.4  Positive-polarity microphone excitation voltage provided to the AUX-FM system from the aircraft DC power system through a suitable resistor network.  A blocking capacitor must be provided to prevent the portable radio microphone excitation voltage from entering the system.  Sidetone for the AUX-FM must also be provided (NAT model AA34-300, Premier model PA-34, or equivalent).

B7.3.4.5  For all items except Reno-Stead referenced in B7.3.3.7 above. The Contractor may substitute one VHF-FM aeronautical transceiver (FM-3) which meets the requirements for the VHF-FM aeronautical transceivers (FM-1 and FM-2), as detailed above, in lieu of the above AUX-FM requirements.

B7.3.5  One Automated Flight Following (AFF) system compatible with the Government’s AFF tracking network (Webtracker) is required.  Not all available AFF systems are compatible with Webtracker nor meet Webtracker’s requirements.  The Contractor must ensure that the AFF system offered is compatible with Webtracker.  To view Webtracker’s current compatibility requirements, refer to https://www.aff.gov.

B7.3.5.1  The AFF system must be powered by the aircraft’s electrical system, installed per the manufacturer’s installation manual, and operational in all phases of flight.  AFF equipment must utilize as a minimum: satellite communications, provide data to the Government’s Webtracker software, use aircraft power via a dedicated circuit breaker for power protection, and be mounted so as to not endanger any occupant from AFF equipment during periods of turbulence.  Any AFF manufacturer-required pilot display(s) or control(s) must be visible/selectable by the pilot(s).  Remote equipment having visual indicators should be mounted in such a manner as to allow visual indicators to be easily visible.

B7.3.5.2  AFF communications must be fully operational in the lower 48 States.  Contractors accepting dispatches to the State of Alaska, Southern Canada, or Western Canada must have an AFF system capable of being tracked in these locations at all times.  Not all manufacturers’ AFF equipment communication links will operate effectively in all geographic areas.

B7.3.5.3  The Contractor must maintain a subscription service through the AFF equipment provider allowing AFF position reporting for satellite tracking via Webtracker.  The position-reporting interval must be every 2 minutes while the aircraft is in flight.  The Contractor must register their AFF equipment with the Fire Applications Help Desk (FAHD) providing: complete tail number, manufacturer and serial number of the AFF transceiver; aircraft make and model; and Contractor contact information.  If the Contractor relocates previously registered AFF equipment into another aircraft, then the Contractor must contact the FAHD making the appropriate changes prior to aircraft use.  In all cases, the Contractor must ensure that the correct aircraft information is indicated within Webtracker.  The Contractor must contact the FAHD of system changes, scheduled maintenance, and planned service outages.

B7.3.5.4  Registration contact information, a Web-accessible feedback form, and additional information are available at https://www.aff.gov.  The FAHD can be reached at (800) 253-5559 or (208) 387-5290.

B7.3.5.5  Prior to the aircraft’s annual contract inspection, the Contractor must ensure compliance with all AFF systems requirements.  The Contractor must additionally perform an operational check of the system.  As a minimum, the operational check must consist of confirming the aircraft being tested is displayed in Webtracker (indicating it is currently transmitting data to Webtracker) and that all information displayed in Webtracker is current.  A username and password are required to access Webtracker.  Log on to the AFF website at https://www.aff.gov to request a username and password, or contact the FAHD.  When the aircraft passes the operational check, an aircraft logbook entry must be made.

B7.3.5.6  This clause incorporates Specification Section Supplement available at https://www.aff.gov/contractspecs with the same force and effect as if it were presented as full text herein.

B7.4   Navigational Systems

B7.4.1  One permanently installed, panel-mounted Global Positioning System (GPS). The GPS must utilize the WGS-84 datum, reference latitude and longitude coordinates in the degrees/minutes/decimal minutes (DM) mode for aircraft positioning, utilize an approved, fixed, external aircraft antenna, and be powered by the aircraft electrical system.  The GPS installation must be FAA approved (or approval pending). Handheld and/or marine-type equipment is not acceptable.

B7.4.1.1  A GPS data port connector must be installed for the purposes of external data retrieval by a GIS laptop computer from the above GPS.  The connector must be a DB-9F type D sub-connector, must be wired for RS-232C serial format for laptop computers (pin 2=transmit data, pin 3=receive data [if applicable], and pin 5=ground), and must be mounted in a location convenient to the front seat observer.  The Contractor must also furnish a cable, terminated in a standard USB plug and of adequate length, for ease of connection of the data port to a laptop computer.

B7.5  Audio Systems

B7.5.1  Two separate audio control systems (which may be combined in a single unit) must be provided for the pilot and ATGS/copilot in a location convenient to both.  Additionally, a third audio control system must be provided at the aft cabin training station.  Each of the three systems must provide the operator with separate controls for selection of receiver audio outputs and transmitter microphone/PTT audio inputs for all installed radios and PA systems.  Each system must also provide the operator with separate controls for adjustment of both the intercommunications system (ICS) and the receiver audio output levels.

B7.5.1.1 Transmitter selection and operation.  Separate transmitter selection controls must be provided for the microphone/PTT inputs of each operator.  The systems must be configured so that the operators may each simultaneously select and utilize a different transmitter (or PA system if installed) via their respective microphone/PTT.  Whenever a transmitter is selected, the companion receiver audio must automatically be selected for the corresponding earphone.  Transmitter sidetone audio must be provided for the user as well as for cross-monitoring via the corresponding receiver selection switch on the other audio control system.

B7.5.1.2  Receiver selection and operation.  Separate controls must be provided for each operator’s   selection of audio from one or any combination of available receivers.  The receiver audio output must be free of excessive distortion, hum, noise and crosstalk and must be amplified sufficiently to facilitate ease of use in a noisy cockpit/cabin environment.

B7.5.1.3  The controls of each audio system must be located and arranged so that both the operators, when seated, have full and unrestricted movement of each control without interference from their clothing, the cockpit structure, or the flight controls.  Labeling and marking of controls must be clear, understandable, legible, and permanent. Electronic labelmaker marking is acceptable.

B7.5.2  An ICS must be provided for the pilot, ATGS/copilot, the training station, and one other aft seat passenger positions.  ICS audio must mix with, but not mute, selected receiver audio.  An ICS audio level control must be provided for each position above.  Adjustment of the ICS audio level at any position must not affect the level at any other position.  A "hot mic" capability, controlled via voice activation [VOX], must be provided for each position above.  ICS sidetone audio must be provided for the earphones corresponding with the microphone in use.  The ICS audio output must be free of excessive distortion, hum, noise, and crosstalk, and must be amplified sufficiently to facilitate ease of use in a noisy cockpit/cabin environment.

B7.5.3  Earphones, microphones, PTTs, and jacks designed for operation with 600-ohm earphones and carbon-equivalent, noise-canceling boom type microphones (Gentex electret type Model 5060-2, military dynamic type M87/AIC with CE-100 TR preamplifier, or equivalent) must be furnished at all required positions.

B7.5.3.1  J-033 and J-034 type connector jacks must be provided at all required positions in the aircraft to accept the PJ-055B and PJ-068 type connector plugs as utilized with the headset/ microphone.

B7.5.3.2  Separate PTT switches must be provided for radio transmitter microphone operation at the pilot, ATGS/copilot, and training station positions.  The pilot's PTT switch must be mounted on the control yoke.  The PTT switches for the ATGS/copilot and training station positions must be mounted on the cord to the headset/microphone connector, or otherwise conveniently located for use; however, PTT switches for the ATGS/copilot, other than those mounted on the flight controls, must be furnished.

B7.6  Other Avionics

B7.6.1  One air traffic control (ATC) transponder and altitude reporting system meeting the requirements of 14 CFR Part 91.215 (a) and (b).

B7.6.2  The aircraft must be equipped with an FAA Technical Standard Order (TSO) -approved traffic awareness and avoidance system (TCAS/TAS/TCAD/etc.) featuring active interrogation of threat aircraft. The system must be equipped with antennas mounted on both the top and bottom of the aircraft to minimize airframe shadowing and provide 360-degree coverage. The system must also incorporate visual alerts for both pilot and copilot and an aural alerting feature which announces an alert of threat aircraft whenever such aircraft enter a zone of a programmable size with range selections from no more than 2 nautical miles to at least 10 nautical miles around the aircraft. The audio alert output must be interconnected to the aircraft's audio system in such a manner that all ICS-equipped positions will receive the alert. If the aircraft is equipped with a multi-function display (MFD), GPS, or other system capable of displaying threat aircraft output data, the system must be also be interfaced to such.

B7.6.2.1  The system must be installed in accordance with an STC or FAA Field Approval based upon an existing STC and the manufacturer’s installation manual.  Installation of the system must be accomplished by a certified avionics repair station which has been approved for such by the system’s manufacturer.  The system must be maintained for continued airworthiness, but may be listed in an approved minimum equipment list (MEL), provided the MEL does not permit the system to be inoperable for a period exceeding 15 days.

B7.6.2.2  The following systems are known to meet the above requirements:

TCAS:  Any TSO’d system which provides a range selection of 2 nautical miles or less.

TAS:  Bendix-King KTA 870, Goodrich Skywatch HP

TCAD:  Avidyne TAS600 (formerly Ryan International TCAD 9900BX) only when a separate, approved multi-function display (MFD) is used to display threat aircraft data.

## B8  Reserved

# PERSONNEL REQUIREMENTS

## B9  Pilot Requirements and Authority

The Contractor must furnish a pilot for each day the aircraft is required to be available. The pilot shall have the authority to represent the Contractor in all matters except changes in price and time, unless the Contracting Officer (CO) is notified otherwise, in writing, prior to performance.

## B10   Pilot Qualifications

B10.1 General.

Pilot flight hours will be verified from a certified pilot log. Further verification of flight hours may be required at the COTR's discretion.

B10.2  Minimum Qualifications.

The Contractor must provide a pilot(s) who meets the following minimum qualifications and who possesses the required certificates or evidence of having satisfactorily passed the evaluations for the required tasks:

B10.2.1  An FAA commercial pilot certificate or higher with airplane single engine and/or multiengine instrument ratings.

B10.2.2  A minimum of a current second-class medical certificate issued in accordance with 14 CFR Part 67.

B10.2.3  An FAA competency check completed in accordance with 14 CFR Part 135.293 in the same make and model as the contract aircraft including single pilot IFR.  This flight check must be valid for the contract exclusive use and postseason period.

B10.2.4  Proficient operation of all equipment identified in Section B (e.g., aircraft and FM radios, GPS).  The agencies may require pilots to demonstrate this proficiency during an evaluation flight.

B10.2.5  Pilots must have logged minimum flying time as pilot-in-command (PIC) as follows:

(a) 1,500 hours…total pilot time.

(b) 1,200 hours…PIC in airplanes.

(c) 200 hours…category and class to be flown.

(d) 100 hours…night flying to include the recent flight experience requirements of Federal Aviation Regulation (FAR) 61.57(d).

(e) 75 hours… actual or simulated instrument flight time (including 50 hours in flight).

(f) 500 hours… cross-country.

(g) 200 hours… over typical (hazardous/mountainous) terrain and landing facilities.

(h) 25 hours…total time in make, model, and series of aircraft to be used.

(i) 5 hours…total time in make and model, in preceding 30 days.

(j) 10 hours…total time in class, in preceding 60 days.

(k) 100 hours…total time in class, in preceding 12 months.

B10.2.6  The Contractor must submit an experience resume for each pilot offered for approval.  The resume must include the names and pilot addresses of past employers, substantiation of related type and typical terrain flying, and any and all accidents involving aircraft.  The information must be submitted on form AMD-64A or FS 5700-20, Airplane Pilot Qualifications and Approval (with supplements if requested).

B10.2.7  Mountain/remote airstrips:  Pilots flying missions to USFS Category 4 mountain/remote airstrips must have successfully passed an evaluation ride given by a qualified Forest Service pilot inspector into a minimum of two typical mountain/remote airstrips and must have a mountain/remote airstrip endorsement on their Interagency Airplane Pilot Qualification Card.  Prior to dispatching a pilot into a mountain/remote airstrip, the Contractor will brief the pilot on the hazards associated with the airstrip and verify that the pilot meets initial, recurrent, and 12-month specific mountain/remote airstrip requirements.  Individual national forests may have specific requirements for a particular airstrip.  The appropriate dispatch office should be contacted to obtain current airstrip information.  Before dispatching an aircraft into a Category 4 airstrip, a pilot must meet
special requirements and the mission must be
coordinated with the local Forest.
See USDA Forest Service Airfield/Airstrip Directory website http://www.fs.fed.us/fire/aviation/av_library/AAD2000.pdf

B10.2.7.1 Category 4 mountain/remote airstrips are restricted by the Forest Service to day VFR flight only.  Use authorization must be obtained from the appropriate dispatch office.  Pilots must have an endorsement on their Interagency Airplane Pilot Qualification Card and meet specific currency requirements in accordance with the USDA Forest Service Airfield/Airstrip Directory.

B10.2.7.2  The Contractor must provide the CO a list of Category 4 mountain/remote airstrips for which each pilot is authorized.  Airstrips, which are approved for Forest Service use, are identified within the USDA Forest Service Airfield/Airstrip Directory.

B10.2.8  An additional pilot (second-in-command (SIC)) may be required on aircraft engaged in IFR missions.  Pilots in addition to the PIC must meet the following requirements:

## B11  Personnel  Duty  Limitations

The Contractor must monitor and remove from duty any personnel for fatigue or other causes before they reach their daily duty or flight limitations.

## B12  Flight Crewmembers Duty and Flight Limitations

B12.1  Assigned duty of any kind must not exceed 14 hours in any 24-hour period.  Duty includes flight time, ground duty of any kind, and standby.  Local travel up to a maximum of 30 minutes each way between the worksite and place of lodging will not be considered duty time.  Flight crewmembers must be subject to the following duty hour limitations:

B12.1.1  A maximum of 14 consecutive duty hours during any assigned duty period.

B12.1.1.1  The pilot must be given 2 calendar days of rest (off duty) within any 14 consecutive calendar days.

B12.1.1.2  The pilot must be given a minimum of 10 consecutive hours of rest (off duty) prior to any assigned duty period.

B12.2   Flight limitations.

B12.2.1  Each crewmember must report all flight time, regardless of how or where performed, except personal pleasure flying.  Crewmembers and relief crewmembers reporting for duty may be required to furnish a record of all duty and/or flight time during the previous 14 days.  This record will be used to administer flight and duty time limitations.

B12.2.2  Flight time to and from a duty station as a flight crewmember (commuting) must be reported and counted toward limitations if it is flown on a duty day.  Flight time includes but is not limited to military flight time, charter, flight instruction, 14 CFR Part 61.56 flight review, flight examinations by FAA designees, any flight time for which a flight crewmember is compensated, or any other flight time of a commercial nature whether compensated or not.

B12.2.3  Pilot flight time computations will be computed in accordance with 14 CFR Part 1.1.

B12.2.4  Flight crewmembers are limited to the following restrictions that fall within their duty hour limitations:

B12.2.4.1   A maximum of 8 hours flight time during any assigned duty period.

B12.2.4.2   When a pilot acquires 36 or more flight hours in a consecutive 6-day period, the pilot must be given the following 1 calendar day off duty for rest, after which a new 6-day cycle will begin.   Maximum cumulative flight time must not exceed 42 hours during any consecutive 6-day period.

B12.3  Federal agencies may issue a notice reducing one or more of the following:  the assigned duty period, maximum flight hours, length of personnel duty days.  The notice issued may also increase number of days off and may be issued either for a specific geographic area or on an agency-wide basis.

## B13  Relief Crew Requirement

B13.1  The Contractor must provide a qualified relief crew, consisting of a pilot, that is available to perform duties during the regular crewmember’s scheduled days off.

B13.2  The Contractor must provide a planned schedule of relief duty days to the Contracting Officer’s Representative (COR) at the start of the exclusive use period.  Relief crewmembers must arrive at the designated base before the scheduled duty period begins to ensure compliance with rest periods set forth herein.

# OPERATIONS

## B14  Pilot Authority and Responsibility

The Contractor must ensure that the pilot is responsible for (1) operating the aircraft within its operating limits, (2) the safety of the aircraft, (3) its occupants, and (4) the cargo.

The contract pilot:

B14.1  Must comply with Government directions except, when in the pilot's judgment, such compliance would violate Federal or State regulations or contract terms and conditions.  The pilot has final authority to determine whether the flight can be accomplished safely and must refuse any flight or landing that is considered hazardous or unsafe.

B14.2  Must not permit any passenger to ride in the aircraft or any cargo to be loaded therein unless authorized by the CO or their authorized representative.

B14.3  Must be responsible for computing the aircraft’s weight and balance for all flights and for ensuring that the gross weight and center of gravity do not exceed the aircraft's limitations.  The pilot must also properly secure all cargo.

B14.4  Must perform takeoff performance calculations which include:

a.	Takeoff distance required vs. runway available.

- Climb performance to include single engine if operating a multiengine aircraft.

Under no circumstances will a takeoff be attempted if existing environmental conditions at takeoff cannot be accurately addressed in the aircraft flight manual (AFM) or pilot’s operating handbook (POH).

B14.5  May perform preventive maintenance in accordance with 14 CFR Part 43.3(h) or with the Contractor’s operational specifications, as appropriate.

B14.6  May function as a mechanic when the aircraft is not available due to required maintenance provided that:

B14.6.1  The pilot has met all of the mechanic qualifications and experience requirements specified herein.

B14.6.2  Any time that the pilot is engaged in mechanic duties will apply against the pilot's duty limitations.  All time in excess of 2 hours (not necessarily consecutive) will apply against the pilot's flight limitations.

B14.6.3  The pilot will not accomplish scheduled maintenance such as 50- and 100-hour inspections.

## B15   Flight Operations

Regardless of any status as a public aircraft operation, the Contractor must operate in accordance with their approved FAA operations specifications and all portions of 14 CFR Part 91 (including those portions applicable to civil aircraft) and each certification required under Section B2 unless otherwise authorized by the CO.  The Contractor must ensure that all personnel operate in compliance with the following requirements:

B15.1  Manifesting.  The PIC must ensure that a manifest of all crewmembers and passengers on board has been completed and that a copy of this manifest remains at the  appropriate dispatch office.  Manifest changes must be made with that office.

B15.2   Passenger briefings.  Before each takeoff, the PIC must ensure that all passengers have been briefed in accordance with 14 CFR Part 135.  Briefings for short flights do not need to be repeated unless new passengers come aboard.  The briefing must describe the location/use of the following:

a.   Emergency locator transmitter

b.   First aid/survival kits

c.   Personal protective equipment

d.   Takeoff and climb performance

B15.3  The pilot must brief the occupant of a pilot position to remain clear of the flight controls at all times.

B15.4  Day/night use.  Both day and night flight may be required by this contract.

B15.4.1 Night/IFR operations.  Only multiengine and single engine turbine aircraft are approved for transporting passengers at night or in instrument meteorological conditions.  Pilots flying night missions must not land at an airport unless it meets Federal Aviation Administration (FAA) airport lighting standards.

B15.5  Flight plans.  Pilots must file and operate on an FAA, International Civil Aviation Organization (ICAO), or agency (DOI bureau or USDA-FS) flight plan.  Contractor flight plans are not acceptable.  Flight plans must be filed prior to takeoff when possible.

B15.6  Flight following.  Pilots are responsible for flight following with the FAA, ICAO, and/or in accordance with the agency’s (DOI bureau or USDA-FS) approved procedures.

B15.7  Smoking will not be allowed in or around the aircraft.

B15.8  The pilot must remain at the flight controls while the engine(s) are running.

B15.8.1  Prior to passenger or cargo loading/unloading, all engines must be shut down and all propellers must have ceased rotation.

## B16  Security of Aircraft and Equipment

The Contractor is responsible for the security of their contract aircraft, vehicles, and associated equipment at all times.

B16.1  Physical Security.  Any aircraft used under this contract must be physically secured and disabled via a dual-lock method whenever the aircraft is unattended.  Any combination of two different antitheft devices designed to lock aircraft flight control surfaces when not in use or designed to secure an aircraft to the ground is acceptable provided the devices are appropriate for the aircraft.  Operational environments and personnel safety must be considered when selecting the locking devices and methods to be used.

B16.1.1  Removal and/or disabling of locking devices and methods must be incorporated into preflight checklists to prevent accidental damage to the aircraft.  The devices must be installed in a manner that precludes their inadvertent interference with in-flight operations.

B16.1.2  Using other means of securing or disabling an aircraft is acceptable, provided it achieves a level of security equal to or greater than the following example locking devices and methods:

Keyed magneto

Keyed starter switch

Keyed master power switch

Hidden battery cutoff switches

Hidden start relay switches

Throttle/power lever lock

Mixture/fuel lever lock

Locking fuel cutoff

Locking tiedown cable

Unacceptable locking devices and methods are:

Locking aircraft doors

Fenced or gated parking area

## B17  Personal Protective Equipment (PPE) for Flight Operations

The Contractor must provide and require personnel to wear PPE for flight operations.  The following PPE must be operable and maintained in accordance with the manufacturer’s instructions throughout contract performance.

B17.1  Contractor personnel shall wear full length trousers made of cotton or fire-resistant polyamide or aramid material or equal (a flight suit is considered equal). Contractor personnel shall wear boots or shoes made of all-leather uppers.

## B18  Exemption for Transportation of Hazardous Materials

The Contractor may be required to transport hazardous materials.  Such transportation must be in accordance with 49 CFR, DOT exemption DOT-SP-9198, and the DOI/USFS Interagency Aviation Transport of Hazardous Materials Handbook/Guide.

B18.1   A copy of the current exemption, handbook, and DOT Emergency Response Guidebook (ERG) must be carried aboard each aircraft transporting hazardous materials.

B18.2  The Contractor must ensure that each employee who may perform a function subject to this DOT exemption receives required training that can only be satisfied by completing Interagency Aviation Training (IAT) module A-110, Aviation Transportation of Hazardous Materials.  The training can be completed online at http://www.iat.gov.  The Contractor must document this training in the employee’s records and make it available to the Government when requested.

Note: The DOT exemption and the DOI handbook are available online at http://amd.nbc.gov.  The Contractor is responsible for obtaining the DOT Emergency Response Guidebook.

## B19  Fuel and Servicing Requirements

B19.1  General

B19.1.1  The Contractor must supply all fuel and lubricating oils required to operate all equipment during the contract period. All fuel must be commercial (or military) grade aviation fuel approved for use by the airframe and engine manufacturer.  Only fuels meeting American Society for Testing and Material (ASTM) or military specifications are authorized for use.  ASTM D-1655 (Jet A, A-1, or B), Mil T-5624 (JP-4, JP-8, JP-5), ASTM-D-910, or Mil T-910 (grade 80, 100, or 100LL).

B19.1.2 Contractors must ensure that fuel obtained from distributors or fixed-base operators (FBO) meets the specifications of B19.  The Contractor must keep the fuel delivery ticket through the period.

B19.2  Operations.  The Contractor must ensure that:

B19.2.1 Government personnel are not on board the aircraft during refueling operations.

B19.2.2   Government personnel are not involved with refueling of contract aircraft unless the pilot has determined that it is an absolute necessity due to an emergency situation.

B19.2.3   Smoking is prohibited within 50 feet of the aircraft and fuel servicing vehicles.

B19.2.4  Cell phone use is prohibited within 50 feet of the aircraft during fueling operations.

# AIRCRAFT MAINTENANCE REQUIREMENTS

## B20  General - Maintenance

The Contractor must ensure that the aircraft and all required equipment are operated and maintained in accordance with the manufacturer's specifications.

## B21  Airworthiness Directives (ADs) and Manufacturers Mandatory Service Bulletins (MMSBs)

B21.1  The Contractor must comply with MMSBs and FAA ADs before and during contract performance.

B21.2  The Contractor must provide and make available a list of FAA ADs applicable to the contract aircraft in a format similar to that in AD 43-9 as revised.

## B22  Manuals/Records

B22.1  The Contractor must ensure that all contract aircraft maintenance is recorded in accordance with 14 CFR Parts 43, 91, and 135 (reference 14 CFR Parts 43.9, 43.11, 91.417, and 135.439) and that a copy of the aircraft's record is kept with the aircraft.

B22.2  If requested by the Government, the Contractor must furnish to the COTR a copy of the Contractor's procedures manuals as outlined in 14 CFR Part 135.21 along with any revisions made during the contract period.

B22.3   Before the start date of the contract, the Contractor must ensure that all maintenance deficiencies have been corrected or deferred in accordance with the operator's accepted/approved maintenance program.  Deferred discrepancies will be evaluated and the aircraft approved for contract use on a case-by-case basis.  In accordance with the appropriate Federal Aviation Regulations (FAR) or the approved maintenance program, the Contractor must correct deficiencies that occur during contract performance.

## B23  Maintenance

B23.1  All maintenance including inspection, rebuilding, alteration, and installation must be accomplished by a person authorized to perform maintenance in accordance with 14 CFR Part 43.

B23.2   The Contractor must ensure that a mechanic who meets the contract qualification requirements inspects the contract aircraft in accordance with the procedures outlined in the operator’s FAA-approved/accepted maintenance program.  Aircraft time-in-service must be recorded.

B23.3  Routine maintenance must be performed before or after the daily use or as approved by the COR.

## B24  Maintenance Test Flight

B24.1  The Contractor must, at their own expense, perform a functional maintenance checkflight following installation, overhaul, major repair, or replacement of any engine, propeller, or flight control system or when requested by the CO.  This must be accomplished before the aircraft resumes service under the contract.

B24.2  The Contractor must immediately notify the COR and COTR of any change to any engine, propeller, flight control, or major airframe component or of any major repair following an incident or accident and must describe the circumstances involved.

## B25  Time Between Overhaul (TBO) and Life-Limited Parts

B25.1  All components, including engines, must be replaced upon reaching the factory-recommended TBO or FAA-approved extension.  Life-limited parts must be replaced at the specified time-in-service hours or cycles.

B25.2  Aircraft operated with components or accessories on approved TBO extension programs are acceptable provided (1) the Contractor is the holder of the approved extension authorization (not the owner if the aircraft is leased) and (2) the Contractor operates in accordance with the extension authorization.

B25.3   The Contractor must supply at the time of the initial agency inspection a list of all items installed on the aircraft that are required to be overhauled or replaced on a specified time basis.  This list must include the component’s name, part number, serial number, total time, service life (or inspection/overhaul time interval), and time and date when component was overhauled, replaced, or inspected.

## B26   Weight and Balance

B26.1  The aircraft's required weight and balance data must be determined by actual weighing of the aircraft within 24 calendar months preceding the starting date of the contract or renewal period and following any major repair, major alteration, or change to the equipment list which significantly affects the center of gravity of the aircraft.

B26.2  All aircraft must be weighed on scales that have been certified as accurate within the preceding 24 calendar months.  Any accredited weights and measures laboratory may serve as the certifying agency.

B26.3  The Contractor must compile a list of equipment installed in the aircraft at the time of weighing.  Each page of the equipment list must identify the specific aircraft by its serial and registration numbers and must be dated to indicate the last date of weighing or computation.  Items that may be easily removed or installed for aircraft configuration changes (seats, radios, special mission equipment, etc.) must also be listed including the name, the weight, and the arm of each item.  The weight and balance must be revised each time new equipment is installed or old equipment is removed.    Weight and balance procedures under 14 CFR Parts 23.29 and 23.1589 are acceptable.

## B27  Turbine Engine Power Assurance Checks (Turbine Engine Aircraft Only)

On the first day of operation and no more than each 10 hours of operation thereafter, the Contractor must perform a power assurance check in accordance with the flight manual (pilot’s operating handbook) or approved company performance monitoring program.  The results must be recorded and kept with the aircraft.  Engines with power output below minimum approved limits must be removed from contract use until the condition is corrected.

# SECTION C – CONTRACT TERMS AND CONDITIONS

# CONTRACT CLAUSES

## C1  Contract Terms and Conditions – Commercial Items (52.212-4 OCT 2008) [Tailored SEPT 2005]

(SEE ADDENDA WHICH FOLLOWS IMMEDIATELY AFTER CLAUSE 52.212-5)

(a) Inspection/Acceptance. The Contractor shall only tender for acceptance those items that conform to the requirements of this contract. The Government reserves the right to inspect or test any supplies or services that have been tendered for acceptance. The Government may require repair or replacement of nonconforming supplies or reperformance of nonconforming services at no increase in contract price.   If repair/replacement or reperformance will not correct the defects or is not possible, the Government may seek an equitable price reduction or adequate consideration for acceptance of nonconforming supplies or services. The Government must exercise its post-acceptance rights (1) within a reasonable time after the defect was discovered or should have been discovered; and (2) before any substantial change occurs in the condition of the item, unless the change is due to the defect in the item.

(b) Assignment. The Contractor or its assignee's may assign its rights to receive payment due as a result of performance of this contract to a bank, trust company, or other financing institution, including any Federal lending agency in accordance with the Assignment of Claims Act (31 U.S.C. 3727).  However, when a third party makes payment (e.g., use of the Governmentwide commercial purchase card), the Contractor may not assign its rights to receive payment under this contract.

(c) Changes. Changes in the terms and conditions of this contract may be made only by written agreement of the parties.

(d) Disputes. This contract is subject to the Contract Disputes Act of 1978, as amended (41 U.S.C. 601-613). Failure of the parties to this contract to reach agreement on any request for equitable adjustment, claim, appeal or action arising under or relating to this contract shall be a dispute to be resolved in accordance with the clause at FAR 52.233-1, Disputes, which is incorporated herein by reference. The Contractor shall proceed diligently with performance of this contract, pending final resolution of any dispute arising under the contract.

(e) Definitions. The clause at FAR 52.202-1, Definitions, is incorporated herein by reference.

(f) Excusable delays. The Contractor shall be liable for default unless nonperformance is caused by an occurrence beyond the reasonable control of the Contractor and without its fault or negligence such as, acts of God or the public enemy, acts of the Government in either its sovereign or contractual capacity, fires, floods, epidemics, quarantine restrictions, strikes, unusually severe weather, and delays of common carriers. The Contractor shall notify the CO in writing as soon as it is reasonably possible after the commencement of any excusable delay, setting forth the full particulars in connection therewith, shall remedy such occurrence with all reasonable dispatch, and shall promptly give written notice to the CO of the cessation of such occurrence.

(g) Invoice.

(1) The Contractor shall submit an original invoice and three copies (or electronic invoice, if authorized,) to the address designated in the contract to receive invoices. An invoice must include--

(i) Name and address of the Contractor;

(ii) Invoice date and number;

(iii) Contract number, contract line item number and, if applicable, the order number;

(iv) Description, quantity, unit of measure, unit price and extended price of the items delivered;

(v) Shipping number and date of shipment, including the bill of lading number and weight of shipment if shipped on Government bill of lading;

(vi) Terms of any discount for prompt payment offered;

(vii) Name and address of official to whom payment is to be sent;

(viii) Name, title, and phone number of person to notify in event of defective invoice; and

(ix) Taxpayer Identification Number (TIN).  The Contractor shall include its TIN on the invoice only if required elsewhere in this contract.

(x) Electronic funds transfer (EFT) banking information.

(A)  The Contractor shall include EFT banking information on the invoice only if required elsewhere in this contract

(B) If EFT banking information is not required to be on the invoice, in order for the invoice to be a proper invoice, the Contractor shall have submitted correct EFT banking information in accordance with the applicable solicitation provision, contract clause (e.g., 52.232-33, Payment by Electronic Funds Transfer -Central Contractor Registration, or 52.232-34, Payment by Electronic Funds Transfer-Other Than Central Contractor Registration), or applicable agency procedures

(C)  EFT banking information is not required if the Government waived the requirement to pay by EFT.

(2) Invoices will be handled in accordance with the Prompt Payment Act (31 U.S.C. 3903) and Office of Management and Budget (OMB) prompt payment regulations at 5 CFR part 1315.

(h) Patent indemnity. The Contractor shall indemnify the Government and its officers, employees and agents against liability, including costs, for actual or alleged direct or contributory infringement of, or inducement to infringe, any United States or foreign patent, trademark or copyright, arising out of the performance of this contract, provided the Contractor is reasonably notified of such claims and proceedings.

- Payment. –

- Items accepted. Payment shall be made for items accepted by the Government that have been delivered to the delivery destinations set forth in this contract.

- Prompt Payment. The Government will make payment in accordance with the Prompt Payment Act (31 U.S.C. 3903) and prompt payment regulations at 5 CFR part 1315.

- Electronic funds transfer (EFT). If the Government makes payment by EFT, see 52.212-5(b) for the appropriate EFT clause.

- Discount. In connection with any discount offered for early payment, time shall be computed from the date of the invoice. For the purpose of computing the discount earned, payment shall be considered to have been made on the date which appears on the payment check or the specified payment date if an electronic funds transfer payment is made.

- Overpayments. If the Contractor becomes aware of a duplicate contract financing or invoice payment or that the Government has otherwise overpaid on a contract financing or invoice payment, the Contractor shall --

(i) Remit the overpayment amount to the payment office cited in the contract along with a description of the overpayment including the-

(A) Circumstances of the overpayment (e.g., duplicate payment, erroneous payment, liquidation errors, date(s) of overpayment);

(B)  Affected contract number and delivery order number, if applicable;

(C) Affected contract line item or subline item, if applicable; and

(D) Contractor point of contact.

(ii) Provide a copy of the remittance and supporting documentation to the Contracting Officer.

(6) Interest. (i)  All amounts that become payable by the Contractor to the Government under this contract shall bear simple interest from the date due until paid unless paid within 30 days of becoming due.  The interest rate shall be the interest rate established by the Secretary of the Treasury as provided in Section 611 of the Contract Disputes Act of 1978 (Public Law 95-563), which is applicable to the period in which the amount becomes due, as provided in (i)(6)(V) of this clause, and then at the rate applicable for each six-month period as fixed by the Secretary until the amount is paid.

(ii) The Government may issue a demand for payment to the Contractor upon finding a debt is due under the contract.

(iii) Final decisions.  The Contracting Officer will issue a final decision as required by 33.211 if –

(A) The Contracting Officer and the Contractor are unable to reach agreement on the existence or amount of a debt within 30 days;

(B) The Contractor fails to liquidate a debt previously specified in the demand for payment unless the amounts were not repaid because the Contractor has requested an installment payment agreement; or

(C) The Contractor requests a deferment of collection on a debt previously demanded by the Contracting Officer (see 32.607-2).

(iv) If a demand for payment was previously issued for the debt, the demand for payment included in the final decision shall identify the same due date as the original demand for payment.

(v) Amounts shall be due at the earliest of the following dates:

(A) The date fixed under this contract.

(B) The date of the first written demand for payment, including any demand for payment resulting from a default termination.

(vi) The interest charge shall be computed for the actual number of calendar days involved beginning on the due date and ending on—

(A)The date on which the designated office receives payment from the Contractor;

(B) The date of issuance of a Government check to the Contractor from which an amount otherwise payable has been withheld as a credit against the contract debt; or

(C) The date on which an amount withheld and applied to the contract debt would otherwise have become payable to the Contractor.

(vii) The interest charge made under this clause may be reduced under the procedures prescribed in 32.608-2 of the Federal Acquisition Regulation in effect on the date of this contract.

(j) Risk of loss.  Unless the contract specifically provides otherwise, risk of loss or damage to the supplies provided under this contract shall remain with the Contractor until, and shall pass to the Government upon:

- Delivery of the supplies to a carrier, if transportation is f.o.b. origin; or

- Delivery of the supplies to the Government at the destination specified in the contract, if transportation is f.o.b. destination.

(k) Taxes. The contract price includes all applicable Federal, State, and local taxes and duties.

(l) Termination for the Government's convenience. The Government reserves the right to terminate this contract, or any part hereof, for its sole convenience. In the event of such termination, the Contractor shall immediately stop all work hereunder and shall immediately cause any and all of its suppliers and subcontractors to cease work. Subject to the terms of this contract, the Contractor shall be paid a percentage of the contract price reflecting the percentage of the work performed prior to the notice of termination, plus reasonable charges the Contractor can demonstrate to the satisfaction of the Government using its standard record keeping system, have resulted from the termination. The Contractor shall not be required to comply with the cost accounting standards or contract cost principles for this purpose. This paragraph does not give the Government any right to audit the Contractor's records. The Contractor shall not be paid for any work performed or costs incurred which reasonably could have been avoided.

(m) Termination for cause. The Government may terminate this contract, or any part hereof, for cause in the event of any default by the Contractor, or if the Contractor fails to comply with any contract terms and conditions, or fails to provide the Government, upon request, with adequate assurances of future performance. In the event of termination for cause, the Government shall not be liable to the Contractor for any amount for supplies or services not accepted, and the Contractor shall be liable to the Government for any and all rights and remedies provided by law.  If it is determined that the Government improperly terminated this contract for default, such termination shall be deemed a termination for convenience.

(n) Title.  Unless specified elsewhere in this contract, title to items furnished under this contract shall pass to the Government upon acceptance, regardless of when or where the Government takes physical possession.

(o)  Warranty.  The Contractor warrants and implies that the items delivered hereunder are merchantable and fit for use for the particular purpose described in this contract.

(p) Limitation of liability. Except as otherwise provided by an express warranty, the Contractor will not be liable to the Government for consequential damages resulting from any defect or deficiencies in accepted items.

(q) Other compliances. The Contractor shall comply with all applicable Federal, State and local laws, executive orders, rules and regulations applicable to its performance under this contract.

(r) Compliance with laws unique to Government contracts. The Contractor agrees to comply with 31 U.S.C. 1352 relating to limitations on the use of appropriated funds to influence certain Federal contracts; 18 U.S.C. 431 relating to officials not to benefit; 40 U.S.C 3701, et seq., Contract Work Hours and Safety Standards Act; 41 U.S.C. 51-58, Anti-Kickback Act of 1986; 41 U.S.C. 265 and 10 U.S.C. 2409 relating to whistleblower protections; 49 U.S.C 40118, Fly American; and 41 U.S.C. 423 relating to procurement integrity.

(s) Order of precedence. Any inconsistencies in this

solicitation or contract shall be resolved by giving precedence in the following order: (1) the schedule of supplies/services; (2) the Assignments, Disputes, Payments, Invoice, Other Compliances, and Compliance with Laws Unique to Government Contracts paragraphs of this clause; (3) the clause at 52.212-5; (4) addenda to this solicitation or contract, including any license agreements for computer software; (5) solicitation provisions if this is a solicitation; (6) other paragraphs of this clause; (7) the Standard Form 1449; (8) other documents, exhibits, and attachments; and (9) the specification.

(t) Central Contractor Registration (CCR).

(1) Unless exempted by an addendum to this contract, the Contractor is responsible during performance and through final payment of any contract for the accuracy and completeness of the data within the CCR database, and for any liability resulting from the Government's reliance on inaccurate or incomplete data. To remain registered in the CCR database after the initial registration, the Contractor is required to review and update on an annual basis from the date of initial registration or subsequent updates its information in the CCR database to ensure it is current, accurate and complete. Updating information in the CCR does not alter the terms and conditions of this contract and is not a substitute for a properly executed contractual document.

(2)(i) If a Contractor has legally changed its business name, "doing business as" name, or division name (whichever is shown on the contract), or has transferred the assets used in performing the contract, but has not completed the necessary requirements regarding novation and change-of-name agreements in FAR Subpart 42.12, the Contractor shall provide the responsible Contracting Officer a minimum of one business day's written notification of its intention to (A) change the name in the CCR database; (B) comply with the requirements of Subpart 42.12; and (C) agree in writing to the timeline and procedures specified by the responsible Contracting Officer. The Contractor must provide with the notification sufficient documentation to support the legally changed name.

(ii) If the Contractor fails to comply with the requirements of paragraph (q)(2)(i) of this clause, or fails to perform the agreement at paragraph (q)(2)(i)(C) of this clause, and, in the absence of a properly executed novation or change-of-name agreement, the CCR information that shows the Contractor to be other than the Contractor indicated in the contract will be considered to be incorrect information within the meaning of the "Suspension of Payment" paragraph of the electronic funds transfer (EFT) clause of this contract.

(3) The Contractor shall not change the name or address for EFT payments or manual payments, as appropriate, in the CCR record to reflect an assignee for the purpose of assignment of claims (see Subpart 32.8, Assignment of Claims). Assignees shall be separately registered in the CCR database. Information provided to the Contractor's CCR record that indicates payments, including those made by EFT, to an ultimate recipient other than that Contractor will be considered to be incorrect information within the meaning of the "Suspension of payment" paragraph of the EFT clause of this contract.

(4) Offerors and Contractors may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov or by calling 1-888-227-2423 or 269-961-5757.

## C2  Contract Terms and Conditions Required to Implement Statutes or Executive Orders-Commercial Items (52.212-5 OCT 2008)

(a) The Contractor shall comply with the following Federal Acquisition Regulations (FAR) clauses, which are incorporated in this contract by reference, to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1)   52.233-3, Protest after Award (AUG 1996) (31 U.S.C. 3553).

(2)  52.233-4, Applicable Law for Breach of Contract Claim (OCT 2004) Public L. 108-77, 108-78)

(b) The Contractor shall comply with the FAR clauses in this paragraph (b) that the Contracting Officer has indicated as being incorporated in this contract by reference to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1) 52.203-6, Restrictions on Subcontractor Sales to the Government (SEPT 2006), with Alternate I (SEPT 2006) (41 U.S.C. 253g and 10 U.S.C. 2402).

(2) 52.219-3, Notice of Total HUBZone Small Business Set-Aside (JAN 1999) (15 U.S.C 657a).

(3) 52.219-4, Notice of Price Evaluation Preference for HUBZone Small Business Concerns (JULY 2005) (if the offeror elects to waive the preference, it shall so indicate in its offer) (15 U.S.C. 657a).

(4 [Reserved]

(5) (i)52.219-6, Notice of Total Small Business Set-Aside (JUNE 2003)(15 U.S.C. 644).

(ii) Alternate I (OCT 1995) of 52.219-6.

(iii) Alternate II (MAR 2004) of 52.219-6.

(6)(i) 52.219-7, Notice of Partial Small Business Set-Aside (JUNE 2003)(15 U.S.C. 644).

(ii) Alternate I (OCT 1995) of 52.219-7.

(iii) Alternate II (MAR 2004 of 52.219-7.

(7) 52.219-8, Utilization of Small Business Concerns (MAY 2004)(15 U.S.C. 637 (d)(2) and (3)).

(8)(i) 52.219-9, Small Business Subcontracting Plan (NOV 2007)(15 U.S.C. 637(d)(4).

(ii)Alternate I (OCT 2001) of 52.219-9.

(iii) Alternate II (OCT 2001) of 52.219-9.

(9) 52.219-14, Limitations on Subcontracting (DEC 1996) (15 U.S.C. 637(a)(14).

(10)(i) 52.219-16, Liquidated Damages – Subcontracting Plan (JAN 1999) (15U.S.C. 637(d)(4)(F)(i).

(11)(i) 52.219-23, Notice of Price Evaluation Adjustment for Small Disadvantaged Business Concerns (OCT 2008)(10 U.S.C. 2323) (if the offeror elects to waive the adjustment, it shall so indicate in its offer).

(ii) Alternate I (JUNE 2003)of 52.219-23.

(12) 52.219-25, Small Disadvantaged Business Participation Program-Disadvantaged Status and Reporting (OCT 1999)(Pub. L. 103-355, section 7102, and 10 U.S.C. 2323).

(13) 52.219-26, Small Disadvantaged Business Participation Program-Incentive Subcontracting (OCT 2000) (Pub. L. 103-355, section 7102, and 10 U.S.C. 2323).

(14) 52.219-27, Notice of Total Service-Disabled Veteran-Owned Small Business Set-Aside (MAY 2004) (15 U.S.C. 657f).

(15) 52.219-28, Post Award Small Business Program Representation (JUNE 2007) (15 U.S.C. 632(a)(2).

(16) 52.222-3, Convict Labor (JUNE 2003)(E.O. 11755).

(17) 52.222-19, Child Labor-Cooperation with Authorities and Remedies (FEB 2008)(E.O. 13126).

(18) 52.222-21, Prohibition of Segregated Facilities (Feb 1999).

(19) 52.222-26, Equal Opportunity (MAR 2007)(E.O. 11246).

(20) 52.222-35, Equal Opportunity for Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212).

(21) 52.222-36, Affirmative Action for Workers with Disabilities (JUN 1998) (29 U.S.C. 793).

(22) 52.222-37, Employment Reports on Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212).

(23)(i) 52.222-39, Notification of Employee Rights Concerning Payment of Union Dues or Fees (DEC 2004)(E.O. 13201).

(24)(i) 52.222-50, Combating Trafficking in Persons (AUG 2007) (Applies to all contracts).

(ii) Alternate I (AUG 2007) of 52.222-50

(25)(i) 52.223-9, Estimate of Percentage of Recovered Material Content for EPA-Designated Products (AUG 2000)(42 U.S.C. 6962(c)(3)(A)(ii)).

(ii) Alternate I (AUG 2000) of 52.223-9 (42 U.S.C. 6962(i)(2)(C)).

(26) 52.223-15, Energy Efficiency in Energy-Consuming Products (DEC 2007)(42 U.S.C. 8259b).

(27) 52.223-16, IEEE 1680 Standard for the Evironmental Assessment of Personal Computer Products (DEC 2007)(E.O. 13423).

(28) 2.225-1, Buy American Act-Supplies (JUNE 2003)(41 U.S.C. 10a - 10d).

(29)(i) 52.225-3, Buy American Act - Free Trade Agreements-Israeli Trade Act (AUG 2007) (41U.S.C. 10a - 10d, 19U.S.C. 3301 note, 19U.S.C. 2112 note, Pub. L. 108-77, 108-78, 108-286,  109-53 and 109-169).

(ii) Alternate I (JAN 2004) of 52.225-3.

(iii) Alternate II (JAN 2004) of 52.225-3.

(30) 52.225-5, Trade Agreements (NOV 2007)(19 U.S.C. 2501, et seq., 19 U.S.C. 3301 note).

(31) 52.225-13, Restriction on Certain Foreign Purchases (JUNE 2008) (E.O’s, proclamations and statutes administered by the Office of Foreign Assets Control of the Department of the Treasury).

(32)  52.226-4, Notice of Disaster or Emergency Area Set-Aside (NOV 2007) (42 U.S.C. 5150).

(33) 52.226-5, Restrictions on Subcontracting Outside Disaster or Emergency Area (NOV 2007) (42.U.S.C. 5150)

(34) 52.232-29, Terms for Financing of Purchases of Commercial Items (FEB 2002)(41 U.S.C. 255(f), 10 U.S.C. 2307(f)).

(35) 52.232-30, Installment Payments for Commercial Items (OCT 1995)(41 U.S.C. 255(f), 10 U.S.C. 2307(f)).

(36) 52.232-33, Payment by Electronic Funds Transfer-Central Contractor Registration (OCT 2003)(31 U.S.C. 3332).

(37) 52.232-34, Payment by Electronic Funds Transfer-Other than Central Contractor Registration (MAY 1999)(31 U.S.C. 3332).

(38) 52.232-36, Payment by Third Party (MAY 1999)(31 U.S.C. 3332).

(39) 52.239-1, Privacy or Security Safeguards (AUG 1996)(5 U.S.C. 552a).

(40)(i) 52.247-64, Preference for Privately Owned U.S.-Flag Commercial Vessels (FEB 2006)(46 U.S.C. Appx 1241 and 10 U.S.C. 2631).

(ii) Alternate I (APR 2003) of 52.247-64.

(c) The Contractor shall comply with the FAR clauses in this paragraph (c), applicable to commercial services, which the Contracting Officer has indicated as being incorporated in this contract by reference to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1) 52.222-41, Service Contract Act of 1965 (NOV 2007)(41 U.S.C. 351, et seq.).

(2) 52.222-42, Statement of Equivalent Rates for Federal Hires (MAY 1989)(29 U.S.C. 206 and 41 U.S.C. 351, et seq.).  (See Exhibits)

(3) 52.222-43, Fair Labor Standards Act and Service Contract Act-Price Adjustment (Multiple Year and Option Contracts) (NOV 2006) (29 U.S.C. 206 and 41 U.S.C. 351, et seq.).

(4) 52.222-44, Fair Labor Standards Act and Service Contract Act-Price Adjustment (FEB 2002)(29 U.S.C. 206 and 41 U.S.C. 351, et seq.).

(5) 52.222-51, Exemption from Application of the Service Contract Act to Contracts for Maintenance, Calibration, or Repair of Certain Equipment – Requirements (NOV 2007) (41 U.S.C. 351, et seq.).

(6) 52.222-53, Exemption from Application of the Service Contract Act to Contracts for Certain Services – Requirements (NOV 2007) (41U.S.C. 351, et seq.).

(7) 52.237-11, Accepting and Dispensing of $1 Coin (SEPT 2008) (31U.S.C. 5112(p)(1)).

(d) Comptroller General Examination of Record. The Contractor shall comply with the provisions of this paragraph (d) if this contract was awarded using other than sealed bid, is in excess of the simplified acquisition threshold, and does not contain the clause at 52.215-2, Audit and Records-Negotiation.

(1) The Comptroller General of the United States, or an authorized representative of the Comptroller General, shall have access to and right to examine any of the Contractor's directly pertinent records involving transactions related to this contract.

(2) The Contractor shall make available at its offices at all reasonable times the records, materials, and other evidence for examination, audit, or reproduction, until 3 years after final payment under this contract or for any shorter period specified in FAR Subpart 4.7, Contractor Records Retention, of the other clauses of this contract. If this contract is completely or partially terminated, the records relating to the work terminated shall be made available for 3 years after any resulting final termination settlement. Records relating to appeals under the disputes clause or to litigation or the settlement of claims arising under or relating to this contract shall be made available until such appeals, litigation, or claims are finally resolved.

(3) As used in this clause, records include books, documents, accounting procedures and practices, and other data, regardless of type and regardless of form. This does not require the Contractor to create or maintain any record that the Contractor does not maintain in the ordinary course of business or pursuant to a provision of law.

(e)(1) Notwithstanding the requirements of the clauses in paragraphs (a), (b), (c) and (d) of this clause, the Contractor is not required to flow down any FAR clause, other than those listed in paragraphs (i) through (vii) of this paragraph in a subcontract for commercial items. Unless otherwise indicated below, the extent of the flow down shall be as required by the clause –

(i) 52.219-8, Utilization of Small Business Concerns (MAY 2004)(15 U.S.C. 637 (d)(2) and (3)), in all subcontracts that offer further subcontracting opportunities. If the subcontract (except subcontracts to small business concerns) exceeds $550,000 ($1,000,000 for construction of any public facility), the subcontractor must include 52.219-8 in lower tier subcontracts that offer subcontracting opportunities.

(ii) 52.222-26, Equal Opportunity (MAR 2007)(E.O. 11246);

(iii) 52.222-35, Equal Opportunity for Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212);

(iv) 52.222-36, Affirmative Action for Workers with Disabilities (JUNE 1998)(29 U.S.C. 793);

(v) 52.222-39, Notification of Employees Rights Concerning the Payment of Union Dues or Fees (DEC 2004)(E.O. 13201);

(vi) 52.222-41, Service Contract Act of 1965 (NOV 2007) (41 U.S.C. 351, et seq.).

(vii) 52.222-50, Combating Trafficking in Persons (AUG 2007) (22 U.S.C. 7104(g)).  Flow down required in accordance with paragraph (f) of FAR clause 52.222-50.

(viii) 52.222-51, Exemption from Application of the Service Contract Act to Contracts for Maintenance, Calibration, or Repair of Certain Equipment – Requirements (NOV 2007) (41U.S.C. 351, et seq.).

(ix) 52.222-53, Exemption from Application of the Service Contract Act to Contracts for Certain Services – Requirements (NOV 2007) (41U.S.C. 351, et seq.).

(x) 52.247-64, Preference for Privately Owned U.S.- Flag Commercial Vessels (FEB 2006)(46 U.S.C. Appx 1241 and 10 U.S.C. 2631). Flow down required in accordance with paragraph (d) of FAR clause 52.247-64).

(2) While not required, the contractor may include in its subcontracts for commercial items a minimal number of additional clauses necessary to satisfy its contractual obligations.

# ADDENDA TO CONTRACT TERMS AND CONDITIONS

## C3  Inspection/Acceptance (52.212-4(a)), the following is added:

C3.1 Inspection Scheduling and Process

C3.1.1  After either contract award or renewal, the COTR will schedule a date to inspect the Contractor's proposed aircraft, equipment and personnel to ensure contract compliance.  The inspection will be conducted at the designated base, Contractor's facility or other location acceptable to the Government.  The inspection will be scheduled to commence as early as 60 days and not later than three days (excluding weekends and holidays) prior to the established reporting date, unless otherwise mutually agreed upon by the COTR and the Contractor.  The inspection time and date will be scheduled for between 0730 and 1630 local time, Monday through Friday, unless otherwise agreed upon by the COTR.  The COTR will confirm the inspection details in writing.  Contractor written requests for inspection rescheduling that are received by the COTR at least 10 days prior to the originally scheduled inspection date may be accommodated by the COTR, depending upon their work schedule.

C3.1.2 The Contractor must provide information specific to the aircraft, equipment, and personnel being proposed for use during each year of the contract when requested by the COTR.

C3.1.3  Approved aircraft and pilots will be issued an Interagency Aircraft Data Card, or Interagency Pilot Qualification card, as applicable.  The aircraft and pilot cards detail the activities for which they are authorized.

C3.1.3.1  The aircraft data card is kept in the aircraft and available for inspection at all times.

C3.1.3.2  The pilot qualification card is kept in the possession of the pilot and available for inspection at all times.

C3.1.4  If the COTR determines any aircraft/equipment/personnel and records/documents presented for inspection are not completely ready for the inspection or are determined to be nonconforming as required by the contract, the COTR may suspend the inspection(s) and schedule a reinspection for another time/date/site.  The Contractor may be charged for the cost of reinspection, in accordance with Section C3.5.

C3.2 Equipment

C3.2.1  The aircraft will be inspected to ensure compliance with all contract requirements. The Government may require in-flight dynamic testing of aircraft systems.  This testing may be conducted in conjunction with pilot evaluation flight(s), and  will be performed at no cost to the Government.

C3.3  Personnel

C3.3.1  Pilots.  Only those individuals whose past flight time and experience can be verified from log books, employment records, etc., will be approved for contract use. The Contractor cannot substitute any pilot flight evaluation time for any of the total pilot flight hour requirements listed in this contract

C3.3.2  The COTR will conduct a pilot flight evaluation to further verify pilot(s)' ability to perform under this contract, when determined necessary.  The evaluation may include but is not limited to:  weight and balance performance, center of gravity limitations, aircraft performance charts, density altitude considerations, load calculation preparation and actual flying of the aircraft.  Portions of the evaluation may be evaluated orally.  A pilot must also be capable of demonstrating proficient operation of all aircraft equipment identified in Section B during an evaluation flight.

C3.3.2.1  The aircraft used for the evaluation(s) must be the same make, model, and series awarded for this contract and be equipped with dual controls.  Flight evaluation(s) will usually be performed in areas that provide access to terrain similar to that to be flown during the contract period.  Flight evaluations are conducted at the Contractor’s expense.

C3.3.2.2  During the flight evaluation, pilot inspectors retain discretionary authority in determining the competency of the pilot and may add, delete, or revise elements of the flight evaluation to determine competency.  The Government will make the final determination as to the pilot’s ability to successfully meet contract requirements.

C3.3.3  Services provided under this contract require DOI special use flight activities as identified herein.  Pilots must have satisfactorily completed an agency initial and/or periodic flight evaluation(s) for these activities before being approved for use under the contract, unless otherwise indicated in the contract.  The COTR will provide detailed information concerning the types and frequency of special use pilot flight evaluations when requested.

Low-level flight (within 500’ of the surface)

Resource reconnaissance

Fire reconnaissance

Air tactical group supervision (airplane only)

C3.4  Substitute Personnel, Aircraft, or Equipment

C3.4.1   The Contractor may request the use of substitute personnel, aircraft, or equipment that was not initially approved for use.  All proposed substitutes must meet pertinent contract specifications and be subject to inspections and approvals identified herein prior to use.   The Contractor must submit a written request for inspections of substitutes to the COTR seven days prior to the scheduled arrival at the site.  Requests received with fewer than seven days’ notice will be accomplished as permitted by the COTR’s schedule.  The Government may charge the Contractor for the cost of any substitute inspections in accordance with Section C3.5

C3.4.2   The Contractor must transport substitute personnel, aircraft, or equipment to the point of use at their expense.

### C3.4.3  The bureau may require substitute pilots to obtain up to three hours each of training or orientation flight time at Contractor's expense.  (This flight time is in addition to any necessary pilot evaluation flight(s)).

C3.5  Reinspection Expenses

C3.5.1  The Contractor must be liable for all Government incurred reinspection costs.  Inspection expenses may be deducted from payments due the Contractor.

C3.5.2  Costs may include, but are not limited to, inspector(s)’ time to include travel time at $75.00 per hour, and transportation and subsistence at actual cost.

## C4  Personal Identity Verification of Contractor Personnel (52.204-9 SEPT 2007)

(a) The Contractor shall comply with agency personal identity verification procedures identified in the contract that implement Homeland Security Presidential Directive-12 (HSPD-12), Office of Management and Budget (OMB) guidance M-05-24, as amended, and Federal Information Processing Standards Publication (FIPS PUB) Number 201.

(b) The Contractor shall insert this clause in all subcontracts when the subcontractor is required to have routine physical access to a Federally-controlled facility and/or routine access to a Federally-controlled information system.

C4.1  Contractor Personnel Security Requirements

C4.1.1  It has been determined that Contractor personnel utilized in the support of this contract will not be allowed routine and regular unsupervised access to a federally controlled facility for more than 180 days, nor will they need unsupervised access to a Federally controlled Level 3 or 4 information system.

C4.1.2  Contractor employees utilized in support of this contract, will be treated as visitors (uncredentialed Contractor) and not be required to receive background investigations and credentialing. However, uncredentialed Contractors may be subject to the screening processes utilized at each federally controlled facility where the Contractor services are required.  As a minimum, Contractor employees will be issued a temporary/visitor badge and shall display it at all times during contract performance when accessing a federally controlled facility.  The COR is responsible for ensuring that all Contractor employees are issued a temporary/visitor badge.

## C5   Availability of Funds (52.232-18 APR 1984)

Funds are not presently available for this contract.  The Government’s obligation under this contract is contingent upon the availability of appropriated funds from which payment for contract purposes can be made.  No legal liability on the part of the Government for any payment may arise until funds are made available to the Contracting Officer for this contract and until the Contractor receives notice of such availability, to be confirmed in writing by the Contracting Officer.

## C6  Aircraft Insurance

The Contractor must maintain as a minimum, aircraft insurance coverage required by 14 CFR, Part 205, during contract performance.

## C7  Reserved

## C8  Prework Meeting

A prework meeting between the Government and the Contractor along with their primary crew members is typically held at or near the starting designated base and is usually in conjunction with the start of the exclusive use period.  The Contractor’s primary crew members must attend any prework meeting that is scheduled.  The meeting may include, but is not limited to:  (1) review of the contract in detail; (2) operational procedures (dispatch, flight following, hazard/risk assessment and reduction, airspace coordination, incident/accident reporting, etc.; and  (3) review of the local base procedures.

## C9 Authority of Government Representatives

C9.1  Contracting Officer (CO)

The CO is the appointed Government official with authority to enter into, administer and terminate this contract.  No one but the CO is authorized under any circumstances to:

C9.1.1  Award, agree to, or execute any contract, contract modification, or notice of intent.

C9.1.2  Obligate in any way the payment of money by the Government.

C9.1.3  Make a final decision on any contract matter that is subject to the Disputes clause of this contract.

C9.1.4  Terminate, for any cause, the Contractor's right to proceed.

C9.2  Contracting Officer's Technical Representative (COTR)

The COTR is authorized to take any or all actions necessary to ensure compliance with the technical portions of the contract.  The COTR will conduct all requested or required inspections.

The COTR for this contract is:

Mr. Stew Walker

DOI – Aviation Management

East Area Office

3190 NE Expressway, Suite 110

Atlanta, Georgia 30341-5323

Phone:	770-458-7474

Fax:	770-458-6677

The DOI – Aviation Management Aviation Safety Manager (ASM) is responsible for all matters concerning accident and incident with potential investigations.  The ASM is:

Mr. Robert Galloway

DOI – Aviation Management

300 E. Mallard Drive, Suite 200

Boise, ID 83706-3991

Phone:	208-433-5071

Fax:	208-433-5007

C9.3 Contracting Officer's Representative (COR)

The COR is authorized to take any or all actions with respect to administrative functions.

The COR for this contract is:

Mr. Cameron Dingman

BLM Utah State Office

PO Box 45155

Salt Lake City,  84145-0155

Phone:	801-539-4241

Fax:	801-539-4198

# ADMINISTRATIVE MATTERS

## C10  Personnel Conduct

C10.1  Replacement of Contractor Personnel

### C10.1.1  Contractor employees required to work or reside on Federal property (National Parks, Refuges, Indian Reservations, etc.) are expected to follow the facility manager’s rules of conduct that apply to both Government or non-Government personnel working or residing at these facilities.  The COR will make available a copy of such rules. The Contractor may be required to replace employees who do not comply with these rules of conduct.

C10.1.2  The Contractor must replace any employee who performs unsafely, ineffectively; refuses to cooperate; is unable or unwilling to adapt to field living conditions; or whose general performance is unsatisfactory, disruptive or detrimental to the purpose for which contracted.

C10.1.3  The CO will notify the Contractor of all known unsatisfactory personnel conduct or unsafe performance.  The employee may be afforded an opportunity for corrective action when the conditions warrant.  When directed by the CO, the Contractor must replace unacceptable personnel not later than 24 hours after such notification, or as otherwise mutually agreed. The decision as to unacceptability will be at the sole discretion of the CO.

C10.2  Suspension of Pilot

C10.2.1  Upon receipt of written correspondence which indicates a serious safety concern, the Government may suspend the pilot.

C10.2.2  Upon involvement in an Aircraft Accident or National Transportation Safety Board (NTSB) Reportable Incident (see 49 CFR Part 830), a pilot will be suspended from pilot duties and from any other activity authorized under the Interagency Pilot Qualification card(s), pending the investigation outcome.

C10.2.3  Upon involvement in an Incident with Potential as defined under Mishaps, a pilot may be suspended from pilot duties and from any other activity authorized under the Interagency Pilot Qualification card(s), pending the investigation outcome.

C10.2.4  When requested, a suspended pilot must surrender all Interagency Pilot Qualification card(s) to the COTR or other authorized agency representative.  Pilot suspension will continue until the investigation findings and decision indicate no further suspension is required and the Interagency Pilot Qualification card(s) is returned to the pilot;  or revoked by the issuing agency.

## C11  Safety and Accident Prevention

C11.1  The Contractor must submit a copy of all reports required by the Federal Aviation Regulations that relate to pilot and maintenance personnel performance, aircraft airworthiness or operations to the Aviation Safety Manager (ASM).

C11.1.1  Examples of these reports are shown in paragraphs 14 CFR Part 135.415 Mechanical Reliability Reports and Part 135.417 Mechanical Interruption Summary Reports required of the Federal Aviation Regulations, 49 CFR Part 830.5 and 49 CFR 830.15, and FAA Form 8010-4, Malfunction or Defect Report.

C11.2  Following a mishap, the CO will evaluate whether the Contractor was in compliance with contract provisions or with the Federal Aviation Regulations applicable to the Contractor's operations, company policy, procedures, practices, or programs, or whether there was negligence on the part of the company officers or employees that may have caused or contributed to the mishap.  The Contractor must fully cooperate with the CO during this evaluation.

C11.3  The Contractor must develop  and maintain programs necessary to ensure safe practices during ground and flight operations.  These programs are a material part of contract performance.

C11.3.1  Examples of such programs are (1) personnel activities, (2) maintenance, (3) safety, and (4) compliance with regulations.

## C12  Mishaps

C12.1  Mishap Definitions

As used throughout this contract, the following terms will have the meanings set forth below.

C12.1.1  The following terms are as defined in 49 CFR Part 830:

Aircraft Accident

Fatal Injury

Incident.

Operator

Serious Injury

Substantial Damage

C12.1.2  Airspace Conflict.  A near mid-air collision, intrusion, or violation of airspace rules.

C12.1.3  Aviation Hazard.  Any condition, act, or set of circumstances that exposes an individual to unnecessary risk or harm during aviation operations.

C12.1.4  Incident with Potential.  An incident that narrowly misses being an accident and in which the circumstances indicate significant potential for substantial damage or serious injury.  Classification of an incident as an "Incident with Potential" is determined by the agency ASM.

C12.1.5  Maintenance Deficiency.  An equipment defect or failure which affects or could affect the safety of operations, or that causes an interruption to the services being performed.

C12.1.6  SafeCom.  An agency Aviation Safety Communique used to report any condition, observance, act, maintenance problem, or circumstance which has potential to cause an aviation related accident (Form AMD-34 or FS 5700-14).

C12.2  Mishap Reporting

The Contractor must immediately, and by the most  expeditious means available, notify the NTSB AND the agency ASM when an "Aircraft Accident" or NTSB reportable "Incident" occurs.

C12.2.1  The ASM must immediately be notified when an "Incident with Potential" occurs.

C12.2.2  The toll free 24-hour Interagency Aircraft Accident Reporting Hot Line number is:

1-888-4MISHAP (1-888-464-7427)

C12.3  Forms Submission

C12.3.1  Following an "Aircraft Accident" or when requested by the NTSB following notification of a reportable "Incident," the Contractor must provide the agency ASM with information necessary to complete a NTSB Form 6120.1/2 “Pilot/Operator Aircraft Accident Report”.

C12.3.2  The Contractor must submit a "SafeCom" to the agency ASM within 5 days upon the occurrence of any condition, observance, act, maintenance problem, or  circumstance which has potential to cause an aviation-related mishap. Submission via the internet at  http://www.safecom.gov/ is preferred.  Blank SafeComs can be obtained from agency ASMs. The submission of an NTSB Form 6120.1/2 does not replace the Contractor's responsibility to submit a “Safecom”.

C12.4  Pilot Suspension

See Suspension of Pilot clause C10.2.

C12.5  Preservation Requirements

C12.5.1  The Contractor must not permit removal or alteration of the aircraft, aircraft equipment, or records following an Aircraft Accident, Incident, or Incident with Potential until authorized to do so by the CO or other authorized agency representative.  Permitted exceptions to this requirement may be when life or property are threatened, when the aircraft is blocking an airport runway, etc.  The Contractor must immediately notify the CO when taking such actions.

C12.5.2  The NTSB's release of the wreckage does not constitute a release by the CO.

C12.6  Mishap Investigations

C12.6.1  The Contractor must maintain an accurate record of all aircraft accidents, incidents, aviation hazards, and injuries to Contractor or Government personnel arising during this contract.

C12.6.2  Following a mishap, the Contractor must ensure that pilots, mechanics or other personnel associated with the aircraft remain in the vicinity of the mishap until released by the CO or their designated representative.  The Contractor must cooperate with the agency during any investigation and make available personnel and aircraft records, and any equipment, damaged or undamaged, that the agency deems necessary.

C12.7  Costs Related to Investigation

The NTSB or agency will determine their individual agency’s investigation cost responsibility.  The Contractor will be fully responsible for any cost associated with the reassembly, approval for return-to-service, and return transportation of any items disassembled by the Government.

C12.8  Rescue and Salvage Responsibilities

The Contractor must be responsible for the cost of search, rescue, and salvage operations made necessary due to causes other than negligent acts of a Government employee.

## C13  Federal Airport and Airway Excise Taxes

Chapters 31 and 33 of the Internal Revenue Code, (26 U.S.C. 4041, 4261 et seq)  impose an excise tax on aviation in one of two ways (1) as a fuel tax or (2) as a transportation tax on transportation of passengers and cargo for aircraft having maximum certificated weights in excess of 6,000 pounds.

C13.1  	Fuel Tax.  Fuel tax is applicable, and this contract requires Contractor-furnished fuel. The Contractor is responsible for paying the fuel tax and including such taxes in their bid price.

C13.2	Transportation Tax.  If the transportation tax on passengers and cargo is applicable and the Contractor is required to pay the transportation tax for those services, the Contractor must add the tax to their invoice for payment as a separate item; and the Government will reimburse the Contractor for the amount of such taxes.

C13.3	Exemptions.  The Internal Revenue Service and the U.S. Treasury Department have issued several rulings regarding imposition of transportation taxes.  These rulings do not exempt imposition of fuel taxes for which the Contractor is responsible under the above paragraphs.

Rev. Rul. 72-156 - Exempts aircraft from passenger and

cargo tax under Section 4261 and 4271 of the Code when

hauling and dropping fire retardant.

Rev. Rul. 76-477 - Exempts aircraft from passenger and

cargo taxes under Sections 4261 and 4271 of the Code

when Contractor's employees are spotting fires, or hauling

and dropping retardant chemicals.

## C14   Economic Price Adjustment - Fuel

C14.1  During the contract period, including any renewal, the hourly flight rate may be adjusted as set forth herein to reflect increases and decreases in the cost of aviation fuel.

C14.2  The Contractor warrants that the prices offered for this contract do not include any allowances for any contingency to cover increased costs for which adjustment is provided under this clause.

C14.3  Base Price.  The base price will be the commercial price obtained by the Government for jet fuel or aviation gasoline (whichever is appropriate) at or near the designated base and at the time the solicitation is issued.

BASE PRICE INFORMATION

"Base Price" of fuel has been established at a source at or near the designated base and is shown below.

ITEM 1 – BLM/Salt Lake City, UT

Jet Fuel "Base Price" -- $                   per gallon

Av Gas "Base Price"   -- $                   per gallon

# Fuel price obtained from: Million Air

Telephone Number:  (800) 752-5382

C14.4  Reference Price.  The reference price will be the commercial fuel price in effect at the time of economic price adjustment.  The reference price will be obtained from the same source as the base price.  The reference price will become the base price for the subsequent adjustment.

C14.5  Flight Rate Adjustment.  Adjustment to the hourly flight rate is the difference between the reference price and the base price multiplied by the hourly fuel consumption rate for the type aircraft involved as shown in the Fixed Wing Fuel Consumption Chart Exhibit.

C14.5.1  The hourly flight rate will be adjusted upward whenever the Contractor notifies the CO in writing that the reference price is more than 10 percent higher than the base price.  The hourly flight rate will be adjusted downward whenever the CO notifies the Contractor in writing that the reference price is more than 10 percent lower than the base price.  The adjusted price will apply to flight time occurring after receipt of said notice.

C14.6  Fuel price adjustments will be subject to review by the CO.

# CONTRACT PERIOD AND RENEWAL

## C15  Contract Period

The contract period will be from date of award through June 6, 2010, unless otherwise extended as allowed herein. The contract period for options shall be as follows:

Option Year 1:   June 7, 2010 – June 6, 2011

Option Year 2:   June 7, 2011 – June 6, 2012

Option Year 3:   June 7, 2012 – June 6, 2013

Option Year 4:   June 7, 2013 – June 6, 2014

## C16  Option to Extend the Term of the Contract (48 CFR 52.217-9, Mar 2000)

(a)  The Government may extend the term of this contract by written notice to the Contractor at least 30 days prior to expiration of the contract.

(b)  If the Government exercises this option, the extended contract shall be considered to include this option clause.

(c)  Options exercised prior to the availability of funds for a new fiscal year are subject to FAR 52.232-18 Availability of Funds, which is incorporated by reference.

(d)  The total duration of this contract, including the exercise of any options under this clause, shall not exceed 60      months (5 years).

## C17 Reserved

## C18  Exclusive Use Period

C18.1  The exclusive use period will extend for 90 calendar days.  The exclusive use period will start on either of the following:

C18.1.1  The date stipulated in Section A.

C18.1.2  The date established by a Notice to Proceed issued by the CO or COR and received by the Contractor at least 20 days in advance of the intended start date which establishes a start date that commences not more than 14 days prior to nor 14 days after the start date stipulated in Section A.

C18.1.2.1  The date established by a Notice to Proceed issued by the CO or COR and received by the Contractor less than 20 days in advance of the intended start date must be mutually agreed upon.

C18.1.3  The date determined according to the following paragraph.

C18.1.3.1  The exclusive use period start date is based on the assumption that the Contractor will receive notification of contract award or renewal at least 30 days before the exclusive use period begins.  If notice of award or renewal is not received at least 30 days in advance of the start date, the exclusive use period will start when service begins or 30 calendar days after notice of award or renewal is received, whichever occurs first.

C18.2  The Government will not consider any contract aircraft to be under its operational control when the Contractor is not available or capable of providing Government scheduled services.

## C19   Mutual Extension of Exclusive Use Period

Upon mutual agreement by the parties, the CO will modify the contract to extend the exclusive use period on a day-to-day basis, either prior to the established starting date or subsequent to the ending date. The contract terms, conditions, specifications and prices will apply to such extension; however, in accordance with the Federal Travel Regulations (FTRs), the Government will pay subsistence daily for each overnight for each authorized crew member while operating at the designated or an alternate base. Extensions that extend the use period prior to the established start date will be paid at the rates for the use period that is being extended.

# AVAILABILITY REQUIREMENTS

## C20  Availability Requirements

During the exclusive use period and any extension, the Contractor must be in compliance with all contract requirements and available and capable of providing service up to 14 hours each day, as scheduled by the Government.  Personnel must be available a minimum of nine hours each day, or as scheduled by the Government.  Pre- and post-flight activities must be accomplished within the 14- hour duty day.  Routine maintenance must be performed before or after the scheduled 14-hour period, or as permitted elsewhere in the contract.

C20.1  Extended standby is intended to provide the Contractor compensation for employee time when ordered services are provided in excess of the first 9 hours of service.  Ordered standby must not exceed individual crew members' daily duty limitations.  Extended standby is not intended to compensate the Contractor on a one-to-one basis for all hours necessary to service and maintain the aircraft.

## C21  Schedule of Operations and Reaction Time

The Government will schedule daily operations with the pilot.  The Contractor's personnel must provide service, as directed by the Government, in one of the following categories:

C21.1  Standby.  Personnel must be on standby each day as scheduled and must be ready for takeoff/dispatch within 15 minutes (or longer as authorized by the Government; e.g. flight planning purposes for long range dispatch) after the Government attempts to contact the Contractor's representative.

C21.2 Release From Duty. Contractor personnel may be released and considered to be off duty prior to lapse of their individual crew duty limitation period.  Once released, they cannot be required to return to duty status that day and service will be recorded as fully available status, provided the COR has approved in advance release of the Contractor's personnel.

## C22   Maintenance During Availability Period

C22.1  The COR may approve Contractor requests to remove the aircraft from service to permit the Contractor to perform scheduled or unscheduled maintenance.  The Government will continue to measure and pay for service availability throughout periods approved for maintenance.  The COR may require the Contractor to resume service within 60 minutes or any other agreed upon time period.  Failure to do so would result in unavailability status.

C22.2    If the aircraft is not scheduled for service or service is unavailable, the aircraft may be removed from the operating base for maintenance, provided the Contractor:  (1) Obtains the schedule of operations from the COR, (2) returns the aircraft to service before the beginning of the next availability period, AND (3) uses the aircraft for maintenance test flights, or flight to and from maintenance facilities, only.

## C23  Unavailability and Damages

C23.1  The Contractor will be considered to be unavailable when they are not in compliance with all contract requirements or are not capable of providing service as scheduled by the Government.   Unavailability status will continue until the Contractor has notified the COR that they are available.

C23.2  During periods of Contractor unavailability, the Government may obtain replacement services elsewhere and charge the Contractor for any resulting excess costs.  The Contractor may be liable for any additional actual damages to the Government resulting from such failure to perform.

# MEASUREMENT AND PAYMENT

## C24  Daily Availability

Availability is measured in full days for the daily period of time (maximum of 14 hours) scheduled by the Government and provided by the Contractor.  Payment for availability will be made as actual services are provided and paid at the rate and for the number of days set forth in Section A.  Payment will be reduced by one hour for each hour, or portion thereof, in accordance with the Unavailability Conversion Chart Exhibit, when services are unavailable or when the aircraft has been released for the Contractor’s benefit.

C24.1.1  The Government will measure extended standby in full hours and will round up to the next whole hour, not to exceed each crew member’s duty limitations specified in Section B.  Payment for extended standby will be made at the prices set forth in Section A, and as measured above.  If unavailability occurs, extended standby will be measured and paid only for full hours of service provided.

## C25  Flight Time

C25.1  Measurement of Flight Time.  Flight will be measured  from the time the aircraft commences its take-off roll until it returns to the blocks.  Elapsed time will be measured in hours and tenths/hundredths of hours.

C25.2  Payment for Flight Time.  The Government will pay for all flights ordered by the CO and flown by the Contractor at the rates set forth in Section A.  The Government does not guarantee any minimum or maximum number of flight hours during this contract.

C25.3  Flights Associated with Inspections.  Flight time associated with the DOI, NBC, Aviation Management (agency) inspection will be at the expense of the Contractor and will not be measured for payment.

C25.4  Flights for Contractor's Benefit.  The Government will not pay for flights benefiting the Contractor, such as flights for maintenance testing, for ferrying to and from maintenance facilities, flights required following an engine change, commercial charters, and flights solely for transporting Contractor's personnel.

## C26  Mobilization/Demobilization

C26.1  The Contractor is be responsible for all mobilization and demobilization costs to and from the designated base(s) stipulated in Section A.  The Government may, at its discretion, release the Contractor from other than the base stipulated in Section A.  The contract price will be adjusted as described below whenever the distance from the point of release to the Contractor's home base is greater than or less than the distance between the Contractor's home base and the designated base stipulated in Section A.

C26.2  Flight distance will be measured using the most direct route taken from low level en route aeronautical charts.  The net distance will be converted into hours of flight using the most economical cruise speed of the aircraft.  The adjustment will be determined by multiplying the difference in distance (hours of flight) by the flight rate stipulated in Section A.

C26.3  Distances that are greater than home base to the base stipulated in the Section A will result in a payment to the Contractor.  Distances that are less than home base to the base stipulated in Section A will result in a decrease to the Contractor.

## C27  Additional Pay Items (from Schedule of Items)

Claims for additional pay items addressed herein must be documented on the invoice for payment and supported by invoice(s) and/or document(s), as required below.  The Government will not pay claims submitted with incomplete or missing supporting documentation.

C27.1  Subsistence Allowance.  Each authorized crewmember may claim a subsistence allowance (lodging and meals) for each overnight stay, including mandatory days off, when assigned to a base away from the designated base.

C27.1.1  The Government, at its option, may provide meals and/or lodging (which may be remote field or fire camp accommodations).  If not Government provided, the Contractor will be paid an overnight allowance equal to the standard Federal Travel Regulation (FTR) rate (or high rate, if applicable).  The Contractor may claim overnight expenses using either of the two following methods:

C27.1.1.1  Payment of the Standard or High Rate, if applicable) lodging and M&IE rate EXCLUDING lodging tax (does not require lodging receipts to be submitted with the invoice) or;

C27.1.1.2  Payment of actual lodging amount and M&IE rate not to exceed that authorized in accordance with the FTR plus lodging tax. An itemized lodging invoice detailing lodging cost and tax must be submitted with the invoice.

(a)  The  lodging and payment invoices must clearly show the county or city where the overnight stay occurred.  High rate claims for subsistence that do not include this information will be reduced to the standard rate.

C27.1.2  If the Contractor does not use Government provided meals and/or lodging, the Government will not pay for contractor costs incurred for travel to alternate meal or lodging locations.

C27.1.3  Unless the Government makes three meals available to the Contractor's employees, the appropriate total rate for meals and incidental expenses will be paid.

C27.1.4  If partial subsistence, either three meals or lodging, is provided by the Government, the Contractor will be paid at current FTR rates for the portion that is Contractor provided.  Lodging will be handled as stated above.  Current rates established by the FTR are:

STANDARD

Meals and Incidental Expense: $39.00

Lodging: $70.00

Total:  $109.00

HIGH RATE

For current FTR per diem rates see Internet site http://www.gsa.gov and select - Per Diem Rates, Domestic.

C27.1.5  The Government is not contractually obligated to provide miscellaneous food/drinks/refreshments for Contractor employees at fire locations.  While some locations may provide food/drink/refreshments to fire crews, including Contractor personnel, this intermittent availability does not create an ongoing Government obligation to furnish at every site/location.

C27.3  Fuel Supply Expense.  The Contractor is responsible for the cost of all fuel required for contract performance. When the Contractor is ordered to operate from an alternate base, the Government will, at its option:

C27.3.1  Furnish fuel and deduct from payment the fuel cost based upon commercial rates at the nearest point fuel is commercially available.

C27.3.2  Direct the Contractor to obtain fuel from commercial sources at no additional cost to the Government.

C27.4 Transportation Costs Associated with Operating Away From the Designated Base.  When operating from an alternate base, the Contractor is required to provide for transporting relief personnel, unless otherwise directed by the Government.  Prior to the exchange, the Contractor must advise the COR of the anticipated costs. The Contractor will be paid actual necessary and reasonable costs for transporting personnel and required equipment listed below.

Relief Crew members.  The complement must be the same as required in Section A.

Maintenance personnel and equipment required to accomplish scheduled maintenance, i.e. 50 and 100 hour inspections.

C27.4.1  The Contractor must complete and submit the Transportation Worksheet Exhibit, attach supporting invoices identified above to the invoice for payment, and enter the total dollar amount as a line entry on the invoice for payment (SC pay item code).  Claims that do not include these items or other documents necessary to verify incurred costs will be returned to the Contractor for proper completion.

C27.4.2  Unless approved in advance by the CO, payment for crew member exchanges is limited to one round trip for one crew members once every 12 days.  Additional payment may be appropriate for circumstances such as personnel reaching flight or duty time limits including agency imposed temporary flight or duty restrictions as specified in Section B.

C27.4.3  Examples of acceptable expenses are airline tickets; car rentals; privately owned vehicle (POV) at the government mileage rate (currently 50.5 cents) (Internet site http://www.gsa.gov) and charter airplane showing aircraft make/model, flight time, hourly rate and departure and destination locations.  Unless authorized in advance by the COR, the expense for charter resources must not exceed reasonable costs by common carrier.  The Government will not reimburse the Contractor for salary and subsistence costs for Contractor personnel in travel status.

C27.5 Miscellaneous Contractor Costs.  Miscellaneous unforeseeable costs that cannot be recovered through the contract payment rates and that are the direct result of ordered services away from the designated base may be paid at actual costs, when authorized in advance by the COR.   Examples of such items are airport use costs (tie-downs) and truck permits at ports-of-entry.  The Contractor must support any cost exceeding $75.00 with an itemized, paid invoice.

C27.6 Landing Fees.  The Government will pay the Contractor for all landing fees the Contractor is required to pay.  The Contractor must support any cost exceeding $75.00 with an itemized, paid invoice.

## C28  Government Miscellaneous Charges

The Government will deduct payment for miscellaneous charges for goods or services furnished to the Contractor.

# BILLING AND REPORTING REQUIREMENTS

## C29  Designated Agency Office and Payment Office

The office identified in Block 18a of the SF 1449 is the office designated by the contract to first receive and review invoices.  This office is also the office issuing payments.  It is the Contractor’s responsibility to submit invoices to the identified office.

## C30  Invoice Submissions

The Contractor may submit invoices every two weeks starting the first day services begin. Services provided must be shown on a daily basis.

## C31  Aircraft Use Report

The Contractor, or Contractor's representative, and the Government must complete and sign an Aircraft Use Report, AMD-23 form.  Instructions for proper completion of the Aircraft Use Report are contained in the AMD-23 booklet.  The Contractor may use the completed and signed Aircraft Use Reports as their invoice.

## C32  Contract Pricing

Unit prices for daily availability and flight hours must be in whole dollars (see D4.2).  If these unit prices are adjusted during the life of the contract, they will be adjusted to a whole dollar as follows:  amounts of 50 cents or less will be rounded down and amounts of 51 cents or more will be rounded up.

# EXHIBITS

C33 The following exhibits are enclosed and made part of this solicitation:

Section B

-Unacceptable Lap Belt and Shoulder Harness Conditions

-First Aid Kit and Survival Kit

-FS/AMD Drawing A-17

Section C

-Statement of Equivalent Rates for Federal Hires

-Department of Labor Wage Determination Information

-Fixed Wing Fuel Consumption Chart

-Unavailability Conversion Chart

-Transportation Worksheet

EXHIBIT

UNACCEPTABLE AIRCRAFT LAP BELT AND SHOULDER HARNESS CONDITIONS

| Item | Unacceptable Conditions |
| --- | --- |
| Webbing | Frayed: 5 percent or more Torn Crushed Swelling: twice the thickness of original web or if difficult to operate through hardware Creased: no structural damage allowed Sun deterioration: severe fading, brittleness, discoloration, and stiffness |
| Hardware | Inoperable buckle or other hardware Nylon bushing at shoulder-harness-to-lap-belt connection missing or damaged Fabricated bushings or tie wraps used as bushings Rust/corrosion: only minor surface rust/corrosion allowed Wear: wear beyond normal use |
| Stitches | Broken or missing Severe fading or discoloring Inconsistent pattern |
| TSO Tags (see 14 CFR 21.607) | Missing Illegible |
| Age | Belts/fabric over 10 years from date of manufacture will be closely inspected for possible damage from exposure to the elements, but do not have to be replaced if they can be determined to be in serviceable condition. |

EXHIBIT

FIRST AID AND SURVIVAL KITS

These are the minimum required items for special use activities in the United States and U.S. possessions.  Additional survival kit items are required for flight activities conducted in Canada and Alaska.

Minimum First Aid Kit Items Each kit must be in a dust-proof and moisture-proof container. The kit must be readily accessible to the pilot and passengers. Passenger Seats Passenger Seats Item 0-9 10-50 Adhesive bandage strips, (3 inches long) 8 16 Antiseptic or alcohol wipes (packets) 10 20 Bandage compresses, 4 inches 2 4 Triangular bandage, 40 inches (sling) 2 4 Roller bandage, 4 inches x 5 yards (gauze) 2 4 Adhesive tape, 1 inch x 5 yards (standard roll) 1 2 Bandage scissors 1 1 Body fluids barrier kit: 1 1 2 pair latex gloves 1 face shield 1 mouth-to-mouth barrier 1 protective gown 2 antiseptic towelettes 1 biohazard disposable bag NOTE: Splints are recommended if space permits.

Minimum Aircraft Survival Kit Items Knife Signal mirror Signal flares (six each) Matches (two small boxes in waterproof containers) Space blanket (one per occupant) Water (one quart per occupant: not required when operating over areas with adequate drinking water) Food (two days' emergency rations per occupant) Candles Water purification tablets Collapsible water bag Whistle Magnesium fire starter Nylon rope or parachute cord (50 feet)

EXHIBIT

DRAWING FS/AMD A-17

Auxiliary FM Radio Interface

FIXED WING FUEL CONSUMPTION CHART

BEECH

Baron 55/58	29

Baron 58P	35

18/45	35

King Air 90 (Series)	70T

King Air 100	80T

King Air 200	93T

King Air 300	89T

Mentor T-34	14

Mini Liner 99	85T

Queen air	43

T-Bone B-50	45

Duke	38

Queen air 80	34

Bonanza 33/35/36	14

BELLANCA

Citabria/Scout	9

BOEING

727	1000T

BRITTEN-NORMAN

Islander	30

CANADAIR

CESSNA

L-19	11

172	9

180	14

182	12

182RG	14

185	16

188	12

206/207	16

T206/207	18

210	16

T210	18

320	28

310	32

T310	34

337	24

T337	26

401	28

402	36

404	46

411	34

414	36

421	46

340	36

425	56T

441	52T

Citation I	140T

Citation II, III	160T

208 Caravan I	53T

CONSOLIDATED

Convair 580/600	338T

DE HAVILLAND

Beaver	30

DH-6 Twin Otter	95T

Beaver T	40T

DH-7	234T

DH-8	183T

DORNIER

DO-228	100T

DOUGLAS

DC-3	93

DC-9	700T

EMBRAER

PW 115 (1600)	159T

FALCON

10	175T

20	240T

50	300T

FAIRCHILD

Porter	44T

F-27	288T

SF 340	161T

GRUMMAN

S2F	75

Goose	50

Goose T	80T

Mohawk	180T

Albatross	160

G-I	288T

G-II	529T

G-III	370T

HELIO

Courier	20

Stallion	44T

ISRAEL

1121/1123/1124	190T

LOCKHEED

P-3/C-130/Electra 188	661T

Jetstar	374T

LEAR JET

25	220T

35/36	185T

55	200T

MAULE

M4-5	9

M7	13

MITSUBISHI

MU-2	77T

MOONEY

Exec	10

NOMAD

22B/24A	53T

### NORTH AMERICAN

AT-6	18

T-28	80

PIPER

Super Cub PA-18	9

Pawnee PA-25	13

Arrow PA-28R	10

Cherokee PA-28-140/161	8

Cherokee 6 PA-32	14

Aztec PA-23	27

Comanche PA-24	15

Navajo PA-31	32

Cheyenne PA-31T	77T

Cheyenne II PA-42T	74T

Aerostar 600/601/602P/700P	33

Cheyenne III PA-42T	110T

Chieftan PA-31-350	34

Lance PA-32-300	16

Seneca II/III PA-34	20

Mojave PA-31P	39

Malibu PA-46	15

PA-42-1000 400LS	75T

ROCKWELL (Gulfstream)

680	40

500	34

690A/B	80T

Sabreliner	…200T

560	…33

840	65T

900	55T

1000	57T

SWEARINGEN

Merlin II, III SA 226/7	78T

SHORT

Skyvan	85T

VOLPAR

TurboLiner	74T

CASA	95T

Turbine DC-3	150T

“T” after the gallons indicates turbine fuel, everything else is Avgas.

Source:   “B and CA” Aircraft Guide and “Flying” Aircraft Guide

EXHIBIT

Statement of Equivalent Rates for Federal Hires (48 CFR 52.222.42)

IS FOR INFORMATION ONLY AND IS REQUIRED TO BE INCLUDED IN THE SOLICITATION BY THE SERVICE CONTRACT ACT

THIS IS NOT A DEPARTMENT OF LABOR WAGE DETERMINATION

(See following page)

Set forth below are wage rates and fringe benefits that would be paid by the contracting activity for the various classes of service employees expected to be utilized under the contract if 5 U.S.C. 5332 (General Schedule-white collar) and/or 5 U.S.C. 5341 (Wage Board-blue collar) were applicable.

A.	EMPLOYEE CLASS			MONETARY WAGE

Aircraft Pilot, GS-11			$ 25.34

B.	Fringe benefits such as, life, accident and health insurance, and sick leave, are not less than 5.1 percent of the basic hourly rate.

C.	Paid holidays are:

1.	New Year's Day		6.	Labor Day

2.	Martin Luther King, Jr.'s Birthday		7.	Columbus Day

3.	President's Day		8.	Veterans Day

4.	Memorial Day		9.	Thanksgiving Day

5.	Independence Day		10.	Christmas Day

D.	The amount of paid vacation time allowed is as follows:

1.	Two (2) hours of annual leave each week for an employee with less than three (3) years of service.

- Three (3) hours of annual leave each week for an employee with three (3) but less than fifteen (15) years of service.

3.	Four (4) hours of annual leave each week for an employee with fifteen (15) or more years of service.

E.	The percentage of the basic hourly rate that is contributed by the contracting agency for retirement is currently 7 to 17.5 percent.

EXHIBIT

DEPARTMENT OF LABOR WAGE DETERMINATION INFORMATION

This solicitation includes Department of Labor (DOL) wage determinations as identified below.  In order that this solicitation may be accessed electronically, the following DOL wage determination information has been extracted from the wage determination(s) listed below and identifies the occupations of service employees that would typically be employed on this type of a solicitation.  This information should be considered when submitting an offer.  The DOL wage determination information identified herein will be included in the awarded contract with complete copies of the wage determinations being provided to the successful Contractor.  To receive the wage determinations in their entirety, please contact the issuing office at 208-433-5026 or submit a written facsimile request to 208-433-5030.

DOL WAGE DETERMINATION NO. 1995-0222, REV. 26 DATED 05/29/08

Area:  			Nationwide

Applicable Occupation:	Airplane Pilot		Minimum Hourly Wage:	$23.62

### FRINGE BENEFITS REQUIRED AND APPLICABLE FOR EACH OCCUPATION IDENTIFIED ABOVE

### WD 1995-0222 Rev. 26

1. Health & Welfare:	$3.24 per hour or $129.60 per week or $561.60 per month

2. Holidays:	 	Minimum of ten paid holidays per year:  New Year’s Day, Martin Luther King Jr’s Birthday, Washington’s Birthday, Memorial Day, Independence Day, Labor Day, Columbus Day, Veterans’ Day, Thanksgiving Day and Christmas Day.  (A Contractor may substitute for any of the named holidays another day off with pay in accordance with a plan communicated to the employees involved.)  (Reg. 29 CFR 4.174)

3. Vacation:		2 weeks paid vacation after 1 year of service with a Contractor or successor; 3 weeks after 5 years; 4 weeks after 15 years.  Length of service includes the whole span of continuous service with the present Contractor or successor, wherever employed, and with the predecessor Contractors in the performance of similar work at the same Federal facility.  (Reg. 29 CFR 4.173)

CONFORMANCE PROCESS - If the offeror intends to employ a class of service employee that is not listed above, the offeror should immediately contact the issuing office of this solicitation and request a complete copy of the wage determinations.  The offeror can then view the wage determinations in their entirety and if needed can make a request for authorization of an additional classification and wage rate through the conformance process as set forth in the wage determinations.

EXHIBIT

UNAVAILABILITY CONVERSION CHART

| HOURS UNAVAILABLE | UNITS OF AVAILABILITY RECORDED AS: | UNITS OF UNAVAILABILITY RECORDED AS: |
| --- | --- | --- |
| 0 | 1.00 | 0.00 |
| 1 | .93 | .07 |
| 2 | .86 | .14 |
| 3 | .79 | .21 |
| 4 | .71 | .29 |
| 5 | .64 | .36 |
| 6 | .57 | .43 |
| 7 | .50 | .50 |
| 8 | .43 | .57 |
| 9 | .36 | .64 |
| 10 | .29 | .71 |
| 11 | .21 | .79 |
| 12 | .14 | .86 |
| 13 | .07 | .93 |
| 14 | 0.00 | 1.00 |

EXHIBIT

TRANSPORTATION WORKSHEET

| When assigned to an alternate base, the Contractor will be paid for actual necessary and reasonable costs associated with transporting authorized personnel. The Contractor is responsible for advising the on-site Government representative(s) of the anticipated cost associated with transporting relief (and/or maintenance) personnel to the alternate base prior to the relief exchange. Claims must be supported by itemized invoices. See contract clause “Transportation Costs Associated with Operating Away From the Designated Base” for detailed information |
| --- |
| DATE | ALTERNATE BASE LOCATION |
| Relief Exchange – Involved Crew Member(s) |
| ( Pilot Name | ( Fuel Servicing Vehicle Driver Name | ( Mechanic (If required by contract) Name |
| Scheduled Maintenance |
| ( Mechanic Name | ( Other Name |
| Maintenance Accomplished | Reason for providing additional personnel |
| ITEMIZATION OF COSTS – Invoices and/or receipts are attached (copies are acceptable) |
| Airline Transportation | Name | $ |
| Airline Transportation | Name | $ |
| Charter Aircraft | Invoice to include aircraft make/model, flight time, hourly rate, passengers, and departure/destination location, date and time | $ |
| Rental Car |  | $ |
| Rental Car Fuel |  | $ |
| POV | Total Mileage | From | To | $ |
| Other (explain) | $ |
|  | $ |
|  | $ |
|  | $ |
|  | $ |
| Total ACTUAL Cost | $ |
| Yes, the COR was notified of the anticipated cost for this alternate base transportation expense prior to mobilization of the relief personnel Contractor Representative Signature | Date |

# section d – instructions to offerors

# INTRODUCTION

## D1.  General Information

D1.1  The services of this Request for Proposals (RFP) are being acquired under the authority of Federal Acquisition Regulations (FAR), Part 12, Acquisition of Commercial Items and FAR Subpart 13.5, Test Program for Certain Commercial Items.

D1.2  If you wish to compete for the contract described in Sections A through C of this RFP, you must submit a proposal that includes a signed and dated offer and other requested information by the time and date shown on the SF1449.

# 52.212-1 INSTRUCTIONS TO OFFERORS--COMMERCIAL ITEMS (JUN 2008) [Tailored]

## D2 North American Industry Classification System (NAICS) Code and Small Business Size Standard

The NAICS code and small business size standard for this acquisition is 481211 and 1,500 employees respectively.

## D3  Proposals

To be considered as a prospective Contractor for the requirement identified in this solicitation, an offeror must submit a proposal consisting of a valid offer and the Offeror Capability Information identified below.  Send proposals to:

By mail, hand carried or express delivery service:

Department of the Interior

Aviation Management

300 E. Mallard Drive, Suite 200

Boise, Idaho 83706-3991

Attn: Solicitation 8009-05

(DO NOT OPEN)

By facsimile:	208-433-5030

## D4   Offer Contents

D4.1  SF 1449, Solicitation/Contract/Order for Commercial Items, completed and signed.

D4.2  Solicitation Section A, pricing page(s) completed where indicated with unit rates offered in U.S. whole dollars for daily availability and flight time.  Offerors may offer varying prices for option years.  Offerors shall compute the extended yearly amounts for availability and flight time by multiplying the unit prices offered times the quantities shown.  Offerors shall enter an extended amount for each year as well an amount for the total for all years.  The Government will round pricing submitted with cents up to the next whole dollar.  Estimates are for evaluation purposes only.

D4.3  A completed copy of the Offeror’s Representations and Certifications included in Section E (see FAR 52.212-3(b) for those representations and certifications that the offeror shall complete electronically).

D4.4  A completed copy of Offeror’s Miscellaneous Information included in Section E.

D4.5  Acknowledgment of Solicitation Amendments (if any).

D4.6  A completed copy of the Aircraft Questionnaire included in Section E.  The aircraft make, model, and capability we confirm will be made a part of your offer and will be binding if your offer is accepted for award.  The confirmed information will be identified in Section A of the conformed contract.

D4.7  Offeror Capability Information.  Offeror must include:

A completed copy of the Reference Questionnaire included in Section E.

D4.8  Period for Acceptance of Offers

The offeror agrees to hold the prices in its offer firm for 60 calendar days from the dated specified for receipt of offers, unless another time period is specified in an addendum to the solicitation.

## D5  Late Submissions, Modifications, Revisions, and Withdrawals of Offers

Late Submissions, Modifications, Revisions and Withdrawals of Offers are subject to the terms of Federal Acquisition Regulation (FAR) clause 52.212-1(f), which is incorporated by reference, except that offers may be withdrawn in writing at any time before award is made.

## D6  Data Universal Numbering System (DUNS) Number)

Data Universal Numbering System (DUNS) Number. (Applies to all offers exceeding $3,000, and offers of $3,000 or less if the solicitation requires the Contractor to be registered in the Central Contractor Registration (CCR) database. The offeror  shall enter, in the block with its name and address on the cover page of its offer, the annotation "DUNS" or "DUNS+4" followed by the DUNS or DUNS+4 number that identifies the offeror's name and address. The DUNS+4 is the DUNS number plus a 4-character suffix that may be assigned at the discretion of the offeror to establish additional CCR records for identifying alternative Electronic Funds Transfer (EFT) accounts (see FAR Subpart 32.11) for the same concern. If the offeror does not have a DUNS number, it should contact Dun and Bradstreet directly to obtain one. An offeror within the United States may contact Dun and Bradstreet by calling 1-866-705-5711 or via the internet at http://fedgov.dnb.com/webform. An offeror located outside the United States must contact the local Dun and Bradstreet office for a DUNS number.  The offeror should indicate that it is an offeror for a Government contract when contacting the local Dun and Bradstreet office.

## D7  Special Notice to Offerors

D7.1 Central Contractor Registration

Unless exempted by an addendum to this solicitation, by submission of an offer, the offeror acknowledges the requirement that a prospective awardee shall be registered in the CCR database prior to award, during performance and through final payment of any contract resulting from this solicitation.  Failure to register in the CCR database prior to award may affect your ability to be awarded a contract and the Contracting Officer may proceed to award to the next otherwise successful registered Offeror. Offerors may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov or by calling 1-888-227-2423 or 269-961-5757.

D7.2  There are no Government facilities at this airport.  Salt Lake City, UT is a full service community with numerous motels, restaurants, rental housing, etc. facilities available.

# EVALUATION OF PROPOSALS

The Government will evaluate proposals and select the Contractor based on (1) offer acceptability, (2) evaluated price, (3) aircraft capability and (4) offeror capability, as explained below.

## D8  Offer Acceptability

The Government must deem offers to be acceptable to consider them further and will base determinations of offer acceptability on the following two subfactors:

D8.1  Assent to Solicitation Terms. Your offer must assent to all terms of this request for proposals and you must provide all information requested.  Your offer will be unacceptable if you take exception to any term of this solicitation.

D8.2  Minimum Aircraft Requirements.  Your offer must propose an aircraft that meets or exceeds the Minimum Aircraft Requirements specification in Section A of this solicitation.  Your offer will be unacceptable if you propose an aircraft that fails to meet any of the Minimum Aircraft Requirements specified in Section A of this solicitation.

D8.3 Unacceptable offers will be eliminated without considering aircraft payload, offeror capability or price.

## D9  Evaluated Price

D9.1  The Government will take the total offered price for all five years as identified in Section A to arrive at the estimated evaluated price for each offeror.  Evaluation of options shall not obligate the Government to exercise the option(s).  Once the estimated evaluated prices of all acceptable offers have been determined, the Government will compare the evaluated prices and eliminate any offer with an unreasonably high-evaluated price, without considering aircraft payload or offeror capability. The Government will then perform a tradeoff analysis, as described below in D12 with the remaining offers.

D9.2  The Government reserves the right to reject offers that have materially unbalanced availability and flight rates in comparison to other offers received.  An offer is materially unbalanced when it is based on prices significantly less than cost for some work and prices which are significantly overstated in relation to cost for other work, and there is a reasonable doubt that the offer will result in the lowest overall cost to the Government even though it may be the low evaluated offer, or if it is so unbalanced as to be tantamount to allowing an advance payment.

## D10  Aircraft Capability

The Government will evaluate the capability of your proposed aircraft to determine whether it is above, at, or below the Target Aircraft Requirements specified in Section A of this RFP. The greater capability your proposed aircraft provides, the better the evaluation you will receive for this factor.

## D11  Offeror Capability

The Government will evaluate your capability based on the following two subfactors:

D11.1  Organizational Experience. The Government will base its evaluations of your experience on the extent to which you have performed services of the kind described in paragraph B1.1 of the Technical Specifications of this RFP and under similar contract terms. The more recent your experience, and the broader and deeper, the better the evaluation you will receive. Only your firm’s experience as an organization will be considered.

D11.2  Organizational Past Performance. The Government will evaluate your past performance in rendering services of the kind described in paragraph B1.1 of the Technical Specifications of this RFP. “Past Performance” refers to the quality of your work in the past.  Your past performance will be evaluated on the basis of information obtained from references and other sources. The Government will give greater weight to its own experiences with you, if any, than it will give to reports obtained from others.

## D12  Tradeoff Analysis and Contractor Selection

The Government will select the Contractor by comparing the acceptable offers on the basis of proposed aircraft capability, offeror capability, and reasonability of evaluated prices. If one offer is best on all the factors, then that offer will be selected as being the best value to the Government. If no offer is best on all the factors, then the Government will consider the differences among offers and make tradeoffs in order to determine which offer is the best value. The Government will award the contract to the offer that has the best combination of aircraft capability, offeror capability, and evaluated price.

## D13  Notice of Award

The Government intends on awarding one contract as a result of this solicitation. The Government will provide the successful Contractor with a written notice of award, either by mail or other means, upon selection.  This notice will result in a binding contract without further action by either party.

# section e – offeror’s representations, certifications and other statements

# 52.212-3 OFFEROR REPRESENTATIONS AND CERTIFICATIONS—COMMERCIAL ITEMS (JUN 2008)

An offeror shall complete only paragraph (b) of this provision if the offeror has completed the annual representations and certifications electronically at http://orca.bpn.gov. If an offeror has not completed the annual representations and certifications electronically at the ORCA website, the offeror shall complete only paragraphs (c) through (m) of this provision.

(a) Definitions. As used in this provision-

"Emerging small business" means a small business concern whose size is no greater than 50 percent of the numerical size standard for the  NAICS code designated.

"Forced or indentured child labor" means all work or service--

(1) Exacted from any person under the age of 18 under the menace of any penalty for its nonperformance and for which the worker does not offer himself voluntarily; or

(2) Performed by any person under the age of 18 pursuant to a contract the enforcement of which can be accomplished by process or penalties.

“Manufactured end product” means any end product in Federal Supply Classes (FSC) 1000-9999, except-

- FSC 5510, Lumber and Related Basic Wood Materials;

- Federal Supply Group (FSG) 87, Agricultural Supplies;

- FSG 88, Live Animals

- FSG 89, Food and Related Consumables;

- FSC 9410, Crude Grades of Plant Materials;

- FSC 9430, Miscellaneous Crude Animal Products, Inedible;

- FSC 9440, Miscellaneous Crude Agricultural and Forestry Products;

- FSC 9610, Ores;

- FSC 9620, Minerals, Natural and Synthetic; and

- FSC 9630, Additive Metal Materials.

“Place of Manufacture” means the place where an end product is assembled out of components, or otherwise made or processed from raw materials into the finished product that is to be provided to the Government.  If a product is disassembled and reassembled, the place of reassembly is not the place of manufacture.

“Restricted business operations” means business operations in Sudan that include power production activities, mineral extraction activities, oil-related activities, or the production of military equipment, as those terms are defined in the Sudan Accountability and Divestment Act of 2007 (Pub. L. 110-174).  Restricted business operations do not include business operations that the person conducting the business can demonstrate—

- Are conducted under contract directly and exclusively with the regional government of southern Sudan;

- Are conducted pursuant to specific authorization from the Office of Foreign Assets Control in the Department of the Treasury, or are expressly exempted under Federal law from the requirement to be conducted under such authorization;

- Consist of providing goods or services to marginalized populations of Sudan;

- Consist of providing goods or services to an internationally recognized peacekeeping force or humanitarian organization;

- Consist of providing goods or services that are used only to promote health or education; or

- Have been voluntarily suspended.

“Service-disabled veteran-owned small business concern”-

- Means a small business concern-

- Not less than 51 percent of which is  owned by one or more service-disabled veterans or, in the case of any publicly owned business, not less than 51 percent of the stock of which is owned by one or more service-disabled veterans; and

- The management and daily business operations of which are controlled by one or more service-disabled veterans or, in the case of a service-disabled veteran with permanent and severe disability, the spouse or permanent caregiver of such veteran.

(2) Service-disabled veteran means a veteran, as defined in 38 U.S.C. 101(2), with a disability that is service connected as defined in 38 U.S.C. 101(16).

"Small business concern" means a concern, including its affiliates, that is independently owned and operated, not dominant in the field of operation in which it is bidding on Government contracts, and qualified as a small business under the criteria in 13 CFR Part 121 and size standards in this solicitation.

“Veteran-owned small business concern” means a small business concern-

- Not less than 51 of which is owned by one or more veterans (as defined by 38 U.S.C. 101(2)) or, in the case of publicly owned business, not less than 51 percent of the stock of which is owned by one or more veterans; and

- The management and daily business operations of which are controlled by one or more veterans.

"Women-owned business concern" means a concern which is at least 51 percent owned by one or more women; or in the case of any publicly owned business, at least 51 percent of its stock is owned by one or more women; and whose management and daily business operations are controlled by one or more women.

"Women-owned small business concern" means a small business concern--

(1) That is at least 51 percent owned by one or more women or, in the case of any publicly owned business, at least 51 percent of the stock of which is owned by one or more women; and

(1) Whose management and daily business operations are controlled by one or more women.

(b) (1) Annual Representations and Certifications.  Any changes provided by the offeror in paragraph (b)(2) of this provision do not automatically change the representations and certifications posted on the Online Representations and Certifications Application (ORCA) website.

(2)  The offeror has completed the annual representations and certifications electronically via the ORCA website at http://orca.bpn.gov.  After reviewing the ORCA database information, the offeror verifies by submission of this offer that the representations and certifications currently posted electronically at FAR 52.212-3, Offeror Representations and Certifications-Commercial Items, have been entered or updated in the last 12 months, are current, accurate, complete, and applicable to this solicitation (including the business size standard applicable to the NAICS code referenced for this solicitation), as of the date of this offer and are incorporated in this offer by reference (see FAR 4.1201), except for paragraphs_______________.

[Offeror to identify the applicable paragraphs at (c) through (m) of this provision that the offeror has completed for the purposes of this solicitation only, if any.

These amended representation(s) and/or certification(s) are also incorporated in this offer and are current, accurate, and complete as of the date of this offer.

Any changes provided by the offeror are applicable to this solicitation only, and do not result in an update to the representations and certifications posted on ORCA.]

(c) Offerors must complete the following representations when the resulting contract will be performed in the United States or its outlying areas. Check all that apply.

(1) Small business concern. The offeror represents as part of its offer that it  is , is not  a small business concern.

(2) Veteran-owned small business concern.[Complete

only if the offeror represents itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents as part of its offer that it  is ,  is not  a veteran-owned small business concern.

- Service-disabled veteran-owned small business

concern. [Complete only if the offeror represents itself as a small business concern in paragraph (c)(2) of this provision.]  The offeror represents as part of its offer that it  is ,  is not  a  service-disabled veteran-owned small business concern.

- Small disadvantaged business concern. [Complete only if the offeror represented itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents, for general statistical purposes, that it is ,  is not  a small disadvantaged business concern as defined in 13 CFR 124.1002.

(5) Women-owned small business concern. [Complete only if the offeror represented itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents that it  is ,  is not  a women-owned small business concern.

Note:  Complete paragraphs (c)(6) and (c)(7) only if this solicitation is expected to exceed the simplified acquisition threshold.

(6) Women-owned business concern. (other than small business concern).  [Complete only if the offeror is a women-owned business concern and did not represent itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents that it  is  a women-owned business concern.

(7) Tie bid priority for labor surplus area concerns.   (Not applicable to this solicitation.)

(8) Small Business Size for the Small Business Competitiveness Demonstration Program and for the Targeted Industry Categories under the Small Business Competitiveness Demonstration Program. (Not applicable to this solicitation.)

(9) Complete only if the solicitation contains the clause at FAR 52.219-23, Notice of Price Evaluation Adjustment for Small Disadvantaged Business Concerns, or FAR 52.219-25, Small Disadvantaged Business Participation Program-Disadvantaged Status and Reporting, and the offeror desires a benefit based on its disadvantaged status.]  (Not applicable to this solicitation.)

(10) HUBZone small business concern. [Complete only if the offeror represented itself as a small business concern in paragraph (c)(1) of this provision.] The offeror represents as part of its offer that--

(i) it  is ,  is not  a HUBZone small business concern listed, on the date of this representation, on the List of Qualified HUBZone Small Business Concerns maintained by the Small Business Administration, and no material change in ownership and control, principal office, or HUBZone employee percentage has occurred since it was certified by the Small Business Administration in accordance with 13 CFR part 126; and

(ii) it  is ,  is not  a joint venture that complies with the requirements of 13 CFR part 126, and the representation in paragraph (c)(9)(i) of this provision is accurate for the HUBZone small business concern or concerns that are participating on the joint venture. [The offeror shall enter the name or names of the HUBZone small business concern or concerns that are participating in the joint venture: __________________________.] Each HUBZone small business concern participating in the joint venture shall submit a separate signed copy of the HUBZone representation

(d) Representations required to implement provisions of Executive Order 11246--

(1) Previous Contracts and Compliance. The offeror represents that--

(i) It  has ,  has not , participated in a previous contract or subcontract subject to the Equal Opportunity clause of this solicitation, and

(ii) It  has ,  has not , filed all required compliance reports.

(2) Affirmative Action Compliance. The offeror represents that--

(i) It  has developed and has on file ,  has not  developed and does not have on file , at each establishment, affirmative action programs required by rules and regulations of the Secretary of Labor (41 CFR Subparts 60-1 and 60-2), or

(ii) It  has not  previously had contracts subject to the written affirmative action programs requirement of the rules and regulations of the Secretary of Labor.

(e) Certification Regarding Payments to Influence Federal Transactions (31 U.S.C. 1352). (Applies only if the contract is expected to exceed $100,000.) By submission of its offer, the offeror certifies to the best of its knowledge and belief that no Federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer or employee of any agency, a Member of Congress, an officer or employee of Congress or an employee of a Member of Congress on his or her behalf in connection with the award of any resultant contract.  If any registrants under the Lobbying Disclosure Act of 1995 have made a lobbying contact on behalf of the offeror with respect to this contract, the offeror shall complete and submit, with its offer, OMB Standard Form LLL, Disclosure of Lobbying Activities, to provide the name of the registrants.  The offeror need not report regularly employed officers or employees of the offeror to whom payments of reasonable compensation were made.

(f) Buy American Act Certificate. (Not applicable to this solicitation.)

(g) Buy American Act - Free Trade Agreements - Israeli Trade Act Certificate.  (Not applicable to this solicitation.)

(h) Certification Regarding Debarment, Suspension or Ineligibility for Award (Executive Order 12689). (Applies only if the contract value is expected to exceed the simplified acquisition threshold.) The offeror certifies, to the best of its knowledge and belief, that the offeror and/or any of its principals--

(1)  Are ,  are not  presently debarred, suspended, proposed for debarment, or declared ineligible for the award of contracts by any Federal agency; and

(2)  Have ,  have not , within a three-year period preceding this offer, been convicted of or had a civil judgment rendered against them for: Commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a Federal, state or local government contract or subcontract; violation of Federal or state antitrust statutes relating to the submission of offers; or Commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, tax evasion, or receiving stolen property; and

(3)  Are ,  are not  presently indicted for, or otherwise criminally or civilly charged by a government entity with, commission of any of these offenses.

(4) Have ,  have not  presently, within a three-year period preceding this offer, been notified of any delinquent Federal taxes in an amount that exceeds $3,000 for which the liability remains unsatisfied.

(i) Taxes are considered delinquent if both of the following criteria apply:

(A) The tax liability is finally determined. The liability is finally determined if it has been assessed. A liability is not finally determined if there is a pending administrative or judicial challenge. In the case of a judicial challenge to the liability, the liability is not finally determined until all judicial appeal rights have been exhausted.

(B) The taxpayer is delinquent in making payment. A taxpayer is delinquent if the taxpayer has failed to pay the tax liability when full payment was due and required. A taxpayer is not delinquent in cases where enforced collection action is precluded.

(ii) Examples.

(A) The taxpayer has received a statutory notice of deficiency, under I.R.C. §6212, which entitles the taxpayer to seek Tax Court review of a proposed tax deficiency. This is not a delinquent tax because it is not a final tax liability. Should the taxpayer seek Tax Court review, this will not be a final tax liability until the taxpayer has exercised all judicial appeal rights.

(B) The IRS has filed a notice of Federal tax lien with respect to an assessed tax liability, and the taxpayer has been issued a notice under I.R.C. §6320 entitling the taxpayer to request a hearing with the IRS Office of Appeals contesting the lien filing, and to further appeal to the Tax Court if the IRS determines to sustain the lien filing. In the course of the hearing, the taxpayer is entitled to contest the underlying tax liability because the taxpayer has had no prior opportunity to contest the liability. This is not a delinquent tax because it is not a final tax liability. Should the taxpayer seek tax court review, this will not be a final tax liability until the taxpayer has exercised all judicial appeal rights.

(C) The taxpayer has entered into an installment agreement pursuant to I.R.C. §6159. The taxpayer is making timely payments and is in full compliance with the agreement terms. The taxpayer is not delinquent because the taxpayer is not currently required to make full payment.

(D) The taxpayer has filed for bankruptcy protection. The taxpayer is not delinquent because enforced collection action is stayed under 11 U.S.C. §362 (the Bankruptcy Code).

(i) Certification Regarding Knowledge of Child Labor for Listed End Products (Executive Order 13126). (Not applicable to this solicitation)

(j) Place of manufacture.  (Does not apply unless the solicitation is predominantly for the acquisition of manufactured end products.)  For statistical purposes only, the offeror shall indicate whether the place of manufacture of the end products it expects to provide in response to this solicitation is predominantly-

(1)  In the United States (Check this box if the total anticipated price of offered end products manufactured in the United States exceeds the total anticipated price of offered end products manufactured outside the United States); or

(2)  Outside the United States.

(k) Certificates regarding exemptions from the application of the Service Contract Act.  (Certification by the offeror as to its compliance with respect to the contract also constitutes its certification as to compliance by its subcontractor if it subcontracts out the exempt services. [The contracting officer is to check a box to indicate if paragraph (k)(1) or (k)(2) applies.]

[  ] (1) Maintenance, calibration, or repair of certain equipment as described in FAR 22.1003-4(c)(1).  The offeror does , does not  certify that –

(i) The items of equipment to be serviced under this contract are used regularly for other than Governmental purposes and are sold or traded by the offeror in substantial quantities to the general public in the course of normal business operations;

(ii) The services will be furnished at prices which are, or are based on, established catalog or market prices (see FAR 22.1003-4(c)(2)(ii)) for the maintenance, calibration, or repair of such equipment; and

(iii) The compensation (wage and fringe benefits) plan for all service employees performing work under the contract will be the same as that used for these employees and equivalent employees servicing the same equipment of commercial customers.

[  ] (2) Certain services as described in FAR 22.1003-4(d)(1).  The offeror does , does not  certify that –

(i) The services under the contract are offered and sold regularly to non-Governmental customers, and are provided by the offeror (or subcontractor in the case of an exempt subcontract) to the general public in substantial quantities in the course of normal business operations;

(ii)  The contract services will be furnished at prices that are, or are based on, established catalog or market prices (see FAR 22.1003-4(d)(2)(iii));

(iii)  Each service employee who will perform the services under the contract will spend only a small portion of his or her time (a monthly average of less than 20 percent of the available hours on an annualized basis, or less than 20 percent of available hours during the contract period if the contract period is less than a month) servicing the Government contract; and

(iv)  The compensation (wage and fringe benefits) plan for all service employees performing work under the contract is the same as that used for these employees and equivalent employees servicing commercial customer.

(3) If paragraph (k)(1) or (k)(2) of this clause applies-

(i) If the offeror does not certify to the conditions in paragraph (k)(1) or (k)(2) and the Contracting Officer did not attach a Service Contract Act wage determination to the solicitation, the offeror shall notify the Contracting Officer as soon as possible; and

(ii) The Contracting Officer may not make an award to the offeror if the offeror fails to execute the certification in paragraph (k)(1) or (k)(2) of this clause or to contact the Contracting Officer as required in paragraph (k)(3)(i) of this clause.

(l) Taxpayer Identification Number (TIN) (26 U.S.C. 6109, 31 U.S.C. 7701).  (Not applicable if the offeror is required to provide this information to a central contractor registration database to be eligible for award.)

(1)  All offerors must submit the information required in paragraphs (l)(3) through (l)(5) of this provision to comply with debt collection requirements of 31 U.S.C. 7701(c) and 3325(d), reporting requirements of 26 U.S.C 6041, 6041A, and 6050M, and implementing regulations issued by the Internal Revenue Service (IRS).

(2) The TIN may be used by the Government to collect and report on any delinquent amounts arising out of the offeror's relationship with the Government (31 U.S.C. 7701(c)(3)).  If the resulting contract is subject to the payment reporting requirements described in FAR 4.904, the TIN provided hereunder may be matched with IRS records to verify the accuracy of the offeror's TIN.

(3)  Taxpayer Identification Number (TIN).

TIN: _____________________.

TIN has been applied for.

TIN is not required because:

Offeror is a nonresident alien, foreign corporation, or foreign partnership that does not have income effectively connected with the conduct of a trade or business in the United States and does not have an office or place of business or a fiscal paying agent in the United States;

Offeror is an agency or instrumentality of a foreign government;

Offeror is an agency or instrumentality of a Federal Government.

(4) Type of Organization

Sole proprietorship;

Partnership;

Corporate entity (not tax-exempt);

Corporate entity (tax-exempt);

Government entity (Federal, State, or local);

Foreign Government;

International organization per 26 CFR

1.6049-4;

Other ________________________________.

(5)Common Parent.

Offeror is not owned or controlled by a common parent;

Name and TIN of common parent:

Name_______________________________

TIN________________________________

(m) Restricted business operations in Sudan.  By submission of its offer, the offeror certifies that it does not conduct any restricted business operations in Sudan.

OFFEROR NAME _______________________________________

# SECTION E EXHIBITS

#### OFFEROR’S MISCELLANEOUS INFORMATION

| Offeror’s DUNS Number |  |
| --- | --- |
| Offeror’s Complete E-mail Address |  |
| Offeror’s Office Telephone Number |  |
| Offeror’s Facsimile (FAX) Number |  |
| Offeror Contact Representative(s) | 1. Name | Telephone |
|  | 2. Name | Telephone |

OFFEROR NAME_______________________________________________

AIRCRAFT QUESTIONNAIRE

You may recreate this form but it must include all the information listed and provide charts, calculations, and supporting documentation as appropriate so that the Government can verify the capability of your offered aircraft.

”N” Number ____________________   Make and model aircraft____________________________________________

__________Number of seats. Seats are  are not   removable for cargo hauling.

__________Cruise speed in True Air Speed (TAS) @ 8,000 ft -ISA plus 20 ºC

__________Cruise endurance at 8,000 ft - ISA plus 20 ºC plus a 30-minute reserve.

__________Positive single engine rate of climb when equipped for the contract and carrying a pilot weighing 200 lb, one observer weighing 220 lb, fuel for 4 hours plus a 30-minute reserve, at 5,000 feet pressure altitude @ ISA plus 33 ºC.

Turbine Powered  Yes   No

__________Payload in pounds with fuel for 250 nautical miles plus VFR reserve @ 8,000 ft - ISA plus 20 ºC.

Minimum restrictions of outward visibility of the ground in level flight for the front seat observer and middle seat observer stations. Please describe any additional features on your aircraft that would increase visibility beyond what the standard make and model aircraft offered provides.

Air conditioning Yes   No

__________Number of Panel-Mounted, Digital, Narrowband, VHF-FM Transceivers without Aux Port and Cable.

REFERENCE QUESTIONNAIRE

You may recreate this form but it must include all the information listed

If you fail to include all requested information or we are unable to contact your references based on the information you provide, you may not receive consideration for the work done.  Include recent (not more than 3 years old) experience of the kind described in paragraph B1.1 of the specifications.

| OFFEROR NAME: | DATE |
| --- | --- |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2008 2007 2006 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2008 2007 2006 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2008 2007 2006 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2008 2007 2006 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2008 2007 2006 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |

# Text boxes

DRAWING FS/OAS A-17

AUXILIARY VHF-FM RADIO INTERFACE