Phenix

EYEBROW STRUCTURAL ANALYSIS

November 14, 1999

jrarchuleta@lanl.gov

505 665 2416

# index

#### TOPIC	page

SECTION  0	EYEBROW PICTORIAL VIEWS	-

index	2

assembly view	3

side view	4

bottom view	6

socket	7

SECTION  1	SUMMARY	-

report information	9

general description

discussion of analysis

summary of stress analysis	10

SECTION 2	GENERAL design notes	11

eyebrow description	12

design requirements	14

material properties	14

SECTION 3	LOADS	15

design loads	16

SECTION 4	REMOVABLE PLATFORM	20

loads

stress

SECTION 5	PERMANENT PLATFORM	25

loads

stress

SECTION 6	miscellaneous	32

back brace

socket

guardrail

Figure 1	  Eyebrow Assembly

Figure  2	  Eyebrow assembly  -side view

Figure 3  Eyebrow assembly---back plate view [looking up]

Figure 4     bottom view of eyebrow

### FIGURE 5    SOCKET

# SECTION 1

# SUMMARY

# SECTION 1 		summary

## REPORT INFORMATION

This report presents the structural analysis of the Eyebrow.

The report is divided into 6 sections.  Each section, following the first 2 general information sections, presents the analysis of a component, e.g.  section 5 discusses results and depicts stress of the Permanent Platform.

Results generally are shown as contour plots except where the loads and reactions are shown.  The maximum stress condition shown is normally the VonMises or maximum bending principle stress given in psi units.  Total deflection or total displacement is given in inches.

Due to the nature of this report, color copies provide the only satisfactory means of data scrutiny.  In most cases the vast amount of information generated has not been saved, except as color contour plots.

The finite element analysis was done by use of COSMOS/M, a software package by Structural Research and Analysis Corporation.

## EYEBROW  general description

The Muon FEE electronic equipment racks are located on a platform attached to the Back Plate of the magnet. The assembly consists of 2 platforms; a Permanent Platform attached to the magnet, and a Removable Platform that attaches to the Permanent Platform.  The assembly is called the Eyebrow which attaches to the Magnet’s Back Plate.

## DISCUSSION OF ANALYSIS

Stress levels and loads shown in this report do not include safety factors, i.e. loads and stresses are due to real loading and are not increased by safety factors.  The summary table shown in the section below [page 10] gives maximum stress levels for actual ‘real’ loads, but the margin of safety (MS) does include a safety factor of 4.  Stress levels of critical sections can be found in the figures included in the report.

This scan of the members that comprise the structure shows the Eyebrow is structurally sound. Stress contours of the Eyebrow are found in Section 4 and Section 5.  Local bolt attachments and higher loaded areas are reviewed in Section 6.

## SUMMARY OF STRESS ANAYLYSIS

| Item | section | element number | stress-psi | Allow Stress | Margin of Safety |
| --- | --- | --- | --- | --- | --- |
| Removable Platform | Outer main Beam | 62 | 582.8 | 33,000 | 13.1 |
|  | Inner main Beam | 213 | 371 | 33,000 | 21.2 |
|  | cross beam | 408 | 479 | 33,000 | 16.2 |
|  | platform mounting bar | 299 | 3,006 | 33,000 | 1.74 |

# section 2

# general notes

# SECTION 2			general

## DESCRIPTION OF EYEBROW

The Eyebrow is located above the South Magnet and straddles the Back Plate as shown in the accompanying figures [figs 1-4]. The Eyebrow is supported at 6 attachment points, four[4] of these supports are centered on the upper edges of the Back Plate and two [2] which provide overturn stability, attach to the downstream face of the backplate. All of the attachments are through a face plate containing 6 each 3/8 inch diameter bolts. For details of a typical brace see drawing 10Y226402-08

The Eyebrow geometry is shown in drawing 10Y226402-02. The Permanent and the Removable Platforms are each approximately 24 inches wide by 24 feet long and span the Eyebrow in the East-West direction. The Eyebrow’s maximum protrusion in the Z direction is 313.7 mm downstream of the Back Plate. The Permanent Platform outer beam is in the same vertical plane as the end of the doughnut.  The upstream protrusion from the Back Plate is 772.6 mm; hangs over the Lampshade.

Access to the Eyebrow is via an opening located in the northeast corner of the Removable Platform

## DESIGN details

Both platforms are similar in construction, use standard structural steel shapes and welded construction.  The floor is made of ¼ inch raised pattern steel plate.  Guardrailing and 4 inch high toeboards are provided around both platforms.

The Permanent Platform 10Y226402-03, is anchored to the Back Plate by means of 2 diagonal braces (Back Brace) 10Y226402-08, 2 vertical struts (Vertical Brace) 10Y226402-07 and 2 vertical load pads located on the Inboard Socket 10Y226402-09.

The Removable Platform 10Y226402-05, extends upstream of the Back Plate over the Lampshades and is attached by means of 6 square beams inserted in sockets welded to the Permanent Platform. See drawing 10Y226402-01

Design detail Summary

    - Two main steel beams (2x6) run the length (east-west) of each platform forming the perimeter structure.  The 2x6 beams are rectangular hollow tubing, 2”wide x 6” high x 0.188”wall,.

    - The ends (east and west ends) of the platforms are closed by square 4x4 tubing and which are also used for attaching lifting lugs.  The tubing is 4” x 4”x 0.188”wall x 24 inch long.

    - Cross ribs between the 2 x 6 beams form the flooring support for the ¼ inch steel floor plate.  These beams also provide framing around cutouts in the floor beneath the racks and serve as support for the floor splice joint.  The cross ribs are 2x2 tubing (2”x 2” X .125”wall).

    - Weld construction details

      - Cross members [Sockets,10Y226402-09,10;cross ribs and lifting end beams] are welded to the main beams. See 10Y226402-04,06.

      - Floor is spot weld to the main [2 x 6] beams and to the cross members.

      - Kick plate is 1/4 inch steel plate by 4 inch high, spot welded to floor.

    - Back Brace (Diagonal) 10Y226402-08, are located at 1 meter spacing (east-west)off the magnet’s center Z axis to provide turn-over stability.  These braces protrude downstream (behind) the Back Plate.

      - Vertical load reaction pads are located at 4 places on the flats of the backplate at the top octant.

        - Vertical Brace (struts) 10Y226402-07,are located on the outboard ends (east-west) of the platform

        - Vertical and Back Brace are made from 4 x 4 x 0.1875 wall square tubing.

    - Square receivers (6 each) made of square 4x4 inch tubing are attached below the Permanent Platform to provide the sockets that join the platforms, see drawing 10Y226402-09,10.

    - The Removable Platform is supported by six 3½”square tubing beams (3½ x3½ x ¼ thick) which insert into the sockets of the Permanent Platform. See Platform Mounting Bar 10Y226402-11.

    - The platforms are retained to each other by 12 each 3/8 inch diameter bolts, cross bolting the 2x6 beams.

## DESIGN REQUIREMENTS

The Permanent Platform provides a mounting location for

instrument racks and the Removable Platform provides working area for installation, wiring and maintenance of the racks. The Removable Platform can be separated from the Eyebrow to facilitate removal or installation of the lampshades.

Three [3] racks are installed on the Permanent Platform. The arrangement of the racks is shown in a frontal view in figure 1 or see drawing 10Y226402-03 (all dimensions are metric). The racks are positioned in the platform with the front and back sides facing East-West.

Each Platform and its components shall be capable of supporting, without failure, its own weight and at least 4 times the maximum intended load applied or transmitted

## MATERIAL PROPERTIES

The material selected for the design conforms to ASTM standard specifications.  The square and rectangular steel tubing shape is cold formed per specification ASTM A500 Grade B which has a tensile yield strength of 45,000 psi.  This allowable is for either welded or seamless tubing.  The Sockets of the Permanent Platform use tubing per ASTM A500 grade A, with an allowable tensile strength of 58,000psi

The table below summarized the maximum allowable strength levels used for Eyebrow design.

| Property ASTM 500 | Allowable | value in psi GRADE B | value in psi GRADE A |
| --- | --- | --- | --- |
| Tension | Ft | 45,000 | 58,000 |
| Yield | Fy | 33,000 | 42,000 |
| Shear | 0.6Ft |  |  |
| Bearing | 0.9Fy |  |  |

# section 3

# general loading

# information

# SECTION 3			loads and geometry

#### GEOMETRY

#### Finite Element representation of the Removable Platform and Permanent Platform is shown below.

figure 6  Removable Platform

figure 7 Permanent Platform

## DESIGN LOADS

#### removable platform

The design condition assumes 12 apostles each weighing 250 pounds standing on the Removable Platform during a photo session.  This loading transposes to 62.5 lbs/ft2  on the platform, which is more than the 50 lbs/ft2  recommended by OSHA for medium duty platforms.  This loading is applied to the cross beams as 14.5 lbs/inch; see figure 8.

The Removable Platform loads are transferred to the Permanent Platform through 6 beam sockets, see figure 11

#### permanent platform

The electronic racks are assumed to weight 1000 pounds each. Loads are introduced through the 2*2 cross beams straddling the racks at 500 lbs.

Additional Permanent Platform Loads

Eyebrow structural weight is estimated as 2000 pounds, 1000 lbs for each platform.  Miscellaneous attached hardware is estimated at 2000 lbs; cables, clamps, hoses, etc.   Platform loading is 60 lbs/ ft2.

This additional loading is introduced by a 11.5 lbs/inch load on the perimeter of the permanent platform.

See figure 13 for loads.

…

# LOADS summary:

  - Permanent Platform;  see figure 13

    - Three equipment racks: each at 1000 pounds.  Load is introduced to the main beams through the 2x2 cross beams on either side of the floor cutout at 500 lbs each.

    - Structural weight, hung loads, platform loads and any miscellaneous: 11.5 lbs/inch

      - Eyebrow structural weight [2000 lbs] is distributed through the 2x6 beams;  Removable Platform and Permanent Platform each weigh 1000 pounds.

      - Include 2000 pounds of Cable and miscellaneous hardware attached to the Permanent platform

      - Platform  floor loading of 60 lbs/ft2

    - Loading at Sockets are reactions from Removable Platform. see figure 11

    - Reaction loads on the Magnet’s Back Plate are through 2 vertical struts(vertical brace}, 2 Diagonal (Back Brace) struts and 2 reaction pads on the back plate..

    - Attachment of the struts to the Eyebrow and Back Plate is through 6 each 3/8 inch diameter bolts. see drawing 10Y226402-01.

  - Removable Platform see 10Y226402-05

    - Use 12 apostles standing side by side each apostle weighs in at 250 pounds.  Load is spread from plate to 9 cross beams.  Cross beams are loaded at 14.5 lbs/in to represent the apostle loading.

    - Loads are reacted through 6 forks that insert into sockets of the fixed platform.

# section 4

# stress analysis

# Removable Platform

# SECTION 4			stress analysis

# Removable Platform

The figures below show the stress distribution, fig 8, and maximum deflections, fig 10, of the Removable Platform. Figure 9 is a close-up look at the maximum stress region.

Maximum stress of 3,006 psi occurs on the inner Platform Mounting Bar, node 299.  Maximum deflection is 0.0202 inches on the Main Platform Beam, node 213.  See summary table page 10 for margins of safety.

Figure 8   Removable Platform Stress.

Figure 9          zoom view of Removable Platform stress pattern.

Figure 10   Deflections of Removable Platform`

Figure 11  Reaction Loads at Sockets

# section 5

# stress analysis

# Fixed Platform

# SECTION 5			stress analysis

# Permanent Platform

# geometry

figure 12  permanent platform FEM geometry

# loads

fig 13  loads on Permanent Platform

loading table

Load Set 1 – FROMPLTFM

Nodal Forces (on Point)

Load in pounds, positive Z is up.

node ident.   load direction

ID     Z

node    3    -1136.    in pounds

4    -647

5    -805.8

10    453.

11    305.

12    331.

16    -1136.

17    -647

18    -805.8

23    453.

24    305.

- 331.

Nodal Forces (on Curve)

curve  ID       Z         Y

53    -500.         0.      in pounds

54    -500.         0.

55    -500.         0.

56    -500.         0.

57    -500.         0.

58    -500.         0.

Nodal Force per Length (on Curve)

ID 		Z           Y

curve  1    -11.5         0.      in pounds/inch

2    -11.5         0.

3    -11.5         0.

4    -11.5         0.

5    -11.5         0.

6    -11.5         0.

7    -11.5         0.

8    -11.5         0.

9    -11.5         0.

10    -11.5         0.

11    -11.5         0.

12    -11.5         0.

13    -11.5         0.

14    -11.5         0.

# stress

The figure below, fig 14, show the stress distribution of the Removable Platform. Figure 15 is a close-up look at the maximum stress region.

Maximum stress  of 8,045 psi occurs on the inner Socket.

figure 14  Permanent Platform stress

this is

the time

that try

mens

souls

figure 15 Permanent Platform.  Max stress region.

8,045 max stress at inboard socket

# section 6

# stress analysis

# Miscellaneous

Loads applied to the braces are shown below.

figure 16. deflection of backbrace

figure 17  stress fringe of backbrace

figure 18 backbrace mount stress pattern.

figure 19  Socket internal load transfer stress.

# Text boxes

Loads transferred from Removable Platform from Platform Mounting Bar through Sockets

Loads due to 3 racks, each at 1000 pounds. Loads are introduced through 2*2 square tubing.

loads due to structural weight, cables, platform load