IMAGINE Robot Project

# Purpose

The IMAGINE robot will provide an Access-Grid compatible roving telepresence.  It will enable people to remotely attend meetings that would not otherwise be accessible to AG equipment, perform remote tours of the Oakland HPC facility, and even enable LBNL-based personnel to remotely assist/supervise remote reset and configuration of hardware in the Oakland facility by the staff there.    For more details, please visit the project website at http://dit.lbl.gov.  The login for the "private" pages listed on this site is "imagine" and the password is "that!".

## Description

The robot base will be approximately 33" in diameter and 5' tall.   The bulk of the robot will be located near the ground with the wheel-base, but a mast will extend to approximately human height as a mounting point for the robot's video-camera and a small LCD display (for the video image of the remote user).   The robot is constructed primarily from off-the-shelf components in order to support long-term maintenance and reliability of the robot platform.

### Motion Control

Typically robots use 2-wheel Akerman (tank-like) steering whereby varying the relative speed of the two drive wheels controls the direction of the robot.  A 3rd swivel wheel provides stability for the base.  Such 3 wheel designs are inherently unstable and likely to tip over if bumped.   A 4-wheel design involving 2 drive wheels and 2 casters  is much more stable, but it is also susceptible to getting stuck on the crest of even a moderate incline since one of the drive wheels will likely be lifted off of the ground.

The IMAGINE robot uses 4 independently steered and motorized wheels in order to provide extremely precise control over motion and to eliminate the stall problem on even steep inclines.  The 4 wheel independent steering allows the IMAGINE robot to move freely in any direction without regard to its current rotational orientation.  Both a 3-wheel (2 drive + 1 caster) and 4 wheel (2 drive + 2 casters) Akerman steering system requires the robot to carve turns in order to point it in the direction it desires to travel.  This would make maneuvering difficult in tight spaces such as a crowded convention floor,or between SP nodes.  Our robot design will be able to spin on it's center axis; maintaining a turn radius close to zero.  The robot's base will also contain a number of active proximity sensors (both infrared and ultrasonic) to prevent it from colliding with people and other obstacles in tight spaces.

You can find engineering diagrams of the wheel design at

http://teracet.lbl.gov:8080/Private/wheels.html

### Access Grid Video/Audio

The robot will provide 2-way video and audio conferencing over a standard 802.11 wireless networking interface.  This will be accomplished using software and hardware that is compatible with the Access Grid environment (http://www.accessgrid.org).  This will allow us to share the robot's audio/video feeds on the Access Grid as well as take advantage of a number of off-the-shelf hardware and software components.  The Access Grid services are hosted on two on-board miniature (3”x5”) Pentium III PC's. (http://dit.lbl.gov/IMAGINE/Progress.html)

### Remote Control

Since the robot's audio and video conferencing subsystem is implemented using Access-Grid technologies, mobility can be controlled through the same Internet connection used to carry the audio and video feeds.  We will typically use the Access Grid in 50B LBNL to remotely access and control the robot.  Once deployed, any AGnode can be used.  The video/audio feeds from our robot can be shared with everyone on the Access Grid and will become an integral part of that collaborative medium.  Integration of drive and a/v control is realized  through the LBNL DevServ software infrastructure. This service has already proved successful  for the  remote control of  video cameras on other Agnodes.  As an added security feature, the control of the robot will be fully encrypted to prevent hackers from hijacking control of the robot.

An initial (debug) GUI design has been posted at

http://teracet.lbl.gov:8080/Private/debug_gui.html

This will eventually lead to more functional GUIs with integrated motion maps such as the one at

http://teracet.lbl.gov:8080/Private/robot_gui.html

# Long Term Support

The robot is being constructed as much as possible from off-the-shelf integrated components.  This ensures the long-term maintainability of the platform due to ease of part replacement from well-established manufacturers.  Those components that are constructed in-house (like the wheel assemblies) are in many ways over-engineered in order to ensure that they outlast any other component on the platform.   The IMAGINE robot development team is carefully documenting all components and interactions between components on the robot platform in order to ensure that the robot can be repaired over the long term if the original development team is not available.  Members of the team will be available for consultation in the event that the robot breaks and needs repair.

There are many additional options for long term maintenance, but we would like to defer discussion of these options until the first prototype is completed.  We need to have some experience operating and testing the prototype before we can evaluate our final plan for long-term maintenance and repair options.

# Cost of Components

Following is a simplified outline of the major component costs involved in constructing the robot.  For a comprehensive itemized list of components and suppliers, please refer to Appendix A.  The list of components involved in construction of the motion platform (the robot motion and drive electronics) has been separated from the components used for the video-conferencing and remote control (the Access Grid compatible set of PC’s and A/V peripherals).

Motion Platform Costs

Qty Description Cost 8 Electric motors (4 for steering and 4 for drive) $180/ea 2 12V sealed lead-acid batteries $100/ea 1 Battery Charger $120/ea 8 Motor Speed Controllers $110/ea 1 Mini Serial Servo Controller (controls 8 motors) $49/ea 2 Incremental encoder-to-serial bus adaptor used to interface to motor position sensors (incremental encoders) $195/ea 3 Basic Stamp 2SX Microcontrollers + Carrier board $100/ea Na. Various proximity sensors (IR and Ultrasonic) $60 Na. Bearings Washers and other mechanical components $500

Anticipated Cost for Robot Motion Platform=$3940

Access Grid Node Costs

Qty Description Cost 2 500MHz Pentium III miniature PC’s with 256Megs RAM, 3 PCI slots, and IBM Microdrive $2,100/ea 2 DC-to-DC ATX PC Power Supplies $175/ea 2 Hauppauge WinTV Video Capture PCI Cards $77/ea 1 Soundblaster Audio Capture PCI Card $60/ea 2 PCMCIA to PCI adaptor for 802.11 wireless $80/ea 2 PCMCIA 802.11 wireless networking cards $150/ea 1 8.4” LCD Display $475/ea 1 Canon VC-C4R video camera with 10x zoom and motorized orientation control $1,200/ea Na. Various (microphones, speakers and cables) $200

Anticipated Cost Per Mobile Access Grid Node=$7,099

# Timelines for Construction

### Overview

We will construct a prototype robot, which is intended to rove on the show floor of the Supercomputing 2001 convention (SC-Global) in Denver Colorado.   We will be able to demonstrate the initial prototype by end-July.  If the design is acceptable, then we will construct a second robot for use in the Oakland HPC facility.  During SC2001, both the Oakland and the show-floor robots will participate in the Access Grid events, which are the central focus of this show and will be a centerpiece for LBNL/NERSC show floor exhibit.  After SC2001, the second robot can either be a hot-spare/parts source for the Oakland Robot or remain in service for meetings at LBNL and for future Supercomputing conferences.

### Robot Base

Currently: 	Completing construction on first motorized wheel

June 1: 	First wheel assembly complete and assembled.

June 12: 	Completed assembly of testing platform.  Initial testing using single drive wheel and 2 casters.

June 19: 	Testing of drive logic/components using serial-cable tethers (no wireless yet)

June 26: 	Construct and assemble 3 more drive wheels.

July 10: 	Testing with platform incorporating all 4 drive wheels and Basic Stamp logic/motion-control/steering using wireless DevServ interface through PC's

July 17: 	Construct “mast” assembly and mount camera+LCD panel on mast.

July 24: 	Testing using DevServ-based motion controls

### Control Software

Currently: 	DevServ is up-and-running on the embedded PC’s

June 13: 	Debug GUI interface can speak securely to DevServ.

June 27: 	DevServ can speak to the Basic Stamp on the 1-wheel testing assembly.  The Debug GUI will be used to drive the single-wheel platform for testing.

July 11:  	DevServ interface controls a Canon video camera as well as switching between 2 microcameras on a second WinTV card on the video capture PC.

July 18: 	Debug GUI used for testing the 4-wheel robot base and Cameras.

July 25: 	A more ergonomic advanced motion control GUI will be tested.

### AccessGrid

June 15: 	Connect PC with battery power supply and test.

June 22: 	Bring up PCMCIA/802.11 wireless network interface and bring up second AG PC.

June 27: 	Testing of routing video/audio network traffic through Multicast Bridge (MBR)

July 6: 	Construct more rugged Lexan cases for mounting the AGnode PC's securely on the robot base (4-wheel platform).

June 11: 	Testing of remote launching of Access Grid components (ie. Using a remote Win2k PC to launch the audio/video capture and devserv on the robot PC's.

July 20:  	Further testing/debugging of audio/video platform and LCD.

July 27: 	Final testing & debug.

This timeline should bring us to a fully functional prototype on July  30th.

Appendix A: Itemized Component Costs (double click on object to get full table)